===============================
KX-P1624 UPGRADE
===============================

Panasonic has become known of late as a supplier of quality printers for the 
computer user.  Performance, price, and compatibility have served to make this 
entire line of equipment some of the most sought after computer peripherals in 
America. 

One member of the Panasonic printer family is the KX-P1624, an excellent 24 
pin wide carriage printer.  This printer has only one relatively small 
shortcoming to mention, it sports a buffer of only 12K, too small for most 
serious users' needs in general.  What we will describe in this short article 
is a way to easily increase the 12K built-in buffer to 44K. Panasonic sells 
this 32K upgrade chip for over $50, yet I will show you how you can do it 
yourself for less than $12!  This upgrade is also required if you wish to 
download custom fonts to the 1624.

You will first need to purchase a 32Kx8 Low Power CMOS static RAM chip, 120 
nanoseconds or better, to upgrade the 12K buffer that currently resides in 
your printer.  One suitable chip would be the Hitachi 62256LP-12, a 28 pin 
chip sporting a black plastic case.  There are numerous sources for this, or 
similar, RAM chip.  Check in Computer Shopper, the back of the various 
computer magazines (in the classified ads section), or ask in the Computer-New 
Conference of EXEC-PC BBS.  One mail order source is Microprocessors 
Unlimited, located in Beggs, Oklahoma.  The telephone number is 918-267-4961.  
The last time I purchased a 62256LP-12 from them (March, 1991) the cost, 
including shipping, was less than $12.00 

NOTE: If you are not familiar with the precautions you need to follow when 
handling CMOS devices, let me advise you that they are extremely sensitive to 
damage from excessive voltage.  Static electric discharge is a very real 
concern when handling these, as well as most, integrated circuits.  Take all 
the precautions you can against generating *any* static electricity while you 
have the 62256LP in your hands.  This includes touching a grounded metal 
object with your hand before handling the chip, not working on a carpeted 
surface, and not wearing synthetic clothing, such as 100% polyester pants.  Be 
especially careful if the air is dry and you have experienced static electric 
discharge in your environment recently.

Let up proceed:

1.      On the front of the printer you will find what we will for now call the 
        "single page feed door".  Open this door, and look at the bottom 
        of the control panel.  The panel is hinged at the top and snaps in at 
        the bottom.  You'll see the plastic clips at the bottom that hold it 
        in place.  With your thumb on the bottom of the panel and forefinger 
        on the top, squeeze the bottom of the control panel and pull outward. 
        The snaps will come loose along the bottom edge.  Carefully remove 
        the two cables from the switch pack and set it aside.

2.      After removing the control panel, you'll find 3 brass phillips head
        screws that are holding on the top cover; remove these.  The top will
        now swing upward from the front and will move rearward as if there
        was a hinge on the hind quarters.

3.      Glancing down at the back of the printer, you will see two large chips
        on the circuit board.  One is in a socket and the other is not.  
        Between these two chips is an empty socket.  This is where the 
        additional RAM chip is installed.  Note that the two existing chips 
        have their orientation notches facing to the right side of the 
        printer, where the platen knob located.  Install the new chip with 
        the notch facing the same direction as the existing chips.  Note that 
        the new chip will completely fill the socket, even though the 
        existing socketed chip does not.


4.      Now reassemble the printer in exactly the reverse order.  Easy, eh?
           

This article was created using source material located on EXEC-PC BBS and 
experience from using and installing these chips in Panasonic printers I have 
owned.

John L. La Pin
Germantown, WI
EXEC-PC BBS