Diamond SpeedSTAR 8514/A Emulation Driver

The instructions that follow explain how to install the appropriate
8514/A emulation driver for your needs. On this disk you should find
these files:

                RIXAI4.EXE
                RIXAI8.EXE
		STAN0715.FNT
		STAN0814.FNT
		STAN1220.FNT
                README.DOC (this file)

Two emulators are provided. Choose either emulator depending on your video
memory configuration and number of colors desired. The following table
illustrates the resolutions available by driver name according to the video
memory configuration on your board.

                                        MINIMUM DISPLAY
RESOLUTION/COLORS       MODE (hex)      MEMORY REQUIRED         DRIVER
 640x480     16         12                      512KB           RIXAI4
1024x768     16         37                      512KB           RIXAI4
 640x480    256         2E                      512KB           RIXAI8
1024x768    256         38                      1MB             RIXAI8


INSTALLATION

1) Create a subdirectory on the hard disk called RIXAI or another name
   of your choosing.

2) Copy the contents of the floppy diskette to that newly-created
   subdirectory.

Decide which version of the emulator is needed based on the amount of
video memory on your video adapter and the number of colors you wish
and proceed.

4) Type RIXAIx at the DOS prompt, where x is either 4 or 8.

5) You can now run your application software under 8514/A emulation.

Remember to load the appropriate emulation driver before running
application software that requires 8514/A. You might want to create a
simple batch file that loads the emulation driver and your software
automatically to simplify the process.

EXAMPLE (acadai.bat)

                        RIXAI8
                        ACAD

You may need to reconfigure some software to run under an 8514/A
driver. Check the user manuals of your applications to determine if
such a driver is supported.