ALL V.32BIS MODEMS ARE NOT CREATED EQUAL!  



14,400 bps --- V.32/32bis TECHNOLOGY AS COMPUCOM SEES IT

   The vast majority of V.32bis modem designs are implemented with third  
party  chip sets from yet another manufacturer.  When CompuCom started  
development on the Speedmodem Star (tm), we decided that none of these  
chip sets would meet our requirements.  Thus we opted for the much more  
time-consuming and costly path  of developing our own CompuCom  
Technology modems.  We're glad we did.  When we designed the Star, low 
cost was not our criteria.  It was our objective to set the highest  
REAL-WORLD performance standard for a V.32bis  modem.  


BACKGROUND ...THE TECHNOLOGICAL CHALLENGE 

   Telephone systems are designed and maintained to provide an 
acceptable quality of voice communications.   When you attempt to send  
computer data over the voice  channels, you take your chances and there  
are no guarantees.  (However, the telephone company will sell you data  
quality channels at an enormous premium over voice quality channels.)   
It should be made clear that reliable high speed modem communications,  
especially V.32bis, is very demanding of the telephone system.  The 
weakest and most error-prone link in modem communication is the 
telephone system itself. Even a telephone connection which is crystal  
clear to the  ear, may be significantly impaired for high speed data  
communications.  In  general, if you don't have an excellent connection,  
you won't have 14,400 bps throughput. 

   The most fundamental problem of high-speed data communication over  
the phone  system is the limited bandwidth of the telephone  
connection...around 3,000  Hertz if you're lucky.  At 2400 bps the task  
is analogous to passing a 2.4" cylinder through a 3" orifice...simple  
enough.  At 14,400 bps (V.32bis) the  problem is analogous to forcing a  
14" diameter cylinder through the same 3" diameter orifice, while  
another 14" piston is coming from the opposite  direction!  How do you  
do that?  The solution is nothing short of magic.  The  problem requires 
computation of complex mathematical algorithms - Modems have to perform
millions  of calculations every second.  The hardware needed to do  this  
is a relatively new class of miniature super-computer, called a Digital   
Signal Processor, or DSP for short.  

  From the digital signal processing programming and algorithm 
standpoint, a  modem may be seen as a number of discrete, highly 
 mathematical functions, which have to operate and interact intimately  
with each other.  Each discrete function has its own set of problems  
which must be solved by a set of highly inspired mathematical  
algorithms.  Unfortunately, each of these discrete modem  functions is  
not independent of the others.  Choosing a specific algorithm  which may  
provide improved performance with one part of the design may actually
worsen the overall performance of the modem.  For example, the effect of 
the specific algorithm may modify the signal character in a way that it   
makes it more difficult for the other functions of the modem to process   
the signal with accuracy.  

   Also, there are many tradeoffs between the choice of the algorithm,  
the amount of processing power available, and the performance of the  
modem.  Many of these tradeoffs are based on the margin of error, or a
reduced modem performance level which the designer considers acceptable.   
For  example, a designer might choose an algorithm which requires less  
digital signal processing power than a more accurate algorithm, if he is 
concerned with minimizing the overall cost of the design.  


COMPUCOM'S POINT OF VIEW 

   For some time CompuCom has publicly stated that the majority of
V.32/32bis implementations do not achieve our technical expectations,  
particularly in the area of echo cancellation and in performance over  
real world telephone connections.  

   When a V.32 modem transmits a signal, at least two echoes are 
 reflected back which directly interfere with the faint received 
signal  from the distant modem.  The first is called the "near" echo.  
It is  usually several times louder than the faint signal received from 
the  distant modem; and, it is too closely spaced to the outgoing signal 
to  be  detectable by the human ear.  The second is called the "far"  
echo.   It can interfere with the signal received from the distant 
modem,  causing many errors in the received data.  (Error correction
can hide  this problem at the price of slower throughput.)  At times,
the ear can  hear this "far echo", echoing back on long-distance 
connections.  

   A V.32 modem must precisely estimate each of these echoes, generate  
their  inverse, and subtract each from its received signal.  The  
remaining signal should be only the signal transmitted from the distant  
modem.  In practice, it must reduce the near echo energy by between 1000  
and 10,000 times, and the  far echo energy by between 10 and 100 times.   
Any error in the process results in self generated noise and 
interference which degrades the received quality of the distant modem.   
Not surprisingly, the echo canceller is the weakest link in  most  
V.32bis modem implementations.  It is also the most complex portion of   
the modem.  Further, it requires a considerable amount of computational  
power and is generally the most costly portion of the modem.  
 

THE STAR DESIGN 

   For starters CompuCom chose two very powerful Digital Signal 
Processing CPUs.  Combined, they produce a computational power of  
approximately 100 million  mathematical operations per second.  The  
hardware operating system supporting the Star is based on a Motorola  
68000 CPU, similar to the one used to power Macintosh and Amiga  
computers.  

   CompuCom's DSP algorithms were developed  specifically to handle the  
real-world telephone line impairments and noise with a degree of  
performance that we feel is unequalled.  

   Dynamic Impedance Stabilization(tm) rounds out the Star Design.   
DIS(tm) is  CompuCom's unique proprietary telephone interface.  DIS was  
developed to improve  signal quality under real-world conditions.  In  
practice, DIS improves the  received signal to interference quality by a  
factor of better than 2:1 over  other modem telephone interfaces.  Some  
observers have confused DIS with "Adaptive  Equalization", which performs
a completely different function. The Star incorporates adaptive equalization
as well.

   We're quite proud of the unique CompuCom technology that goes into  
every Speedmodem Star.  That's why we feel the Star represents the best  
performing V.32bis  modem available, regardless of cost.      


ANSWERS TO OFTEN ASKED QUESTIONS 

Q: How can a 14,400 bps V.32bis modem with this performance cost so 
little?  

A: The Star is among the lowest cost V.32bis modems available at the  
time  of this writing.  However it isn't a cheap modem to manufacture.   
CompuCom  manufacturing engineers estimate the Star's production cost to  
be greater than  the production cost of another dual technology modem
selling for over twice  the price of the Star.  We feel we have  
accomplished our performance objectives simultaneously with good cost 
engineering.  Lastly the profit margins in CompuCom products are lower  
than industry standards.  However in todays economy CompuCom feels this  
makes practical business sense...since more and more buyers are examining
the cost effectivity of their purchases. 

Q: How does the Star compare to other modems in its price range?  
 
A: A typical low cost V.32bis modem design based on a popular chip set
uses a single DSP operating at 38 million operations per second.  We  
estimate that the Star  provides approximately 2.5 times the digital  
signal processing power of this  design.  We also estimate that the  
analog to digital converter in the Star has four times the accuracy of  
this design.  This is very important for good echo cancelling and  
dynamic signal range.  Finally, only CompuCom modems have  Dynamic  
Impedance Stabilization.  

Q: This discussion seems somewhat technical ...what does all this DSP stuff 
mean to the average  modem user.  

A: A higher throughput a higher percentage of the time.  This translates   
directly to a savings in time and money spent on Ma Bell.  For example:  If 
your  modem is distant from the central telephone station or you call  other 
modems  which are distant from the central telephone station (this  is quite 
likely), there will be considerable degradation in the high  frequency 
throughput of the telephone circuit.  While some V.32bis modems might slow down 
under these degraded conditions...the Star could  shine!  If you make long 
distance or international calls, again, the  Star's signal  handling ability 
could save you money on expensive calls.   
                                
Q: Some magazine test I've read indicates little performance difference
between  various V.32 modems...?  

A: There are two reasons for this:  First many modems are made with the  
same  Rockwell data pump or chip set.  More importantly, published  
comparative test haven't examined these modems under REAL-WORLD  
operating conditions,  particularly with regard to echo effects and line  
impedance variations.  Modem experts have recently criticized these 
tests  and some magazine editors are now planning more stringent 
testing.  Unfortunately, even the best of laboratory  testing doesn't 
replicate  REAL-WORLD telephone connections.  

Q: What options does the Star support?  

A: In the second quarter of '92 CompuCom expects to release Fax, Voice  
Mail and Caller ID options.  These options are available as in field  
upgrades.  

Q: What is the cost of the Star?  

A: The suggested retail cost of the basic stand alone 14,400 bps V.32bis 
Star is $539.   Since the Star achieved full production volume shipments 
in February,  CompuCom has decided to offer the Star at a special 
promotional price of $399 until  May 31, '92.  

Patent pending.