Support Commands for voice mode operation
   ------------------------------------------

   AT+FCLASS=<mode>

	  This command selects a DCE mode as follows:

	  <mode> = 0 (Default), Data mode.
	  <mode> = 2, Fax mode.
	  <mode> = 8, Voice mode.

	  Result codes:

	  OK :	 The DCE issues this result code if DCE accept this command.
	  ERROR: The DCE issues this result code if <mode> is not permitted.


   AT+FCLASS?

	  DCE will return current mode setting, followed by the OK result code.

   AT+FCLASS=?

	  DCE will return permitted modes. The response is:

	       0,2,8
	       OK

	  with <CR><LF> between each line.

   ATA (with AT+FCLASS=8)

	  This command causes DCE to answer the phone. DCE will return VCON
	  result code immediately.

   ATD (with AT+FCLASS=8)

	  This command causes the DCE to dial a phone number.

	  Result codes:

	      VCON: The DCE issues this result code when the DCE
		    has determined that the remote station is off hook.

	      NO ANSWER: The DCE issues this result code when the DCE has
			 continuously detected Ringbacks for the S7 specified
			 amount of time.


   ATH (with AT+FCLASS=8)

	  This command causes the DCE to hang up the phone with the following
	  considerations for a hang up while in Voice mode:

	  - Force the command AT+FCLASS=0, but will not destroy any of the
	    Voice parameters.

	  - Force voice I/O device to Telco line.

   AT+VNH=<value>

	  This command causes the DCE to disable or enable automatic hang-ups
	  to a varying degree in the DATA and FAX modes.

	<value> = 0 (Default), the DCE shall not disable automatic hang-ups.

	<Value> = 1, the DCE shall disable automatic hang-ups. This behavior
		  shall persist until the DTE issues ATH, ATZ, or AT+VIP
		  command, or DTR drop.
		  The DCE shall perform on hook on a ATH command.

	<Value> = 2, the DCE shall disable automatic hang-ups. This behavior
		  shall persist until the DTE issues ATH, ATZ, or AT+VIP
		  command, or DTR drop.
		  The DCE shall not perform on hook on a ATH command.


   AT+VNH?

	  DCE will return current hang up setting, followed by the OK result code.

   AT+VNH=?

	  DCE will return permitted hang-up modes. The response is:

	  0-2
	  OK

	  with <CR><LF> between each line.

   ATZ

	  This command causes the DCE to enter DATA MODE (AT+FCLASS=0) and
	  set all of the voice related parameters to their default values.



   Voice mode commands
   --------------------

   AT+VBT=<value>

	  This command causes the DCE to set the default DTMF/tone generation
	  duration used in conjunction with AT+VTS command.

	  The range of the <value> is from 1 to 255. The units are 0.1 seconds.

	  Result codes:

	  OK :	 The DCE issues this result code if DCE accept this command.
	  ERROR: The DCE issues this result code if <value> parameter is out
		 of range.

   AT+VBT?

	  DCE will return current beep duration setting, followed by the OK
	  result code.

   AT+VBT=?

	  DCE will return permitted values of beep duration. The response is:

	      1-255
	      OK

	  with <CR><LF> between each line.

   AT+VIP

	  This command causes the DCE to initialize all the Voice parameters
	  to the default settings as follows:

	       Compression method: 2-bit ADPCM
	       Silent thresthod  : 15
	       Activity Timer	 : 7 sec.
	       Silence interval  : 7 sec.
	       Ringback gone away timer : 7 sec.
	       Ringback never appear timer : 5.7 sec.
	       Default beep tone duration : 1 sec.


	  Result codes:

	  OK :	 The DCE issues this result code if DCE accept this command.
	  ERROR: The DCE issues this result code if the DCE is not connected
		 to at least one Voice I/O devices.


   AT+VLS=<device>


	  This command causes the DCE to select a voice I/O device.

	  The permitted <device> is as follows:

	  0: disconnect all I/O devices
	  2: Telco line
	  8: External Mic. (connect a Mic to dial-up line RJ-11 jack)
	  16: Internal Speaker

	  Result codes:

	  OK :	 The DCE issues this result code if DCE accept this command.
	  ERROR: The DCE issues this result code if <device> is not
		 permitted.

   AT+VLS?

	  DCE will return current I/O device followed by the OK
	  result code.

   AT+VLS=?

	  DCE will return permitted I/O devices. The response is:

	  0,2,8,16
	  OK

	  with <CR><LF> between each line.

   AT+VRA=<value>

	  This command set the amount of time the DCE shall wait between
	  Ringbacks before the DCE can assume that the remote station
	  has gone off hook. The default value is 70 (7 seconds).

	  The range of the <value> is from 0 to 255. The units are 0.1 second.
	  A value of zero force the DCE to return VCON immediately after the
	  ATD command is received.

	  Result codes:

	  OK :	 The DCE issues this result code if DCE accept this command.
	  ERROR: The DCE issues this result code if <value> is out
		 of range.

   AT+VRA?

	  DCE will return current Ringback Goes Away Timer, followed by the OK
	  result code.

   AT+VRA=?

	  DCE will return permitted interval of Ringback Goes Away Timer.

	  The response is:

	    0-255
	    OK

	  with <CR><LF> between each line.

   AT+VRN=<value>

	  This command set the amount of time the DCE will wait looking for
	  Ringback. If the DCE does not detect a Ringback in this time period,
	  the DCE shall assume that the remote station has gone off hook.

	  The range of the <value> is from 0 to 255. The units are 0.1 second.
	  A value of zero force the DCE to return VCON immediately after the
	  ATD command is received.

	  Result codes:

	  OK :	 The DCE issues this result code if DCE accept this command.
	  ERROR: The DCE issues this result code if <value> is out
		 of range.

   AT+VRN?

	  DCE will return current Ringback Never Appeared Timer, followed by the OK
	  result code.

   AT+VRN=?

	  DCE will return permitted interval of Ringback Never Appeared Timer.

	  The response is:

	     0-255
	     OK

	  with <CR><LF> between each line.

   AT+VRX

	  This command causes the DCE to start the voice reception process.

	  The DCE begins the voice receive mode by returning the CONNECT result
	  code to the DTE. After this report, the DCE sends <DLE> shielded
	  Voice data to the DTE.

	  The DTE can abort the voice receive state by sending a character other than
	  <XON> and <XOff>. On termination of the voice receive state, the DCE
	  will append a <DLE><ETX> character pair, followed by the VCON result
	  code.

   AT+VSD=<sds>,<sdi>

	  This command causes the DCE to set the silence detection sensitivity
	  , and the required period of silence before the DCE can report silence
	  detected at the end of a voice receive either with the QUIET or SILENCE
	  <DLE> shielded code.

	  See the description of the <DLE> shielded code for the difference between
	  SILENCE and QUIET report.

	  The range of the sensitivity <sds> is from 0 to 31. Larger values of this
	  parameter imply that the DCE want to treat noisier conditions as silence.
	  A value of zero disables the DCE silence detection; the DCE shall not
	  report QUIET or SILENCE <DLE> shielded code.

	  The range of the interval <sdi> is from 0 to 255 in units of 0.1 seconds.

	  Result codes:

	  OK: The DCE issues this result code if DCE accept this command.
	  ERROR: The DCE issues this result code if the <sds> or <sdi> is out
		 of range.

    AT+VSD?

	  This command causes the DCE to report current <sds> and <sdi> settings.
	  The form of the response is:

	      <sds>,<sdi>
	      OK

	  with <CR><LF> between each line.

    AT+VSD=?

	  This command causes the DCE to report the permitted range of <sds>
	  and <sdi>. The response is:

		 (0-31),(0,255)
		 OK

	  with <CR><LF> between each line.


    AT+VSM=<cml>

	  This command causes the DCE to select a compression method as follows:

	      <cml> = 1, 9.6 KBps CELP (Code Excited Linear Prediction)

	      <cml> = 2 (Default), 19.2 KBps 2-bit ADPCM

	      <cml> = 3, 28.8 KBps 3-bit ADPCM

	  Note: Only E-Plus model supports CELP mode.

    AT+VSM?

	  This command causes the DCE to report current compression
	  setting in the following form:

	     <cml>;<scs>;<vsr>
	     OK

	  with <CR><LF> between each line. Where:

	  <cml>: compression method label.
	  <scs>: silence compression sensitivity.
	  <vsr>: voice sampling rate.

    AT+VSM=?

	  This command causes the DCE to report the compression methods
	  supported. The response is as follows:

	   1;CELP;1;0;(9600)
	   2;ADPCM;2;0;(9600)
	   3;ADPCM;3;0;(9600)
	   OK

	  with <CR><LF> between each line.


    AT+VTS=<string>

	  This command causes the DCE to produce DTMF and other tones.

	  The tone generation string shall consist of elements in a
	  list with each element seperated by commas. Each element can
	  be:

	    1) A single ASCII character in the set, 0-9, A-D, #, and *.
	       The DCE shall interpret the ASCII character as a DTMF
	       digit with a duration given by AT+VBT command.

	    2) Three numbers seperated by commas and enclosed in square
	       brackets. The DCE shall interpret the first and the second
	       number as the frequency of the dual tone, and the third one as
	       the duration of the tone.

	       The frequency range is from 200 Hz to 3300 Hz, a frequency of
	       zero means silence. The range of the duration is from 0 to 255
	       in units of 0.1 seconds.


	    3) A single ASCII character and a number, seperated by commas and
	       enclosed in curly braces. The DCE should interpret the ASCII
	       chracter as a DTMF digit, and the number as the duration of the
	       tone.


    AT+VTS=?

	  This command causes the DCE to report the allowable tone string
	  elements. The response is as follows:

	      (0,200-3300),(0,200-3300),0-9,A-D,*,#
	      OK

	  with <CR><LF> between each line.


    AT+VTX

	 This command causes the DCE to start voice transmission process.

	 The DCE begins the voice transmit mode by returning the CONNECT result
	 code to the DTE. After this report, the DCE accepts <DLE> shielded
	 Voice data from the DTE.

	 The DTE can abort the voice transmit state by sending a <DLE><ETX>
	 character pair to the DCE. On termination of the voice transmit state,
	 the DCE will send the VCON result code.



     <DLE> shielded codes
    ----------------------

       In voice transmit/receive mode, BYSYNC protocol should be applied
       to the data stream to/from DCE. During this period, commands and
       responses will be in <DLE> shielded form. The supported <DLE> shielded
       codes are as follows (all <DLE> shield codes are case sensitive):

       commands:

       <DLE><ETX>: terminate trasmission process.

       responses:

       <DLE>0: DTMF '0' received
       <DLE>1: DTMF '1' received
       <DLE>2: DTMF '2' received
       <DLE>3: DTMF '3' received
       <DLE>4: DTMF '4' received
       <DLE>5: DTMF '5' received
       <DLE>6: DTMF '6' received
       <DLE>7: DTMF '7' received
       <DLE>8: DTMF '8' received
       <DLE>9: DTMF '9' received
       <DLE>#: DTMF '#' received
       <DLE>*: DTMF '*' received
       <DLE>c: T.30 calling tone received
       <DLE>b: Busy tone received

       <DLE>q: Quiet detected. The DCE has determined that there was voice
	       energy present at the the beginning of the voice recording
	       session followed by a period of silence greater than the amount
	       of time selected by AT+VSD command.

       <DLE>s: Silence detected. The DCE has determined that there was no voice
	       energy present at the the beginning of the voice recording
	       session followed by a period of silence greater than the amount
	       of time selected by AT+VSD command.



    Examples of voice mode operation
   ---------------------------------

  1. Greeting message recording (Put a MIC into dial-up line RJ-11 jack)

	    DTE 		   DCE		 comments
	 -------------	       -----------    ---------------------
	 AT+FCLASS=8	--->		       Swich to VOICE MODE
			<---	   OK

	 AT+VSM=?	--->
			      1;CELP;1;0;(9600)
			      2;ADPCM;2;0;(9600)
			      3;ADPCM;3;0;(9600)

			<---	  OK
	 AT+VSM=1	--->		       select CELP compression method
			<---	  OK

	 AT+VLS=8	--->		       Activate internal MIC.
			<---	   VCON
	 AT+VRX 	--->		       Start to record
			<---	   CONNECT
			<---	   <DATA>
	 AT		--->		       Stop recording
			<---	   <Data>
			<---	   <DLE><ETX>
			<---	   VCON        return to commnad state
	 AT+VLS=0	---->		       Deactivate intrnal MIC
			<---	   OK
	 AT+FCLASS=0			       Return to Data Mode
			<---	   OK


  2. Voice file playing via internal speaker

	    DTE 		   DCE		    comments
	 -----------	     -----------------	-------------------
	 AT+FCLASS=8	--->		       Swich to VOICE MODE
			<---	   OK
	 AT+VSM=?	--->
			      1;CELP;1;0;(9600)
			      2;ADPCM;2;0;(9600)
			      3;ADPCM;3;0;(9600)
			<---	  OK
	 AT+VSM=1	--->		       select CELP compression method
			<---	  OK

	 AT+VLS=16	--->		       Activate internal speaker
			<---	   VCON
	 AT+VTX 	--->		       Start to Play
			<---	   CONNECT
	 <DATA> 	--->
	 <DLE><ETX>	--->
			<---	   VCON        return to commnad state
	 AT+VLS=0	--->		       Deactivate intrnal speaker
			<---	   OK
	 AT+FCLASS=0			       Return to Data Mode
			<---	   OK

  3. Voice file playing via line

	    DTE 		   DCE		 comments

	 AT+FCLASS=8	--->		       Swich to VOICE MODE
			<---	   OK
	 AT+VSM=?	--->
			      1;CELP;1;0;(9600)
			      2;ADPCM;2;0;(9600)
			      3;ADPCM;3;0;(9600)
			<---	  OK
	 AT+VSM=1	--->		       select CELP compression method
			<---	  OK

	 AT+VLS=2	--->		       connect to line
			<---	   VCON
	 AT+VTX 	--->		       Start to Play
			<---	   CONNECT
	 <DATA> 	--->
	 <DLE><ETX>	--->
			<---	   VCON        return to commnad state
	 AT+VLS=0	--->		       Deactivate intrnal speaker
			<---	   OK
	 AT+FCLASS=0			       Return to Data Mode
			<---	   OK

  4. Answering machine (Voice call)

	    DTE 		   DCE		 comments

	 AT+FCLASS=8	--->		       Swich to VOICE MODE
			<---	   OK
	 AT+VSM=?	--->
			      1;CELP;1;0;(9600)
			      2;ADPCM;2;0;(9600)
			      3;ADPCM;3;0;(9600)
			<---	  OK
	 AT+VSM=1	--->		       select CELP compression method
			<---	  OK

	 AT+VLS=2	--->		       connect to line
			<---	   VCON
	 AT+VTX 	--->		       Start to Play greeting message
			<---	   CONNECT
	 <DATA> 	--->
	 <DLE><ETX>	--->
			<---	   VCON        return to commnad state

	 AT+VTS=[933,0,12]  --->	       DTE anotates the greeting messgae
					       with a 1.2 second beep
			<---	  OK

	 AT+VRX 	--->		       Start to record
			<---	   CONNECT
			<---	   <DATA>
			<---	   <DLE>b      DCE detect busy tone
				     or 	      or
				   <DLE>q      long period of quiet
	 AT		---->		       Stop recording
			<---	   <DATA>      DCE deliver remaining data
			<---	   <DLE><ETX>
			<---	   VCON        return to commnad state

	 AT+VLS=0	--->		       Deactivate intrnal speaker
			<---	   OK
	 AT+FCLASS=0			       Return to Data Mode
			<---	   OK



  5. Answering machine (Fax call)


	    DTE 		   DCE		 comments

	 AT+FCLASS=8	--->		       Swich to VOICE MODE
			<---	   OK
	 AT+VSM=?	--->
			      1;CELP;1;0;(9600)
			      2;ADPCM;2;0;(9600)
			      3;ADPCM;3;0;(9600)
			<---	  OK
	 AT+VSM=1	--->		       select CELP compression method
			<---	  OK

	 AT+VLS=2	--->		       connect to line
			<---	   VCON
	 AT+VTX 	--->		       Start to Play greeting message
			<---	   CONNECT
	 <DATA> 	--->
			<---	   <DLE>c      T.30 calling tone detected
				    or			 or
				   <DLE>5      DTMF digit '5' detected
	 <DATA> 	--->
	 <DLE><ETX>	--->
			<---	   VCON        return to commnad state

	 AT+FCLASS=2	--->		       Try to handshake Fax mode
			<---	   OK
	 ATA		--->
		    Swich to Fax mode and answer fax call
				    .
				    .
				    .

  6. Answering machine (Data call)


	    DTE 		   DCE		 comments

	 AT+FCLASS=8	--->		       Swich to VOICE MODE
			<---	   OK
	 AT+VSM=?	--->
			      1;CELP;1;0;(9600)
			      2;ADPCM;2;0;(9600)
			      3;ADPCM;3;0;(9600)
			<---	  OK
	 AT+VSM=1	--->		       select CELP compression method
			<---	  OK

	 AT+VLS=2	--->		       connect to line
			<---	   VCON
	 AT+VTX 	--->		       Start to Play greeting message
			<---	   CONNECT
	 <DATA> 	--->
	 <DATA> 	--->
	 <DLE><ETX>	--->
			<---	   VCON        return to commnad state
	 AT+VRX 	--->		       Start to record
			<---	   CONNECT
			<---	   <DATA>
			<---	   <DLE>s      DCE detect silence
	 AT		---->		       Stop recording
			<---	   <DATA>      DCE deliver remaining data
			<---	   <DLE><ETX>
			<---	   VCON        return to commnad state
		      (DTE delete this silence file)
	 AT+FCLASS=0	--->
			<---	   OK

	 ATA		--->		       Try to handshake data mode
		    Swich to data mode and answer data call
				    .
				    .
				    .