TMED is copyrighted 1992 by Liang Chen. No portion of this program may be
  reproduced without the written permission of Liang Chen. It is a
  shareware now. If you find it is useful and continue to use it, please
  send $20 registration fee at following address

                        Liang Chen
                        3227 Middlesex, Apt C
                        Toledo, OH 43606
                        USA

                        lchen2@uoft02.utoledo.edu

  Good suggestion for major enhancement from the user are welcomed. If it
  is implemented in the future TMED version, you can have it for free.
  There is no fee charged for upgrade.

  STANDARD DISCLAIMERS: THE COPYRIGHT HOLDER OFFERS NO WARRANTY WITH THIS
  PROGRAM WHATSOEVER. NEITHER SHALL HE BE LIABLE FOR DAMAGES OF ANY KIND
  THAT MAY ARISE FROM ITS USE.




                                 INTRODUCTION

  TMED is a TSR memory editor which takes 8K memory when is loaded. It
  can be used as an auxiliary debugging tool for programmers, or
  sometime as a gamebuster. TMED can view what is in the memory and edit
  the memory while other programs are running. TMED works great with
  Turbo Debugger.

  TMED versions after 1.20 come with a key macro function. Since TMED is
  resident in the memory, this key macro function may be used for any
  other foreground running programs. But if the foreground programs also
  hook to the INT08, INT09 handlers and use it heavily, the time delay
  by the foreground program may cause problems for the macro function.
  This is because a BIOS problem that some keys are overwritten before
  it can be read.


  WARNING:  TMED is not bug proof. The system may halt due to an
            improper operation (such as editing or loading in critical
            memory area, set wrong breakpoints, enter wrong data, etc.).
            Not all people will benefit from this program. You have to
            know something about programming in order to make full use
            of it.


                                  OPERATION

  LOADING:

            Enter 'TMED' at DOS prompt, then press <RETURN>.


  INVOCATION:

            There are two ways to invoke the TMED, a) Hotkey: press left
            <Ctrl> key twice; b) Breakpoint; it will pause and invoke
            TMED when DOS runs to breakpoint (See how to set breakpoint
            in the following instructions). If the invocation is
            successful, TMED will display a memory page (256 bytes) in
            hex and ascii codes and the command options.

            (Try to run TMED as a TSR now and activate it (press the
            left <Ctrl> key twice) while you are reading this file. It
            will help you understand the following commands.)


  KEY MACRO FUNCTIONS:

            Macro function may be used any time when the TMED is in
            resident. The macro buffer are big enough for 192 keys.

            Press Mky1 (default F11 key) once to record the key macro
            (you will hear a short sound). Press F11 again will end
            macro recording mode (you will hear a longer sound).

            Press Mky2 (default F12 key) will execute the key macro.
            There is no time delay while executing the key macro.

            If you press Mky2 key while macro is in recording mode, then
            it is a recursive macro. For example, you can let a
            recursive macro continuously turns page for you. While
            a recursive macro is executing, press any key will stop the
            macro running.

            Mky1 and Mky2 may be assigned to other keys (see below), in
            case these keys are used by the foreground running programs.


  COMMANDS:
            Commands are invoked by pressing the <Alt> key with the upper
            case letter in the command option line.


      TMED: <Alt>-T will display the TMED data segment. The cursor will
            be placed at the first byte of the string input buffer. To
            reduce the size of TMED, some data are entered by editing
            the corresponding memory addresses in the data segment.
            Useful information shown in this page and next page are:

                  Mode:XBodc:X        Editing mode and screen board
                                          color.
                                          May be changed by editor.

                  Txtc:XHilc:X        Text color and highlight
                                          color. highlight color are
                                          used to display bytes in
                                          memory that are different from
                                          the saved buffer or dumped
                                          file. The saved memory buffer
                                          is 256 bytes (a page). May be
                                          changed by editor.

                  Swpg:XSwmd:X        Switch page and video mode
                                          when TMED is invoked. TMED
                                          will try to work in different
                                          video page. If it does not
                                          work normally, try different
                                          Txtc, Hilc, Swpg. TMED does
                                          not save the original screen.
                                          After quit TMED, programs will
                                          operate as before the popup.
                                          But the graphic display and
                                          colors may be changed. May be
                                          changed by editor.


                                          NOTE: AFTER CHANGING THE SWPG,
                                          ALL DISPLAY WILL OUTPUT TO THE
                                          NEW PAGE. YOU SHOULD QUIT
                                          EDITOR MODE AND TMED, THEN
                                          POPUP AGAIN.

                  Odpg:XOdmd:X        Old video mode and page before
                                          popup. Please do not change it.

                  Endc:XWldc:X        The ending char and the wild
                                          char in the search string. By
                                          default, ending char is hex
                                          00; wild char is hex FF. For
                                          example, to find

                                               instruction        hex

                                               cmp     al,XX      3C XX
                                               jne     XX         75 XX

                                          the search string may be
                                          entered as (in hex)

                                               3C FF 75 00

                                          Endc and Wldc may be changed
                                          by editor.

                  Ustc:XCsrc:X        Unset breakpoint byte and
                                          cursor color. By default, Ustc
                                          is hex 'CD' (hex code for
                                          interrupt 'int'); May be
                                          changed by editor.


                  AX= XXBX= XX        The register values before popup
                  CX= XXDX= XX        or breakpoint.
                  SI= XXDI= XX

                  CS= XXIP= XX        CS:IP, next instruction address
                                          after breakpoint pause.

                  Line of input:        16 bytes string buffer for 'Find'
                  XXXXXXXXXXXXXXXX        command. Using editor
                                          to change the string.

                               (next memory page)

                  Seg1XXSeg2XX        Search start and end segment
                                          addresses. By default, Seg1 is
                                          set to the top memory address of
                                          TMED; Seg2 is set to A000, ie.,
                                          the top of the conventional
                                          memory.
                                          May be changed by editor.

                  GadrXXPadrXX        Current and previous addresses.
                  DadrXXJadrXX        Memory dump and relative jump
                                          start addresses.
                                          May be changed by editor.

                  Mky1XXMky2XX        Scan codes of Mky1 and Mky2.
                                          May be changed to other keys by
                                          the editor.

                  MadrXXKadrXX        Memory and KeyMacro buffer
                                          addresses.

                  KnumXXSflgXX        Knum = Macro key number.
                                          Sflg = sound flag.
                                               = 0      sound off
                                               = 1      sound on (default)
                                          May be changed by editor.

                  SnhiXXSnlwXX        Beep sound high and low tones.
                                          May be changed by editor.

                  DmpfXXXX.XXX           ASCIIZ dump file name.
                                          May be changed by TMED editor.

      You may find other variables in the TMED data area. But these data
      are not explained and marked. You are supposed not to change them.

      ALPHA/HEX MODE:  Change editing modes.

      EDIT:       Invoke the alpha/hex memory editor to edit current
                  memory page (not ROM). <ESC> or <ENTER> to quit edit
                  mode. Using direction keys to move cursor.


      FIND/NEXT:  <Alt>-F will find the first string that you entered in
                  the search string buffer between the memory addresses
                  of Seg1 and Seg2. <Alt>-N will find the next string.


      GOTO/JUMP/PREVIOUS: <Alt>-G will read a new segment address from
                  the keyboard (in hex, no echo), then go to the new
                  address; <Alt>-J will read a relative jump address
                  from the keyboard (in hex, no echo), then jump to the
                  new address. The actual address is affected by the
                  base address saved in Jadrs; <Alt>-P will goto
                  previous address.

      DUMP/COMPARE/MORE: <Alt>-D will dump 64k (256 pages) memory start
                  from current page to the dump file; <Alt>-C will enter
                  the comparing mode and compare the dump file with the
                  current memory. The changed memory bytes are displayed
                  in highlight color; <Alt>-M will move to next page
                  that has changes; <Alt>-C again will quit comparing
                  mode.

      CONVERT:    Convert decimal number ( < 65535 ) at the string
                  buffer to hex code. Useful when try to find the stored
                  game score addresses and cheat the game.

      KEYCODE:    <Alt>-K once, the string buffer will display the scan
                  code of any key input that follows. <Alt>-k again will
                  exit. Macro recording in this mode will just record
                  the keystrokes.

      RESTORE:    Restore the byte at current cursor position from the
                  memory buffer to the memory.

      SETBREAKPOINT/IP: <Alt>-S will set the break point at current
                  cursor position; <Alt>-I will goto the breakpoint that
                  invoked TMED. The breakpoint byte may also be changed
                  by the editor. Tips for activating TMED when play
                  games: if hotkey works, fine; if hotkey does not work,
                  use a binary editor put 'CC' in the game executable
                  file (be sure you keep a copy of it).

                  Please note that if the breakpoint you set is not the
                  first byte of an executable instruction, unpredictable
                  results will be seen as program execution passes
                  through the breakpoint. A breakpoint in a ROM area
                  will not operate since instructions in ROM cannot be
                  replaced with a breakpoint instruction.

                  When Turbo Debugger is running, the breakpoints set by
                  TMED will like the breakpoints set by Turbo Debugger.
                  But You have to restore the original codes before
                  executing following instructions.

      Update:     <Alt>-U will update the current memory page.

      LOAD:       <Alt>-R will restore the dumped memory region from the
                  dumped file.

      Boot:       <Alt>-B will do a warm boot.

      Quit:       <Alt>-Q will quit TMED.

      (Operation):<Alt>-O will toggle between the foreground mode and
                  background operation mode. There is no screen output
                  in a background operation mode, but all other command
                  options (include the macro function) are still
                  available when TMED is invoked. This mode is useful
                  when the foreground running programs is in graphic mode
                  and you do not want destroy the screen.


                               ACKNOWLEDGEMENT

      The original TSR shell I used for TMED was written by Thomas
      Brandenborg (filename TSRDEMO2.ARC on simtel20 site). His copyright
      and address are included below

            Copyright 1987 by Thomas Brandenborg. All Rights Reserved.

             Thomas Brandenborg
             Lundbyesgade 11
             DK-8000 Aarhus C
             DENMARK


                                 WHAT IS NEW?

                       Major revisions in version V1.5C
                                  (10/23/92)

      1)    Now TMED can be operated in completed background mode. When the
            foreground running program is in graphic mode the screen will
            not be distroyed, since there is no screen output.

      2)    Some bugs in key macro function are fixed.


                       Major revisions in version V1.4C
                                  (10/16/92)

      1)    The screen output speed is simply three times faster than the
            old version.


                       Major revisions in version V1.3A
                                  (10/12/92)

      1)    A major bug fixed in the key macro function.


                       Major revisions in version V1.2H
                                  (10/9/92)

      1)    Add key macro function to TMED.

      2)    Commands are now invoked by press <Alt> key and the upper
            letters in the command option line. This avoids the confusion
            of commands and data entry operation.


                       Major revisions in version V1.10
                                  (9/25/92)

      1)    Fix the bottom display shift-up problem when using the Compare
            command without dumping the memory first (or tmed.dmp file not
            found in current directory).

      2)    Allow cursor has different color from the highlight text color.

      3)    Some improvement in the display.