||||| Scan It |||||

                       Version 1.1

                       Readme.doc


     Scan It was written to print barcode labels to a thermal
printer. With version 1.0, only code 39 can be printed on a
3/4" x 2.25" label. It has the ability to take an input from
a barcode reader and send the data to the thermal printer for
barcode duplication. You can also manually input data through
the keyboard that will be transposed into barcode form and
printed.


                    Hardware Setup


     Scan It was originally designed to work with an Intermec
model 9510 barcode reader and an Eltron thermal barcode
(parallel) printer, but should work with other makes.

     Hardware setup is simple. The barcode reader must be
connected to COM1 and configured to 2400 baud, 8 Bits, No
Parity. The printer must be connected to LPT1. That's it!


                    Software Setup


     Before running Scan It, use the DOS Mode command to set
COM1 at 2400 baud, 8 Bits, No Parity. See your DOS manual for
more information on Mode.

     To start Scan It, at the DOS command prompt type
"Scan-It1" without the quotes. After the welcome screen is
displayed, Scan It will present the main menu. Just select
your choice and Scan It will do the rest! We feel that it is
so simple to use, there is no need for an explanation.
However, if you get stuck, you can contact me at (609) 547-
1600 between the hours of 8:00am to 4:40pm Eastern time.


     Watch for future versions of Scan-It that will allow you
to print different barcodes on different size labels.  Also,
if you have a particular application request, please feel
free to call the number above.