Chernobyl' 

     In April 1986, Chernobyl' (Chornobyl' in Ukrainian) was an
obscure city on the Pripiat' River in north-central Ukraine. 
Almost incidentally, its name was attached to the V.I. Lenin
Nuclear Power Plant located about twenty-five kilometers
upstream.
     On April 26, the city's anonymity vanished forever when,
during a test at 1:21 A.M., the No. 4 reactor exploded and
released thirty to forty times the radioactivity of the atomic
bombs dropped on Hiroshima and Nagasaki.  The world first learned
of history's worst nuclear accident from Sweden, where abnormal
radiation levels were registered at one of its nuclear
facilities. 
     Ranking as one of the greatest industrial accidents of all
time, the Chernobyl' disaster and its impact on the course of
Soviet events can scarcely be exaggerated.  No one can predict
what will finally be the exact number of human victims.  Thirty-
one lives were lost immediately.  Hundreds of thousands of
Ukrainians, Russians, and Belorussians had to abandon entire
cities and settlements within the thirty-kilometer zone of
extreme contamination.  Estimates vary, but it is likely that
some 3 million people, more than 2 million in Belarus' alone, are
still living in contaminated areas.  The city of Chernobyl' is
still inhabited by almost 10,000 people.  Billions of rubles have
been spent, and billions more will be needed to relocate
communities and decontaminate the rich farmland.
     Chernobyl' has become a metaphor not only for the horror of
uncontrolled nuclear power but also for the collapsing Soviet
system and its reflexive secrecy and deception, disregard for the
safety and welfare of workers and their families, and inability
to deliver basic services such as health care and transportation,
especially in crisis situations.  The Chernobyl' catastrophe
derailed what had been an ambitious nuclear power program and
formed a fledgling environmental movement into a potent political
force in Russia as well as a rallying point for achieving
Ukrainian and Belorussian independence in 1991.  Although still
in operation, the Chernobyl' plant is scheduled for total
shutdown in 1993.


                                                  
                                                       40
Not for publication                                              
                                                  Secret
          
                                        21 Feb. 79  05363
                                        Return to the General
                                        Section of the Central
                                        Committee of the CPSU
                                             
                                   Central Committee of the CPSU
                              
  USSR COMMITTEE OF STATE SECURITY [KGB]     
  February 21, 1979   No. 346-A
               Moscow

Construction Flaws at the Chernobyl Nuclear Power Plant [AES]
     
     According to data in the possession of the KGB of the USSR,
design deviations and violations of construction and assembly
technology are occurring at various places in the construction of
the second generating unit of the Chernobyl AES, and these could
lead to mishaps and accidents.

     The structural pillars of the generator room were erected
with a deviation of up to 100 mm from the reference axes, and
horizontal connections between the pillars are absent in places.
Wall panels have been installed with a deviation of up to 150 mm
from the axes.  The placement of roof plates does not conform to
the designer's specifications.  Crane tracks and stopways have
vertical drops of up to 100 mm and in places a slope of up to 8.
     
     Deputy head of the Construction Directorate, Comrade V. T.
Gora, gave instructions for backfilling the foundation in many
places where vertical waterproofing was damaged.  Similar
violations were permitted in other sections with the knowledge of
Comrade V. T. Gora and the head of the construction group,
Comrade IU. L. Matveev.  Damage to the waterproofing can lead to
ground water seepage into the station and radioactive
contamination of the environment.

     The leadership of the Directorate is not devoting proper
attention to the foundation, on which the quality of the
construction largely depends.  The cement plant operates
erratically, and its output is of poor quality.  Interruptions
were permitted during the pouring of especially heavy concrete
causing gaps and layering in the foundation.  Access roads to the
Chernobyl AES are in urgent need of repair.

     Construction of the third high-voltage transmission line is
behind schedule, which could limit the capacity utilization of
the second unit.

     As a result of inadequate monitoring of the condition of
safety equipment, in the first three quarters of 1978, 170
individuals suffered work-related injuries, with the loss of work
time totalling 3,366 worker-days.

     The KGB of Ukraine has informed the CPSU Central Committee
of these violations.  This is for your information.


Chairman of the Committee [KGB]       [signed] IU. Andropov       
...............................................................

                                                             42
                                               Secret
                                          Copy no. 1
       USSR MINISTRY OF 
     POWER AND ELECTRIFICATION
       (MINENERGO USSR)               Central Committee CPSU     

     
     Kitaiskii pr. 7
     Moscow, K-74  103074                      
     Minenergo USSR                          Central Committee
                                             of the CPSU
     Moscow K-11  A.T. 112604                  MAR. 16, 79  07738
     3-16-79  No. 1381-2c                    Return to General   
No. ____  from  ______                       Section of the 
                                             Central Committee

Checking the structural condition of the first unit of the
Chernobyl AES. 

     At the instruction of the USSR Minister of Power and
Electrification, a commission under the chairmanship of Deputy
Minister Comrade F. V. Sapozhnikov was formed to check the
quality of construction and assembly work on the first unit of
the Chernobyl AES.

     The commission visited the site on March 5-6, 1979, and
examined the state of the buildings and structures of the first
unit of the Chernobyl AES and the notes on the quality of
construction and assembly work.

     The Commission found that violations of construction
technology and design deviations have been documented.

     In each specific instance, engineering solutions were
adopted (in the construction, the operation, or by the designers)
to eliminate deviations and make the structures conform to the
specifications of the original design and normative documents.

     Some of the measures have been realized; the rest of the
work is being completed according to a rigid timetable set by the
commission.

     At the present time the power station is operating
successfully, and there are no hindrances to its further
operation.

     Taking into account the specifics of nuclear power stations,
and attaching primary significance to the reliability and safety
of their operations, the USSR Ministry of Power and
Electrification has issued an order to enhance monitoring of
technical standards observance and the quality of construction
and assembly work at all AESs under construction.

     A letter of similar content was sent to the Central
Committee of the Communist Party of Ukraine.


Deputy Minister          [signed]  P. P. Falaleev
................................................................

                                                  Secret


                    CENTRAL COMMITTEE OF THE CPSU

          Defects in the Construction of the Chernobyl AES

     Chairman of the KGB of the USSR, Comrade IU. V. Andropov,
reports about the low quality of construction work on various
sections of the second unit of the Chernobyl AES of the USSR
Ministry of Power and Electrification.

     As instructed, Comrade Minister P. S. Neporozhnii has formed
a special commission under the leadership of Deputy Minister
Comrade Sapozhnikov to examine and carefully analyze the facts
cited.  The commission visited the site to conduct a thorough
investigation of design deviations and to inspect the system of
monitoring the quality of construction and assembly work.

     It was found that in erecting individual pillars, wall
panels, and crane track stopways, there indeed were instances of
deviation from the reference axes and substandard construction
practices.  Most of these deviations were exposed by the design
inspectorate of the Gidroproekt Institute and a technical site
inspection, and they were documented.
     
     The Chernobyl AES construction directorate along with the
design organization and client have adopted coordinated
engineering solutions ensuring design reliability and
construction quality.  Some of the deviations have been
eliminated, and the rest of the measures are being carried out. 
A timetable under the control of the Ministry leadership has been
established to eliminate the noted deficiencies.

     The specialists conclude that at present there are no
obstacles to the subsequent operation of the Chernobyl AES, and
the electric power station is operating reliably.

     To raise the quality of construction and assembly work and
strengthen control over fire and radiation safety, the Ministry
has published instructions stipulating strict verification of the
quality of work at AES construction sites by Ministry
commissions, enhancing quality inspection laws, training
engineers and technicians, strengthening fire-fighting
procedures, and monitoring observation of safety regulations.

     ....

     The Central Committee of the Communist Party of the Ukraine
has been informed of the measures taken by the ministry.

Head of the Section of Machine Building of the
Central Committee of the CPSU.     [SIGNATURE]    (V. Frolov)

March "23", 1979

Nos. 05363,07738,
     60A/II.