FASTA20.SYS, A SOLUTION TO USING SOME FAST MACHINES WITH QEMM-386

	  Some fast computers which can run at 66 MHZ, have a bug in their 
BIOSes.  When you use Function 87 of Interrupt 15, the BIOS call which you use 
to move data into extended memory, the BIOS does not wait long enough for the 
8042 (the keyboard controller chip, a port of which you use to enable/disable 
address line A20, the address line you must enable to use any memory above one 
megabyte) to enable the A20 address line.  Because the 8042 is typically slow, 
QEMM-386 always enables it twice when it must enable it.  When you run such a 
computer at the 66 MHz speed, it does not give the 8042 enough time to honor 
the BIOS's request to enable line A20 so when you try to use any of the memory 
you need to enable line A20 to use (all even megabytes), then try to use this 
memory, you crash.
     This device driver, FASTA20.SYS, hooks Int 15, and, when a function 87 
comes in, does an enable of A20 so that by the time the BIOS enables A20, it 
will be the second time, and, by the time the machine expected to have enabled 
A20, it will be ready.
     Load this driver in the CONFIG.SYS before QEMM386.SYS:

     device=c:\qemm\fasta20.sys
     device=c:\qemm\qemm386.sys ram st:m

     Currently the only machine we know this works on is the Swan 486DB.  But 
the problem and this solution are generic and you do yourself no harm by 
trying loading FASTA20.SYS before QEMM-386 if you crash on loading QEMM-386 
when in the clock-doubled mode.
     The reason you do not have this problem with HIMEM/EMM386 is that HIMEM 
enables the A20 line but does not use the memory, while EMM386 uses the 
memory, and enough time has elapsed between HIMEM's enabling of the A20 line 
and EMM386's use of the memory for the 8042 to have enabled A20.
     QEMM-386 enables the A20 line only once, when it loads, so using FASTA20 
entails no performance degradation.

 ************************************************************************
 *This technical note may be copied and distributed freely as long as it*
 *is distributed in its entirety and it is not distributed for profit.  *
 *          Copyright (C) 1993 by Quarterdeck Office Systems            *
 ************************ E N D   O F   F I L E *************************