___________________________________________________________________________
STACKER NOTE                             Stac Electronics Technical Note

Subject: Stacker and Anti-Virus Programs.

Tec037 - 6/22/92
____________________________________________________________________________

Stacker is compatible with anti-virus programs such as Norton Anti-Virus (NAV) 
and Central Point Anti-Virus (CPAV).  However, there a few guidelines to 
follow for them to peacefully coexist. 

I. Installing Stacker.

Before installing Stacker, disable any TSRs and Anti-Virus programs that are
memory resident.  Device drivers such as NAV&.SYS, NAV_.SYS, and VWATCH.SYS
should be disabled by REMarking the drivers in Config.sys and rebooting.  
Failure to disable these could result in an incomplete installation. 

II. Configuring Device Drivers.

It is generally recommended that any anti-virus devices be loaded after the
Stacker device in Config.sys.  Loading devices such as NAV_.SYS before Stacker 
may cause the system to hang while loading the driver.  

III.  Immunization.   

CPAV allows you to "immunize" executables by adding signature information to 
the file. Do not immunize the Stacker driver files.  These files use their 
own signature information for a checksum self check at boot time. Immunizing
the files disrupts this checksum information and prevents them from loading.     
Exempt the files from immunization by adding them to the immunization 
exception list.  Add the following files: STACKER.COM, SSWAP.COM, STACKER.XT, 
STACKER.AT, STACKER.MC.  If these files have been immunized accidently, 
restore them from the Stacker diskette or remove the immunization.

IV. BOOTSAFE from Central Point Anti-Virus:

Bootsafe is Central Point's partition table and boot sector security 
system. Usually loaded in Autoexec.bat, it examines the boot sector and 
partition information of the default drive (usually C:).  If Stacker is 
swapping drive letters, Bootsafe it will attempt to read this information 
on the Stacker logical drive and report: "WARNING partition/boot sector has 
been modified!"   This solution is simply to make Bootsafe look at the 
original boot partition.  The syntax is:     BOOTSAFE d: 
(where d: is the letter of the SSwapped boot drive.)

-----------------------------------------------------------------------------
1992 STAC ELECTRONICS