SHADOW RAM MEMORY CONTROLLERS

                                  supported by


                        THE LAST BYTE MEMORY MANAGER (tm)







                                  Version 2.20










                              Copyright (C) 1990-92
                               All Rights Reserved


                                       by


                              KEY SOFTWARE PRODUCTS

                                440 Ninth Avenue
                          Menlo Park, California 94025
                                  415-364-9847














        The Last Byte Memory Manager is a trademark of Key Software Products.



        



                                TABLE OF CONTENTS



        CHAPTER 1 - INTRODUCTION        ...........................    1
           1.1  Hardware Requirements       .......................    1
           1.2  Supported Chipsets       ..........................    1
              1.2.1  ACC Microelectronics       ...................    1
              1.2.2  AddTech Research (PCChip)      ...............    2
              1.2.3  Appian Technology       ......................    2
              1.2.4  Atmel Corporation       ......................    2
              1.2.5  Chips and Technologies      ..................    3
              1.2.6  EFAR Microelectronics       ..................    3
              1.2.7  ETEQ Microelectronics       ..................    4
              1.2.8  Forex Computer Corporation      ..............    4
              1.2.9  Headland Technology (G2)      ................    5
              1.2.10  Intel Corporation       .....................    5
              1.2.11  Mosel Corporation       .....................    5
              1.2.12  Oak Technology       ........................    5
              1.2.13  OPTi Electronics       ......................    6
              1.2.14  PicoPower Technology       ..................    7
              1.2.15  Silicon Integrated Systems (SiS)     ........    7
              1.2.16  Sun Electronics (SUNTAC)      ...............    7
              1.2.17  Symphony Laboratories       .................    7
              1.2.18  Texas Instruments       .....................    8
              1.2.19  UNIchip Incorporated       ..................    8
              1.2.20  United Microelectronics Corporation (UMC)        8
              1.2.21  VIA Technologies       ......................    8
              1.2.22  VLSI Technology       .......................    9
           1.3  Unsupported Chipsets       ........................   10
              1.3.1  No Shadow Ram Support     ....................   10
              1.3.2  Shadow Ram is not Read/Write    ..............   10
              1.3.3  Overly Complex Control      ..................   10
              1.3.4  Locked Configuration Registers      ..........   11
              1.3.5  Configuration I/O Ports Reassigned     .......   11
           1.4  Checking Compatibility Using CHIPSET     ..........   11





















        




        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                 1


                        CHAPTER 1 - INTRODUCTION        


        1.1 Hardware Requirements        

        To  install The Last Byte Memory Manager, your computer must have
        a  means  of providing read-write memory in the Upper Memory Area
        between  640k  and  1 megabyte.  This is possible if you have any
        of the following: 

             o  Fixed  RAM memory already resident in the upper area
                (such  as  the 32-bit "Built In Memory" installed in
                some Compaq 386 machines), or 

             o  An  expanded memory board (EEMS, LIM 3.2 EMS, or LIM
                4.0 EMS), or 

                        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                        ³ NOTE: Using a LIM 3.2 EMS board is not advised  ³ 
                        ³ as a method of providing upper memory.  It pro- ³ 
                        ³ vides only 64k of upper memory and prevents ap- ³ 
                        ³ plication software from using expanded memory.  ³ 
                        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

             o  A  386sx,  386,  486,  or  486sx  processor  and the
                Microsoft  Windows  3.0/3.1  or  DOS  5  versions of
                EMM386, or 

             o  One  of  the  shadow  ram  memory  controller  chips
                listed in the next section.  


        1.2 Supported Chipsets        

        Key  Software  Products  is  continually  adding  support for new
        chipsets  as  they  become  known to us and technical information
        can  be  obtained.  Those that are currently supported in version
        2.20  are  listed in the paragraphs below.  Some that we know of,
        but which cannot be supported are listed in the next section.  


        1.2.1 ACC Microelectronics        

        The  following  chips  all provide a single block of 64k by using
        the chip set EMS page frame.  

             ACC2036 - Single Chip Solution for the 286 and 386SX
             ACC2121 - From the Turbo PC/AT Chip Set for the 286 and 386SX

        The  following  chip  provides  a  single  block  of 128k between
        E000-FFFF: 



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                 2



             ACC2300 - From the 82300 386 AT Chip Set


        1.2.2 AddTech Research (PCChip)       

        AddTech  chipsets  are  usually  labelled  "PCChip"  or "Hedaka".
        AddTech  designs  their  chips for use on their own motherboards,
        and   they  identify  their  chipsets  by  the  motherboard  part
        numbers.   There  is at least one AddTech chipset that is used on
        two   different  motherboards  with  different  motherboard  part
        numbers.   To  avoid  confusion,  The  Last  Byte  Memory Manager
        refers  to  these  chips  using  "PCCHIP"  followed  by  a unique
        number.  

             PCCHIP1 - Used on 286/386SX AT motherboards M205 and M209
             PCCHIP2 - Used on 386 AT motherboard M321

        PCCHIP1  provides  256k  of  memory  in twenty 16k blocks between
        C0000-FFFFF.   

        PCCHIP4  provides  192k  of  memory  in twelve 16k blocks between
        C0000-EFFFF.   If  you  have  a  VGA  or EGA adapter, you may get
        additional  memory  with  these  chips  by using the MOVE=OVERLAY
        option of LASTBYTE.SYS.   

        PCCHIP4  is functionally identical to the OPTi Electronics 82C391
        and  the  Atmel AT40391; their corresponding PHYSICAL options are
        equivalent.  


        1.2.3 Appian Technology        

        The  following chip provides 256k of memory in sixteen 16k blocks
        between C0000-FFFFF.  

             P915 - 486/386DX System Controller


        1.2.4 Atmel Corporation        

        The  following  chips  all  provide  192k of memory in twelve 16k
        blocks  between  C0000-EFFFF.   If you have a VGA or EGA adapter,
        you  may  get  additional memory by using the MOVE=OVERLAY option
        of LASTBYTE.SYS.  









        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                 3


             AT40281 - 386SX Core Logic Controller w/Cache
             AT40283 - 386SX Core Logic Controller w/o Cache
             AT40391 - From the 80386DX PC/AT Chip Set
             AT40493 - From the 80486DX PC/AT Chip Set

        All  of  the above chips are functionally identical to chips with
        similar  part  numbers  made  by OPTi Electronics: the AT40281 to
        the  OPTi  82C281, the AT40283 to the OPTi 82C283, the AT40391 to
        the  OPTi  82C391  and  to  AddTech  Research's  PCCHIP4, and the
        AT40493  to the OPTi 82C493; these corresponding PHYSICAL options
        are equivalent.  


        1.2.5 Chips and Technologies       

        The  following  chips  all  provide 384k of memory in twenty-four
        16k blocks between A0000-FFFFF.  

             82C212 - From the CS8221 NEAT (tm) chipset
             82C222 - From the CHIPS/250 PS/2 50/60 chipset
             82C230 - The PS/2 30 Single Chip Controller
             82C235 - The SCAT (tm) Single Chip AT VLSI chip
             82C241 - From the CS8223 LeAPset (tm) chipset
             82C302 - From the CS8230 386/AT CHIPSet (tm)
             82C307 - From the CS8231 386/AT CHIPSet (tm)
             82C311 - From the CS8233 PEAK 386/AT CHIPSet (tm)
             82C351 - From the CS82310 PEAK DM/386 AT CHIPSet (tm)
             82C812 - From the CS8281 NEATsx (tm) chipset
             82C836 - The SCATsx (tm) Single Chip AT VLSI chip
             82C841 - From the CS8283 LeAPset-sx (tm) chipset

        The    82C212   is   functionally   identical   to   the   United
        Microelectronics  UMC82C212; their corresponding PHYSICAL options
        are equivalent.  

        The  following chip provides 384k of memory in sixteen 16k blocks
        between A0000-DFFFF and one 128k block between E0000-FFFFF.  

             82C322 - From the CHIPS/280 PS/2 70/80 chipset

        The  following  chip  provides  a maximum of 384k of memory using
        two  64k  blocks  between  A0000-BFFFF,  four  16k blocks between
        C0000-CFFFF,  and three 64k blocks between D0000-FFFFF.  However,
        any  of  the  first two and last two 64k blocks might be "locked"
        and  unavailable due to the design of your particular bios.  This
        may reduce the amount of memory from 384k to as little as 128k.  

             4021 - From the ISA/486 chipset.






        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                 4


        1.2.6 EFAR Microelectronics        

        The  following  chips  all  provide  192k of memory in twelve 16k
        blocks  between  C0000-EFFFF.   If you have a VGA or EGA adapter,
        you  may  get  additional memory by using the MOVE=OVERLAY option
        of LASTBYTE.SYS.  

             82EC495 - From the EF8290WB 486/386 PC/AT ChipSet
             82EC798 - From the EC798 386/486 PC/AT Single Chip


        1.2.7 ETEQ Microelectronics        

        The  following  chips  all  provide  192k  of memory in three 64k
        blocks  between  C0000-EFFFF.   If you have a VGA or EGA adapter,
        you  may  get  additional memory by using the MOVE=OVERLAY option
        of LASTBYTE.SYS.  

             ET6000 - From the Cheetah 486DX/SX Non-Cache System
             ET9000 - From the Jaguar 486DX/SX Cache System
             ET9800/ET391SX - From the Firefox 386SX Write Back chipset

                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                ³ If you have a ET9800/ET391SX chipset and an     ³ 
                ³ adapter that occupies non-shadow ram address    ³
                ³ space between C800-CFFF, you will need to re-   ³ 
                ³ configure that adapter to use another location. ³
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

        The  following  chips  all  provide  192k of memory in twelve 16k
        blocks  between  C0000-EFFFF.   If you have a VGA or EGA adapter,
        you  may  get  additional memory by using the MOVE=OVERLAY option
        of LASTBYTE.SYS.  

             ET82C391  - From the Bobcat 386DX/486DX chipset
             ET82C491  - From the Cougar 386DX/486DX chipset
             ET82C4901 - From the Bengal 386DX/486DX chipset

        The   CHIPSET   program   cannot  distinguish  the  ET82C391  and
        ET82C491; their corresponding PHYSICAL options are equivalent.  


        1.2.8 Forex Computer Corporation       

        The  following  chip  provides  256k  of memory in six 32k blocks
        between C0000-EFFFF and one 64k block between F0000-FFFFF.  

             FRX36C300 - From the FRX36C300/200 Cache chipset
             FRX46C411 - From the FRX46C411/412 Cache chipset
             FRX46C421 - From the FRX46C421/422 Cache chipset




        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                 5



        1.2.9 Headland Technology (G2)       

        The  following  chip provides 64k of memory by using the four 16k
        blocks of the EMS page frame.  

             HT12 - Single 286 AT Chip

        The  following  chips all provide 128k of memory by using the EMS
        mapping area between C0000-DFFFF.  

             HT18  - 286/386SX Advanced Memory Manager Chip
             HT21  - 286/386SX Advanced Memory Manager Chip
             HT22  - 286/386SX Advanced Memory Manager Chip
             HT103 - 286/386SX Advanced Memory Manager Chip
             HT113 - 286/386SX Advanced Memory Manager Chip

        The  CHIPSET  program cannot distinguish the HT18 and HT22; their
        corresponding PHYSICAL options are equivalent.  


        1.2.10 Intel Corporation        

        The  following  chips provide 192k of memory in twelve 16k blocks
        between  C0000-EFFFF.   If you have a VGA or EGA adapter, you may
        get  additional  memory  by  using  the  MOVE=OVERLAY  option  of
        LASTBYTE.SYS.  

             82343 - From the 82340SX Chip Set
             82346 - From the 82340DX Chip Set

        The  82343  is  functionally  identical  to  the  VLSI Technology
        VL82C320,  and  the  82346 to the VLSI Technology VL82C330; these
        corresponding PHYSICAL options are equivalent.  

        The  following  chip  provides  384k of memory in twenty-four 16k
        blocks between A0000-FFFFF.  

             82359 - From the 82350DT EISA Chip Set


        1.2.11 Mosel Corporation        

        The  following  chip  provides  256k of memory in four 16k blocks
        between C0000-CFFFF and three 64k blocks between D0000-FFFFF.  

             MS400 - From the 486SX/DX Single Chip AT







        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                 6


        1.2.12 Oak Technology        

        The  following  chips  all  provide 256k of memory, consisting of
        four  32k  blocks between C0000-DFFFF, and two 64k blocks between
        E0000-FFFFF.  

             OTI-021 - From the OTI-020 Desktop PC Chip Set
             OTI-041 - From the OTI-040 OakNote Chip Set

        The  CHIPSET  program cannot distinguish the OTI-021 and OTI-041;
        their corresponding PHYSICAL options are equivalent.  


        1.2.13 OPTi Electronics        

        The  following  chips  all  provide  192k of memory in twelve 16k
        blocks  between  C0000-EFFFF.   If you have a VGA or EGA adapter,
        you  may  get  additional memory by using the MOVE=OVERLAY option
        of LASTBYTE.SYS.  

             82C281 - From the Cache SX/AT chipset (w/Cache)
             82C282 - From the Cache SX/AT chipset (w/o Cache)
             82C283 - From the Block Interleave SX/AT chipset
             82C382 - From the HiD/386 AT chipset
             82C391 - From the 386WB PC/AT chipset
             82C461 - From the Notebook PC/AT chipset
             82C482 - From the HiB/486 AT chipset
             82C491 - From the 486SXWB PC/AT chipset
             82C493 - From the 486SXWB PC/AT chipset
             82C495 - From the 486SXWB PC/AT chipset
             82C495SX - From the LCWB PC/AT chipset
             82C496A - From the DXBB PC/AT chipset (Rev. A)
             82C498 - From the DXWB PC/AT chipset
             82C499 - From the DXSC PC/AT Single Chip

        The  CHIPSET  program  cannot  distinguish the 82C281 and 82C282,
        and  the  82C281  is functionally identical to the Atmel AT40281;
        these corresponding PHYSICAL options are equivalent.  

        The  82C283 is functionally identical to the Atmel AT40283; their
        corresponding PHYSICAL options are equivalent.  

        The  82C391  is  functionally  identical to the Atmel AT40391 and
        AddTech  Research's PCCHIP4; their corresponding PHYSICAL options
        are equivalent.  

        The  CHIPSET  program  cannot distinguish the 82C491, 82C493, and
        82C495,  and  the  82C493  is functionally identical to the Atmel
        AT40493; these corresponding PHYSICAL options are equivalent.  

        The  following  chips provide 256k of memory in twelve 16k blocks



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                 7


        between C0000-EFFFF and one 64k block between F0000-FFFFF.  

             82C291 - From the SXWB PC/AT chipset
             82C496B - From the DXBB PC/AT chipset (Rev. B)

        The  following  chip  provides 256k of memory in eight 16k blocks
        between C0000-DFFFF and two 64k blocks between E0000-FFFFF.  

             82C682 - From the 386/486WB EISA chipset
             82C683 - From the 386/486AWB EISA chipset


        1.2.14 PicoPower Technology        

        The  following  chips  all  provide  256k of memory in twelve 16k
        blocks   between   C0000-EFFFF   and   one   64k   block  between
        F0000-FFFFF.  

             PT86C168 - Evergreen Portable Computer Core Logic Chip
             PT86C268 - Evergreen HV Core Logic Chip (Hybrid 3.3/5.0 volts)


        1.2.15 Silicon Integrated Systems (SiS)      

        The  following chips all provide 192k of memory in six 32k blocks
        between  C0000-EFFFF.   If you have a VGA or EGA adapter, you may
        get  additional  memory  by  using  the  MOVE=OVERLAY  option  of
        LASTBYTE.SYS.  

             85C360 - ISA 386DX Single Chip
             85C401 - ISA 486DX/SX Chipset
             85C411 - EISA 386/486 Chipset
             85C460 - ISA 486DX/SX Single Chip


        1.2.16 Sun Electronics (SUNTAC)       

        All  SunTac  chips  provide  128k  of  memory  in four 32k blocks
        between  E0000-FFFFF.   An  additional  128k  in eight 16k blocks
        between  C0000-DFFFF  is available at the expense of all Expanded
        Memory  by adding the word NOEMS to the SUNTAC Physical option as
        in: Physical=ST62C202,NOEMS.  

             ST62C202 - From the chipset 20 for 286
             ST62C241 - From the chipset 24 for 386
             ST62C251 - From the chipset 25 for 286 and 386sx








        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                 8


        1.2.17 Symphony Laboratories        

        The  following  chips  provide 256k of memory in eight 16k blocks
        between   C0000-DFFFF   and   another   two  64k  blocks  between
        E0000-FFFFF.  

             SL82C361 - From the Haydn SL82C360 80386DX/SX chipset
             SL82C461 - From the Haydn SL82C460 80486 chipset
             SL82C471 - From the Mozart SL82C470 486/386 EISA chipset


        1.2.18 Texas Instruments        

        The  following  chips  provide  384k of memory in twenty-four 16k
        blocks between A0000-FFFFF.  

             TACT82411  - The Snake Single-Chip AT Controller
             TACT82S411 - The Snake+ Single-Chip AT Controller


        1.2.19 UNIchip Incorporated        

        The  following  chip  provides 192k of memory in three 64k blocks
        between  C0000-EFFFF.   If you have a VGA or EGA adapter, you may
        get  additional  memory  by  using  the  MOVE=OVERLAY  option  of
        LASTBYTE.SYS.  

             U4800 - From the 386/486 AT Chip Set


        1.2.20 United Microelectronics Corporation (UMC)      

        The  following  chip  provides  384k of memory in twenty-four 16k
        blocks between A0000-FFFFF.  

             UM82C212 - From the UM82C210 386SX/286 AT Chip Set

        The   UMC82C212  is  funcitonally  identical  to  the  Chips  and
        Technologies  82C212;  their  corresponding  PHYSICAL options are
        equivalent.  

        The  following  chip  provides 256k of memory in eight 16k blocks
        between C0000-DFFFF and two 64k blocks between E0000-FFFFF.  

             UM82C481 - From the UM82C480 50Mhz 80486 Chip Set









        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                 9


        1.2.21 VIA Technologies        

        The  following  chips  provide 256k of memory consisting of eight
        16k  blocks  between  C0000-DFFFF  and  two  64k  blocks  between
        E0000-FFFFF.  

             VT82C470 - From the Jupiter Chip Set (w/o cache)
             VT82C475 - From the Jupiter Chip Set (w/cache)
             VT82C495 - From the Venus Chip Set


        1.2.22 VLSI Technology        

        The  following  chip  provides  384k  of memory in six 64k blocks
        between A0000-FFFFF.   

             VL82C202 - PC/AT-Compatible High Speed Memory Controller

                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                ³ Pin 69 on th VL82C202 controls whether its      ³ 
                ³ shadow ram is enabled or relocated.  This pin   ³
                ³ is usually tied to a jumper on the motherboard  ³ 
                ³ which must be set properly to work.             ³
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

        The  following  chips  provide  384k of memory in four 32k blocks
        between  A0000-BFFFF,  eight  16k blocks between C0000-DFFFF, and
        four 32k blocks between E0000-FFFFF.  

             VL82C310 - From the SCAMP 286/386sx Chip Set
             VL82C311 - From the SCAMP 286/386sx Chip Set
             VL82C315 - The SCAMP II PC/AT-Compatible System Controller
             VL82C316 - The SCAMP II Chip Set for Power-Managed Portables

        The   CHIPSET   program   cannot  distinguish  the  VL82C315  and
        VL82C316; their corresponding PHYSICAL options are equivalent.  

        The  following  chips provide 192k of memory in twelve 16k blocks
        between  C0000-EFFFF.   If you have a VGA or EGA adapter, you may
        get  additional  memory  by  using  the  MOVE=OVERLAY  option  of
        LASTBYTE.SYS.  

             VL82C320 - From the TOPCAT 286/386sx Chip Set
             VL82C330 - From the TOPCAT 386 DX Chip Set

        The  VL82C320  is  functionally identical to the Intel 82343, and
        the  VL82C330  to  the Intel 82346 ; their corresponding PHYSICAL
        options are equivalent.  

        The  following  chip  provides  384k of memory in twenty-four 16k
        blocks between A0000-FFFFF.  



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                10



             VL82C486 - Single Chip, High Performance 486 PC/AT Controller


        1.3 Unsupported Chipsets        

        If  your computer has shadow ram capability, then it probably has
        a  shadow ram memory controller.  However, some of these chipsets
        cannot  be  supported by The Last Byte Memory Manager for reasons
        shown below.  

        Some  of  these  chips, however, do have hardware EMS support and
        thus  many  of  their motherboards come with an EMS device driver
        designed  specifically  to take advantage of this capability.  So
        in  many  cases,  you can install this driver first, and then The
        Last  Byte  Memory  Manager can use it to manage the upper memory
        area.  


        1.3.1 No Shadow Ram Support      

        Some   of   the   older   chipsets  do  not  provide  shadow  ram
        capability.  

        Examples: VLSI Technologies 82C100 series
                  Western Digital chipsets
                  Texas Instruments TACT82300 series
                  Early Suntac chipsets (ST62BC001-6)
                  United Microelectronics Corp. UM82C231


        1.3.2 Shadow Ram is not Read/Write     

        Some  chipsets  have  shadow ram, but can only put it into either
        write-only  mode  (for copying rom contents to ram), or read-only
        mode  (to  prevent accidental writes into what's supposed to be a
        copy  of  rom).  The hardware EMS in some such chipsets sometimes
        provides  a limited amount (e.g., 64k) of Hi-DOS memory, but only
        if the user doesn't need expanded memory.  

        Examples: CONTAQ 82C591 (no hardware EMS support)
                  Headland/G2 (many do have hardware EMS however)
                  ACC Microelectronics (many do have hardware EMS)
                  USA Integration (USAi) (no hardware EMS)


        1.3.3 Overly Complex Control       

        The  Last Byte Memory Manager software is table-driven, making it
        relatively   easy   to   adapt  to  different  memory  controller
        architectures, but there are limits!   



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                11



        Examples: Zymos/Appian System 90 chipset
                  United Microelectronics Corp UM82C384, '388, '389
                  Forex Computer Corp. FRX36C100
                  Silicon Integrated System (SiS) 85C310.


        1.3.4 Locked Configuration Registers       

        Some  memory  controllers  are  designed  so  that  they  can  be
        "locked"  at the end of the main bios initialization, requiring a
        hardware  reset  to  unlock,  and  thus  preventing The Last Byte
        Memory Manager from accessing the controller.  

        Examples: Intel 82335, 82335SX


        1.3.5 Configuration I/O Ports Reassigned      

        Some  memory  controllers  are  designed so that the "index/data"
        pair  of I/O ports used to access the configuration registers can
        be  reassigned  to  different  I/O  addresses.   This  makes  the
        configuration  registers  effectively  inaccessible  to  The Last
        Byte  Memory  Manager since it has no way of knowing what new I/O
        port addresses may have been established within the main bios.  

        Examples: Texas Instruments TACT84500
                  GS Technology GS62CS03


        1.4 Checking Compatibility Using CHIPSET      

        CHIPSET  is a program that attempts to determine if your computer
        has  one  of the memory controllers required to use The Last Byte
        Memory  Manager.   To  run  CHIPSET, simply enter its name on the
        command line: 

                A>CHIPSET 

        and  follow  the  prompts.   CHIPSET  will  try  to  identify the
        particular  memory controller you have, if any.  If it can't find
        a  memory  controller, it will look for fixed memory in the upper
        area  or  expanded  memory as a means of installing The Last Byte
        Memory  Manager.   If  it  is  successful,  it  will give you the
        option  of  automatically linking to the INSTALL program to setup
        for use of The Last Byte Memory Manager.  

        CHIPSET   automatically  senses  whether  you  have  a  color  or
        monochrome  display  to  determine  how  to  present  data on the
        screen.   However,  you  may  force  the mode by using one of the
        command  line  options:  /MONO  or  /COLOR (for monochrome liquid



        Copyright (C) 1990-92, Key Software Products. All Rights Reserved



        Jan 31, 1993      SHADOW RAM MEMORY CONTROLLERS                12


        crystal displays).  

        If  your  computer  has  one of the listed devices, then The Last
        Byte Memory Manager should work on your computer.  


















































        Copyright (C) 1990-92, Key Software Products. All Rights Reserved