-------------------------------------------------------------------------
     The following are things that are specific to CLOVER
-------------------------------------------------------------------------

In terminal mode there are a small number of commands you can use
to control the operation of the PCI-4000.  Most of these commands
are also available in FWD.MB scripts, and as "Init" and "Discon"
commands in PORTS.MB.


CH n	    -  Use voice subchannel n (1 to 5).

CN <call>   -  Initiate a normal link to <call>.
CR <call>   -  Initiate a robust link to <call>.

CW <on/off> -  Turn CWID on or off.

R <number>  -  Set retry count.  Normal, robust, and CCB retry counts
	       are set to the number given.

BF	    -  Set fast bias.
BN	    -  Set normal bias.
BR	    -  Set robust bias.


The following are available only in terminal mode.


T	    -  Send test tones.

I <a> <b>   -  Initialize the board using the PCC.LOD file given as <a>
	       and the PCC.S28 file given as <b>.  MYCALL is set, and
	       other parameters required for correct MailBox operation
	       are also set.

I	    -  With no file names given, defaults to using the files
	       \PCC\PCC.LOD and \PCC\PCC.S28


The following are available only in scripts (FWD.MB and PORTS.MB).


X p command -  Send command out serial port p.	For Transceiver control.

Note that the COM port baud rate, etc. must have been previously set
(using for example the DOS MODE command), and that CTS/RTS handshaking
is used.  If CTS/RTS is not required, those pins must be jumpered at
the PC end of the cable.