INTRODUCTION   
         

              This disk contains a limited version of GASFLO, along with 
         instructions and sample problems. This version is limited 
         only in the number of pipe sizes (4 inch, 12 inch, 20 inch)
         available for use; all other features of GASFLO are included.
              GASFLO is a program to assist the Engineer in the sizing 
         and operational analysis of buried natural gas pipelines. In
         addition to calculating flow, pressure drop, pipe size, and
         efficiency GASFLO estimates the temperature profile of the
         pipeline. The temperature is used interactively when calculating 
         flow, pressure, pipe size, and efficiency.
              GASFLO is menu driven, has screen display of input and 
         results, and will print a full report.  
              Please drop me a line if you have problems running 
         GASFLO or have comments on the program.
              If you find GASFLO useful, the full featured version (pipe 
         size 4 inch through 48 inch) is available for $100, and 
         includes a complete user guide and free telephone support.
                               
         

                                    ORDER FORM

         NAME___________________________________DATE____________________

         COMPANY________________________________PHONE___________________
          
         STREET_________________________________________________________
         
         CITY_____________________________STATE_____________ZIP_________
         
         Specify 5.25" or 3.5" disks 
         
         QUANTITY________________@$100.00=______________________________
         
         Texas Residents Add    Sales Tax ______________________________
         
                                                  TOTAL_________________

         Make checks and money orders payable to and mail to:
         
                                  G. E. STEWART
                                25303 Pepper Ridge
                                 Spring, TX 77373
                                  (713) 288-4982


           


                                   INSTRUCTIONS 

              GASFLO is a basic language program written with GW-BASIC, 
         ver 3.20, (c) Copyright Microsoft 1983,1984,1985,1986.
              GASFLO uses a rational, isothermal flow equation and 
         calculates the friction factor with the Colebrook-White algorithm.
              The program is divided into a pipeline DESIGN section and 
         a pipeline ANALYSIS section. The DESIGN section solves for (1) 
         flow rate, or (2) outlet pressure, or (3) required pipe size.
         The ANALYSIS section solves for (1) pipeline efficiency and (2) 
         soil thermal conductivity from data taken from an operating 
         pipeline.
              To run the design section, choose the DESIGN option from 
         the MAIN MENU. Input data as prompted, pressing ENTER to pass 
         over requests for data to be calculated. ELEVATION CHANGE is 
         entered as + or -. Outlet above inlet is a (+) change. Default
         values for SOIL CONDUCTIVITY, PIPELINE EFFICIENCY, TEMPERATURE
         BASE, and PRESSURE BASE are shown and can be accepted or revised. 
         At the end of input you will be given an opportunity to edit 
         the data.  
              To edit, press ENTER to accept value shown or input
         revised data. There is one exception; when editing ELEVATION 
         CHANGE a value must be entered each time. The indicated value
         cannot be accepted by pressing ENTER. 
              At the completion of input a calculation menu appears. 
         Choose calculation desired. At completion of calculation the 
         input and calculated data are displayed, along with a menu of 
         options. The velocity indicated is at the outlet of the 
         pipeline.
              To run the analysis section choose the ANALYSIS option 
         from the MAIN MENU. Input data as described above in the DESIGN 
         section and all prompts (except ELEVATION CHANGE) require input.
         The PIPELINE EFFICIENCY is calculated using the pressure, flow
         rate, gas temperatures from an operating pipeline and the SOIL
         CONDUCTIVITY is calculated using the same flow, pressure, gas
         temperature data along with ground temperature.
                                                   
         

                              EXAMPLE NO.1-DESIGN

              Calculate the flow expected through a 4.062 inch inside 
         diameter pipeline two miles long. Inlet pressure is 80 psi, 
         outlet pressure 45 psi. Inlet temperature is 100 deg F, with 
         out any elevation difference between inlet and outlet.The 
         pressure base is 14.7 psia, temperature base is 520 deg R,
         pipeline efficiency is .94, soil thermal conductivity is 
         .8, pipe cover is 36 inches, and ground temperature is 58 deg 
         F. Gas specific gravity is .75, specific heat is .6, viscosity 
         is .013 centipoise and the Joules-Thompson coefficient is 69
         deg F per 1000 psi.
              GASFLO calculates a flow rate of 1.7 MMSCFD, maximum 
         velocity of 52.2 feet per second, outlet gas temperature of 
         57.7 deg F and an average compressibility of .9774.
              For a copy of this problem and solution select PRINTOUT
         in the display menu.
        

         

                              EXAMPLE NO.2-DESIGN

              Calculate the outlet pressure of a 19.25 inch inside 
         diameter pipeline 75 miles long.Inlet pressure is 1400 psi 
         and the flow is 235 MMSCFD. Inlet temperature is 120 deg F, 
         with the line outlet 5000 feet above the inlet. The pressure 
         base is 14.7, temperature base is 520 deg R, pipeline
         efficiency is .94,soil conductivity is .8,pipe cover is 36
         inches, and ground temperature is 58 deg F. Gas specific
         gravity is .6, viscosity is .013 centipoise and the Joules-
         Thompson coefficient is 65 deg F per 1000 psi.
              GASFLO calculates an outlet pressure of 963.2 psi,maximum 
         velocity of 16.6 feet per second, outlet gas temperature of    
         49 deg F and an average compressibility of .844.
              For a copy of this problem and solution select PRINTOUT 
         in the display menu.
         
         
                              EXAMPLE NO.3-DESIGN
         
              Calculate the minimum pipe inside diameter required for
         a 75 mile long pipeline flowing 260 MMSCFD. Inlet pressure is
         1400 psi, outlet pressure is 800 psi. All other data is same 
         as EXAMPLE NO.2.
              GASFLO calculates a minimum diameter of 18.14 inches. 
         Select an actual pipe inside diameter larger than the 
         calculated minimum.
              Calculate flow using the pipe diameter selected and the 
         specified inlet and outlet pressures.
              GASFLO calculates a flow of 306.5 MMSCFD, maximum velocity 
         of 26.7 feet per second, outlet gas temperature of 48.8 deg F 
         and an average compressibility of .8514.
              For a copy of this problem and solution select PRINTOUT 
         in the display menu.
         
         
                             EXAMPLE N0.4-ANALYSIS
         
              Calculate pipeline efficiency and soil conductivity for 
         a 12 inch inside diameter 25 mile long pipeline flowing 
         166.6 MMSCFD. Inlet pressure is 1400 psi,outlet pressure is 
         550 psi. Inlet temperature is 120 deg F, outlet temperature 
         is 49.9 deg F, with the line outlet 500 feet lower than the 
         inlet. The pressure base is 14.7, temperature base 520 deg 
         R, pipe cover is 36 inches, and ground temperature is 58 deg 
         F. Gas specific gravity is .65, specific heat is .6, 
         viscosity is .013 centipoise and the Joules-Thompson 
         coefficient is 60 deg F per 1000 psi.
              GASFLO calculates a pipeline efficiency of .93 and a 
         soil conductivity of .6, maximum velocity of 55.2 feet per 
         second, and an average compressibility of .8358. 
              For a copy of this problem and solution select PRINTOUT
         in the display menu.