An abridged spice3 manual, it might even be useful.  This manual
covers basic spice syntax and commands for using Spice TR3e2 in both
interactive and batch modes.  It may not be complete, but a more
complete version is being worked on.

SPICE (simulation program with integrated circuit emphasis) was
developed in the Electronics Research Laboratory at the University of
California at Berkeley.  Spice3 is based on spice2.  When used in batch
mode, most of the syntax and commands are the same, but there are
changes.  For example, the output can be similar, using the -o option,
or the may be written in a "RAW" file format (the raw file format must
be used if it is to be plotted with Spice TR3e2's graphics capability).
Polynomial non-linear sources are replaced by a General non-linear
source (NOTE: most opamp libraries are made for spice2g6 and use
polynomial non-linear sources-> exception:  most of Linear Technology
Corporation's models will work with either spice2 or spice3).
Polynomial nonlinear capacitors are not supported in Spice3.

*************** input format ****************************

A circuit to be analyzed by Spice is described by a netlist which
defines the circuit topology, element (or part) values, and may
include the type of analysis to be run.

Spice uses ASCII input files.  The input format for Spice is of the
free format type.  Fields on a line are separated by one or more
blanks, a comma, an equal (=) sign, or a left or right parenthesis;
extra spaces are ignored.  A line may be continued by entering a "+" in
column one of the following line.  Comments can be included in the
listing-just place a "*" in column one of the line (a space will also
work for Spice3).

The first line in a Spice input file is assumed to be the circuit
title.  The last line must be the ".END" line.  Between are the parts,
type of analysis, and any subcircuits or models.  The order of these
statements is arbitrary (except [of course], that continuation lines
must immediately  follow  the  line  being continued, and element lines
belonging to a subcircuit must be between the  ".SUBCKT" and ".ENDS"
lines for that subcircuit).  Other files may be added by using the
".include file_name" command.

Spice is not case-sensitive most of the time (the ".include" command
must be lower case).

In Spice2, nodes must be labeled as number, in Spice3 they may be may
be arbitrary character strings, except for the ground node which must
be named "0".  All nodes must have a dc path to ground. The circuit
cannot contain a loop of voltage sources and/or inductors and cannot
contain a series connection of current sources and/or capacitors.
Every node must have at least two connections, except for transmission
line nodes (to permit unterminated transmission lines) and MOSFET
substrate nodes (which have two internal connections anyway).

Numbers may be interred directly, followed by a integer exponent, or a
scale factor.  6000, 6e3, and 6k all have the same value. The scale
used are:  T=e12  G=e9   Meg=e6   K=e3    mil=25.4e-6
           m=e-3  u=e-6  n=e-9    p=e-12  f=e-15
Letters immediately following a number that are not scale factors are
ignored, and letters immediately following a scale factor are ignored.
Hence, 10, 10V, 10VOLTS, and 10hz all represent the same number, and M,
MA, MSEC, and MMHOS all represent the same scale factor.

Each element in the circuit is specified by an element line that
contains the element name, the circuit nodes to which the element is
connected, and the values of the parameters that determine the
electrical characteristics of the element.  The first letter of the
element name specifies the element type.  The  format  for the SPICE
element types is given in what follows.  The strings  XXXXX, YYYYY, and
ZZZZZ denote arbitrary alphanumeric strings.  For example, a resistor
name must begin with the letter `R' and can  contain one or more
characters.  Hence, R, R1, RSE, ROUT, and R3AC2ZY are valid resistor
names.





******* Command line Usage ************

spice [ -n ] [ -b ] [ -o outfile ] [ -r rawfile ] [ input_file ]

     -n (or -N)
          Don't try to source the file "spice.rc" upon startup.
          Normally Spice tries to find this file in the current
          directory.

     -b (or -B)
          Run in batch mode. Spice will read the specified input
          file and do the simulation.

     -r rawfile (or -R rawfile)
          Use rawfile as the default file into which the results of
          the simulation are saved.  If the -r option is used, the
          .print and .plot commands will be ignored.

     -o outfile (or -O outfile)
          Print analysis time and memory usage to a file, and if the
          -r option is not used, use the .print and .plot commands to
          make a Spice2 type output file.

Further arguments are taken to be Spice input files, which are read and
saved. (If batch mode is requested then they are run immediately.)

Spice files specified on the command line are read in before the
"spice.rc" file is read.  Thus if you define aliases there, any that
are used in a Spice source file mentioned on the command line won't be
recognized.




**************** Parts ******************************
Data fields that are enclosed in less than and greater than signs ("<"
or ">") are optional.

resistor
     Format: Rname Node1 Node2 value
     Examples: R1 32 45 1k
               rload 8 0 200

         The name must start with the letter R.  The value may be
         positive or negative, but not zero.

capacitor
    Format: Cname Node1 Node2 value
    Examples: C1 32 45 1uf
              cload 8 0 200pf

         The name must start with the letter C.

inductor
    Format: Lname +Node -Node value
    Examples: L1 32 45 1uh
              lload 8 0 200uh

         The name must start with the letter L.

mutual inductor
    Format: Kname Lname1 Lname2 value
    Example: k1 L5 L9 .987

         The name must start with the letter K.  Two inductors are
         referenced.  The standard dot convention determines polarity-
         with the positive node on the inductors having the dot.  Value
         is the coefficient of coupling, which must be between 0 and 1.

Lossless Transmission Lines

     Format: Tname N1 N2 N3 N4 Z0=value TD=value
             Tname N1 N2 N3 N4 Z0=value F=freq NL=nrmlen

    Example: t1 1 0 2 0 z0=75 td=15ns

         The name must start with the letter T. N1 and N2 are the nodes
         at port one; N3 and N4 are the nodes at port two.  Z0 is the 
         characteristic impedance.  The length of the line must be 
         expressed in either one of two forms : the delay may be specified
         directly (TD=value) or a frequency (F=freq) must be given.  If 
         the frequency is given, the normalized electrical length 
         (NL=value) may be given (the default is NL=.25).            

         NOTE1: This models only one propagating mode.  If all four nodes 
                are distinct in the actual circuit, then two modes may be 
                excited.  To simulate this, two transmission line elements
                are required. 

         NOTE2: The lossy transmission line with zero loss may be more 
                accurate due to implementation details.

sources
  independent source
    Format: _name +node -node [dc value] [ac value] [tran_value]
    Examples: Vcc 10 0   15
              Icc 2 5   1ma
              vin 1 0 dc 0 ac 1 pulse(-0.5 0.5 20us 20us 20us 200us 400us)

      If the name starts with a V it is a voltage source and if it
      starts with an I it is a current source.  The transient value
      may have the following values:
       PULSE(v1 v2 pulse_delay [rise_time fall_time pulse_width period])
       SIN(offset_voltage amplitude frequency [start_delay damping_coef])
       PWL(time_point1 volt_or_amp1 [t2 v_or_a2 ...])

  linear dependent sources
    Format: _name +nodeOut -nodeOUT +nodeIN -nodeIN value
    Examples: G1 10 0 5 0  15mmho
              E1  2 0 5 0  1e8

        If the name starts with a G, it is a voltage controlled
        current source.  If the name starts with a E, it is a voltage
        controlled voltage source.

    Format: _name +nodeOut -nodeOUT vname value
    Examples: F1 1 2 vz 26
              H3 5 7 vy 345

         Vname is the name of a voltage source through which the
         controlling current flows.  If the name starts with a F, it is
         a current controlled current source.  If the name starts with
         a H, it is a current controlled voltage source.

  non-linear dependent sources (these sources are not spice2 compatible)
    Format: Bname +nodeOut -nodeOUT <I=expr> <V=expr>
    Examples: b1 1 0 i=cos(v(1))+sin(v(2))
              b2 5 3 v=log(v1))^2

         The name must start with the letter B.  The values of the V
	 and I parameters determine the voltages and currents across
	 and through the device, respectively.  Only one of these
         parameters must be given.  The expressions given for V and I
         may be any function of voltages and currents through voltage
         sources in the system.  The following functions of real
         variables are defined:  abs     asinh     cosh    sin
                                 acos    atan      exp     sinh
                                 acosh   atanh     ln      sqrt
                                 asin    cos       log     tan

         The following operations are defined:
              +   -   *   /   ^   unary

         If the argument of log, ln or sqrt becomes less than zero, the
         absolute value of the argument is used.  If a divisor becomes
         zero, an error will result.  Other problems may arise where
         the partial derivative of a function is undefined.

Parts that need MODELS:

 Some devices (or parts) that spice simulates require many parameter
 values.  Since these devices may be used more than once in a circuit
 (with the same set of parameters), they have a set of "model"
 parameters that is defined on a separate model line with the format:
   .MODEL model_name type(parameters)
 Examples:
   .model mod1 npn (BF=50 IS=1e-13 VBF=50)
   .model dm1 d (is=2e-17)
 Among the model types used in Spice TR3e2bl are npn, pnp, d, njf, pjf,
 ltra and sw.

 NOTE: Although the model line is required for these parts, spice will
       use the default values for the unspecified parameter values.
       Please see some "real" spice documentation for the semiconductor 
       default values.

diodes (D)
    Format: Dname NodeA NodeC modname
    Example: d1 32 45 d1n4841

         The name must start with the letter D.  NodeA is the anode and
         NodeC is the cathode.

bipolar junction transistors (NPN, PNP)
    Format: Qname collector base emitter modname
    Examples: Q1 32 45  40 Q2N2222A
              q27 1 2 3 q2n2222a

         The name must start with the letter Q.

junction FETs (NJF, PJF)
    Format: Jname drain gate source modname
    Example: J1 32 45  40 JN2

         The name must start with the letter J.

Lossy Transmission Lines (LTRA)
    
    Format: Oname N1 N2 N3 N4 modname
    Example: o1 1 0 2 0  tran1

         The name must start with the letter O. N1 and N2 are the nodes 
         at port one; N3 and N4 are the nodes at port two.  Note: a 
         lossy transmission line with zero loss may be more accurate 
         than a lossless transmission line due to implementation details.

         MODEL    parameters
         R             resistance/length (default 0.0)
         L             inductance/length (default 0.0)
         G             conductance/length (default 0.0)
         C             capacitance/length (default 0.0)
         LEN           length of line required -> no default
         REL           breakpoint control (default 1)
         ABS           breakpoint control (default 1)
         NOSTEPLIMIT   do not limit timestep to less than time delay (flag)
         NOCONTROL     don't do complex timestep control (flag)
         LININTERP     use linear interpolation (flag)
         MIXEDINTERP   use linear when quadratic seems bad (flag)
         COMPACTREL    special reltol for history compaction
         COMPACTABS    special abstol for history compaction
         TRUNCNR       use Newton-Raphson method for timestep control (flag)
         TRUNCDONTCUT  don't limit timestep to keep impulse-response errors 
                       low (flag)

    Only the following types of lines have been implemented so far:
        RLC -  uniform transmission line with series loss only
        RC  -  uniform RC line
        LC  -  lossless transmission line
        RG  -  distributed series resistance and parallel conductance
    Any other combination will yield erroneous results and should not be tried.

Switches (SW)
    Format: Sname N+ N- NC+ NC- modname <on><off>
    Example: s1 2 5 3 0 sw1

         The name must start with the letter S (for a voltage
	 controlled switch).  Switches must always have a finite
	 positive value.  It is wise to set switch impedances only high
	 and low enough to be negligible with respect to other circuit
	 elements.  Switches will not change state in AC analyses.

     MODEL    parameters
       VT     threshold voltage (default 0.0v)
       VH     hysteresis (default 0.0v)
       RON    on resistance (default 1 ohm)
       ROFF   off resistance (default 1/GMIN ohm)




******************** Subcircuits **********************

A subcircuit consists of spice elements and can be referenced in a
fashion similar to device models.  Spice will automatically insert the
group of elements wherever the subcircuit is referenced.

  Format for subcircuit reference: xname node1 node2 <node...> subname

         The name must start with the letter X.

  Format for subcircuit: .subckt subname sub_node1 <sub_node...>
                         parts sub_nodes...
			 .ends

         The subcircuit must end with the line: ".ends <subname>"
	 Ground (the 0 node) may be used in a subcircuit but can not
	 be listed as an external node.  Node references in a subcircuit
	 are independent of (not the same node as) any node which may have
	 the same name in either the main circuit or another
	 subcircuit.

**  example of a subcircuit **
.subckt pienet 2 3
c1 2 0 100p
l1 2 3 10u
c2 3 0 100p
.ends pienet
** end of example **




*************** Spice file commands *********************

These commands are placed in the input files for use in the batch mode,
or with the interactive "run" command.

dc operating point

    Format: .op
        This command directs spice3 to include the dc operating
	information in the RAW output file.

DC analysis

    Format: .dc source_name vstart vstop vincrement

AC analysis

    Format: .ac dec nd fstart fstop
        dec is for the decade variation, oct or lin can be used instead
	for the octave or linear variation.  nd is the number of points
	per decade, octave or absolute, depending on option chosen.
	At least one independent source must have been specified with
	an ac value for the analysis to be meaningful.
    NOTE: AC analysis is a linear small-signal analysis.  No clipping
        of signals will take place.

Transient analysis

    Format: .tran tstep tstop <tstart <tmax>>
        Transient analysis always start at time zero, if tstart is
        non-zero, the data between zero and tstart is not saved.


***************** other file commands **********************

These commands are placed in the input files, all are used in the batch
mode, some will not do anything in the interactive mode.  Try it.  If
it works, it works.

.NODESET  V(node_number)=value V(node_number)=value ...
   This line may help spice find the DC or initial transient solution
   by making a preliminary pass with the specified nodes held to the
   given voltages.  The restriction is then released and the iteration
   continues to the true solution.  The .NODESET line may be necessary
   for convergence on bistable or astable circuits, but it should not
   otherwise be needed.

.IC V(node_number)=value V(node_number)=value ...
   This line is for setting transient initial conditions.  It has two
   different interpretations, depending on whether the UIC parameter
   is specified on the .TRAN line.  The .IC line should not be confused
   with the .NODESET line -> the .NODESET line does not affect final
   bias solution (except for multi-stable circuits).
       If the UIC parameter is not specified on the .TRAN control line,
   the DC bias (initial transient) solution is computed before the
   transient analysis.  In this case, the node voltages specified on
   the .IC control line is forced to the desired initial values during
   the bias solution.  During transient analysis, the constraint on
   these node voltages is removed.  This is the preferred method since
   it allows spice to compute a consistent DC solution.
       If the UIC parameter is specified on the .TRAN control line, the
   node voltages specified on the .IC control line are used to compute
   the capacitor, diode, BJT JFET, and MOSFET initial conditions.  This
   is equivalent to specifying the IC=... parameter on each device
   line, but is more convenient.  The IC=... parameter can still be
   specified and takes precedence over the .IC values.  Since no DC
   bias (initial transient) solution is computed before the transient
   analysis, one should take care to specify all dc source voltages on
   the .IC control line if they are to be used to compute device
   initial conditions.

.OPTIONS  option1=value option2=value ...
   This line allows the user to reset program control and user options
   for specific simulation purposes.  Any combination of the following
   options may be included, in any order.  Below, 'x' represents some
   positive number.

     option        effect

     GMIN=x        the minimum conductance allowed (default 1.0e-12)
     RELTOL=x      the relative error tolerance (default .001 -> 0.1
                       percent)
     ABSTOL=x      the absolute current error tolerance (default 1
                       picoamp)
     VNTOL=x       the absolute voltage error tolerance
                       (default 1 microvolt)
     CHGTOL=x      the charge tolerance (default 1.0e-14)
     TRTOL=x       the transient error tolerance (default 7)  This
                       parameter is an estimate of the factor by which
                       spice overestimates the actual truncation error.
     PIVTOL=x      the absolute minimum value for a matrix entry to be
                       accepted as a pivot (default 1.0e-13)
     PIVREL=x      the relative ratio between the largest column entry
                       and an acceptable pivot value (default 1.0e-3)
     TNOM=x        the nominal temperature at which device parameters
		       are measured (default 27 deg C)
     TEMP=x        the operating temperature of the circuit (default
                       27 deg C)
     ITL1=x        the DC iteration limit (default 100)
     ITL2=x        the DC transfer curve iteration limit (default 50)
     ITL3 and ITL5 are not implemented in spice3
     ITL4=x        the transient analysis timepoint iteration limit
                       (default 10)
     METHOD=name   sets the numerical integration method used by spice.
		       possible names "Gear" or "trapezoidal" (or
		       "trap") (default trap)

.save [ node1 ] [ node2 ... ]
   Save a set of outputs, discarding the rest.  Useful only in batch
   mode when a raw file format is used. If a node has been mentioned in
   a save command, it will appear in the raw file.  If there are no
   save commands given, all outputs are saved.  The save command must
   be given before an analysis command to have an affect.

.print analysis_type output_var1 <output_var2 ... output_var8>
.plot analysis_type output_var1 <output_var2 ... output_var8>
   These commands are ignored if a raw file is produced.
    Examples:
    .print ac vdb(1) db(out)
    .print tran v(2) i(vin)
    .plot tran out

.four fundamental_frequency [ value ... ]
   This command is ignored if a raw file is produced.  Does a fourier
   analysis of each of the given values, using the first 10 multiples
   of the fundamental frequency.
    Example:
    .four 10k out

.include file_name
    Examples:
    .include d1n4148.mod
    .include ltc\lm301a



***************** interactive commands ******************

This chapter describes the most important interactive commands
available for use with Spice TR3e2.  It must be remembered that Spice
3e2 was written for the Unix operating system.  Not all of the
"Berkeley" commands will work under DR(MS)-DOS.  Commands that did not
work, or were considered not useful, are not listed.  Those who may
disagree on my definition of "what is useful" are free to call Berkeley
for the "real" documentation(??).

Analysis Commands:

    Note: While commands, in general, are not case sensitive in input
          files, they ARE case sensitive in the interactive mode -> use
          lower case.

     op   Do an operating point analysis.

     tran [ .tran card args ]
          Do a transient analysis.

     ac [ .ac card args ]
          Do an ac analysis.

     dc [ .dc card args ]
          Do a dc transfer curve analysis.

Other Commands:

     alias [ word ] [ text ... ]
          Causes word to be aliased to text.  History substitutions
          may be used, as in C-shell aliases.

     cd [ directory ]
          Change the current working directory to directory, or to
          the user's home directory if none is given.

     destroy [ plot_name ] [ all ]
          Throws away the data in the named plot.  This can be
	  necessary if a lot of large simulations are being done.
	  Spice should warn the user if the size of the memory usage
          is approaching the maximum allowable size (within about 90%).
	  It is advisable to run the rusage command occasionally if
	  running out of space is a possibility, since Spice will crash
	  if it does runs out of memory. If the argument to destroy is
	  all, all plots except the constant plot will be thrown away
	  (it is not possible to destroy the constant plot).  If no
	  argument is given the current plot is destroyed.

     display [ vector_name ... ]
          Prints a summary of currently defined vectors, or of the
	  names specified.  The vectors are sorted by name unless the
	  variable nosort is set.  The information given is the name of
	  the vector, the length, the type of the vector, and whether
	  it is real or complex data.  Additionally, one vector will be
	  labeled [scale]. When a command such as plot is given without
	  a vs argument, this scale is used for the X-axis. It is
	  always the first vector in a rawfile, or the first vector
	  defined in a new plot. If you undefine the scale (i.e, let
	  TIME = []), a random remaining vector will become the scale.

     edit [ file ]
          If a filename is given, then edit that file and (when done)
	  load it (making the circuit the current one)- else edit the
	  current SPICE3 deck.  The default editor is "VI".  The "set
	  editor=XXX" command (in either spice or DOS) can be used to
	  select a different editor.

     fourier fundamental_frequency [ value ... ]
          Does a fourier analysis of each of the given values, using
	  the first 10 multiples of the fundamental frequency (or the
	  first nfreqs, if that variable is set). The output is like
	  that of the .four  card. The values may be any valid
	  expression.  The values are interpolated onto a fixed-space
	  grid with the number of points given by the fourgridsize
	  variable, or 200 if it is not set.  The interpolation will be
	  of degree polydegree if that variable is set, or 1.  If
	  polydegree is 0, then no interpolation will be done.  This is
	  likely to give erroneous results if the time scale is not
	  monotonic, though.

     hardcopy file plotargs
          Just like plot, except creates a file containing the plot.
	  The default file format is postscript.  Other available
	  formants are not useful under DOS.

     history [ number ]
          Print out the history, or the last number commands typed at
	  the keyboard.  Historical substitution is possible, !!<CR>
	  will repeat the last command, !1<CR> will repeat the first
	  command given.

     linearize [ vec ... ]
          Create a new plot with all of the vectors in the current
	  plot, or only those mentioned if arguments are given.  The
	  new vectors will be interpolated onto a linear time scale,
	  which is determined by the values of tstep, tstart, and tstop
	  in the currently active transient analysis.  The currently
	  loaded deck must include a transient analysis (a tran command
	  may be run interactively before the last reset, alternately),
	  and the current plot must be from this transient analysis.
	  This command is needed because SPICE3 doesn't output the
	  results from a transient analysis in the same manner that
	  SPICE2 did.

     listing [ logical ] [ physical ] [ deck ] [ expand ]
          Print a listing of the current circuit. If the "logical"
	  argument is given, the listing is with all continuation lines
	  collapsed into one line, and if the "physical" argument is
	  given the lines are printed out as they were found in the
	  file. The default is logical. A deck listing is just like the
	  physical listing, except without the line numbers it
	  recreates the input file verbatim (except that it does not
	  preserve case).  If the word "expand" is present, the circuit
	  will be printed with all subcircuits expanded.

     load [ filename ] ...
          Loads the raw data from the files named. The default
          filename is rawspice, or the argument to the -r flag
          if there was one.

     plot exprs [ samep ] [ ylimit ylo yhi ] [ xlimit xlo xhi ]
        [ xindices xilo xihi ] [ xcompress comp ] [ xdelta xdel ]
	[ ydelta ydel ] [ xlog ] [ ylog ] [ vs xname ] [ xlabel word ]
	[ ylabel word ]
          Plot the given exprs on the screen.  If samep is given, the
	  values of the other parameters (other than xname) from the
	  previous plot, or hardcopy command will be used unless
	  re-defined on the command line.  The xlimit and ylimit
	  arguments determine the high and low x- and y-limits of the
	  axes, respectively. The xindices arguments determine what
	  range of points are to be plotted - everything between the
	  xilo'th point and the xihi'th point is plotted.  The
	  xcompress argument specifies that only one out of every comp
	  points should be plotted. If an xdelta or a ydelta parameter
	  is present, it specifies the spacing between grid lines on
	  the X- and Y-axis.  These parameter names may be abbreviated
	  to xl, yl, xind, xcomp, xdel, and ydel respectively.  The
	  xname argument is an expression to use as the scale on the
	  x-axis. If xlog or ylog are present, the X or Y scale
	  respectively will be logarithmic.  The xlabel and ylabel
	  arguments cause the specified labels to be used for the X and
	  Y axes, respectively.

     print [ col ] [ line ] expr ...
          Prints the vector described by the expression expr. If the
	  col argument is present, print the vectors named side by
	  side. If line is given, the vectors are printed horizontally.
	  col is the default, unless all the vectors named have a
	  length of one, in which case line is the default.  The
	  options width, length, and nobreak are effective for this
	  command. If the expression is all, all of the vectors
	  available are printed.  The scale vector (time, frequency)
	  will always be in the first column unless the variable
	  noprintscale is true.

     quit
          Quit, return to DOS.

     rusage [ resource ... ]
          Print resource usage statistics.  If any resources are given,
	  just print the usage of that resource.  Currently valid
	  resources are:

                     elapsed
                       The amount of time elapsed since the last rusage
		       elapsed call.

                     space
                       Data space used.

                     time
                       CPU time used so far.

                     everything
                     all
                       All of the above, and more.

     resume
          Resume a simulation after a stop (a control C will stop a
	  run).

     run [ rawfile ]
          Run the simulation as specified in the input file. If a
	  rawfile is given, the data is written, it is also 
	  available interactively.

     save [ node1 ] [ node2 ... ]
          Save a set of outputs, discarding the rest. If a node has
	  been mentioned in a save command, it will appear in the
	  working plot after a run has completed.  If there are no save
	  commands given, all outputs are saved.  The save command must
	  be given before an analysis command to have an affect.  To
          save the branch current through voltage source, add
          "source_name#branch" to the list of nodes.

     set [ variable ] [ variable = value ]
          Set the variable to value, if it is present.  If no value is
	  given then the value is the boolean 'true'.  You can set a
	  variable to be any value (numeric or string).  If a variable
	  is set to a list of values that are enclosed in parentheses
	  (which must be separated from their values by white space),
	  the value of the variable is that list.

           Variables for Spice TR3e2:

             abstol  The absolute tolerance used by the diff command.

             appendwrite
                     Append to the file when a write command is issued,
		     if one already exists.

             combplot
                     Plot vectors by drawing a vertical line from each
		     point to the X-axis, as opposed to joining the
		     points.  Note that this option is subsumed in the
		     plottype option, below.

             editor  The editor to use for the edit command.

             fourgridsize
                     How many points to use for interpolating into when
		     doing fourier analysis.

             gridsize
                     If this variable is set to an integer, this number
		     will be used as the number of equally spaced
		     points to use for the Y-axis when plotting.
		     Otherwise the current scale will be used (which
		     may not have equally spaced points).  If the
		     current scale isn't strictly monotonic, then this
		     option will have no effect.

             height  The length of the page for print col.

             history
                     The number of events to save in the history list.

             nfreqs  The number of frequencies to compute in the
	             fourier command. (Defaults to 10.)

             noaskquit
                     Do not check to make sure that there are no
		     circuits suspended and no plots unsaved.  Normally
		     SPICE3 will warn the user when he tries to quit if
		     this is the case.

             nobjthack
                     Assume that BJT's have 4 nodes.

             nobreak
                     Don't have print col break between pages.

             noclobber
                     Don't overwrite existing files when doing IO
                     redirection.

             nogrid  Don't plot a grid when graphing curves (but
                     do label the axes).

             nomoremode
                     If nomoremode is not set, whenever a large amount
		     of data is being printed to the screen (e.g, the
		     print or display commands), the output will be
		     stopped every screenful and will continue when a
		     carriage return is typed. If nomoremode is set
		     then data will scroll off the screen without
		     hesitation.

             noprintscale
                     Don't print the scale in the leftmost column when
		     a print col command is given.

             nosort  Don't have display sort the variable names.

             numdgt
                     The number of digits to print when printing tables
		     of data (fourier, print col).  The default
		     precision is 6 digits.  Approximately 16 decimal
		     digits are available, so numdgt should not be more
		     than 16.  If the number is negative, one fewer
		     digit is printed to ensure constant widths in
		     tables.

             polydegree
                     The degree of the polynomial that the plot command
		     should fit to the data. If polydegree is N, then
		     nutmeg will fit a degree N polynomial to every set
		     of N points and draw 10 intermediate points in
		     between each end point.  If the points aren't
		     monotonic, then it will try rotating the curve and
		     reducing the degree until a fit is achieved.

             polysteps
                     The number of points to interpolate between every
		     pair of points available when doing curve fitting.
		     The default is 10. (This should really be done
		     automatically.)

             prompt  The prompt, with the character `!' replaced by
                     the current event number.

             rawfile
                     The default name for rawfiles created.

             rawfileprec
                     The number of digits to use in the ascii rawfile
		     format.  The default is 15.

             reltol  The relative tolerance used by the diff command.

             sourcepath
                     A list of the directories to search when a source
		     command is given.  The default is the current
		     directory and the SPICE_PATH\scripts.

             units   If this is degrees, then all the trig functions
                     will use degrees instead of radians.

             unixcom
                     When this variable is set, Spice will try to
                     "shell" any non-spice command.

             vntol   The absolute voltage tolerance used by the
                     diff command.

             width   The width of the page for print col.

     setcirc [ circuit name ]
          Change the current circuit. The current circuit is the one
	  that is used for the simulation commands below.  When a
	  circuit is loaded with the "source" command (see below) it
	  becomes the current circuit.

     setplot [ plotname ]
          Set the current plot to the plot with the given name, or if
	  no name is given, prompt the user with a menu.  (Note that
	  the plots are named as they are loaded, with names like tran1
	  or op2. These names are shown by the setplot and display
	  commands and are used by diff, below.) If the "New plot" item
	  is selected, the current plot will become one with no vectors
	  defined.  Note that here the word "plot" refers to a group of
	  vectors that are the result of one SPICE run.  When more than
	  one file is loaded in, or more than one plot is present in
	  one file, they are keep separate and only the vectors in the
	  current plot can be plotted.

     shell [ args ... ]
          Fork a shell, or execute the arguments as a command to DOS.
	  If the "set unixcom" command is used (as it is in the default
	  spice.rc file), Spice will try to "shell" any non-spice
	  command that it can not "source".

     show device
          Show a device's parameters.

     source file
          Read the Spice input file file.  Interactive Spice commands
	  may be included in the file, but they must be enclosed
	  between the lines ".control" and ".endc"  (the file
	  "spice.rc" which is read on startup does not need these two
	  lines).  These commands are executed immediately after the
	  circuit is loaded.  Spice3 command scripts, other than
	  spice.rc, must begin with a blank or title line.  Also, any
	  line beginning with the characters "*#" will be executed as a
	  command.

          The use of this command is some what unnecessary, since Spice
          will try to "source" any non-spice command.

     unalias [ word ... ]
          Removes any aliases present for the words.

     unset [ word ] ...
          Unset the variables word.

     version [ version_id ]
          displays the version of Spice that is running.  If there are
	  arguments, it checks to make sure that the arguments match
	  the current version of Spice.  This is mainly used as a
	  command line in rawfiles.

     where
          Gives the name of the last node or device to cause
	  non-convergence (for transient and operating point analysis).
	  Note: only one node or device is printed- there may be more
	  than one problem.

     write [ file ] [ exprs ... ]
          Writes the expr's to file. First vectors are grouped together
	  by plots, and written out as such.  Additionally, if the
	  scale for a vector isn't present, it is automatically written
	  out as well.  The default filename is rawspice.raw, or the
	  argument to the -r flag on the command line, if there was
	  one, and the default expression list is all.