STANDARD MICROSYSTEMS CORPORATION 
                         ** SuperDisk **

                 Local Area Network Software Drivers
                               For
                EtherCard PLUS Family of LAN Adapters


                            Version 4.6
                          8 January 1993

     This software is licensed by SMC for use by its customers only.
         Copyright (c) 1993 Standard Microsystems Corporation.
                       All rights reserved.


== CONTENTS ==

The following files are located in the main (root) directory of this
SuperDisk driver diskette:

       File                       Contents

    EZSETUP.EXE    Setup program for use with software configurable
                   adapters (8003EP, 8003EB, 8003W, 8013EP, 8013W,
                   8013EW , 8013EPC, 8013EWC, 8013WC).
    JUMPERS.DOC    Jumper settings and configuration information for
                   Standard Microsystems and Western Digital LAN adapters.
    README.DOC     This file.
    SYSMAP.DOC     System configuration information helpful for
                   identifying configuration conflicts.
    xxx.LAN and    NetWare 286 server and shell driver files that are
    xxx.OBJ        required to be in the root directory.

    DRIVERS.BAT    Copies the AppleTalk Phase 2 files into the root
                   directory on the SuperDisk. Your original SuperDisk 
                   is write protected. You must first make a backup 
                   of the SuperDisk using DISKCOPY before running
                   the DRIVERS.BAT file.

    SOFTWARE.DOC   Software Product Compatibility Guide

    xxx.ADF        Configuration files for Micro Channel adapters.

                   @6FC0.ADF - For Ethernet Micro Channel adapters
                   @6FC1.ADF - For StarLAN Micro Channel adapters
                   @6FC2.ADF - For 10BaseT twisted pair Micro Channel
                               adapters
                   @61C8.ADF - For Elite/A coaxial Ethernet adapters
                   @61C9.ADF - For Elite 10T/A twisted pair Ethernet
                               adapters

    !SMCxx3E0.CFG  EISA Configuration files

                   !SMC03E0.CFG - For EtherCard PLUS Elite Family LAN
                                  Adapters
                   !SMC13E0.CFG - For EtherCard PLUS Elite16 Family
                                  LAN Adapters

    OEMSETUP.INF   Installation Information File for Microsoft Windows
                   for WorkGroups

    SMCMAC.DOS     Driver required for Microsoft Windows for
                   WorkGroups

    IPX.COM        Pre-generated Novell IPX Shell driver

    NETX.COM       Novell's NetWare Re-director shell
    EMSNETX.EXE    Novell's NetWare Re-director that can run in EMS.
    XMSNETX.EXE    Novell's NetWare Re-director that can run in XMS.


Drivers for many LAN operating systems and software utilities are
located in separate subdirectories as follows:

     Subdirectory                 Contents

    DECNET   <DIR> DLL driver for DECnet-DOS and PCSA operating systems

    DIAGNOSE <DIR> LAN adapter diagnostic program and support files

    EZSETUP  <DIR> Documentation for EZSETUP software configuration program 
                   for ISA adapters which is located in root directory.

    NETW_286 <DIR> Documentation for drivers for Novell NetWare 286
                   (shell and server driver files are located in
                   the root of this diskette as required by NetWare
                   286 installation)

    NETW_386 <DIR> Server driver for Novell NetWare version 3.1 (shell
                   drivers are located in the root of this diskette)

    PKT_DRVR <DIR> Packet driver interface allowing concurrent operation
                   of Novell NetWare and many TCP/IP packages

    DOS_ODI  <DIR> Open data-link interface driver to be used with ODI
                   protocol stacks

    NDIS     <DIR> NDIS compliant drivers to be used with NDIS compliant
                   network operating systems and protocol stacks

    OS2_ODI  <DIR> Driver for OS/2 nodes in the Novell NetWare environments

    NADD     <DIR> Program to display the base I/O and network address
                   of installed LAN boards

    PCAGENT        Documentation and driver for the PC Agent/SNMP utility.

In addition to the driver or utility program itself, each subdirectory
contains:

     o an INSTALL.DOC or USER.DOC file that explains how to
       install and use the software; and

     o a RELEASE.DOC file that states the current version,
       release date, and any improvements that were made
       in this version of the software.

**** PLEASE NOTE ****

Each driver on this diskette contains modifications for the 83C690
Network Interface Controller LSI device.  The latest version of each driver
must be used with adapters which contain the 83C690 device.  It
is recommended that the latest version be used in ALL applications.

USE OF ADAPTERS WHICH CONTAIN THE 83C690 WITH OLDER VERSIONS
OF DRIVERS MAY LEAD TO DATA INTEGRITY PROBLEMS.

All of the drivers on this SuperDisk driver diskette function with XT/AT 
bus, EISA and Micro Channel bus systems:

    Ethernet:    EtherCard PLUS Elite (SMC 8003EP or WD8003EP)
                 EtherCard PLUS Elite16 (SMC 8013EPC or SMC 8013EP)
                 EtherCard PLUS Elite16C (SMC 8013EWC or SMC 8013EW)
                 EtherCard PLUS (WD8003E)
                 EtherCard PLUS With Boot ROM Socket (WD8003EBT, 
                  WD8003EB)
                 EtherCard PLUS/A For Micro Channel (SMC 8013EP/A, 
                  WD8003ET/A, SMC 8003E/A)
                 EtherCard PLUS16 (WD8013EBT)

    Ethernet Twisted Pair:
                 EtherCard PLUS Elite16T (SMC8013WC or WD8013W)
                 EtherCard PLUSTP (WD8003WT)
                 EtherCard PLUS10T (SMC8003WC or SMC8003W)
                 EtherCard PLUS10T/A For Micro Channel (SMC8013WP/A,
                  SMC8003W/A)

    StarLAN:     StarCard PLUS (WD8003S)
                 StarLink PLUS (WD8003SH)
                 StarCard PLUS/A For Micro Channel (WD8003ST/A)


== DRIVERS AVAILABLE FROM SMC BBS and COMPUSERVE ==

Standard Microsystems makes documentation, diagnostic software, and
drivers available to its resellers and customers for use with Standard
Microsystems products on the SMC BBS (714-707-2481) and COMPUSERVE.
Once connected to COMPUSERVE enter GO SMC to connect to the Standard 
Microsystems forum.

== BOOT ROMs ==

Use the Standard Microsystems ELITE boot ROM or the latest Western 
Digital boot ROM, marketing model number ROM-NOV F001, on the 
ELITE family boards. This ROM can also be used on older Western 
Digital adapters. Older ROMs sold under marketing model number 
WDROM-NOV F000 from Western Digital will not operate properly on the 
ELITE family of adapters.

== TECHNICAL SUPPORT ==

For assistance call your dealer or distributor's technical support
department.

You can also contact SMC Technical Support via Internet.  The address is:

techsupt@ccmail.west.smc.com

== MANUAL CORRECTIONS ==

The cable 10baseT UTP cable recommendations in Table A-1 reference
Belden part # 9562. This part # should be replaced with 1227A, 1597A
or 1588A.


EtherCard PLUS, TokenCard, and SuperDisk are trademarks, and SMC and 
Standard Microsystems are registered trademarks of Standard
Microsystems Corporation. Other trademarks mentioned herein belong to
their respective companies.