This README file of UDF355.ZIP accompanies USERDEF.EXE for NetWare
v2.15C and above.

The following files are included for this revision:

	USERDEF  EXE    195923 09-30-92   4:14p
	UDF355.DOC       (This file)


USERDEF.EXE version 3.55 fixes the following problem.

With USERDEF.EXE v3.54 and earlier the following sequence will cause a "run-
time R6001 -null pointer assignment" error to occur when you have more than
50 groups defined in the bindery.  Load USERDEF select Edit/View Templates,
select a template from the list, then select View Parameters.  It is possible
that the border of the template parameter screen will show some corruption. 
When you exit USERDEF you will get the above mentioned run-time error.

When you enter the parameter screen USERDEF builds a 50 x 40 array and reads
in the groups from the bindery.  When more than 50 groups exist the array is
over run which causes the null pointer assignment.  USERDEF v3.55 creates an
array that is 250 x 40.  


To install this version of USERDEF complete the following
instructions:  

1)   Login as SUPERVISOR and go to the PUBLIC directory.

2)   Flag USERDEF  SRW.
     (syntax: FLAG USERDEF.* SRW)

3)   Copy the USERDEF.EXE file in UDEF.ZIP to the PUBLIC directory.

4)   Flag the files to SRO.
     (syntax:  FLAG USERDEF.* SRO)


***************************************************************** 
                    DISCLAIMER  
  
Novell, Inc. makes no representations or warranties with respect to
any NetWare software, and specifically disclaims any express or
implied warranties of merchantability, title, or fitness for a
particular purpose.  
Distribution of any NetWare software is forbidden without the
express written consent of Novell, Inc.  Further, Novell reserves
the right to discontinue distribution of any NetWare software.

Novell is not responsible for lost profits or revenue, loss of use
of the software, loss of data, costs of re-creating lost data, the
cost of any substitute equipment or program, or claims by any party
other than you.  Novell strongly recommends a backup be made before
any software is installed.   Technical support for this software
may be provided at the discretion of Novell.
*****************************************************************


*****************************************************************************
                                   CAUTION

ALWAYS backup your system before implementing any program/utility revision
involving the low-level functions of NetWare including re-linking of
operating system .OBJ files, Bindery utilities, drive and volume operation,
etc.

*****************************************************************************