==============================================================================

                               L2 Version 2.1
                             A. Donnie Hale, Jr.
                          Copyright (c) 1992, 1993

                       An OS/2 2.0 file-viewer utility

                             SANSoft Development
                              4971 Pegasus Ct.
                             Hilliard, OH  43026
                         Voice-mail: (614) 898-2675

==============================================================================


Description
-----------
L2 is a text file-viewer utility created for OS/2 2.0 developers and users.
It is developed entirely as a 32-bit application (save the text-mode
interface, which IBM left as 16-bit). Multiple files may be specified on the
command line (now including wildcards!!), and there is no restriction as to
the maximum line length of a file. In addition to the standard features of a
file-viewer utility, L2 incorporates intelligent tab expansion, multiple text
modes, jumping to a specific line number, setting and retrieving of
bookmarks, and regular expression searches.  Also, because L2 loads the file
to be viewed entirely into memory, scrolling, jumping to specific or saved
locations, and text searches are extremely fast.


Release 2.1 Notes
-----------------
To improve ease of use, L2 can now be started without any command-line 
parameters. When this is done, L2 will prompt for a file name or names. Any 
number of file names (with or without wildcards) may be entered at this 
prompt, separated by spaces (up to 60 characters total). L2 will treat this 
list exactly as if it had been entered on the command line. If <Escape> is 
pressed at this point, L2 will exit.

Along with this, while a file is being viewed, the 'N' key will bring up this 
same prompt to allow viewing a new file while within L2. The same rules for 
entering file names given above apply here. The expanded list of files will 
be appended to any current list of files, and the first file found out of the 
additional files will be displayed.

If L2 gets through its entire list of files without being able to load any of 
them, it will bring up the file prompt. Hitting <Escape> will exit at this 
point.

The number of files that may be contained in the file list has been increased 
to 256 files.


Release 2.0 Notes
-----------------
Release 2.0 of L2 incorporates several new features, including wildcard 
filename expansion and a file-selection list. Command-line arguments passed 
to L2 which have wildcards ('*' and '?') are expanded into full file names.  
Arguments without wildcards are left as-is. The F6 and Shift-F6 keys move 
forward and backward through the expanded list of files. The Ctrl-F6 key 
brings up a list of all of the expanded file names, with the currently listed 
file hilited. The desired file may be hilited, and when <Enter> is pressed, 
that file will be loaded. Up to 50 files may be contained in this expanded 
file list.

If there is a problem loading the next/previous/selected file, a message is 
displayed, there is a short pause, and the next file in the list is loaded. 
If L2 gets through the entire list of files without being able to load any of 
them, it will exit.

To work with this capability, the file-search criterion remain across files.  
Thus, if a search is performed on one file and then a new file is selected, 
only the 'A' key needs pressed to repeat that search from the top of the new 
file. The <Esc> key exits L2 altogether.

Also, bookmarks maintain the file in which they are set. Thus, if 5 files are 
in the file list and bookmark 2 is set in file 3, the specified location in 
file 3 will be returned to when bookmark 2 is retrieved while viewing file 1.


Features of L2
--------------
L2 uses "intelligent tab expansion": most text editors allow a tab width to
be set. When <Tab> is pressed, the cursor goes to the next multiple of that
tab stop on the current line. For example, if the tab width is 4, tab stops
would be at columns 1, 5, 9, 13, etc. If the cursor is in column 10 and <Tab>
is pressed, the cursor goes to column 13, where the next character will be
placed.  Editors operate this way so that source code will have correct
indentation.  Assuming that the tabs are saved in the file, most file-viewers
simply display the character after a tab after moving the tab-width number of
places to the right. In the previous example, with a tab-width of 4 and a tab
at column 10, the standard file-viewer would display the next character at
column 14 rather than 13. Thus columns are not aligned correctly, and the
file doesn't look the same in the file-viewer as in the editor. L2 corrects
this problem by using the tab width for locating tab stops the same way that
an editor does.

L2 supports up to 15 video modes, depending on hardware. Its default mode is
80x30 (720x480). When cycling through video modes, L2 stops at the next valid
mode. Also, L2 supports up to 16 BACKGROUND colors, as well as the standard
16 foreground colors, again, depending on hardware.

Specific line numbers may be jumped to. Also, bookmarks may be set and
retrieved. This is useful when examining source code and jumping from one
function to another and back, etc.

L2 supports regular expression searches, so that complex search expressions
may be entered and acted on. This goes beyond the capabilities of most file
viewers.

L2 is strictly for viewing text (ASCII) files, with lines delimited by CR/LF 
combinations. Attempting to view non-text files with L2 will yield 
unpredictable results.


Using L2
--------
First, copy L2.EXE to a directory that is in your PATH statement. Then, to
run L2, simply type L2 at an OS/2 2.0 full-screen or windowed prompt (L2 runs
much better in full-screen mode), followed by 1 or more file names, and then
press <Enter>:

  L2 filenam1.ext [filenam2.ext [filenam3.ext...]] <Enter>

If you run L2 with no file names, L2 will prompt you for the file(s) to view.

L2 will be started in its currently configured state. Initially, that is 80
column by 30 row (720x480 pixels), with default colors, tab expansion on, and
a tab width of 3. There is a means to change these, described later.

L2 comes up with the top of the file displayed starting on the second row,
continuing to the next to the bottom row. The top row is an informational /
status line as shown below:

 FILENAME.EXT  9,999,999 9,999,999  +999,999   999,999      MM/DD/YY  HH:MM:SS
      ³            ³         ³          ³         ³            ³         ³
  file name      line #   # lines    column   file size    file date file time

The column offset area is only displayed when not in the leftmost column.
Also, if the file size exceeds 1,000,000 bytes, it will be displayed in terms
of the number of kilobytes (e.g. 1,354K).

The bottom line on the display is for messages and text input. "Top of file"
and "End of file" are examples of the messages displayed there. Text to be
input includes the text for searches and line numbers for jumping.

Pressing <F1> brings up a simple help screen describing available keys and
their functionality.  Pressing the Escape key (<Esc>) exits L2.


Navigating L2
-------------
The standard navigation keys are used to move throughout the file. These
include:

  Cursor keys ()    - line/column at a time scrolling,
  Ctrl-Left, Ctrl-Right - tab-width at a time horizontal scrolling
  PgUp, PgDn            - page up and page down scrolling
  Home                  - top of file, stay in current column
  Ctrl-Home             - top of file, column 1
  Backspace             - go to column 1
  End                   - end of file, column 1

Other navigation keys include:

  'G' key               - prompted for a line number; go to that line
  '0' - '9' keys        - set bookmarks 0 through 9
  Shift '0' - '9' keys  - retrieve bookmarks 0 through 9


Searching in L2
---------------
There are three types of searches in L2: case-sensitive text search,
case-insensitive text search, and regular expression search. To perform a
search, press:

  'F' key               - perform a case-insensitive search; enter up to 60
                          characters to search for; escape or 0 length search
                          text cancels the search
  'S' key               - case-sensitive search, up to 60 characters
  'R' key               - regular expression search, up to 60 characters in
                          the expression (although the found text may be
                          longer)
  'A' key               - repeat the last search from the last found text

All new searches (i.e., those begun with the 'F', 'S', or 'R' keys) begin at
the top of the file. If the text is found, L2 will move to the line
containing the text and hilite the text.  If the text is not found, a message
will be displayed at the bottom of the screen.  Pressing 'A' after getting a
"Text not found..." message will begin the search again at the top of the
file.

A repeated text search will begin at the first character after the previously
found text. Regular expressions, however, are line-at-a-time searches;
therefore, a repeated regular expression search will begin on the line after
the line containing the previously found text.

The characters available for regular expression searches are:

  ^      - matches beginning of line
  $      - matches end of line
  .      - matches any character
  \      - followed by a single character matches that character, except:
  \b     - backspace
  \s     - space
  \t     - tab
  \\     - backslash
  []     - character class
  [^...] - negative character class
  *      - match 0 or more occurences of the preceding regular expression
  |      - match expression before | or expression after |

Ranges of ASCII characters may be specified in character classes. For
instance, [a-zA-Z0-9] matches any alphanumeric character. The characters * .
^ $ are not special characters within a character class.


Configuring L2
--------------
There are several configurable items in L2, including tab expansion (on/off),
tab width (2-8), screen colors (text, border, hilite, and help), and video
mode. To modify these items, press:

  'T' key               - toggle tab expansion on/off
  'W' key               - cycle the tab width from 2-8 spaces
  'M' key               - cycle the video mode; there are 15 potential video
                          modes, depending on the support your hardware
                          provides
  F2, Shift-F2          - background, foreground text colors
  F3, Shift-F3          - background, foreground border colors
  F4, Shift-F4          - background, foreground hilite colors (found text)
  F5, Shift-F5          - background, foreground help colors

  Note: There are 16 available foreground AND background colors, assuming the
        hardware supports it.

If any of the configurable items are changed, the changes WILL BE LOST if the
configuration is not saved. To save L2's configuration, press the <F10> key.
L2 maintains its configuration information in the L2.EXE file (this is done
to make loading L2 as fast as possible). Since OS/2 keeps the .EXE file open
in DENYWRITE mode while L2.EXE is running, L2 cannot save its configuration
to itelf; therefore L2 saves its configuration in a file called L2CLONE.EXE.
This file can then be renamed to L2.EXE after exiting L2 (to use the RENAME
command, L2.EXE must be deleted or renamed first). One advantage of this
approach is that you can create multiple copies of L2 for viewing different
file types, such as L2C.EXE for C files; L2ASM.EXE for assembler files; etc.
The configuration for each version could be appropriate to that file type.


Registering L2
--------------
L2 was developed to support the author's responsibility of evaluating and
documenting a system with 400+ modules for which the source code was acquired
from a third-party company. It is distributed as shareware with the
confidence that it can help others as well. Your comments, suggestions, and
constructive criticisms are welcome. Please enclose them, along with the
$25.00 registration fee, addressed to:

    SANSoft Development
    4971 Pegasus Ct.
    Hilliard, OH  43026
    Voice-mail: (614) 898-2675

Contact SANSoft Development for site licenses or volume purchases of L2.

Thank you in advance for your support.


Distributing L2
---------------
SANSoft Development retains the sole right to sell L2; however, it may be
distributed, provided:

  A. It is only distributed in its unmodified, archived form (L2.ZIP)
  B. No attempt is made to profit from the distribution of L2 (a duplication
     fee not to exceed $5.00 may be charge by recognized users' groups)


Warranty/Disclaimer
-------------------
SANSoft Development makes no representations or warranties as to the
merchantibility or fitness of this product to a particular purpose. There is
no other warrenty, expressed or implied. SANSoft Development  will not be
liable for any special, incidental, consequential, indirect or similar
damages due to loss of data or any other reason, even if SANSoft or an agent
of SANSoft has been advised of the possibility of such damages. In no event
shall SANSoft Development's liability for any damages ever exceed the price
paid for the license to use the software, regardless of the form of the
claim. The person using the software bears all risk as to the quality and
performance of the software. Use of this package constitutes agreement on the
part of the user to this disclaimer.

============================ E N D  O F  F I L E =============================