Orchid Fahrenheit Display Driver Installation Instructions
                               for IBM OS/2 2.0

                          Driver Release (Beta) 3.0




OS/2 versions supported
-----------------------

This driver release is intended for use with IBM OS/2 2.0 General Availability
(GA), OS/2 2.0 with the application of the IBM OS/2 2.0 Service Pack. Support
for OS/2 2.1 Beta (all versions) is being enhanced. (The drivers have
been tested with OS/2 2.1 Beta 12/92 release and no problems were noted.
Drivers to support OS/2 2.1 GA are under development and will ship at the same
time, or shortly after, OS/2 2.1 becomes a retail (non-beta) product.)



Adapters supported
------------------

This driver release is intended for all Orchid Fahrenheit adapters
(ISA & local bus) using the S3 86C911, 86C924, 86C801 and 86C805 chips.
All supported adapters must have at least 1Mb of video memory installed.
Adapters with 512Kb video memory are not supported.  Memory upgrade
kits are available from Orchid Technology Customer Service
Department. 



Video Resolutions supported
---------------------------

F10X8.DLL supports a resolution of 1024 x 768 with 256 colors at
vertical refresh rates of 45Hz (interlaced), 60Hz or 70Hz (both
non-interlaced).

F8X8.DLL supports a resolution of 800 x 600 with 256 colors at
vertical refresh rates of 56Hz, 60Hz, or 72Hz.



Adapter configuration
---------------------

No special configuration settings are needed.



Installation Procedure
----------------------

Before installing new drivers, it is recommended that a full back up
of the OS/2 system partition be performed.  

For OS/2 2.0 (GA) with ServicePak installed, the installation is
automatic using DSPINSTL.EXE  With OS/2 installed for VGA or previous
driver release, select DSPINSTL.EXE from DRIVES folder (on drive A:
or B: containing Orchid OS/2 driver disk) and select appropriate
options from menu.


When DSPINSTL is complete, please verify on your OS/2 boot drive
(C:\OS2) system directory, that a new SVGADATA.PMI file has been
created.  If not, create a SVGADATA.PMI file by running SVGA.EXE.
SVGA can be run in a DOS full screen session (the preferred choice),
an OS/2 full screen session, or a real DOS environment. For the first
two choices 

        svga on

should result in the creation of a SVGADATA.PMI file located in the
C:\OS2 subdirectory. 

If SVGA.EXE is run in a real DOS environment, the following command
line should be used 

        svga on dos

In a "real" DOS environment, SVGA.EXE creates a file SVGADATA.DOS
which must be renamed to SVGADATA.PMI. SVGADATA.PMI must reside in
the C:\OS2 subdirectory located on the OS/2 boot volume. If the boot
volume is not located on C:, then a dummy \OS2 subdirectory must be
created and a copy of the SVGADATA.PMI must be placed in it. 


Manual Installation 
-------------------

For OS/2 2.0 the installation has to be performed manually.  Follow
the procedure described below.

Note: in the following examples, the Orchid Fahrenheit OS/2 drivers
disk is assumed to be in drive A: and the OS/2 system files are
assumed to be on drive C:. If your situation is different, please
substitute the approriate drive letters.


Installing DISPLAY.DLL
----------------------

Create a subdirectory under C:\OS2\DLL on the OS/2 boot partition.

        md c:\os2\dll\orchid
        cd c:\os2\dll\orchid

Then copy the appropriate driver file from the Orchid Fahrenheit OS/2
driver diskette to this directory using the OS/2 UNPACK command.
(UNPACK is supplied with OS/2 and can be found in the \OS2
subdirectory.) For example, to install the 800x600 256 color driver
use

        UNPACK a:\f8x8.dl@

To install the 1024x768 256 color driver use

        UNPACK a:\f1x8.dl@




OS/2 CONFIG.SYS file changes
----------------------------

Use a text editor and modify the LIBPATH statement in the OS/2 2.0
CONFIG.SYS to put the ORCHID subdirectory in the LIBPATH path. It
should be placed before any other LIBPATH entries.

As an example 

        LIBPATH=.;C:\OS2\DLL;C:\OS2\MDOS;C:\;

should be changed to

        LIBPATH=C:\OS2\DLL\ORCHID;.;C:\OS2\DLL;C:\OS2\MDOS;C:\;

While editing the CONFIG.SYS file, add the following line

        DEVICE=C:\OS2\MDOS\VSVGA.SYS

Remove or comment out the following line

        DEVICE=C:\OS2\MDOS\VVGA.SYS

Also, add the line 

        SET VIO_VGA=DEVICE(BVHVGA,BVHSVGA)

and remove or comment out line

        SET VIO_VGA=DEVICE(BVHVGA)



BVHSVGA (Base Video Handler Super VGA) support file installation
----------------------------------------------------------------------

In the C:\OS2\DLL subdirectory, rename file BVHSVGA.DLL to
BVHSVGA.RTL.  Copy the BVHSVGA.DL@ from the Orchid Fahrenheit OS/2
driver diskette to this subdirectory using the UNPACK command

        UNPACK a:\bvhsvga.dl@


VSVGA (Virtual Device Driver - VDD) support file installation
-------------------------------------------------------------------

Switch to the C:\OS2\MDOS subdirectory. If the file VSVGA.SYS exists, rename
it to VSVGA.RTL. Copy the Orchid VSVGA.SY@ file from the Orchid Fahrenheit
OS/2 Driver diskette to this subdirectory using the UNPACK command

        UNPACK a:\vsvga.sy@

Return to the C:\OS2 subdirectory and if the file SVGA.EXE exists,
rename it to SVGA.RTL. Copy the SVGA.EX@ file from the Orchid
Fahrenheit OS/2 Driver diskette into the C:\OS2 subdirectory using
the UNPACK command.

        UNPACK a:\svga.ex@

Create a SVGADATA.PMI file by running SVGA.EXE. SVGA can be run in a
DOS full screen session (the preferred choice), an OS/2 full screen
session, or a real DOS environment. For the first two choices 

        svga on

should result in the creation of a SVGADATA.PMI file located in the
C:\OS2 subdirectory. 

If SVGA.EXE is run in a real DOS environment, the following command
line should be used 

        svga on dos

In a "real" DOS environment, SVGA.EXE creates a file SVGADATA.DOS
which must be renamed to SVGADATA.PMI. SVGADATA.PMI must reside in
the C:\OS2 subdirectory located on the OS/2 boot volume. If the boot
volume is not located on C:, then a dummy \OS2 subdirectory must be
created and a copy of the SVGADATA.PMI must be placed in it. 



DOS settings
------------

Switch-Notification

Recommended setting for most reliable operation is OFF. Setting this
setting to OFF forces the VDD to assume complete responsibility for
saving or restoring the video hardware state upon a background or
foreground switch. 


I/O Trapping

When turned ON, accessess to the S3 86C911/924/801/805 enhanced I/O
ports are trapped and shadowed by the VDD. This trapping and
shadowing will affect performance, but is necessary when the
Fahrenheit adapter is being used in one of the enhanced modes and the
state is required to be restored completely. 


Known Shortcomings or Problems
------------------------------

For Fahrenheit VA and VLB (S3 86C80X) boards, the SVGA VESA mode support
in full screen DOS modes has not been fully verified.


Support & Feedback
------------------

Driver support questions or feedback can be addressed to the Orchid
Technical Support Department by voice phone: 510 683 0323; CIS EMAIL
(use Orchid's Customer Service ID 76467,1424); or by FAX (510 683
0379 or 510 683 0355). 

If submitting a problem report, or just supplying feedback, please
have ready a complete system hardware description along with detailed
steps to re-create the symptoms. If submitting problem or feedback
reports via CIS EMAIL or FAX, please include a daytime phone number
and a best time to call in case Orchid Technical Support needs more
information. 



Warranty Disclaimer
-------------------

The software and documentation is a beta release and one or both may
be modified  in subsequent releases. Performance and reliability of
this software release may not be at the level usually associated with
Orchid display drivers. Driver and documentation are supplied "as
is" basis.