=========================================================================
Date: 4 December 92, 11:38:05 EST
From: BEIDL    at RALVM29
To:   ADOMAVIC at CANVM2
Hi George,
    I have just sent you 3 additional files.  After talking with Danny,
I learned that the Toshiba 4500 uses the Intel 82365 controller and not
the proprietary part used on the Toshiba 3300.  Also, since you have an old
engineering card, it is possible that the CIS data on the card does not
contain a checksum.  The new enablers will reject the card if a valid
checksum is not found.  The description of the 4 enablers we sent you is
as follows:

     TOSH3270.EXE    For use on Toshiba 3300 with proprietary controller.
                     - requires checksum tuple on 3270 Credit Card.

     INTL3270.EXE    For use with any system having the Intel 82365 controller.
                     - requires checksum tuple on 3270 Credit Card.

     TOSH8LV.EXE     For use on Toshiba 3300 with proprietary controller.
                     - Does not validate CIS data (old card should work).

     INTL8LV.EXE     For use with any system having the Intel 82365 controller.
                     - Does not validate CIS data (old card should work).

     The enabler must be run before executing the diagnostics or an
emulator (such as PC3270).  The enabler configures the card to use
     I/O            2D0 -> 2DF
     Memory         CE00:0
     IRQ9           (which gets revectored to IRQ2 by BIOS).

     Also, once an emulator has been started it must be terminated or
the system rebooted before running the diagnostics.  (Both the emulator
and the diagnostics will fail it they both THINK they own the hardware at
the same time).

    John