ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10DC X10 Direct Control
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Version 1.3
July 1993

Copyright 1993 ù D.Huras ù All Rights Reserved

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
CONTENTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 1. DESCRIPTION
 2. WARRANTY
 3. FEATURE OVERVIEW
 4. REQUIREMENTS
 5. INSTALLATION INSTRUCTIONS
 6. COMMAND LINE ARGUMENTS
 7. OPERATING MODES
 8. DEBUG MODE
 9. PROGRAM OVERVIEW
10. KEYBOARD USAGE
11. MENU BAR
12. CP290 SELF TEST
13. SIGNAL TEST GENERATOR
14. CLOCK SYNCHRONIZATION
15. BASE HOUSECODE
16. PROBLEM RESOLUTION
17. REGISTRATION INFORMATION
18. OTHER X-10 BASED SOFTWARE
19. RELEASE HISTORY

1. DESCRIPTION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10DC is a program which sends immediate commands to the X10 CP290
(*1) Computer Interface.  The CP290 transmits these commands over the
power line to control X10 devices.  X10DC does not currently modify
the EVENT DATA stored in the CP290 Interface (*2).  X10DC is a DOS
program that uses a simple point & click user interface.  (A Mouse
though not required is highly recommended).  X10DC is designed to be
robust software that is processor speed independant.  This program is
shareware and you are invited to evaluate it for 30 days. If you
continue to use the program after the 30 day evaluation period you are
asked to register it.  The author retains all rights to the program.

(*1) The CP290 Computer Interface is a device manufactured by X-10
     that can be connected to a micro-computer serial port.  The CP290
     also plugs into an electrical outlet and it is through this
     connection that the CP290 imposes X-10 commands onto the powerline.
     X-10 commands use the power line as a carrier; other X-10 devices
     connected to the power line will respond to these commands (ie.
     switch ON/OFF lights, appliances).

2. WARRANTY
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10DC is supplied as is.  The author disclaims all warranties,
expressed or implied, including, without limitation, the warranties
of merchantability and of fitness for any purpose.  The author
assumes no liability for damages, direct or consequential, which may
result from the use of X10DC.

3. FEATURE OVERVIEW
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ù User-Friendly point & click DOS character-based Interface

ù All program functions can be controlled using a mouse; no keyboard
  intervention is required.

ù The Program supports 3 operating modes; each mode uses a different
  combination of on-screen controls.  Mode 1 is suggested for users
  not using a mouse.

ù When running in Mode 3, the program reads in an X10.DAT file
  [this file format is used by the X10 Program supplied with
  the CP290 Interface] and presents a list box of device
  descriptions/locations which can be targetted for commands.
  (The Unregistered version will only send commands to the 1st
   8 Devices found; SEE REGISTRATION BENEFITS)

ù Commands can be sent to all 256 X10 device addresses.

ù Commands can be targetted for any number of units within an X10
  House Code (effectively supporting for ALL ON and ALL OFF).

ù Supports 16 discrete dimming levels.

ù Acknowledgements sent from the CP290 (after receiving commands from
  the program) are monitored and checksums are verifed.

ù A scrollable Command History is available for browsing while the
  program is running.

ù A software-based Signal Test Generator is available to assist in
  identifying and isolating X10 transmission/reception problems.

ù A Debug Mode is available which reports all data sent from the
  CP290 as well as timing information.

ù A CP290 Self Test with event preservation is supported.
  (*2) NOTE, the self test overwrites the EVENT DATA.  X10DC
  will preserve the EVENT DATA by downloading it from the
  CP290, saving it in memory, running the Self Test, and
  finally uploading the saved EVENT DATA back to the CP290.

ù Clock Synchronization function for the CP290 and the PC

ù Change Base HouseCode stored in the CP290 function with
  or without Event Preservation.

ù A comprehensive on-line Help sub-system that can be disabled
  at the user's option to decrease program load time.

ù The program WILL load without a CP290 Interface attached, however
  all attempts at serial communications will result in errors; the
  program will attempt to trap all such errors.

4. REQUIREMENTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ù An IBM-Compatible PC w/serial port [COMMPORT 1 or 2]

ù An X10 CP290 Computer Interface attached to COMMPORT 1 or 2.
  [NOTE: Support for COMMPORT's 3 & 4 may be provided in the
         future depending on user response to the program]

ù A Microsoft-Compatible Mouse is highly recommended

ù A Colour adapter/display is recommended although the program
  should run with a monochrome display/adapter.  If you
  experience problems with the default colors, then try the /BW
  command line argument which will set everything to Black &
  White.

The program requires approximately 415K available conventional memory
to run.  The Command History will consume up to an additional 32K
of memory however this translates to approximately 1000 commands; its
unlikely that this many commands will be sent during one invokation of
the program.  However, if Debug Mode is on, the Command History will
quickly fill up since all CP290 responses are reported in the
Command History list box.

6. INSTALLATION INSTRUCTIONS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
There are no special installation instructions; simply copy the
program to a sub-directory of your choice and run it.  The program
will look for 3 files in the directory it is run from.  However,
the program will run with or without the following 3 files:

  1) X10.DAT
     If you want to use Mode 3 then you may want to copy an
     X10.DAT file to the sub-directory where you have installed
     X10DC.EXE.  Alternatively, you can load an X10.DAT file from
     any sub-directory by using the 'Load X10 File' menu option.
     An X10.DAT file is a file format used by the X10 program
     supplied by X10 with the CP290 interface.  The unit
     addresses, locations and descriptions are read from this
     file and presented in a list box by X10DC.  X10DC DOES NOT
     MODIFY THE X10.DAT FILE.  A sample X10.DAT is provided
     with X10DC.

  2) X10DC.HLP
     X10DC retrieves the on-line help text from this file. If the
     file is not found then X10DC will display a message during
     startup and then continue.  The help feature will be
     unavailable in this case.  If you decide that you no longer
     need the help sub-system, then you should run the program
     with the /NH command line argument; this will suppress the
     'Help not found' message and decrease program load time.

  3) X10DC.INI
     The registered version of the program will look for a
     X10DC.INI file in the current directory.  The X10DC.INI file
     is a text file containing all program parameters; there is no
     need to create this file yourself since the program will
     generate one whenever you select the 'Save Options' menu item.
     A sample X10DC.INI file (generated by X10DC.EXE) is shown
     below:

;
;X10DC.INI File Created: 07-18-1993 01:30:00
;
;All Lines prefixed with ; are ignored
; Program Options
; ---------------
; Commport=1/2                   DEFAULT=1
; Mode=1,2 OR 3                  DEFAULT=1
; Debug=ON/OFF                   DEFAULT=OFF
; X10FileName=[d:]\FILENAME.EXT  DEFAULT=X10.DAT
; LoadHelp=YES/NO                DEFAULT=YES
; Sounds=ON/OFF                  DEFAULT=ON
;
CommPort=1
Mode=2
Debug=ON
X10File=F:\X10\X10\X10.DAT
;
; Colour Values
; -------------
; 0=Black  4=Red       8=Gray          12=Bright Red
; 1=Blue   5=Magenta   9=Bright Blue   13=Pink
; 2=Green  6=Brown    10=Bright Green  14=Yellow
; 3=Cyan   7=White    11=Bright Cyan   15=Bright White
;
BackColor=7
ForeColor=0
HiLiteKey=14
DisabledItem=8
MenuBackColor=1
MenuForeColor=7
MenuSelectedBackColor=15
MenuSelectedForeColor=1
LabelBackColor=8
LabelForeColor=15
DebugForeColor=4
HelpTitleBackColor=5
HelpTitleForeColor=15
StatusTitleBackColor=4
StatusTitleForeColor=15
WarningTitleBackColor=12
WarningTitleForeColor=15
;
; Other Screen Settings
; ----------------------
; ThreeD=ON/OFF*                 DEFAULT=ON
; Shadow=ON/OFF*                 DEFAULT=ON
;  * OFF Recommended for Monochrome Displays
;
ThreeD=ON
Shadow=ON
;
; End of X10DC.INI (01:30:00)

This X10DC.FILE was created using the 'Save Options' menu item.

6. COMMAND LINE ARGUMENTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
DEFAULTS:  If the program is run without any command line arguments
           it will default to COMMPORT 1,OPERATING MODE 1,DEBUG OFF,
           F:X10.DAT.

The following command line arguments can be entered in any order:

/BW ù Use Monochrome colours (Black & White)

/Cn ù COMMPORT where n = 1 OR 2

/F:[d]\filename ù X10.DAT FILE SPECIFICATION for MODE 3
      where [d] = drivespec eg. /F:C:\X10\X10.DAT

/D  ù TURNS ON DEBUG MODE
      When DEBUG MODE is ON, the CP290 responses & checksums are
      displayed in the Command History List Box.

/Mn ù MODE where n = 1,2 or 3
      MODE 1 Provides a List Box of Unit Codes; only 1 Unit Code
             can be selected.  However, this mode will be easier to
             use if you don't have a mouse since you'd have to TAB
             through all the unit code check boxes used in MODE 2.
      MODE 2 Provides a Check Box for each Unit Code plus ALL and
             NONE buttons to quickly Check/Uncheck all check boxes.
             In this mode, multiple Unit Codes can be targetted for
             the X10 Command.
      MODE 3 Provides a List Box of Devices which are read from
             an X10.DAT file; X10DC will look for "X10.DAT" in the
             current directory UNLESS the /F: command line argument
             is supplied.  If X10.DAT cannot be found, the program
             will switch to Mode 1.  Select 'Load X10 File' under
             the File menu to load an X10.DAT file from another
             sub-directory. (Once the file is loaded, its location
             can be saved [REGISTERED VERSION ONLY] by selecting
             'Save Options' under the Options menu.

             NOTE: ONLY THE 1st 8 DEVICES CAN BE TARGETTED FOR
                   COMMANDS WITH THE UNREGISTERED VERSION.

NOTES: 1) All Command Line directives (with the exception of /NH)
          can be modified once the program loads by selecting
          the appropriate menu items under the Options Menu.
          Registered Users can then save all these settings to the
          X10DC.INI file by using the 'Save Options' menu item.

       2) COMMAND LINE OPTIONS OVERRIDE ALL X10DC.INI SETTINGS

7. OPERATING MODES
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Operating Mode can be set using the 'Options' menu, the MODE command
button (cycles through the modes), or the /M command line argument.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
MODE 1                    Unit
                          Code            NOTE: Mode can be toggled
In this mode only        ÚÄÄÄÄÄ¿                at runtime by clicking
one Unit Code can be     ³   1                 the MODE button.
selected from the        ³   2 Û                (Keyboard users press
Unit Code List Box.      ³   3 °                 ALT-m).
                         ³   4 °
                         ³   5 °                Can also be set from
                         ³   6                 the Options Menu.
                         ÀÄÄÄÄÄÙ
RECOMMENDED IF YOU DON'T HAVE A MOUSE.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
MODE 2                             Unit Code(s)
                         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
In this mode multiple    ³[X] 1  [ ] 5  [ ] 9   [ ] 13³
Unit Codes can be        ³[ ] 2  [ ] 6  [ ] 10  [ ] 14³
checked; in addition     ³[ ] 3  [ ] 7  [ ] 11  [ ] 15³
the ALL button can be    ³[ ] 4  [ ] 8  [ ] 12  [ ] 16³
clicked to check all     ³ÚÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄÄÄÄÄÄ¿³
the Unit Codes. The      ³³    ALL    ³  ³    NONE   ³³
NONE button unchecks     ³ÀÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÙ³
all the unit codes.      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
MODE 3          ** Example 1 **
                  Unit Location               Description
An X10.DAT      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
is read and     ³ A  1³DINING ROOM           ³TABLE LAMP             
a List Box      ³ A  2³FAMILY ROOM           ³TV                     Û
replaces the    ³ A  3³GARAGE                ³CEILING LIGHT          °
House/Unit      ³ A  4³GUEST ROOM            ³DE-HUMIDIFIER          °
Controls used   ³ G  7³HALL                  ³CEILING LIGHT          
in Modes 1 & 2. ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
Also note that   {11 Device(s) Found}       Brightness[             ]
due to a                                    [1 = OFF]
shortage of
screen real
estate, a Combo
Box replaces                                          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
the Brightness  ** Example 2 **                       ³  1 ÷  0.0 %  
List Box. When    Unit Location               Descript³  2 ÷  6.7 %  Û
the down-arrow  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ³  3 ÷ 13.3 %  °
is clicked (or  ³ A  1³DINING ROOM           ³TABLE LA³  4 ÷ 20.0 %  °
F4 is pressed)  ³ A  2³FAMILY ROOM           ³TV      ³  5 ÷ 26.7 %  °
a List Box will ³ A  3³GARAGE                ³CEILING ³  6 ÷ 33.3 %  °
pop up as shown ³ A  4³GUEST ROOM            ³DE-HUMID³  7 ÷ 40.0 %  °
in Example 2.   ³ G  7³HALL                  ³CEILING ³  8 ÷ 46.7 %  
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                 {11 Device(s) Found}       Brightness[ 8 ÷ 46.7 %  ]
                                            [1 = OFF]

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
8. DEBUG MODE

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³ Using COMMPORT: 2        X10 DIRECT CONTROL     CP290 Day: Tuesday ³
³Base House Code: P           Version 1.2          CP290 Time: 11:51 ³
³Mode: 1   Debug ON        (c)1993 ù D.Huras          PC Time: 11:52 ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
               ÀÄÄÄÄ¿
                  ÄÄÁÄÄÄÄÄ
When enabled, the DEBUG ON message appears in the screen Header and all
responses from the CP290 are displayed in the Command History List Box,
as well as Checksums and Timing Information.

Debug Mode can be toggled ON/OFF from the Options Menu.

NOTE: Debug Mode increases program overhead; memory requirements will
be greater and program performance will be somewhat degraded.  It is
recommended that you only toggle Debug Mode ON when necessary.

9. USING THE PROGRAM
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
When the program first loads, it requests the base house code and
time stored in the CP290 via serial I/O using the selected COMMPORT.
This information will be reported in the Screen Header if found.
Note:  the CP290 Time and PC Time reported in the Screen are static
and are only updated when the Base House Code is changed, a
Self-Test is run or the Time is set.  You can use the 'Refresh' menu
item under the 'Clock' menu to force an update to the on-screen Time
displays.  The House Code List Box defaults to the Base House Code
if the CP290 is found.  Once the program is loaded the SEND command
button is disabled until you have selected a Unit Code(s). If the
DIM command is selected a Brightness Level must be be selected
before the SEND button becomes enabled.  The Command History list
box is scrollable and will store up to 1000 commands after which it
becomes a circular FIFO buffer.

10. KEYBOARD USAGE
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Use the TAB/Shift-TAB keys to move among the various controls.(*3)
The Up/Down arrows can be used to move up and down List Boxes, and
the Spacebar and Enter key can be used to select the current List
Box item, check/uncheck a check box, or invoke a command button.
The ESCAPE key will exit the current function or the program if no
other windows are visible.  All of the Command Buttons and controls
have quick access keys:

     House Code ù Alt-o [Mode 1 & 2]
   Unit Code(s) ù Alt-u [Mode 1 & 2]
    Device List ù Alt-u [Mode 3]
            ALL ù Alt-l [Mode 2]
           NONE ù Alt-n [Mode 2]
         Action ù Alt-a
     Brightness ù Alt-b [when enabled]

           MODE ù Alt-m (*3)
           SEND ù Alt-s
           EXIT ù Alt-x
           HELP ù Alt-h
      SELF TEST ù Alt-t [When DEBUG Mode Enabled] (*3)

Command History ù Alt-c

(*3) The MODE Command Button is NOT in the TAB STOP sequence;
     Keyboard users must use ALT+character to access this
     button. (This eliminates extraneous TAB keystrokes)

11. MENU BAR
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Press & release the ALT key to activate the Menu Bar.  Menu items
can be selected by pressing the highlighted key (when applicable),
or by positioning the highlight bar using the up/down arrow keys and
pressing ENTER.  Some screen button functions are replicated within
the menus (eg. Exit, Help).  However, there are some functions which
are only available from within menus.  CommPort, Operating Mode, &
Debug can all be set from the Options Menu; the current state of
each of these parameters is indicated on the menu itself with a 'ù'
character to the left of the menu item.

The following short-cut keys can also be used at any time to
select menu items:

*FILE* Menu
     Load X10 File ù Ctrl-L
         Exit      ù Ctrl-X (Same as Exit Button, Alt-X)

*CLOCK* Menu
         Set PC Clock ù Ctrl-T (Enter Time)
      Set CP290 Clock ù Ctrl-K (Synchronize w/PC) - Registered Version
       Refresh Clocks ù Ctrl-R
   Set Base HouseCode ù Ctrl-B (Preserve Events) - Registered Version

*TEST* Menu
      CP290 Self Test ù Ctrl-E
Signal Test Generator ù Ctrl-G

*OPTIONS* Menu
           CommPort 1 ù Ctrl-F1
           CommPort 2 ù Ctrl-F2

               Mode 1 ù Shift-F1
               Mode 2 ù Shift-F2
               Mode 3 ù Shift-F3

        Sounds Toggle ù Ctrl-D
    Debug Mode Toggle ù Ctrl-D

       Screen Colours ù Ctrl-C

         Save Options ù Ctrl-S  [Not Available in Unregistered Version]

*HELP* Menu
                 Help ù F1 (Same as Help Button, Alt-H)
                About ù Ctrl-A

12. CP290 SELF TEST
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The CP290 can perform a Self-Test to determine if there are any
detectable problems within the device.  The Self-Test will return
either a pass or fail status when it is run.  X10DC will report the
results of the test in the CP290 Status window.  Whenever a
Self-Test is run the memory contents of the CP290 are overwritten.
X10DC can preserve the CP290 Event Data by downloading it from the
CP290 prior to the Self-Test and uploading it back to the CP290
after the Test.  (X10DC also allows a Self-Test to be invoked
without event preservation, but this leaves the device in a state
which may cause problems with other programs that communicate with
the CP290. It is recommended that the Self-Test always be invoked
with Event Preservation regardless of whether or not there is any
stored Event Data.)

13. SIGNAL TEST GENERATOR
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The Signal Test Generator is a powerful feature that enables the
user to track down and isolate X-10 transmission/reception problems
and faulty modules.  This feature will send X-10 ON/OFF commands
repeatedly until the test is ended by the user.  (Similar to the
Leviton 6385 device).  The address to be targetted for commands can
be a fixed House Code and Unit Code; alternatively, either the House
Code or Unit Code (or both) can be varied. This allows you to send
commands repeatedly to:

ù A 'Fixed' House Code & 'Fixed' Unit Code (eg. A1)
ù A 'Fixed' House Code & 'Variable' Unit Code (eg. A1 - A16)
ù A 'Variable' House Code & 'Variable' Unit Code (ie. A1 - P16;
  All 256 addresses would be tested in this case)
ù A 'Variable' House Code & 'Fixed' Unit Code (eg. A1 - P1)

When the Signal Test Generator is selected, a window is
displayed that allows you to set the House Code & Unit Code to
either 'Fixed' or 'Variable' mode; if 'Fixed' is selected then
a List Box is enabled so that the fixed code can be selected.
The Delay between commands can be set from 0 to 60 seconds;
this delay applies to the pause between each pair of ON/OFF
commands.  Once all required settings have been made the OK
button becomes enabled.  When the OK button is clicked the
test will begin; the test can be terminated by pressing [Esc].
Note, if the Delay is set to 0, then the [Esc] key may have to
be hit several times to stop the Signal Test.  X10DC will emit
a brief beep before each ON command is sent, and another lower
pitched beep before each OFF command is sent.  These beeps can
be disabled by toggling the Sounds item on the 'Options'
Menu.

'Fixed' Mode Testing
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Generally speaking, you would want to use the 'Fixed' option
to test the range of X-10 signal reception by starting the
Signal Test using address P1 for example (the "only" address
that the Leviton 6385 will test) and then walking around to a
variety of outlet locations within your home and plugging in a
module set to P1 to see if the ON & OFF commands are being
received at all locations.  The program attempts to let you
know when the commands are sent by beeping although you may
not be able to hear the beep from all outlet locations.

'Variable' Mode Testing
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The 'Variable'(*4) option can be used when you suspect that an
X-10 module has trouble receiving commands targetted for
specific House and/or Unit Codes.  In this case, instead of
walking around to locations, you would adjust the House and/or
Unit Code dials on the module as the Signal Test cycles
through each combination.  You may want to toggle the Sounds
off in this case.

ÄÄÄÄ
(*4) Not available in UNREGISTERED Version

14. CLOCK SYNCHRONIZATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Clocks tend to run either fast or slow and therefore should be
synchronized periodically.  X10DC allows you to set the time in both
the PC and CP290 manually by specifying hh:mm and also allows you to
synchronize the PC and CP290 by using one of the clocks to set the
other.  When the PC clock is used to synchronize the CP290 clock,
X10DC will wait until the seconds are at zero since the resolution
of the CP290 clock is limited to minutes.  (This wait can be
cancelled by pressing the [Esc] key).  When the CP290 is used to
synchronize the PC, the hours and minutes from the CP290 are used
immediately to set the PC Clock; since the CP290 cannot provide
'seconds', it is recommended that a CP290->PC Clock Sync be followed
by a PC->CP290 Clock Sync.  This will ensure that both Clocks are
synchronized.

15. BASE HOUSECODE
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The Base HouseCode stored in the CP290 is only applicable to the
rocker keys on the top of the CP290.  These keys are labelled 1 to 8
and correspond to whatever House Code is stored as the Base
HouseCode in the CP290.  The CP290 re-initializes itself whenever
the Base HouseCode is changed; as a result, all of the CP290 Event
Data is erased.  X10DC gives you the option of either Preserving or
Erasing the Event Data whenever the Base HouseCode is changed.  If
the user elects to preserve the Event Data, it is downloaded from
the CP290 before the Base HouseCode is changed and then uploaded
back to the CP290 after the Base HouseCode has been changed.

16. PROBLEM RESOLUTION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Generally, if your CP290 works with the X10 supplied software then
you should have no problems running X10DC.  Ensure that you include
the Command Line argument /C2 if your CP290 is connected to COMMPORT
2.  If you run X10DC with a modem attached to the COMMPORT, you may
get unpredictable results since the modem will echo everything back
to X10DC.  If problems persist, try using the /D Debug mode and then
scrolling through the Command History List Box; see if the calc-
culated checksums match; look at the TIMER and MaxTimer Values. If
the MaxTimer Value exceeds the TIMER value then the program is
timing out while waiting for X10 responses.  PLEASE REPORT ANY
TIMING PROBLEMS TO ME; adjustments can be made to the program to
improve its compatibility if this turns out to be a problem.  As a
last resort, you may want to run the CP290 Self Test, but only do so
if you have backed up your EVENT DATA.  In some cases X10DC may
report that a command failed, or a checksum did not match, but in
fact the command was accepted by the CP290 and transmitted on the
powerline.  This could happen if spurious responses are received
from the CP290, ie. if you were to press buttons on the CP290 just
after sending a command.  If this happens, exit the program and
re-invoke it to resynchronize, alternatively, if you have 2 serial
ports you could try toggling the CommPort. (ie. if your CP290 is on
CommPort 1 then switch to CommPort 2, then switch back to CommPort
1).

The open architecture of the PC compatible operating environment and
the near infinite combinations of hardware and software complicate
the compatibility of applications software.  While every attempt has
been made to ensure that X10DC is compatible with all hardware/
software combinations, there may be operating environments in which
X10DC will not run properly.  The author will attempt to resolve any
problems you experience; please report all problems to:

   David Huras
   CIS ID: 72767,472

You can also report problems in writing to:

    David Huras
    37 Ruddell Crescent
    Georgetown, Ont. L7G 5N4
    CANADA

    FAX: 416-873-6429

  ù Any feedback (both positive & negative) is welcomed! ù

17. REGISTRATION INFORMATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10DC is currently supplied as fully functioning software without
built-in delays or "nag" screens prompting you to register.  The
ABOUT screen contains registration information in case this
documentation file gets misplaced.  A significant amount of time and
effort went into this program; please register the program if you
intend to use it beyond the 30 day evaluation period.  Registered
Users will be shipped a printed manual and a 3«" diskette (if you
would prefer a 5¬" diskette please advise) containing the Registered
Version of the program which includes the following features:

ù Full support for the Signal Test Generator which allows you to
  cycle through all House & Unit Codes and send an ON/OFF command
  to each address.

ù Full support for operating mode 3 which reads in an X10.DAT file
  and builds a "list box" of device names which can be targetted
  for X10 commands.  (Unregistered Version will only send commands
  to the first 8 Devices).

ù Support for an INI file which provides complete program
  customization capabilities including Screen Colours.

Register via CompuServe Shareware Registration;
 GO SWREG (Registration ID# 620)

   -=OR=-

Register by sending $20 to:

   David Huras
   37 Ruddell Crescent
   Georgetown, Ont. L7G 5N4
   CANADA

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
ºREGISTERED USERS of prior versions of X10DC can upgrade to theº
ºcurrent version at ANY TIME by simply sending a diskette      º
ºcontaining their registered version of the software to the    º
ºaddress above.                                                º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

18. OTHER X10-BASED SOFTWARE by David Huras
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Program   Description                                     Status
-------   ------------------------------------------   --------------
X10DC     X10 Direct Control - CP290 Point & Click     Version 1.30
          Initial Release: February '93                July '93

X10EC     X10 Event Control - CP290 Point & Click      Version 0.95
          Interface Program to manage Event Data.      Beta Testing
          Includes Sunrise/Sunset Time Offsets.
          Expected Release Date: Sept '93

X10UC     X10 Ultimate Control                         Development
          A program which combines the features of
          X10DC & X10EC and provides multiple modeless,
          screen windows.

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Please register this software if you use it regularly; by registering
you reinforce my commitment to ongoing development.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

19. RELEASE HISTORY ù X10DC Shareware/Registered Version
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 Date      Version     Changes
------   ----------   ----------------------------------------------
JUL'93    1.30        þENABLED SEND Command under MODE 3 in Unregistered
                       version for 1st 8 Devices in X10.DAT File
                      þENABLED ALL Clock Sychronization options in
                       Unregistered version
                      þENABLED Change Base HouseCode with Event
                       Preservation in Unregistered version
                      þENABLED Screen Colours dialogue in Unregistered
                       version
                      þTest menu item added to Menu Bar;
                       ù CP290 Self Test disassociated with Debug Mode
                         and Self Test button removed from Screen
                         Header; Self-Test feature now a sub-menu
                         item under Test.
                       ù Signal Test Generator feature added; send
                         ON/OFF commands repeatedly to a fixed/variable
                         House Code/Unit Code address.  Unregistered
                         version supports the fixed option only.
                      þHelp Sub-system added; contains additional
                       X10 background information as well as extracts
                       from the documentation file.
                      þ/NH command line argument added to optionally
                       not load the help system for faster program
                       load times.
                      þ/NS command line argument added to disable
                       sounds generated during the Signal Test.
                      þSounds Toggle added as a sub-menu item under
                       Options.
                      þINI Overwrite warning now uses the WARNING
                       screen title colour(*5)
                      þ'Save Options' displays a message box whenever
                       INI options are saved(*5)
                      þThe access key for the 'Exit' option under the
                       'File' menu changed from 'E' to 'x'.
                      þ[Esc] key will now back out any screen
                       colour changes while in the Screen Colours
                       dialogue
                      þ[Esc] key will now skip the wait while
                       SYNC'ing the CP290 clock based on the PC
                       Clock
MAR'93    1.20        þMerged Shareware & Registered Versions;
                       Registered Version features are disabled in
                       the Unregistered version, specifically:
                         ù Complete Mode 3 Support (X10.DAT File)
                         ù Complete Screen Color Customization
                           Dialogue
                         ù INI File Support to save/modify
                           Program settings/colors
                         ù Preserve/Restore Event Data when
                           Base House Code changed
                         ù PC ¯ CP290 Clock Synchronization
                         ù CP290 ¯ PC Clock Synchronization
                      þENABLED Self Test EVENT Preservation
                       in Unregistered version
                      þENABLED MODE 3 Switch & X10.DAT File Load
                       in Unregistered version (SEND-Disabled)
                      þENABLED some Clock Functions, & Base House
                       Code Setting in Unregistered Version
                      þCP290 Self Test changed to reset interface
                       upon completion (The self test overwrites
                       the Event Data and this data may cause
                       problems with some programs)
                      þAdded /BW command line argument to startup
                       with monochrome color settings
                      þAdded 'Refresh' menu item to refresh on-screen
                       Clock Displays
                      þError handling improved
                      þRetry logic added for all CP290 communications
                       with automatic wait time adjustment (if program
                       times out waiting for a response, it will
                       increase the wait time if the command is retryed)
                      þCommand History caption now indicates which
                       entry is highlighted (ie. entry x of n)

MAR'93    1.10        þMENU BAR Added - CommPort,Mode, & Debug can
                       now be changed using the Options Menu
                      þMode Indicator added to Screen Header
                      þMinor Screen Colour modifications

FEB'93    1.00        þMode Switch Command Button Added (Alt-M)
                      þDebug Command Button TAB Stop disabled-keyboard
                       users must use ALT-T
                      þCIS Software Registration # added to ABOUT

FEB'93    1.00 á.02   þOperating Mode 2 Added (FIRST PUBLIC RELEASE)
                      þOperating Mode 3 Added to Registered Version
                      þClock/Base House Code manipulation added to
                       Registered Version

JAN'93    1.00 á.01   þDebug Mode Added

JAN'93    1.00 á.00   þInitial Beta (not publicly released)

ÄÄÄÄÄÄ
 (*5) Applicable to REGISTERED VERSION Only.