±±±±Ü ±±±±Ü   ±±±±±±±±Ü
                               ±±Ûß  ±±Ûß   ±±Ûßßß±±Û
                               ±±Û   ±±Û    ±±Û    ßß
                               ±±±±±±±±Û    ±±±±±±±±Ü
                               ±±Ûßßß±±Û      ßßßß±±Û
                               ±±Û   ±±Û    ±±Ü   ±±Û
                              ±±±±Û ±±±±Û   ±±±±±±±±Û
                               ßßßß  ßßßß    ßßßßßßßß



                                  H S / L i n k 

                                 High Speed Link 

                              File Transfer Protocol


                                   Version 1.21
                                  Revised 5/06/93


        ___________________________________________________________________

         Please refer to HSLINK.NEW for details of recent program changes!
        ___________________________________________________________________

     HS/Link  is a  high speed  file transfer  protocol with  full streaming,
     simultaneous  send, receive and CHAT, and advanced Full-Streaming-Error-
     Correction(tm).  Each side of  the link is allowed to provide  a list of
     files to be  sent.  Files will travel simultaneously  in BOTH directions
     until both sides of the link are satisfied.

     HS/Link is not just  another bi-directional protocol, it is  also a very
     fast protocol  for normal downloading and  uploading, incorporating some
     new ideas  (such as  Full-Streaming-Error-Correction(tm),  Dynamic-Code-
     Substitution  and Minimal-Blocks(tm)) to make things happen a bit faster
     and with greater reliability.


        ___________________________________________________________________

                                     Copyright
        ___________________________________________________________________

     All Tool  Shop(tm) products are  trademarks or registered  trademarks of
     Samuel H. Smith  DBA The Tool Shop.   Other brand and product  names are
     trademarks or registered trademarks of their respective holders.

     Copyright (C) 1991, 1992, 1993 Samuel H. Smith
     All rights reserved.


     HS/Link 1.21                      - 1 -                  Reference Guide





        ___________________________________________________________________

                                 Table of Contents
        ___________________________________________________________________

     Introduction  . . . . . . . . . . . . . . . . . . . . . . . . . . .    3

     Quick Tour  . . . . . . . . . . . . . . . . . . . . . . . . . . . .    5

     Command Line Format . . . . . . . . . . . . . . . . . . . . . . . .    7

     HSCONFIG: The HS/Link Configuration Manager . . . . . . . . . . . .    9

     HSCONFIG: Basic Settings  . . . . . . . . . . . . . . . . . . . . .   10

     HSCONFIG: Advanced COM settings . . . . . . . . . . . . . . . . . .   12

     HSCONFIG: Advanced Optional Features  . . . . . . . . . . . . . . .   14

     HSCONFIG: Advanced Optional Features 2  . . . . . . . . . . . . . .   16

     HSCONFIG: Screen Settings . . . . . . . . . . . . . . . . . . . . .   18

     Advanced Command Line Options . . . . . . . . . . . . . . . . . . .   20

     Command Line Examples . . . . . . . . . . . . . . . . . . . . . . .   21

     Calling HS/Link from COMM programs  . . . . . . . . . . . . . . . .   22

     Calling HS/Link from BBS programs . . . . . . . . . . . . . . . . .   22

     CHAT During File Transfer . . . . . . . . . . . . . . . . . . . . .   24

     Flow Control  . . . . . . . . . . . . . . . . . . . . . . . . . . .   25

     Full Streaming Data Transmission  . . . . . . . . . . . . . . . . .   26

     Full Streaming Error Recovery . . . . . . . . . . . . . . . . . . .   27

     Transmission of Minimal Blocks  . . . . . . . . . . . . . . . . . .   27

     Dynamic Code Substitution . . . . . . . . . . . . . . . . . . . . .   28

     Auto Downloading  . . . . . . . . . . . . . . . . . . . . . . . . .   29

     DSZLOG Statistic Logging  . . . . . . . . . . . . . . . . . . . . .   30

     HS/Link Messages  . . . . . . . . . . . . . . . . . . . . . . . . .   31

     Support . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .   37

     Index . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .   38


     HS/Link 1.21                      - 2 -                  Reference Guide





        ___________________________________________________________________

                                   Introduction
        ___________________________________________________________________

     What is a file transfer protocol?

     A file transfer protocol is a means of transferring information from one
     computer  to another.  The protocol has the responsibility of protecting
     against errors  in transit, and  taking measures to  correct any  errors
     that are detected.  The design and implementation of a protocol can make
     the difference between slow and  unreliable communication, and fast  and
     trouble free communication.

     Not all protocols  are created equal.   With today's high speed  modems,
     packet  switched  networks  (such as  PC  Pursuit),  and  expensive long
     distance charges,  users demand more  than ever that  files get  through
     quickly and without corruption.

     The  HS/Link protocol  is  the result  of  many years  of  communication
     experience,  and uses some  new and  very solid technology to  see to it
     that  you can  easily move files  as quickly  as possible,  and with the
     least amount of hassle.

     The HSLINK  program can be used  from the DOS  command line, from  BATCH
     files, or  as an "external protocol" from most  modern COMM programs and
     BBS  programs.  If  your favorite  BBS does not yet  support the HS/Link
     protocol, please ask your SYSOP to install it.


     Recent advances in high speed modem technology have   =================
     made it possible to simultaneously transfer data at   === Quick Tip ===
     high speeds in both directions.   This standardized   =================
     technology is  called "V.32"  or "V.32bis",  and is      Bi-directional
     available in many new modems.  Until HS/Link, these       features that
     advanced  modems were  left half  idle, due  to the     really work... 
     single-direction  nature  of  other  file  transfer         HS/Link can
     protocols.    The  bi-directional  capabilities  of      simultaneously
     HS/Link  take  full  advantage  of   these  modems,    send and receive
     cutting  online  time as  much  as  50% when  equal              files!
     amounts of data are transmitted and received.

     HS/Link also takes  full advantage of 1200 and 2400  baud modems, giving
     you very nearly the best thru-put such modems are capable of.










     HS/Link 1.21                      - 3 -                  Reference Guide





        ___________________________________________________________________

                              Summary of Key Features
        ___________________________________________________________________

     ù Speed.
          HS/Link operates at, or  very near peak efficiency,  often reaching
          98%  or more  with  pre-compressed files  and  non-buffered modems.
          Even higher speeds  are possible with buffered or  error correcting
          modems.  A number of features, such as fast  32 bit CRC protection,
          Full-Streaming-Error-Recovery     and    Dynamic-Code-Substitution,
          combine to give maximum performance and security.

     ù Simple interface for beginners.
          In many cases,  HS/Link requires only the  COM port number and  the
          filename to be transmitted.   Configuration files are not required.
          The  program is easily installed in most COMM programs that support
          external protocols.  The HSLINK program has multiple help  screens,
          providing  a quick reference to the basic and advanced command line
          options, including examples of how the program is used.

     ù Batch file transfers.
          The protocol can handle any  size batch of files, and can take file
          specifications from either the command line or from a listing file.

     ù Bi-directional options that really work.
          The  program can simultaneously  upload and download  with a single
          host  request.   What's even  better is  how easy  it is  to use...
          instead of a complex setup all you do is:

          1)   Tell the BBS the names of the files you  want to download, and
               then
          2)   Press  PGUP (or  whatever  your COMM  program  uses  to UPLOAD
               files) and then tell your COMM program which files to upload

          By virtue of the  BBS being told that it is  sending files and your
          COMM program telling HS/Link that it too is sending files, you then
          have  a bi-directional transfer.   There's nothing else  to set up.
          You use the familiar BBS interface to request files to download and
          your  COMM program's familiar  interface to tell it  which files to
          upload.  It couldn't get easier!

     ù Aborted file crash recovery.
          When desired, HS/Link can resume an aborted transfer, verifying all
          existing data blocks to insure the resumed file completely  matches
          the file being transmitted.   This function can also  update a file
          that has only a small number of changed, added, or deleted blocks.







     HS/Link 1.21                      - 4 -                  Reference Guide





        ___________________________________________________________________

                                    Quick Tour
        ___________________________________________________________________

     If  you are  eager to  see HS/Link  in action,  follow the  simple steps
     below.   The following pages will tell  you how to install and configure
     the HS/Link program for optimal ease of use and performance. 

     1.  Unpack the HSLINK  program into a working  directory or your choice.
     All you really need is HSLINK.EXE for now.

     2.  Use  the TERMINAL  program of  your  choice to  call up  a  BBS that
     supports the HS/Link protocol.  If you don't know of a BBS in your area,
     you can  always call  the Tool  Shop BBS  at (818)  891-1344 to  see how
     HS/Link works.

     3.  When online  with  your  BBS, select  a  DOWNLOAD  using the  HSLINK
     protocol.  

     4.  When the  BBS is  ready for  you to  begin, press  the SHELL  TO DOS
     command in your  terminal program.   In many terminal programs,  this is
     the ALT-J command.  Later  you will be given instructions to tie HS/Link
     into  the  DOWNLOAD command,  but for  now  we are  going to  run HSLINK
     manually so you can see it in action right away.

     5. CD into the HSLINK working directory you set up in step 1.

     6. If your modem is on COM1, type the command
               HSLINK -P1
     If your modem is on COM2, instead use the command
               HSLINK -P2

     You should  now  see HS/Link  in action.    If your  copy of  HSLINK  is
     registered, you can press the ENTER key to begin a CHAT session with the
     person  running the BBS.   If  you aren't registered yet,  you can still
     CHAT, but the BBS operator has to start the CHAT for you.

     In  this sample session  you aren't doing a  bidirectional transfer, but
     you  to do  so  all  you need  to  do is  add  the outgoing  file  names
     (including drive and directory) to the end of the command line above.

     7. When HSLINK finishes, type the command
               EXIT
     to return to your TERMINAL program to continue your BBS session.









     HS/Link 1.21                      - 5 -                  Reference Guide





        ___________________________________________________________________

                            Full Screen Status Display
        ___________________________________________________________________

     When HS/Link  is operating, it  produces a full  screen status  display,
     divided into five windows.  For example:
  ÕÍÍÍÍÍÍÍÍÍÍ HS/Link v1.21 (5/06/93) Copyright 1993 Samuel H. Smith ÍÍÍÍÍÍÍÍÍÍ¸
  ³ [UNREGISTERED] Courtesy of The Tool Shop BBS (818) 891-1344.               ³
  ³ Command line: -@tolap.cfg test\*.* -s2048 -w12 -a                          ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  ÕÍÍÍÍÍÍÍÍÍ 5 InComing Files, 710782 bytes ÍÍÍÍÍÍÍÍÍ¸ ÕÍÍÍÍÍÍ Settings ÍÍÍÍÍÍÍ¸
  ³ \TMP\VIROSCAN.ZIP (79 blocks, 161003 bytes)      ³ ³  COM2 open at: 115200 ³
  ³ File received OK, 2930 cps, 58 seconds.          ³ ³Remote Serial#: 00001  ³
  ³ \TMP\PM.ZIP (37 blocks, 73745 bytes)             ³ ³Remote Version: 1.10   ³
  ³ Block 14 (28672 bytes) 2622 cps                  ³ ³        Window: NONE   ³
  ³ ÛÛÛÛÛÛÛÛÛÛÛÛÛ°°°°°°°°°°°°°°°°°°°°°° 18 seconds   ³ ³    Block size: 2048   ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³      XON/XOFF: ON     ³
  ÕÍÍÍÍÍÍÍÍ 9 OutGoing Files, 2297792 bytes ÍÍÍÍÍÍÍÍÍ¸ ³ CTS handshake: OFF    ³
  ³ TEST\PHASE1.EXE (179 blocks, 365810 bytes)       ³ ³ RTS handshake: OFF    ³
  ³ File sent OK, 5907 cps, 01:01 minutes.           ³ ³Slow handshake: ON     ³
  ³ TEST\PHASE2.EXE (204 blocks, 416884 bytes)       ³ ³        Resume: OFF    ³
  ³ Block 20 (40960 bytes/w:20) 5570 cps             ³ ³  Keep partial: ON     ³
  ³ ÛÛÛ°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° 01:08 minutes³ ³     Overwrite: ON     ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ÀÄ ^X^X^X^X to abort! ÄÄÙ
  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Batch Status ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  ³ Total 2047451 bytes (of 3008574) in 04:00 minutes, thruput 8509 cps.       ³
  ³ ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ°°°°°°°°°°°°°°°°° 01:53 minutes remaining³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ PLEASE REGISTER HS/LINK! ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     The  first window  contains  the program  identification  and copyright.
     When you  register your copy of  HSLINK, this window will  also show the
     registered serial number.  Some warning messages may also appear in this
     window.

     The "Settings" window shows a summary of the various parameters that can
     be altered with  command line options.   This display space is  replaced
     with the InComing Chat and OutGoing Chat windows during CHAT operation.

     The "InComing  Files" window shows  the status of  files being  received
     from the remote system.

     The  "OutGoing Files" window shows the status of files being transmitted
     to the remote system.

     The  "Batch  Status"  window  summarizes  overall session  progress  and
     estimates the time remaining for the selected files.

     To  stop display bleedthrough  under DesqView or DoubleDOS,  use the -NV
     option to disable  direct video writing.  The result  will be a slightly
     slower display, but it will not bleed from one partition to another.

     If desired, the full screen status display can be turned off. 

     HS/Link 1.21                      - 6 -                  Reference Guide





        ___________________________________________________________________

                                Command Line Format
        ___________________________________________________________________

     To  run the HSLINK program,  a command line must be  given.  The command
     line has the following format:

     HSLINK [options] [SENDFILE] [@DRIVE:\PATH\FILELIST]

     SENDFILE  Indicates  a  list  of  files  to  be  transmitted  to  remote
               computer.   The list  may include the  DOS wildcard characters
               '?' and '*'.  Specify ONLY   files to be transmitted; received
               file names are determined automatically.

     @FILELIST Transmit  list  of  files  contained  in  FILELIST  to  remote
               computer.  This is used when  you want to make a long list  of
               files  in advance,  then  transmit  them  all  with  a  single
               command.   It is  also used  by BBS  programs to  produce long
               batches of downloads.

     ù    Anything shown in brackets "[]" is optional and may  not need to be
          specified for proper operation of HS/Link.

     ù    The HSLINK command line is NOT  case sensitive, and will work  when
          typed in upper, lower or mixed case.

     ù    Please make sure that HSLINK.EXE is in a search PATH directory.


        ___________________________________________________________________

                            Basic Command Line Options
        ___________________________________________________________________

     The most important command line  options are -P (set COM port),  -U (set
     download file directory), and -HS (enable slow handshake).

     -Pport    This sets which COM port you are using.  
               Example:  -P2

     -Udir     This  sets  the destination  directory  for downloaded  files.
               Without this option,  all download files  are placed into  the
               current directory.
               Example:  -Uc:\bbsfiles

     -HS       Handshake Slow (send  XOFF and/or lower RTS  during disk I/O).
               This  option may  be required  if your  computer is  unable to
               simultaneously access the disk  and the COM port.  If  you see
               frequent CRC  error messages, even  on clean phone  lines, you
               probably need to include -HS in your command line.

     To abort an HS/Link transfer, press Control-X four or more times.

     HS/Link 1.21                      - 7 -                  Reference Guide





        ___________________________________________________________________

                                Configuration Files
        ___________________________________________________________________

     Because  of the  large number  of  possible command   =================
     line options, you can store frequently used command   === Quick Tip ===
     options in a  configuration file.   This eliminates   =================
     the  need  to  repeatedly  type  the options  at  a    HS/Link does NOT
     command  line.   If  you  are  calling HSLINK  from             require
     multiple   batch   files,    you   can   also   use       configuration
     configuration files to store "common" options, that              files.
     can be changed in  one place rather than separately
     in the various batch files.

     HSLINK  will first search the current directory for   =================
     the HSLINK.CFG  file.  If  not found, it  will then   === Quick Tip ===
     search  the directory  where HSLINK.EXE  is stored,   =================
     followed  by  all  directories  in  the   DOS  PATH   For best results,
     setting. If the HSLINK.CFG file is found, each file    add your HS/Link
     line is loaded as a command line option.                or COMM program
                                                           directory to your
                                                             PATH statement.
     If you want to use an alternate configuration file,
     use  the -@fname  command line  option,  which will
     cause 'fname' to be loaded.  For example:
          HSLINK -@C:\WORK\TOLAP.CFG
     will cause HSLINK to use C:\WORK\TOLAP.CFG as the configuration file.

     If -@fname is not the first command  line option, the default HSLINK.CFG
     file  will be searched for and loaded before the specified configuration
     file.

     Use  -@ (without  a filename)  to prevent  HSLINK  from searching  for a
     configuration  file, slightly speeding operation on  systems that have a
     long search PATH setting in effect.



     To aid in creation and alteration  of configuration   =================
     files, the HS/Link  Configuration Manager  program,   === Quick Tip ===
     HSCONFIG, was written.                                =================
                                                             Use HSCONFIG to
                                                             create and edit
                                                              HS/Link option
                                                             (configuration)
                                                                      files.







     HS/Link 1.21                      - 8 -                  Reference Guide





        ___________________________________________________________________

                    HSCONFIG: The HS/Link Configuration Manager
        ___________________________________________________________________

     HSLINK includes the HS/Link Configuration Manager program, HSCONFIG.EXE.
     With  this  program you  can  easily manipulate  most of  HS/Link's many
     options.

     The opening display for HSCONFIG looks like this:

  C:\HSL >hsconfig
  HS/Link Configuration Manager 1.2 (C)1993 Samuel H. Smith; ALL RIGHTS RESERVED

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ New Configuration ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³                                                          ³
         ³ The specified configuration file cannot be located.      ³
         ³                                                          ³
         ³ This probably indicates that you are creating a new      ³
         ³ configuration for HS/Link.  All options will be set      ³
         ³ to default values.                                       ³
         ³                                                          ³
         ³ Alternate configuration files can be specified on        ³
         ³ the command line to HSCONFIG.  The default configuration ³
         ³ file is HSLINK.CFG, and it may be located either in the  ³
         ³ current directory, or in any PATH directory.             ³
         ³                                                          ³
         ³ Press <ENTER> or <ESC> to continue.                      ³
         ³                                                          ³
         ³  Index  <ESC>                                            ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

  Can't find: C:\UTIL\HSLINK.CFG


     HSCONFIG  can be used to edit any configuration file, but the default is
     to edit HSLINK.CFG  in the current directory,  or the same directory  in
     which HSLINK.EXE is found.  If you want to edit some other configuration
     file, you must specify the  filename on the HSCONFIG command line.   For
     example:
          HSCONFIG TOLAP.CFG

     will create or  edit TOLAP.CFG, which can later be used by HSLINK with a
     command line like this:
          HSLINK -@TOLAP.CFG

     When   no  configuration   filename  is   specified,  and   the  default
     configuration file  HSLINK.CFG cannot be located,  it will automatically
     be created in the  same directory that HSLINK.EXE  is found in.   If you
     wish to create the configuration file in a different directory, you must
     explicitly specify  the directory/filename  to be  used on  the HSCONFIG
     command line.


     HS/Link 1.21                      - 9 -                  Reference Guide





        ___________________________________________________________________

                             HSCONFIG: Basic Settings
        ___________________________________________________________________

     The primary  screen in HSCONFIG  is the "Basic  Settings" screen,  which
     controls the most  important settings for HS/Link operation.   The other
     screens contain  advanced settings that  need not be  changed until  you
     become more familiar with the program and begin to  explore the advanced
     capabilities.

   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ HS/Link: Basic Settings [Page 1 of 5] ÍÍÍÍÍÍÍÍÍÍÍÍÍÍOVRÍ¸
   ³                                                                          ³
   ³    These are the most important settings for proper HS/Link operation    ³
   ³                                                                          ³
   ³  COM port number (1-8) . . . . . . . . . . . 1                           ³
   ³                                                                          ³
   ³  Directory for downloaded files. . . . . . . __________________________  ³
   ³                                                                          ³
   ³  Use "SLOW HANDSHAKE" during disk I/O. . . . N                           ³
   ³                                                                          ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄ Help topic: Welcome! ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
              ³ Welcome to the HS/Link Configuration Manager.       ³
              ³ The easy way to handle HS/Link configuration files. ³
              ³                                                     ³
              ³ Use the     keys to select entries on this page.    ³
              ³ Use the PgUp/PgDn keys to change pages.             ³
              ³ Press ESC to save changes when you are finished.    ³
              ³                                                     ³
              ³ Use the F1 key to get HELP at any prompt.           ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

    PgDn [next page]     PgUp [prior page]             F1 [help]     ESC [exit]

     The HSCONFIG program contains context sensitive pop-up help for each and
     every  input prompt.  Simply  press the F1 key  to get an explanation of
     the current entry.  For example:

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ -U ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ -Udir  > Download directory.                                    ³
         ³                                                                 ³
         ³ This option controls the destination directory for downloaded   ³
         ³ files.  Without this option, all download files are placed into ³
         ³ the current directory.                                          ³
         ³                                                                 ³
         ³  Index  <ESC>                                                   ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     When in  the online help system,  press the SPACE and  BACKSPACE keys to
     select from the topics available at the bottom of  the window, and press
     ENTER to select a topic.  Press ESCAPE to return to the prior screen.

     HS/Link 1.21                     - 10 -                  Reference Guide





     This screen manipulates the following options:

     -Pport
          Use COM port 1-8 (default=1).   Standard COM port definitions:
               Channel   I/O Port  Interrupt
                COM1      0x3F8          4
                COM2      0x2F8          3
                COM3      0x3E8          4
                COM4      0x2E8          3
                COM5      undefined
                COM6      undefined
                COM7      0x2E8          5
                COM8      0x3E8          5
          Use -PB and -PI instead of -P to define a non-standard COM port.

     -Udir
          Destination   directory   for   received   files   (default=current
          directory)

     -HS
          Handshake Slow (send XOFF and/or lower RTS during disk I/O).
          The slow handshake  option is available for systems with  slow disk
          access.   Use this if  you get frequent  CRC errors  or COM overrun
          errors  on otherwise clean lines.  The slow handshake option causes
          XOFF to be sent and/or RTS to be lowered  during any disk activity.
          Even  when -HS is active, the HS/Link protocol should transfer data
          very nearly as fast as the slowest part of the link allows.



























     HS/Link 1.21                     - 11 -                  Reference Guide





        ___________________________________________________________________

                          HSCONFIG: Advanced COM settings
        ___________________________________________________________________

     The  "Advanced COM  Settings"  screen determines  the  settings  of many
     communications related  options.   See the following  section, "Advanced
     Options" for a description of each of these options.

   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍ HS/Link: Advanced COM Settings [Page 2 of 5] ÍÍÍÍÍÍÍÍÍÍOVRÍ¸
   ³                                                                          ³
   ³          These settings control advanced communication features          ³
   ³                                                                          ³
   ³  Non-Standard COM base (in HEX, 0 = standard COM port) . . . . . . 0000  ³
   ³                                                                          ³
   ³  Non-Standard COM IRQ (1-15, 0 = standard COM port). . . . . . . . 0_    ³
   ³                                                                          ³
   ³  COM port open speed (300-115200, 0 = automatic) . . . . . . . . . 0___  ³
   ³                                                                          ³
   ³  Effective modem-to-modem speed (0 = same as open speed) . . . . . 0___  ³
   ³                                                                          ³
   ³  Enable CTS hardware handshake . . . . . . . . . . . . . . . . . . Y     ³
   ³                                                                          ³
   ³  Enable RTS hardware handshake . . . . . . . . . . . . . . . . . . Y     ³
   ³                                                                          ³
   ³  Enable XON/XOFF software handshake. . . . . . . . . . . . . . . . Y     ³
   ³                                                                          ³
   ³  Enable Carrier Detect checking. . . . . . . . . . . . . . . . . . Y     ³
   ³                                                                          ³
   ³  Preserve original time/date stamp on received files . . . . . . . Y     ³
   ³                                                                          ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

    PgDn [next page]     PgUp [prior page]             F1 [help]     ESC [exit]


     This screen manipulates the following options:

     -PBbase
          Set  non-standard COM  port base  address.   Base addresses  may be
          specified in either decimal or hex.   Hex addresses must begin with
          $ or  0x.  For example,  -PB1000, -PB$3E8 and -PB0x3E8  all specify
          the same port base address.

     -PIirq
          Set  non-standard COM port IRQ level to  1-15.  This option must be
          used when  -PB is used.  IRQ  levels 8-15 are supported  only on AT
          class machines with cascaded interrupt controllers.

     -Bbaud
          COM  port opening baud rate 300-115200 (default is the current port
          OPEN speed).
          This option  controls  the speed  at which  the  COM port  will  be

     HS/Link 1.21                     - 12 -                  Reference Guide





          opened.                                          =================
                                                           === Quick Tip ===
          Normally, the COM port speed can be determined   =================
          from hardware and need not be specified.          Don't use the -B
                                                               option if you
     -Ebaud                                               don't need to!  In
          Effective modem-to-modem baud rate.             most cases HS/Link
          This is used  to estimate transfer  times, and          is able to
          is   included    in   the    DSZLOG    output.   automatically set
          (default=current -B setting)                       the proper port
                                                                      speed.
     -HC
          Disables CTS hardware handshake.
          CTS  transmitter  handshake  is  automatically  enabled,  but   may
          conflict with some  unusual modem cables or  serial ports.  If  the
          CTS signal is  not active when HSLINK loads, it  will automatically
          disable CTS  handshake for you.   Use the  -HC command to  manually
          disable CTS handshake.

     -HR
          Disables RTS hardware handshake.
          RTS receiver handshake  is used when  the slow-handshake option  is
          selected.  This form of  handshake causes the RTS line to the modem
          to be lowered  whenever the disk is  being accessed.   Some unusual
          modem or  cable arrangements may  not tolerate the  RTS line  being
          lowered.   In this  case, the RTS  handshake can  be disabled  with
          the -HR option.

     -HX
          Disable XON/XOFF handshake.
          XON/XOFF handshake is a software handshake scheme that  should work
          well on all combinations of modems and networks, and is enabled  by
          default.   If you prefer not to use XON/XOFF handshake, or you find
          that it is not required for error-free transfer, you can disable it
          with the -HX option.

          Note  that both  the sender  and  the receiver  must simultaneously
          disable XON/XOFF handshake, otherwise it will remain in effect.

     -C
          Disable  carrier detect  checking.   Use this option  when directly
          connecting two machines via a null modem cable.

     -NT
          Stamp current file time.   This option stamps the current time/date
          on  received   files,  instead  of  retaining   the  original  file
          time/date.







     HS/Link 1.21                     - 13 -                  Reference Guide





        ___________________________________________________________________

                      HSCONFIG: Advanced Optional Features 1
        ___________________________________________________________________

     The  "Advanced  Optional  Features  1"  screen  controls  many  advanced
     protocol  features.  See the following section, "Advanced Options" for a
     description of each of these options.

   ÕÍÍÍÍÍÍÍÍÍÍ HS/Link: Advanced Optional Features 1 [Page 3 of 5] ÍÍÍÍÍÍÍOVRÍ¸
   ³                                                                          ³
   ³             These settings control various optional features             ³
   ³                                                                          ³
   ³  Attempt to Resume aborted transfers . . . . . . . . . . . . . . . N     ³
   ³                                                                          ³
   ³  Keep partial files from aborted transfers . . . . . . . . . . . . N     ³
   ³                                                                          ³
   ³  Allow received files to overwrite/modify existing files . . . . . N     ³
   ³                                                                          ³
   ³  Enable file read/write buffering. . . . . . . . . . . . . . . . . Y     ³
   ³                                                                          ³
   ³  Enable "Dynamic-Code-Substitution" logic. . . . . . . . . . . . . Y     ³
   ³                                                                          ³
   ³  Size of transmitted data blocks (64-4096 bytes/block) . . . . . . 1024  ³
   ³                                                                          ³
   ³  Number of blocks in transit before ACK is required (0-1000) . . . 8___  ³
   ³                                                                          ³
   ³  Disable transmission of ACK for each block received . . . . . . . N     ³
   ³                                                                          ³
   ³  Force remote unit to use local option settings. . . . . . . . . . N     ³
   ³                                                                          ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

    PgDn [next page]     PgUp [prior page]             F1 [help]     ESC [exit]

     This screen manipulates the following options:

     -R
          Resume  aborted transfer.   The  receiver  and   =================
          transmitter  will  verify  the contents  of an   === Quick Tip ===
          existing file, and  will begin transmission at   =================
          the  first block  that does  not match.   This     Use -R -K -O if
          provides  a  reliable  means of  restarting an   you want Download
          aborted  transfer, or  of updating  a modified      Crash Recovery
          file.  You must also use -O to recover aborted
          downloads.

          Note  to BBS operators:  Crash recovery is enabled  by the caller's
          use of -R -K  -O options and should NOT be  directly enabled in the
          BBS command line or configuration file.

     -K
          Keep partial files from aborted transfers.

     HS/Link 1.21                     - 14 -                  Reference Guide





     -O
          Allow receive files to overwrite existing files.

     -NB
          Disable buffering of receive and transmit files.  The default is to
          divide approximately  24k of  memory between InComing  and OutGoing
          files.

     -NC
          Disable Dynamic-Code-Substitution logic.
          Certain  byte codes  cannot be  transmitted directly  over  the COM
          link. For instance, the codes for Control-X, Control-S and Control-
          Q must be  "escaped" to  prevent a  conflict with  flow or  program
          control.

          The HS/Link protocol uses a new Dynamic-Code-Substitution system to
          drastically reduce the number  protocol overhead and "escape" codes
          needed  to transmit certain  data streams.   Highly compressed data
          files  (such as ZIP  and GIF  files) benefit  the most,  since they
          often have many byte codes that cannot be transmitted directly over
          the COM link.

     -Ssize
          Sets transmit  block size 2-4096 (default=1024)  Larger block sizes
          may result in higher transfer speeds under clean line conditions.

     -Wwindow                                              =================
          Number  of blocks  allowed without  ACK 1-1000   === Quick Tip ===
          (default=8)                                      =================
          Use  -A  or -W0  to  establish  an  "infinite"    Use -W4 -S512 -!
          window (i.e. no ACK required at all).              with PC-Pursuit

          The "ACK window" is  the number of blocks that
          will be sent  to the modem before an  ACKnowledge code is required.
          If the specified number of blocks have been sent and no ACK has yet
          been received, output  will be suspended until the ACK  is received
          or  the link  times out.   This  provides a  form of  software flow
          control that  works  well when  parts  of the  link are  very  slow
          compared to other parts, such as when PC Pursuit is in use.

          The /w:XXX value displayed in the InComing Files window reports the
          actual  number  of  blocks  that  are being  transmitted  prior  to
          acknowledge.  Setting  the -W value higher than the  highest /w:XXX
          value observed will have no further effect on transfer thru-put.

     -A
          Disable  transmission  of ACK  codes  after each  block.   This may
          improve transfer speeds under some conditions. 

     -!
          Take priority.  Locally specified -A, -HX, -S, and -W settings will
          be used by the remote system.  The -N! option cancels the effect of
          the -! option.

     HS/Link 1.21                     - 15 -                  Reference Guide





        ___________________________________________________________________

                      HSCONFIG: Advanced Optional Features 2
        ___________________________________________________________________

     The  "Advanced  Optional  Features  2"  screen  controls  more  advanced
     protocol  features.  See the following section, "Advanced Options" for a
     description of each of these options.

   ÕÍÍÍÍÍÍÍÍÍÍ HS/Link: Advanced Optional Features 2 [Page 4 of 5] ÍÍÍÍÍÍÍOVRÍ¸
   ³                                                                          ³
   ³               These settings control more optional features              ³
   ³                                                                          ³
   ³  Idle method (0=none, 1=BIOS, 2=DesqView, 3=DDOS, 4=WIN/OS2) . . . 0     ³
   ³                                                                          ³
   ³  Enable "Minimal-Blocks" logic (requires MNP). . . . . . . . . . . N     ³
   ³                                                                          ³
   ³  Disable NS16550AN buffering logic . . . . . . . . . . . . . . . . N     ³
   ³                                                                          ³
   ³  NS16550 Fifo Threshold (1-15) . . . . . . . . . . . . . . . . . . 4__   ³
   ³                                                                          ³
   ³  DSZLOG status logging file. . . . . . . . . __________________________  ³
   ³                                                                          ³
   ³  Incoming file duplication check list. . . . U:\PCB\GEN\DLPATH.LST_____  ³
   ³                                                                          ³
   ³  Force CTS handshake even when CTS is initially missing. . . . . . N     ³
   ³                                                                          ³
   ³  Use Alternate XON/XOFF method during initial handshake. . . . . . Y     ³
   ³                                                                          ³
   ³  Maximum number of repeated errors before aborting transfer. . . . 20    ³
   ³                                                                          ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

    PgDn [next page]     PgUp [prior page]             F1 [help]     ESC [exit]


     This screen manipulates the following options:

     -Iidle
          This option controls  how idle time is given up  under multitasking
          environments.  The possible values are:
               -I0  Default, do not give up idle time
               -I1  Spend idle time checking keyboard status
               -I2  Give up idle time under DesqView
               -I3  Give up idle time under DoubleDOS
               -I4  Give up idle time under Windows/OS2/VCPI/DOS5
          Some network server software, such as LanTastic, performs best when
          the -I1 option is used.

     -NM
          Enable Minimal-Blocks  logic.  Use  with caution.   This option  is
          recommended for use only on error-corrected links, such as with MNP
          or V.42 connections.

     HS/Link 1.21                     - 16 -                  Reference Guide





     -N5
          This  option causes  HS/Link  to disable  NS16550  buffering logic.
          This  option may be  needed with some early  versions, or incorrect
          clone versions of  the NS16550 chip, which do not  properly perform
          buffering.

     -FTn
          Sets NS16550 FIFO Threshold.
          This option controls the number of characters that will be buffered
          by  the  NS16550 internal buffer before an interrupt  is generated.
          Higher FIFO  thresholds will produce fewer  interrupts and somewhat
          less  CPU loading,  but with  the risk  of  overrun errors.   Lower
          thresholds  will prevent  overrun errors  under  multi-taskers like
          Windows or Desqview.

     -LFlogfile
          Specify status log file.
          This option allows you to override the DSZLOG environment  variable
          to  specify the  file to  be  used for  status  logging. Omit  this
          option,  or leave blank to control this function through the DSZLOG
          environment variable.

     -NOdirlist
          Incoming file duplication checklist.

          This option allows you to check incoming files for duplication in a
          list of  directories.   This feature prevents  incoming files  from
          duplicating files in directories other than the current -U setting.

          The dirlist is a text file which contains one filename or directory
          specification  per line.    See MKDLIST  documentation  for special
          instructions to speed CD-ROM duplication checking.

          Note   that  this  option  is  effective  ONLY  if  the  -O  (allow
          overwrites) is NOT used.

     -FC
          Force CTS hardware handshake.
          This  option  prevents  HSLINK  from  automatically  disabling  CTS
          hardware handshake if CTS is not active initially.

     -NA
          This  option causes HS/Link  to use the old  XON/XOFF method rather
          than the new alternate method during the initial handshake with the
          remote.   This option  is needed only  if handshake fails  when the
          remote unit is  version 1.12  or earlier and  should not be  needed
          when communicating with newer versions.

     -NEn
          Controls the number of repeated errors needed to abort a transfer.




     HS/Link 1.21                     - 17 -                  Reference Guide





        ___________________________________________________________________

                             HSCONFIG: Screen Settings
        ___________________________________________________________________

     The "Screen  Settings" screen allows  you to control  the format of  the
     status  display screen, the colors to be  used, and to enable or disable
     direct-video screen updates.

   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ HS/Link: Screen Settings [Page 5 of 5] ÍÍÍÍÍÍÍÍÍÍÍÍÍOVRÍ¸
   ³                                                                        ³
   ³            These settings control the screen format and colors         ³
   ³                                                                        ³
   ³  Enable Full-Screen status display . . . . . . . . . . . . . . . . Y   ³
   ³  Enable direct video writing (turn off in DesqView/DoubleDOS/etc). Y   ³
   ³  Position of status display (0-2)  . . . . . . . . . . . . . . . . 2   ³
   ³  Color of BORDER in full screen mode . . . . . . . . . . . . . . . 7__ ³
   ³  Color of PROMPTS in full screen mode. . . . . . . . . . . . . . . 47_ ³
   ³  Color of WINDOW TITLE in full screen mode . . . . . . . . . . . . 79_ ³
   ³  Color of WINDOW CONTENTS in full screen mode. . . . . . . . . . . 31_ ³
   ³  Color of PROGRESS GRAPHS in full screen mode. . . . . . . . . . . 14_ ³
   ³                                                                        ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
       ÚÄÄ Color Table ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³   0   1   2   3   4   5   6   7   8   9  10  11  12  13  14  15  ³
       ³  16  17  18  19  20  21  22  23  24  25  26  27  28  29  30  31  ³
       ³  32  33  34  35  36  37  38  39  40  41  42  43  44  45  46  47  ³
       ³  48  49  50  51  52  53  54  55  56  57  58  59  60  61  62  63  ³
       ³  64  65  66  67  68  69  70  71  72  73  74  75  76  77  78  79  ³
       ³  80  81  82  83  84  85  86  87  88  89  90  91  92  93  94  95  ³
       ³  96  97  98  99 100 101 102 103 104 105 106 107 108 109 110 111  ³
       ³ 112 113 114 115 116 117 118 119 120 121 122 123 124 125 126 127  ³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
    PgDn [next page]     PgUp [prior page]             F1 [help]     ESC [exit]


     This screen manipulates the following options:

     -NF  Disable Full screen mode.  The standard status   =================
          display takes over the full screen (except the   === Quick Tip ===
          top 2  lines, which  may contain a  BBS status   =================
          line).                                              HS/Link's Full
                                                               Screen status
          This option  bypasses the full  screen display    display does not
          and causes a line-oriented output  to be used.   alter the first 2
          Use this option  if your environment's  screen  display lines. Use
          management  does  not   allow  a   full-screen   the -CP option to
          display.                                                change the
                                                            position of this
                                                                    display.




     HS/Link 1.21                     - 18 -                  Reference Guide





     -NV                                                   =================
          Disable direct Video for  DesqView, DoubleDOS,   === Quick Tip ===
          and etc.   Use  this option if  you experience   =================
          "bleeding"  of the  status  display  from  one     You may need to
          partition to another.                              use -NV to stop
                                                           display bleeding.
     -CPn
          Control  the position  of the  status display.
          Use  a setting of  -CP0 to move  the display UP so  that the bottom
          lines will be  untouched.  The default is -CP2,  which protects the
          top 2 lines of the original display.

     -CBcolor
          Defines the border color in full screen mode.

     -CMcolor
          Defines the main screen color in full screen mode.

     -CTcolor
          Defines the window title color in full screen mode.

     -CWcolor
          Defines the window contents color in full screen mode.

     -CGcolor
          Defines the file  and batch progress bargraph color in  full screen
          mode.



























     HS/Link 1.21                     - 19 -                  Reference Guide





        ___________________________________________________________________

                           Advanced Command Line Options
        ___________________________________________________________________

     The HS/Link  protocol program has  a number of  additional command  line
     options, most  of which  are rarely  needed, or  which are  provided for
     advanced users to obtain maximum performance and flexibility.

     -@
          When the -@  option is given as the FIRST  parameter on the command
          line,  it prevents  HSLINK from  performing the  normal search  for
          HSLINK.CFG,  possibly  speeding   load  times  and  preventing  the
          accidental loading  of a configuration  file meant for  a different
          application.

     -@fname
          Uses fname  as an alternate configuration  file.  Each  line in the
          specified  file  may contain  a  single command  line option.   The
          default is to search PATH directories for HSLINK.CFG.

     -N!
          Do  not force  remote to  use local  settings.   Will  override any
          previous  -! option in  either the command line  or a configuration
          file.

     -NG
          Do not allow  Control-G (BEEP) characters in CHAT mode.  This keeps
          remote callers from beeping your speaker during a file transfer.

     -NK
          Cancels the effect  of the -K option, if present,  to force partial
          files from aborted transfers to be deleted.

     -NU
          Block uploads.    This option  is used by BBS  programs that cannot
          (yet) cope with bi-directional uploads.  It is used in place of the
          -U option on  the 'download' command  line, and has  the effect  of
          blocking any simultaneous upload requests from a user.

     -T
          Activates  a  "mini  terminal"  mode  prior to  starting  the  file
          transfer.  If  used with the -C option, you can use HS/Link to type
          "AT" commands directly to your modem to dial out.










     HS/Link 1.21                     - 20 -                  Reference Guide





        ___________________________________________________________________

                               Command Line Examples
        ___________________________________________________________________

     HSLINK -?
          Display a summary of HS/Link command line formats.

     HSLINK -P1
          Download from  a  BBS using  HS/Link.   COM1 will  be  used at  the
          current  port speed.    Received files  will  go into  the  current
          directory.

     HSLINK -P2 -Uc:\bbsfiles -K
          Download  from  a BBS  using HS/Link.    COM2 will  be used  at the
          current  port speed.   Received files will go  into the c:\bbsfiles
          directory.  Partial files from aborted transfers will be kept.

     HSLINK -P1 -Uc:\bbsfiles -R -K -O
          Continue  an aborted download from a BBS  using HS/Link.  COM1 will
          be used at the current port speed.  Received files will go into the
          c:\bbsfiles directory.

     HSLINK -Uc:\bbsfiles c:\uploads\*.zip
          Download from  a  BBS using  HS/Link.   COM1 will  be  used at  the
          current  port speed.   Received files will go  into the c:\bbsfiles
          directory.  Simultaneously upload all *.ZIP files in the c:\uploads
          subdirectory.

     HSLINK file1.zip file2.zip file3.zip
          Upload to a BBS using  HS/Link.  COM1 will  be used at the  current
          port speed.  Simultaneously  downloads selected files from the  BBS
          into the current directory.

     HSLINK -b115200 -p2 -c -hs -hc -a file1.zip file2.zip
          Communicate  files with  a laptop  computer using  port COM2  and a
          three wire null modem cable.

     HSLINK -w4 -s512 -! -uc:\download
          Download files through PC-Pursuit using  a window of 4 blocks and a
          block size of  512 bytes.  This setting stops  most errors when PC-
          Pursuit is heavily loaded.












     HS/Link 1.21                     - 21 -                  Reference Guide





        ___________________________________________________________________

                        Calling HS/Link from COMM programs
        ___________________________________________________________________

     The  HS/Link  protocol  can  be easily  installed  in  most modern  COMM
     programs.  Specific  instructions have  been prepared  for many  popular
     COMM programs, and are available in separate files for download.

          Comm program             Instructions posted in

          BOYAN 5.0                HS-BOY50.ZIP
          GT POWER 15.50           HS-GT15.ZIP
          ProComm Plus             HS-PCPTD.ZIP
          ProComm Plus/Windows     HS-PROW.ZIP
          QMODEM 4.3               HS-QMOD.ZIP
          ROBO COMM 3.1            HS-RC31.ZIP
          TELEMATE 2.1             HS-TMATE.ZIP
          TELIX 3.1                HS-TELIX.ZIP

     Installation  instructions for new  COMM programs are  being written all
     the time, so  check with your local  bulletin board or on the  Tool Shop
     for instructions for additional communication programs.


        ___________________________________________________________________

                         Calling HS/Link from BBS programs
        ___________________________________________________________________

     The HS/Link protocol can easily be installed in most modern BBS programs
     as an external  protocol.  Specific instructions have been  prepared for
     many  popular  BBS programs,  and  are available  in separate  files for
     download.

          BBS program              Instructions in         =================
                                                           === Quick Tip ===
          GAP 5.1                  HS-GAP51.ZIP            =================
          MarkMail/GAP             HS-MKML.ZIP                Check The Tool
          PCBOARD 14.5a            HS-145A.ZIP              Shop BBS for the
          PROBOARD 1.17            HS-PB117.ZIP            latest version of
          PRODOOR 3.44             HS-PROD.ZIP             HS-INST.ZIP.  New
          RemoteAccess 1.11        HS-RA111.ZIP                 COMM and BBS
          RBBS 17.3C               HS-R173C.ZIP                 programs are
          Rybbs                    HS-RYBBS.ZIP             frequently added
          SuperBBS 1.15 G4         HS-S1154.ZIP            to the library of
          Searchlight BBS          HS-SLBBS.ZIP                      install
          Spitfire BBS v3.0        HS-SF30.ZIP                  instructions
          UltraBBS v2.08           HS-UB208.ZIP                   available.
          Virtual BBS v5.40        HS-VBB54.ZIP
          Waffle                   HS-WAF.ZIP
          Wildcat! TD v2.15        HS-WC215.ZIP
          WWIV v4.20               HS-WWIV.ZIP

     HS/Link 1.21                     - 22 -                  Reference Guide





        ___________________________________________________________________

                                 BBS Requirements
        ___________________________________________________________________

     HS/Link's  demands on  a bulletin  board program  are extremely  easy to
     fill.  The following is all that is necessary:

     1)   The  protocol  accepts  either  a  filename to   =================
          download  or  a  list  of  files of  the  form   === Quick Tip ===
          @DRIVE:\PATH\DOWNLIST.LST.   The protocol will   =================
          send  only the  specified files  if  filenames     Send file lists
          (without leading  @) are given, or  all of the      are text files
          files found in the file C:\BBS\DOWNLIST.LST if    that contain one
          the option @C:\BBS\DOWNLIST.LST is specified.    path/filename per
                                                                       line.

     2)   The  protocol will create  a DSZLOG compatible
          log file indicating the names  of all files transferred as  well as
          their status (refer  to the DSZ standard and the  "DSZLOG Statistic
          Logging" section for the specific contents of the file).


     3)   Any files  found in the DSZLOG  file which BBS   =================
          did not tell the  protocol to SEND are assumed   === Quick Tip ===
          to have instead been RECEIVED by the protocol.   =================
          The BBS should then check for the existence of    HS/Link does NOT
          such files and if found, ask for  descriptions   modify BBS upload
          and post them in the upload directory.           listings! The BBS
                                                                program must
                                                          detect uploads and
                                                            do it's own file
                                                                 management.




     If the BBS program is not yet able to cope with bi-   =================
     directional uploads, the -NU  option can be used on   === Quick Tip ===
     the 'download' command line to prevent  attempts to   =================
     perform a bi-directional upload.                       Use -NU to block
                                                          all bi-directional
                                                                    uploads.











     HS/Link 1.21                     - 23 -                  Reference Guide





        ___________________________________________________________________

                             CHAT During File Transfer
        ___________________________________________________________________

     While  you are waiting for files to transfer, you can also type messages
     to the remote operators screen and see what he types in return.  This is
     called "CHAT mode".  

     If your copy  of HSLINK is  registered, you can  press the ENTER  key to
     begin  a CHAT session  with the person running  the BBS.   If you aren't
     registered yet,  you can still CHAT,  but the BBS operator  has to start
     the CHAT for you.

     Once you activate CHAT, the "Settings" portion of the display is removed
     and replaced with two new windows:  "InComing Chat" and "OutGoing Chat".
     Anything you type will appear in the OutGoing Chat display, and anything
     the remote operator types will appear in your InComing Chat display.  

     Chat mode features automatic word-wrap and keyboard correction using the
     backspace key.  

     You  can  "page" the  remote  user  by  pressing  Control-G  repeatedly.
     Control-G is the "BELL" character, which causes HSLINK to BEEP.  You can
     use the -NG command line option to disable  this feature, keeping HSLINK
     silent.

     When you  are finished chatting, just  press the ESC key  to restore the
     Settings  display and  to  terminate  the chat  mode.    Chat mode  will
     automatically terminate if you type nothing for 30 seconds and all files
     are finished transferring.


        ___________________________________________________________________

                               Optimizing CHAT Mode
        ___________________________________________________________________

     The CHAT  mode display may appear  sluggish, or jerky.   This is because
     HSLINK gives priority to the  file transfer and transmits CHAT text only
     between whole blocks of the file.   This effect is made worse by the use
     of large block sizes, especially at low baud rates.

     If you want  to have snappier chat displays, at  the expense of slightly
     slower  file transfers,  try  reducing the  BLOCK  SIZE (-S  option)  or
     setting a smaller ACK WINDOW (-W option).  Try adding 
          -S256 -W4
     to your command line, for example.






     HS/Link 1.21                     - 24 -                  Reference Guide





        ___________________________________________________________________

                                   Flow Control
        ___________________________________________________________________

     Flow Control  is required when  the sending and  receiving computers  or
     modems  operate at  different speeds,  or when  computers are  unable to
     simultaneously access disk  drives and the COM port.   Flow Control is a
     software  and/or hardware means of slowing down  the faster parts of the
     connection to prevent overloading the slower parts of the system.

     HS/Link uses  both XON/XOFF (software) and  RTS/CTS (hardware) handshake
     when  communicating  with high  speed  modems  or slow  packet  switched
     networks.   The protocol also  uses a  window algorithm to  suspend data
     transmission if the receiver  does not eventually respond to transmitted
     data.

     XON/XOFF  handshake is a software handshake scheme that should work well
     on all combinations of modems  and networks, and is enabled  by default.
     If you prefer not to use  XON/XOFF handshake, or you find that it is not
     required  for error-free  transfer,  you can  disable  it with  the  -HX
     option.   Note that both the sender and the receiver must simultaneously
     disable XON/XOFF handshake, otherwise it will remain in effect.

     The slow  handshake option  (-HS) is  available for   =================
     systems with slow disk access.  Use this if you get   === Quick Tip ===
     frequent  CRC  errors  or  COM  overrun  errors  on   =================
     otherwise clean  lines.  The slow  handshake option      The -HS option
     causes XOFF  to be  sent and/or  RTS to  be lowered  stops most overrun
     during any disk activity.  Even when -HS is active,      and CRC errors
     the  HS/Link protocol  should  transfer  data  very   that occur during
     nearly as  fast as  the  slowest part  of the  link      or immediately
     allows.                                                  after disk I/O
                                                                takes place.

     CTS transmitter handshake is automatically enabled,
     but may conflict with some unusual modem cables or serial ports.  If the
     CTS  signal is  not  active when  HSLINK  loads, it  will  automatically
     disable  CTS handshake for you.  Use the -HC command to manually disable
     CTS handshake.

     RTS  receiver  handshake  is  used  when the  slow-handshake  option  is
     selected.  This form of handshake causes the RTS line to the modem to be
     lowered  whenever the  disk is  being accessed.   Some unusual  modem or
     cable arrangements may not tolerate the RTS line being lowered.  In this
     case, the RTS handshake can be disabled with the -HR option.

     If  you have frequent CRC errors or COM overrun errors, which persist in
     spite of the handshake-slow option (-HS), you should  consider upgrading
     your serial  port from  the usual  8250 to  a newer, buffered  NS16550AN
     chip.  The buffered chips are highly recommended if you are operating at
     high  baud  rates (>9600)  or  are  accessing  extended  memory  or  are
     multitasking.

     HS/Link 1.21                     - 25 -                  Reference Guide





     I have  also had  reports that use  of large numbers  of dos  BUFFERS in
     CONFIG.SYS can cause  overrun errors.  Try reducing the  BUFFERS setting
     to 10 or less, especially if you also use a DISK cache.

     Some  disk cache  programs  have also  been  reported to  cause  overrun
     errors.  Try turning the cache OFF before calling HSLINK, and turning it
     back ON again after the transfer is completed.



        ___________________________________________________________________

                               Buffered ASYNC chips
        ___________________________________________________________________


     The National NS16550AN is  a pin compatible plug in   =================
     replacement for  8250 and  16450 serial chips.   It   === Quick Tip ===
     contains  hardware   buffering  to   allow   faster   =================
     operation  in systems  with high  interrupt service  The NS16550AN chip
     latency.                                             stops most overrun
                                                              and CRC errors
     If  you  have  an  NS16550AN  buffered  UART  chip,    encountered with
     HS/Link  will  automatically  enable  buffering for    COM port opening
     better  performance  with  high  speed  modems  and  speeds of 9600 and
     multi-tasking environments.                                     higher.

     The  -N5  option  may  be  needed with  some  early
     versions, or incorrect clone versions  of the NS16550 chip, which do not
     properly perform buffering.



        ___________________________________________________________________

                         Full Streaming Data Transmission
        ___________________________________________________________________

     The  HS/Link protocol  allows multiple  data  blocks to  be  transmitted
     before an acknowledgement  is required by use of block  numbers combined
     with a window algorithm.

     The  protocol  also  allows acknowledgements  to be   =================
     combined   with  data   flowing  in   the  opposite   === Quick Tip ===
     direction,  making  it  possible  to  achieve  full   =================
     streaming  simultaneously in both directions over a    The HST modem is
     full duplex communication link.                         not well suited
                                                          for bi-directional
     Even   though  the  transmitters  operate  in  full  transfers.  Switch
     streaming  mode,   the  receivers   normally   will   to V.32 modes, if
     periodically  acknowledge   that  data   is   being      available, for
     received.    This  acknowledgement can  be disabled    higher thru-put.
     with the -A option.

     HS/Link 1.21                     - 26 -                  Reference Guide





     Recent advances in high speed  modem technology have made it possible to
     simultaneously  transfer data at  high speeds in both  directions.  This
     standardized technology is called "V.32" or "V.32bis", and are available
     in many  new modems.   The bi-directional capabilities  of HS/Link  take
     full advantage of these modems,  cutting online time as much as 50% when
     equal amounts of data are transmitted and received.

     Some  older high speed modems, such  as the HST and   =================
     Hayes-V,  do not  implement  V.32 and  are  able to   === Quick Tip ===
     transfer quickly in only  one direction, while  the   =================
     other direction  is relatively slow.   HS/Link will     The "Ping Pong"
     still  perform well as a  single direction protocol    effect slows bi-
     with these modems, but bi-directional thru-put will         directional
     be low due  to the "ping pong" effect of  the modem  transfers on older
     switching the high speed channel back and forth.      9600 baud modems.



        ___________________________________________________________________

                           Full Streaming Error Recovery
        ___________________________________________________________________

     The  HS/Link  protocol  has  the unique  ability  to  recover from  many
     transmission errors without breaking out of full streaming mode.

     This  is important with buffered modems or packet switched networks with
     long turnaround times.

     Conventional  protocols,  such  as  Zmodem,  simply   =================
     reposition   the   transmitter   after   an  error,   === Quick Tip ===
     requiring  a   re-transmission  of  not   only  the   =================
     erroneous data, but also  the entire stream of data    Error correction
     that was  in transit  at  the time  the  error  was    cannot stop flow
     detected.                                              control failure-
                                                             related errors.
     The HS protocol can  correct bad blocks without re-        See the Flow
     transmitting intermixed good  blocks, resulting  in  Control section if
     excellent transfer speeds under moderate line noise            you have
     conditions.                                          persistent errors.



        ___________________________________________________________________

                          Transmission of Minimal Blocks
        ___________________________________________________________________

     The  HS/Link  protocol  includes a  Minimal Blocks  feature,  which when
     activated, causes the protocol  to strip away repeated information  from
     the  protocol frames and transmit only the minimal amount of information
     required for data flow.


     HS/Link 1.21                     - 27 -                  Reference Guide





     This feature results  in a savings  of over 50%  of   =================
     the  normal protocol  overhead  characters  in each   === Quick Tip ===
     block of data, while retaining full data integrity.   =================
     All data and control  blocks are fully protected by     Enable Minimal-
     a 32 bit CRC  calculation, even when Minimal Blocks     Blocks with the
     is in effect.                                        -NM option only if
                                                           you are operating
     The final block  in a file rarely ends on  an exact  with an error free
     transfer  block  boundary.    The  HS/Link protocol               link.
     automatically shortens the final block, eliminating
     extraneous data transmission at the end of file.



        ___________________________________________________________________

                             Dynamic Code Substitution
        ___________________________________________________________________

     Certain byte  codes cannot be  transmitted directly over  the COM  link.
     For instance, the  codes for Control-X, Control-S and Control-Q  must be
     "escaped" to prevent a conflict with flow or program control.

     The  HS/Link protocol  uses a  new Dynamic  Code Substitution  system to
     drastically reduce number protocol overhead and "escape" codes needed to
     transmit certain data streams.

     Highly compressed  data files (such  as ZIP and  GIF files) benefit  the
     most, since they  often have many byte codes  that cannot be transmitted
     directly over the COM link.

     The Dynamic Code Substitution feature can be disabled, if you wish, with
     the -NC option.



        ___________________________________________________________________

                               Network Compatibility
        ___________________________________________________________________

     All  file processing  is fully network  and "share"   =================
     compatible.    HSLINK can  be  easily  installed in   === Quick Tip ===
     multi-user or networked computers.  This works with   =================
     DOS version 3.0 and later.                                      HS/Link
                                                               automatically
     When  transmitting a  file, the  file is  opened in        enables file
     "allow read, deny none" mode.                        sharing in network
                                                               environments.
     If  a  file  sharing  violation  is  detected  when
     opening a  file, control is passed  to the system's
     current  "critical  error"  handler.   To  automate  recovery  from file
     sharing  violations,  you  can  install  my FATAL14.ZIP  program,  which

     HS/Link 1.21                     - 28 -                  Reference Guide





     automatically retrys  after sharing violations, and keeps a detailed log
     of all critical errors in a system.

     Files transmitted  or received with HS/Link retain  their original exact
     size and time/date stamp.   No extra data is  added beyond EOF, as  with
     older  protocols.   The current  date/time will  be stamped  on incoming
     files  if the  -NT  option  is used.    Otherwise,  the original  file's
     time/date stamp will be retained.

     When run under  DOS 2.x, HSLINK automatically reverts to  non-share file
     modes.



        ___________________________________________________________________

                                 Auto Downloading
        ___________________________________________________________________

     It  is  possible  for  some  terminal  programs  to   =================
     support  HS/Link  auto  downloading  by   means  of   === Quick Tip ===
     "scripts"   which  wait  for  the  HS/Link  "ready"   =================
     packet, and  then shell out to  the HSLINK receiver  With HS/Link Auto-
     protocol.                                            Download you don't
                                                             have to hit any
     This capability is currently active when HS/Link is  additional keys to
     installed  in  Telix  1.2,  Telemate,  Qmodem  Pro,  execute the HSLINK
     {COMMO}, BOYAN 5.0, any may be available soon under             driver.
     many  other  terminal  programs as  the  respective
     authors  add the  capability to  recognize external
     protocol signon signatures.

     The  HS/Link  "ready" packet  is  repeated at  10 second  intervals when
     waiting for  the  HSLINK receiver  to be  started.   The  format of  the
     "ready" packet is:
          "HS*" ^B 
     or in hex,
          0x48 0x53 0x2a 0x02

     When this sequence of characters is received during a terminal 
     session, the HSLINK protocol should be executed.

          NOTE:  To  perform   a  bi-directional   transfer  with   Auto
          Downloading  active, you simply omit the final "CR" you key to
          the BBS  and instead allow HSLINK  to send then  when you have
          finished specifying  outgoing file names.   Otherwise the auto
          download will take  control before you have a chance  to enter
          outgoing (upload) file names into your comm program.






     HS/Link 1.21                     - 29 -                  Reference Guide





        ___________________________________________________________________

                             DSZLOG Statistic Logging
        ___________________________________________________________________

     When you define the environment variable DSZLOG, the HSLINK program will
     enable transfer  logging to  the specified filename.   The log  file can
     also be set with the -FL option.  For example, the AUTOEXEC statement:
          SET DSZLOG=C:\LOGS\LOG.OUT
     will cause  HSLINK to log  files transmitted to  C:\LOGS\LOG.OUT.   This
     form of logging  provides compatibility with programs  that are designed
     to operate with DSZ or other DSZLOG-type protocols.

     The  log  file  consists  of  a  single  line  of  text  for  each  file
     transferred.  Here are some sample log entries:

  h 227596 10100 bps 1138 cps   0 errors   112 2316 V:\UPLOAD\ZLABP_13.ZIP 0
  H 177901 10100 bps 1116 cps   1 errors     0  749 U:\PLAY1\ECOMM22.ZIP 0
  h  16155 10100 bps 1061 cps   0 errors     4  795 W:\ULW\WINROACH.ZIP 0
  L 136991 10100 bps    0 cps   0 errors    55 1823 W:\ULW\WINDE223.ZIP 11
  E 152614 10100 bps    0 cps  14 errors    22   38 W:\ULW\CLPGR21C.ZIP 0 2

     Each line contains the following fields:

     Size Description

     1    "H"=file received from remote
          "h"=file sent to remote
          "E"=file receive was aborted
          "e"=file transmit was aborted
          "L"=lost carrier during file receive
          "l"=lost carrier during file transmit

     7    The length  of the file, in bytes.    If the  transfer was aborted,
          this  field will contain the number of bytes transferred before the
          transfer was aborted.
     6    The effective modem-to-modem connect speed.
     4    Literally " bps"
     5    The average transfer rate, in characters per second.
     4    Literally " cps"
     4    The total number of blocks which required retransmission during the
          transfer.
     7    Literally " errors"
     6    The number of flow control restrictions.
     5    The length of the last block transferred in the file.
     ?    The full pathname of the file which was transferred.
     ?    The Serial Number of the remote HSLINK, if registered.  
          Otherwise 0.






     HS/Link 1.21                     - 30 -                  Reference Guide





        ___________________________________________________________________

                                 HS/Link Messages
        ___________________________________________________________________

     Bad ____ CRC
          These messages  indicate that an  error was detected  in a  control
          message between the  sender and the receiver.  All  control packets
          are protected by a 32 bit CRC calculation to  provide highly secure
          and reliable communication.

     Bad data CRC (#)
     Dropped bytes -# (#)
     Noise burst # (#)
          These messages indicate  that an error was  detected in a block  of
          data  in the file  being received.  "Dropped  bytes" indicates that
          some expected  bytes did not  arrive, and  "Noise burst"  indicates
          that  more bytes  than  expected  arrived.    Error  correction  is
          automatic, because  of Full-Streaming-Error-Correction,  may  occur
          without breaking the stream of data being received.

          If  this message occurs at regular intervals,  it is a sign of flow
          control failure.   In  most cases, this  can be corrected  with the
          addition of the -HS command line option.

     COM#: Break! Framing! Overrun! Parity!
          These  messages indicate that  an error was detected  in the serial
          port receiver.   Framing and  Parity errors often  indicate a  baud
          rate (-B) mismatch.   Overrun errors usually indicate the  need for
          flow  control or for an upgrade to a buffered serial chip.  Overrun
          errors  can often be reduced or eliminated  with the use of the -HS
          command line option.

     Can't create file '___'
          This indicates that the  received file could not be  created.  This
          usually  indicates that the  directory specified in  the -U command
          line option is invalid, or that the disk is full.

     Carrier lost!
          This indicates that Carrier detect was dropped, aborting the HSLINK
          session.   If  your connection  does not  provide a  carrier detect
          signal, you can disable this check with the -C command line option.
          This is often  required when directly  connecting two computers  by
          means of a "null modem" cable.

     Disk write failure!  (#)
          This  usually  indicates that  the  disk is  full and  that further
          downloads cannot be received.

     File received OK, # cps, # seconds.
          The file  was received  correctly and is  now closed.   The average
          transfer speed  is calculated  based on  the elapsed  time  between
          receiving  the file  open packet  and the  last byte  of the  file.

     HS/Link 1.21                     - 31 -                  Reference Guide





          Transfer speeds are  calculated using the DOS timer tick,  which is
          not accurate for  transfers taking less than 1 minute  to complete.
          For very short transfers, a cps rating of 9999 will be returned.

     File sent OK, # cps, # seconds.
          The file was  transmitted correctly and is now closed.  The average
          transfer speed  is calculated  based on  the elapsed  time  between
          sending the first byte of the file and the last byte of the file.

     File skipped by remote!
          The transmitter prints this  message when the receiver requests the
          current  file be skipped.   This usually happens  when the receiver
          detects  a  duplicate filename  and  is  not allowed  to  overwrite
          existing files.

     File was incomplete!  (# #)
          This  message indicates that  the transfer was aborted  in some way
          before  the  specified  file  was  completely received.    Normally
          incomplete files are erased from disk, but they will be retained of
          the -K command line option is used.

     Flow control released (#### t:# r:#)
          If  output flow has  been suspended by either  software or hardware
          flow control for more than 15 seconds, the program will assume that
          there has been a failure of flow control and  will release the hold
          so data can continue.  The codes in parenthesis indicate which flow
          controls were  active at  the time (C=CTS  was down,  T=transmitter
          XOFF  was pending,  R=receiver XOFF  was pending,  A=transmitter is
          currently  active)  and the  counts  of bytes  in the  transmit and
          receive holding queues.

     Handshake: CTS XON/XOFF SLOW ALT
          This  message indicates  the  current combination  of  flow control
          options  that are  in  effect.   CTS  indicates CTS  hardware  flow
          control is active.  XON/XOFF indicates that  XON/XOFF software flow
          control is  active.  SLOW  indicates that flow  will be  restrained
          during disk I/O to prevent overrun errors.  ALT indicates  that the
          alternate XON/XOFF method is being used.

     HS/Link finished! (t:# r:#) Exit code = #
          When HSLINK terminates, it sets the DOS ERRORLEVEL to the specified
          value.    This can  be  checked  in  batch files  to  detect  error
          conditions.  The following ERRORLEVEL codes are possible:

          ERRORLEVEL     Reason for link termination

             0           One or more files transferred successfully
             1           ^X typed at local keyboard
             2           ^X received over COM port
             3           Incompatible BETA versions
             4           No files transmitted or received
             5           Remote did not respond within 2 minutes
             6           Too many framing errors, possible -B mismatch

     HS/Link 1.21                     - 32 -                  Reference Guide





             7           Possible tampering or corruption in HSLINK.EXE
             8           Possible tampering or corruption in HSLINK.EXE
             9           COM port not responding, incorrect -P options
            10           Carrier lost during initial handshake with remote
            11           Link aborted due to CTS lockup
            12           Bad command line option
            13           Excessive repeated errors

          COMM  and  BBS programs  should  use  the  DSZLOG  output  file  to
          determine more specific details of transfer results.

          The  (t:# r:#) display  indicates the number  of files successfully
          transmitted and received.

     Not allowed to overwrite existing file '___'
          This  indicates that a file was received but there was another file
          with the same  name already in the download file directory.  Either
          erase the  duplicate file, or use  the -O option  to allow existing
          files to be overwritten.

     Insufficient memory to load program.
     Not enough memory!
          There  was  not enough  memory  available  to  run  HSLINK.    Free
          additional  memory  by  removing  "TSR"  software,  device drivers,
          ramdisks or  disk caches.  If  your COMM program has  the option of
          swapping  to  DISK or  EMS,  enable the  option to  free additional
          memory for  HSLINK's use.   Current beta copies  of HSLINK  require
          about 64k  of RAM, but  the specific amount  of memory required  is
          subject to change from beta to beta.  You can reduce  the amount of
          memory required if you use  the -NB command line option  to disable
          file buffering.

     Out of sequence # (#)
          This  indicates  that  the  received  block  was out  of  sequence,
          indicating  that  a  block  was  possibly  missed  or  lost  during
          transmission.    The  receiver  will  request  the  transmitter  to
          retransmit the missing block(s).

     Read failure at #
          This indicates  that there  was a disk  error reading a  file being
          transmitted.

     Receive timeout (#)
     ACK timeout, resend #
          This message indicates that it has been too long since the receiver
          responded to data transmission.  The last data block is repeated in
          an attempt to wake up the receiver.

     Received block # (# bytes) # cps
          This  displays the current status of  the file being received.  The
          current number of blocks and bytes received is displayed after each
          block is received.  The estimated transfer  speed in ch/sec is also
          displayed.

     HS/Link 1.21                     - 33 -                  Reference Guide





     Received block # (# bytes) E#
          When "E#" is  displayed following the received block #  message, it
          indicates  that  error  recovery  is  in  progress,  and  that  the
          specified block  number was  in error and  is in  transit from  the
          transmitter.   When the erroneous block has been received correctly
          the E# display  will advance to the next erroneous block number, or
          will be erased if no more erroneous blocks are pending.

     Received block # (# bytes) R
          When  "R" is displayed  following the received block  # message, it
          indicates that current block has been previously received correctly
          and  is  therefore a  "repeat"  block.   Repeat blocks  occur under
          severe error conditions and are usually corrected automatically.

     Receiving file: ___ (# blocks, # bytes)
          This message indicates that  a new file is being received  from the
          transmitter.  The file size is displayed in blocks and bytes.

     Remote not responding!
          This  indicates that the remote computer did not execute HSLINK and
          establish  a connection within the two minute timeout period.  This
          message  could also  indicate  that the  wrong  com port  is  being
          selected,  or that  the port  is configured improperly  (wrong port
          speed or IRQ setting).

     Resending block #
          This message indicates that the receiver has detected an  erroneous
          block  and is  requesting a  re-transmission  to correct  the data.
          Data flow continues where it left off prior to the resend, allowing
          error recovery to take place without breaking out of full streaming
          mode and without discarding data that is already in  transit to the
          receiver.  This is the basis of Full-Streaming-Error-Correction.

     Restarting current file
          This  indicates that the receiver was unable to recover from errors
          encountered in  processing the current file  being transmitted, and
          has requested that the file be started again from scratch.

     Seek from block # to #
          Under the most  severe error conditions,  the receiver may  request
          the transmitter to discard data that is  in transit to the receiver
          and  to  rewind to  an  earlier position  in  the  file and  resume
          transmission.

     Sending block # (# bytes/w:#) # cps
          This  is  the   normal  status  display  while  a  file   is  being
          transmitted.  The  message indicates the latest block number  to be
          transmitted,  and  in parenthesis  indicates  the  number of  bytes
          transmitted and  the  current  number  of  blocks  that  have  been
          transmitted without acknowledgement,  which represents the  size of
          the transmit  "window" that  is currently  in use.   If  this value
          hangs  at the current -W setting, you  may benefit from a higher -W
          setting on the command line.  The estimated transfer  speed is also

     HS/Link 1.21                     - 34 -                  Reference Guide





          reported in ch/sec.

     Sending file: ___ (# blocks, # bytes)
          This message indicates that a new file is being transmitted  to the
          receiver.  The file size is displayed in blocks and bytes.

     Transfer aborted!
          This  message  indicates that  the current  file transfer  has been
          aborted  for some  reason.   The specific  reason for  the transfer
          abort is usually also printed on the screen.

     Waiting for remote.
          This message indicates that HSLINK is waiting to handshake with the
          remote computer.   HSLINK will  wait for  60 seconds for  the other
          computer to come online; after that the transfer is aborted.   This
          message can  also  indicate that  you  don not  have the  COM  port
          correctly specified  or that a non-standard  COM port configuration
          may be required.

     Warning: CTS signal missing!  -HC will be assumed.
          The CTS hardware handshake is normally enabled by default.  If,  on
          initial  loading,  HSLINK finds  that  the CTS  signal is  down, it
          assumes that  the current hardware  configuration is not  using CTS
          handshake and automatically disables further  CTS handshake checks.
          Use the -HC command line to manually disable CTS handshake.

     Window: #
          This  indicates the actual number of  blocks that are allowed to be
          in transit without  acknowledgement.  This is controlled by  the -W
          parameter,  and may  be overridden  by the  remote computer  if the
          remote uses the -!  (take priority) option.

     Window: NONE
          This  indicates that the -A command line option has been specified,
          and  that  the transmitter  is  required  to continue  indefinitely
          without  receiving any  kind of  acknowledgement from  the receiver
          that data is being received correctly.

















     HS/Link 1.21                     - 35 -                  Reference Guide





        ___________________________________________________________________

                             License and Registration
        ___________________________________________________________________

     This program is  not free!  You are hereby licensed  to use this program
     for a trial period  of 30 days free of  charge.  If, after  30 days, you
     decide that you would like  to continue using HSLINK, you  must complete
     the  registration form (REGISTER.FRM)  and return it to  the author with
     the required registration fee enclosed.

     Registration  removes the "UNREGISTERED"  messages as  well as  all time
     delays and enables  you to initiate a  CHAT session.   Your registration
     number will be broadcast to the remote copy of hslink.

     Basic HSLINK registration  costs $20 US,  which includes a  registration
     certificate showing a Serial Number and Password.  The latest version of
     HSLINK is available on disk.  A nicely typeset and bound reference guide
     is also available.  Please print out  the file REGISTER.FRM for specific
     registration details. 

     Please feel free  to distribute unregistered HSLINK to your  friends and
     local BBSs as long  as all of the files in this archive are included and
     unmodified.

     Send your registration payment to:
                         SAMUEL H.  SMITH
                         P. O. BOX 4808
                         PANORAMA CITY, CA 91412-4808
                         U.S.A.

     HS/Link registration can also be ordered ON LINE by credit card  through
     any of the Tool Shop BBS phone lines.





        ___________________________________________________________________

                   License Agreement for Shareware distributors
        ___________________________________________________________________

     Shareware distributors may distribute this program as long as the author
     has been  notified, in  writing, prior  to ANY  distribution.   The "per
     disk" charge may  not exceed $6 and  the shareware distributor  will not
     change the  above license fee for the end user of HSLINK.  End users are
     not  exempt  from  registering  HSLINK with  the  author  at the  normal
     registration fee.





     HS/Link 1.21                     - 36 -                  Reference Guide





        ___________________________________________________________________

                                      Support
        ___________________________________________________________________

     HS/Link was Written by Samuel H. Smith.   Contact me at:

               The Tool Shop BBS

               Phone number   Modem type
               (818) 891-1344 v.32bis/v.42bis
               (818) 891-6780 Hayes-V 9600
               (818) 891-3772 USR HST 9600

     You will always find the  latest release version of HS/Link on  the Tool
     Shop, as well as a variety of support files and programs.

     HS/Link  is also  supported  by  a  number  of  authorized  distributors
     throughout  the world.    Please refer  to  DISTRIB.DOC for  the  latest
     distributor list.

     The HS/Link Support Conference is carried by UN'I-Net/US, SmartNet, RIME
     and  possibly a  number of  other  echo networks.   You  can  get direct
     product support through a local BBS that carries this echo conference.

     Voice  support is available  tuesday through friday between  9am and 6pm
     pacific time at (818) 891-4228.




        ___________________________________________________________________

                                    Disclaimer
        ___________________________________________________________________

     IN NO EVENT WILL  I BE LIABLE TO YOU FOR ANY DAMAGES, INCLUDING ANY LOST
     PROFITS,  LOST  SAVINGS OR  OTHER  INCIDENTAL  OR CONSEQUENTIAL  DAMAGES
     ARISING OUT  OF YOUR USE  OR INABILITY  TO USE THE  PROGRAM, OR  FOR ANY
     CLAIM BY ANY OTHER PARTY.














     HS/Link 1.21                     - 37 -                  Reference Guide





        ___________________________________________________________________

                                       Index
        ___________________________________________________________________

     Aborting a transfer (7)
     Auto-download (29)
     Basic settings (9)
     Configuration files
          HSCONFIG (8)
          specifying alternate configuration files (8)
     Context sensitive help (10)
     Crash recovery
          -R (14)
     DesqView
          -I2 (16)
          -NV (19)
     Display bleeding (6)
     DoubleDOS
          -I3 (16)
          -NV (19)
     DSZLOG (30)
     ERRORLEVEL (32)
     Errors
          -HS (7)
          COM Overrun (11), (25)
     Exit codes (32)
     File sharing (28)
     Flow control (24), (25)
          -HS (7)
     HSCONFIG (8)
     HST (27)
     Installation
          In BBS programs (22)
          In COMM programs (22)
     Non-standard COM ports (12)
     NS16550AN (26)
     Options
          -! (15)
          -@ (8)
          -@fname (20)
          -A (15)
          -Bbaud (12)
          -C (13)
          -CBcolor (19)
          -CGcolor (19)
          -CMcolor (19)
          -CP (19)
          -CTcolor (19)
          -CWcolor (19)
          -Ebaud (13)
          -FC (17)
          -FT (17)

     HS/Link 1.21                     - 38 -                  Reference Guide





          -HC (13)
          -HR (13)
          -HS (7), (11)
          -HX (13)
          -Iidle (16)
          -K (14)
          -LFlogfile (17)
          -N! (20)
          -N5 (17)
          -NA (17)
          -NB (15)
          -NC (15)
          -NF (18)
          -NG (20)
          -NK (20)
          -NM (16)
          -NOdirlist (17)
          -NT (13)
          -NU (20)
          -NV (6), (19)
          -O (15)
          -PBbase (12)
          -PIirq (12)
          -Pport (7), (11)
          -R (14)
          -Ssize (15)
          -T (20)
          -Udir (7), (11)
          -Wwindow (15)
     PC-Pursuit
          -W (15)
          Example (21)
     Registration (36)
     Support (37)
     V.32 (27)
     Zmodem (27)


















     HS/Link 1.21                     - 39 -                  Reference Guide