====================
                                +----+ |         | |
                                |    | +--+ ---+ | |
                                |  -+| |  | +--+ | |
                                +---++ +--+ +--+ - -
                                    +-
                                ====================


                           SMALL ARMS EXTERIOR BALLISTICS

                                        for

                              IBM PC's and COMPATIBLES
                                     __________

                              Application Programming
                                 and Documentation

                                         by

                                Benjamin  W. Hartley
                              Forest Park Estates #103
                              Jaffrey, NH        03452
                                        ---
                              Voice#:   (603) 532-6248
                              America OnLine: BHartley
                              CompuServe:   70033,2612
                              GEnieMail:    B.HARTLEY1
         __________________________________________________________________
                 _______
            ____|__     |               (R)
          -|       |    |-------------------
           |   ____|__  |  Association of
           |  |       |_|  Shareware
           |__|   o   |    Professionals
          ----|   |   |---------------------
              |___|___|    MEMBER

               The author is a member of the Association of Shareware Pro-
          fessionals, the ASP.   ASP wants to make sure that the shareware
          principle works for you.   If you are unable to resolve a share-
          ware-related problem with an ASP member by contacting the member
          directly, ASP may be able to help.  ASP's Ombudsman can help you
          resolve a dispute or  problem with an  ASP member,  but does not
          provide technical support for members' products. Please write to
          the ASP Ombudsman at 545 Grover Rd., Muskegon, MI 49442-9427 USA
          (FAX 616-788-2765, 24 hrs./day) or send a message via CompuServe
          mail to: ASP Ombudsman 72050,1433.
         __________________________________________________________________

            "QBALL" -- source code, executable files, and documentation
            are (c) 1991-93 by Benjamin W. Hartley. All rights reserved.


         [ QBALL                                                       ii ]
                                 TABLE OF CONTENTS

            Dedication, Disclaimer, License, Copyright Information... i
            Table of Contents....................................... ii
            List of Figures........................................ iii
            List of Tables......................................... iii
            Introduction............................................ iv
            About Shareware.......................................... v

                Chapter                                        page
                 1. Getting Started............................. 1
                  1.1 Files Required............................ 1
                  1.2 Will It Work ?............................ 1
                  1.3 Copying the Program....................... 1
                  1.4 General Instructions...................... 2
                  1.5 Starting QBALL............................ 3
                 2. Computing Ballistic or Gun Data............. 7
                  2.1 Preliminary Data Entry.................... 7
                  2.2 Computing and Displaying a Range Table.... 8
                  2.3 Displaying Graphics...................... 10
                  2.4 Changing Input Data...................... 15
                  2.5 Other Ballistics Procedures.............. 17
                   Point-Blank Range........................... 17
                   Wind Vector Corrections..................... 18
                   Slant Angle of Fire......................... 19
                   Sectional Density........................... 20
                   Free Recoil Velocity and Energy............. 20
                  2.6 Bullet Lookup Facility................... 21
                 3. Inferring Ballistic Coefficients........... 23
                  3.1 First Run: r1 = 0........................ 24
                  3.2 Second Run: r1 = 25...................... 25
                 4. Printed Output............................. 27
                  4.1 Printer Warnings......................... 27
                  4.2 Screen Dumps............................. 27
                  4.3 Printer Setup............................ 27
                  4.4 Print Functions.......................... 28
                  4.5 Typical Printed Output................... 28
                 5. Configuring Display/Default Starting Values 31
                  5.1 The Utilities and Configuration Menu..... 31
                  5.2 Toggle Active Switches................... 31
                  5.3 Configuring Display Colors............... 32
                  5.4 Using the Values You've Set.............. 33
                  5.5 Invoking a DOS Shell..................... 34
                  5.6 Reading Range Tables/Translating Graphics 34
                 6. Recalling Saved Trajectory Data............ 35
                 7. File Handling.............................. 37
                 8. QBALL's Associated Utilities............... 39
                  8.1 RRGTABLE.EXE............................. 39
                  8.2 GRFXLATE.EXE............................. 40
                Appendices:--
                 A. Glossary................................... 43
                 B. Ballistic Coefficient from Tabular Data.... 49
                 C. Typical Saved Trajectory File.............. 51
                 D. Selected Bibliography...................... 53
                 E. Error Analysis............................. 55
                 F. QBALL and Other Programs................... 57
                 G. Error Messages............................. 61
                 H. Default Starting Values.................... 63


         [ QBALL                                                       iv ]

                                    INTRODUCTION

           QBALL is a menu-driven application for the rapid computation of
         ballistic data for small arms projectiles. QBALL will quickly 
         compute point-of-impact data, velocity and energy levels, 
         trajectories relative to line-of-sight, and times of flight. 
         Additional routines permit the calculation of ballistic coeffi- 
         cients, slant-fire corrections, point-blank range, and gun free 
         recoil. Printing routines (parallel printers only, LPT1) may be 
         used to produce hard copy. Starting values and the display to 
         which the program will default may be changed using the built-in 
         configuration routines.

           You are assumed to have some knowledge of exterior ballistics.
         QBALL will not teach you exterior ballistics. Several of the ref-
         erences in the Bibliography contain basic introductions to the
         subject. Their study will amply repay the effort expended.

           Warning!  All QBALL-generated data should be used as a guide to 
         ballistic performance! You MUST verify QBALL's data with a stan-
         dard reloading manual. Several manuals are listed in Appendix C.

           If you find QBALL of use, but would like it to do something that
         it doesn't do now, or have suggestions to improve what it does 
         already, please send in a copy of the Enhancement Form. If you are
         the first to suggest an improvement which is included in a later
         QBALL release, you will receive a free copy of that release.

           Should you have problems with QBALL, you may call the author at 
         603-532-6248; no collect calls, please! Try to call during 
         reasonable hours. (For guidance: no calls later than 11:00 p.m. 
         Eastern Time.) You may contact the author by CompuServe mail 
         message to Ben Hartley, 70033,2612; on America On Line, address 
         BHartley; or on GEnieMail, address B.Hartley1. If you would prefer
         to write, please do so. The author will respond to all requests 
         help.

           The latest registered version of QBALL is available from the 
         author for a $25.00 registration fee. Registration entitles you to 
         the latest version with one free upgrade, and a 3-hole-punched, 
         printed manual. The Professional Development System 7.1 source 
         code for the current version is available to registered users for 
         $50.00. You may register and get the source code at the same 
         time for $60.00.

           The most current shareware version of QBALL, which is func- 
         tionally the same as the same-numbered registered version, is 
         available direct from the author for a $7.50 fee, and on the 
         EXEC-PC BBS (Modem: 414 789-4210, 1200/2400 8N1); the LegalEase BBS
         (Modem: 509 326-3238, up to 14400 8N1); in the CompuServe Outdoor
         Forum, filename "QBLnnn.ZIP";  and on America OnLine, in the
         "Sports" Conference, keyword "ballistics." (The author uploads to
         these services and BBS. Downloads from other sources may not
         include all the files -- caveat emptor.)


























                                       QBALL

                                    User's Guide


         [ QBALL                                                        1 ]

                                     Chapter 1
                                  Getting Started
                                  """""""""""""""

         1.1  Files Required.

           Shareware copies of QBALL are distributed with the following 
         files in the QBALL220.ZIP/QBL220.ZIP distribution file:

           QBALL.EXE       The QBALL executable file;
           EGA_SAV.0       EGA format trajectory graphics file;
           CGA_SAV.0       CGA format trajectory graphics file;
           RRTABLE.EXE     } QBALL utilities, stand-alone and
           GRFXLATE.EXE    } callable from within the program;
           AMMO.DAT        Data for on-line bullet lookup;
           D.NDX, M.NDX    Index files for bullet lookup;
           QBALLODD.DOC    Documentation, odd-numbered pages;
           QBALLEVN.DOC    Documentation, even-numbered pages;
           QBALLENH.DOC    Suggested enhancement form;
           QBALLREG.DOC    QBALL registration form;
           QBREADME.BAT    Prints short intro on screen;
           ONEDOC.COM      Utility to consolidate documentation.

           The only absolutely required file is QBALL.EXE. 

         1.2  Will It Work ?

           QBALL is written in and compiled as a stand-alone .EXE file 
         using Microsoft Professional Development System 7.1 on a Gateway 
         2000 AT clone (80286 processor), AMI BIOS, MS-DOS 6.0, 4DOS 4.02, 
         1-5¬ inch (1.2 meg) and 1-3« inch (1.44 meg) floppy drive, dual 
         40-megabyte hard disks, and Samsung CM4531 EGA monitor. No co- 
         processor was used.

           QBALL is fully operational with MS-DOS 3.3, 4.01, 5.0, and 6.0, 
         both with "plain vanilla" COMMAND.COM and 4DOS 4.00/4.02, and 
         should function properly on any PC-DOS or MS-DOS computer. QBALL 
         will also function properly in the WINDOWS 3.n "DOS box;" insuf- 
         ficient experience is available regarding OS/2 to generalize, but 
         it is known that QBALL will not operate under OS/2 protected mode. 
         Routines are included to detect CGA or EGA installation; if no 
         graphics are available, QBALL internally disables the graphics 
         routines.

         1.3  Copying the Program Files.

           It would be wise to make a copy of the original QBALL files, and 
         keep it in a safe place. Run QBALL from copies of the original!

           If you have a hard disk, it is recommended that you make a spe- 
         cial QBALL directory on it. (QBALL will run from a floppy, but it 
         is s-l-o-o-o-w!) Make sure that you copy QBALL.EXE, RRTABLE.EXE, 
         and GRFXLATE.EXE to the same directory, or onto the same disk. 
         QBALL.EXE will look for its associated utility files in the 
         current directory. Copy AMMO.DAT, the two *.NDX files, and the two
         *GA_SAV.0 files to the QBALL directory as well.


         [ QBALL                                                        3 ]

         1.5  Starting QBALL

           Log into the directory or onto the drive where you've put 
         QBALL.EXE and type:

                                 QBALL (+ [Enter]).

           Hint: If you have a monochrome monitor, or you just don't like
          colors, start QBALL with: QBALL /b (+ [Enter]). Save the black-
          and-white configuration; see Chapter 5.

           The next thing you'll see is the opening screen, which looks 
         something like this:

            ------------------------------------------------------------

            +==========================================================+
            |            +=======+  =            =  =                  |
            |            |       |  |      ___   |  |                  |
            |            |       |  |         |  |  |                  |
            |            |       |  +---+ +---+  |  |                  |
            |            |    =+ |  |   | |   |  |  |                  |
            |            +=====+=+  +---+ +---+  -  -                  |
            |                  +=         Reg #N220SW                  |
            |                                                          |
            |      [ Exterior Ballistics for PC's & Compatibles ]      |
            |      [ Using G1 Drag Functions  ---  version 2.20 ]      |
            |      [ Copyright (c) 1991-3,  Benjamin W. Hartley ]      |
            +----------------------------------------------------------+

               Welcome to computer ballistics with QBALL!

               QBALL provides small arms trajectory data quickly...

               Users are encouraged to verify QBALL data with a...
              handbook!  The author will NOT be responsible for ...
              misapplication of QBALL-generated data.
                                                              EGA
                               ===> press any key <===      Graphics

            ------------------------------------------------------------
                             Figure. 1. Opening Screen.

           If your computer is graphics-equipped, QBALL reports what kind 
         of graphics it has found: "CGA," or "EGA."  (VGA graphics "fall 
         through" to EGA standard.) If no graphics equipment is detected, 
         QBALL specifies "No Graphics."

           The version number are shown on the opening screen. (Here, it's 
         "version 2.20." If you need to contact the author with comments, 
         suggestions, or requests for help, it would be helpful if you 
         include the version number with your communication.

           Press any key to continue.


         [ QBALL                                                        5 ]

           Note, also, that standard metro is shown on the info line. There 
         are several occasions when you'll need to confirm that QBALL is 
         indeed using standard metro; make a mental note of what the 
         standard metro display looks like:

                            [ Met: 59d 0' 29.53" 78%  ].

           One frequent use for QBALL is the production of ballistics 
         tables for a specific cartridge/load. With the Main Menu shown on 
         the screen, press <C> to open the menu for computation of ballis- 
         tic and gun data. More information about using this option is 
         contained in Chapter 2.

           If you wish to infer a ballistic coefficient, then press <B>. 
         More information is to be found in Chapter 3.

           Use <U>tilities... accesses the menu which permits changing the 
         display colors, the status of the printer, graphics grid, and 
         noise toggles, and several values which QBALL will use when 
         started. A "shell to DOS" routine is also included. See Chapter 5 
         for more information about configuring QBALL. You may also access  
         "RRTABLE" and "GRFXLATE" from within the Utilities Menu.

           <R>ecall Saved Graphics...accesses saved trajectory data, and 
         allows you to use that data. If there is no trajectory data saved, 
         this option will not appear. (You did copy the two "*GA_SAV.0" 
         files from the distribution disk, didn't you?) This option is dis- 
         cussed in detail in Chapter 6, Recalling Saved Trajectory Files.

           <Q>uit... -- press <Q> to return to DOS. QBALL will ask you to 
         confirm that you indeed wish to quit. Press [Y] to return to DOS 
         or press "N" to continue using QBALL. If you confirm that you wish 
         to quit, and you have saved trajectory data, you will also be 
         prompted:

                          Retain Saved Data ? ([Y] or N).

         The default is [Y] -- that is, keep the saved data. It is strong- 
         ly recommended that you press <N>: erase the saved data, at least 
         until you've played with QBALL for awhile.

           Let's put QBALL to work...

           Press <C> to compute ballistic data, and to do the tutorial 
         which follows. Go on to Chapter 2, page 7.


         [ QBALL                                                        7 ]


                                     Chapter 2
                          Computing Ballistic or Gun Data
                          """""""""""""""""""""""""""""""

         2.1  Preliminary Data Entry.

           Before doing anything else, we're going to have to enter some 
         information for QBALL to chew on. The items of information for 
         which QBALL will prompt you are, in order, (with suggested 
         practice entries):

                a. The ballistic coefficient (C1) for the
                           projectile in question................ .300

                    [  For tutorial purposes, enter ballistic ]
                    [ coefficients and bullet weight by hand, ]
                    [ and reserve trying QBALL's bullet look- ]
                    [ up facility for later on.               ]

                b. The bullet weight in grains...................  180

                    [ Automatic entry if data lookup is used. ]

                c. Whether or not to use the displayed metro.....  [Y]

                    [ QBALL  will  default to Standard Metro; ]
                    [ you can use nonstandard metro, but just ]
                    [ to keep things simple,  stay with stan- ]
                    [ dard metro for the present.             ]

                d. The muzzle velocity in FPS.................... 2200

           Enter values at the appropriate places when prompted. If you try 
         to use an impossible value, QBALL will respond with an error 
         message specifying a valid range of values for that parameter. Try 
         entering some impossible values and see what happens. A complete
         list of QBALL's error messages is contained in Appendix G, with a
         description of the most common conditions under which they
         are displayed.

         [ Bullet Lookup Facility:                                        ]
         [     For initial ballistic coefficient and bullet weight entry, ]
         [ Press [L] while  the appropriate entry box  is displayed.  Use ]
         [ PgUp, PgDn, Home, End, and arrow keys  to navigate through the ]
         [ list. Press [Enter] to use the highlighted data. Bullet lookup ]
         [ sets/resets both  ballistic coefficient and bullet weight when ]
         [ used. Maker abbreviations: HDY=Hornady, LYM=Lyman, NOS=Nosler, ]
         [ SRA=Sierra, SPR=Speer.   Bullet lookup is displayed in bullet- ]
         [ diameter order by default;  press  [M]  to change  to by-maker ]
         [ order.                                                         ]


         [ QBALL                                                        9 ]

           Note that the Range <T>able... option will now display the zero 
         range.

                        +=================================+
                        |  Range <T>able (0 = 250 Yards)  |
                        +---------------------------------+
                   Figure 4. Partial Computations Menu, Zero Set

           A zero range must be set in order to compute and display a range 
         table. If no valid zero range is set, QBALL will ask you for one. 
         You may set or reset the zero range by pressing <Z>; the Range 
         <T>able... option will display that zero range.

         Let's continue with this range table; enter the data shown.

                       Range to Point of Impact.......... 300
                       Range Increment...................  50

         The following table is displayed:

          ---------------------------------------------------------------
                    > Ballistic Computations: Typical Firearm <

                      Range Table, Zeroed at Highlighted Range
                      ----------------------------------------

          Range  R e m a i n i n g  Total  Path/Sight Line  Defl'n  Time
          Yards  Velocity   Energy   Drop  M.O.A.   Inches  10 MPH  Flght
          -----  -----------------  -----  ---------------  ------  -----
              0    2200      1934     0.0   0.0      -1.0     0.0   0.000
             50    2068      1708     0.9   7.8       3.9     0.4   0.070
            100    1939      1503     3.9   6.8       6.8     1.5   0.145
            150    1816      1319     9.1   4.9       7.3     3.5   0.225
            200    1700      1155    17.1   2.6       5.2     6.7   0.311
          >>250    1589      1010    28.1   0.0       0.0    10.8   0.402<<
            300    1485       881    42.4  -2.8      -8.5    15.9   0.499
                      ----------------------------------------
                              ===> press any key <===
          ---------------------------------------------------------------
                           Figure 5. Typical Range Table

           Range tables are interpreted as follows: for a bullet having the 
         given ballistic characteristics and fired at the given muzzle 
         velocity, then, at a range of, say, 200 yards, it will retain 1700 
         FPS velocity, 1155 ft-lbs of energy, will have dropped 17.1 inches 
         below the line of departure, will have risen to a maximum of 7.3 
         inches above the line of sight (at 150 yards), will strike 5.2 
         inches (2.6 minutes of arc) high, will have been blown 6.7 inches 
         sideways by a 10 MPH crosswind, and will have taken 0.311 seconds 
         to travel 200 yards downrange from the muzzle. In similar fashion, 
         data for other ranges may be read from the table for each of the 
         listed ranges. Note that the table specifies that Path/Sight Line 
         is 0.0 at 250 yards, the zero range. That line is highlighted on 
         the screen display; here, it's shown >> thus <<.


         [ QBALL                                                       11 ]

                    > Ballistic Computations: Typical Firearm <
          +--------------------------------------------------------------+
          | |                             *                              |
          |I|                  *                                         |
          | | 5                                      *                 5 |
          |N|        *                                                   |
          | |                                                            |
          |C|-0------------------------------------------------*-------0-|
          | *                                                            |
          |H|    [draw a smooth curve]                                   |
          | |-5  [connecting the "*".]                                -5 |
          |E|                                                            |
          | |                           YARDS                            *
          |S|       50        100        150        200       250        |
          +--------------------------------------------------------------+
          |     [ --- Remaining Velocity/Energy, Current Round --- ]     |
          +--------------------------------------------------------------+
          |           >Current<    >Previous<    +=======================+
          |Max Ht :  7.4" @ 135                  | *** Graphics Menu *** |
          |Min Ht : -8.5" @ 300                  | --------------------- |
          |MuzVel :   2200 FPS                   |<G>rid Toggle On/Off   |
          |TermVel:   1485 FPS                   |<S>ave Current Data    |
          |BCoeff :   .300                       |<R>ecall <0>           |
          |ZeroRg :  250 Yards                   | --------------------- |
          |Metro  :  Standard                    |<ESC>ape to Choose Next|
          +--------------------------------------------------------------+
          |        [ --- info line schematically indicated --- ]         |
          +--------------------------------------------------------------+
                           Figure 7. The Graphics Screen

           The upper portion of the screen represents your firing range as 
         viewed from the side. The firing point is at the left; the maxi- 
         mum range, 300 yards, at the right. Each range increment is indi- 
         cated by a vertical line, numbered across the bottom. The hori- 
         zontal lines, indicating distance above or below the line of sight 
         are numbered at both the left and right. The curved line indicates 
         the bullet's trajectory relative to the line of sight: the 
         emphasized line numbered "0-0."  The circle on the curved line 
         indicates the point at which the maximum height is reached. The 
         numbers immediately below the trajectory plot are the remaining 
         velocity and energy at the indicated range for the current round.

           The data shown at the bottom left are: the maximum and minimum 
         heights, and the ranges at which they occur; the muzzle and term- 
         inal velocities; the ballistic coefficient; the zero range; and 
         the metro currently in effect.

           Press <G> to redraw the screen without the background grid 
         lines. Tick marks are displayed at the left and right, and on the 
         sight line; appropriate numbers are shown. Press <G> again to re- 
         display the grid lines.

           <R>ecall... tells you that you have one set of trajectory data 
         saved to disk. (Yes, that's a "zero;" I'll explain in a bit.)


         [ QBALL                                                       13 ]

           Now let's play "what if...?"  What would happen to the trajec- 
         tory if, say, the muzzle velocity is increased from 2200 to 2700 
         FPS?  Let's find out. Press <ESC> to return to the Computations 
         Menu, and with the Computations Menu displayed, press <N> to 
         access the "New or Changed Input Data" Menu.

           A complete explanation of the New Input Data Menu can wait for a 
         bit; this time, when it is displayed, press <V> to change the 
         muzzle velocity. Note that "2200" is displayed in the entry 
         window; overtype the new velocity, thus:

                        Muzzle Velocity         (FPS)  2700

           Note that is possible to change more than one item of input data 
         at a time; this is not recommended, because it is difficult to 
         determine which change has which effect. Now <ESC> back to the 
         Computations Menu. Note that your zero range, 250 yards, is still 
         set. Note that Press <T>, and note that the maximum range, 300 
         yards, is also set. Press <enter> to accept the displayed range; 
         then press <enter> again to accept the range increment of 50 
         yards. After the range table is displayed, press any key. When 
         presented with the "Choose Next" menu, press <G>. The new graphic 
         representation of trajectory data looks like Figure 9, page 14.










            [ HINT:                                                   ]
            [                                                         ]
            [   If you plan to save a lot of data, especially range   ]
            [ tables, you need all the disk room you can get! Range   ]
            [ tables get big, fast. If either of the following is     ]
            [ true:                                                   ]
            [                                                         ]
            [ You're running QBALL from the distribution disk,        ]
            [ (tsk,tsk!)                                              ]
            [ You're running QBALL on any floppy with other files on  ]
            [ it,                                                     ]
            [                    then quit QBALL (from here, the      ]
            [ keystrokes are: <ESC><ESC><ESC><Q><Y><Y>) and copy all  ]
            [ the QBALL*.* files to a fresh (empty) disk. Then re-    ]
            [ start QBALL from the new disk.                          ]
            [   QBALL is set up to detect a "disk full" error but why ]
            [ take the chance? Should a "disk full" error occur,      ]
            [ QBALL disables all "save" functions for the duration of ]
            [ the current session.                                    ]


         [ QBALL                                                       15 ]

                    > Ballistic Computations: Typical Firearm <
          +--------------------------------------------------------------+
          | |                             *                              |
          |I|                  *                                         |
          | | 5                *          *          *                 5 |
          |N|        *                               *                   |
          | |        *                                                   |
          |C|-0------------------------------------------------*-------0-|
          | *                                                            |
          |H|    [draw smooth curves ]                                   |
          | |-5  [connecting the "*".]                                -5 *
          |E|                                                            |
          | |                           YARDS                            *
          |S|       50        100        150        200       250        |
          +--------------------------------------------------------------+
          |     [ --- Remaining Velocity/Energy, Current Round --- ]     |
          +--------------------------------------------------------------+
          |           >Current<    >Previous 1<  +=======================+
          |Max Ht :  4.6" @ 138    7.4" @ 135    | *** Graphics Menu *** |
          |Min Ht : -5.3" @ 300   -8.5" @ 300    | --------------------- |
          |MuzVel :   2700 FPS      2200 FPS     |<G>rid Toggle On/Off   |
          |TermVel:   1877 FPS      1485 FPS     |<S>ave Current Data    |
          |BCoeff :   .300          .300         |<R>ecall <0> thru <1>  |
          |ZeroRg :  250 Yards     250 Yards     | --------------------- |
          |Metro  :  Standard      Standard      |<ESC>ape to Choose Next|
          +--------------------------------------------------------------+
          |        [ --- info line schematically indicated --- ]         |
          +--------------------------------------------------------------+
                    Figure 10. Two Sets of Data Graphics Screen

         2.4  Changing Input Data.

           From time to time, you may wish to change some or all of the 
         data which you have input to the program. The <N>ew Input Data 
         Menu, Figure 11, may be accessed from the Computations Menu for 
         that purpose. Press <N> to display the:

                        +=================================+
                        |   *** New Input Data Menu ***   |
                        |  -----------------------------  |
                        |  <C>artridge/Bullet Identifier  |
                        |  Muzzle <V>elocity              |
                        |  <B>allistic Coefficient        |
                        |  Bullet <W>eight                |
                        |  <M>etro (dF 'Alt "Hg  %RH)     |
                        |  Sight <H>eight                 |
                        |  Yds/Mets <S>wap (Now Yards)    |
                        |  -----------------------------  |
                        |  <ESC> to Computations Menu     |
                        +---------------------------------+
                          Figure 11. New Input Data Menu.

           Cartridge/Bullet Identifier: You may change the designation of 
         the cartridge, bullet, or firearm with which you are working. 
         Enter any string of characters at the prompt, e.g., ".30-'06 
         Springfield."  Identifiers are limited to a length of 40 charac- 
         ters; QBALL defaults to "Typical Firearm." You may keep the same 
         identifier by writing QBALL initialization data as explained in 
         Chapter 5.


         [ QBALL                                                       17 ]

         2.5  Other Ballistics Procedures.

           Five "other ballistic procedures" are described in this section. 
         Two, point-blank range and wind vector corrections, directly 
         affect the range table/graphics displays. The remaining three, 
         slant angle of fire corrections, sectional density, and gun free 
         recoil are informational in nature, only. From the Computations 
         Menu, press <O> to display the "Other Procedures Menu."

                        +=================================+
                        |  *** Other Procedures Menu ***  |
                        |  -----------------------------  |
                        |  <P>oint-blank Range            |
                        |  <W>ind Vector Corrections      |
                        |  Slant <A>ngle of fire          |
                        |  <S>ectional Density            |
                        |  <F>ree Recoil of Gun           |
                        |  -----------------------------  |
                        |  <ESC> to Computations Menu     |
                        +---------------------------------+
                          Figure 12. Other Procedures Menu

         Point-Blank Range.

           The point-blank range for any weapon/ammunition combination may 
         be defined as that range for which the trajectory deviates not 
         more than a specified distance above or below the line of sight. 
         Press <P> to access the point-blank range determination routines. 
         Enter the maximum deviation in inches, say, 5, as shown in figure 
         13.

                    +==========================================+
                    |                                          |
                    |    Determination of Point Blank Range    |
                    |    ----------------------------------    |
                    |                                          |
                    | Maximum Deviation                      5 |
                    |                                          |
                    |       Trial Zero Range = 512 Yards       |
                    |                                          |
                    +------------------------------------------+
                      Figure 13. Enter the Maximum Deviation.

           After a pause, during which the trial zero range changes several 
         times, the following is displayed:

                       +====================================+
                       |                                    |
                       | ---------------------------------- |
                       |    Point Blank Zero Range = 257    |
                       |         Maximum Range = 304        |
                       | ---------------------------------- |
                       |                                    |
                       +------------------------------------+
                      Figure 14. Point Blank Range Displayed.


         [ QBALL                                                       19 ]

         Slant Angle of Fire.  

           Virtually all firing tables and ballistics computation pro- 
         grams, QBALL among them, assume that the angle of fire is 
         relatively close to horizontal. It is known, however, that firing 
         "upslope" or "downslope" will cause the bullet to hit high 
         relative to the point of aim. How high? Press <A>, and enter the 
         following data: maximum range 400 yards and range increment 100 
         yards. You may enter the "vertical" dimension as an angle, or as a 
         height in feet above/below the firing point. You'll be prompted 
         thus:

                      Use <H>eight above/below firing point or
                      Vertical <A>ngle above/below horizontal:

         For this example, press <A> and enter the vertical angle 25d (the 
         vertical angle may be entered as positive or negative). The fol- 
         lowing table is displayed.

                        +=================================+
                        |                                 |
                        |  Hits High for Slant Fire, 25d  |
                        |    Above or Below Horizontal    |
                        |  -----------------------------  |
                        |    Range      True      Hits    |
                        |    Yards      Drop      High    |
                        |    -----     -----     -----    |
                        |       0        0.0       0.0    |
                        |     100        3.6       0.3    |
                        |     200       16.2       1.5    |
                        |     300       41.0       3.8    |
                        |     400       82.9       7.8    |
                        |  -----------------------------  |
                        |     ===> press any key <===     |
                        |                                 |
                        +---------------------------------+
                     Figure 16. Slant Fire "Hits High" Display

           The table tells you that the given weapon/ammunition combina- 
         tion, fired at an angle of 25d above or below the horizontal, will 
         hit high by the specified distance at each listed range. The 
         effect is relatively small at short range and smaller vertical 
         angles, but can become large enough to be of real concern as the 
         range or the vertical angle increases. Try several examples and 
         see.

         QBALL prompts...

                      ---> More? ([Y] or N) <C>ontinuous  <---

                          ...if there are more data lines than will fit on 
         one screen. Acceptable values for this routine are as follows:

             Range and range increment:     As for Range Tables;
             Vertical Angle:                0d to 45d, inclusive; or
             Vertical Height:               Height difference expressed in
                                            feet (1200 in the example).


         [ QBALL                                                       21 ]

           Unfortunately, these figures are relatively meaningless without 
         some basis for comparison. Here are three for starters, all data 
         computed using QBALL:

                +------------------------------+-------------------+
                |                              |       Weapon      |
                | Selected Weapon, Caliber,    +----------+--------+
                |          and Load            | Velocity | Energy |
                |                              |   FPS    | Ft-Lbs |
                +------------------------------+----------+--------+
                |                              |          |        |
                | 1. Ruger M77R (6.75 pounds)  |          |        |
                |    .22-250 Remington         |    7.86  |   6.49 |
                |       Muz Vel = 3680         |          |        |
                |       Bul Wt  =   55         |          |        |
                |       Pow Wt  =   36         |          |        |
                |                              |          |        |
                | 2. Marlin 336CS (7 pounds)   |          |        |
                |    .30-30 Winchester         |   10.67  |  12.39 |
                |       Muz Vel = 2390         |          |        |
                |       Bul Wt  =  150         |          |        |
                |       Pow Wt  =   35         |          |        |
                |                              |          |        |
                | 3. M1 Garand (9.5 pounds)    |          |        |
                |    .30-'06 Springfield       |   10.88  |  17.47 |
                |       Muz Vel = 2700         |          |        |
                |       Bul Wt  =  180         |          |        |
                |       Pow Wt  =   50.5       |          |        |
                |                              |          |        |
                +------------------------------+----------+--------+
                      Table 1. Free Recoil, Selected Weapons.

           The ammunition specified is a "best estimate" using published 
         Winchester data for velocities and bullet weights; the powder 
         weights are from the Hornady Handbook. The weapon weights were 
         taken from the 1991 edition of Gun Digest.


         2.6  Bullet Lookup Facility.

           Whenever QBALL prompts for a ballistic coefficient or a bullet
         weight, you may press [L] to activate the bullet lookup facility.
         If the AMMO.DAT file and either of the *.NDX files is present, a
         listing of a number of bullets is "windowed" over the prompt screen.
         (A sample appears on the next page.) The supplied AMMO.DAT file
         contains information about 502 bullets from several makers.

           Assuming that D.NDX is available, bullet lookup defaults to a
         listing sorted by diameter and weight. If you prefer, and if M.NDX
         is available, you may change to a list sorted by maker, diameter and
         weight by pressing [M].

           You may navigate through the list by using the PgUp, PgDn, Home,
         End, and the arrow keys. Press [Enter] to accept the highlighted
         bullet, or [ESC] to exit and enter the value manually.


         [ QBALL                                                       23 ]

                                     Chapter 3
                          Inferring Ballistic Coefficients
                          """"""""""""""""""""""""""""""""
           From time to time, you may have need of the ballistic 
         coefficient of a particular bullet, and the available tables do 
         not include that data.

           Select "Infer <B>allistic Coefficient" at the Main Menu. (The 
         first time you invoke this routine in a given session, you will be 
         encouraged to read this section of the manual.)  Press [Y] to 
         continue with the routine, or "N" to return to the Main Menu.

           QBALL will ask you for four pieces of information: two ranges, 
         and two velocities. The following diagram, a schematic layout of a 
         firing range viewed from above, will help you visualize the setup. 
         (Two chronographs are shown. See the note on page 26 if only one 
         chronograph is available.)

            +---------------------------------------------------------+
            |                         |  ( > > > >  =  bullet path )  |
            |                         |  ( C = chronograph location)  |
            |   +---[r1]----+         +-------------------------------+
            |   +-----------[r2]----------+                           |
            |                                                         |
            |   Gun > > > > C > > > > > > C > > > > > > > > > > > >   |
            |              v@1           v@2                          |
            |                                                         |
            |       r1  = range, muzzle to first chronograph          |
            |       r2  = range, muzzle to second chronograph         |
            |       v@1 = velocity at first range                     |
            |       v@2 = velocity at second range                    |
            |                                                         |
            +---------------------------------------------------------+
             Figure 18. Schematic Layout, Infer Ballistic Coefficient.

           It is possible for r1 to equal zero; in that case, of course, 
         v@1 would equal the muzzle velocity. (This is the only time that 
         QBALL will allow you to enter a range of zero; "zero" is the de- 
         fault value for r1.)
           The routine for inferring a ballistic coefficient allows use of 
         nonstandard metro, should you have developed your own velocity 
         data from live firing. You may change the metro conditions to be 
         used before beginning to enter velocity data. The ballistic coef- 
         ficient reported, however, is adjusted to standard metro 
         conditions in all cases.
           You may enter as many as twenty-five (25) individual range/vel- 
         ocity pairs. The average v@1, v@2, and ballistic coefficient are 
         reported. If r1 is greater than zero, i.e., you are not working 
         with a muzzle velocity, QBALL reports an inferred muzzle velocity. 
         Let's work through the process. We'll do this twice: once, with r1 
         set to 0, and once more with r1 set to 50; r2 will be set at 100 
         in both cases. (The data is that found in the table on page 9.)


         [ QBALL                                                       25 ]

         3.2 Second Run: r1 = 50

           Enter "first range" = 50 and "second range" = 100. When prompted 
         for the velocities, enter 2068 and 1939. You should end up with 
         the following display:

          +==============================================================+
          |               -----------------------------------            |
          |                      Metro: as displayed                     |
          | Relative Air Density = 1.000 Relative Sonic Velocity = 1.000 |
          |               -----------------------------------            |
          |                                                              |
          |                                                              |
          |                       For Round Number 1                     |
          |            First Velocity        (Ft/Sec)      2068          |
          |            Second Velocity       (Ft/Sec)      1939          |
          |                                                              |
          |               For Standard Atmosphere, C1 = .299             |
          |                                                              |
          |               Calculate another Round? ([Y] or N)            |
          |                                                              |
          |                                                              |
          |                                                              |
          |           [ Lower & Upper Ranges (yards)  50 & 100 ]         |
          +--------------------------------------------------------------+
                     Figure 21. Ballistic Coefficient Entry 2.

           Press "N"; (you would probably use more than one round in a 
         "real world" situation.) After a pause, the following is dis- 
         played:

                +=================================================+
                |    -----------------------------------------    |
                |          Average C1 for 1 round = .298          |
                |      Between Mean Velocities 2068 and 1939      |
                |        Calculated Muzzle Velocity = 2201        |
                |    -----------------------------------------    |
                |                                                 |
                |             Print C1 Data? ([Y] or N)           |
                +-------------------------------------------------+
                    Figure 22. Ballistic Coefficient Display 2.

           Press "N" to skip printing the table, and return to the Main 
         Menu. Again note that the information line shows the calculated 
         muzzle velocity and the inferred ballistic coefficient. You may 
         now go on to calculate ballistic data using the values obtained 
         using this routine; QBALL will use the calculated ballistic 
         coefficient and muzzle velocity until changed.

           Now, granted, the calculated muzzle velocity does not equal what 
         we know it has to be, that is, 2200 FPS, nor does the ballistic 
         coefficient exactly match what we know to be correct. If, however, 
         you run a range table using 2201 FPS and C1 = .298, and another 
         using 2200 FPS and C1 = .300, the difference is well within 
         QBALL's roundoff error. (Try it using the input data used to 
         develop the table on page 9 and see.)  You may use the calculated 
         muzzle velocity and still expect excellent practical accuracy.


         [ QBALL                                                       27 ]

                                     Chapter 4

                                   Printed Output
                                   """"""""""""""

         4.1 Printer Warnings.

           QBALL is internally configured to print to parallel printers, 
         only, specifically, to LPT1. If your printer is connected to 
         another parallel port, you will need to "swap" ports for the 
         duration of the QBALL session, or even reconfigure your printer 
         setup. 

           QBALL will detect whether or not your printer is on/on-line; it 
         is not specifically set up to detect "paper out."  Ensure that 
         your printer is properly set up before you try to print any QBALL 
         output!  (The error recovery routine dumps you back into the 
         previous menu, so you do end up losing some displayed data.)

           Some "generic" printer buffers will not respond properly to the
         print routines. If you are using a printer buffer, and you keep 
         getting the error message "Printer does not respond," then try 
         bypassing your buffer. Buffers which are built into printers do 
         not seem to cause any problem.

           While no extensive testing has been done, QBALL's print routines 
         have been found to work properly on an ALPS Allegro 24, an Epson 
         LQ-570, and a Tandy DMP-130.

         4.2 Screen Dumps.

           It is possible to print a screen's worth of tabular information 
         using the Shift-PrtScr key combination available in DOS. This 
         practice is not recommended, however, as you might very well lose 
         information which has already scrolled past on the screen. If your 
         computer is properly configured, however, you might want to print 
         out a graphics screen using Shift-PrtScr; see your DOS documenta- 
         tion, probably under "Graphics," for details.

         4.3 Printer Setup.

           You need not set up your printer to skip perforations in fanfold 
         paper; QBALL keeps track of the number of lines printed and issues 
         a formfeed (ASCII12) when appropriate. Continuation pages are 
         sequentially numbered, and each page will have the appropriate 
         column heading printed on it. (No formfeed is issued at the end of 
         any table.)

           You need not set your printer to indent from the left margin, 
         either. It is best, in fact, to use a printer setup of "left mar- 
         gin = 0," as QBALL is set up to indent each table an appropriate 
         number of spaces.

           You may also toggle the printer prompt completely off, replacing 
         it with a "press any key" prompt. This feature is useful if you do 
         not have a printer, or you are sure you won't want hard copy. 
         QBALL defaults to printer "ON," and displays the


         [ QBALL                                                       29 ]

           Typical printed "Infer Ballistic Coefficient..." output, using 
         the data from Chapter 3, second run, looks like this:

              ========================================================
              > Inferring Ballistic Coefficient for: Typical Firearm <
              --------------------------------------------------------
                   Given the following meteorological conditions:
          Temperature..........: 59 deg F Barometric Pressure....: 29.53"Hg
          Relative Humidity....: 78 %     Gun Altitude...........: 0 Feet
          Relative Air Density.: 1.000    Relative Sonic Velocity: 1.00
                   and the number of rounds shown, the ballistic
                   coefficient (C1) was computed using the veloci-
                                  ties indicated.
                   ----------------------------------------------
                   Round          V1            V2            C1
                   -----         ----          ----          ----
                     1           2068          1939          .298
                   ----------------------------------------------
                           Average C1 for 1 round = .298
                       Between Mean Velocities 2068 and 1939
                         Calculated Muzzle Velocity = 2201
                   ==============================================

                         Figure 25. Sample Printed Output,
                          Inferring Ballistic Coefficient.




















           [ Hint: Don't want to wait while the printer churns through ]
           [ a long range table?   Rather than choosing <P>rint in the ]
           [ Choose Next Output menu,  choose  <S>ave  instead.  Then, ]
           [ when you go off to lunch, or  whatever, issue the follow- ]
           [ ing command: COPY RGTABLE.nn PRN and let the machinery do ]
           [ the work while you do something else that's more fun..... ]


         [ QBALL                                                       31 ]

                                     Chapter 5
                  Configuring Display and Default Starting Values
                  """""""""""""""""""""""""""""""""""""""""""""""

         5.1  The Utilities and Configuration Menu.

           Should you wish to change some or all of QBALL's start-up data 
         or its current configuration, access QBALL's associated utilities, 
         or invoke a DOS shell, press <U> at the Main Menu, to display this 
         "Utilities Menu:"

                         +===============================+
                         |  ***   Utilities  Menu   ***  |
                         |  ---------------------------  |
                         |  Toggle <S>witches            |
                         |  Change Display <C>olors      |
                         |  <W>rite QBALL.INI Data       |
                         |  Invoke a <D>OS Shell         |
                         |  <R>ead a Range Table File    |
                         |  <T>ranslate a Graphics File  |
                         |  ---------------------------  |
                         |  <ESC> to  M A I N   M E N U  |
                         +-------------------------------+
                           Figure 26. The Utilities Menu.

                    Toggle <S>witches will change several of QBALL's opera- 
         ting settings; ...<C>olors is used to choose the display colors; 
         <W>rite QBALL.INI Data saves the current configuration; and 
         ...<D>OS shell permits "dropping" to the operating system without 
         exiting QBALL. <R>ead... and <T>ranslate... "shell out" to the two 
         associated QBALL utilities, RRTABLE.EXE and GRFXLATE.EXE; if the 
         utility program is not present in the current directory, the op- 
         tion is disabled. <R>ead and <T>ranslate are discussed in detail 
         in Chapter 8, QBALL's Associated Utilities, page 39.

         5.2  Toggle Active Switches.

           Press <S> to display this "Switch Toggle Menu."  Pressing the 
         appropriate key toggles that particular item; the current setting 
         is reflected immediately, and QBALL will act accordingly until it 
         is again changed.

                         +===============================+
                         |  *** Switch Toggle Menu ***   |
                         |  --------------------------   |
                         |  Yds/Mets <S>wap (Now Yards)  |
                         |  Graphics <G>rid (Now ON)     |
                         |  <P>rinter on/off (Now ON)    |
                         |  <N>oises on/off (Now ON)     |
                         |  --------------------------   |
                         |  <ESC> to Utilities Menu      |
                         +-------------------------------+
                         Figure 27. The Switch Toggle Menu.


         [ QBALL                                                       33 ]

           Figure 28 indicates "Now set -- " as the supplied default 
         settings. If you started QBALL with the "/b" switch, the values 
         will be, in order: 7, (white/light gray); 15, (high intensity 
         white); 7, (white/light gray); 0, (black); 0, (black).

         5.4  Using The Values You've Set.

           Having set the display colors and toggles as you like them, 
         <ESC> to the Utilities Menu, where you may:

                               <W>rite QBALL.INI Data
         or, you may:
                             <ESC> to M A I N   M E N U.

           If you're sure of the values you've entered, press <W> to write 
         the new QBALL initialization data to the end of QBALL.EXE. (And 
         remember, if you change your mind, there's nothing to stop you 
         from running Configuration again.)

           If you'd like to use the values for this session only, perhaps 
         to see how they work out, press <ESC>. If you decide later to save 
         your "temporary" setup, choose <U> from the Main Menu, then choose 
         <W> immediately from the Configuration Menu. QBALL doesn't care if 
         there's a delay between choosing configuration values and writing 
         the configuration  data; it will quite cheerfully write that data 
         using whatever values are in effect at the time the <W> option is 
         chosen.

           If you choose the <W> option, remember that the QBALL.INI data 
         includes a good bit more information than just the display colors 
         and toggle status. It also controls the starting text and values 
         for the:
                        a. Cartridge/bullet identifier;
                        b. Meteorological conditions; and
                        c. Sight height.

           Upon invocation of the <W>rite... option, the new configuration 
         data will include the text or values of these items which are 
         currently in effect. This allows you to "tailor" your copy of 
         QBALL to match your own conditions: your weapon, and the actual 
         (or anticipated) metro which is encountered at your own firing 
         range.

           Specific times you might very well want to use metro values 
         other than standard are, for example, if your range is not at sea 
         level, or if you're shooting during the summer, when the tempera- 
         ture might very well exceed 59ø Fahrenheit. You can configure 
         QBALL to start with the altitude of your range, or an expected 
         temperature, without the hassle of changing the values after 
         start-up.

           In similar fashion, you may configure QBALL to start with the 
         name of your own weapon, say, "Ruger M77/.270" and the actual 
         measured height of that weapon's sight, say, 1.25 inches.


         [ QBALL                                                       35 ]

                                     Chapter 6
                          Recalling Saved Trajectory Data
                          """""""""""""""""""""""""""""""

           Assuming that one or more trajectory graphics files exist on/in 
         the current disk/directory, QBALL's Main menu allows you to access 
         them without having to work your way to the graphics display 
         routines. At the Main menu, press <R>ecall Saved Trajectory Data 
         to access this informational screen and the Recall Trajectory Data 
         menu:

                             Recall Saved Graphics Data
                             --------------------------
                 EGA_SAV.0                          Typical Firearm
                 --------------------------------------------------
           Muzzle Velocity      2700 FPS   Ballistic Coefficient     .300
           Bullet Weight      180 grains   Zero Range           200 Yards
           Metro conditions     Standard   Maximum Range        300 Yards

                       +===================================+
                       |  *** Recall Trajectory Data ***   |
                       |  ------------------------------   |
                       |  <R>ecall <0> thru <1>            |
                       |  Display Trajectory <G>raphic     |
                       |  Use Displayed As <D>efault       |
                       |  ------------------------------   |
                       |  <ESC> to M A I N   M E N U       |
                       +-----------------------------------+

                 Figure 29. Recall Trajectory Data Display and Menu

           For purposes of this example, it is assumed that you have copied 
         the two saved trajectory files from the distribution disk, and 
         that one trajectory file was saved when you ran the "tutorial" in 
         Chapter 2.

           The information shown above the menu specifies the saved file- 
         name, the identifier, and sufficient other information to permit 
         you to decide which one you're looking at. (If you are using a 
         CGA-equipped computer, the specified filename will be 
         "CGA_SAV.0.") This routine always displays *GA_SAV.0 first. You 
         may recall the others by pressing <R>ecall, then the <number>; 
         e.g., to examine EGA_SAV.1, press <R>, then press <1>.

           Option <G> and option <D> will reset the input data. If you 
         don't want to change the input data, press <ESC> to return to the 
         Main menu.


         [ QBALL                                                       37 ]

                                     Chapter 7
                                   File Handling
                                   """""""""""""

           QBALL does perform disk reads and disk writes. Running QBALL 
         from a floppy disk is possible, but reads and writes are necess-
         arily slow. It is recommended, therefore, that you run QBALL 
         from a hard disk, or, if at all possible, a RAM disk.

           That said, QBALL deals with the following disk files.

         QBSHELIT.BAT batch file.
          
           When first started, QBALL writes a special batch file to the 
         current disk or into the current directory: QBSHELIT.BAT. This 
         batch file does several things, the most visible of which is 
         setting the DOS prompt within the shell. That prompt looks like 
         this:

                     [ Exit >> QBALL ] [drive:]\[directory] > _

           Additionally, QBALL will look for this batch file when being 
         started. If QBSHELIT.BAT is found, you'll be shown "QBALL is 
         already loaded!" and get dumped back to the DOS prompt; this 
         prevents starting a second copy of QBALL while you're in a DOS 
         shell. (If you're running QBALL from a floppy, ensure that there 
         is a copy of COMMAND.COM on that floppy! Otherwise, you'll be able 
         to run only one command in the shell.)

           QBSHELIT.BAT is erased upon normal exit from QBALL, i.e., when 
         you <Q>uit... QBALL from the Main menu. If, however, you break out 
         of QBALL using, say, Cntrl-Alt-Del to reboot, you will be unable 
         to start QBALL again until QBSHELIT.BAT is erased, which you'll 
         have to do manually in this case. Log onto the disk or directory 
         where QBALL resides, and enter this command:

                           DEL QBSHELIT.BAT (+ [enter]).

         QBALL will now start normally.

           Under ordinary circumstances, the operation of QBSHELIT.BAT is
         completely transparent; you won't even know it's there.

         Graphics Trajectory Data.

           Trajectory data saved with QBALL versions 2.09 and preceding are 
         not compatible with those saved with QBALL 2.20, and QBALL 2.20 
         will simply ignore them. The only workaround, if you've got some 
         favorites, is to "start from scratch" with version 2.20 and regen- 
         erate the graphics files. Please note, too, that CGA-equipped 
         computers are directed to ignore EGA graphics files; EGA compu- 
         ters, to ignore CGA graphics files. It is possible to translate 
         from one format to the other; see Chapter 8, QBALL's Associated 
         Utilities, page 39.


         [ QBALL                                                       39 ]

                                     Chapter 8
                            QBALL's Associated Utilities
                            """"""""""""""""""""""""""""

           Two custom utilities are included with QBALL 2.20: RRTABLE.EXE 
         and GRFXLATE.EXE. Both may be accessed from the QBALL Utilities 
         menu, and either may be started from the command line, as well. 
         Once loaded, the procedures are exactly the same; the remainder of 
         this chapter assumes that you are accessing the utilities from 
         within QBALL.

         8.1 Range Table Reader (RRTABLE.EXE).

           In order to access the Range Table Reader from within QBALL, 
         both of the following conditions must be true: first, QBALL.EXE 
         and RRTABLE.EXE are on/in the same disk/directory; and second, a 
         saved range table--" RGTABLE.[ext]"-- exists on/in that disk/di- 
         rectory. If either of these conditions is untrue, QBALL disables 
         the <R>ead a Range Table File option in the Utilities menu, i.e., 
         the option is displayed in low-intensity video.

           At the Utilities menu, assuming that the option is activated, 
         press "<R>." After a short pause, the following screen will 
         appear:

          +==============================================================
          ===== -       - -   ------  ----------  ---  ------------------
          |   | |-+  -+ | |   +-+| -   | |-|+-+|  |-   +-+|- |-|| ||- +-+
          |   | | | +-| | |   ||_|_|   | | ||_||__|__  ||_|__| ||_||__||_
          |___| |_| |_| | |                                           1.0
          -- |_----------------------------------------------------------
          ---------------------------------------------------------------

          1 QBALL-generated Range Table found:
          ------------------------------------
          RGTABLE.01
          ------------------------------------
          Enter file EXTENSION ("0" exits):

                       Figure 31. QBALL's Range Table Reader

           There is one range table available to be read. Enter "1" (or 
         "01") to examine that range table. Looks a lot like the printed 
         output from Chapter 4, doesn't it? It should: it's the same file, 
         stripped of blank lines, form feeds, and page continuation head- 
         ers. If this saved range table were longer, you would use the up- 
         and down arrows, PgUp, PgDn, Home, and End keys to navigate. Press 
         <ESC> to return to the opening screen as shown in Figure 31. If 
         you had more than one range table available, you could then read 
         one (or more) additional tables. When you're finished looking at 
         range tables, enter "0" to return to QBALL.


         [ QBALL                                                       41 ]

           After a short pause, during which GRFXLATE will report that it 
         is, indeed, translating, you will be asked if you wish to trans- 
         late another file. A "no" response returns you to QBALL.

           If you invoke GRFXLATE and decide that you don't want to 
         translate any files at all, press <ESC>, which returns you to 
         QBALL. The newly-translated EGA_SAV.2 is now fully usable by 
         QBALL's graphics routines.

                                     ----------

           Both RGTABLE.EXE and GRFXLATE.EXE may be used as stand-alone 
         utilities, invoked from the command line, as noted above. Their 
         use, either accessed from within QBALL or from the command line 
         requires a series of disk reads, and in the case of GRFXLATE.EXE, 
         disk writes. These are necessarily slow on floppy disks. Further- 
         more, you may discover that a floppy doesn't have sufficient space 
         for QBALL, its associated utilities, and any saved data. 
         Experimentation is in order.

           Note, too, that both RGTABLE.EXE and GRFXLATE.EXE obtain their 
         start-up colors from QBALL.EXE. If you have temporarily changed 
         QBALL's display colors, those in the utilities display won't 
         match.


         [ QBALL                                                       43 ]
                                     Appendix A

                                      Glossary

         absolute zero - Properly, that temperature at which all molecular 
         motion ceases. For practical purposes, -459.67d Fahrenheit, or 0d 
         Rankine.

         air density - The mass (or loosely, the weight) of a unit volume 
         of air.

         air resistance - The retardation of a bullet's forward flight due 
         to the atmosphere.

         altitude - The vertical distance above or below sea level. 
         Altitudes above sea level are taken as positive; those below, as 
         negative.

         ballistics - The study of moving projectiles. Commonly, what is 
         meant is exterior ballistics: that portion of the bullet's flight 
         between the muzzle and the point of impact. (Internal ballistics 
         studies events prior to the bullet's exit from the muzzle; term- 
         inal ballistics, the interaction between the bullet and the 
         target.)

         ballistic coefficient - The ratio of the sectional density of a 
         projectile to its coefficient of form. A measure of how well a 
         bullet retains its velocity. Commonly supplied by reloading 
         manufacturers, or it may be derived from their ballistic tables. 
         In QBALL, the ballistic coefficient is always taken at standard 
         metro. The program corrects for nonstandard conditions, but does 
         not display the corrected ballistic coefficient(s). See also: 
         standard metro.

         ballistic efficiency - The relative ability of a bullet in flight 
         to overcome air resistance.

         bore - The inside of a firearm's barrel. In rifled firearms, the 
         bore diameter is the original dimension of the barrel before the 
         rifling grooves are cut or swaged in it. Bore diameter may also be 
         taken as the transverse dimension between the lands of the rif- 
         ling. See also: grooves, lands, rifling.

         brass - Alloy of copper and zinc commonly used in the fabrication 
         of cartridge cases. Also, one or more cartridge cases containing 
         neither powder, primer, nor bullet.

         bullet - The actual projectile in small arms ammunition. Commonly 
         corrupted to refer to the entire cartridge.

         bullet weight - Weight of the actual projectile, usually stated in 
         grains. See also: grain.


         [ QBALL                                                       45 ]

         Ft.-Lbs. (also FtLbs and Ft#) - Foot pounds. A unit of energy 
         equal to the effort required to lift one pound a vertical distance 
         of one foot. 

         form factor - A multiplier which relates a bullet's shape to that 
         of the standard projectile used to prepare a particular ballistic 
         table.

         grain - A unit of weight equal to 1/7000 of a pound, or 1/(437.5) 
         ounces. May also refer to an individual particle, or kernel, of 
         powder. In cartridge specifications, always refers to the weight 
         of the powder charge, never to individual particles.

         grooves - Swaged impressions or cuts spiraled through a bore to 
         impart spin to projectiles. See also: lands.

         group - The pattern made at the target by a number of shots fired 
         at a single point of aim and (usually) a common sight setting. 
         Usually measured from center-to-center of the two most widely 
         spaced holes.

         gun - In popular usage, refers to firearms, generally. Properly, a 
         type of artillery or naval ordnance.

         handgun - A firearm designed to be held and fired with one hand.

         hold off - The distance a shooter must shift his point of aim to 
         the left or right to compensate for wind deflection.

         hold over - The distance a shooter must raise his point of aim to 
         be on target when his firearm is zeroed at a lesser range.

         horizontal fire - That type of fire occurring if the firearm's 
         barrel is not elevated significantly above or below the horizon- 
         tal. Generally taken as 1 degree of arc or less.

         Ingalls' Tables - A set of ballistic tables first calculated by 
         Col. J. M. Ingalls in 1918. Probably the most widely used tables 
         for small arms ballistics calculations.

         iron sights - In popular usage, metallic sights.

         lands - Those portions of a rifled bore not cut away by rifling 
         grooves. See also: grooves.

         lead - (leed) How far ahead of a moving target a shooter must aim 
         to be assured of hitting it.

         lead - (led) Soft, dense, silvery-gray metal with relatively low 
         melting point which forms the basis for many bullets.

         line of departure - An imaginary line formed by extending the axis 
         of a firearm's bore in a downrange direction.


         [ QBALL                                                       47 ]

         point of aim - That downrange point with which a firearm's sights 
         are aligned.

         point of impact - That point which a bullet actually strikes. In 
         most cases, considered in relation to point of aim.

         powder - The propellant material used in firearms. Usually not in 
         powder form, but in the form of small rods, spheres, or flakes.

         primer - Impact-sensitive component of a cartridge which ignites 
         the powder charge upon being struck by the firing pin or the 
         striker of a firearm.

         projectile - A bullet, shell, golfball, rock, or other object 
         shot, hit, thrown, or hurled in space; a projectile receives a 
         single impetus, and continues in motion by its own inertia. A 
         bullet is not properly a projectile until it is in motion.

         relative air density - The density of air at the measured metro 
         divided by the density of air at standard metro, expressed as a 
         dimensionless decimal fraction; e.g., 1.000.

         relative sonic velocity - The velocity of sound at the measured 
         metro divided by the velocity of sound at standard metro, ex- 
         pressed as a dimensionless decimal fraction; e.g., 1.000.

         remaining energy - A projectile's energy in foot-pounds at a given 
         range.

         remaining velocity - A projectile's velocity in FPS at a given 
         range.

         rifling - The spirally-cut or swaged grooves in a firearm's bore, 
         taken collectively with the resulting lands, which impart a stab- 
         ilizing spin to the bullet. See also: grooves, lands.

         round - One complete cartridge. May also refer to the sequential 
         number of a shot in a number of shots; e.g., "Round #3."

         scope - Optical or telescopic, as opposed to metallic, sights.

         sight height - The measured vertical distance between the horiz- 
         ontal centerline of the sights and the axis of the bore.

         sighting in - The process of firing to determine point of impact 
         at a given range and adjusting the sights so that the point of 
         impact has the desired relationship to the point of aim. See also: 
         zero.

         sight radius - The distance between the rear and the front sight, 
         on those weapons equipped with iron (non-optical) sights.

         small arms (also smallarms) - Rifles, pistols, or revolvers, 
         generally.


         [ QBALL                                                       49 ]

                                     Appendix B

                 Example of Ballistic Coefficient from Tabular Data

         The following tables summarize the determination of a ballistic 
         coefficient using tabular values. The values for Table B1 are 
         taken from data published in the 1990 edition of The Gun Digest, 
         page 229; the values for Table B2 were calculated using QBALL.

              +-----------------------------------------------------+
              | From Gun Digest Table for 30-06 Spfd, 180 gr bullet:|
              |                                                     |
              |                          Range in Yards             |
              |               ------------------------------------  |
              |               Muz     100      200     300     400  |
              |               ------------------------------------  |
              | Velocity      2700   2469     2250    2042    1846  |
              | Energy        2913   2436     2023    1666    1362  |
              | Trajectory    -1.5    2.5      0.0    -9.3   -27.0  |
              +-----------------------------------------------------+
                     Table B1. Data Taken From Published Table.

           Using the "Infer Ballistic Coefficient" routines in QBALL, 
         entering 100 and 200 yards for the required ranges, and using the 
         velocities as published, QBALL reports that C1 (the ballistic 
         coefficient) is equal to 0.384.

           Returning to QBALL's Main Menu, selecting the Calculate 
         Ballistic Data option, and entering the appropriate values for 
         muzzle velocity, bullet weight, and zero range, QBALL produces 
         the data shown in Table B2.
         
              +-----------------------------------------------------+
              | QBALL Data Table for 30-06 Spfd, 180 gr bullet:     |
              |                                                     |
              |                          Range in Yards             |
              |               ------------------------------------  |
              |               Muz     100      200     300     400  |
              |               ------------------------------------  |
              | Velocity      2700   2470     2251    2043    1846  |
              | Energy        2913   2437     2024    1668    1362  |
              | Trajectory    -1.5    2.1      0.0    -9.0   -26.2  |
              +-----------------------------------------------------+
                       Table B2. Data Calculated Using QBALL.

           The maximum variations are: Velocity, 1 FPS; Energy, 2 FtLbs; 
         and Trajectory 0.8 inches. It may be seen, therefore, that QBALL 
         can produce results in substantial agreement with published data.


         [ QBALL                                                       51 ]

                                     Appendix C

                         Typical Saved Trajectory Data File

           The following table represents, in part and in somewhat com- 
         pressed form, the EGA_SAV.0 file provided in the distribution 
         package. The header data contains data as detailed in the key, 
         below. The first data column is the range; the second, the 
         trajectory height relative to the sight line. Note that the range 
         increment is 1/100 of the maximum range. This is true if the 
         computer used is equipped with an EGA card/monitor. CGA_SAV.* 
         tables use a range increment of 1/50 of the maximum range.

               +----------------------------------------------------+
               |  Yards                                             |
               |  1                                                 |
               |  2700      1876.864  .3        200       2.580286  |
               | -10.07583  111       300       166.53              |
               |  180       Typical Firearm                         |
               |  59        0         29.53     78                  |
               |              0                           -1.0      |
               |              3                           -0.8      |
               |              6                           -0.6      |
               |              9                           -0.5      |
               |  - - - - - - - - - - - - - - - - - - - - - - - -   |
               |            (major portion of data omitted)         |
               |  - - - - - - - - - - - - - - - - - - - - - - - -   |
               |            291                           -8.8      |
               |            294                           -9.2      |
               |            297                           -9.6      |
               |            300                          -10.1      |
               |  06-01-1993    12:00:00                            |
               |  [end EGA_SAV.0 ]                                  |
               +----------------------------------------------------+
                       Table C1. Saved Trajectory Data File.

         Key to values listed in the table:

         [Unit of Range Measure]
         [Sight Height]
         [Muzzle velocity] [Terminal velocity] [Ballistic coefficient]
         [Zero range] [Max Height][Min Height] [Range at Max Height]
              [Max Range] [Metro Constant]
         [Bullet weight] [Identifier]
         [Fahrenheit Temperature] [Gun Altitude] [Barometric Pressure]
              [Relative humidity]
                 [Range]          [Bullet position ñ sight line]
         [Date] [Time]
         [End of file indicator with Filename and number]

                  +----------------------------------------------+
                  | Graphics files generated by QBALL v 2.20 are |
                  | not compatible with any other QBALL version. |
                  +----------------------------------------------+


         [ QBALL                                                       53 ]

                                     Appendix D

                               Selected Bibliography

         Davis, William C., Jr. "Ballistics on the Home Computer," The 
         American Rifleman, CXXXI, 6 (June, 1983), p. 36.

         Davis, William C., Jr. "Ballistics on A Pocket Calculator," The 
         American Rifleman, CXXXV, 6 (June, 1987), p. 42.

         Davis, William C., Jr. "Calculate Ballistic Coefficients," The 
         American Rifleman, CXXXVII, 3 (March, 1989), p. 44.

         Davis, William C., Jr. "What Is The Ballistic Coefficient?," The 
         American Rifleman, CXXXVII, 3 (March, 1989), p. 12.

         Federal 1992 Ammunition [Catalog and Guide]. Anoka: Federal 
         Cartridge Company, 1991.

         Hodgdon Basic Data Manual, Shawnee Mission: Hodgdon Power Company, 
         Incorporated, 1987

         Ramage, C. Kenneth (ed.). Lyman Reloading Handbook. 46th ed. 
         Middlefield: Lyman Products Corporation, 1982.

         Reiber, Ron L., and Heers, Edward A. (eds.). Hornady Handbook of 
         Cartridge Reloading, Rifle-Pistol. 3d ed. Grand Island: Hornady 
         Manufacturing Company, 1980.

         Reloaders' Guide for Hercules Smokeless Powders. Wilmington: 
         Hercules Incorporated, 1988.

         Remington Firearms, Ammunition, Clothing and Accessories Catalog. 
         Wilmington, Remington Arms Company, Inc., 1992.

         Speer Reloading Manual #11, Lewiston: Omark Industries, 
         Incorporated, 1987

         Warner, Ken (ed.). Gun Digest, 1990. 44th ed. Northbrook: DBI 
         Books, 1989.

         Warner, Ken (ed.). Gun Digest, 1991. 45th ed. Northbrook: DBI 
         Books, 1990.

         Warner, Ken (ed.). Gun Digest, 1992. 46th ed. Northbrook: DBI 
         Books, 1991.

         Warner, Ken (ed.). Gun Digest, 1993. 47th ed. Northbrook: DBI 
         Books, 1992.

         Winchester Ammunition Product Guide. East Alton: Winchester/Olin 
         Corporation, 1993.


         [ QBALL                                                       55 ]

                                     Appendix E

                                   Error Analysis

           Results from several QBALL runs were compared with comparable 
         data from two sets of published tables: the Speer Reloading Manual 
         #11, and the Hornady Handbook of Cartridge Reloading, 3d edition. 
         Two questions were to be answered: first, how well do velocity 
         figures compare between the three sources?; second, are the 
         trajectories found by the different sources comparable?

           Some difficulty was experienced in the choice of ballistic coef- 
         ficients and velocities due to the differences between the two 
         published sources. Speer, for example, rounds all ballistic coef- 
         ficients to two decimal places, while Hornady carries three. In 
         addition, when comparable values of ballistic coefficients could 
         be found, the Hornady tables quite often did not have the spread 
         of velocities available in the Speer manual.

           The following table summarizes as-comparable-as-possible velo- 
         city data from all three sources. While severely limited, the data 
         shows that the results obtained from QBALL are in general agree- 
         ment with the two published sources.

           +------------------------------------------------------------+
           |          Remaining Velocity, Conditions as Shown           |
           |          =======================================           |
           |            [ Range = 200 yards, Standard Met ]             |
           +------------------------------------------------------------+
           |         MuzVel = 2100     MuzVel = 2500     MuzVel = 3300  |
           |            C1 = .12          C1 = .26          C1 = .50    |
           |        ---------------   ---------------   --------------- |
           | QBALL        1112              1879               2899     |
           | SPEER        1102              1872               2895     |
           | HORNADY      1126              1875               2892     |
           +------------------------------------------------------------+
            (Key: MuzVel = Muzzle Velocity  C1 = Ballistic Coefficient)

            Table D1.  Remaining Velocities With Given Inputs. Note should
            be made that the Hornady ballistic coefficients were actually
            .122, .259, and .496 for the three sets of data shown. This
            accounts for the apparent "high-on-low" spread of values seen
            here. QBALL was run with the ballistic coefficients as shown.

           An examination of the data in Table D1 indicates that remaining 
         velocities found using QBALL will be, on average, 0.47% high rel- 
         ative to the Speer data, and 0.42% low relative to to the Hornady 
         data. The Hornady data, however, must be considered suspect, as 
         the actual ballistic coefficients available in the Hornady table 
         do not exactly match those specified. Even so, it would appear 
         that QBALL's velocity results are certainly within one or two 
         percent of published data. In practical terms, there is probably 
         that much variation in velocity between successive rounds in a 
         string, if not more. QBALL, it would appear, can produce velocity 
         figures which are accurate enough for practical purposes.


         [ QBALL                                                       57 ]

                                     Appendix F

         QBALL user Jim McCausland, out Washington State way, provided sev- 
         eral sets of data developed with other ballistics programs, all 
         believed to be "commercial" in nature (i.e, they aren't "share- 
         ware." The following tables contain the information which Jim sent 
         along, with as-comparable-as-possible QBALL data.

          +--------------------------------------------------------------+
          | Program: Sierra Ballistics.                                  |
          | Input Data:                                                  |
          |     Ballistic Coefficient (C1)....... .299                   |
          |     Bullet Weight.................... 130 grains             |
          |     Zero Range....................... 200 yards              |
          |     Maximum Range.................... 450 yards              |
          |     Range Increment..................  50 yards              |
          |     Sight Height..................... 0.9 inches             |
          |     Crosswind........................ -- no wind --          |
          |     Metro............................ Standard               |
          |--------------------------------------------------------------|
          |Range R e m a i n i n g  Total Path/Sight Line Defl'n Time    |
          |Yards Velocity   Energy  Drop  M.O.A.   Inches 0 MPH  Flght   |
          |--------------------------------------------------------------|
          |Sierra Ballistics Reports:                                    |
          |                                                              |
          |    0  3000.0     2597   0.00            -0.90 +0.00 0.000000 |
          |   50  2840.3     2328   0.46  +-----+    1.07 +0.00 0.051389 |
          |  100  2686.3     2083   2.00  | Not |    1.96 +0.00 0.105659 |
          |  150  2537.4     1858   4.74  |Given|    1.66 +0.00 0.163151 |
          |  200  2393.3     1653   8.83  +-----+       0 +0.00 0.224021 |
          |  250  2253.9     1466  14.43            -3.17 +0.00 0.288606 |
          |  300  2119.1     1296  21.74            -8.05 +0.00 0.357243 |
          |  350  1989.0     1142  30.98           -14.85 +0.00 0.430310 |
          |  400  1863.9     1003  42.41           -23.85 +0.00 0.508220 |
          |  450  1744.1      878  56.34           -35.35 +0.00 0.591424 |
          |                                                              |
          |QBALL Reports:                                                |
          |                                                              |
          |    0    3000     2598    0.0     0.0     -0.9  0.0   0.000   |
          |   50    2840     2329    0.5     2.1      1.1  0.0   0.051   |
          |  100    2686     2083    2.1     2.0      2.0  0.0   0.106   |
          |  150    2537     1858    4.9     1.1      1.6  0.0   0.163   |
          |  200    2393     1653    9.0     0.0      0.0  0.0   0.224   |
          |  250    2254     1466   14.6    -1.3     -3.2  0.0   0.289   |
          |  300    2119     1296   22.0    -2.7     -8.1  0.0   0.357   |
          |  350    1989     1142   31.4    -4.3    -15.0  0.0   0.431   |
          |  400    1863     1002   42.7    -6.0    -23.8  0.0   0.508   |
          |  450    1744      878   56.9    -7.9    -35.5  0.0   0.591   |
          +--------------------------------------------------------------+
                   Table F1. Sierra Ballistics and QBALL Compared

         Summary of absolute differences. Remaining Velocity: 0.9 FPS; Re- 
         maining Energy: 1 FtLb; Total Drop: .56 inches; Path/Sight Line: 
         0.15 inches; Time of Flight: 0.000424 seconds.


         [ QBALL                                                       59 ]

          +--------------------------------------------------------------+
          | Program: BALTEC.                                             |
          | Input Data:                                                  |
          |     Ballistic Coefficient (C1)....... .295                   |
          |     Bullet Weight.................... 130 grains             |
          |     Zero Range....................... 200 yards              |
          |     Maximum Range.................... 600 yards              |
          |     Range Increment..................  50 yards              |
          |     Sight Height..................... 0.9 inches             |
          |     Crosswind........................  10 MPH                |
          |     Metro............................ Standard               |
          |--------------------------------------------------------------|
          | Range R e m a i n i n g Total Path/Sight Line Defl'n    Time |
          | Yards Velocity   Energy Drop* M.O.A.   Inches 10 MPH*  Flght*|
          |--------------------------------------------------------------|
          | BALTEC Reports:                                              |
          |                                                              |
          |     0    3000     2598    0.0    0.0    -0.9  -0.00    -.000 |
          |    50    2838     2325    0.5   -2.2     1.1   0.24    0.051 |
          |   100    2682     2076    2.1   -2.0     2.0   1.04    0.106 |
          |   150    2531     1850    4.9   -1.1     1.7   2.36    0.163 |
          |   200    2386     1643    9.0    0.0     0.0   4.26    0.224 |
          |   250    2245     1454   14.7    1.3    -3.2   6.91    0.289 |
          |   300    2109     1283   22.1    2.7    -8.2  10.28    0.358 |
          |   350    1977     1128   31.5    4.3   -15.0  14.38    0.432 |
          |   400    1850      988   42.9    6.0   -24.0  19.27    0.509 |
          |   450    1730      864   57.2    8.0   -35.8  25.34    0.594 |
          |   500    1616      754   74.4   10.1   -50.6  32.43    0.684 |
          |   550    1507      656   94.7   12.4   -68.4  40.40    0.780 |
          |   600    1407      572  119.2   15.1   -90.4  49.73    0.883 |
          |                                                              |
          | QBALL Reports:                                               |
          |                                                              |
          |     0    3000     2598    0.0    0.0    -0.9    0.0    0.000 |
          |    50    2838     2325    0.5    2.2     1.1    0.2    0.051 |
          |   100    2682     2076    2.1    2.0     2.0    1.0    0.106 |
          |   150    2531     1850    4.9    1.1     1.7    2.4    0.163 |
          |   200    2386     1643    9.0    0.0     0.0    4.3    0.224 |
          |   250    2245     1454   14.7   -1.3    -3.2    6.9    0.289 |
          |   300    2109     1283   22.1   -2.7    -8.2   10.3    0.358 |
          |   350    1977     1128   31.5   -4.3   -15.0   14.4    0.432 |
          |   400    1850      988   42.9   -6.0   -24.0   19.3    0.509 |
          |   450    1730      864   57.2   -8.0   -35.8   25.3    0.594 |
          |   500    1616      754   74.4  -10.1   -50.6   32.4    0.684 |
          |   550    1507      656   94.7  -12.4   -68.4   40.4    0.780 |
          |   600    1407      572  119.2  -15.1   -90.4   49.7    0.883 |
          |--------------------------------------------------------------|
          | *BALTEC requires two  tabular displays. Combined data shown. |
          +--------------------------------------------------------------+
                        Table F3. BALTEC and QBALL Compared

         Summary of absolute differences. Deflection for 10 MPH crosswind: 
         0.04 inches.

         Available with BALTEC, unavailable with QBALL. Bullet Momentum in 
         Lb-Seconds; Maximum Ordinate, Maximum Height, both in inches.


         [ QBALL                                                       61 ]

                                     Appendix G

           QBALL error messages, with a description of the circumstances 
         under which they will be encountered.

                                     ----------

         AMMO.DAT Not Found: You've called for bullet lookup and the required
         bullet data file is not on/in the current disk/directory.

         Cannot sort by [key]: The required bullet lookup index file is not
         on/in the current disk/directory, or the listing is already sorted
         on the requested sort [key].

         Disk Full: Insufficient space remains on/in the default disk/dir- 
         ectory to write the desired file. This most commonly occurs when 
         running QBALL from a floppy disk which has other files on it. Copy 
         QBALL.EXE to a fresh disk, and start over.

         Enter  0.000 < Ballistic Coefficient < 1.000: You're trying to 
         enter a value outside the acceptable range of between 0.000 and 
         1.000. Ballistic coefficients are, by definition, greater than 
         zero and less than unity. 

         Enter  25 < Barometric Pressure < 35: You're attempting to enter a 
         barometric pressure value which is out of range. (These are rea- 
         sonable "real world" values.) 

         Enter  Bullet Diameter > 0: In determining sectional density, the 
         bullet must have a diameter.

         Enter  0 < Bullet Weight < 1000: You're attempting to enter a zero 
         bullet weight. (1000 gr = 2.3 ounces.) 

         Enter  -1312 < Gun Altitude < 29028: You're attempting to enter a 
         gun altitude value which is out of range. (-1312 is the altitude 
         of The Dead Sea; 29028, of Mount Everest.) 

         Enter  0 < Gun Weight <= 30 lbs: In determining gun free recoil, 
         you're attempting to enter an out-of-range gun weight.

         Enter Lbs + [space] + 0 <= Ounces < 16: In determining gun free 
         recoil, you're entering an incorrect format for pounds/ounces 
         data. Enter whole pounds, then a space, then ounces.

         Enter  0 < Powder Weight < 200 gr: In determining gun free recoil, 
         you're attempting to enter a zero propellant weight. 

         Enter  Range greater than zero: You're really trying to enter a 
         range of "zero." Range = 0 is valid only when inferring ballistic
         coefficients.


         [ QBALL                                                       63 ]

         Maximum Deviation Reset to Sight Height: Not an error, really, but 
         a warning. In determining point-blank range, the sight height is a 
         built-in deviation.

         Not Enough Velocity Remains - Input Greater MV: QBALL is unable to 
         complete a computation because the remaining velocity is less than 
         300 FPS.

         Printer does not respond: Your printer is off or off-line.

         QBALL is already loaded!: You're attempting to load a second copy 
         of QBALL from within the DOS Shell. Alternatively, QBSHELIT.BAT 
         wasn't deleted from the current disk/directory. See page 34.


         [ QBALL                                                       65 ]

                                     Appendix H

                              Default Starting Values

           QBALL stores its initialization data in binary format at the 
         "tail end" of QBALL.EXE. That data is used to set the display col- 
         ors and several of the values with which QBALL starts. As supplied 
         that data is as follows: 

         "Typical Firearm" 15 10 7 1 7 "Yards " "Meters" 1 -1 59 0 29.53 _
                               78 1 -1 -1

         In order, the individual entries translate as follows: 

         "Typical
         Firearm"      Cartridge/bullet identifier
               15      Foreground (text) color ( = HI white    )
               10      Highlighted text color  ( = HI green    )
                7      Title/Info line color   ( = white       )
                1      Background color        ( = blue        )
                7      Help display background ( = white       )
         "Yards "      Unit of range measure (trailing space necessary)
         "Meters"      Alternate unit of range measure
                1      Sight height in inches
               -1      Noises on or off        ( = on  )
               59      Air temperature, degrees Fahrenheit
                0      Gun altitude in feet
            29.53      Barometric pressure in inches of mercury
               78      Relative humidity, in percent
                1      Relative air density at given metro
               -1      Graphics grid on or off ( = on  )
               -1      Print prompt on or off  ( = on  ).


           Invoking the "<W>rite .INI Data" option from QBALL's Utilities 
         Menu will replace the existing intialization data with whatever 
         values are in effect when the option is invoked. This will cause 
         DOS to redate the QBALL.EXE file, and may (or may not) change 
         QBALL.EXE's size on disk. If you regularly use a virus-scanning 
         utility, it may react to these changes. If your virus detector can 
         be directed to ignore certain files, you may wish to instruct it 
         to ignore QBALL.EXE.


         [ QBALL                                                       67 ]

                                       Index

              -A-                             ballistic coefficient 7
         Already Loaded! 34, 37               bullet [L]ookup 7
         AMMO.DAT 21                          bullet diameter 20
         Automatic 3                          bullet weight 7
           file renaming 38                   default metro 7
           graphics detect 3                  gun weight, decimal pounds 20
           printer detect 3                   gun weight, pounds/ounces 20
                                              maximum deviation 17
              -B-                             maximum range for table 9
         Ballistic Coefficients 23            muzzle velocity 7
           [L]ookup 7                         powder (propellant) weight 20
           entry 7                            range, slant angle of fire 19
           example from tabular data 49       range increment, slant angle
           inferring (calculating) 23-26        of fire 19
           valid limits 16                    range increment for table 9
         Bibliography 53                      target above/below gun 19
         Bullet [L]ookup 7                    wind direction 18
           AMMO.DAT 21                        wind velocity 18
           changing input data 16             zero range 8
           index (*.NDX) files 21           Default values 4
           initial data entry 7               changing/saving 33
           using and display 21-22            metro 4
         Bullet Weight                        range unit 4
           [L]ookup 7                         sight height 4
           valid limits 16                    supplied 65
                                            DOS Shell 34
              -C-
         Cartridge/Bullet Identifier 15
         Changing Input Data 15-16               -E-
           ballistic coefficient 16         Error Analysis 55-56
           Bullet [L]ookup 15               Error Messages 61-63
           bullet weight 16                 Exiting QBALL 5
           Cartridge/Bullet
             Identifier 15                       -F-
           metro 16                         Files 1
           muzzle velocity 16                 automatic renaming 38
           sight height 16                    copying 1
           swap range units 16                distribution 1
         Chronograph 23                       QBSHELIT.BAT 37
           using single 26                    required 1
         Configuring... 31                    trajectory data 51
           alert noises 32                    trajectory incompatible 37
           graphics grid 32                 Free Recoil Velocity, Energy 20
           printer on/off 32                  data entry 20
           range units 32                     examples of... 21
           saving configuration data 33       gun weight 20
           screen colors 32                   powder (propellant) weight 20
                                              valid data limits 20
              -D-
         Data Entry 7