CONTENTS



      1.  INTRODUCTION..................................................   2


      2.  PROTOCOL FILE TRANSFERS.......................................   3
          2.1   Graphic File Transfer Display...........................   3
          2.2   Choosing the Best Protocol..............................   4
          2.3   ZMODEM-90(TM)...........................................   4
          2.4   Sending files with ZMODEM...............................   6
                2.4.1   File Maintenance with ZMODEM....................   6
                2.4.2   MobyTurbo Accelerator...........................   6
                2.4.3   ZMODEM Compression..............................   6
          2.5   Receiving files with ZMODEM.............................   7
                2.5.1   ZMODEM AutoDownload.............................   7
          2.6   Tuning ZMODEM Parameters................................   7
                2.6.1   Receiver Window Size Override...................   8
                2.6.2   Terminal Multiplexers...........................   8
                2.6.3   7 Bit Environments..............................   8
                2.6.4   Manual ABORT....................................   8
          2.7   XMODEM Family Protocols.................................   9
                2.7.1   TRUE YMODEM(TM).................................   9
                2.7.2   YMODEM-1k.......................................   9
                2.7.3   YMODEM with OverThruster........................   9
                2.7.4   XMODEM-1k.......................................  10
                2.7.5   XMODEM-CRC (with fallback)......................  10
                2.7.6   Classic XMODEM..................................  10
                2.7.7   Relaxed XMODEM..................................  11
                2.7.8   XMODEM with OverThruster........................  11
                2.7.9   YMODEM-g: Traditional Overdrive.................  11
                2.7.10  XMODEM Mutants Misrepresented as YMODEM.........  12
                2.7.11  Qmodem-G/Streaming XMODEM.......................  12
          2.8   Transferring Files with Unix Systems....................  13
                2.8.1   Terminal Servers / Port Multiplexers............  13
                2.8.2   Uploading Files to Unix Systems.................  13
                2.8.3   The rz and sz Programs..........................  13
                2.8.4   Downloading Files from Unix Systems.............  14
          2.9   VAX/VMS File Transfers..................................  15
                2.9.1   Version 4 rz/sz.................................  15
          2.10  GEnie File Transfers....................................  16
          2.11  BIX File Transfers......................................  17


      3.  FLOW CONTROL..................................................  18


      4.  SELECTED COMMANDS.............................................  21











      5.  Protocol File Transfer OPTIONS................................  29


      6.  NUMERIC PARAMETERS............................................  37
          6.1   X/Y/ZMODEM Numeric Parameters...........................  37


      7.  HARDWARE/SOFTWARE COMPATIBILITY...............................  41
          7.1   Hardware Compatibility Notes............................  41
          7.2   Brain Damaged UARTS.....................................  42
          7.3   Software Compatibility..................................  44


      8.  CROSS REFERENCE INDEX.........................................  49











































                                  Chuck Forsberg






                               DSZ Manual Addendum
                     (Selected Pieces of the Pro-YAM Manual)

                                Formatted 1-27-94

                                For DSZ Users ONLY
                                For DSZ Users ONLY
                                For DSZ Users ONLY
                                For DSZ Users ONLY


                                       With
                           Cybernetic Data Recovery(TM)
                                       and
                                 True YMODEM(TM)

                          Universal Line Printer Edition


                   Copyright 1992 Omen Technology Incorporated
                               All Rights Reserved



                           Omen Technology Incorporated


                          The High Reliability Software

                       17505-V Northwest Sauvie Island Road
                              Portland Oregon 97231
                            VOICE: 503-621-3406 :VOICE
                     Modem: 503-621-3746 Speed 1200,2400,9600
                         Compuserve:70007,2304  GEnie:CAF
                        UUCP: ...!tektronix!reed!omen!caf













      (C) 1994 Omen Tech Inc                                      Chapter 0



      DSZ Manual Addendum                                 Line Printer Draft
      2

      1.  INTRODUCTION

      The chapters included here are taken from the Pro-YAM manual.  Some of
      the features described here do not apply to DSZ.

      DSZ does not support ZMODEM Command Download, ZMODEM Security Check,
      Kermit and certain traditional protocols (WXMODEM, *LINK, MODEM7,
      etc.).

      When DSZ is called from a bulletin board or other communications
      program, automatic ZMODEM file download is not available.  ZMODEM
      AutoDownload is available from DSZ's t command (talk/term function).

      EXAMPLE: dsz port 1 speed 2400 t -8g


      Chapter numbers refer to chapters in the ZCOMM user's manual.



                Welcome to the Rain Forest

                        (_)  /~\\
                 /~\\       /   \\/\\
                /   \\ /\\  / |   \\ \\
               /\\     /     \\  \\/ /|\\   \\ \\
              /  \\   /       \\ / //|\\\\   \\ \\
            _/_   \\_/     ___ \\ ///|\\\\\\  _\\_\\
        _________________ _______  |  ________


                               -A Usenet Signature





















      (C) 1994 Omen Tech Inc               Chapter 1 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfers                                              3

      2.  PROTOCOL FILE TRANSFERS

      2.1  Graphic File Transfer Display


      #---------------------------------------------------------------------#
      #        Professional-YAM  Copyright 1991 Omen Technology INC         #**
      #                                                                     #**
      #                           ZMODEM RECEIVE                            #**
      #                                                                     #**
      #   File  pcmagc.dmp                                1 of       5      #**
      #                                                                     #**
      #   Current     43520 of   43520      Total     43520 of   999879     #**
      #                                                                     #**
      #   This   ##################################################         #**
      #         0------------------------50------------------------100%     #**
      #   Total  ##-                                                        #**
      #   State  START FILENAME COMPARE DATA CORRECTING FINISH WAIT         #**
      #   Throughput    8704   Retries     0   Time left     2 min          #**
      #   Connect ET   13:09   Time    13:18   Modem status                 #**
      #                                                                     #**
      #                                                                     #**
      #   Packet LEN    43520  TRANSPORT   COMPRESSED     DATA BINARY       #**
      #   Subpkt LEN      512  Window SIZ                                   #**
      #              ALT-F Cancel File   ALT-B Cancel Batch                 #**
      #                                                                     #**
      #---------------------------------------------------------------------#**
       ************************************************************************

      38kbps batch file download from a Unix system.[1] ZMODEM-90(TM)
      compression yields 87kbps effective speed on the PC Magazine
      Compressible File benchmark.[2]

      GSZ, ZCOMM and gYAM feature a full screen graphics status display of
      file transfer statistics.  The amount of information displayed depends
      on the protocol and sending program.  XMODEM, CompuServe B+, and
      Kermit download displays use information supplied to the estimate
      command.  In the absence of a user specified throughput value, Time
      left is calculated with real time data.  Real time throughput may be


      __________

       1. Pto-YAM screen snapshot made with ALT-Z.  The resultant YAMPIC
          file was renamed to YAMPIC.BIN and read in to THEDRAW.  Thedraw
          output the screen contents in IBM ANSI format, which was then
          typed and screen dumped to Postsctipt with SCRtoPS(TM) by Olfe
          Enterprises.

       2. Page 159, April 30 1991 PC Magazine.



      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      4                                              Protocol File Transfers

      inflated for the first 5-20 kilobytes when a streaming protocol sends
      data.

      On PCDOS YAM flavors, call (connect) elapsed time, time of day, and
      MODEM status are displayed.  MODEM status is displayed as follows:

      x   Software flow restraint (XOFF)

      X   Hardware flow restraint (CTS, etc.)

      L   Loss of Carrier Detect signal (CD)

      H   On Hook (DTR off)

      2.2  Choosing the Best Protocol

      A file transfer protocol should have high integrity (assurance of
      accurate data) and high robustness (low probability of aborting a
      transfer).  And, it should be as fast as possible without compromising
      reliability.

      When PC Magazine tested file transfer protocols in early 1991, they
      ignored the file transfer recommendations given in this manual.  Their
      ignorance slowed Pro-YAM file transfers by as much as 400 per cent.

      With many different ways to transfer files, your choice of file
      transfer methods can make the difference between efficient, error free
      data and slow or error prone transfers.

      The following subchapters discuss file transfer methods in more
      detail.


      2.3  ZMODEM-90(TM)

      ZMODEM was developed in 1986 for the public domain (PD) under contract
      by Telenet, a major packet switched network.  Omen Technology's
      commitment to file transfer technology did not stop with PD ZMODEM.
      ZMODEM-90(TM) is Omen Technology's copyrighted refinement of PD
      ZMODEM.  ZMODEM-90 speeds transfers with COMPRESSION and other
      accelerators.  ZMODEM-90 adds frame types to support transfers in 7-
      bit environments.  ZMODEM-90 sends files faster and more reliably than
      PD ZMODEM.  Omen Technology's ZMODEM-90 transfers files accurately in
      many applications where other ZMODEM programs abort or corrupt data.

      ZMODEM provides a greatly simplified user interface.  The file name is
      entered once, and transfer options may be given to the sending
      program, even those that apply to the receiver.  ZMODEM
      AutoDownload(TM) allows menu and mouse driven programs to download
      files and commands with no extra keyboarding required.



      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfers                                              5

      ZMODEM transfers one or more files with a single command.  The size
      and transfer time for each file is displayed, and the total number of
      files, size, and transmission time is displayed when more than one
      file remains to be sent on a command.

      Keyboarding ALT-F allows the receiver to bypass an individual file
      without having to restart the batch.

      ZMODEM transfers both files and commands.  Command download allows one
      of the computers to take positive control of the session.  A security
      challenge (activated by ZMODEM AutoDownload(TM)) guards against Trojan
      Horse messages.*

      ZMODEM file transfers can preserve the file date and the exact file
      contents, unlike traditional protocols that append garbage to files.

      Streaming transmission provides full throughput over satellite links
      and packet switched networks.  One of three ZMODEM streaming control
      methods may be used with systems that allow the sender to monitor the
      received data for error correction packets without interrupting
      transmission.  ZMODEM's "block length" is the entire file!
      Individually acknowledged packets support other systems.

      ZMODEM allows programs to adjust the protocol parameters for optimum
      efficiency as the file is being sent.  ZMODEM-90 allows programs to
      adjust character encoding for best results with a variety of systems.

      ZMODEM is immune to conditions that prevent reliable, accurate file
      transfers with traditional protocols:

       + ZMODEM data transfers are protected by the Federal Standard 32 bit
         CRC to assure reliable transfers.  This 32 bit CRC gives an
         undetected error rate five orders of magnitude better than XMODEM's
         16 bit CRC, and more than a billion times better than checksum
         XMODEM.  ZMODEM uses 16 bit CRC for file transfers with programs
         that do not support 32 bit CRC.

       + Most important, all ZMODEM protocol transactions are protected by
         CRC.  Other protocols advertising 16 or 32 bit CRC sometimes fail
         under stress because critical control messages are not CRC
         protected.

      If you've ever been disconnected when a huge file transfer was almost
      finished, you'll appreciate resuming/recovering the file transfer with
      ZMODEM Crash Recovery Omen Technology Incorporated's Intelligent Crash
      Recovery(TM) guards against file corruption during Crash Recovery
      operations.  (ZMODEM r and rr options.)






      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      6                                              Protocol File Transfers

      2.4  Sending files with ZMODEM

      To send a file with ZMODEM, the command sz file1 can be given from
      either the main command prompt, or from the term function via a
      secondary command prompt obtained with ALT-2.  Multiple files and wild
      cards may be used.

      EXAMPLE: sz file1 file2 *.lst

      Please refer to the sz and zcommand commands in Chapter 19 for more
      examples and information.


      2.4.1  File Maintenance with ZMODEM  Omen Technology ZMODEM gives you
      the tools to maintain up to date files on multiple machines.  You can
      use the ZMODEM n option to transfer only those files that have changed
      since the last time they were transferred.  With the p option, you can
      unconditionally protect files that exist on the destination system.
      To update only the files you already have while skipping the rest, use
      the Yn options.  You can update an entire directory subtree with the R
      option.

      SEE ALSO: File Transfer Options, Chapter 20.

      2.4.2  MobyTurbo Accelerator  Standard ZMODEM escapes network control
      characters.  This causes a slight drop in throughput when sending
      compressed files.  When transferring compressed files over circuits
      that pass all 256 8 bit codes, MobyTurbo(TM) may be used to optimize
      speed.  MobyTurbo provides the raw transfer speed of YMODEM-g and
      other fragile protocols without sacrificing ZMODEM's safety or
      robustness.

      MobyTurbo is activated with the m option.  The m option may be used
      with the sz or rz command.

      EXAMPLE: sz -m *.zip

      MobyTurbo may be used with ZMODEM AutoDownloads by adding the m option
      to the DSZOPT environment variable.

      EXAMPLE: C>set DSZOPT=m



      SEE ALSO: m file transfer option

      2.4.3  ZMODEM Compression  ZMODEM-90 programs support ZMODEM
      compression for fast transfers of compressible files with the Z file
      transfer option.  The amount of compression (and speed increase)
      depends on the structure of data in the files.



      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfers                                              7

      EXAMPLE: sz -Z pcmagc.dmp


      SEE ALSO: Z file transfer option

      2.5  Receiving files with ZMODEM

      2.5.1  ZMODEM AutoDownload  YAM's term function (t command) will
      detect a ZMODEM transmission, and receive the file(s) automatically.
      File transfer options for ZMODEM automatic downloads may be specified
      with the DSZOPT environment variable.

      EXAMPLE: C> set DSZOPT=m Requests MobyTurbo(TM) accelerator for
      downloads.

      .H 3 "Manual ZMODEM Downloads" The rz command may be also given from a
      command prompt.

      SEE ALSO: rz command

      2.6  Tuning ZMODEM Parameters

      Chapter 24.2 describes a number of ZMODEM numeric parameters which may
      be adjusted for extraordinary situations, or to fine tune the last 0.1
      per cent of possible performance.

      The ZMODEM subpacket length (zmodem L parameter) and the ZMODEM frame
      length (zmodem l parameter) deserve special mention.  People tend to
      confuse these with the familiar 128 and 1024 byte block length used in
      XMODEM transfers.

      When a ZMODEM frame length of 0 is specified (the default), a single
      frame will span the entire file if there are no errors.  This is the
      main source of ZMODEM's reputation for fast transfers.

      Setting the ZMODEM frame length to a number between 64 and 16384
      restricts the frame length to that value.  At the end of each frame,
      the sender stops sending and waits for an acknowledgement from the
      receiver.  When set, the ZMODEM frame length corresponds in function
      to the 128 or 1024 byte block length of XMODEM based protocols.

      Each ZMODEM frame consists of one or more subpackets of 32 to 1024
      bytes.  Since the subpackets within a frame are sent without pause, a
      short subpacket length does not exact the terrible throughput penalty
      associated with short XMODEM and Kermit blocks.  In the absence of
      transmission errors, a 256 byte subpacket length has about two per
      cent more overhead than a 1024 byte subpacket length.  However, the
      longer subpacket length does increase error recovery time.

      Professional-YAM dynamically adjusts the ZMODEM subpacket length on
      the basis of transmission speed and observed error rate.  If you know


      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      8                                              Protocol File Transfers

      what the error rate on a particular call will be before starting a
      ZMODEM file transfer, setting the zmodem L numeric parameter will
      provide a small but noticeable improvement in performance, with 1024
      best for clean lines and smaller numbers better for noisy lines.

      When sending files over noisy phone lines not involving networks, the
      speed of error recovery may be increased by decreasing the values of
      the ZMODEM t and p numeric parameters.

      Information about YMODEM and ZMODEM protocol internals is provided in
      ymodem.doc and zmodem.doc, part of Omen Technology's ZMODEM
      Developer's Collection.

      2.6.1  Receiver Window Size Override  Some ZMODEM senders control the
      network window size to improve error recovery and/or overcome bad flow
      control configuration.  The optimum size of this depends on the
      average error rate on the link, information that may not be available
      to the sender.  ZMODEM-90(TM) allows the receiver to specify the
      window size, with the Wn option, overriding the sender's window size.

      SEE ALSO: Wn option

      2.6.2  Terminal Multiplexers  Terminal multiplexers and telnet servers
      provide a semi transparent serial link to host computers.  The sz e
      and m options may be used in conjunction with the xmtxesc and zmrxesc
      string parameters to specify more control characters which cannot be
      passed over the serial line.

      SEE ALSO: zmtxesc, zmrxesc string parameters for details

      2.6.3  7 Bit Environments  ZMODEM-90 automatically detects 7 bit
      environments and adjusts accordingly.  If the environment is known to
      be 7 bits, use the E option to provide 7 bit compatibility in minimum
      time.

      EXAMPLE: sz -E file.doc


      When transferring files with a large number of bytes with the 8th bit
      set, the P ("pack") option may be used to optimize 7 bit encoding.

      EXAMPLE: sz -P zipfile.zip


      2.6.4  Manual ABORT  If a ZMODEM transfer fails abruptly under
      exceptional conditions the program on the remote machine may be
      manually terminated by repeatedly typing Ctrl-X characters at it until
      the program exits.





      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfers                                              9

      2.7  XMODEM Family Protocols

      All XMODEM family protocols require an absolutely transparent data
      path from sender to receiver.  Modems must not be configured for
      software flow control.

      2.7.1  TRUE YMODEM(TM)  Developed in 1981, YMODEM is finding its way
      into many communications programs.  With Omen Technology's Enhanced
      Data Recovery(TM), YMODEM gives excellent efficiency, integrity, and
      fair robustness in many applications.

      True YMODEM transfers one or more files in a batch, without alteration
      or added garbage characters.  True YMODEM also preserves the file date
      across multiple time zones.  Professional-YAM and the Unix(TM) rb and
      sb programs preserve the file modification date.[3]


      2.7.2  YMODEM-1k  The sb k option (1024 byte blocks) may be used to
      enhance throughput, especially when using timesharing systems,
      satellite links, or packet networks that can support the longer
      blocks.


      EXAMPLE: sb -k *.c *.h sends all .c and .h files in the current
      directory with 1024 byte blocks.[4]

      YMODEM and YMODEM-1k transfers can be received with the rb or F3
      commands.

      YMODEM file transfers with Unix and VMS systems are discussed later in
      this chapter.

      Some programs claim to support YMODEM but actually use XMODEM with
      1024 byte blocks.  These programs do not meet the YMODEM Minimum
      Requirements defined by the YMODEM protocol.

      One can use Pro-YAM's XMODEM sx -k and rc commands with these
      traditional programs.

      2.7.3  YMODEM with OverThruster  YMODEM and YMODEM-1k file downloading
      from networks and timesharing systems is slowed by response times.
      This slowing may be significant even when 1k blocks are used.  With


      __________

       3. Controlled by the d and z numeric parameters

       4. YAM switches to 128 byte blocks at the end of a file when the
          length warrants.



      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      10                                             Protocol File Transfers

      some systems, one can speed up YMODEM downloads by using the o option
      with the rb command to receive the file.  Because OverThruster(TM)
      defeats error recovery, a line hit will usually abort a download.
      OverThruster(TM) may be used with X.PC or MNP error correcting link
      level protocols.

      EXAMPLE: rb -o


      SEE ALSO: O numeric parameter

      2.7.4  XMODEM-1k  The XMODEM-1k protocol transfers one file per
      command with 1024 byte blocks and a nominal 16 bit CRC.  The file name
      must be entered for both the sender and the receiver.  Programs
      lacking YAM's Cybernetic Data Recovery(TM) logic are less likely to
      transfer data accurately under marginal conditions.  XMODEM's use of
      every possible 8 bit code causes problems in some applications.

      The end of the file may be padded by up to 127 or 1023[5] garbage
      characters.

      To send a file with XMODEM-1k: sx -k file1

      To receive a file with XMODEM-1k: rc file1

      2.7.5  XMODEM-CRC (with fallback)  The XMODEM-CRC protocol transfers
      one file per command.  The XMODEM-CRC protocol requires the receiving
      program to initiate an XMODEM-CRC transfer.

      The file name must be entered for both the sender and the receiver.
      Even with CRC-16, programs lacking YAM's Cybernetic Data Recovery(TM)
      are less likely to transfer data under marginal conditions.  XMODEM-
      CRC's use of every possible 8 bit code causes problems in some
      applications.

      The end of the file may be padded by up to 127 garbage characters.

      To send a file with XMODEM (or XMODEM-CRC): sx file1

      To receive a file with XMODEM-CRC: rc file1

      2.7.6  Classic XMODEM  The original MODEM protocol, developed by Ward
      Christensen, is supported by a large and growing number of programs
      operating on a variety of micros and minis.  The base level XMODEM
      protocol gives good results when used over low error rate direct


      __________

       5. Some programs (including YAM) limit this padding to 127 bytes.



      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfers                                             11

      telephone connections.  XMODEM's short data blocks and use of every
      possible 8 bit code preclude its application in many environments.

      File transfers with this protocol add up to 127 garbage characters to
      transferred files.  The XMODEM protocol can transfer one file per
      command.  The file name must be entered at both the sender and the
      receiver.

      To send a file with XMODEM: sx file1

      To receive a file with Classic XMODEM: rx file1

      2.7.7  Relaxed XMODEM  Professional-YAM's XMODEM and YMODEM support
      has been optimized for maximum reliability with a wide variety of
      systems under a wide variety of conditions.

      The default XMODEM and YMODEM timeout parameterss are "relaxed"
      timings.  They rarely need to be lengthened except under the most
      sluggish of conditions.  The zmodem t, T, and p numeric parameters
      (q.v.) control timeouts for XMODEM, YMODEM, and ZMODEM.  The default
      values allow 10 seconds for a packet to appear and a 10 second pause
      within a packet before starting error recovery.

      EXAMPLE: zmodem pt200 pp150  :: Set more relaxed X/Y/ZMODEM timing


      For best reliability, Omen Technology does not recommend tightening
      these timings for XMODEM and YMODEM transfers on noisy lines.

      2.7.8  XMODEM with OverThruster  XMODEM file downloading from networks
      and timesharing systems is slowed by short blocks and long response
      times.  With some systems, one can speed up downloads by using the ro
      command to receive the file.  Because OverThruster(TM) defeats error
      recovery, a line hit will usually abort a download.  With nearly error
      free connections, one can save enough time from the increased
      throughput to make up for the failed transfers.  OverThruster(TM) may
      be used with X.PC or MNP error correcting link level protocols.

      EXAMPLE: ro file1


      EXAMPLE: rb -o


      SEE ALSO: O numeric parameter

      2.7.9  YMODEM-g: Traditional Overdrive  The proliferation of error
      correcting modems has sparked a proliferation of YMODEM-g programs,
      more and more of which actually meet minimal YMODEM protocol
      specifications.



      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      12                                             Protocol File Transfers

      YMODEM-g transmits 0 or more files per batch with an ACK-less variant
      of YMODEM-1k.  The sender does not wait for individual data blocks to
      be acknowledged, allowing high speed transfers with error correcting
      modems.

      YMODEM-g assumes an error free communications channel.  A single
      transmission error or character lost because of DOS or TSR interrupt
      latency ruins the entire transfer, and YMODEM-g does not support Crash
      Recovery(TM).

      YAM supports True YMODEM-g with the sb and rb -g commands.

      EXAMPLE: sb *.old Sends files in the current directory with YMODEM or
      YMODEM-g protocol.  The receiver controls whether YMODEM or YMODEM-g
      is used for the transfer.


      EXAMPLE: rb -g Receives with YMODEM-g protocol.


      2.7.10  XMODEM Mutants Misrepresented as YMODEM  Despite continuing
      education efforts, a few lazy software providers insist on identifying
      their mutant XMODEM protocols as "ymodem".  They choose to ignore the
      definition of YMODEM that Ward Christensen wrote when he coined the
      term YMODEM in his April 1985 message:

         (a) a record 0 containing filename date time and size
         (b) a 1K block size option
         (c) CRC-16.

      Use the XMODEM sx-k and rc commands to deal with these nonstandard
      programs.

      In case of questions, please refer to ymodem.doc, part of yzmodem.zoo
      for for the official YMODEM protocol.  (Available in Omen's ZMODEM
      Developer's Collection.)

      2.7.11  Qmodem-G/Streaming XMODEM  The Qmodem program and certain
      bulletin boards provide an ACKless XMODEM mutant protocol selected
      with the Qmodem G protocol menu choice.

      The sx and rx -g commands support this mutant XMODEM.

      EXAMPLE: rx -g qmodem.fil









      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfers                                             13

      2.8  Transferring Files with Unix Systems

      2.8.1  Terminal Servers / Port Multiplexers  Some Unix systems are
      accessed via a port multiplexer or other network.  Some of these
      interfere with data transmission.  In some cases it has been necessary
      to contact the manufacturer to obtain undocumented instructions or
      software updates to make the multiplexers or networks suitable for
      file transfers.

      These systems may require additional control characters to be escaped.
      The sz command e option may be used to escape all control characters.

      SEE ALSO: e option

      Individual control characters can be escaped with the zmtxesc string
      parameter.

      SEE ALSO: zmtxesc string parameter

      Sometimes it is necessary to use 7-bit transfers with the E or EP
      options.

      EXAMPLE: sz -EP bigkahuna.zip


      2.8.2  Uploading Files to Unix Systems  Files may be sent to Unix
      systems conveniently and quickly with ZMODEM.  Unix flavors of
      Professional-YAM support the full ZMODEM-90(TM) feature set including
      Intelligent Crash Recovery(TM) and selective transfers with the rz
      command, a hard link to the /usr/bin/yam program.

      If the Unix system is operating with 7 bits, the sender's zmodem d
      parameter may have to be increased to allow the rz program time to
      change Unix to 8 bits for the transfer.

      SEE ALSO: zmodem d numeric parameter

      Traditional Unix systems limit serial input buffering to a few hundred
      characters or less.  This is sometimes too small to prevent data loss
      and retransmissons when operating at high speeds.  On SCO Unix 3.2.4
      this bufering can be increased by increasing the TTYHOG and NCLIST
      kernel parameters.

      2.8.3  The rz and sz Programs  Professional-YAM is the fastest Unix
      ZMODEM upload program.  Pro-YAM uses a minimum of CPU resources for
      uploads.  Pro-YAM provides the best ZMODEM technology and feature set
      available., but it may not be available on a particular system.  The
      rz program, part of the rzsz package, may be used to support a subset
      of Pro-YAM's ZMODEM features.

      If rz is not installed on the target Unix system, unpack the rzsz.zoo


      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      14                                             Protocol File Transfers

      file on your MSDOS system with: booz x rzsz.zoo given from the DOS
      prompt.[6] Next, the command source zupl.t calls the zupl.t script to
      upload the bootstrap file minirb.c, compile it, and use it to upload
      the remainder of the source files.  After the rest of the files have
      been uploaded, compile rz.c and sz.c using the directions given in the
      README file and in the C source files.

      The rz and sz manual pages may be formatted with a make doc command.

      The undos program may be used to remove carriage returns in files
      uploaded to Unix machines.

      2.8.4  Downloading Files from Unix Systems  To download files from
      Unix(TM) systems, use the Unix sz command to send the desired files to
      YAM.  To Unix keyboard: sz file ...  Professional-YAM's ZMODEM
      AutoDownload(TM) takes care of the rest for you, saving unnecessary
      keystrokes.

      If one or more of the files already exists on the destination disk,
      use sz -y file ...  instead, to replace the old copies on your
      computer.

      Another useful option sends only the files that exist on both
      computers (Y), and furthermore sends only those that are newer (n):
      sz -Yn file ...

      When files are long and transmission slow, you can save time by
      compressing them first.  The zoo program, available for DOS and Unix,
      may be used to compress file(s) before transmission.

      Omen Technology products support ZMODEM compression with the Z option.
      All Omen Technology products support compression by Run Length
      Encoding (RLE).  Unix flavors of Professional-YAM also support LZW
      compression.

      Unix source files normally do not contain carriage returns used by
      CP/M and DOS.  Some CP/M or DOS programs, such as C compilers, do not
      require carriage returns in the source files.  Others, such as the
      Microsoft Macro Assembler, become quite confused by such files,
      although such files fully meet the requirements of the ASCII standard.

      Carriage Returns may be added before downloading with the todos or


      __________

       6. On Unix systems with Professional-YAM installed, the rzsz source
          files and man pages are installed in the /usr/src/command/rzsz
          directory, or on the distribution diskette in the file
          /tmp/yamusrc.tar.Z.



      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfers                                             15

      tocpm programs.  Carriage returns may be added during the transfer
      with the sz a option.  Carriage Returns may be added after the
      transfer by some program editors, including uEMACS.  (Other editors,
      such as DOS edlin may crash trying to edit such files.) Short files
      (less than 64kb) may be converted using YAM's read and create commands
      to pass the data through YAM's capture buffer.

      Text files may also be downloaded using the capture buffer if sz has
      not been installed on the Unix machine.

      If a file or set of files are to be transported between two Unix
      systems, it may be helpful to place them in a tar or cpio archive (and
      possibly compress the archive) before transmission.  This procedure
      will preserve the Unix file modes and modification times, and bypass
      pathname restrictions imposed by DOS.

      As with rz, Unix Professional-YAM is linked to sz to support the full
      ZMODEM-90(TM) feature set.  Otherwise the separate Unix sz program may
      be obtained as described in the previous subchapter.

      2.9  VAX/VMS File Transfers

      Most of the comments made above about Unix file transfers apply to VMS
      as well.  Many VAX/VMS systems attach terminals with terminal
      multiplexers just as nasty as those used with Unix systems.  They
      require fixes similar to those described above for Unix systems..

      Automatic uploads to VMS may require setting the zmodem d (delay)
      numeric parameter to give time for the VMS rz program to properly
      initialize.

      SEE ALSO: zmodem d numeric parameter

      EXAMPLE: zmodem pd15


      2.9.1  Version 4 rz/sz  Omen provides VMS flavors of version 4 rz and
      sz precompiled in rzsz.tlb, a VMS "text library".  Version 4 rz
      supports most ZMODEM-90 features including Crash Recovery,
      compression, and MobyTurbo.  Binary uploads write files with a default
      VMS 512 byte fixed length record format.

      EXAMPLE: sz biglib.tlb


      Sending to VMS with the i option selects the VMS Stream_LF record
      format.  Stream_LF preserves the exact file length and data contents
      when read by C programs.

      EXAMPLE: sz -i vmsemacs.exe



      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      16                                             Protocol File Transfers

      Sending to VMS with the I option causes the VMS receiver to use
      variable length binary records.  VMS Kermit-32 and some other programs
      understand this record format.

      Text files uploaded with the a option are written in variable length
      records with CR carriage control.

      EXAMPLE: sz -a emacs*.c


      Version 4 VMS sz supports standard VMS wild card and directory
      recursion syntax.

      EXAMPLE: $ sz -qa [*...]*.prn sends all accessible .prn files on the
      system in ASCII mode. The VMS sz q option suppresses the initial tally
      of the number of files and their lengths.  This tally can take some
      time when a large number of files and directories are invloved.  The f
      option may be added to send directory names as well.


      If you use Kermit to upload the rzsz.tlb file to VMS, command the
      receiving Kermit program to SET FILE TYPE FIXED.  (Some VMS Kermit
      programs may require SET FILE TYPE BLOCK.) Otherwise Kermit will
      garble the data.

      2.10  GEnie File Transfers

      The General Electric Consumer Information Service service (GEnie) uses
      ZMODEM-90(TM) for efficient downloads.  GEnie's ZMODEM server selects
      ZMODEM RLE Compression or MobyTurbo(TM) for optimum download speed on
      each file.

      GEnie uses a large network to provide callers with local access
      numbers.  This requires technical tradeoffs to control data flow in
      the network.  If you have a reliable, error-free connection to GEnie,
      download speeds can be improved by increasing GEnie's ZMODEM window
      size.

      EXAMPLE: C> set DSZOPT=W16384



      The sx file.exe command is used for XMODEM-CRC uploads to GEnie.  When
      uploading with XMODEM-CRC, Wait for GEnie's "READY FOR INPUT, start
      your XMODEM upload." message, and then wait for the XMODEM-CRC C to
      appear before issuing the sx command.  Issuing the sx command before
      the C appears may corrupt the uploaded file.

      A number of GEnie access scripts are provided in scripts.zoo with
      filenames starting with ge.  The main GEnie login script is provided
      in phones2.t witin scripts.zoo.


      (C) 1994 Omen Tech Inc               Chapter 2 Protocol File Transfers



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfers                                             17

      2.11  BIX File Transfers

      BIX (Byte Information Exchange) supports ZMODEM-90 and Kermit file
      transfers.

      The Tymnet phone number in the bix telephone directory entry should be
      changed for your calling area.  Other scripts are provided to handle
      BIX mail and conferences.

      When setting up a new BIX account, give the command call bix,new to
      force a login to the BIX new account program.

      Be sure to select ZMODEM downloads and uploads with the BIX "OPTIONS"
      menu choice.  Set the DSZOPT environment variable  m or mr to enable
      MobyTurbo and ZMODEM Crash Recovery.

      When uploading over Tymnet or other networks, it may be necessary to
      set the zmodem w numeric parameter to a value between 2048 and 8192
      for best upload performance.  The optimum value depends on load and
      the particular node you dial in to.

      EXAMPLE: z pw6144


      BIX's transfer time predictions are about 40 per cent too pessimistic
      for ZMODEM transfers.

      A number of BIX scripts are included in SCRIPTS.ZOO.

                      //-n-\\
              _____---=======---_____
          ====____\   /.. ..\   /____====
        //         ---\__O__/---        \\
        \_\                            /_/

          Enterprise... Surrender or we'll
          send back your *&^$% tribbles !!!
              -A Usenet Signature















      (C) 1994 Omen Tech Inc                          Chapter 2 Flow Control



      DSZ Manual Addendum                                 Line Printer Draft
      18                                                        Flow Control

      3.  FLOW CONTROL

      All of us must sometimes tell people to "slow down" lest they overload
      us with information faster than we can write it down.  "Wait!" is a
      Flow Control Signal for the English language.  When the receiving
      Pro-YAM complains about Garbled Data Subpacket or Line Status Register
      01 you should suspect a flow control problem.

      When buffered modems, timesharing systems, networks, or computers of
      differing speeds are involved, a machine readable "Wait!" signal is
      required.

      Flow control is sometimes necessary to display long messages without
      skipping over the good parts.  If you see pieces of text missing from
      messages but don't see the usual funny characters caused by line
      noise, you have a flow control problem.

      File transfers that use long blocks or streaming protocols may not
      work well unless slower parts of the system regulate the speed of
      transmission to prevent loss of data.  With ZMODEM, SuperKermit, and
      other streaming protocols, inexplicable retransmissions of data
      blocks, often at regular intervals, indicate flow control failure.

      If you wish to keep things simple, the sending computer should not
      operate at a higher interface speed than the slowest link in the
      network.  Otherwise precautions must be taken to prevent data loss
      with interactive operations and unnecessary retransmissions with
      streaming file transfer protocols.

      YAM, ZCOMM, and DSZ default to software flow control with XON and XOFF
      characters.[1] When used with modems that require hardware flow
      control, the handshake command (q.v.) should be used to specify which
      hardware lines are to be used for flow control.

      Non transparent software flow control is incompatible with Emacs
      editors, XMODEM and YMODEM transfers.  XMODEM and YMODEM require
      complete transparency to all 256 8 bit codes.  An XMODEM transfer that
      always fails at the same block results from non transparent flow
      control.  When XMODEM-1k and YMODEM-1k are used, the network must
      assert flow control, or handle bursts of 1040 characters without data
      loss.  When X.25 or hardware CTS is unavailable, flow control that
      does not "eat" any characters may be used with XMODEM and YMODEM.
      When buffers fill up, an XOFF should be emitted.  An XON should be


      __________

       1. The PCDOS flavor enables "handshake both" when selecting a port
          with an active Clear To Send (CTS) signal that was previously
          initialized to a speed greater than 2400 bps



      (C) 1994 Omen Tech Inc                          Chapter 3 Flow Control



      DSZ Manual Addendum                                 Line Printer Draft
      Flow Control                                                        19

      sent when the buffer has emptied.  Otherwise, the network should
      neither generate nor eat XON or XOFF characters.

      On Telenet, this is obtained by setting CCIT X3 5:1 and 12:1 in the
      PADs (Packet Assembler Disassembler) at both ends of the network.
      Packets should be forwarded when the packet is a full 128 bytes, or
      after a moderate delay (3:0,4:10).  Set parameter 5 to 1 at both ends
      AFTER one is connected to the remote modem.  (Sorry, these commands
      must be given each time you connect to a modem in the far city!)
           <ENTER>@<ENTER>
           set 5:1<ENTER>
           rst? 5:1<ENTER>
           cont<ENTER>
      ZMODEM and Kermit protect all 4 XOFF and XON characters, commonly used
      network control characters and trigger strings.  ZMODEM and Kermit are
      compatible with many networks that do not support XMODEM family
      protocols, including some that claim network compatibility.  For PADs
      that do not accept "rst?", use:
           <ENTER>@<ENTER>
           set 4:2,5:1,12:1<ENTER>
           cont<ENTER>
      For best Telenet download throughput, parameter 64 (advance ACK)
      should be set to 7.  The parameter 0 is a dummy argument that
      distinguishes Telenet parameters from CCIT parameters.
           <ENTER>@<ENTER>
           set 0:0,64:7<ENTER>
           cont<ENTER>
      Sometimes Telenet flow control stops data transmission when the
      network buffers are not yet full.  If you often see "STOPPED" flashing
      in the status line (DOS versions), or if you see the modem send data
      light pause in a ZMODEM or SuperKermit file send, poor flow control
      may be the culprit.  Such slowdowns are typical when a network is
      overloaded.  If this condition persists, the network should take steps
      to reduce the congestion.  Turning OFF network flow control and
      activating ZMODEM's or SuperKermit's protocol flow control may
      increase throughput under these conditions.

      Instead of or in addition to XON/XOFF flow control, the sending
      program's ZMODEM w numeric parameter can restrict the window size to a
      value that does not overload the network.  A zmodem pw2048 command
      restricts the window size (maximum number of bytes in transit) to
      2048.  This causes the sz command to trigger the receiver's
      acknowledgement every 512 bytes (one fourth the value of the ZMODEM w
      numeric parameter).  The sender monitors these responses and suspends
      transmission when necessary to restrict the window to the specified
      size.  Until a network dependent lower limit is reached, lower window
      sizes improve the speed of error recovery at the expense of slight
      increases in protocol overhead.  When the window size becomes less
      than the number of characters sent within the network's transit time,
      throughput falls off rapidly.  Frequent protocol acknowledgements slow
      down high speed pseudo full duplex modems (US Robotics HST, Telebit


      (C) 1994 Omen Tech Inc                          Chapter 3 Flow Control



      DSZ Manual Addendum                                 Line Printer Draft
      20                                                        Flow Control

      TrailBlazer) and should be avoided.

      ZMODEM-90(TM) allows the receiver to specify the window size with the
      -Wn option where n is the desired window size.  requests an 8192 byte
      window size.


      Some modems and networks can be configured to flush (discard the
      contents of) their buffers when a break signal is received.  If this
      is possible, error recovery with ZMODEM transfers may be speeded up by
      setting the ZMODEM b parameter to 1, which sends a break whenever the
      ZMODEM sending program gets a retransmission request.
                   Network and Flow Control (FC) Compatibility

      ______________________________________________________________________
      |    Network     | Interactive | XMODEM | WXMODEM | S-KERMIT | ZMODEM |
      |________________|_____________|________|_________|__________|________|
      |No Network      | YES         | YES    | YES     | YES      | YES    |
      |8 bit, no FC    | NO          | YES    | YES     | YES(1)   | YES(1) |
      |Transparent FC  | YES         | YES    | YES     | YES      | YES    |
      |Non Transparent | YES         | NO     | NO      | YES      | YES    |
      |7 bit           | YES         | NO     | NO      | YES      | YES(2) |
      |________________|_____________|________|_________|__________|________|

      (1) Window size must be restricted to avoid buffer overrun if the
      network cannot transfer data at full speed.
      (2) Requires ZMODEM-90(TM) 7-bit support


























      (C) 1994 Omen Tech Inc                     Chapter 3 Selected Commands



      DSZ Manual Addendum                                 Line Printer Draft
      Selected Commands                                                   21

      4.  SELECTED COMMANDS

      Commands and arguments must be entered in lower case except where
      stated.

      estimate length speed Use the specified length and specified effective
        speed for the next receive file to be created.  A length of 0
        bypasses the length substitution.  Once a speed (in effective bits
        per second) is given, it is used for all locally displayed
        transmission time calculations until the next speed or port command.

        EXAMPLE: "speed 19200; estimate 0 2400" Use an effective
        transmission speed of 2400 for transmission time estimates instead
        of the 19200 bps interface speed.


      HAndshake {off|on|cts|dsr|dcd|both|slow} Some modems and printers
        cannot accept continuous full speed data.  These devices send
        control characters (XOFF and XON) for flow control, or generate a
        hardware flow control signal on the CTS, DSR, or DCD pin.  The
        Handshake command controls the modem port hardware handshake
        (default off).

        If hardware handshaking is selected, an ON to OFF transition on the
        specified line pauses transmission, and an XON character will not
        override the hardware restraint.

        After a timeout set by the S numeric parameter (default 60 seconds),
        or if characters are in the keyboard input buffer, a warning message
        is displayed, the restraint is released, and characters are sent.

        As a special case, handshake on obeys output flow control with the
        CTS input signal, asserts input flow control with the RTS output
        signal, and disables the transmission of XOFF characters when the
        modem input buffer becomes nearly full.  In addition, handshake slow
        drops the RTS output signal while writing to disk when receiving
        with XMODEM, YMODEM, or ZMODEM.

        The command handshake both allows either CTS or XOFF to pause
        output, in addition to asserting input flow control with the RTS
        output.

        The handshake dcd command enables d term option (q.v.).
        Subsequently, selecting a different type of handshaking will disable
        d term option.

        The handshake command releases flow control (allows data to flow if
        it had been stopped by handshaking).

        Changing the communcations port with the port or portx command
        disables hardware handshaking.


      (C) 1994 Omen Tech Inc                     Chapter 4 Selected Commands



      DSZ Manual Addendum                                 Line Printer Draft
      22                                                   Selected Commands

        SEE ALSO: S numeric parameter

        EXAMPLE: handshake cts Turns on CTS handshaking.



      port n Change the modem port to COMn.  On DOS, the legal values for n
        are 1...18.

        Selecting a new port normally selects software handshaking
        ("handshake sw").  The PCDOS flavor enables both hardware and
        software handshaking ("handshake both") iff the port speed exceeds
        2400 bps and the Clear To Send (CTS) signal is active at the time
        the port command is given.

        Standard Ports (PCDOS):
        COM1            3F8 IRQ4 (Standard IBM)
        COM2            2F8 IRQ3 (Standard IBM)

        NON STANDARD PORTS:
        COM3            3E8 IRQ4 (Alternate)
        COM4            2E8 IRQ3 (Alternate)
        COM5            2B8 IRQ3 (Columbia)
        COM6            2B8 IRQ2 (Alternate for IBM)

        COM7            2E8 IRQ5 (Alternate "COM3")
        COM8            3E8 IRQ5 (Alternate "COM4")

        COM9            Uses the port address and interrupt vector
        previously set by the portx command.

        COM1 and COM2 are the standard serial ports defined by the IBM
        Technical Reference Manual.

        COM3 and COM4 are supported by many serial cards and modem boards.
        COM3 and COM1 share the same dedicated hardware interrupt line, and
        these ports may not be used at the same time.  Likewise, COM4 and
        COM2 may not be used at the same time.

        Columbia computers support COM5.

        COM6 to COM8 are alternate configurations that may be accessed by
        cross jumpering between printer port decoders and serial port
        enables on some multifunction boards.

        COM7 and COM8 support alternative definitions for "COM3" and "COM4"
        respectively.

        Since YAM uses the interrupt line on the selected port, no other
        program or device driver may use the same port address and/or
        interrupt vector concurrently.  Certain disk controllers and mice


      (C) 1994 Omen Tech Inc                     Chapter 4 Selected Commands



      DSZ Manual Addendum                                 Line Printer Draft
      Selected Commands                                                   23

        interfaces use IRQ2 and IRQ5.  IRQ5 is sometimes used by network
        cards and printer ports.  Ports sharing the same interrupt vector
        (IRQ number) cannot be used concurrently.

        The port command sets the d term option (which suppress the No
        Carrier Detect message).

        EXAMPLE: port 2


        DOS YAM begins with COM1 unless overridden by the DPORT environment
        variable.

        EXAMPLE: C>set DPORT=2


        On Unix, the argument of the port command is a character special
        file in the /dev directory.  Unix and Xenix flavors have no default
        port.  If the DPORT environment variable is set, that port will be
        selected when Pro-YAM initializes.  Otherwise, a port is selected by
        the startup and/or dialing script.  Typical values are tty01
        (386/ix) and tty2A (Xenix).

        EXAMPLE: DPORT=tty1A; export DPORT

        If the port is in use by another program that supports UUCP port
        arbitration, or otherwise not accessible, port selection fails and
        the error counter is incremented.

        EXAMPLE:                 pe0; port tty1A; if !e goto gotport
                        pe0; port tty1B; if !e goto gotport
                        pe0; port tty1C; if !e goto gotport
                        echo "No Ports available";  fail
        gotport:


        SEE ALSO: handshake command, dport string parameter, e test
        condition

      portx hbase,irq[,divisor] * To support specialized multiport serial
        interfaces, the portx command selects a communications port with a
        specified hexadecimal base address hbase and Interrupt Request Line
        irq (3 <= irq <= 15).[1] Nonstandard baudrate clock inputs are
        supported with the optional divisor argument.  To support a


      __________

       1. IRQ2 can be used on some machines, on others it must be specified
          as IRQ9.



      (C) 1994 Omen Tech Inc                     Chapter 4 Selected Commands



      DSZ Manual Addendum                                 Line Printer Draft
      24                                                   Selected Commands

        nonstandard bit rate source, multiply 5760 by the new raw bit rate
        source frequency in MHz divided by 1.84320.

        The portx does not check its argument for validity.  The
        consequences of an invalid selection are quite undefined.  The
        specified base address and IRQ number are assigned to COM9, where
        they may be used by the port command and the x numeric parameter.
        The status line and s command will indicate COM9.  This command not
        available on X.PC, Unix, Xenix, or OS/2.

        EXAMPLE: portx 3e8,15,57600 Selects a comm port with a base address
        of 3e8 using IRQ15 and the 18.432 MHz clock option on the Boffin
        Electronics "WinSport II" 2 port serial board.


      rb [-options] Receives with options 1 or more files using YMODEM
        protocol.  The rb command also receives files sent with SEAlink
        protocol.  Chapter 20 describes the available options.  YMODEM
        transmits the pathname and length of each file.  If a file is
        received in error (retries exhausted, etc.), the batch transfer will
        terminate.  If Restricted, a file received in error will be unlinked
        (erased).

        EXAMPLE: rb -y Receive file(s) with YMODEM replacing old files, if
        any.


        EXAMPLE: rb -g Receive file(s) with YMODEM-g.

        Many programs claiming to support YMODEM actually use XMODEM with
        1024 byte blocks; use YAM's sx -k, rx and rx -g XMODEM commands with
        these mutants.

        SEE ALSO: YMODEM protocol, Chapter 13.

      rb [-options] [dir] [file ...] Receives with options 1 or more files
        using YMODEM protocol.  An optional disk and/or directory dir may be
        specified.  The optional supplied pathnames file ...  are used in
        place of pathnames normally provided by the sending program.  If the
        sending program attempts to send more files than the number of names
        supplied to the rb command, the transfer is aborted.

      rc [-options] file Receives with options a single file using the Ward
        Christensen XMODEM protocol, 128 or 1024 byte blocks, and CRC-16
        instead of an 8 bit checksum.  YAM signals the sending program that
        CRC-16 is to be used.  After four errors while attempting to receive
        the first sector, YAM will cancel the CRC-16 option and reverts to
        checksum operation.

        The probability of an undetected transmission error is much less if
        CRC-16 is used in place of the default 8 bit arithmetic checksum.


      (C) 1994 Omen Tech Inc                     Chapter 4 Selected Commands



      DSZ Manual Addendum                                 Line Printer Draft
      Selected Commands                                                   25

        Omen Technology Incorporated Recommends use of the 16 bit CRC to
        maintain data integrity at professional levels.  Chapter 20
        describes the available options to the rc command.  If Restricted, a
        file received in error will be deleted.

        EXAMPLE: rc foo.com


        SEE ALSO: XMODEM-CRC protocol, Chapter 13.

      ro [-options] file Receives with options a single file using non-
        standard XMODEM-CRC protocol logic.  OverThruster(TM) speeds file
        downloads at the expense of error recovery.  OverThruster operation
        is controlled by the O numeric parameter.  As fans of Buckaroo
        Bonzai know, the OverThruster is not universally applicable.  A
        transmission error will almost always terminate an OverThruster file
        download.

        If Restricted, a file received in error will be unlinked (erased).

        EXAMPLE: ro foo.com


        SEE ALSO: O numeric parameter

      rx [-options] file Receives with options a single file using the Ward
        Christensen XMODEM protocol.  CRC-16 is not the default because most
        commercial comms programs only support the 8 bit checksum.  Chapter
        20 describes the available options.  If Restricted, a file received
        in error will be unlinked (erased).

        EXAMPLE: rx foo.com

        The rc command should be used whenever possible instead of rx.

        EXAMPLE: rx -g foo.txt Receive a single file with an ACKless XMODEM
        protocol mutant incorrectly called "ymodem-g" by PCBoard and Qmodem
        programs.

        SEE ALSO: XMODEM protocol, Chapter 13.

      rz [-options] Receives with options 1 or more files using ZMODEM
        protocol.  Chapter 20 describes the available options.  Each file's
        pathname is obtained from the sending program.  The +, a, b, n, N,
        r, and y options are accepted from the sending program, subject to
        Restriced privileges.  If the +, b, n, N, r, or y option is
        specified to the receiver, it overrides any contrary options
        specified to the sender.  Only one of the a, b, or r options may be
        specified.  Only one of the +, n, N, or y options may be specified.
        If a file is received in error (retries exhausted, etc.), the batch
        transfer will terminate.  If Restricted, a file received in error


      (C) 1994 Omen Tech Inc                     Chapter 4 Selected Commands



      DSZ Manual Addendum                                 Line Printer Draft
      26                                                   Selected Commands

        will be unlinked (erased).

        EXAMPLE: rz -y


        SEE ALSO: Z term option

        SEE ALSO: ZMODEM protocol, Chapter 13.

      rz [-options] [dir] [file ...] Receives with options 1 or more files
        using ZMODEM protocol.  An optional disk and/or directory dir may be
        specified.  The optional supplied pathnames file ...  are used in
        place of pathnames normally provided by the sending program.  If the
        sending program attempts to send more files than the number of names
        supplied to the rz command, the transfer is aborted.  To allow use
        of the rz command, Z term option (ZMODEM AutoDownload) should be
        turned off with a dis -Z command.

      sb [-options] [PREFIX=p | ONAME=x] pathspec Send the files specified
        in pathspec using True YMODEMTm Protocol.  The pathname, length, and
        modification time of each file are transmitted.  Files which cannot
        be opened are skipped.  An empty pathspec sends all files in the
        current directory.  A directory name expands to all regular files in
        that directory.

        If an error aborts a file transmission (retries exhausted, etc.),
        batch transfers terminate.  The sb command will send files with
        SEAlink protocol if the receiving program requests SEAlink.

        EXAMPLE: sb -k *.com Sends *.com using 1024 byte packets.

        The receiver must be commanded to receive the files with an rb
        command.  Unix and OS/2 users: sb command cannot be used to send
        source files that grow after the beginning of transmission.

        SEE ALSO: YMODEM protocol, Chapter 13, SEAlink protocol, Chapter 13.

      sx [-options] file Send a single file using the Ward Christensen
        XMODEM or XMODEM-CRC protocol.  The receiving program may request
        use of a 16 bit CRC, which is more accurate than the default
        checksum.  DOS/Unix files sent this way will have Control-Z (CPMEOF)
        garbage characters appended to make the file length a multiple of
        128.

        EXAMPLE: sx foo.com


        EXAMPLE: sx -k foo.com Sends foo.com using 1024 byte blocks

        The receiver must be commanded to receive the file with an rx
        filename or rc filename command.


      (C) 1994 Omen Tech Inc                     Chapter 4 Selected Commands



      DSZ Manual Addendum                                 Line Printer Draft
      Selected Commands                                                   27

        SEE ALSO: XMODEM, XMODEM-1k, XMODEM-CRC protocols, Chapter 13.

      sz [-options] [PREFIX=p | ONAME=x] pathspec Send the files specified
        in pathspec using ZMODEM Protocol.[2] If the remote supports ZMODEM
        AutoDownload, or accepts rz followed by carriage return as a command
        to receive files with ZMODEM protocol, only the sz command need be
        given.  Otherwise, the receiver must be commanded to receive the
        files with an rz command or menu choice.

        The +, a, b, n, N, r, y, and Z options are sent to the receiving
        program.  Only one of the a, b, or r options may be specified.  Only
        one of the +, n, N, or y options may be specified.

        Each skipped file is counted as an error as indicated by the e test
        condition and e numeric parameter.  If the q option is used, files
        skipped as a result of selective file transfers are not counted as
        errors.

        The pathname, length, and modification time of each file are
        transmitted.  Files which cannot be opened are skipped.  An empty
        pathspec sends all files in the current directory.  A directory name
        expands to all regular files in that directory.

        If ONAME=x is given after the options (if any) and before the file
        name(s), x will be used exactly as given as the COMPLETE destination
        pathname instead of each file's actual pathname.  It is the sender's
        responsibility to use lower case for x unless the filename is really
        supposed to be all caps.

        EXAMPLE: sz -y ONAME=B:/spiked/secret /soviet/sdi/newlaser.doc
        Results in the destination file secret on drive B: in the /spiked
        directory.  (Destination directories must exist and be writable).


        If instead PREFIX=p is given after the options (if any) and before
        the file name(s), p will be added to the destination pathname(s) as
        a prefix.  It is the sender's responsibility to use lower case for p
        unless the prefix is really supposed to be all caps.

        EXAMPLE: sz -y PREFIX=C:/foobaz/ /biff/bam/aardvark.wak
        Results in the destination file "C:/foobaz/aardvark.wak"


        EXAMPLE: sz *.com   Sends all files with a .com extension.


      __________

       2. The receiver may use the sz command to send files by uploading an
          sz command with the zcommand command.



      (C) 1994 Omen Tech Inc                     Chapter 4 Selected Commands



      DSZ Manual Addendum                                 Line Printer Draft
      28                                                   Selected Commands

        EXAMPLE: sz -r ??log Crash Recovery sends only the new data if the
        receiver has incomplete versions of these files.


        EXAMPLE: sz -fn src/*.c src/*.h maildir
        Sends only newer .c and .h files in the src subdirectory, and all
        new files in the maildir subdirectory.


        EXAMPLE: zcommand "sz -fn /bin /wp"
        commands a remote YAM system in Host Operation (unrestricted) to
        send all new files in the /bin and /wp directories.


        EXAMPLE: sz -Yn *.c Sends only newer versions of files that already
        exist at the destination.


        EXAMPLE: sz -Rf usera Sends all files in the usera directory and all
        subdirectories thereof.  Directories are not sorted when the R
        option is used on 16 bit systems.

        SEE ALSO: ZMODEM protocol, Chapter 13, Options, Chapter 20.






























      (C) 1994 Omen Tech Inc        Chapter 4 Protocol File Transfer OPTIONS



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfer OPTIONS                                      29

      5.  Protocol File Transfer OPTIONS

      Options modify the way the protocol file transfer commands send and
      receive files.  They are reset before each command line.

      The a, b, r and rr options are mutually exclusive.  With ZMODEM, a b
      option given to the sender or receiver will override any a option.

      The +, c, r, rr, N, n, p, and y options are mutually exclusive.  The Y
      option may be followed by the c, +, r, n, or N option.  Specifying
      these options to the receiver overrides the ZMODEM sender's
      specification of these options.

      The DOS append command interferes with some of these options.


      +  When receiving to a file already on disk, append the new data to
         the file.  If the specified file does not exist, it is created.
         This option is not allowed if YAM is Restricted.

         EXAMPLE: rc -+ evrybody.dat


         When sending files with ZMODEM, the + option commands the receiver
         to append to a file already on the receiver's disk.

         EXAMPLE: sz -+ ONAME=master.log *.log sends all .log files in the
         current directory to be appended to master.log on the receiver's
         computer.

         NOTE: Append (+) is not the same as crash recovery (-r).  Append is
         used to concatenate (add) new data to an existing file.  The
         resulting file contains both old and new data.
         NOTE: If an append (+) file transfer is interrupted and restarted,
         data may be duplicated.

         SEE ALSO: r option

      7  Strip data to 7 bits for file transfers with the Kermit protocol.
         Program executables and other 8 bit binary files cannot be sent
         this way.  In the absence of the 7 option YAM transfers all 8 bits
         of each byte.  If the communications line is set to 8 bits no
         parity, the 8th bit is transmitted, otherwise YAM requests 8th bit
         quoting.  NOTE: The 7 option is distinct from the 7e and 7o term
         options.

      a  (ASCII) The a option applies to files received with XMODEM, YMODEM,
         or ZMODEM protocol.  It converts newlines not preceded by CR to
         CR/LF pairs.  NULL, RUBOUT, and all characters in each packet
         beginning with Ctrl-Z are excluded.  The a option is useful when
         receiving text files without carriage returns directly from Unix


      (C) 1994 Omen Tech Inc        Chapter 5 Protocol File Transfer OPTIONS



      DSZ Manual Addendum                                 Line Printer Draft
      30                                      Protocol File Transfer OPTIONS

         systems.

         When sending with ZMODEM, the a option instructs the receiver to
         convert text files to the conventions used in its operating
         environment.  When sending to VAX/VMS rz this selects CR carriage
         control variable length record format.

         The a option does not apply to the Kermit, sx, or sb commands.
         Files transferred with the a option cannot be processed with the
         ZMODEM r (recover/resume) option.

         EXAMPLE: rc -a program.c receives program.c and converts end of
         lines to CR/LF.


      b  (Binary) With ZMODEM, inhibits the receiver from translating the
         file contents.  If either the ZMODEM sender or receiver specifies b
         option, any contrary requests will be ignored.

         EXAMPLE: sz -b program.exe


      c  With ZMODEM, change the file name to prevent collision if the
         destination file exists.  The receiving program must support the
         ZMODEM c option or file disposition will be undefined.  The form of
         the invented (changed) filename is implementation dependent.

         Use CRC-16 with the rx, rt, and r7 commands.

      e  Normally, ZMODEM senders escape XON, XOFF, Ctrl-P, CR-@-CR, and
         Ctrl-X, and ZMODEM receivers ignore XON and XOFF.  The e option
         escape all control characters when sending files with the ZMODEM
         protocol.  In 7-bit environments, the e option also escapes RUBOUT
         (7F).[1] This option is useful when operating with brain damaged
         data PBX systems and other types of "front ends".

         SEE ALSO: zmtxesc, zmrxesc string parameters

      E  With ZMODEM-90, force 8th bit encoding even if the transmission
         medium appears to support 8 bits.[2]

      f  Send the full pathname as specified (exclusive of disk identifier)
         when using a batch send command.  Normally only the file name


      __________

       1. In 7-bit environments, ZMODEM always escapes FF.

       2. Not featured in DSZ.COM.



      (C) 1994 Omen Tech Inc        Chapter 5 Protocol File Transfer OPTIONS



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfer OPTIONS                                      31

         portion (without any directory prefix) is transmitted.  The f
         option applies to batch file transmission with the kermit sb, sb,
         send, and sz commands.

         EXAMPLE: cd /src; sz -f robot/r2d2.h sends the file with the
         pathname robot/r2d2.h.


         EXAMPLE: sz -f /src/robot/vox/3tpi0.*


         SEE ALSO: PREFIX=p flag for the sb and sz commands.

      F  Insert a pause after each transmitted data subpacket transmitted
         with ZMODEM.  This is useful in certain situations when
         conventional flow control methods are unavailable, ineffective, or
         unreasonably slow (i.e., "broken").  The length of pause is set by
         the zmodem F numeric parameter.

         EXAMPLE: sz -F honker.dat


         SEE ALSO: zmodem F numeric parameter

      g  Given to the receiving program, the g option to the rb command
         allows the sender and receiver to dispense with acknowledging each
         transmitted packet when using YMODEM batch transfers.  YMODEM-g
         increases throughput when the transmitting medium itself (direct
         connection, X.PC session, or error correcting modems) provides
         error free transmission.  The transmitting medium can use XOFF and
         XON to enforce flow control.

         If the transmitting medium does not enforce flow control,[3] the
         user must insure the receiver is not overrun.  YAM on a PC or XT
         accepts data at 9600 bps without flow control when the file is
         being written to a hard disk or ramdisk.[4]

         If an error is detected when the g option is used, the transfer is
         aborted.

         EXAMPLE: rb -g



      __________

       3. X.PC automatically enforces end to end flow control.

       4. Provided no memory resident programs or special drivers hog CPU
          cycles.



      (C) 1994 Omen Tech Inc        Chapter 5 Protocol File Transfer OPTIONS



      DSZ Manual Addendum                                 Line Printer Draft
      32                                      Protocol File Transfer OPTIONS

         The g option may also be used with the rx command to receive files
         from Qmodem's G protocol.

      i  With YMODEM or ZMODEM, instructs the receiver to write file(s) in
         stream oriented Image format.  When sending to the VAX/VMS version
         of rz, the i option selects Stream_LF record format.  Stream_LF
         preserves the exact contents of binary files read by VMS C
         programs.  Stream_LF is useful for file servers and archives that
         service PCs, as well as C programs on VMS itself.  (Without the i
         option, the VMS rz default is 512 byte fixed length record format.)

      I  With YMODEM or ZMODEM, instructs the receiver to write file(s) in
         variable length binary record Image format.  When sending to the
         VAX/VMS version of rz, the i option selects Variable length
         (mrs=510) binary record format.  Certain programs such as Kermit32
         understand this binary record format better than Stream_LF.

      k  Use 1024 byte (1K) packets with the sb and sx commands.  The
         default packet length is 128.  This increases throughput when the
         speed is high relative to the response times of the communications
         channel and the computers.  The k option is useful with 9600 or
         19200 bps transfers with directly connected timesharing systems.
         The k option may not work properly uploading to some systems,
         particularly heavily loaded or poorly implemented timesharing
         systems at high speeds.  The k option is valid only when sending to
         YAM, Unix rb, or other compatible programs.  If the file length is
         not a multiple of 1024, the remainder of the file will be sent with
         128 byte blocks.  This option does not affect Kermit transfers.

         EXAMPLE: sb -k *.c *.h

         With the sz command, the k option forces an initial 1024 byte
         subpacket length.

         EXAMPLE: sz -k *.c *.h


      K  Use 4096 byte (4k) packets with the sb and sx commands.  The
         default packet length is 128.  This increases throughput when the
         speed is high relative to the response times of the communications
         channel and the computers.  The K option is useful with 9600 or
         19200 bps transfers with directly connected timesharing systems.
         The K option may not work properly uploading to some systems,
         particularly heavily loaded or poorly implemented timesharing
         systems at high speeds.

         The K option is valid only when sending to compatible programs.  If
         the file length is not a multiple of 4096, the remainder of the
         file will be sent with shorter blocks.  This option is useful when
         working with non-ZMODEM programs that support the "XMODEM 4k"
         protocol, and for settling arguments.


      (C) 1994 Omen Tech Inc        Chapter 5 Protocol File Transfer OPTIONS



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfer OPTIONS                                      33

         EXAMPLE: sb -K *.c *.h


      l  Force pathnames that are all uppercase to lower case.  This option
         is reset by the call command.  This option is ignored on DOS and
         OS/2 flavors of Pro-YAM.

      m  (ZMODEM-90) Activate MobyTurbo(TM) for maximum throughput on
         compressed files sent over completely transparent connections.
         MobyTurbo can be used over links that support YMODEM-g.  MobyTurbo
         can not be used with most forms of software flow control or over
         networks that reserve control characters.  The m option can be
         given to either the sending or receiving ZMODEM-90 program.

         Likewise MobyKermit(TM) increases the speed of Kermit file
         transfers.  Unlike ZMODEM, the Kermit m option can only be given to
         the sending program.  Some Kermit programs do not work with the m
         option.

      M  Locks out MobyTurbo even if the other program has given the m
         option.  This option is useful if the transmission path does not
         support complete transparency.

         The Kermit receive M option causes unprefixed control characters to
         be ignored.  This is useful in certain environments that insert
         spurious characters into Kermit packets.

      n  (ZMODEM) Each file is transferred if the corresponding destination
         file does not exist, or if the source file is newer.  The n option
         can be given with either the sz or rz commands.  This option is not
         allowed if the receiver is Restricted.

         EXAMPLE: sz -n *.* attempts to send all files in the current
         directory.  Only those files that do not exist in the destination
         directory, and those for which the source is newer will be sent.


      N  (ZMODEM) Transfer the file if the corresponding destination file
         does not exist, or if the source file is newer or longer.  The N
         option be used with the sz and rz commands.  This option is not
         allowed if the receiver is Restricted.

         EXAMPLE: sz -N *.*


      p  (ZMODEM) Protect destination file; bypass this file if it already
         exists on the destination system.

      P  (ZMODEM-90) When transferring files over 7 bit paths, pack 4 8-bit
         bytes into 5 7-bit bytes for transmission instead of quoting the
         8th bit.[5] This increases transmission speed on compressed files.


      (C) 1994 Omen Tech Inc        Chapter 5 Protocol File Transfer OPTIONS



      DSZ Manual Addendum                                 Line Printer Draft
      34                                      Protocol File Transfer OPTIONS

      q  (Quiet) suppresses block by block status line update during Kermit
         and X/YMODEM file transfers.  Also prevents skipped files from
         incrementing the e numeric parameter and e test condition.

      r  (ZMODEM) Resume/Recover an interrupted file transfer with the
         ZMODEM protocol.  May be given with either the sz or rz commands.

         The r option may be used to resume the transmission of a long file
         after a disconnect or power loss, without having to start over at
         the beginning of the file.  The r option may also be used when the
         source file grows from time to time and only the incremental
         portion needs to be sent.  The r option assumes that the contents
         of the destination file are identical to the corresponding
         beginning portion of the source file.  The r option should not be
         applied to a file that has been modified by the a option.  This
         option is not allowed if the receiver is Restricted.

         EXAMPLE: sz -r hugefile.lst


         SEE ALSO: zmodem c numeric parameter

         For convenience, the r option can be specified on all files if
         desired, even those that have not been interrupted during a
         transfer.  However, if you do make the r option the default with
         DSZOPT  you could inadvertently overwrite valuable data with
         unrelated data from a random file with the same file name.

         The "ZMODEM Crash Recovery at NNNN" message may not appear when
         performing Crash Recovery on very short files.

      rr As above, but the files are compared by taking a 32 bit CRC on the
         contents before deciding on whether to start a fresh transfer.

         EXAMPLE: sz -rr maybenewer.lst


         With the -rr option, all of the files are compared or transmitted
         by default.  The number of bytes used in the comparison may be
         restricted by setting the zmodem R numeric parameter to a number
         between 2048 and 32000 (1 billion on 32 bit flavors).

         EXAMPLE: zmodem pR20000




      ______________________________________________________________________

       5. Not supported in DSZ.COM.



      (C) 1994 Omen Tech Inc        Chapter 5 Protocol File Transfer OPTIONS



      DSZ Manual Addendum                                 Line Printer Draft
      Protocol File Transfer OPTIONS                                      35

      s  SlugBait modifies the logic of ZMODEM sending to detect and report
         attempts at evading accountability for receiving files.  Such
         attempts are flagged with a Q status in the log of sent files.
         SlugBait adds a slight delay to file transmission, and a transfer
         that is cut off at the very end of file may very infrequently be
         reported with Questionable instead of ERROR status.

      S  When sending file(s) with ZMODEM, interrogate the receiving program
         for its serial number.  S option terminates when a serial number is
         received or when the call command is given.  Receiving file(s) with
         YMODEM or ZMODEM from programs providing a serial number also
         provides the other program's serial number.  The serial number
         received is listed by the performance log.

      t  Enter the term function after file transfer(s) complete.  The t
         option should not be used in commands given from within the term
         function, either directly or with soft key definitions.

      u  Unlink (remove, delete) the file after it has been sent with the sz
         command.

      v  View the data being transmitted or received.  Only correct data is
         displayed.  Viewing standard ASCII files does not interfere with
         correct transmission at high speeds, although throughput may be
         degraded.

         The output may be redirected to a capture file or DOS device with
         the > or >> command.  Unless output is redirected, this option must
         not be used when YAM is in Host Operation.

         When invoking Unix Pro-YAM as xyam, rz, sz, rb, sb, rx, or sx,
         creates a logging file with information useful for debugging
         purposes.  More v's create more detailed debugging information.

         SEE ALSO: v numeric parameter, LOGFILE environment variable

      wN Use a window size of N bytes with the sz command, overriding the
         zmodem w numeric parameter.  If N is missing, use a ZMODEM window
         size of 4096 bytes.

         SEE ALSO: Flow Control Chapter 14, zmodem w numeric parameter

      WN Request the sending program to use a window size of N bytes,
         overriding the sender's window size setting, 4096 bytes if N is
         missing.[6]


      __________

       6. The W option is supported when receiving files from ZMODEM-90(TM)
          program versions after Jan 21 1990.


      (C) 1994 Omen Tech Inc        Chapter 5 Protocol File Transfer OPTIONS



      DSZ Manual Addendum                                 Line Printer Draft
      36                                      Protocol File Transfer OPTIONS

      y  Yes it is OK to replace a file already on disk when receiving a
         file.  If absent, the operator is given a choice of appending to
         the current file (a), erasing it (y) or aborting (n).  This option
         is not allowed if YAM is Restricted.  When sending with ZMODEM,
         commands the receiver to replace a file on its disk.

      Y  (ZMODEM) Transfer only those files for which a file with the same
         pathname exists at the destination, overwriting the destination
         files.  The Y option may be followed by other ZMODEM options to
         further qualify the selection of files to transfer.  This option is
         not allowed if YAM is Restricted.

         EXAMPLE: sz -Yn *.* If the source directory contains files A, B,
         and C, each dated today, and the destination directory contains B
         and C, with B a week old and C dated today, only B will be sent.


      zT Use T minutes behind GMT (Greenwich Mean Time) as the local
         timezone instead of the z parameter value for the file(s)
         transferred with this command.

         EXAMPLE: sb -k -z300 ESTfile sends ESTfile corrected for creation
         in Eastern Standard Time.


      Z  Transmit files with compression.  The ZMODEM receiver must indicate
         its ability to decompress received files for this option to take
         effect.

         When sending between Unix systems, files are compressed with 12 bit
         Lempel-Ziv compression.  Otherwise, packets are transmitted with
         Run Length Encoding.

         Over slow channels, compression increases the transmission speed of
         compiler listings, screen dumps, etc. by up to 50 per cent.  LZW
         compression is more effective on more types of data than RLE
         compression.  Some files, including the Personal Computing Magazine
         ASCII Test File, speed up by more than an order of magnitude with
         either RLE or LZW compression.  Heavily encrypted data and
         compressed files, including ARC and ZOO archives, do not benefit
         from ZMODEM compression.

         The situation with fast compressed modems is more complex.  The
         benefits of ZMODEM compression will depend on the particular
         application; try the transfers with and without ZMODEM compression
         to determine the most efficient options.







      (C) 1994 Omen Tech Inc                    Chapter 5 Numeric Parameters



      DSZ Manual Addendum                                 Line Printer Draft
      Numeric Parameters                                                  37

      6.  NUMERIC PARAMETERS

      O    Controls OverThruster(TM) operation with the ro command (XMODEM,
           XMODEM-1k, and YMODEM) downloads.  This parameter should be set
           as follows:

           CompuServe XMODEM Negative numbers control the number of bytes
           added to the window on XMODEM downloads from the CompuServe
           Information Service.  Larger numbers increase throughput, but
           cause improperly interfaced MNP modems on CIS nodes to drop
           characters under stress, disrupting the file transfer.

           EXAMPLE: dsz pO-512 ro file1.ext

           Other XMODEM Positive numbers up to a system dependent value less
           than the protocol block size increase throughput.  Larger values
           induce timeouts and/or retransmitted blocks.  The optimum value
           must be determined by experiment.  30 to 60 gives best results
           with MNP modems at 2400 bps.  The optimum value varies depending
           on the remote computer, modem(s), system traffic, and the network
           node.  Performance improvement with high O parameter values is
           greater with sluggish networks.

           EXAMPLE: dsz pO60 ro file1.ext

           EXAMPLE: dsz pO1000 rb -o              (EXEC-BBS, MNP 5, 9600
           bps)

      6.1  X/Y/ZMODEM Numeric Parameters

      These parameters control XMODEM, YMODEM, and ZMODEM protocol
      transfers.  They are set with the z px# command available with ZMODEM
      flavors of YAM.

      EXAMPLE: z pl16384
      Forces ZMODEM packet length of 16384 (default packet length is
      infinite).

      Their current values can be displayed with a z p command.  These
      parameters rarely need changing in normal environments.

      b If non zero, ZMODEM sends a break when it is sending a file and
        receives a retransmission request.  This mode of operation may be
        used with high speed modems to clear unwanted characters from the
        modem's buffer during error recovery.  Usually, the modem must be
        given a configuration command to make it clear its transmit buffer
        when receiving a break signal.

      B Sets the duration of the break signal in tenths of a second, default
        2 (200 milliseconds).



      (C) 1994 Omen Tech Inc                    Chapter 6 Numeric Parameters



      DSZ Manual Addendum                                 Line Printer Draft
      38                                                  Numeric Parameters

      c Enables Cybernetic Data Recovery(TM) on XMODEM and YMODEM transfers.
        Setting this parameter to 0 accommodates programs with non standard
        XMODEM/YMODEM protocols and slightly quickens file transfers.  The
        default value of 1 provides optimum reliability for XMODEM and
        YMODEM transfers with programs that meet the XMODEM/YMODEM spec.

        Setting this parameter to -1 disables error checking provided by the
        r option.

      e If non zero, escape all control characters.  This allows ZMODEM
        transfers to operate over data PBX and other systems that freak out
        when they receive control characters.

      d Some operating systems, most notably VAX/VMS, use ^X to stop
        programs.  ZMODEM uploads consist of a "rz" command to start the rz
        program followed by a ZMODEM packet.  If the ^X in the ZMODEM packet
        causes problems, the zmodem d parameter can be used to delay the
        initial ZMODEM packet until the rz program initializes itself.  The
        zmodem d parameter sets a delay in tenths of a second on ZMODEM
        sends (uploads) between the "rz" command and the first packet.

      f Flow control mask, only used with Unix/Xenix systems.  Setting this
        to 0 (the default) disables hardware (RTS/CTS) flow control for
        Xenix/Unix systems with broken hardware flow control.  On Xenix/Unix
        systems where only CTS flow control works properly, set this to 8192
        to allow CTS flow control only.

        Use 32768 for newer SCO systems that support CRTSFL.

      F Sets the pause after each data subpacket sent with the sz command
        when the F option is used, or when failing flow control is detected.
        The default value of 1 causes a one tenth second delay.

        SEE ALSO: F option On some Unix operating systems the pause will be
        rounded up to the next second or two.

      l Normally, the ZMODEM "packet length" ("block length") is the file
        length.  Setting this parameter non zero forces ZMODEM to close a
        frame and wait for an ACK after each # bytes (default 0).  This
        makes ZMODEM behave like XMODEM, YMODEM, or JMODEM, which wait after
        each block/packet for an acknowledgement before going on to the next
        block.  The packet length may be adjusted to prevent buffer overflow
        in data PBX systems.  The call command resets this parameter to 0.

      L (Default 0) If non zero, overrides the nominal length of data
        subpackets within each ZMODEM frame.  A smaller value speeds error
        recovery on noisy lines, a large value (maximum 1024) reduces the
        overhead of CRC characters.  The call command resets this parameter
        to 0.

        Please note that streaming ZMODEM has no direct equivalent to


      (C) 1994 Omen Tech Inc                    Chapter 6 Numeric Parameters



      DSZ Manual Addendum                                 Line Printer Draft
      Numeric Parameters                                                  39

        XMODEM/YMODEM/JMODEM block length unless the zmodem l parameter is
        set non zero.  In the absence of errors, ZMODEM normally sends the
        entire file without pause.  If somebody claims ZMODEM's 1024 byte
        subpacket length is slowing things down by more than one half per
        cent, he doesn't understand ZMODEM and should be ignored.

      n Sets the number of NULLS (default 0) sent before each ZDATA frame.
        Some buffered modems (Fastcomm) have a firmware bug which loses
        characters when changing the direction of transmission.  This causes
        data frames to fail with a CRC or other error.  ZMODEM n parameter
        values in the range of 100 to 150 have obviated this syndrome.

      P When set to 2 (the default), purge the transmit buffer and force a
        receiver response when a CR/LF sequence (indicating a PC-Pursuit
        DATA LOSS message) is detected.  A value of 1 does not purge the
        transmit buffer.  A value of 0 disables special processing of CR/LF
        sequences received by the sending ZMODEM.

      w If non 0, restrict the ZMODEM transmit window to the specified
        number of bytes.  Setting this parameter to N requests
        acknowledgements from the receiver every N/4 characters.  Pro-YAM
        then waits for acknowledgements from the receiver whenever it has
        sent N more characters than it has received acknowledgements for.
        This parameter is useful with networks with defective flow control.
        Error recovery when ZMODEM is used with networks that store an
        excessive number of characters in transit can usually be improved by
        restricting the window size.  The call command resets this parameter
        to 0.

        Setting this parameter non zero also causes the sz command to
        perform an extra step that actively prevents an ALT-F given to a
        receiver from generating a spurious successful file transfer
        completion.

      W Adjusts the number of characters the ZMODEM receiver will silently
        ignore when searching for the beginning of a new frame.  This may be
        set larger to accomodate networks with excessive in transit storage,
        smaller to speed error recovery from long error bursts on direct
        connections.  The call command resets this parameter to the default
        (1400).

      Z Number of minutes (default 0) to adjust the file modification date
        when using the Telink or Clink/SEAlink file transfer protocol to
        transfer a file between different time zones.

      The timeout parameters below may be set lower for faster X/YMODEM
      error recovery when transferring files between two micros, higher to
      accomodate extremely sluggish systems.  Only in pathological cases is
      it necessary to modify these parameters.  The call command resets
      these parameter to their defaults.



      (C) 1994 Omen Tech Inc                    Chapter 6 Numeric Parameters



      DSZ Manual Addendum                                 Line Printer Draft
      40                                                  Numeric Parameters

      p Timeout in tenths of seconds for gaps within a packet (default 100).

      r If non zero, remove incomplete files received with a protocol except
        those received with the + option (default 0).

      R When non 0, limits the number of bytes of file comparision used with
        the sz and rz -rr option.  This parameter may be set to a value
        between 2048 and 32000 (1 billion on 32 bit systems).  This
        parameter is given to the receiving program.

        EXAMPLE: z pR30000


        SEE ALSO: -rr option

      s Timeout interval in seconds waiting for XON characters or positive
        flow control (default 15).  If an XON is not received within this
        time, transmission resumes anyway.  A value of 0 disables this
        timeout.

      t XMODEM, YMODEM, and ZMODEM Receiver timeout in tenths of seconds
        waiting for a packet or command acknowledgement (default 100).

      T Transmitter timeout in tenths of seconds waiting for a packet
        (default 600).
                                                  /
                                               ==|--
                                               == \
                                               ==
                                               ==
                                             [][][]

                      "I don't know what this thing does,
                      but it's pointing in your direction."
                      -Dr. Who, from A Usenet Signature


















      (C) 1994 Omen Tech Inc                Chapter 6 Hardware Compatibility



      DSZ Manual Addendum                                 Line Printer Draft
      Hardware Compatibility                                              41

      7.  HARDWARE/SOFTWARE COMPATIBILITY

      7.1  Hardware Compatibility Notes

      IBM PS/2 Model 50Z Early samples of this machine have a design error
        on the motherboard that causes comms programs to lock up the
        machine.  Replacing the motherboard with a correctly functioning
        unit from current production corrects the problem.  The part number
        of the replacement PS2/50 Z motherboard is 35F5928.  (Information
        provided by John M. Choma 73047,3566) In the U.S. IBM has
        stonewalled on this issue, but in December 1988 agreed to replace
        the defective motherboards under warranty.

      Zenith Computers Older Zenith computers may need a ROM update to work
        properly with interrupt driven programs such as YAM.

      NEC Multispeed The NEC Multispeed computer locks up unless STACKS is
        set in CONFIG.SYS.  In addition, one should disable floppy disk
        power save mode, and set popup program memory allocation to 0.  For
        best results, use the latest NEC software patches to the NEC MSDOS,
        and/or use an IBM PC-DOS instead of the DOS supplied by NEC.

      EGA/VGA Multimode Boards Some multimode EGA and VGA boards include an
        "auto select" feature designed to configure the board to various
        display standards using software trickery.  In the case of Paradise
        VGA and others, this feature causes excessive interrupt latency and
        loss of data at high speeds.  Disabling the auto select on the
        display board corrects this problem.

      EGA Wonder The BIOS in the ATI EGA Wonder has been observed to
        increase interrupt latency to the dismay of 9600 bps operation on an
        8 mHz no wait state AT clone.  There has also been a report
        (unexplained) that an EGA board has induced line noise in one
        instance.

      Tecmar Graphics Master To use YAM with this display board, give a mode
        mono command before running Pro-YAM.

      Leading Edge MODEMS and I/O BOARDS Some Leading Edge modems and
        interface boards use 8250 UART devices that do not respond correctly
        when the software turns the transmitter interrupts on and off.  High
        performance communications programs such as Professional-YAM require
        properly functioning UART chips, such as the National Semiconductor
        16450 or 16550A.









      (C) 1994 Omen Tech Inc                Chapter 7 Hardware Compatibility



      DSZ Manual Addendum                                 Line Printer Draft
      42                                              Hardware Compatibility

      7.2  Brain Damaged UARTS

      Omen Technology has received reports of problems with buggy 8250 type
      UART integrated circuits in Leading Edge modem boards, serial port
      interfaces, and computers.  The defective chip logic affects high
      performance software.  Replacing the buggy chip with a newer chip
      (NS16550AFN) corrects the problem.

      The UM82450 chip in the Zoom 2400HC also appears to cause problems.
      Zoom Telephonics advises that this problem is limited to their old
      model.  The old model has an external volume control.

      You can identify an old chip by inspecting the serial interface board
      for 8250 or UM82450 type devices.  A service technician or hardware
      hacker can help if you are not familiar with reading chip numbers.

      Dsz users can identify old chips with the following software command:

      EXAMPLE: dsz port 1 speed 2400 p

      The value for the P numeric parameter should be 1.  A value of 0
      indicates a non-buffered chip or a chip with a defective buffer.

      ZCOMM and Professional-YAM users can look at the printout produced by
      the s command;  old UART chips register as TYP 0.

      The National Semiconductor NS16550AFN is a pin compatible plug in
      replacement for 8250 and 16450 serial chips.  Omen Technology PCDOS
      software enables the FIFO buffer in the NS16550AFN to prevents loss of
      data from poorly written device drivers, TSR programs, etc.

      We are also using the Goldstar GM82C550 chip with a 9025 date code.
      This Goldstar chip is plug compatible with the National chips.  No
      problems have been discovered with this chip.

      The NS16550AFN has better electrical characteristics than the older
      UART chips.  386 and fast 286 machines should use the NS16550AFN for
      best results.  Omen Technology software has been written to allow time
      for the older UART chips to operate. However, there is a limit to how
      much the software can rearrange chip accesses without resorting to
      performance robbing wait loops.  Some other software is not as
      forgiving of slow chips.

      Be sure to ask for the NS16550AFN.  It is VITAL to get the National
      Semiconductor "AFN" or "AN" chip.  Other vendors' chips not mentioned
      above won't do.  Current Western Digital WD16C550 chips do not
      function properly at low speeds.

      As of this writing, the Goldstar GM82C550, National Semiconductor
      NS16550AN and NS16550AFN are the only plug compatible chips that are
      known to work.


      (C) 1994 Omen Tech Inc                Chapter 7 Hardware Compatibility



      DSZ Manual Addendum                                 Line Printer Draft
      Hardware Compatibility                                              43

      If your UART chip is soldered in or otherwise not replaceable, you
      will need a new plug-in board with a good UART chip.  The cheapest
      such board to date is the KW-524E-1 Serial/Parallel/Game card, $30.90
      from TSD Systems, 800-331-9130 (FAX 407-331-8130).  A board populated
      with two FIFO UARTS is $41.85.

      The Hayes ESP board comes with two serial ports with NS16550AFN
      devices.  The ESP definitions for COM3 and COM4 agree with the
      industry standard definitions used by Omen Technology.  All option
      switches on the ESP board should be OFF except those used to select
      the port number (COMn).


      The $99 "WinSport II" from Boffin LTD 612-894-0595 has two NS16550AFN
      FIFO UARTS and also supports MobyBaud (18.432 MHz clock).  This card
      also supports higher IRQ numbers, freeing up the low IRQs for other
      applications.

      Software Electronics 503-640-1946 sells a $59 board with two FIFO
      UARTS and a bidirectional enhanced parallel port.

      The following information comes from a number of people:

      "I have located a small dealer in New York who has the cards with or
      without the 16550.  I believe the price is around $50.00.  The company
      is RJK Consulting and the number is 718-968-9167. The gentleman to
      speak to is a Mr. RJ Kulman. ...  I got this information off the
      "Interlink" BBS system." Fm: Nick Braak [TRICON] 75156,1254

      Fry's - 415-770-FRYS.  This is a Silicon Valley electronic department
      store.

      Jameco Electronics at 415-592-8097 800-538-5000 sells National
      NS16550AFN chips mail order (credit card) in small quantities.
      Unfortunately, we received a number of reports (none recently) that
      their serial i/o card was supplied with the defective WD16C550
      soldered in, even when ordered with specific instructions to include
      16550AFN chips.

      TSD Systems advertise a 2 serial/parallel/game card with one or two
      NS16550-AFN chips.  800-331-9130(voice) 407-331-8130(fax)

      Microprocessors Unlimited, 24000 South Peoria, Beggs, OK. (918) 267-
      4961. The price for the chip is $13.50 plus shipping costs.

      Consolidated Computers 4 Shoppers Lane Suite 121 Turnersville, NJ
      08012 (609)751-9595(voice) (609)751-3843(bbs) (609)751-3840(fax)

      Arrow Electronics at 800-932-7769 (516-467-1000).

      Willies Computer Software Company: 800/835-4832.


      (C) 1994 Omen Tech Inc                Chapter 7 Hardware Compatibility



      DSZ Manual Addendum                                 Line Printer Draft
      44                                              Hardware Compatibility

      N.B.: Current Western Digital WD16C550 chips do not function properly
      at low speeds.  This has been confirmed with samples received directly
      from Western Digital.  WD is aware of this problem, but has not
      informed us of a corrected chip.


      7.3  Software Compatibility

      Some programs and device drivers affecting the operation of PC-DOS may
      interfere with YAM, especially when YAM is operating at high baud
      rates.  Historically, loss and corruption of data have been caused by
      memory resident programs.  Some of these programs increase interrupt
      latency preventing YAM from reading a character from the UART holding
      register before the next character comes in on top of it.  In other
      cases, programs do not properly restore the state of the machine when
      they exit from interrupts.

      If such a problem is suspected, run YAM without any memory resident
      programs or special drivers to locate the source of the problem.  Once
      the offending program is identified, a call to the program's vendor
      may obtain a corrected version.

      The design of memory resident programs is a little known black art.
      Subtle bugs, non reproducible interactions, and magic combinations are
      commonplace results of attempts to impose various aspects of
      multitasking on top of an operating system that was not properly
      designed to permit such extensions.  Omen Technology Incorporated may
      be able to help identify these interactions if provided with the
      source code of the offending programs.

      Some of the known troublemakers are mentioned below.

      Smartdrive This disk cache program (Windows 3.1 version) has been
        observed to cause communications errors even when a FIFO UART is
        used.

      BREAK ON This DOS command causes ^C to be intercepted by DOS at
        various, sometimes awkward, times.  BREAK ON must be used with
        extreme caution as interrupting most programs with ^C compromises
        the integrity of the file system.  If a program is interrupted by ^C
        or Ctrl-Break, the file system should be immediately checked with
        CHKDSK.  In some cases it may be necessary to reboot DOS with Ctrl-
        Alt-Del if DOS runs out of file descriptors.  A synonym for BREAK ON
        might be NUKE FILESYSTEM ON.

        Someday MicroSoft may discover what to do with ^C (DEC figured it
        out about two decades ago).  In the meantime, we recommend you not
        use it.  When Professional-YAM starts up, it stores the status of
        the BREAK ON flag, then clears it.  On Exit, or when calling a DOS
        program, YAM restores the BREAK ON flag to its previous state.



      (C) 1994 Omen Tech Inc                Chapter 7 Software Compatibility



      DSZ Manual Addendum                                 Line Printer Draft
      Software Compatibility                                              45

      Disk Cache Programs Microsoft SMARTDRVIVE Norton NCACHE Multisoft
        PCQWIK Many disk cache programs tie up the computer long enough to
        lose modem data.  (It only takes a few thousandths of a second!)
        Some disk cache programs are worse than others.  Some are so bad not
        even a FIFO UART can overcome them.

        Some programs (SMARTDRV) can be set to cache disk reads only,
        avoiding the delayed writes that disrupt file downloads.

      Mouse Drivers Some mouse drivers have been reported to interfere with
        file transfers.

      DOS append command The DOS append command allows one or more
        directories to be partially "grafted on" to a specified directory.
        Some DOS system calls "see" files in the new directory, some do not.
        This interferes with file transfer options such as -y, -r and -n.
        If the DOS append command must be used, use the /x:on switch.

      TOPDOS TOPDOS, ver 2.00i by Frontrunner Development Corp., has caused
        ZCOMM and other programs to lock up.  Disabling TOPDOS restores
        normal operation.

      DOS 3.2 DOS 3.2 introduces the concept of a fixed number of interrupt
        stacks.  The default value chosen is not always sufficient, and DOS
        3.2 sometimes prints the infamous Internal Stack Failure message and
        cheerfully halts the computer.  Adding the line STACKS=20,128 to the
        CONFIG.SYS file should correct the problem.  Lacking any useful
        documentation from Microsoft, you may wish to experiment with
        different values.

      Extended Memory RAMDISKS Extended Memory electronic disks (ramdisks)
        require the 80286 chip to switch in and out of protected mode during
        block transfers.  A hardware reset pulse is used to switch back to
        the "real mode" required for DOS.  This causes loss of modem data at
        high speeds.

        It may be possible to reduce excessive interrupt latency by reducing
        the length of protected mode block transfers to 128 or less.  In one
        instance, replacing the ROM BIOS with a newer version increased the
        maximum transmission speed without losing characters to 9600 bps.

        This problem has not been observed with expanded memory
        (Intel/Lotus/AST/etc.) ramdisks.

        The new generation NS16550AN or 82510 serial interface circuits
        should be used instead of 8250's for best results at high speed.
        The NS16550AN allows operation at a communications speed of 115200
        bps compared to 9600 bps (typical) for the 8250 and 16450.

      Disk Drivers Disk drivers, especially hard disk drivers for 80286
        machines, lock out interrupts for varying periods of time.  The


      (C) 1994 Omen Tech Inc                Chapter 7 Software Compatibility



      DSZ Manual Addendum                                 Line Printer Draft
      46                                              Software Compatibility

        actual interrupt latency depends on the speed of the computer and
        the particular BIOS code used.  In one case, upgrading to a newer
        BIOS allowed operation at 38400 bps, compared to 4800 bps
        previously.  Such an improvement is well worth the small ($25
        typical) cost of a new set of ROM BIOS chips.

      DOS 3.x Each new version of PC-DOS adds new features and eats up more
        of the 8088's meager resources.  DOS 3.2 increases interrupt latency
        enough to interfere with YAM's operation at 19200 bps on an IBM PC.
        If this is a problem, switching to DOS 2.1 will reduce the interrupt
        latency.  Replacing 8250 and 16450 serial interface chips with the
        new NS16550AN chip allows YAM to operate smoothly at high speeds.

      FANSI-Console Versions of this program before 1.07 did not maintain
        the pointer to the active display board in the IBM documented memory
        location.  A DOS mode command may cause YAM to reference the wrong
        display adapter address.  This caused incorrect sync signals and
        possible damage to certain monitors.  Current versions (2.X)
        increase interrupt latency enough that the serial line drops
        characters when the keyboard is touched.

      Seaware Batch Versions of this program has been known to cause loss of
        data.

      Spotlight/Lotus Metro This TSR program has been reported to cause
        Pro-YAM to lock up.

      Pathname Modifiers Programs such as FILEPATH and GLOBALS allow files
        to be visible in more than one directory at a time.  Such programs
        may interfere with security when YAM is restricted, since that
        security is based on restricting access to directories.  In general,
        sensitive files should not be made global when YAM is made
        accessible to outside callers.

        Pro-YAM may not recognize file names generated by such programs
        unless the program traps the DOS FINDFIRST calls as well as the file
        open calls.

        We have received various reports of strange behavior which have been
        traced to filesystem modifications caused by such programs,
        including damaged file systems.  We recommend such programs be
        phased out as soon as possible, as they may not operate at all with
        future versions of DOS or distributed file systems.

      BRKBOX This program locks out interrupts up to 17 milliseconds while
        waiting for the vertical retrace.  For a communications program, 17
        milliseconds is a very long time, and data will be lost at speeds
        above 300 bps.

      CGCLOCK Programs such as CGCLOCK.COM use clock interrupts to update a
        time display on the screen.  Some increase interrupt latency so much


      (C) 1994 Omen Tech Inc                Chapter 7 Software Compatibility



      DSZ Manual Addendum                                 Line Printer Draft
      Software Compatibility                                              47

        that YAM cannot respond in time to accept characters from the
        remote, even at 1200 baud.

      Concurrent PC-DOS YAM runs under Version 4.1 of Digital Research
        Concurrent PC-DOS (CPCDOS).  The - numeric parameter must be set to
        0.  The CPCDOS "addmem" command should be used to allocate extra
        memory if DOS Gateway are to be used.

      ANSI.SYS YAM uses direct keyboard input from the ROM BIOS because the
        DOS keyboard input calls do not handle Ctrl-BREAK properly.  As a
        side effect, keyboard keys redefined by ANSI.SYS have no effect on
        YAM's operation.  It is possible to program some of the keys to call
        YAM with arguments.  The following file, reassigns ALT-C, ALT-H, and
        ALT-V to execute the commands shown below.  The $ character
        represents ESCAPE.

              $[0;46;"cd \tmp";13;"YAM call -200 cbbs-r";13p
              $[0;35;"YAM call host";13p
              $[0;47;"cd \tmp";13;"YAM call cissig";13p

        YAM uses the ROM BIOS CRT functions and direct output to the
        display, bypassing any processing provided by ANSI.SYS.  Perhaps
        someday Microsoft will enhance ANSI.SYS to make it useful for
        programs like YAM ...

      PRINT.COM Once the DOS PRINT program is memory resident, file
        downloads at high speeds (38kb on a PC) suffer from interference,
        even if a file is not currently being printed.

        With certain printers, the DOS PRINT command will preempt the
        running program for several seconds at a time.  These "swapouts" can
        be confusing when you are accessing an interactive application.
        They may interfere with file transfers, especially if the remote
        program uses "tight" timing.  If this happens, PRINT should be
        suspended during file transfers.  Operation of the PRINT command
        does not appear to cause loss of data downloaded from timesharing
        services at 1200 bps, as long as the interruptions last less than
        ten seconds.  Perhaps IBM or Microsoft will someday fix this bug in
        the DOS PRINT command.  PRINT should not be invoked from YAM for the
        first time as DOS memory allocation will become fragmented.

        If PRINT or some other spooler is outputting to a serial port using
        the BIOS INT 14h serial port driver, YAM's "!~subprogram" command
        will redirect the printer output to the remote and thus should be
        avoided.

      SWITCHAR = -  YAM will work properly when the DOS switch character is
        set to "-", allowing Unix style pathnames.  The - numeric parameter
        must be set non zero to allow YAM DOS Gateway to use / to delimit
        directories.



      (C) 1994 Omen Tech Inc                Chapter 7 Software Compatibility



      DSZ Manual Addendum                                 Line Printer Draft
      48                                              Software Compatibility

        It may be necessary to remove this line from CONFIG.SYS and reboot
        DOS before using the IBM dump and restore commands.
        N.B.: DOS 3.0 does not support SWITCHAR in the config.sys file.  A
        short program, DASH, will set switchar to -.  It prevents many
        oaths.  Microsoft has removed all SWITCHAR support in DOS 5.0.  So
        much for POSIX compliance.


      This manual is Copyright 1992 Omen Technology Incorporated, All Rights
      Reserved.

      It was formatted 1-27-94.









































      (C) 1994 Omen Tech Inc                Chapter 7 Software Compatibility



      DSZ Manual Addendum                                 Line Printer Draft
      Software Compatibility                                              49

      8.  CROSS REFERENCE INDEX




















































      (C) 1994 Omen Tech Inc                Chapter 8 Software Compatibility





                                  Chuck Forsberg



      8.  CROSS REFERENCE INDEX


















































      (C) 1994 Omen Tech Inc                 Chapter 8 Cross Reference Index



      Version 18.09 TurboDial 2.36                        Line Printer Draft
                              Cross Reference Index

      4 kb packet length 32                file date 5, 9
      50Z 41                               file download 14, 14
      7 bit data 29                        file name override 24, 26
      80286 45                             file transfer 24, 24, 25, 26, 27
      8250 UART 42                         file transfer packet length 32,
      ANSI.SYS 47                          32
      append 29                            Flow Control 18, 22, 31, 35, 37,
      append DOS command 29, 45            39, 40
      batch file transfer 24, 25, 26,      frame length 38
      27                                   front end 30
      baud rate 46                         GEnie 16
      BIX Timesharing Service 17           graphic file transfer display 3
      Block length 7, 38                   handshake 18
      Break 37                             handshake command 21
      BREAK ON 44                          hard disk 45
      Byte Information Exchange 17         Hayes ESP board 43
      Cache, disk 45                       IBM PS/2 Model 50Z 41
      carrier detect 21, 23                image option 32
      Clear to Send 21, 22                 interrupt latency 45, 46
      Clink 24, 26, 39                     Kermit 33
      collision 30                         Lempel-Ziv 36
      comm port 22                         Lotus Metro 46
      compression 6, 36                    LZW 36
      CompuServe 25                        minirb program 14
      Concurrent PC-DOS 47                 MobyKermit 33
      control character escaping 30        MobyTurbo 6, 33
      CPCDOS 47                            modem port 22, 23
      CPMEOF 10, 10, 11, 26                MODEM protocol 25, 26
      CR 14, 29                            Mouse Drivers 45
      Crash Recovery 5                     Multispeed 41
      CRC-16 24, 26, 30                    NEC Multispeed 41
      CTS 21, 22                           newline 29
      Cybernetic Data Recovery 38          no carrier detect 21, 23
      data PBX 30                          ONAME= 26, 27
      Data Set Ready 21                    options 24, 24, 25, 26, 27, 29
      date stamping 5, 9                   OverThruster 9, 11, 25
      DCD 21                               packet length 38, 38
      delete 35, 36                        PAD 19
      directory specification 24           pathname override 24, 26
      disk cache 45                        pathname, full 30
      DOS 3.2 45, 46                       pathnames, received 24, 25
      DOS append command 29, 45            pathnames, transmitted 26, 27
      DSR 21                               PBX, data 38
      EGA Auto-select 41                   PC Pursuit 19
      Emacs 18                             PC-Pursuit 39
      erase 36                             Performance log 35
      estimate command 21                  port command 22
      Extended memory 45                   portx command 23
      FANSI-Console 46                     PREFIX= 26
      Fastcomm 39                          PREFIX=p 27
      FIDO 24, 26, 39                      printer spoolers 47


      (C) 1994 Omen Tech Inc                 Chapter 8 Cross Reference Index



      Version 18.09 TurboDial 2.36                        Line Printer Draft
                              Cross Reference Index

      Qmodem-G 12, 32                      XON 18
      RAMDISK 45                           YMODEM 9, 12, 18, 24, 26
      rb command 24                        YMODEM-4k 32
      rc command 24                        YMODEM-g 11, 24, 25, 31
      Relaxed XMODEM 11                    Zenith 41
      Relaxed YMODEM 11                    ZMODEM 4, 25, 26, 29, 33, 36, 37
      remove 35                            ZMODEM protocol 27
      RLE compression 36
      ro command 25
      rx command 25
      rz command 25
      sb command 26
      SCRtoPS 3
      SEAlink 24, 26, 39
      security 24, 26
      Serial Number 35
      SlugBait 35
      Smartdrive 44
      Spotlight 46
      STACKS= 45
      Stream_LF record format 32
      Streaming XMODEM 12
      Subpacket length 7
      SWITCHAR 47
      sx command 26
      sz command 27
      Telenet 19
      Telink 39
      term function 35
      Terminal Multiplexers 8
      Thedraw 3
      time zone 5, 9
      Timing 40
      TOPDOS 45
      transparency 30
      Unix 13
      unlink 35
      VAX/VMS 15
      VDISK.SYS 45
      VGA Auto-select 41
      view 35
      VMS 15, 32
      VMS Stream_LF record format 32
      window size 19, 35, 39
      X.PC 10, 11, 31
      XMODEM 10, 10, 18
      XMODEM Protocol 25, 26
      XMODEM-1k 10
      XMODEM-4k 32
      XMODEM-CRC 10
      XOFF 18, 40


      (C) 1994 Omen Tech Inc                 Chapter 8 Cross Reference Index