This is the wiring diagram for the cable necessary to link two
machines together by their parallel ports.  This is the same wiring
diagram used by a Turbo LapLink cable, available for sale from many
PC parts outlets.

1 - 1
2 - 15
3 - 13
4 - 12
5 - 10
6 - 11
7 nc
8 nc
9 nc
10 - 5
11 - 6
12 - 4
13 - 3
14 - 14
15 - 2
16 - 16
17 - 17
18 nc
19 nc
20 nc
21 nc
22 nc
23 nc
24 nc
25 - 25 (ground)