FCL Construction
      A segment is the basic module in the GAF system.  A typical FCL file
      contains a segment and optional configuration like this.

            configuration_declaration

            segment_declaration

                  cycle_declaration

                  variable_declaration(s)

                  symbol_declaration(s)

                  preset_declaration(s)

                  init_run_declaration

                  rule_declaration(s)

            end_declaration

Configuration: configuration_declaration
      FCL allows configuration information been declared for specific
      module(s).  The configuration declaration must be enclosed inside
      following key words.  Please refer GAF.DOC for more detail about
      configurable attributes and values.
            CONFIGURATION
                  attribute = value;
                  . . .
            END_CONFIGURATION;

Declare Segment: segment_declaration, end_declaration
      There are three types of segments: normal control segment, feedback
      segment, and evaluation segment.
      Format for segment_declaration:
            FORMAT       SEGMENT seg_name
                         FEEDBACK seg_name
      Format for end_declaration:
            FORMAT       END seg_name ;
            Where
                  seg_name     : the name of the segment
            Example
                  SEGMENT main_control
                         CYCLE_TIME 0.1
                         . . .
                  END main_control;

      The key SEGMENT declares a normal control segment or an evaluation
      segment.  Use the key FEEDBACK to declare a feedback segment.  In
      simulation and adapt modes the feedback segment's output value will be
      feed back to the control segment(s) based on variable name(s).

Define Cycle Time: cycle_declaration
            FORMAT       CYCLE_TIME value
            Where
                  value        : the cycle time in seconds
            Example
                  SEGMENT main_control
                         CYCLE_TIME 0.1
                         . . .
                  END main_control;

      Cycle_time defines how frequently the segment runs.  For example a
      value of 0.1 defines the segment runs every 100 milliseconds.  Note that
      actual delay time between two consecutive runs may be longer than 100
      milliseconds if GAF is heavily loaded with segments.


Declare Variable: variable_declaration
      There are four different kinds of variables: IN, OUT, INOUT, and LOCAL. 
      The segment will only read (reference) from those IN variables, and write
      (generate new value) to the OUT variables.  The segment can read and
      write to both INOUT and LOCAL variables, however, local variables are
      not visible from outside the segment.
            FORMAT       var_type seg_name (min_value, max_value)
            Where
                  var_type     : one of the 4 types IN OUT INOUT LOCAL
                  var_name     : the variable name
                  min_value    : the minimum value of the variable
                  max_value    : the maximum value of the variable
            Example
                  SEGMENT main_control
                         CYCLE_TIME 0.1

                         IN          Reference   (0, 100)
                         OUT         Result      (0, 10)
                         LOCAL       Temp        (-1, 1)
                         . . .
                  END main_control;
      Variable name must be unique in the same segment.  A variable should not
      be declared as an output variable (OUT or INOUT) in more than one
      segments.

Declare Fuzzy Symbol: symbol_declaration
      The basic fuzzy membership set definition is a trapezoid with 4 points
      below, low, high, above, and a max_truth value.

                   _____            <----- max_truth: maximum truth value
                  /     \
                 /       \
                /         \
        -------+--+-----+--+------- <----- 0: minimum truth value
               |  |     |  |
               |  |     |  above: false above
               |  |     high: high truth
               |  low: low truth
               below: false below
      As depicted in above diagram, the truth for different values are:
            if value <= below        truth = 0
            if value >= above        truth = 0
            if low <= value <= high  truth = max_truth
            for other values use interpolation to derive truth
      The range of truth value is 0.0 to 1.0.

            FORMAT       SYMBOL sym_name [OF var_name] fuzzy_membership_set
            Format for fuzzy_membership_set
                         ( below, low, high, above [, truth [, center ] ] )
            Where
                  sym_name     : the name of the symbol
                  var_name     : the name of the variable for this symbol
                  fuzzy_membership_set
                               : defines the four points of a membership set and
                  truth        : the max truth value
                  center       : the center value
            Example
                  SEGMENT main_control
                         CYCLE_TIME 0.1

                         IN    Reference   (0, 100)
                         OUT   Result      (0, 10)
                         LOCAL       Temp  (-1, 1)

                         SYMBOL small OF Reference (0, 0, 10, 20, 1.0)
                         SYMBOL strong  (8, 9, 10, 10, 1, 10)
                         . . .
                  END main_control;
      The fuzzy symbol declaration is used to declare a named fuzzy
      membership set.  This named symbol can then be used in the fuzzy rules. 
      The symbol defines the shape of a trapezoid fuzzy membership set, as
      described above, and the optional truth value and the center value.  If
      the center value is specified, GAF uses this value, otherwise GAF
      calculates the center of gravity as the center value.  A generic symbol
      can be defined for all variables or defined for a specific variable with
      "OF var_name" option.  If a symbol is defined for a specific variable, it
      can only be used for that variable.  Symbol names are not required to be
      unique in a segment.  For example, two symbols "VERY_SMALL" can be
      defined for two different variables "SPEED" and "POPULATION" with two
      different shapes.

Initialization and Run : init_run_declaration
      Initialization declaration is a sequence of assignments to initialize the
      segment.  The run declaration is a sequence of assignments with
      conditional branch to be executed every cycle.

            FORMAT       INITIALIZATION
                               calc_statement(s)
                         BEGIN
                               calc_statement(s)
                         END;
      Where calc_statement is a math calculation statement, in C++ C syntax
      with optional conditional IF THEN ELSE ENDIF constructions.  The
      supported calc operators are: + - * / > < >= <= = and <>.  For example:
            Example
                  INITIALIZATION
                         speed = 0;
                  BEGIN
                         IF position > 50 THEN
                               speed = 3.5;
                         ELSE
                               speed = speed + 2;
                         END IF;
                  END;
      The statements between INITIALIZATION and BEGIN defines how to
      initialize the segment at startup or requested by user.  The statements
      between BEGIN and END define the run calculation of this segment.  Every
      time GAF runs this segment, it goes through all statements defined then
      evaluates all fuzzy rules.

Declare Preset: preset_declaration
      Just like the initialization declaration, a preset declaration is a
      sequence of assignments to setup the segment to a known state. 
      Normally this is done by assigning values (constants) to local and output
      variables.  There is no limit of the number of presets in a segment. 
      Presets are used for genetic adapt for testing new rules' result.  They
      also can be requested by user during simulation and check modes.  Please
      refer to INITIALIZATION for format.
            Example
                  PRESET
                         Reference = 100;
                         Position = 0;
                  END ;

Define Rule: rule_declaration
      FCL uses IF THEN construct to define a fuzzy rule.  The IF statement
      contains multiple fuzzy evaluations bound with AND or OR.  The format of
      fuzzy evaluation is defined as:
                  variable IS symbol
      which describes "What is the truth value of the current value of
      'variable' in the fuzzy membership set 'symbol'?". The result of the
      evaluation will be the truth value between 0 and 1 as described in the
      symbol_declaration.  The overall result of the IF statement will be the
      fuzzy AND/OR result (min/max of all truth values).

      The THEN statement contains only one fuzzy induction.  The format of a
      fuzzy induction is one of these forms:
                  variable IS symbol
                  variable  + symbol
                  variable  - symbol
      The variable must be an OUT, INOUT, or LOCAL variable.  The first format
      simply defines the result of 'variable' is the 'symbol' fuzzy membership
      set with the max truth be the overall result from the IF statement.  The
      second and third format is to increment/decrement the current 'variable'
      by the amount defined by 'symbol'.

            Example
                  SEGMENT main_control
                         CYCLE_TIME 0.1

                         IN    Reference   (0, 100)
                         IN    Speed       (-1, 1)
                         OUT   Result      (0, 10)
                         LOCAL       Temp  (-1, 1)

                         SYMBOL small OF Reference (0, 0, 10, 20, 1.0)
                         SYMBOL slow OF Speed (0, 1, 2, 3, 1)
                         SYMBOL strong  (8, 9, 10, 10, 1, 10)

                         IF Reference IS small AND Speed IS slow
                         THEN Result IS strong

                         . . . .

                  END main_control;

      A rule can be repeated more than once in a segment to intensify the
      effect of the rule.