To run the W0RLI MailBox under DESQview do the following steps:


	   1) Using DESQview SETUP:

Under performance:

  Set the swapping time slices:

  For 6 Mhz AT, try 6 foreground and 6 background.
  For 4.77 Mhz XT, try 24 foreground and 24 background.
  For 25 Mhz 386/486, try 3 foreground and 3 background.

  Common Memory 		     12
  Dos buffer for EMS		      0
  Optimize communications	      N
  Allow Swapping of programs	      Y
  Manage printer contention	      N

Under Logical drives:
 logical drives:	       none
 swap drives   :	       none

Under video monitor:
 video monitor :	       for EGA use 3....CGA option for color
			       gives maximum memory. Mono is the best for
			       memory.
  display text/graphics        Y if you want the screen blanker to work.
  Monitor require sych access  N
  Screen blanker	       What ever is appropriate. If disp text graphics
			       not set to y then it will not work.

	   2) Set up the MailBox window:


Program Name:		       MB
Key to use on open menu:       MB	       [Anything you like]
Memory Size (in K):	       80
Program:		       MB.EXE
Parameters:
Directory:		       C:\BBS	       [Where you put MB.EXE]
Writes directly to screen:     N
Displays graphics information: N
Virtualize text/graphics       N
Uses serial ports (Y,N,1,2)    N
Requires floppy diskette:      N

ADVANCED OPTIONS:
System Memory:		       0
Maximum Program Memory Size:
Script Buffer Size:	       1000
Max Expanded Memory Size:
Text Pages:		       1
Graphics Pages: 	       0
Interrupts:		       00 to FF
Close window on exit to DOS:   Y
Allow close window command:    Y
Uses math co-processor:        N
Uses own colors:	       N
Can be swapped out	       N
Runs in background:	       Y
Keyboard Conflict:	       1  or 0
Share EGA when fore/zoomed     Y  for EGA only
Protection level	       0     <-  This must be 0 !