README FILE FOR FATIGUE IN ENGINEERING MATERIALS (Fatigue.zip)
    ==============================================================

OPERATIONAL DETAILS
ßßßßßßßßßßßßßßßßßßß
Exploding windows are used for data entry. Most groups of data entered 
require a second enter key hit to accept the final values. Entering 
the decimel point will always right justify the number in the cell
but is not required. The file: tmsrb.fon should be in the same directory
as fatigue.exe.

This program covers four basic areas of fatigue:

     1) Mean Stress Conversions
     2) Modified Goodman Analysis
     3) Cumulative Damage Analysis
     4) Local Strain Analysis

MEAN STRESS CONVERSIONS
ßßßßßßßßßßßßßßßßßßßßßßß

Most fatigue data obtained from the laboratory is for completely reversed 
alternating stresses (zero mean cyclic stress). Being that most real world 
applications involve nonzero mean cyclic stress, it is important to have a way 
of converting nonzero mean cyclic stress data to its equivalent zero mean 
cyclic stress. These conversions are performed using the following
relationships:
		ù Smith's Relationship
		ù Goodman's Linear Relationship
		ù Gerber's Parabolic Relationship
		ù Elliptic Relationship

MODIFIED GOODMAN ANALYSIS
ßßßßßßßßßßßßßßßßßßßßßßßßß
For high cycle fatigue, the modified Goodman relationship is very popular. This
method produces a range of stress diagram where points inside the diagram
represent the condition that failure will not occur in N cycles, and points 
located outside the diagram represent the condition that failure will occur 
with fewer then N cycles.

Provisions for handling multiaxial fatigue are included.

CUMULATIVE DAMAGE
ßßßßßßßßßßßßßßßßß

The cumulative damage module consists of a basic spreadsheet for
computing the cumulative damage. The linear damage rule is used. Each
damage fraction is calculated and then summed. If the result is > unity,
failure is predicted to occur.

LOCAL STRESS/STRAIN ANALYSIS
ßßßßßßßßßßßßßßßßßßßßßßßßßßßß
The local strain analysis module consists of three seperate programs used 
in modeling the crack initiation phase of fatigue failure. This module uses 
numerical methods which are not "funny numbers" proof and will abort if
unreasonable numbers are entered.
 
The first program is called Cyclic Stress/Strain and is used to obtain 
the cyclic stress/strain curve.

The second program is called Strain Versus Life and solves the empirical
expression for total strain amplitude versus life.

The third program is called Notch-Root Stress/Strain and is used to obtain
the stress range with a stress concentration factor.