XIRCOM CREDITCARD ETHERNET ADAPTER FLASH UPDATE UTILITY
			      INSTALL DOCUMENT
			   Release 2.13 Revision E
			      December 16, 1993
   =======================================================================


   When CEUPDATE.EXE is running, power to the computer must NOT be 
   interrupted or the Xircom Adapter could be damaged.  We suggest
   therefore, that the user does not rely on an internal battery alone.  Power
   to the computer must be from a wall socket.

   No PCMCIA Card Services drivers can be running at the same time as the 
   CEUPDATE.EXE.  The program does detect for these Card Services and will 
   exit out when a Card Service is detected.  The Card Service drivers will
   need to be removed from the CONFIG.SYS or boot the system from a floppy
   drive that has no CONFIG.SYS.  Once the card has been updated the Card
   Service drivers can be restored.

   Refer to the README.DOC that accompanies this file for other information
   on CEUPDATE.EXE   


   Instructions: 
   
   The Flash Update Utility is designed to use only one memory window.  
   This memory window by default is at D000:0000 but can be user specified 
   by using the command line option "-m".
   
   To invoke the flash update type:  CEUPDATE.EXE.  Messages will be displayed
   from the update utility reporting success or failure.  CEUPDATE.EXE is the 
   only file needed to perform this update.

   After using CEUPDATE.EXE, reboot the system.   

   To verify that the CEUPDATE.EXE utility upgraded the firmware to revision
   'E', use CETEST.EXE.  It should display 'Rev. E' in the Model: field.
   
   The utility does not function on the following computers:
   =========================================================            

		Gateway 2000 Colerbook:  PCMCIA slot does not go to 12v.
		Grid Convertible Pentop: PCMCIA slot does not go to 12v.
		IBM 720 Thinkpad

   ===============================[  END  ]================================