XIRCOM CREDITCARD ETHERNET ADAPTER
				README DOC
			       Release 2.00
			     December 16, 1993
     ========================================================================
     Thank you for purchasing the Xircom CreditCard Ethernet Adapter.  Xircom
     has done everything to ensure that our CreditCard Ethernet Adapter is
     compatible with notebooks that support the Personal Computer Memory Card
     International Association's (PCMCIA) 2.0 to 2.1 I/O slot configuration.  
     Xircom is committed to making all of its networking products compatible 
     with the widest range of notebook and laptop PCs possible.  As a company,
     we are equally committed to customer satisfaction and timely response to
     the needs and concerns of our customers.  

     As this technology evolves and more PCMCIA 2.0 and 2.1 PCs become 
     available, you can be assured Xircom will continue to provide the 
     highest level of hardware and software compatibility in the industry.

     If you have compatibility issues related to your specific environment, 
     or you have general questions, please contact Xircom Technical Support.
     Information on Xircom Technical Support is located at the end of this 
     file.

	Remember to register your Xircom CreditCard Ethernet Adapter
	to receive information about future software upgrades and
	new products.
		      
	
	CONTENTS:
	---------

	1)  CreditCard Ethernet Adapter Characteristics
	2)  New features in this release
	3)  CECFG.EXE notes
	4)  Microsoft Windows for Workgroups v3.11 with Netware Configuration
	5)  IBM OS/2 LAN Requester installation (for IBM OS/2 LAN Server 
	    version 3.0)
	6)  Special software notes
	7)  Machine specific notes
	8)  Xircom Technical Support
     
     CREDITCARD ETHERNET ADAPTER CHARACTERISTICS
     ==================================================
     This release of Xircom's CreditCard Ethernet Adapter has the following
     characteristics:

     - Card and Socket Services set versions 2.0 to 2.1 compatibility.  
       Card and Socket Services is a software specification defined by the 
       PCMCIA organization.  Its purpose is to serve as an intermediary 
       between the network device driver and the system resources required by 
       the PCMCIA Adapter.
     
     - Intended for use with Intel 82365 PCIC, Sharp PHIC, Databook TCIC, 
       Cirrus Logic CL-PD6710 or CL-PD6720 or Toshiba ICCNT PCMCIA 
       interface chips.

     - Variable interrupts, 3 to 15, default interrupt 5.

     - Variable I/O window, 16 bytes needed, default base at 300h.

     - Requires a 8Kbyte memory window on a 8Kbyte boundary, within segment
       C000h to E800h, default is D000h.

     - Keyword support to disable link integrity.

     - ODI, NDIS for OS/2 2.1 and DOS support, and PACKET drivers.
	

     FEATURES OF NEW RELEASE
     =======================
      
      Features of release 2.0 of the Xircom CreditCard Ethernet
      Adapter Network drivers from previous releases:
	    
      -  Advanced Power Management for suspend/resume through the use of Card
	 and Socket Services
      -  Increased performance from Memory Mapped I/O mode
      -  Support of Cirrus Logic PCMCIA controller in operating the 
	 CreditCard adapter in both 8 and 16 bit mode
      -  OS/2 version 2.0 and above support for DOS and NDIS
      -  Hot swapping through the use of Card and Socket Services
      -  Artisoft LANtastic 5.0 support
 
     
     CECFG.EXE CONFIGURATION UTILITY
     ===============================
     Supplied on this disk is a utility called CECFG.EXE.  The utility can be
     run from the DOS command line or included in the AUTOEXEC.BAT file or the
     CONFIG.SYS file.  It is recommended that CECFG.EXE be run prior to
     loading any DOS Xircom network driver.  This utility is intended for DOS
     usage only. 

     The CECFG.EXE utility must be informed about which type of network
     driver your network uses: NDIS, ODI, or Packet driver.  The CECFG.EXE
     file must be located in the same directory as the network driver.

     The CECFG.EXE allows the Xircom Credit Card to become a client of 
     Card Services.  This is mandatory to support the functions of Card and  
     Socket Services.  CECFG.EXE must be loaded prior to loading a network
     driver when using Card and Socket Services.


     MICROSOFT WINDOWS FOR WORKGROUPS V3.11 WITH NETWARE CONFIGURATIONS
     ==================================================================
     
     The following installation instructions are not available in the 
     manual.
     
     Begin by copying the Xircom ODI drivers as outlined in the
     Xircom Users Manual in the Novell NetWare section.  Copy 
     them into the Windows directory of the machine, run those 
     drivers at the top of the AUTOEXEC.BAT and log in to the 
     NOVELL server in the AUTOEXEC.BAT.

     After arriving at a DOS prompt, install Windows For 
     Workgroups 3.11 while you are simultaneously logged in to 
     the NOVELL server.  When the time comes to configure the 
     network portion of Windows For Workgroups, choose a Xircom 
     Pocket Ethernet Adapter II (ODI/NDIS3).  

     When choosing drivers, make IPX/SPX the default protocol.  
     Choose setup and choose ODI interface.  Windows For 
     Workgroups will modify your CONFIG.SYS, AUTOEXEC.BAT, 
     SYSTEM.INI, PROTOCOL.INI and NET.CFG files.  

     Edit the SYSTEM.INI and remove the [netcard] and [transport] 
     lines in the NETWORK DRIVERS section (denoted by Brackets 
     []).  When finished, it should match the stub in the 
     SYSTEM.INI below.  Modify the PROTOCOL.INI, NET.CFG and 
     AUTOEXEC.BAT replacing any reference to PE2ODI with CEODI. 

     Reboot the machine, log in to the NOVELL server and then 
     launch Windows.  After Windows launches, log in to Windows 
     For Workgroups.

     EXAMPLES:

     ************************************************************
     *                    CONFIG.SYS                            *
     ************************************************************
     device=C:\WINDOWS\HIMEM.SYS
     device=C:\WINDOWS\EMM386.EXE noems x=d000-d1ff
     FILES=50
     BUFFERS=32
     FCBS=16,8
     STACKS=9,256
     DEVICE=C:\WINDOWS\IFSHLP.SYS

     ************************************************************
     *                     AUTOEXEC.BAT                         *
     ************************************************************
     C:\WINDOWS\net start
     cd \windows
     cecfg driver=odi
     lsl
     ceodi
     ipxodi
     C:\WINDOWS\odihlp.exe
     netx
     f:
     login 
     C:\WINDOWS\SMARTDRV.EXE /X
     doskey
     path C:\WINDOWS;c:\dos;c:\
     SET TEMP=C:\WFW\TEMP
     prompt $p$g

     ************************************************************
     *                     SYSTEM.INI                           *
     ************************************************************
     [Network]
     winnet=wfwnet/00025100
     multinet=netware3
     FileSharing=Yes
     PrintSharing=Yes
     LogonDisconnected=yes
     EnableSharing=Yes
     UserName=PATTI
     Workgroup=XIRCOM
     ComputerName=PATTI
     Comment=patti
     logonvalidated=no
     reconnect=yes

     [NetWare]
     NWShareHandles=FALSE
     RestoreDrives=TRUE

     [network drivers]
     devdir=C:\WINDOWS
     LoadRMDrivers=No

     [Password Lists]
     *Shares=C:\WINDOWS\Share000.PWL
     PATTI=C:\WINDOWS\PATTI.PWL

     [NWNBLINK]
     LANABASE=0

     **********************************************************
     *                    PROTOCOL.INI                        *
     **********************************************************
     [network.setup]
     version=0x3110
     netcard=ms$xirc,1,MS$XIRC,4
     transport=ms$nwlinknb,NWLINK
     transport=ms$netbeui,NETBEUI
     lana0=ms$xirc,1,ms$nwlinknb
     lana1=ms$xirc,1,ms$netbeui

     [MS$XIRC]

     [NWLINK]
     BINDINGS=CEODI

     [NETBEUI]
     BINDINGS=CEODI
     LANABASE=1

     [net.cfg]
     PATH=C:\WINDOWS\NET.CFG


     [Link Driver CEODI]
     data=   Frame Ethernet_802.3
     data=   Frame Ethernet_SNAP
     data=   Frame Ethernet_802.2
     data=   Frame Ethernet_II


     ************************************************************
     *                           NET.CFG                        *
     ************************************************************
     link driver ceodi
     frame ethernet_802.3
     frame ethernet_802

	 ====== End of Windows for Workgroups instructions======


     LAN REQUESTER INSTALLATION (for IBM OS/2 LAN Server version 3.0) 
     ================================================================

     The following notes covers installation of the CENDIS.OS2 driver into 
     the above mentioned NOS.  This information is not provided in the 
     manual.
	1. Follow the instructions in your OS/2 documentation for an ADVANCED
	   LAN Requester installation.
	2. When installing and configuring the Requester component, under
	   Select Requester Services, choose "Neither of the above" for
	   messaging services, unless you know you need them and have the
	   information required for configuring these services.
	3. When you reach the Configure window, select LAN Adapter and 
	   Protocol Support, then under the OPTIONS window choose Copy
	   additional network adapter drivers.
	4. On the Copy Additional CreditCard Drivers window, type in the path
	   A:\NDIS, then insert the Xircom CreditCard Drivers diskette in drive
	   A: and follow the prompts.
	5. When the Options window is displayed again, select Configure 
	   Workstation and choose the Xircom CrediCard Ethernet Adapter with
	   IBM OS/2 NETBIOS protocol.
	6. Follow the prompts to complete the installation.
	7. Shut down OS/2 and reboot the PC.
	
		   
     SPECIAL SOFTWARE NOTES   
     ======================

     ***                     MEMORY MANAGERS                           *** 

     *** When using a memory manager be certain to exclude the memory  ***
     *** range being used by the CreditCard adapter.  An 8k range will ***
     *** need to be excluded with in C000 to E800.                     ***    
		example:   device=c:\dos\himem.sys
			   device=c:\dos\emm386.exe x=D000-D1FF
     *** This example excludes the D000 segment that is used by the    ***
     *** CreditCard in a default configuration.  If the CreditCard is  ***
     *** configured for a memory address different from the default be ***
     *** certain to exclude that memory address range in use.          ***
     
     - The OS/2 drivers available on the disk are intended to support OS/2 
       versions 2.0 and above.  These drivers do not support Microsoft OS/2 
       version 1.3.

     - When using the CEODI.OS2 driver in a OS/2 2.1 workstation environment 
       for attaching to a Netware 4.01 server, we have observed in certain 
       situations trying to login will generate an error "can not load a 
       segment of the program login".  If this occurs we recommend using 
       NWTOOLS.EXE in the netware subdirectory, on the workstation, to login 
       to the NW 4.01 server.
   
     - The drivers contained on this disk support promiscuous mode which 
       allows the drivers to be used with Lan Analyzer packages.  However, 
       the drivers only capture valid packets, the drivers will not report 
       those packet that are short, runt or have CRC errors. 

     - During installation of Netware Requester version 2.01 for OS/2, when 
       prompted for the source drive, which has default A:, insert the 
       Xircom CreditCard disk and hit return following prompted instructions.
       The CEODI.OS2 driver is located in the root of this diskette as well 
       in the ODI subdirectory for an easier installation.

     
     MACHINE SPECIFIC NOTES
     ======================
     

     NEC Ultralite VERSA
     -------------------
     If you are using Card and Socket services on the machine we recommend 
     setting the Xircom's CreditCard memory address to 'DE000'.  See the 
     Xircom manual appendix 'C' for configuration of memory keyword.

     
     Sharp 6781 and Dell 320 Sli
     ---------------------------
     If you are experiencing problems try the following.
     
     The above laptops may have an early version of Socket Services, built 
     into the BIOS, that is not compatible with newer PCMCIA software 
     specifications.  In this case, either the NET.CFG file must be edited to
     include the keyword string 'socketservices NO', or the PROTOCOL.INI 
     file must include the keyword string 'socketservices = NO'.  To use the 
     Packet driver load the drivers in the following manner:

	  cecfg driver=packet socketservices=no
	  cepd  socketservices=no

	** Sharp 6781 only **

     We recommend using memory segment D000 for the PCMCIA Card on the Sharp 
     6781, this is the default memory assignment. 
     
     The Sharp BIOS should also be configured.  On page 2-of-4 in the setup,
     underneath the section heading "Floppy Drives & IC Card," configure
     the third entry as follows:

	  Device 3 (Other):   IC Card COM Port:   COM3 I/O 3E8H, IRQ 5
     
     Also on page 3-of-4 in the setup have the heading EMS Pageframe: DISABLED
     
     Toshiba T3300SL and Grid Convertible
     ------------------------------------
     The above laptops must be run in 8-bit mode.  This requires that the
     'iowordsize' keyword be set to '8' in either the NET.CFG or PROTOCOL.INI 
     file, or on the command line for Packet driver.  
	  
	  Packet driver example:
	  cecfg driver=packet iowordsize=8
	  cepd iowordsize=8

	** Toshiba T3300SL only **
     
     The BIOS also must be set up to accommodate I/O cards.  To set up the
     PCMCIA slot, select the SETUP option in the program TEST3.EXE.  Change
     the option on the 'Card Modem' entry to 'Not Used'.  This prevents
     BIOS from enabling the PCMCIA slot for a proprietary Toshiba modem card.
     
     Toshiba 1950, 4500, and 4600 series 
     -----------------------------------
     The Toshiba laptop may have a version of Card and Socket Services that is
     not compatible with the newer specifications.  When using socket services
     1.0, card services release 2.0 version 1.0 from Toshiba do the following.
     Use the Keyword 'SOCKETSERVICES' and 'CARDSERVICES' set to 'NO' to allow
     the Xircom CreditCard to bypass card and socket services, see Xircom 
     manual 'Appendix C' for configurations of these keywords for the various 
     drivers.  Or remove card and socket services from the config.sys of the 
     laptop.

     CompuAdd 425tx
     -------------------------------------------------------------------------
     To support the CompuAdd notebook using a Databook "TCIC" PCMCIA 
     controller use the following configuration.

     - CEODI.COM "ODI" driver support:
	 Append the following lines to the end of the net.cfg file.
	 
	 link driver cecfg
	   TCIC 2C0     
     
     - CENDIS.EXE
	 Contact Xircom Technical Support for an update or specific 
	 instructions for using this driver on a CompuAdd 425tx.

     XIRCOM TECHNICAL SUPPORT
     ========================
     To obtain technical support for your Xircom product, please call or send
     a facsimile to the appropriate number listed below.  Access the Xircom  
     INFOSYS BBS at up to 14400 bps, No parity, 8 data bits, 1 stop bit 
     (N-8-1).
     
       Corporate Offices        Technical Support and Information
       -----------------------  ---------------------------------------------
       Xircom, Inc.             North and Latin America... TEL:  800-874-4428
       Corporate Headquarters   International ............ TEL:  818-878-6280
       26025 Mureau Road        24-Hour Facsimile......... FAX:  818-878-7175
       Calabasas, CA 91302      24-Hour Data Lines ....... BBS:  818-878-7618
	  TEL: (818) 878-7600   24-Hour Internet.......... INT: cs@xircom.com
	  FAX: (818) 878-6630   CompuServe                 CIS:  GO XIRCOM
	     HOURS:  6:00 a.m. to 4:30 p.m., Monday through Friday (Pacific)

       Xircom Europe NV         Europe, Mid-East, Africa.. TEL:  32 3 326 3494
       Bisschoppenhoflaan 82-84 24-Hour Facsimile......... FAX:  32 3 326 3150
       2100 Antwerp, Belgium    24-Hour Data Lines........ BBS:  32 3 326 2368
       TEL: 32 3 326 34 94
	  FAX: 32 3 326 31 50
	     HOURS:  8:30 a.m. to 5:30 p.m., Monday through Friday
		     8:30 a.m. to 4:30 p.m., Friday

       Xircom Asia LTD.         Asia Pacific.............. TEL:  852-525-2078
       1604 Centry Square       24-Hour Facsimile......... FAX:  852-525-8955
       1-13 D'Aguilar Street    24-Hour Data Lines........ BBS:  852-537-6048
       Hong Kong
	  TEL: 852-525-2078
	  FAX: 852-525-8955
	     HOURS: 9:00 A.M. TO 5:00 P.M., Monday through Friday

	 ---------------------------------------------------------------
		Thank you for making Xircom a part of your network.

     ------------------------------------------------------------------------

     Xircom acknowledges all tradenames and trademarks used in this document
     as the property of their respective owners.
     
     ===============================[  END  ]================================