Installation Guide
Reference Manual
for
Universal OS/2 Device Driver
for
DigiCHANNEL Intelligent 
Communications Boards

92000100C


DigiBoard, DigiCHANNEL, PC/Xi, PC/16i, PC/8i, PC/Xe, PC/16e, PC/8e, PC/4e,
PC/2e, Xem, PC/Xem, MC/Xem, EISA/Xem, COM/Xi, COM/8i, COM/4i, MC/Xi, MC/16i, 
MC/8i, MC/4i and C/X are trademarks of DigiBoard.  All other brand and product
names are the trademarks of their respective holders.


c Digi International, Inc.
All Rights Reserved

Information in this document is subject to change without notice and does not
represent a commitment on the part of DigiBoard.
DigiBoard provides this document "as is," without warranty of any kind, either 
expressed or implied, including, but not limited to, the particular purpose.
DigiBoard may make improvements and/or changes in this manual or in the product(
s) and/or the program(s) described in this manual at any time.
This product could include technical inaccuracies or typographical errors. 
Changes are periodically made to the information herein; these changes may be
incorporated in new editions of the publication.

RESTRICTED RIGHTS:

For non-U. S. Government use:
These programs are supplied under a license.  They may be used, disclosed,
and/or copied only as permitted under such license agreement.  Any copy must 
contain the above copyright notice and this restricted rights notice.  Use,
coping , and/or disclosure of the programs is strictly prohibited unless
otherwise provided in the license agreement. 

For U.S. Government use:
Use, duplication, or disclosure by the Government is subject to restrictions
as set forth in sub-paragraph (c)(1)(ii) of the Rights in Technical Data and
Computer Software clause of DFARS 52.227-7013.

Table of Contents
Table of Contents	3
Introduction	4
The Distribution Diskette	6
Installing the Device Driver	7
Global Parameters	7
Per-Card Parameters	10
Examples	13
Testing the Ports	15
Troubleshooting	16
Error Messages	18
DMODE I/O Port Configuration Utility	19
Examples	23
Appendix-Synchronous Communications Modes	25


Introduction
This release of the DigiWARE device driver for OS/2 supports the 
entire line of DigiCHANNEL intelligent asynchronous serial 
communications controllers:

Micro Channel (MCA) bus:	
DigiCHANNEL MC/Xi 4, 8 and 16 port boards
DigiCHANNEL MC C/X cluster controller system
DigiCHANNEL MC/Xem
PC/AT (ISA) bus:
DigiCHANNEL PC/Xe 2, 4, 8 and 16 port boards
DigiCHANNEL PC/Xi 8 and 16 port boards
DigiCHANNEL COM/Xi 4 and 8 port boards
DigiCHANNEL ISA C/X cluster controller system
DigiCHANNEL PC/Xem
EISA bus:
DigiCHANNEL EISA C/X cluster controller system
DigiCHANNEL EISA/Xem

The device driver software supports multiple boards and multiple 
board types in a single machine, and can handle up to 256 ports 
from any combination of the boards listed above.  As new products 
are introduced, the driver will be upgraded to include those devices 
as well.
The driver takes all its configuration information from the device= 
command line in CONFIG.SYS, and all DigiCHANNEL intelligent 
boards in a system are configured from a single command line.


In addition to the device driver, the configuration utility 
DMODE.EXE is provided to change communication parameters for 
individual ports without rebooting.  DMODE.EXE is similar to the 
OS/2 MODE command, but has some added features, and supports 
communications devices beyond OS/2's range of COM1 to 
COM8.

 
Before installing this device driver software, 
complete the installation of the DigiCHANNEL 
intelligent communications board(s) in your 
system, according to the hardware installation 
manual provided with the board(s), and write 
down your configuration!  The driver supports all 
legal I/O and memory address settings, but must 
be informed of these settings in the device driver 
command line.


The Distribution Diskette
The diskette accompanying this manual contains all of the files and 
documentation needed to install the DigiWARE OS/2 Universal 
Intelligent Device Driver in your system.  A list of these files 
follows:

XALL.SYS		The installable device driver.
DMODE.EXE		A MODE work-alike program for configuring I/O 
			ports beyond COM8.
INSTALL.DOC		Installation instructions for the current 
			release of the driver.
RELNOTES.DOC		Release notes.
DMODE.DOC		Instructions for the DMODE program.
XALL.DOC		Programmer's information about the driver 
			and applicable system calls.
*.bin			Miscellaneous binary files used by the driver.


Installing the Device Driver

Copy all of the files from the distribution diskette to a single 
directory on your hard drive.  By default, driver and data files are 
expected to be in \DIGI.  

The device driver is invoked by placing its name and configuration 
arguments into the system's CONFIG.SYS file.  All Digi-
CHANNEL intelligent asynchronous serial communications boards 
must be installed from a single command line, which contains 
complete set-up information for each board.  The format of the 
command line is:

device=\digi\xall.sys [/n:names] [/b:baud] [/d:dtype] 
[/f:digipath] [/v:messagepath] /t:card /p:port /m:mem [, 
/t:card /p:port /m:mem] [, ...]

Note that the path for XALL.SYS is \DIGI.  This is the default 
path.  If an alternative path is specified with the /f:digipath option, 
substitute that path for \DIGI.

 
The above command line must appear on a single 
command line in the CONFIG.SYS file.  This line 
may be up to 255 characters long.


Global Parameters

The first six parameters in the command line above are global 
parameters, and affect all boards installed.  These parameters are 
optional, and may be omitted.  If omitted, default values will be 
used.

/n:names

	Defines the naming convention to be use for the 
DigiCHANNEL ports.  names consists of an optional 
"stem" followed by the starting device number.  The 
new stem must be enclosed in double-quotes ("").  If 
the stem is omitted, "COM" will be used.  If the 
number is omitted, "3" will be assumed.  If the /n 
parameter is not specified, the default name COM3 will 
be assigned to the first port.

/n:"digi"0	DIGI0, DIGI1, DIGI2, ... DIGIn
/n:4			COM4, COM5, COM6, ... COMn
/n:"qdev"	QDEV3, QDEV4, QDEV5, ... QDEVn

/b:baud

	Sets the default baud rate to be used for all ports.  If this 
parameter is not specified, all ports will be set to the 
OS/2 default of 1200 baud.  Baud rates of up to 38,400 
are supported.  Use the DMODE.EXE command to set 
baud rates of individual ports.

/b:9600		Initializes all ports to 9600 baud.

/d:dtype

	Sets the initial data type (parity, character length and 
number of stop bits).  If this parameter is omitted, the 
OS/2 default data type of even parity, 7 data bits and 1 
stop bit is used.  The syntax is pds, where p is E, O or N; 
d is 8, 7, 6 or 5; and s is 1 or 2.  All three values must 
be supplied, in the correct order.

/d:N81		No parity, 8 data bits, 1 stop bit.

/f:digipath

Defines an alternative directory path for the driver and 
data files.  If this option is present, all files from the 
distribution diskette must be present in this directory.

/f:d:\drvr\digi	
				All data files are in "D:\DRVR\DIGI".



/v:messagefile

Forces the driver to direct all verbose messages to the 
file named.  If /v: is given without a filename, 
messages will be placed in \XALL.MSG.  This flag 
prevents any information from being displayed on the 
console; useful in some situations as when the machine 
is a "headless server", where calls to Standard Output 
will cause problems.  Without this flag, all messages will 
appear on the system console.

The message file is overwritten each time the system is 
started.

/v:errmsg 	Writes banner and other info to file 
"\ERRMSG".

/v:			Writes banner and other info to file 
"\XALL.MSG".

/a:a		Enable the alternate pin assignment of Data Carrier 
Detect (DCD) for all ports (see discussion of Alt-Pin 
processing on page 24).


Per-Card Parameters

The remaining three parameters are per-card parameters, and are 
used to inform the driver of the type of board and where it is to be 
addressed in the host's I/O and memory buses.  These parameters 
are mandatory, and must be given for each board!

The per-card parameters must be given in complete sets, and the 
sets must be separated by commas.

/t:card

	Defines the card type to the driver.  Legal values for 
card are:  i for the ISA C/X, e for the EISA C/X, m for 
the MC C/X, p for Xem systems (PC/Xem, MC/Xem 
or EISA/Xem) and x for COM/Xi boards.  This 
parameter must be omitted for PC/Xe, PC/Xi and 
MC/Xi boards.  The designators i, e, and m must be 
followed by an additional two digits defining the 
number and arrangement of DigiCHANNEL C/CON-
16 or C/CON-16e concentrators on each host adapter 
channel.  If the concentrator(s) are connected to the host 
adapter via a dial-up or leased line (remote 
concentrators), each of the two digits must be followed 
by a parameter, enclosed in parentheses, specifying the 
synchronous communications mode to be used for that 
line.  See the Appendix for a list of available 
synchronous communications modes.

/t:i10	ISA C/X, one local concentrator on line 1 
	only.
/t:e11	EISA C/X, one local concentrator on each of 
	lines 1 and 2.
/t:m21	MC C/X, two local concentrators on line 1 
	and 1 on line 2.
/t:e12	EISA C/X, one local concentrator on line 1, 
	and two on line 2.
/t:i22	ISA C/X, two local concentrators on each of 
	lines 1 and 2.
/t:i2(21)3(27)	

ISA C/X, two remote concentrators on line 
1, and two remote concentrators on line 2.  
The concentrators on line 1 will use mode 
#21 (76,800 baud, 8-wire, external clock) to 
communicate with the host adapter, and the 
concentrators on line 2 will use mode #27 
(614,400 baud, 8-wire, internal clock).  See 
the Appendix for a list of synchronous 
communications modes.

/t:x		COM/Xi (4 or 8 channels)
/t:p		PC/Xem, MC/Xem or EISA Xem

/p:port		Defines the I/O port address for the card.

/p:300		Board is addressed at I/O port 300h.
/p:2005		EISA board (EISA C/X or EISA/Xem 
		host adapter) is in slot 2 (EISA I/O 
		addresses are 4 digits-the slot number, 
		followed by "005").

When plugging an ISA board (PC/Xe, ISA C/X host 
adapter, etc.) into an EISA machine, the /p parameter 
must contain the 3-digit I/O address as set by the DIP 
switches on the board, and not the 4-digit address based 
on the EISA slot number.


/m:mem

	Dual-ported memory starting address.  This is the full 
32-bit hexadecimal address of the beginning of the 
board's dual-ported memory.

/m:d0000	Sets dual-ported memory start 
		address to 0D0000h (in the BIOS 
		expansion area between 640K and 1 
		megabyte).
/m:e80000	Sets start address of E80000h (in the 
		fifteenth megabyte).

EISA and ISA boards (except the COM/Xi), may all 
share the same memory starting address.  COM/Xi and 
all Micro Channel boards must each have unique 
memory addresses.


Examples

The following examples start out with just the minimum to install a 
DigiCHANNEL board.  After locating an example for your type of 
board, read the rest of the examples for optional situations that may be 
appropriate to your application.  Default options will be altered by your 
application program(s) when you configure the application.

Example 1:	COM/Xi

One COM/Xi at I/O port 300h, memory start address D8000h; 
devices to be named COM5 COM6, etc.  All data files are in the 
directory \DIGI:

device=c:\digi\xall.sys /n:5 /p:300 /m:d8000 /t:x 

(Note that the above must all appear on one line in CONFIG.SYS)


Example 2:	PC/Xe, PC/Xi
One PC/Xe (or PC/Xi) at I/O port 220h, memory address D0000h   
Ports will be named COM3, COM4, etc. (default names).  All data 
files are in the directory \MISC\DIGI:

device=c:\misc\digi\xall.sys /f:\misc\digi /p:220 /m:d0000 

(Note that the above must all appear on one line in CONFIG.SYS)



Example 3:	MC/Xi

One MC/Xi at I/O port F1F0h, memory address FC0000h.  Devices 
will be named DIGI1, DIGI2, etc. and will have an initial baud rate of 
38,400.  All data files are in the default directory \DIGI:

device=c:\digi\xall.sys /n:"digi"1 /b:38400 /p:F1F0 /m:FC0000 

(Note that the above must all appear on one line in CONFIG.SYS)


Example 4:	Two board installation with optional global 
		parameters.

Two PC/Xi (or PC/Xe) boards at I/O ports 320h and 300h, with dual-
ported memory of both starting at D0000h.  Ports will be named 
COM0, COM1, etc., and will be initialized to 38,400 baud, no parity, 
8 data bits and 1 stop bit; messages will be contained in the file 
MESSAGES.MSG located in the \DIGI directory.  All data files are in 
the default directory \DIGI:

device=c:\digi\xall.sys /n:0 /b:38400 /v:\digi\messages.msg 
/d:N81 /p:320 /m:D0000, /p:300 /m:D0000 


(Note that the above must all appear on one line in CONFIG.SYS)


Example 5:	PC/Xem

One PC/Xem at I/O port 224h, memory start address C8000h; devices 
to be named COM3 COM4, etc.  All data files are in the default 
directory \DIGI:

device=c:\digi\xall.sys /p:224 /m:C8000 /t:p
(Note that the above must all appear on one line in CONFIG.SYS)




Example 6:	ISA C/X 

One ISA C/X host adapter at I/O port 228h, memory address 
D0000h, with one concentrator on line 1 and two on line 2.  Devices to 
be named DCX1, DCX2, etc. and will have an initial baud rate of 
38,400.  All data files are in the default directory \DIGI:

device=c:\digi\xall.sys /n:"dcx"1 /b:38400 /p:228 /m:d0000 /t:i12 

(Note that the above must all appear on one line in CONFIG.SYS)


Example 7:	EISA C/X with a remote concentrator via an RS-
		232 synchronous modem.

One EISA C/X host adapter in slot 3, memory address D8000h, with 
two local concentrators on line 1 and one remote concentrator at 9600 
baud and external clocking on line 2.  Devices to be named COM5, 
COM6, etc. and will have an initial baud rate of 19,200.  All data files 
are in the directory \OS2\DIGI:

device=c:\os2\digi\xall.sys /n:5 /b:19200 /f:c:\os2\digi 
/p:3005 /m:d8000 /t:e21(17)
(Note that the above must all appear on one line in CONFIG.SYS)



Example 8:	MC C/X and MC/Xem
One MC C/X host adapter at I/O port 228h, memory address 
D8000h, with one concentrator on line 1 and one concentrator  on line 
2; one MC/Xem at I/O Port 304h, memory address D0000h.  Devices 
will be named DIGI1, DIGI2, etc. and will have an initial baud rate of 
38,400, Alt-Pin enabled, no parity, 8 data bits, and 1 stop bit.  All data 
files are in the default directory \DIGI:

device=c:\digi\xall.sys /n:"digi"1 /b:38400 /a:a /d:N81 /p:228 
/m:d8000 /t:m11, /p:304 /m:d0000 /t:p 

(Note that the above must all appear on one line in CONFIG.SYS)
(Note that for MC C/X and MC/Xem, the addresses 104 and 108 
should not be used to avoid possible conflicts)


Testing the Ports

The simplest (and probably the best) way to check the driver and 
I/O connections is to connect an ASCII terminal to one of the ports 
and redirect some output to that port.  If the terminal is connected to 
COM3, try something like the following:

dmode com3	(this will verify that the driver can find the 
		port-the port's parameters will be displayed.)

dmode com3 octs=off odsr=off
		(this insures that the hardware handshaking 
		signals CTS and DSR will not prevent output-
		we are not concerned with flow control at this 
		time.)

dir > com3	(this redirects the current directory to COM3.)

The console should simply respond by repeating the C:\> prompt, 
and the current directory (in this case, C:\) will appear on the 
terminal.


Troubleshooting

If the C:\> prompt doesn't reappear, and the system seems to be 
"hung", you probably used a memory start address that is being 
used by some other device, or the board is not set for the address 
specified in CONFIG.SYS.  Try a different address.  If it still hangs, 
try a different I/O port.  If your computer has a memory cache and 
the board's memory start address is above 1 megabyte, try either 
disabling the cache or moving the board to a low-memory address 
(D0000 is usually a good choice).

It is also possible that a conflict exists with another device driver 
which has been loaded via CONFIG.SYS.  The XALL.SYS line 
should be placed near the end of the CONFIG.SYS, and must not 
be placed before the DEVICE=TESTCFG.SYS line.
Due to potential device naming conflicts, the pair of lines

	DEVICE=\OS2\COM.SYS
		and
	DEVICE=\OS2\VCOM.SYS

may cause problems.  Be sure that the XALL.SYS line is placed 
before these lines in CONFIG.SYS.  If the XALL.SYS driver 
generates an error message, try temporarily putting "REM" in front 
of the above two lines.  If this works, there is probably a naming 
conflict.  You may need to add a /n: command line flag to the 
XALL.SYS line to force the driver to use a different base name or 
start numbering the COM devices at 5 or above.

If the C:\> prompt does reappear, but there is no output on the 
terminal screen, there is probably a cabling problem.  Make sure 
that all cable plugs are securely seated in receptacles, and that they 
are configured correctly (see the appropriate section of the 
hardware installation guide for your board).

If the terminal displays output, but the data on the screen is garbled, 
the terminal is probably not set with the same baud rate and data 
type as specified in CONFIG.SYS (or the defaults, if not specified).  
Verify these settings.

If everything checks out and you still have problems, there could 
be a problem with your board.  Contact your distributor or 
DigiBoard Technical Support for further assistance.


Error Messages

If, when the driver is loaded, it cannot find the board(s), or if they 
fail to respond properly to commands, certain error messages may 
be sent to the console.  These error messages are defined in the 
following table:

Could not find BIOS file
Could not find FEP file
Could not find data file

One or more files were missing from the digipath directory.  
The default digipath directory is /digi.  If you have loaded the 
driver and data files into a different directory, that directory 
must be specified in the xall command line with the 
/f:digipath parameter.

IO Port Not Responding

I/O port address set incorrectly, or conflicting with some other 
device. Verify setting, or try a different address.

DigiBoard BIOS Will Not Boot
DigiBoard BIOS Will Not Respond
DigiBoard FEPOS Will Not Boot

BIOS on DigiCHANNEL board will not respond to commands 
from the driver.  Typically due to a memory conflict, or a 
memory cache conflict.  

Driver Failed to Hook Timer
System Cannot Allocate Memory

A system call to OS/2 has failed.

Invalid Command Line Arguments

Syntax error in the command line in CONFIG.SYS.  Double-
check your entries.



DMODE I/O Port Configuration Utility

DMODE is DigiBoard's I/O channel configuration utility. DMODE 
functions like the OS/2 MODE command, but is more flexible, and 
provides some added features.

*	Supports communications device names other than COM1-
	COM8.
*	Any single parameter may be changed without causing all 
	others to be reset to default values.
*	Can be used to enable or disable the Alt-Pin feature on 
	individual ports.
*	Maintains the familiar MODE syntax.

DMODE arguments may be entered in any order, and in many cases 
may be abbreviated.  For example, a baud rate of 19,200 may be 
entered simply as "19", since within the context of the DMODE 
command, "19" cannot be interpreted as anything else. Arguments 
may be separated by spaces or commas, and unspecified 
parameters are left unchanged.  DMODE returns the settings of all 
parameters after any requested changes have been made. If no 
parameters are given, DMODE simply returns the current settings.

The syntax of DMODE is:

dmode port_name [parameters]


Port names and parameters are not case sensitive, so upper and 
lower case letters may be freely mixed without effect on the 
operation of the DMODE command.

The following parameters are accepted:

Baud Rate	Baud rates can be specified with 2 to 5 digit 
designations, according to the following table:

Accepted Values            Baud Rate

11   110                   110
15   150                   150
30   300                   300 
60   600                   600
12   120   1200            1200 
24   240   2400            2400
48   480   4800            4800
96   960   9600            9600
19   192   1920   19200    19200                    
38   384   3840   38400    38400
56   567   5670   56700    56700



Character Length

Characters may be 5, 6, 7 or 8 bits long.  Enter the 
appropriate number in the DMODE arguments.

Parity		Enter the desired parity checking method with a single 
		letter E, O, N, M or S for Even, Odd, None, Mark or 
		Space, respectively.

Stop Bits	Enter the desired number of stop bits.  Recognized 
		values are 1, 2 and 1.5.

Flags		DMODE supports the following flags in the same way as 
		the OS/2 MODE command.  Refer to your OS/2 
		documentation for explanations of the flags. To set a 
		flag, enter the mnemonic for the flag, followed by an 
		equals sign (=), and the desired value (ON, OFF, etc.).

Read Timeout Flag
TO=ON		Read timeout in effect.
TO=OFF	No timeout.

XON/XOFF Handshake Flag
XON=ON	XON/XOFF handshaking enabled.
XON=OFF	XON/XOFF handshaking disabled.

Input DSR Sensitivity
IDSR=ON	Enables Input DSR Sensitivity.
IDSR=OFF	Disables Input DSR Sensitivity.

Output DSR Sensitivity
ODSR=ON	Enables Output DSR Sensitivity.
ODSR=OFF	Disables Output DSR Sensitivity.


Output Handshake on CTS
OCTS=ON	Enables CTS output flow control.
OCTS=OFF	Disables CTS output flow control.

DTR Signal Control
DTR=ON	Sets DTR to "ON" or HIGH.
DTR=OFF	Sets DTR to "OFF" or LOW.
DTR=HS	DTR used for output flow control.

RTS Signal Control
RTS=ON	Sets RTS to "ON" or HIGH.
RTS=OFF	Sets RTS to "OFF" or LOW.
RTS=HS	RTS used for output flow control.
RTS=TOG	Toggles RTS from LOW to HIGH, or 
from HIGH to LOW.

Alt-Pin Processing
ALT=ON	Internally swaps DSR and DCD signals 
(see explanation below).
ALT=OFF	DSR and DCD are not swapped.

DigiCHANNEL products use 10-pin RJ-45 
connectors in order to support all of the signals 
normally available on a 9-wire RS-232 connection.  
However, many commercially available RJ-45 
connectors have only 8 pins.  8-pin RJ-45 plugs will 
fit in a 10-pin jack, but the first and last pins 
(numbers 1 and 10) are not connected.  DigiBoard 
uses these pins for the modem control signals RI 
(Ring Indicator, pin 1) and DCD (Data Carrier 
Detect, pin 10). While Ring Indicator is rarely a 
concern (since most modems have auto-answer 
capability), Data Carrier Detect is often monitored to 
insure that the modem has established, and is 
maintaining, a valid connection with a remote 
modem.  

To facilitate the use of 8-pin RJ-45 connectors in 
modem applications, a special DMODE flag, ALT, has 
been provided.  ALT instructs the device driver to 
monitor pin 1 of an 8-pin RJ-45 for DCD.

See the Hardware Installation guide for your board 
for cabling diagrams and pin assignment charts for 
DB-25 and RJ-45 connectors.

Examples

dmode digi12	
Returns the current settings of device digi12.  No changes are 
made.

dmode com5 2	
Configures COM5 for 2 stop bits.  All other parameters remain 
unaffected.

dmode com5:38 rts=on
Configures COM5 for a baud rate of 38,400 and sets RTS to "ON" 
or HIGH.

dmode com5 8	
Configures COM5 for 8 data bits.  No other parameters are 
affected.

dmode comdv83 idsr=off, to=off e 7 12
Sets COMDV83 to disable Input DSR Sensitivity, disable input 
timeout, select even parity, 7 data bits and a baud rate of 1200.

dmode com5 38 alt=on
Sets up COM5 for a baud rate of 38,400, and enables Alt-Pin 
Processing.

dmode com5 e alt=off
Sets COM5 for even parity checking and disables Alt-Pin 
processing.

dmode com3 odsr=off octs=off
Disables sensing of output flow control signals Clear To Send 
(CTS) and Data Set Ready (DSR).


Appendix-Synchronous Communications Modes

The DigiCHANNEL C/X host adapter communicates with attached 
C/CON-16 concentrators via two RS-422 synchronous channels 
(newer concentrators and host adapters also support RS-232 
synchronous communication-see your hardware Installation 
Guide).  The default operating mode for these channels is 1.2 
megabaud, 8-wire, internally clocked.  This provides the fastest 
possible communication between the host adapter and locally 
connected concentrators (in this context, local indicates that 
concentrators are connected directly, via a 4 or 8 wire cable, to the 
host adapter; remote refers to concentrators that are connected to 
the host adapter via data communications devices such as modems 
or DSUs).

Local concentrators always communicate with the host adapter in 
either an eight wire internally clocked mode or a four wire self-
clocked mode (in the four wire modes the clock is encoded with 
the data instead of being carried on separate lines as in the eight 
wire modes).

Remote concentrators always use an eight wire externally clocked 
mode (the clock signal is provided by the synchronous modem).

The table on the following page shows the modes that are 
supported by the XALL.SYS device driver.  Note that the external 
clock baud rates are approximates used to set up time-outs and 
tuning parameters only.  Values do not need to be exact; select the 
speed closest to the actual sped of your synchronous modem.



Eight-Wire               Eight-Wire              Four-Wire 
Internal Clock           Enternal Clock          Self-Clocking

Mode   Baud Rate         Mode   Baud Rate        Mode   Baud Rate
Mode

0      115k              15     2400             1      250k 
                         16     4800             2      460k                
3      2400              17     9600  
4      4800              18     19.2k
5      9600              19     38.4k
6      19.2k             20     57.6k
7      38.4k             21     76.8k
8      57.6k             22     115k
9      76.8k             23     230k
10     115k              24     460k
11     230k              25     920k
12     460k              26     1.2M
13     920k
14     1.2M              29     614k
                         30     737k             
27     614k
28     737k