6/1/93
	-- INSTALL.DOC--xall.sys V1.4.5

6400 Flying Cloud Drive Eden Prairie, MN 55344 (612) 943-9020

DigiBoard, GmbH Schmittgasse 64 5000 Cologne 90 Germany 49-2203-81083


Installation Guide Reference Manual for Universal OS/2 Device Driver for
DigiCHANNEL Intelligent Communications Boards

92000100C

DigiBoard, DigiCHANNEL, PC/Xi, PC/16i, PC/8i, PC/Xe, PC/16e, PC/8e,
PC/4e, PC/2e, Xem, PC/Xem, MC/Xem, EISA/Xem, COM/Xi, COM/8i, COM/4i,
MC/Xi, MC/16i, MC/8i, MC/4i and C/X are trademarks of DigiBoard.  All
other brand and product names are the trademarks of their respective
holders.


Digi International, Inc.  All Rights Reserved


Information in this document is subject to change without notice and
does not represent a commitment on the part of DigiBoard.  DigiBoard
provides this document as is, without warranty of any kind, either
expressed or implied, including, but not limited to, the particular
purpose.  DigiBoard may make improvements and/or changes in this manual
or in the product(s) and/or the program(s) described in this manual at
any time.  This product could include technical inaccuracies or
typographical errors.  Changes are periodically made to the information
herein; these changes may be incorporated in new editions of the
publication.

RESTRICTED RIGHTS:

For non-U.  S.  Government use: These programs are supplied under a
license.  They may be used, disclosed, and/or copied only as permitted
under such license agreement.  Any copy must contain the above copyright
notice and this restricted rights notice.  Use, copying, and/or
disclosure of the programs is strictly prohibited unless otherwise
provided in the license agreement.

For U.S.  Government use: Use, duplication, or disclosure by the
Government is subject to restrictions as set forth in sub-paragraph
(c)(1)(ii) of the Rights in Technical Data and Computer Software clause
of DFARS 52.227-7013.

Table of Contents				3 
Introduction					4 
The Distribution Diskette			6 
Installing the Device Driver			7 
Global Parameters				7 
Per-Card Parameters				10 
Examples					13 
Testing the Ports				15 
Troubleshooting					16 
Error Messages					18 
DMODE I/O Port Configuration Utility		19 
Examples					23 
Appendix Synchronous Communications Modes	25  

Introduction 

This release of the DigiWARE device driver for OS/2 supports the 
entire line of DigiCHANNEL intelligent asynchronous serial communications 
controllers:

Micro Channel (MCA) bus: 
	DigiCHANNEL MC/Xi 4, 8 and 16 port boards
	DigiCHANNEL MC C/X cluster controller system 
	DigiCHANNEL MC/Xem PC/AT

(ISA) bus: 
	DigiCHANNEL PC/Xe 2, 4, 8 and 16 port boards 
	DigiCHANNEL PC/Xi 8 and 16 port boards 
	DigiCHANNEL COM/Xi 4 and 8 port boards
	DigiCHANNEL ISA C/X cluster controller system 
	DigiCHANNEL PC/Xem 
	
EISA bus: 
	DigiCHANNEL EISA C/X cluster controller system 
	DigiCHANNEL EISA/Xem

The device driver software supports multiple boards and multiple board
types in a single machine, and can handle up to 256 ports from any
combination of the boards listed above.  As new products are introduced,
the driver will be upgraded to include those devices as well.  The
driver takes all its configuration information from the device= command
line in CONFIG.SYS, and all DigiCHANNEL intelligent boards in a system
are configured from a single command line.

In addition to the device driver, the configuration utility DMODE.EXE is
provided to change communication parameters for individual ports without
rebooting.  DMODE.EXE is similar to the OS/2 MODE command, but has some
added features, and supports communications devices beyond OS/2s range
of COM1 to COM8.


Before installing this device driver software, complete the installation
of the DigiCHANNEL intelligent communications board(s) in your system,
according to the hardware installation manual provided with the
board(s), and write down your configuration!  The driver supports all
legal I/O and memory address settings, but must be informed of these
settings in the device driver command line.

The Distribution Diskette The diskette accompanying this manual contains
all of the files and documentation needed to install the DigiWARE OS/2
Universal Intelligent Device Driver in your system.  A list of these
files follows: 

XALL.SYS	The installable device driver.
DMODE.EXE	A MODE work-alike program for configuring I/O ports beyond COM8
INSTALL.DOC	Installation instructions for the current release of the driver.
RELNOTES.DOC	Release notes.
DMODE.DOC	Instructions for the DMODE program.  
XALL.DOC 	Programmers information about the driver and applicable 
		system calls.
*.bin		Miscellaneous binary files used by the driver.



Installing the Device Driver Copy all of the files from the distribution
diskette to a single directory on your hard drive.  By default, driver
and data files are expected to be in \DIGI.  The device driver is
invoked by placing its name and configuration arguments into the
systems CONFIG.SYS file.  All DigiCHANNEL intelligent asynchronous
serial communications boards must be installed from a single command
line, which contains complete set-up information for each board.  The
format of the command line is: 

device=\digi\xall.sys [/n:names] [/b:baud] [/d:dtype] [/f:digipath] [/v:messagepath] /t:card /p:port /m:mem [, /t:card /p:port /m:mem] [, ...] 

Note that the path for XALL.SYS is \DIGI.  This is the default path.  If an 
alternative path is specified with the /f:digipath option, substitute that 
path for \DIGI.

The above command line must appear on a single command line in the
CONFIG.SYS file.  This line may be up to 255 characters long.

Global Parameters The first six parameters in the command line above are
global parameters, and affect all boards installed.  These parameters
are optional, and may be omitted.  If omitted, default values will be
used.  

	/n:names 	Defines the naming convention to be use for the
			DigiCHANNEL ports.  names consists of an optional 
			stem followed by the starting device number.  The new 
			stem must be enclosed in double-quotes ("").  If 
			the stem is omitted, COM will be used.  If the 
			number is omitted, 3 will be assumed.  If the /n 
			parameter is not specified, the default name COM3 will 
			be assigned to the first port.  
			
		/n:"digi"0 	DIGI0, DIGI1, DIGI2, ...  DIGIn 
		/n:4		COM4, COM5, COM6, ...  COMn 
		/n:"qdev"	QDEV3, QDEV4, QDEV5, ...  QDEVn

	/b:baud 	Sets the default baud rate to be used for all ports.  
			If this parameter is not specified, all ports will be 
			set to the OS/2 default of 1200 baud.  Baud rates of 
			up to 38,400 are supported.  Use the DMODE.EXE 
			command to set baud rates of individual ports.  
			
		/b:9600		Initializes all ports to 9600 baud.

	/d:dtype	Sets the initial data type (parity, character 
			length and number of stop bits).  If this parameter 
			is omitted, the OS/2 default data type of even 
			parity, 7 data bits and 1 stop bit is used.  The
			syntax is [pds], where p is E, O or N; d is 8, 7, 6 
			or 5; and s is 1 or 2.  All three values must be 
			supplied, in the correct order.  
			
		/d:N81		No parity, 8 data bits, 1 stop bit.

	/f:digipath	Defines an alternative directory path for the driver 
			and data files.  If this option is present, all files 
			from the distribution diskette must be present in this 
			directory.  
			
		/f:d:\drvr\digi		All data files are in D:\DRVR\DIGI.


	/v:messagefile	Forces the driver to direct all verbose messages 
			to the file named.  If /v: is given without a 
			filename, messages will be placed in \XALL.MSG.  
			This flag prevents any information from being 
			displayed on the console; useful in some situations 
			as when the machine is a headless server, where 
			calls to Standard Output will cause problems.  Without 
			this flag, all messages will appear on the 
			system console.  The message file is overwritten 
			each time the system is started.  
			
		/v:errmsg	Writes banner and other info to file \ERRMSG.  
		/v: 		Writes banner and other info to file \XALL.MSG.

	/a:a		Enable the alternate pin assignment of Data Carrier
			Detect (DCD) for all ports (see discussion of Alt-Pin 
			processing.

Per-Card Parameters The remaining three parameters are per-card
parameters, and are used to inform the driver of the type of board and
where it is to be addressed in the hosts I/O and memory buses.  These
parameters are mandatory, and must be given for each board!  The
per-card parameters must be given in complete sets, and the sets must be
separated by commas.

	/t:card		Defines the card type to the driver.  Legal values 
			for card are:	i for the ISA C/X, 
					e for the EISA C/X, 
					m for the MC C/X, 
					p for Xem (PC/Xem, MC/Xem or EISA/Xem) 
					x for COM/Xi boards.  
			This parameter must be omitted for PC/Xe, PC/Xi and 
			MC/Xi boards.  The designators i, e, and m must be 
			followed by an additional two digits defining the 
			number and arrangement of DigiCHANNEL C/CON-16 or 
			C/CON-16e concentrators on each host adapter channel.
			If the concentrator(s) are connected to the host 
			adapter via a dial-up or leased line (remote 
			concentrators), each of the two digits must be 
			followed by a parameter, enclosed in parentheses, 
			specifying the synchronous communications mode to 
			be used for that line.  See the Appendix for a 
			list of available synchronous communications modes.  
			
		/t:i10		ISA C/X, one local concentrator on line 1 only.
		/t:e11		EISA C/X, one local concentrator on each of 
				lines 1 and 2.  
		/t:m21		MC C/X, two local concentrators on line 1 and 
				1 on line 2.  
		/t:e12		EISA C/X, one local concentrator on line 1, 
				and two on line 2.  
		/t:i22		ISA C/X, two local concentrators on each of 
				lines 1 and 2.
		/t:i2(21)3(27)	ISA C/X, two remote concentrators on line 1, 
				and two remote concentrators on line 2.  
				The concentrators on line 1 will use mode 
				#21 (76,800 baud, 8-wire, external clock) to 
				communicate with the host adapter, and the 
				concentrators on line 2 will use mode #27 
				(614,400 baud, 8-wire, internal clock).  See 
				the Appendix for a list of synchronous 
				communications modes.  
				
		/t:x		COM/Xi (4 or 8 channels) 

		/t:p           PC/Xem, MC/Xem or EISA Xem

	/p:port		Defines the I/O port address for the card.  

		/p:300 		Board is addressed at I/O port 300h.  
		/p:2005		EISA board (EISA C/X or EISA/Xem host adapter) 
				is in slot 2 (EISA I/O addresses are 4 
				digits : the slot number, followed by 005).  
				When plugging an ISA board (PC/Xe, ISA 
				C/X host adapter, etc.) into an EISA 
				machine, the /p parameter must contain the 
				3-digit I/O address as set by the DIP switches 
				on the board, and not the 4-digit address 
				based on the EISA slot number.  

	/m:mem		Dual-ported memory starting address.  This is the full 
			32-bit hexadecimal address of the beginning of the 
			boards dual-ported memory.  
			
		/m:d0000	Sets dual-ported memory start address to 
				0D0000h (in the BIOS expansion area between 
				640K and 1 megabyte).  
		/m:e80000	Sets start address of E80000h (in the 
				fifteenth megabyte).  EISA and ISA boards 
				(except the COM/Xi), may all share the same 
				memory starting address.  COM/Xi and all 
				Micro Channel boards must each have 
				unique memory addresses.

Examples The following examples start out with just the minimum to
install a DigiCHANNEL board.  After locating an example for your type of
board, read the rest of the examples for optional situations that may be
appropriate to your application.  Default options will be altered by
your application program(s) when you configure the application.

--------

Example 1:      COM/Xi One COM/Xi at I/O port 300h, memory start address
D8000h; devices to be named COM5 COM6, etc.  All data files are in the
directory \DIGI: 

device=c:\digi\xall.sys /n:5 /p:300 /m:d8000 /t:x 

(Note that the above must all appear on one line in CONFIG.SYS)

--------

Example 2:      PC/Xe, PC/Xi One PC/Xe (or PC/Xi) at I/O port 220h,
memory address D0000h   Ports will be named COM3, COM4, etc.  
(default names).  All data files are in the directory \MISC\DIGI:

device=c:\misc\digi\xall.sys /f:\misc\digi /p:220 /m:d0000 

(Note that the above must all appear on one line in CONFIG.SYS)

--------

Example 3:      MC/Xi One MC/Xi at I/O port F1F0h, memory address
FC0000h.  Devices will be named DIGI1, DIGI2, etc.  and will have an
initial baud rate of 38,400.  All data files are in the default
directory \DIGI: 

device=c:\digi\xall.sys /n:"digi"1 /b:38400 /p:F1F0 /m:FC0000 

(Note that the above must all appear on one line in CONFIG.SYS)

--------

Example 4:      Two board installation with optional global parameters.
Two PC/Xi (or PC/Xe) boards at I/O ports 320h and 300h, with dual-ported
memory of both starting at D0000h.  Ports will be named COM0, COM1,
etc., and will be initialized to 38,400 baud, no parity, 8 data bits and
1 stop bit; messages will be contained in the file MESSAGES.MSG located
in the \DIGI directory.  All data files are in the default directory
\DIGI: 

device=c:\digi\xall.sys /n:0 /b:38400 /v:\digi\messages.msg /d:N81 /p:320 /m:D0000, /p:300 /m:D0000 

(Note that the above must all appear on one line in CONFIG.SYS)

---------

Example 5:      PC/Xem One PC/Xem at I/O port 224h, memory start address
C8000h; devices to be named COM3 COM4, etc.  All data files are in the
default directory \DIGI: 

device=c:\digi\xall.sys /p:224 /m:C8000 /t:p

(Note that the above must all appear on one line in CONFIG.SYS)

---------


Example 6:      ISA C/X One ISA C/X host adapter at I/O port 228h,
memory address D0000h, with one concentrator on line 1 and two on line
2.  Devices to be named DCX1, DCX2, etc.  and will have an initial baud
rate of 38,400.  All data files are in the default directory \DIGI:

device=c:\digi\xall.sys /n:"dcx"1 /b:38400 /p:228 /m:d0000 /t:i12 

(Note that the above must all appear on one line in CONFIG.SYS)

-----------

Example 7:      EISA C/X with a remote concentrator via an RS-232
synchronous modem.  One EISA C/X host adapter in slot 3, memory address
D8000h, with two local concentrators on line 1 and one remote
concentrator at 9600 baud and external clocking on line 2.  Devices to
be named COM5, COM6, etc.  and will have an initial baud rate of 19,200.
All data files are in the directory \OS2\DIGI:

device=c:\os2\digi\xall.sys /n:5 /b:19200 /f:c:\os2\digi /p:3005 /m:d8000 /t:e21(17) 

(Note that the above must all appear on one line in CONFIG.SYS)

----------

Example 8:      MC C/X and MC/Xem One MC C/X host adapter at I/O port
228h, memory address D8000h, with one concentrator on line 1 and one
concentrator  on line 2; one MC/Xem at I/O Port 304h, memory address
D0000h.  Devices will be named DIGI1, DIGI2, etc.  and will have an
initial baud rate of 38,400, Alt-Pin enabled, no parity, 8 data bits,
and 1 stop bit.  All data files are in the default directory \DIGI:

device=c:\digi\xall.sys /n:"digi"1 /b:38400 /a:a /d:N81 /p:228 /m:d8000 /t:m11, /p:304 /m:d0000 /t:p 

(Note that the above must all appear on one line in CONFIG.SYS) 
(Note that for MC C/X and MC/Xem, the addresses 104 and 108 should not be 
 used to avoid possible conflicts)

----------
----------

Testing the Ports The simplest (and probably the best) way to check the
driver and I/O connections is to connect an ASCII terminal to one of the
ports and redirect some output to that port.  If the terminal is
connected to COM3, try something like the following: 

dmode com3

(this will verify that the driver can find the portthe ports parameters will 
be displayed.) 

dmode com3 octs=off odsr=off 

(this insures that the hardware handshaking signals CTS and DSR will 
not prevent outputwe are not concerned with flow control at this time.) 

dir > com3          

(this redirects the current directory to COM3.) The console should simply 
respond by repeating the C:\> prompt, and the current directory 
(in this case, C:\) will appear on the terminal.



Troubleshooting If the C:\> prompt doesn't reappear, and the system
seems to be hung, you probably used a memory start address that is
being used by some other device, or the board is not set for the address
specified in CONFIG.SYS.  Try a different address.  If it still hangs,
try a different I/O port.  If your computer has a memory cache and the
boards memory start address is above 1 megabyte, try either disabling
the cache or moving the board to a low-memory address (D0000 is usually
a good choice).  It is also possible that a conflict exists with another
device driver which has been loaded via CONFIG.SYS.  The XALL.SYS line
should be placed near the end of the CONFIG.SYS, and must not be placed
before the DEVICE=TESTCFG.SYS line.  Due to potential device naming
conflicts, the pair of lines

DEVICE=\OS2\COM.SYS and 
DEVICE=\OS2\VCOM.SYS 

may cause problems.  Be sure that the XALL.SYS line is placed before 
these lines in CONFIG.SYS.  If the XALL.SYS driver generates an error 
message, try temporarily putting REM in front of the above two lines. 
If this works, there is probably a naming conflict.  You may need to 
add a /n: command line flag to the XALL.SYS line to force the driver to use 
a different base name or start numbering the COM devices at 5 or above.  
If the C:\> prompt does reappear, but there is no output on the terminal 
screen, there is probably a cabling problem.  Make sure that all cable plugs 
are securely seated in receptacles, and that they are configured correctly 
(see the appropriate section of the hardware installation guide for your 
board).  If the terminal displays output, but the data on the screen is 
garbled, the terminal is probably not set with the same baud rate and data 
type as specified in CONFIG.SYS (or the defaults, if not specified).  
Verify these settings.  If everything checks out and you still have 
problems, there could be a problem with your board.  Contact your distributor 
or DigiBoard Technical Support for further assistance.

Error Messages If, when the driver is loaded, it cannot find the
board(s), or if they fail to respond properly to commands, certain error
messages may be sent to the console.  These error messages are defined
in the following table:

Could not find BIOS file 
Could not find FEP file 
Could not find data file 	One or more files were missing from the 
				digipath directory.  The default digipath 
				directory is /digi.  If you have loaded the 
				driver and data files into a different 
				directory, that directory must be 
				specified in the xall command line with 
				the /f:digipath parameter.  
				
IO Port Not Responding 		I/O port address set incorrectly, or 
				conflicting with some other device.  Verify 
				setting, or try a different address.  

DigiBoard BIOS Will Not Boot	
DigiBoard BIOS Will Not Respond 
DigiBoard FEPOS Will Not 	DigiCHANNEL board will not respond to 
				commands from the driver.  Typically due to a
				memory conflict, or a memory cache conflict.  

Driver Failed to Hook Timer
System Cannot Allocate Memory	 A system call to OS/2 has failed.  

Invalid Command Line Arguments	Syntax error in the command line in 
				CONFIG.SYS.  Double-check your entries.


========

DMODE I/O Port Configuration Utility DMODE is DigiBoards I/O channel
configuration utility.  DMODE functions like the OS/2 MODE command, but
is more flexible, and provides some added features.

	-Supports communications device names other than COM1-COM8.  
	-Any single parameter may be changed without causing all others 
	 to be reset to default values.  
	-Can be used to enable or disable the Alt-Pin feature on 
	 individual ports.  
	-Maintains the familiar MODE syntax.

DMODE arguments may be entered in any order, and in many cases may be
abbreviated.  For example, a baud rate of 19,200 may be entered simply
as 19, since within the context of the DMODE command, 19 cannot be
interpreted as anything else.  Arguments may be separated by spaces or
commas, and unspecified parameters are left unchanged.  DMODE returns
the settings of all parameters after any requested changes have been
made.  If no parameters are given, DMODE simply returns the current
settings.  The syntax of DMODE is: dmode port_name [parameters]

Port names and parameters are not case sensitive, so upper and lower
case letters may be freely mixed without effect on the operation of the
DMODE command.  The following parameters are accepted:

Baud Rate       Baud rates can be specified with 2 to 5 digit designations, 
		according to the following table:

Accepted Values 	Baud Rate

11 110 			110
15 150 			150
30 300 			300
60 600 			600
12 120 1200 		1200
24 240 2400 		2400
48 480 4800 		4800
96 960 9600 		9600
19 192 1920 19200	19200
38 384 3840 38400 	38400
56 567 5670 56700 	56700


Character Length Characters may be 5, 6, 7 or 8 bits long.  Enter 
the appropriate number in the DMODE arguments.

Parity:  Enter the desired parity checking method with a single
letter E, O, N, M or S for Even, Odd, None, Mark or Space, respectively.

Stop Bits: Enter the desired number of stop bits.  Recognized
values are 1, 2 and 1.5.

Flags : DMODE supports the following flags in the same way as
the OS/2 MODE command.  Refer to your OS/2 documentation for
explanations of the flags.  To set a flag, enter the mnemonic for the
flag, followed by an equals sign (=), and the desired value (ON, OFF,
etc.).  

TO=ON		Write timeout in effect.  
TO=OFF		No timeout (infinite write timeout)

XON=ON		XON/XOFF handshaking enabled.  
XON=OFF		XON/XOFF handshaking disabled.

IDSR=ON		Enables Input DSR Sensitivity.  
IDSR=OFF	Disables Input DSR Sensitivity.  

ODSR=ON		Enables Output DSR Sensitivity.
ODSR=OFF	Disables Output DSR Sensitivity.

OCTS=ON		Enables CTS output flow control.
OCTS=OFF        Disables CTS output flow control.

DTR=ON		Sets DTR to ON or HIGH.  
DTR=OFF		Sets DTR to OFF or LOW.  
DTR=HS		DTR used for input flow control.  RTS Signal Control

RTS=ON		Sets RTS to ON or HIGH.
RTS=OFF		Sets RTS to OFF or LOW.  
RTS=HS		RTS used for input flow control.  
RTS=TOG		Toggles RTS on every transmit request. (Not supported)

ALT=ON		Internally swaps DSR and DCD signals (see explanation below).  
ALT=OFF		DSR and DCD are not swapped.

DigiCHANNEL products use 10-pin RJ-45 connectors in order to support all
of the signals normally available on a 9-wire RS-232 connection.
However, many commercially available RJ-45 connectors have only 8 pins.
8-pin RJ-45 plugs will fit in a 10-pin jack, but the first and last pins
(numbers 1 and 10) are not connected.  DigiBoard uses these pins for the
modem control signals RI (Ring Indicator, pin 1) and DCD (Data Carrier
Detect, pin 10).  While Ring Indicator is rarely a concern (since most
modems have auto-answer capability), Data Carrier Detect is often
monitored to insure that the modem has established, and is maintaining,
a valid connection with a remote modem.  To facilitate the use of 8-pin
RJ-45 connectors in modem applications, a special DMODE flag, ALT, has
been provided.  ALT instructs the device driver to monitor pin 1 of an
8-pin RJ-45 for DCD.  See the Hardware Installation guide for your board
for cabling diagrams and pin assignment charts for DB-25 and RJ-45
connectors.

Examples 

dmode digi12 

(Returns the current settings of device digi12.  No changes are made.)

dmode com5 2 

(Configures COM5 for 2 stop bits.  All other parameters remain unaffected.)

dmode com5:38 rts=on 

(Configures COM5 for a baud rate of 38,400 and sets RTS to ON or HIGH.)

dmode com5 8 

(Configures COM5 for 8 data bits.  No other parameters are affected. )

dmode comdv83 idsr=off, to=off e 7 12 

(Sets COMDV83 to disable Input DSR Sensitivity, disable output timeout, 
 select even parity, 7 data bits and a baud rate of 1200. )

dmode com5 38 alt=on 

(Sets up COM5 for a baud rate of 38,400, and enables Alt-Pin Processing.)

dmode com5 e alt=off 

(Sets COM5 for even parity checking and disables Alt-Pin processing.)

dmode com3 odsr=off octs=off 

(Disables sensing of output flow control signals Clear To Send (CTS) 
 and Data Set Ready (DSR). )


===========

Appendix

Synchronous Communications Modes 

The DigiCHANNEL C/X host adapter communicates with attached C/CON-16 
concentrators via two RS-422 synchronous channels (newer concentrators and 
host adapters also support RS-232 synchronous communicationsee your hardware 
Installation Guide).  The default operating mode for these channels is 
1.2 megabaud, 8-wire, internally clocked.  This provides the fastest 
possible communication between the host adapter and locally connected 
concentrators (in this context, local indicates that concentrators are 
connected directly, via a 4 or 8 wire cable, to the host adapter; 
remote refers to concentrators that are connected to the host adapter via 
data communications devices such as modems or DSUs).  Local concentrators 
always communicate with the host adapter in either an eight wire internally 
clocked mode or a four wire self-clocked mode (in the four wire modes the 
clock is encoded with the data instead of being carried on separate lines as 
in the eight wire modes).  Remote concentrators always use an eight wire 
externally clocked mode (the clock signal is provided by the synchronous modem).
The table on the following page shows the modes that are supported by
the XALL.SYS device driver.  Note that the external clock baud rates are
approximates used to set up time-outs and tuning parameters only.
Values do not need to be exact; select the speed closest to the actual
sped of your synchronous modem.