----====<   VBE/AI Driver Sample Source Code   >====----
	     ----====<	Copyright (c) 1993,1994 VESA, Inc.  >====----
	     ----====<		All Rights Reserved	    >====----
	     ----====<	      Version 0.98   12/16/93	    >====----


    INTRODUCTION:


	This document describes the VESA VBE/AI Software Developers
	Kit as found on the VBE/AI SDK release diskette. Included
	are sample WAVE drivers for the Pro Audio Spectrum, Disney
	Sound Source, and Sound Blaster cards.	Also included are
	sample MIDI drivers for the OPL2, OPL3 FM chip, and Roland
	MPU-401 MIDI transmitter/receiver.

	Each body of code is as complete as possible for the 0.98
	revision of the VBE/AI specification. The code may still
	change to match any changes when the specification is
	adopted, or to fix bugs.


    EXAMPLE DRIVERS:

	The VBE/AI example drivers were written as DOS TSRs. There
	is one API per TSR. Each one must be loaded separately into
	memory. The program, SETPREF.EXE lets the user assign a
	preference level to each driver.


    LOADING SAMPLE DRIVERS:

	Each driver uses a common set of command line parameters. The
	set looks like this:

            /H      helps
	    /?	    helps
	    /B:dd   board # if multiple boards are present
	    /A:xx   board address
	    /D:xx   dma channel
	    /I:dd   irq channel
	    /MB:xx  memory base (segment)
	    /MR:xx  memory range
	    /P:dd   user preference setting
	    /U	    unload this driver from memory

		dd=decimal #, xx=hex #


	To load a driver, just run the program. The program decides
	if the hardware is present, then will stay resident. The
	VBE/AI architecture does allow resident TSR drivers to be
	unloaded. Only the first driver loaded will be permenantly
	resident, all others may unload. The available drivers are:

	    PASWAVE.COM - Pro Audio Spectrum WAVE driver
	    SSWAVE.COM	- Disney Sound Source driver
	    SBWAVE.COM	- Sound Blaster & Compatible driver
	    OPL2.COM	- OPL2 MIDI driver
	    MPU.COM	- MPU-401 driver


    RUNNING SAMPLE APPLICATIONS:

	There are five sample programs currently available in the
	SDK. The source for each program is included on the
	diskette. Two programs test the WAVE drivers, two test the
	MIDI drivers, and the last is a utility for both setting
	user preference levels and displaying the current installed
	driver list.


    PMIDI.EXE

	This program will play any type 0 or type 1 MIDI file. The
	file must be under 64k in size. Currently, the program
	requires the driver's patch library to be resident in the
	current directory, specfically, OPL2.BNK. This version can
	only handle patch banks under 64K, but will soon support
	unlimited sizes. The following is a dump of the banner and
	command line parameter list:


	VESA VBE/AI MIDI Output Test Program, V0.98
	Copyright (c) 1993,1994  VESA, Inc. All Rights Reserved.

	To Use:  DOS>pmidi [song] [H] [L] [Mxxx] [K{+|-xx}] [R{+|-xx}] [V{xx}]

	Where: [song] is the .MID file to be played
	   [H]	      High end synth playing on channels 1-10.
	   [I]	      to receive MIDI input only.
	   [K{+|-}xx] shifts all key #s up|down by xx count (cheap transpose).
	   [L]	      Low end synth playing on channels 11-16.
	   [Mxxxx]    patch Map file name (256 bytes for 2 tables).
	   [Pxx]      selects a VBE device at this (xx) user preference level.
	   [R{+|-}xx] shifts all patch #s up|down by xx count.
	   [T+|-xx]   Tempo shift faster (+) or (-) slower, in percent.
	   [V{xx}]    verbose mode to dump events as they play. xx can be 1-5.


    NOTE.EXE

	This program allows the user to enter a channel and note
	number to be loaded into the target MIDI device. Once the
	patch has been loaded, a menu of functions will be provided
	to allow the user to turn the note ON or OFF.

	To Use:  DOS>note [Pxx]

	Where:	 [Pxx] is the user preference #.

	NOTE: all values are zero based, so the key number ranges
	      from 0 to 127. Channels range from 0 to 15. Channel
	      number 9 is the percussive channel.


    PLAY.EXE

	This program tests the WAVE output of a given driver. It
	allows the user to specify a starting block size,
	incremental length, number of times to play the block, and
	more. The program will send the block to the driver, and
	wait for the appropriate callback within a fixed amount of
	time. This time depends upon the sample rate and block size.
	The following is a dump of the banner and command line
	parameter list:


	VESA VBE/AI WAVE Output Test Program, V0.98
        Copyright (c) 1993,1994  VESA, Inc. All Rights Reserved.

	To Use:  DOS>play [16] [Axxx] [Fxxx] [Dxxx] [Ixxx] [Lxxx] [R] [S] [Txxx]

	Where: [16] enables 16 bit audio (8 bit is default).
	    [Axxx]  uses PlayCont/RecordCont. xxx is an optional block size.
	    [Fxxx]  user selects an alternate .WAV/.VOC file by the name of xxx.
	    [Dxxx]  allows for delays between blocks of xxx clock ticks (18.2tps).
	    [Ixxx]  after each block, Increment the next length by xxx.
	    [Lxxx]  block Length of first pcm block.
	    [R]     Reload the sample rate after each block finishes.
	    [S]     selects Stereo mode operation.
	    [Txxx]  number of Times to play the block.



    REC.EXE

	This program tests the WAVE input of a given driver. It
	allows the user to specify a starting block size,
	incremental length, number of times to play the block, and
	more. The program will send the block to the driver, and
	wait for the appropriate callback within a fixed amount of
	time. This time depends upon the sample rate and block size.
	The following is a dump of the banner and command line
	parameter list:


	VESA VBE/AI WAVE Input Test Program, V0.98
        Copyright (c) 1993,1994  VESA, Inc. All Rights Reserved.

	To Use:  DOS>rec  [16] [Axxx] [Fxxx] [Dxxx] [Ixxx] [Lxxx] [O{+}] [R] [S] [Txxx]

	Where: [16] enables 16 bit audio (8 bit is default).
	    [Axxx]  uses PlayCont/RecordCont. xxx is an optional block size.
	    [Fxxx]  user selects a new File by the name of xxx.
	    [Dxxx]  allows for delays between blocks of xxx clock ticks (18.2tps).
	    [Ixxx]  after each block, Increment the next length by xxx.
	    [Lxxx]  block Length of first pcm block.
	    [O{+}]  Save one recorded block. '+' saves all blocks.
	    [R]     Reload the sample rate after each block finishes.
	    [S]     selects Stereo mode operation.
	    [Txxx]  number of Times to play the block.


    SETPREF.EXE

	This program allows the user to set his/her preference level
	to each driver. This allows the application to choose which
	driver is the most desirable to use. Also, the program shows
	a listing of the driver configuration. The following is a
	dump of the banner and command line parameter list:


	VESA VBE/AI Preference setting Program, V0.98
        Copyright (c) 1993,1994  VESA, Inc. All Rights Reserved.

	To Use: DOS>SETPREF [H|?] [L] [+] [+xx] [-] [-xxx] [Vxxx]

	Where: [L]	  lists all devices.
	       [+]	  increments all preference levels by 1
	       [+xxx]	  increments a specific devices's preference.
	       [-]	  decrements all preference levels by 1
	       [-xxx]	  decrements a specific devices's preference.
	       [Vxx]	  give a verbose listing of this driver.

	NOTE: The highest preference level is zero (0), so incrementing the
	      preference actually lowers the user preference, and visa versa.


    COMPILING SAMPLE SOURCE CODE:

	All the example code was developed using Microsoft 'C' and
	MASM Assember.	Debugging of the TSR's was done using
	Nu-Mega's Soft-ICE and applications using Codeview. To build
	the code, use the included batch files and MAKE files.
	Again, the MAKE files depend upon the above directory
	structure to build the executables. The following list
	describes the files needed to build this driver release:

	1. The file 'MKSDK.BAT' executes several MAKE sequences
	   to build the VBE/AI SDK program set.

	2. The file 'MAKEFILE' is the general make file to
	   compile the five sample drivers.

        3. The file 'PLAY' is the make file to build the WAVE
	   playback (PLAY.EXE) and record (REC.EXE) test programs.

	4. The file 'PMIDI' is the make file to build the MIDI
	   player program.

	5. The file 'NOTE' is the make file to build the NOTE
	   player program.

	6. The file 'SETPREF' is the make file to build the user
	   preference adjustment program.

	7. The file 'VOLUME' is the make file to build the Volume
	   control test program.


    DRIVER DISKETTE CONTENTS:

	Disk Contents:

        SDK.DOC         Intro documentation to the SDK
        SDK.BAT         Batch file to build the release floppy
	MKSDK.BAT	Batch file to build the example programs

	PASWAVE.COM	Pro Audio Spectrum WAVE VBE/AI driver
	SSWAVE.COM	Disney Sound source WAVE VBE/AI driver
	SBWAVE.COM	Sound Blaster & Compatibles WAVE VBE/AI driver
	OPL2.COM	OPL2 VBE/AI MIDI driver
	MPU.COM 	MPU-401 VBE/AI MIDI driver

	ALFRE.MID	Sample MIDI file
	GUPPY.WAV	Sample WAVE file

	OPL2.BNK	Instrument bank for the OPL2 MIDI driver
	MT32		Patch map from GM to an MT32

	PLAY		Make file for the WAVE PLAY.EXE program
	PLAY.C		Source to PLAY.EXE
	PLAY.EXE	PLAY.EXE executable for playback testing of WAVE audio
	REC.EXE 	REC.EXE executable for record testing of WAVE audio

	NOTE		Make file for the single MIDI note test program
	NOTE.C		Source code for the single MIDI note test program
	NOTE.EXE	Executable MIDI note test program

        PMIDI.C         Source to PMIDI.EXE midi file player
	PMIDI		Make file for the MIDI PMIDI.EXE program
	PMIDI.EXE	PMIDI.EXE executable for MIDI playback
	PDATA.C 	Static data for PMIDI.C

	SETPREF 	Make file for setting user preferences & general query
	SETPREF.C	Source to SETPREF.EXE executable
	SETPREF.EXE	SETPREF.EXE executable to set user preference levels

	VOLUME		Make file for the volume test program
	VOLUME.C	Tests the Volume control of a given device
	VOLUME.EXE	Executable volume test program

        VESA.C          Mid level helper code for VBE/AI driver support

	MIDI.H		Miscellaneous header files
	VBEAI.H
	VESA.H
	MIDI.INC
	VBEAI.INC
	WAVE.INC

	MIDI\OPL2\TOOLS A directory with s/w for building the OPL2.BNK and
			MT32 patch map.