FixMBR v3.0                   October, 1993
        
           FixMBR is a combination recovery/integrity management program 
       for  the protection of hard disks. In the case of an Master  Boot 
       Record  infection  FixMBR  may  be used  to  restore  either  the 
       original  Master Boot Record or to rebuild it using  an  original 
       Partition Table taken from either inside the virus or from one of 
       the "hidden" sectors (where most MBR infectors hide them).
        
           According   to   the  latest  (1993)  figures   from   McAfee 
       Associates,  producers  of the popular SCAN, VSHIELD,  and  CLEAN 
       programs,  MBR infecting viruses were the cause of over  half  of 
       all  reported infections. FixMBR is designed to  provide  warning 
       and recovery from such infections.
        
           Additionally, FixMBR also provides for capture/storage of  an 
       off-line   copy  of  the  MBR  sector  that  may  be   used   for 
       reconstruction and capture.
        
           FixMBR  requires no complicated switches and will prompt  for 
       all  necessary information and permissions. Further  FixMBR  will 
       suggest   only legitimate partition tables found in the track   0 
       "hidden" area.
        
           User commands are limited to y(es)/n(o)/q(uit) and  will  be
       requested when appropriate. On  single disk systems  q(uit)  will
       terminate the program. On systems having multiple physical disks,
       q(uit)  will  skip to the next disk. This is useful when the only 
       activity desired is to back-up the original MBR(s).
        
                           WARNING Message
        
           The only real "caveat"s involve the error checking mechanisms 
       used  by FixMBR. When the program starts, the drive  table(s)  as 
       reported  by  the system is read and these  disk  parameters  are 
       output.  If  the  CMOS (AT class & 386  and  later  machines)  is 
       corrupt due to battery failure or rogue software, the  parameters 
       as reported will probably be different than exist. In this  case, 
       the  program should be q(uit)ed and the CMOS restored to  correct 
       parameters before continuing. 
        
           The other case is if the disk is not completely allocated  to 
       partitions  (rare).  This would occur if FDISK was  not  told  to 
       allocate  all  of  the  disk  to  active,  extended,  or  non-DOS 
       partitions  during the low-level format process. What will  occur 
       is that on partition table display a warning message will appear.
       Should  this  occur, either check the  original  partition  table 
       values to verify entries or look for another table to use  before 
       loading.  In  most  cases  a mismatch  will  indicate  a  corrupt 
       partition table.


                            Other Functions
        
           While  FixMBR  is designed to install the  SafeMBR  code  for 
       detection  of attacks by MBR and partition table viruses,  it  is 
       also designed to allow easy storage and recovery of original  MBR 
       code in the event that the SafeMBR code cannot be used.     
        
        
                            BIOS Boot Control
        
           Many modern ROM BIOSes  today  allow  selection  of the  boot 
       drive yet many people are hesitant to use this since  maintenance 
       sometimes requires booting from a floppy. v2.7 added the  ability
       to permit such floppy booting even though the BIOS is set to hard
       disk only. If the CTRL key is held down during boot, once SafeMBR
       completes its check, the boot process will be transferred to  the
       floppy A: drive. 
       
		               Suggested Use
        
           FixMBR   is   best utilized before  infection  or  corruption 
       strikes.   In  this case, run the program, save the original  MBR 
       when  prompted, select the partition table found  in sector  one, 
       and  allow use of the SafeMBR code. It is further suggested  that 
       the saved MBR(s) be copied as .COM file(s) along with the SafeMBR 
       program  to a known clean bootable (restoration) floppy  that  is 
       then write-protected and stored in a safe location. If a  printer 
       is connected, Print-Screen may be used to automatically create  a 
       hard  copy  of  the selected partition table(s)  that  should  be 
       stored with the recovery floppy.
        
        	           If an Infection Occurs
        
           In the event of an identified infection (e.g. STONED), simply 
       boot   from the restoration floppy, run FixMBR and  increment  to  
       the sector  in  which the virus stores the real MBR (e.g.  sector  
       7)  then  use  this  to either restore the original MBR  or   use  
       the SafeMBR code.
        
           In the case of an unknown infection, the best bet would be to 
       select   a   partition  table from a sector other than sector one 
       following a clean floppy boot.
        
           In  the event that a valid partition table is only  found  in 
       sector   one (e.g. Azusa) then the SafeMBR replacement code  must  
       be   selected  -  again only after a  known  clean  floppy  boot. 
       Alternatively,  the user can use the original MBR stored  offline 
       (see MBR8x.DAT below).
           
           If  used prior to infection, FIXMBR provides for  storage  of 
       the original MBR code offline in separate programs for each disk.
       (physical disks, not partitions). These  programs  will  be named
       MBR80.DAT for the first disk responding, MBR81.DAT for the second
       disk,   etc.   When   renamed with  a   .COM   extension,   these 
       become executable programs that will restore  the  original  MBR.  

           It  is very unlikely that a virus will attack the MBR of  any 
       fixed disk other than the first (disk 80) since this is the  only 
       one in which the MBR is executed, however just in case...  FixMBR 
       is designed to operate on ALL physical fixed disks responding  as 
       such and will provide for saving all MBRs found.
        
       WARNING: Since MBR code is generally unique to each PC, execution 
       of these programs  could  cause  serious data loss if executed on 
       a different machine. DO NOT MIX PROGRAMS. If used in a  multiple-
       PC environment, these files should be renamed to identify with  a
       specific machine. Further, if any extensive change  to  partition
       sizes are made or if a new OS is installed, rerunning  of  FixMBR
       will be necessary to insure a proper recovery file.
        
       IMPORTANT:  For  FixMBR  to  work properly, it is essential  that 
       any disk caching software (e.g. PC-Kwik) be turned OFF !
        
        
                         Recovery Using FixMBR
        
           Nearly  every  known  MBR infection (with  the  exception  of 
       AZUSA)  will store the original MBR sector in one of  the  hidden 
       sectors  (2-11 on MFM and many "translating" drives, 2-26 on  RLL 
       drives).  For  example, the STONED virus and  its  many  variants 
       store the original MBR in absolute sector 7. Furthermore, so that 
       a  PC  can be booted from a floppy, the partition table  MUST  be 
       found  in absolute sector 1 (see below for a description  of  the 
       MBR and Partition Table). Consequently, every known non-"stealth" 
       virus keeps a copy of the P-Table in its own body.
        
        
                    Recovery Using the Original MBR
        
           Since  it  is  often necessary to  boot  "bare"  an  infected 
       machine,  it is recommended that the first step after receipt  of 
       FixMBR be creation of a "recovery" disk.
        
           The  advisability of running FixMBR on a "clean"  system  and 
       saving  the  original MBR to a floppy  cannot  be  overemphasized 
       since  this  is a sure way to recover a system once  failure  has 
       occurred. For this reason more detail is provided.
        
        Step 1: Prepare a bootable  floppy  disk with the same operating
                system  currently  used. Copy the SYS  program  (may  be 
                either .COM or .EXE extension) to the disks.
        Step 2: Run FIXMBR and respond with a unique (7 max char) system
                name when asked.
        Step 3: With  the  bootable floppy in the A:  drive,  enter  the
                command: COPY *.DAT A:*.COM
        Step 4: Place   a   write protect tab on the  floppy,  label  it 
                SafeMBR recovery disk (if you have more than one PC each  
                should be separately labeled - serious loss could occur 
                if the  recovery program is executed on a different PC) 
                & store in a safe place.
        
           Following   infection,  easy  restoration  to  the   original 
       condition (without SafeMBR code) may be accomplished by executing
       the .COM file(s) for the machine after  booting from the recovery 
       disk.

        
                Recovery using FixMBR (original MBR code)
        
           If you have elected not to use the SafeMBR code and the  disk 
       becomes  infected, then recovery MAY be possible as follows:  Run 
       FixMBR but reject (n) the first sector and do not save a copy  of 
       the  MBR (unless you or someone else wishes to analyze it  -  the 
       saved  file has the extension .DAT and is harmless unless  either 
       renamed  or otherwise forced to execute. In this case be  careful 
       not to mix it with your recovery file.
        
           If  another  sector  on the first track is found  to  have  a 
       "possible  partition table" either compare it with  the  original 
       hard  copy  (see above) or analyze it using the  Partition  Table 
       description  below.  If  it matches your  disk  then  the  sector 
       probably  also contains the original MBR code. In any  event  you 
       can try it by selecting this sector (y) and rejecting use of  the 
       SafeMBR code (n). If necessary, repeat for other drives.
        
                 Recovery Using SafeMBR Code
        
           In  this  case it is generally "safe" to  use  the  Partition 
       Table found in the first sector - select it (y) and permit use of 
       the  SafeMBR code (y again). In some cases (e.g. AZUSA) this  may 
       be  the  only recovery method other than using the  original  MBR 
       code saved offline that will work.
        
                   The Master Boot Record
        
           When the IBM-PC architecture was expanded to allow the use of  
       hard  disks in 1982, provision was made for the accommodation  of 
       more  than one operating system on each hard  disk.  Accordingly, 
       the  first  FDISK  program permitted up  to  four  partitions  or 
       logical  disks  on  each physical disk.  While  rarely  used  for 
       multiple  operation systems (though systems such as OS/2,  XENIX, 
       CMP/86  have exploited this capability), the most common  use  of 
       partitioning was to allow early DOS versions to accommodate disks 
       larger  than  32  Mbytes - the largest disk  that  DOS  prior  to 
       Compaq/Zenith  3.31 could accommodate without third party help  - 
       by dividing the disk into multiple logical drives.
        
           At  boot time, the BIOS had to be able to recognize not  only 
       that  the disk was divided into partitions, but also needed  some 
       way  to determine which partition contained the operating  system 
       to be loaded.
        
           This  requirement  was satisfied by the Master  Boot  Record. 
       Always  occupying the first physical sector on a disk the MBR  is 
       divided  into two parts: the Partition Table and the Master  Boot 
       Record  Program - a special code segment that is able to  extract 
       the  partition table information and to load the first  stage  of 
       the operating system.
        
           Traditionally,  this is ALL the MBR code was designed to  do, 
       the  assumption  was made that it was operating in  a  valid  and 
       stable environment, consequently no error checking is done beyond 
       a simple "signature" validation.
        
           Since the MBR is very well defined both in both structure and 
       location, it is a target for some of the most successful computer 
       viruses today.
        
        
                    The Partition Table
       
            Note: hexadecimal (base 16) numbers will be indicated by the 
       suffix "h", other numbers are in decimal notation.
       
            The  partition table is a 40h (64) byte area in  the  Master 
       Boot  Record that describes the partitioning of a disk. Each  10h 
       (16) byte line describes a single partition: what it is, how  big 
       it is, and where it is found on the disk. Some of the information 
       is seemingly redundant, but all is used during the boot process.
       
            If  booting  is done from floppy disk, the MBR  sector  (the 
       first on the disk) need only contain the partition table, the MBR 
       code  segment is not necessary. However, if the fixed disk is  to 
       be bootable, then the MBR code segment must be present.
       
            The  partition  table is able to contain a maximum  of  four 
       entries  or logical partitions and versions of MS-DOS (&  PC-DOS) 
       prior  to 3.31 (sometimes called 3.3+) were only able to  address 
       FFFFh  (65535) 512 byte sectors for a maximum partition  size  of 
       33,553,920 bytes commonly referred to as 32 Mb though not exactly 
       this  value.  Since a maximum of four partitions  are  permitted, 
       this gave an effective maximum disk size of 128 Mb, an incredible 
       size  in 1982 when a 10 Mb ST-412 disk cost nearly  $1000.00  and 
       floppies had just gone from 160kb to 360 kb each.
       
            Note: the apparent "loss" of a sector was caused by the 
       fact that the original BIOS did not recognize any disk sector  as 
       "0", sector addressing starts with "1".
       
            Of  course, from the beginning, the partitions  permitted  a 
       doubleword  (four  bytes) for the sector numbers  rather  than  a 
       single word (two bytes) so the partition table was from the first 
       able to accommodate much gigabyte disks, a size which began to be 
       exploited with MS-DOS 3.31. However earlier versions were limited 
       to 32 Mb partitions.
       
            Prior  to  3.31,  a  number  of  manufacturers  had  already 
       provided  proprietary means for handling larger disk sizes.  EDSI 
       disks commonly used 1024 byte sectors permitting 64Mb partitions. 
       Other  manufacturers  used  extended partition  tables  by  daisy 
       chaining  the  tables (each logical partition had its  own  table 
       linking to the next). Still others such as OnTrack's  DiskManager 
       used custom device drivers to break the 32 Mb "barrier". However, 
       Compaq's  introduction of MS-DOS 3.31, a convention also used  by 
       Zenith  and DR-DOS finally allowed larger  partitions.  
       
            Microsoft  used a slightly different means with  MS-DOS  4.x 
       that  still required a custom driver to enable programs  to  used 
       "large"  partitions, a requirement that was  finally  eliminated 
       with  the introduction of DOS 5.0. The only important  factor  to 
       note  is  that all of these used the same basic  partition  table 
       (and   still   do)  with  only  the  addition  of  a   "Type   6"  
       partition indicating a "large" (over 32Mb) partition.
       
            In  any  event,  the partition table is  actually  a  simple 
       construct - once understood the only limitation to reconstruction 
       of  it  is knowledge of exactly how the disk is  partitioned  and 
       even 
       this information, though beyond the scope of this discussion, may 
       be recovered by someone knowlegable in disk structure.
       
            Each 10h (16d) byte entry in the partition table is made  up 
       of  six elements. The first byte (0h) determines which  partition 
       is "active" e.g. to be used for booting MS-DOS. This is indicated 
       by a hex "80" in the first byte. All other partitions should have 
       "00" in the first byte.
       
            The next three bytes (1-3h) contain information used by  the 
       MBR   to   locate   the  first  sector  of   the   partition   in 
       track/head/sector  format: the low order four bits (16  max.)  of 
       the first byte indicates the head number (the upper four bits are 
       not  used), the first six bits of the second byte are the  sector 
       number (63 max - 0 is not used). The upper two bits are  prefixed 
       to  the third byte to generate the track number (1024  max),  and 
       the upper nibble of the last byte is the head number (16 max). In 
       theory  this should provide for 1,032,192 sectors (at  512  bytes 
       per  sector this would allow 516 MB disks) but since  few  drives 
       have   16  heads  or  63  sector  tracks,   often   "translating" 
       controllers  or 1024 byte sectors are used to  permit  addressing 
       large disks. 
       
            The   fifth  byte (4h) describes the "type"  of   partition:  
       00h 
       indicates  "unknown"  and is often used by other  O/Ss.  Type  01 
       indicates a primary (active) partition with a 12-bit FAT. This is 
       rarely seen except on floppy disks since it can only  accommodate 
       4096   "allocation  units".  04  indicates  a  primary   (active) 
       partition  using  a  16-bit FAT and can be  used  for  partitions 
       containing  up  to 65,536 "allocation units", 05 is  an  extended 
       partition, and 06 a "large" partition. Other numbers are used  to 
       designate partitions used by other Operating systems such as OS/2 
       and Unix.
       
            Bytes  5-7h  contain  information used to  locate  the  last 
       sector in a partition the layout is the same as in bytes 1-3h.
       
            Bytes 8-Bh and C-Fh are double words indicating the starting 
       sector   offset   for  each partition and  the  absolute   sector  
       count. 
       These  are read backwards with the least significant byte  first. 
       Thus the first partition begins 00000011h (17) sectors after  the 
       MBR  and  extends for 0000C826h (51,238) sectors -  25  MB).  The 
       second  partition  begins at offset 0000C837h (C826h +  11h)  and 
       extends for 00007B2Fh (31,535) sectors (15 Mb). 


       Sample valid Partition Table: 42 MB disk with 2 partitions
       
            |A | Start  |T | End    | Absolute  | Absolute  |
            |C | Head/  |Y | Head/  | Partition | Partition |
            |T | Track/ |P | Track/ | Starting  | Sector    |
            |V | Sector |E | Sector | Sector    | Count     |
            |E |        |  |        | Offset    |           |
       
             80 01 01 00 04 04 91 5A 11 00 00 00 26 C8 00 00
             00 00 81 5B 05 04 D1 CD 37 C8 00 00 2F 7B 00 00
             00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 
             00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 
       
        Byte: 0  1  2  3  4  5  6  7  8  9  A  B  C  D  E  F
       
       For  a  more  complete description of the  Fixed  Disk  Partition 
       Table,  refer to the *IBM-PC Technical Reference  Manual*  (IBM), 
       also  the QUE book *DOS Programmer's Reference  Manual*  and Ralf  
       Brown's INTERRUPT list provide excellent references.
        
        
        		       SAFEMBR v3.0
               
           An   integrity  checking Master Boot Record program for  IBM-
       PCs and Clones by Padgett. Copyright (C) 1991,  1992,  1993:  all  
       rights reserved by the author.
      
           This  program  is designed to replace  the  standard   MS-DOS         
       master  boot  record program with code that does more  than  just 
       find  the  active  partition and jump to  the  O/S  boot  record, 
       SAFEMBR   first  checks  the  disk  access  integrity,  its   own 
       integrity, and validates the indicated partition.
       
            SAFEMBR  will  detect  all known Master  Boot  Record  virus 
       infections  including  those  using  "stealth"  such  as   JOSHI, 
       MICHELANGELO,  and   the EVIL EMPIRE as well as the  most  common 
       known infector, STONED and its variants.
       
            Used in conjunction with NoFBoot (C) or a BIOS allowing boot
       selection of the fixed disk, the likelihood of an undetected BIOS
       level infection going undetected drops to near zero.
       
            Using the techniques proven by its more rigorous  commercial 
       relative,  DISKSECURE II, SAFEMBR can provide  immediate  generic 
       front-line  detection of viruses both known and unknown  for  the 
       individual PC.
       
            Being  a MBR replacement only, SAFEMBR does not go  resident 
       and  thus  does  not require any  dedicated  RAM.  Following  the 
       IBM/MicroSoft specifications for a MBR, SAFEMBR is effective even 
       with  validating  BIOSes such as the TANDON  and  is designed  to 
       accommodate "unruly" disk controllers such as the Western Digital 
       WD10002A-27X which may write directly to the MBR.
               
            When installed, SAFEMBR will display its logo on each  boot. 
       Failure  to  print the logo could indicate a replacement  and  is 
       cause  for concern. The program CHKSMBR.EXE is provided to  allow 
       determination that SAFEMBR code is present.
       
            Should an exception occur, the boot will halt with an  error
       message such as "Low Interrupt Vector", "Invalid  First  Sector",
       "Invalid Master Boot Record", or "Missing Operating System".  The
       system can then be booted with  a floppy disk  and  investigation 
       made to determine the cause of the exception.
        
            It should be noted that many  security  products  using  MBR
       relocation techniques  are  incompatible  with SAFEMBR. If such a 
       product  uses  MBR  redirection  to prevent booting from a floppy 
       disk,  this  will  be  the case. If use  of  such  a  product  is 
       necessary,  SAFEMBR will have to be removed and the original  MBR 
       restored.
        
	                  CHKSBR30
        
           The  CHKSMBR program is supplied so that the user (or  Network 
       Server)  can verify that the SafeMBR code has been installed  and 
       is intact. Like FixMBR, CHKSMBR has no switches: on invocation  it 
       will display either an error message or the SafeMBR logo. It will 
       also  return  the following DOS Errorlevels for use  from  within 
       a .BAT batch file or other program.
        
           There  are  some common viruses which  simply  overwrite  the 
       original  MBR  code  (e.g. AZUSA). If the PC is  booted  from  an 
       infected floppy there is no way to prevent this from taking place 
       and there will be no warning that infection has occurred. CHKSMBR 
       is  designed to fill this gap by verifying that SafeMBR is  still 
       intact on the disk.
                     
           Note that since different signatures have been used with each
       SAFEMBR version, only the CHKSMBR for version  3.0  will  operate
       properly.

                     Errorlevel Returns
        
              0 - SafeMBR found in MBR (correct response)
              1 - Abnormal Termination (disk read error, etc.)
              2 - SafeMBR NOT found in MBR
        
          Thus any return OTHER than 0 indicates a problem. 
        
       Note:  CHKSMBR will operate properly ONLY if the SafeMBR  code  is 
       loaded onto the system.
        
                        Padgett Peterson
                        POB 1203
                        Windermere, FLA, 34786 USA
                        padgett@tccslr.dnet.mmc.com        
        
       DISCLAIMER: This software is furnished "as is" and all  liability 
            for  the effects of the use of this software rests  entirely 
            with the user. Adequate backups are the best protection from 
            loss.
        
            Extensive testing has been made but obviously this cannot
            include every conceivable combination.


                            FREEEWARE NOTICE        
        
            With version 3.0, FixMBR is made FREEWARE and  may  be  used
       without restriction or charge by individuals so long as no change 
       is made  to the program or its accompanying documentation and  it
       is only distributed as a complete package.
        
            Custom logos, warning notices, and boot delays (e.g. Display
       of  message  "Use  Subject  to  Monitoring   &  Unauthorized  use 
       Prohibited"  and  requirement  for  a  key  to  be pressed before 
       continuing) or  floppy  boot capability removal are available for
       a one-time fee.        
        
        
       v3.0 - 1993 - Checking made more rigorous
       v2.8 - 1993 - Correct improper sector count/boot for unusual P-table
       v2,7 - 1993 - Added floppy boot capability 
       v2.6 - 1993 - (unreleased) Added automatic save of old MBR with naming
       v2.5 - 1992 - (unreleased) Corrected lack of display on older monitors
       v2.4 - 1992 - Changed Suggested Remuneration
       v2.4 - 1992 - Added detection and notice for 1k byte sectors
       v2.3 - 1992 - not released
       v2.2 - 1992 - Added drive table information and check
       v2.1 - 1992 - Added early Zenith BR compatibility
       v2.0 - 1992 - MBR restoration programs made executable.
                     User interface improved. Program restructured.
       v1.7 - 1991 - Multiple drive handler added
       v1.6 - 1991 - Fixes "Invalid Partition Table" with unusual table 
       v1.5 - 1991 - First beta version released