TECHNOTE.DOC                                             February 1994
                Technical information on the RAR archiver

   Version 1.40 beta


***************************************************************************
    The author may change the format and structure data given below,
    although as soon as possible he will create a corrected and updated
    version.
***************************************************************************


   1. RAR archive format

   1.1. Archive header

HEAD_ID
4 bytes         Archive identifier:  0x52 0x45 0x7e 0x5e

HEAD_LEN
2 bytes         Full length of archive header, including archive
                comments and all supplementary fields

HEAD_FLAGS
1 byte          Status flags:

                0x01    - part of multi-volume archive
                0x02    - archive comment is present
                0x04    - archive locked against modification
                0x08    - archive is "solid"
                0x10    - packed comment in archive
                0x20    - EXT1 fields supported in archive

                the rest of the byte is reserved for internal use

COMM_LEN
2 bytes         Length of archive comment.
                present only if  (HEAD_FLAGS & 0x02) != 0

MAIN_COMMENT    Archive comment.
                present only if  (HEAD_FLAGS & 0x02) != 0

EXT1_LEN
2 bytes         Length of EXT1 field.
                present only if  (HEAD_FLAGS & 0x20) != 0

EXT1            Supplementary field.
                present only if  (HEAD_FLAGS & 0x20) != 0

????            Other supplementary fields - not used in this version


   1.2. File header within archive

PACK_LEN
4 bytes         Compressed file size

UNP_LEN
4 bytes         Original file size

CHECK_SUM
2 bytes         Checksum

HEAD_LEN
2 bytes         Total length of file header, including file comment,
                filename line and possible supplementary fields

FTIME
4 bytes         Date and time of file creation, in MS-DOS format

ATTR
1 byte          File attributes

FLAGS
1 byte          Status flags:

                0x01 - file continues from preceding volume
                0x02 - file continues in following volume
                0x04 - file is password-protected
                0x08 - file comment is present

VER
1 byte          Minimum RAR version needed to unpack:
                0 - RAR 0.99 (no longer supported)
                1 - RAR 1.00 (no longer supported)
                2 - RAR 1.30

NAME_LEN
1 byte          Length of filename

METHOD          Packing method: 0 - storing
                                1 - fastest
                                2 - fast
                                3 - normal
                                4 - good
                                5 - maximal


FILE_COMM_LEN
2 bytes         Length of file comment.
                present only if  (FLAGS & 0x08) != 0

FILE_COMMENT    File comment.
                present only if  (FLAGS & 0x08) != 0

FILE_NAME       Filename - line length as NAME_LEN

????            Supplementary fields - not used in this version

Comments:

1. When supplementary fields appear in headers, their length must be
   taken into account in HEAD_LEN.


2. In processing SFX archives it is necessary to skip the SFX module by
   searching for the archive's HEAD_ID. HEAD_ID is guaranteed not to
   appear within the SFX module.

   2. Remarks on compression methods

   RAR utilises one of several Lempel-Ziv methods with a search window
   of 64K (really 62): all lines of symbols, which have already been met
   in the file, are replaced in long lines and shifted until they match
   the previously appearing lines.

   Given the lengths of lines, the space between them, but also
   individual bytes, these are processed dynamically via the Huffman
   code index. In files with code symbol tables that do not remain
   intact - the Huffman table constantly removes excessive symbols, but
   symbols are assigned according to frequency of appearance in lines
   found during processing.

   Such a method gives significant advantages compared with static
   encoding in the situation of quickly changing non-homogeneous data
   (such as *.EXE and *.LIB files, and many others). If, however, you
   are archiving a large graphic file, which contains runs of 20 - 30
   identical bytes, archivers of the PKZip type will secure a higher
   degree of compression.

   On large files (in particular text files) RAR may also gain compared
   with the majority of archivers thanks to its larger search windows.