Voice              B.J. Guillot            Data/Fax
            713.893.9320      2611 Rushwood Circle      713.893.9124
                            Houston Texas 77067-1941

          Copyright (C) 1993-1994 B.J. Guillot.  All Rights Reserved.

         =============================================================
         BGFAX 1.21                                      FRI 25 MAR 94
                                                     EXPIRES 30 JUN 94
         =============================================================

                         Dedicated to Gene Roddenberry
                                  1921-1991

         -------------------------------------------------------------
         ABSTRACT                                  FidoNet 1:106/400.0
         -------------------------------------------------------------

         * Allows sysops to receives faxes on their BBS telephone line
           without needing a fax switch box and real fax machine

         * Everything runs in the foreground, no TSR programs needed

         * If you are already running a Fido mailer, you can configure
           your mailer to exit and run BGFAX when the line is hot, thus
           BGFAX does not necessarily have to answer the phone itself

         * Comes with a small and quick fax viewing program that supports
           CGA, EGA, and VGA display modes as well as FAX->PCX conversion

         * Works with modems that offer a feature known as adaptive
           answering on Class 1, Class 2, Class 2.0 and ZyXEL fax modems

         * Can send faxes

         -------------------------------------------------------------
         INCLUDED FILES
         -------------------------------------------------------------

         1.     BGFAX.DOC -- general documentation

         2.     WHATS.NEW -- release notes

         3.     BGFAX.EXE -- the main executable

         4.    HELPME.ARJ -- specialized help files for various setups

         5.      VIEW.EXE -- fax viewing and PCX conversion utility

         6.      NFAX.COM --\  optional TSR utility to notify the user
         7.    FAXOFF.COM --/  if a fax has been received

         8.   MAKEFAX.EXE --\ converts PCX and ASCII files to ZFAX format
         9.     BGFAX.FNT --/ font file for MAKEFAX

         10.   SOURCE.ARJ -- TP 7.0 source to VIEW.EXE and MAKEFAX.EXE

         11. REGISTER.FRM -- registration form

         -------------------------------------------------------------
         DISCLAIMER
         -------------------------------------------------------------

         BGFAX and accompanying files are provided AS IS without any
         warranty, expressed or implied.  This includes without limitation
         the fitfulness for a particular purpose or application and any
         warranties of merchantability.

         While I tried to be as through as possible in preparing BGFAX,
         B.J. Guillot shall not be liable for any damages, whether direct,
         indirect, special, incidental or consequential arising from a
         failure of this program or accompanying files to operate in a
         manner desired by the user.  B.J. Guillot shall not be liable for
         any damage to data or property which may by caused directly or
         indirectly by use of this program.

         In no event will B.J. Guillot be liable to you for any damages,
         including any lost profits, lost savings or other incidental or
         consequential damages arising out of your use or inability to use
         the program, or for any claim by any other party.  Individuals using
         the software bear all risk as to its quality and performance.
  
         -------------------------------------------------------------
         CONTACTING ME
         -------------------------------------------------------------

          FidoNet:  1:106/400                   Voice: +1 713.893.9320
         InterNet:  st1r8@jetson.uh.edu      Data/Fax: +1 713.893.9124

         The latest versions of BGFAX can be obtained by Fido FREQ at the
         above Fido node number with the magic name "BGFAX" and can be
         obtained by anonymous FTP for InterNet users at the site
         "CSN.ORG" in the "Computech" directory.

         BGFAX can also be obtained from Fido 2:512/39.  This system is
         called The Owl's Nest and is the Dutch Supra Distributor.  They
         have three nodes:

         +31 0.2155.10921      +31 0.2155.12571      +31 0.2155.28096
 
         An alternate distribution site is Fido 3:635/552.  Cloud Nine.

         +61-3-803-6954

         -------------------------------------------------------------
         MISCELLANEOUS NOTES
         -------------------------------------------------------------

         Currently, BGFAX does not come with a utility to print faxes.  If
         you wish to be able to print faxes, you will need to have a copy
         of ZyXEL's ZFAX software (version 2.23 perferred) or Smith Micro
         Software's QuickLink II, a commerical program included with many
         fax modems.

         Support for Fax Talk Plus-style fax images will be added in a
         later version.  WinFax support may or may not be offered.  It
         depends on whether or not Delrina will release the information to
         me I need.

         BGFAX supports Desqview's alternate video buffer zone, if used,
         and will return ticks to other tasks.  BGFAX also issues an
         Interrupt 28h call every now and then for OS/2 time slices.

         This program was compiled under Borland's Turbo Pascal 7.0.

         I routinely test BGFAX with a Supra Fax Modem (v.32bis external
         with V1.80-02 firmware), a USR 21.6K terbo (with 12/08/93
         firmware), a Hayes Optima 288 (V3.1 firmware), and a generic
         SIERRA based 2400 data/9600 fax modem from Computer City.

         If you wish to put BGFAX in DEBUG mode (where it logs most of the
         strings sent out and in from the modem in a DEBUG.LOG file), you
         must set the following environment variable:

              SET FAX=DEBUG

         -------------------------------------------------------------
         TALKING WITH THE COM PORT
         -------------------------------------------------------------

         BGFAX does not require a FOSSIL driver.  It will normally use its
         own internal communications routines to talk to your UART chip.
         BGFAX supports the 8250, 16450, and 16550A chips directly.

         BGFAX assumes...

             COM1=3F8x4     COM2=2F8x3     COM3=3E8x4     COM4=2E8x3

         NONSTANDARD PORTS
         =================

         If you are using a nonstandard port configuration, whenever BGFAX
         requires a port number to be entered (such as po=2), instead of
         entering the port number, enter the base address and IRQ seperated
         by an 'x' character (such as po=2E8x5).  BGFAX requires the base
         address be given in HEXIDECIMAL notation, and the IRQ to be given
         in DECIMAL notation, since all IO boards seem to use this method.
         If your COM3 was at 2F8h and IRQ 10, you would say (in the .CNF):

              po=2f8x10

         THE 19200 SHIFT
         ===============

         Many Class 2 fax modems require a DTE shift to 19200 bps when
         performing fax operations.  Yes, even if you have your port locked
         at 57600 bps, BGFAX will temporarily shift the speed to 19200.  It
         should be noted, however, that there are some exceptions to this
         rule.  Some modem manufactuers did not follow the 19200 shift
         method, and thus, you will have to tell BGFAX if you have one of
         these special modems.  The ZyXEL modem is a prime example.  Also,
         it has been brought to my attention that some Zoom modems also do
         not need to be shifted to 19200 bps.  (Which ones?  It seems very
         random.  You'll have to discover for yourself with trial and
         error.)  So, how do you tell BGFAX _not_ to shift to 19200?

         Putting an exclamation mark (bang) after the port will tell BGFAX
         not to shift the DTE speed to 19200 when receiving a fax.  (i.e.,
         whenever you want to specify COM2, do as as "2!" instead of "2").

         Class 1 and Class 2.0 fax modems do not require the 19200 DTE
         shift and BGFAX already knows this.

         IF YOU ARE NUTS AND WANT TO USE BGFAX WITH A FOSSIL DRIVER
         ==========================================================

         If for some reason, you NEED to use a FOSSIL driver (this is not
         recommended), you can put the letter 'F' in front of the COM port
         designator and BGFAX will use your FOSSIL driver.  BGFAX treats
         COM1 as F1, COM2 as F2, etc.  So, to use FOSSIL-COM2:

              po=F2

         If you are using a Class 2 fax modem that requires a 19200 shift
         when operating in fax mode, if you "lock" your FOSSIL driver,
         BGFAX will not be able to shift the port speed to 19200!  You will
         have to tell your FOSSIL driver to "unlock" the port, i.e.:

              BNU /L0=0
              BGFAX /FAX C:\BGFAX F1 Z
              BNU /L0=38400

         Note the "F1" means for BGFAX to use the FOSSIL on COM1.  The
         "/L0=0" parameter on BNU means for BNU to "unlock the port".
         Why?  Because, the FOSSIL driver will *ignore* a DTE shift request
         when its in "locked" mode.  BGFAX will be unable to relock your
         port with the FOSSIL driver, so that is the purpose of the
         second BNU line.  It re-locks COM1 at 38400 (or whatever) rate
         you want to use.

         Rememeber that BGFAX has its own communications routines, and
         doesn't need to use a FOSSIL driver, but it can if you absolutely
         have to use one.

         OPTIONS WHEN NOT USED IN THE BGFAX.CNF FILE
         ===========================================

         If you are running BGFAX in rear end mode (using one of the /Fxxxx
         parameters on the command line), BGFAX does NOT look for the
         BGFAX.CNF file.  Everything is passed to it on the command line,
         so if you needed to specify an alternate address and IRQ:

              bgfax /fax c:\bgfax 3f8x9 z

         ...or use a FOSSIL driver on COM4...

              bgfax /fax c:\bgfax F4 z

         -------------------------------------------------------------
         RECOMMENDED INITIALIZATION AND ANSWER STRINGS
         -------------------------------------------------------------

         This section tells you the recommended initialization and answer
         strings for your modem.  It will not tell you what the commands
         do.  Look in the "Quick tutorial" second to find that out.

         Class 2 modems (Supra v.32bis, PPI, Zoom, etc.)
            Init-1 ... ATZ|
            Init-2 ... AT+FCR=1;+FDCC=1,5,0,2,0,0,0,0|
            Init-3 ... AT+FLID="713 555 1212"|
            Answer ... AT+FAA=1;A|
            Dial ..... ATDT

         Class 2.0 modems (USR 21.6K)
            Init-1 ... ATZ|
            Init-2 ... AT+FCLASS=2.0|
            Init-3 ... AT+FLI="713 555 1212"|
            Answer ... AT+FCLASS=2.0|~AT+FAA=1+FNR=1,1,1;A|
            Dial ..... AT+FCLASS=0DT

         Class 1 modems (Hayes Optima 288, Supra 144LC)
            Init-1 ... ATHZ|
            Answer ... AT+FCLASS=1|~AT+FAE=1;A|
            Dial ..... AT+FCLASS=0DT

         ZyXEL modems (ZyXEL E, S, E+, S+, etc.)

            Init-1 ... ATZ|
            Init-2 ... AT#P713 893 9124
            Init-3 ... AT#B1+FCLASS=6|
            Answer ... ATA|
            Dial ..... ATDT|

         -------------------------------------------------------------
         QUICK TUTORIAL ON FAX COMMANDS AND ODDITIES
         -------------------------------------------------------------

         AT+FCLASS=?
         ===========
         This command asks the modem to tell you what fax classes it
         is compatible with.  It will respond with something like:

         0,1,2  or  0,2  or  0,1,2.0  or  0,2,6  or  0,1,2,6  or  ERROR

             0 = Data
             1 = Fax Class 1 capable
             2 = Draft Fax Class 2 "compatible"
           2.0 = Fax Class 2.0 capable
             6 = ZyXEL or Rockwell voice mode compatible
         ERROR = no fax capabilities

         GROUP and CLASS
         ===============

         Many people are often confused between the terminology "GROUP" and
         "CLASS" with regards fax modems.

         ALL FAX EQUIPMENT is "GROUP 3" compatible.  This includes fax
         machines, fax modems, standalone PC fax cards, etc.  Group 3 just
         defines the fax specifications, e.g., black-and-white, the
         resolutions, etc.

         "CLASS" refers only to fax modems.  CLASS has NOTHING AT ALL to do
         with fax machines.  Class 1, Class 2 and Class 2.0 are different
         methods of sending COMMANDS to a fax modem from a computer serial
         port.  Many fax modems offer the Class 2 command set.

         GROUP III
         =========

         Most Group III fax images are 1728 bits across.  A normal
         resolution page is approximately 1100 scan lines long, while
         a high resolution page is approximately 2200 scan lines long.

         When the fax devices are handshaking, this occurs at 300 bps,
         regardless of what the negoiated fax DCE rate is (i.e., 9600).

         Computer fax modems use v.17 modulation at 12000 and 14400,
         v.29 at 7200 and 9600, and v.27ter at 2400 and 4800 bps.

         Fax images can use one or two-dimensional modified huffman
         encoding.  One-dimensional is known as MH, and two-dimensional is
         known as MR (Modified Read).  MR encoding sends one scan line,
         followed by special bits that spell out differences between the
         above line and the current line.  Some higher tech machines also
         use MMR encoding (Modified, Modified Read).  MMR encoding sends
         the first scan line of the page, followed by x-number of
         difference lines, rather than just 1 difference line.  BGFAX
         currently supports only MH encoding.  The remote fax machines will
         always default to MH encoding since MR and MMR is not available.

         Fax images have things known as EOLs and RTC.  EOL stands for
         End-Of-Line and is represented as 000000000001.  Fax viewing
         programs read through the fax image file, scan line by scan line.
         They know where each scan line ends by searching for all the EOLs
         in the file.  RTC, Return-To-Control, is a series of six EOLs.
         The RTC sequence usually indicates an "end of page".  No huffman
         codes start with 11 zeros like the EOL character.  Why am I
         telling you all this?  Because many older fax machines send "fill"
         to your fax modem when receiving.  "Fill" is just extraneous zeros
         that are stored on your hard disk that take up space.  For
         example, you might have an scan line that ends with...

              0000000000000000000000000000000000000000000000000000000000001

         ...but, all that is actually needed is 000000000001.  As you can
         see, many extraneous zeros could be filtered from this line to
         reduce the size of fax image files a few bytes per scan line.

         Another interesting Group III fact is that a "training check" is
         performed by fax machines shortly after they connect.  The
         training check consists of the sender sending zeros for
         approximately 1.5 seconds (at the negoiated rate, i.e., 9600
         bps).  The receiving end will count all the zeros received, and
         any non-zeros received (bad bits that got corrupted by noise over
         the phone line), and if 10% of the bytes received were bad
         (non-zero), the receiving end will request a RETRAIN.  This
         usually involves a downshift of 2400 bps, i.e., 9600 -> 7200 bps.
         After the shift, another training check will be performed.

         AT+FAA=1
         ========
         This command will put a Class 2/Class 2.0 modem in ADAPTIVE
         ANSWERING mode.

         Your modem will properly mate with either a standard modem
         data call or a fax machine/fax modem.  Some modems, such as the
         Supra, will report a "FAX" response the instant a fax CNG tone is
         heard from the remote end.

         All modems, on true fax calls, will report a "+FCON" response code
         when the fax connection is truly established.  (This is similar to
         a "CONNECT 9600" or "CONNECT 14400" on a data call.)

         Many modems are slightly brain dead and will forget the +FAA
         setting when another command is issued to the modem.  To ensure
         you always answer in adaptive mode, rather than using "ATA" to
         answer the phone, use the following: "AT+FAA=1;A".

         The ";", semicolon, is used as a seperator for fax commands.  Some
         modems, such as the Supra, do not require it.  Others, such as the
         PPI, will "ERROR" out if the semicolons are not used.

         Please note that many modem manufactuers did not test adaptive
         answering as much as they should have before they released their
         modems.  Some modems won't allow low speed callers into your BBS
         when adaptive answering is enabled.  Others won't allow high
         speed callers into your BBS when adaptive answering is enabled.
         If this is happening, you will need to call your modem manufactuer
         and request new ROMs if any are available.  For example, the 14.4K
         PC Logic modem's adaptive answering doesn't work at all.  Even
         well known companies sometimes overlook adaptive answering.  A key
         example is that early version of the USR 21.6K modem would lock up
         whenever an HST call would come into their BBS when adaptive answer
         mode was enabled.

         The Supra Fax Modem, for example, is pretty good concerning
         adaptive answering.  (Note that very earlier versions of the
         Supra, did not offer adaptive answering until the 1.2-H and 1.2-J
         ROMs appeared on the scene.)  However, many older fax machines do
         not send out a CNG tone when they are engaged.  Many fax modems,
         including the Supra, won't know what to do, and will assume the
         old fax machine is really a data caller.  Again, this is not good,
         but its not that much of a problem.  Tell the operator of the old
         fax machine to push their "START" button *IMMEDIATELY* after dialing
         the last digit of the telephone number instead of waiting to hear
         the fax tones on our end like many office people do.

         AT+FAE=1
         ========
         This is the Class 1 command to enable adaptive answering.

         AT+FCR=1
         ========
         This is a Class 2/2.0 command to give your modem PERMISSION to
         take faxes.  Note that Class 2.0 modems default +FCR=1, so you
         won't need to use this command.

         AT+FLID="713 893 9124"
         ======================
         ( The Class 2.0 command is AT+FLI="713 893 9124" )

         The above command sets your modems fax ID string.  This is the
         string that is send to the remote end on fax connects.  (It's the
         deal that's printed on the little 'confirmation reports' that many
         fax machines make.)  The fax ID can ONLY BE A MAXIMUM OF *20*
         CHARACTERS.  If you try to stuff more than 20 characters in a fax
         ID string, the modem will respond with an "ERROR".  DO NOT USE
         HIGH-BIT ASCII CHARACTERS IN THIS STRING.  Use only simple
         letters, numbers, and punctuation marks.  (High-bit ASCII
         characters include foreign accented letters, inverted question
         marks, etc.)

         I've been told that some older fax machines will go nuts if you
         use a fax ID with ALPHABETIC letters and that the only true valid
         values, as specified by the CCITT (PLUS, SPACE, DASH, and the
         numbers ZERO through NINE).  I've never seen this happen
         personally, but am informing you of it nevertheless.

         Class 1 fax modems have their ID set by the fax software.

         AT+FDCC=1,5,0,2,0,0,0,0
         =======================

         The above command is what the power on defaults to a 14400 fax
         modem are, with one exception.  The first number, 1, allows your
         fax modem to accept high resolution fax documents.  The power on
         default to most modems are to accept only low resolution
         documents.  The second number, 5, allows your fax modem to use fax
         speeds up to 14400 bps.

         If you issue the above command on a fax modem with an upper limit
         of 9600 on fax tranmissions, you will receive an "ERROR" or cause
         the modem to behave odd.  Use this string on a 9600 fax modem:

         AT+FDCC=1,3,0,2,0,0,0,0

         The remaining numbers are not that important.  Changing them
         around, though, may cause BGFAX to fail.  The command can also be
         abbreviated to "AT+FDCC=1,5" or "AT+FDCC=1,3".

         You do not need to use this command on Class 1 and 2.0 modems.

         STACKING
         ========
         A single command string can be made using what we need ...

         AT+FAA=1;+FCR=1;+FLID="713 893 9124";+FDCC=1,5,0,2,0,0,0,0

         However, if you are using BGFAX in rear end mode with a Fido
         mailer, you may have a hard time of making an initialization
         string that long, so you may be required to split the line into a
         few pieces.  Remeber to make your ATA command "AT+FAA=1;A" if it
         is possible to change in your mailer.

         The +FDCC string must come at the end of the stack of commands!

         AT+FMFR?
         ========
         ( The Class 2.0 command is AT+FMI? )

         If you want to find out who makes the fax datapump for your modem,
         this command should tell you if you enter it in while in terminal
         mode.  My Supra (and many others) report "ROCKWELL".  My Cheap
         2400 data, 9600 S/R fax modem reports "SIERRA".  Others report
         "EXAR" and other things as well.

         AT+FNR=1,1,1
         ============

         This is a Class 2.0 command that tells the USR modem to let BGFAX
         know many details about the current fax reception, such as the
         resolution of the fax, what the fax DCE speed is currently
         negotiated at, etc.  Class 2 modems always report this.  However,
         for some strange reason, the Class 2.0 spec writers thought it's
         be "nice" to have the fax program NOT knowing this critical
         information.  I can think of no logically reason for this command
         existing, but if you forget to set it, your faxes on your Class
         2.0 modems may look elongated or smashed together.

         AT#B1+FCLASS=6
         ==============

         This is a ZyXEL fax command.  This is of use only to ZyXEL owners,
         and the ZyXEL user manual explains it very nicely.

         FAX MODE
         ========

         Probably 95% of you will be using BGFAX with a high speed modem
         (v.32 or v.32bis).  Many of you may have started off with slower
         300, 1200, or 2400 modems from long ago.  If you can remember back
         that far, when an incoming data call came in, you would see a
         string like "CONNECT 1200".  If your port was set at 2400, you
         would garbage on the screen unless you shifted your bps rate down
         to 1200 to match that of the caller.  Many newer terminal programs
         refer to this speed shift as "Autobaud".

         Modern modems require your serial port be locked at a specific
         speed (such as 19200, 38400, 57600, etc.) so that you can achieve
         higher thruput via compression engines such as MNP and v.42bis.
         The modem-to-modem speed may only be 14400, but the modem-to-
         computer speed stays "locked" at 38400.  Autobaud is not required,
         and if used, would result is garbage on the screen.

         Why am I telling you all this?  Well, I don't know who's silly
         idea it was, but the powers that be decided that fax modems should
         use the ancient method of changing the port rate when a fax is
         incoming or outgoing.

         After your modem reports the result code "+FCON" all further
         communications *MUST* be done at 19200 bps, even if you are locked
         at 38400 or 57600.  If the port speed is not relocked at 19200,
         nothing but garbage will come on the screen.

         I'm telling you this because I frequently get mail asking me why
         I'm changing the port speed to 19200.  It's not my fault!  That's
         the way is has to be done!  The only modem that I know that does
         not require this idiotic speed shift is the ZyXEL modem.  In fact,
         a special option must be used to tell BGFAX you are using a ZyXEL
         or BGFAX will fail as it will try talking to the ZyXEL modem at
         19200 instead of 57600 or whatever rate it's locked at.

         Note that the 19200 shift is not needed on Class 1 and 2.0 modems.

         BIT ORDER
         =========

         Class 2 fax modems receive in reverse bit order and transmit in
         direct bit order.  Actually, this is not in the Class 2 spec, but
         a bug in Rockwell's Class 2 implementation.  This reverse bit
         order bug became so wide spread, that other fax modem manufactuers
         now have to receive in reverse bit order to make their modems
         compatible with existing fax software.  :-)

         BGFAX will save all incoming fax files in direct bit order, so it
         effectively flips all the bytes on the fly when receiving.

         Class 1, Class 2.0, and ZyXEL modems receive and transmit in
         direct bit order.

         -------------------------------------------------------------
         FRONTEND/HOST MODE
         -------------------------------------------------------------

         If you want BGFAX to answer the phone, BGFAX is started up using
         the /HOST command line parameter.

         If you plan on using BGFAX in Frontend mode, you need to do a
         couple of things first.

         1. An evironment variable called BGFAX needs to be inserted in
            your AUTOEXEC.BAT or someother batch file.  Example:

            SET BGFAX=C:\BGFAX

            This environment variable points to the location of your BGFAX
            configuration file and the directory where faxes will be
            received into.

            (Note, some people don't like cluttering their environment with
            variables.  You can start up /HOST mode using a different config
            file other than BGFAX.CNF, by using the "$" modifier, e.g.:

              BGFAX /HOST /50 $C:\BAT\ROBIN.CNF
              BGFAX /SEND C:\BGFAX\FAX0001.FAX 893-9124 $C:\BAT\BATGIRL.CNF

            The "$" modifer must be the last thing on the command line.
            Instead of looking for a BGFAX.CNF file as specified by the
            BGFAX environment variable, this will cause BGFAX to look for
            a "ROBIN.CNF" (in host mode) or "BATGIRL.CNF" if sending.
            The "$" modifer has NO EFFECT on rear end mode operation.)

         2. Make sure the BGFAX.CNF configuration file is in the directory
            pointed to by the BGFAX environment variable and make any
            changes you think necessary.  The included configuration file
            is self explantory.  I won't repeat the format here.

         3. BGFAX can exit with 7 possible internal errorlevels:

               6 - host mode idle for more than x minutes
               4 - fax was received
               3 - local logon
               2 - data call
               1 - restart batch file

            If no errorlevel is encountered, it means the sysop aborted
            BGFAX by pressing the [Esc] key or a serious error occurred.

         4. When BGFAX is waiting for a call, pressing Ctrl-R will reset
            the on screen counters.  Ctrl-A will force BGFAX to send the
            answer string to the modem.

         5. If you some reason, you want to use the USR Class 2.0 modem in
            Class 1 mode with BGFAX's /HOST mode, you will need to use the
            /ATO switch which will cause BGFAX to send an "ATO" to the
            modem after the "DATA" response is received.

         6. When a data call comes in, BGFAX creates a DOBBS.BAT file that
            looks like so:

            C:\BGFAX\EXEBBS.BAT 9600 1 528 /ARQ
            
            The first parameter is the DCE data speed, then the com port,
            number of minutes until the next event, and then the error
            correcting string, if any.  The EXEBBS.BAT file must be created
            by you so that your bulletin board software is loaded up in
            frontend mode (ie., the data connection is already hot.)

                 %1 -> the DCE speed, modem-to-modem real connect speed
                 %2 -> the COM port
                 %3 -> number of minutes until the next event
                 %4 -> error correction/reliable mode indicators

         DOBBS.BAT theory
         ================

         If you have never used a frontend program uses DOBBS.BAT theory,
         there are several things you need to know.  You have to be pretty
         confident in DOS and batch files, or you will get lost very
         easily.  First, you need a main batch file that runs BGFAX.  Let's
         call this FBBS.BAT:

              @echo off
              c:
              cd\bgfax
              bgfax /host
              if errorlevel 4 goto faxrcvd
              if errorlevel 3 goto datacall
              if errorlevel 2 goto datacall
              if errorlevel 1 fbbs.bat
              goto end
              :faxrcvd
                rem [you can put a printing batch here if you want]
                %bgfax%\doprint.bat
                del %bgfax%\doprint.bat
              :datacall
                rem [errorlevel 3 is local login, 2 is data caller]
                %bgfax%\dobbs.bat
              :end

         Note that DOS requires all if-errorlevel statements to go in
         DESCENDING ORDER!  (255,254,253,...,4,3,2,1).  This is a fact that
         many people forget.

         This FBBS.BAT file will run BGFAX and when a data caller calls
         your system, BGFAX will exit with an errorlevel of 3.  This will
         cause the batch file to jump to the ":datacall" label.  Here, the
         line "%bgfax%\dobbs.bat" is executed, causing DOS to shift control
         of the computer to the DOBBS.BAT file.  Rememeber, this is a file
         that BGFAX creates!  You do not need to make a DOBBS.BAT file.
         The DOBBS.BAT then executes _another_ batch file called EXEBBS.BAT
         which will look something like:

              @echo off
              bbsprog /f:%1:%2
              fbbs

         The EXEBBS.BAT file will look different for EVERY different type
         of BBS software!  PC Board, Wildcat, GT, etc. all use different
         formats.  You will have to look up the info for the EXEBBS.BAT
         file in your BBS user's manual.  I can't help you with that.
         Notice that the last line "fbbs" restarts the original FBBS.BAT
         file that runs BGFAX in /HOST mode.

         In review: (1) Modify FBBS.BAT to meet your needs, (2) BGFAX will
         MAKE a DOBBS.BAT file by itself, (3) YOU will need to MAKE an
         EXEBBS.BAT file, (4) the EXEBBS.BAT file must restart FBBS.BAT.

         Do not use the CALL statement anywhere unless you really know what
         you are doing.  "FBBS.BAT" and "CALL FBBS.BAT" causes two
         completely different things to happen.  Only experienced DOS/batch
         file writers need to experiment with that.

         -------------------------------------------------------------
         INITIALIZATION MODE
         -------------------------------------------------------------

         If you want BGFAX just to initialize the modem, you can have it do
         so with the BGFAX /INIT parameter.  BGFAX will get the port,
         speed, and initialization strings from the BGFAX.CNF file in the
         directory specified by the BGFAX environment variable.

         This mode is provided for people who need to use BGFAX in rear end
         mode, but their Fido mailers (or BBS software) do not allow them
         to use the long initialization strings required for fax usage.

         -------------------------------------------------------------
         REAR END MODE (FIDO MAILERS, ETC.)
         -------------------------------------------------------------

         Rear end mode is useful for those of us who are FidoNet members
         where a Fido mailer is required to be running 24 hours a day.  It
         will be your job to figure out how to get your mailer to exit to
         BGFAX when your modem informs the mailer a fax call is coming
         through.  (See the HELPME.ARJ file for hints on specific mailers.)

         You will need to know the result code your modem sends when an
         incoming fax call is detected.  Some modems send TWO fax connect
         strings.  For example, the Supra will send "FAX" followed by an
         "+FCON" response about 2 seconds later.  The ZyXEL will send
         "CONNECT FAX" followed immediately by "ZyXEL".  Most fax modems
         report only one string though.  Use this chart for reference:

         Result   Modems
         ======   ====================================================
         FAX      Supra, Zoom, Hayes, most Rockwell based chipsets
         +FCON    PPI, other Class 2 modems
         +FCO     USR 21.6K and other Class 2.0 modems

         You need to configure your mailer (or BBS software) to exit
         IMMEDIATELY upon receipt of the proper fax result code.  You
         need to call BGFAX in the following manner:

         BGFAX /how [faxpath port faxtype [pid]]

         FAXPATH will be the directory where incoming faxes are to be
         placed.  PORT is a valid communications port from 1 to 4, or,
         optionally, a hexidecial base address and IRQ formatted as
         followed "3F8x5".  Also, optionally, if the port has a bang, !,
         following it, it will force the port to stay locked at the current
         speed rather than shifting to 19200 on fax connects.  FAXTYPE is a
         single character 'Z' or 'Q'.  'Z' for ZyXEL ZFAX format, 'Q' for
         Smith Micro Software's Quick Link II fax format.

         The "/how" deal is the most critical switch.  There are three
         possible settings.

              /FAX   ... Modem reports "FAX" or "CONNECT FAX".
                         BGFAX will automatically detect whether it should
                         use Class 2 (Supra, Zoom) or the ZyXEL fax mode
                         based on the next message (ie, "+FCON" or "ZyXEL").

              /FAX:713_893_9124     If your modem in Class 1, try one of
              /FHAY:713_893_9124    these two options.

              /FAST  ... Modem reports "+FCON" (PPI, other Class 2 modems)
              /FCON  ... Try this option if /FAST doens't work.

              /FCO   ... Modem reports "+FCO" (USR 21.6K)
              /FCOS  ... Try this option if /FCO doesn't work.

              /FZYX  ... ZyXEL owners use this if /FAX doesn't work.

         Here is a schematic of how each option behaves:

              /FAX [ Supra, ZyXEL, i.e. all modems that report "FAX" ]
                1. keeps port at locked DTE
                2. waits for "+FCON"     _or_  2. waits for "ZyXEL"
                3. drops port to 19200         3. waits for high CTS
                4. waits for "OK"              4. sends <DC2>
                5. sends "AT+FDR"

              /FAX:713_893_9124 [ Supra LC modem, Class 1 modem ]
                1. keeps port at locked DTE
                2. waits for "CONNECT"
                3. begins sending Class 1 HDLC frames

              /FHAY:713_893_9124 [ Hayes 288, other Class 1 modems ]
                1. keeps port at locked DTE
                2. blindly starts sending Class 1 HDLC frames

              /FAST [ PPI, i.e. all modems that report "+FCON" ]
                1. drops port to 19200
                2. waits for "OK"
                3. sends "AT+FDR"

              /FCON [ PPI, use this if above options don't work ]
                1. drops port to 19200
                2. blindly sends "AT+FDR"

              /FCO  [ USR, i.e. all Class 2.0 modems that report "+FCO" ]
                1. keeps port at locked DTE
                2. waits for "OK"
                3. drops port to 19200 _only if_ DTE rate is 38400
                   (leaves port alone if set at 19200, 57600 or 115200)
                4. sends "AT+FDR"

              /FCOS [ USR, i.e. all Class 2.0 modems that report "+FCO" ]
                1. drops port to 19200 _only if_ DTE rate is 38400
                   (leaves port alone if set at 19200, 57600 or 115200)
                2. blindly sends "AT+FDR"

              /FZYX  [ ZyXEL, use this only if /FAX doesn't work ]
                1. waits for high CTS
                2. sends <DC2>

         When a fax is inbound, I call BGFAX in rearend mode with the
         following command line for my Supra:

              BGFAX /FAX C:\BGFAX 1 Z
              bgfax /fax c:\bgfax f3 z
              bgfax /fax c:\bgfax 3f8x7 z

         Using my Hayes 288, example command line options might be:

              bgfax /fhay:713_893_9124 c:\bgfax 1 z

         ...note that the ID string MUST be presented on the command line
         when you are receiving with a Class 1 modem in rear end mode.
         In Class 1, the fax software is responsible for sending the ID
         string to the remote machine.  (In contrast to Class 2/2.0 modems,
         which automatically send the ID to the remote machine.)

         The /FAX means that I used the modem response "FAX" as a trigger
         for FD (see BGFAX.HLP for more details), C:\BGFAX is the path
         where I want all faxes to be stored, "1" is the communications
         port, and the "Z" represents I want faxes saved in ZyXEL's ZFAX
         image format.

         If you want to run BGFAX on a multinode system, an optional fifth
         parameter can be used.  This fifth parameter can be up to three
         characters and it is called the PID.  Example:

              BGFAX /FAX C:\BGFAX 1 Z 99

         The only difference between the command above and the previous one
         is that rather than making a BGFAX.LOG, all log entries will be
         written to a file called BGFAXpid.LOG, in this case, BGFAX99.LOG.

         -------------------------------------------------------------
         MISCELLANEOUS /HOST AND REAREND (/Fxxx) OPTIONS
         -------------------------------------------------------------

         Stop that hopping blue box
         ==========================

         In /HOST mode, the BGFAX status box hops around the screen every
         10 seconds to prevent screen burn-in.  However, some people got
         dizzy watching the box, and others complained that the screen move
         was taking up too many time slices in multitasking environment.
         The /NH parameter will force "No Hop" mode which has considerably
         less screen writes when sitting idle.

              bgfax /host /nh

         50 Line Mode
         ============

         BGFAX can use VGA's 50 line mode if you wish by using the /50
         command line parameter:

              bgfax /host /50
              bgfax /send c:\bgfax\fax0004.fax 893-9124 /50
              bgfax /fco c:\bgfax 1 z /50

         BGFAX and the USR 21.6K modem with September 93 chips
         =====================================================

         If you are using BGFAX with the USR 21.6K modem, BGFAX will
         default to use the 12/08/93 firmware revision.  If you wish to use
         BGFAX with the 09/20/93 firmware, you will need to use the /OU
         switch on the BGFAX command line.  Example:

              bgfax /host /ou
              bgfax /fco c:\bgfax 4 q /ou

         ...DO NOT USE THE /OU SWITCH WITH ANY OTHER MODEM *EXCEPT* THE USR
         21.6K WITH SEPTEMBER 1993 FIRMWARE!

         Turning off the alert sound BGFAX makes when it receives a fax
         ==============================================================

         BGFAX will automatically sound an "alarm" to let you know when a
         succesful fax reception occurs.  This "alarm" is annoying to some
         people.  To disable the "alarm", use the /NS switch for No Sound

              bgfax /host /ns
              bgfax /fast c:\bgfax 1 z /ns

         Telling Class 1 modems to receive at a maximum of 9600 bps
         ==========================================================

         If your Class 1 modem can receive at a maximum of 9600, strange
         things will happen if you forgot to tell BGFAX this, since it will
         default to tell the other side you will be using 14400 bps for fax
         operations.  To force BGFAX to receive at a maximum of 9600 bps
         with Class 1 faxmodems, use the /DIS:79 parameter, i.e.:

              bgfax /fhay:713_893_9124 c:\bgfax 1 z /dis:79 /ns

         Don't try using any other values on the /DIS: parameter.  It is
         mainly available as a debuging option for me.

         TSR fax notification
         ====================

         BGFAX comes with an optional TSR program (NFAX.COM) that will
         place the word "FAX" on your screen whenever a successful incoming
         fax occurs.  However, you must tell BGFAX that you wish to alert
         NFAX.COM to display the message.  You can do this by using the /NF
         switch.  Example:

              bgfax /fcon c:\bgfax 2 q /nf

         This will activate the NFAX.COM interrupt and cause the message to
         get displayed.  To turn the message off, you can run the FAXOFF.COM
         program contained in the BGFAX archive.  Remember, NFAX.COM is a
         TSR and must be loaded in your AUTOEXEC.BAT properly if you wish
         to use it with BGFAX.  It is totally optional!

         NFAX.COM/FAXOFF.COM techinical information:
         ===========================================

         Here is a snip of the Turbo Pascal source code that tells NFAX.COM
         to put the fax indicator on the screen:

              var
                regs : registers;
              begin
                writeln('Activating "NFAX" interrupt.');
                regs.ah := 30; { nfax-function }
                regs.al := 21; { nfax-sub function }
                regs.bl := 95; { nfax-"FAX" attribute, white on purple }
                intr($55, regs); { nfax-tsr }
              end;

         When you want to turn off the "FAX" alert message, you need to
         run the included "FAXOFF.COM" file.  It basically issues the
         same code above except that "regs.al := 22" instead of 21.
         (Go into DEBUG and do an unassemble on the .COM file to see
         exactly how to turn it off.)

         -------------------------------------------------------------
         AFTER YOU RECEIVE THE FAX
         -------------------------------------------------------------

         NAMING CONVENTION
         =================
         The name of the fax file will be FAXnnnn.xFX where "nnnn" is a
         number that is padded with zeros and "x" is the letter "Z" or "Q"
         depending upon which fax format you save the file in.  If you ever
         see a BGFAX.$$$ file in your directory, it should *NOT* be there,
         as it should have been renamed in the FAXnnnn.xFX format.  If it
         is there, it means some kind of problem happened during the fax
         reception.

         FAXIN.LOG
         =========
         BGFAX creates a BGFAX.LOG file that contains a bunch of
         information that is mainly only for debug purposes.  A much
         cleaner log file is called FAXIN.LOG and looks like this:

Date  Time  ET    Bytes   Rate  Filename     Remote Fax ID        Pgs  Notes
-------------------------------------------------------------------------------
12-21 11:52 00:42   18183  9600*FAX0001.FAX  Unknown                2  Finished
12-21 18:04 00:38   18182  9600 FAX0002.FAX  Unknown                2  Not Done
12-22 21:30 00:29   17793 14400*FAX0003.FAX  7138939124             1  Finished
12-22 21:42 00:29   17541 14400 FAX0004.FAX  TRANQUILITY BASE       1  Finished
12-23 06:44 00:32   16941  9600*FAX0005.FAX  Null ID Received       1  Finished
12-25 17:21 01:22  107392 14400*FAX0006.FAX  7132424708             1  Finished

         The asterick between the fax DCE rate and the filename indicates
         the fax was marked as high resolution.  "Not Done" under Notes
         means that BGFAX believed more pages were to have followed, but
         were not actually received.  "ET" is estimated time.  Everything
         else is self explanatory.

         VIEWING/PCX CONVERSION
         ======================

         You can use the included VIEW.EXE file to view the faxes you have
         received.  It's use is quite simple:

              VIEW FAX0002.FAX

         ...will cause VIEW.EXE to start viewing operations on FAX0002.FAX.
         Note that VIEW will default to VGA graphics mode.  If you need to
         use EGA or CGA modes, do so like this:

              VIEW FAX0002.FAX /CGA   or  VIEW FAX0002.FAX /EGA

         When you are viewing the fax, you have a few options:

         Alt-F ... Flip the image (makes upside down and mirrors)
         Alt-I ... Inverse the image (white-black -> black-white)
         Alt-S ... Shrink current on-screen image to 1/3 width
         PgDn .... go to next page
         PgUp .... go to previous page
         ...and the Up/Down/Right/Left arrows do their normal job.

         Note that viewing the fax, with my VIEW.EXE program, takes up
         quite a bit of memory.  (It uses 216 bytes of memory for each scan
         line, so a single high resolution fax page of 2200 lines uses
         a minimum of 475K of memory!)

         If you want to convert a fax to PCX ...

              VIEW FAX0002.FAX /PCX

         ...would create a FAX0002.P01 and FAX0002.P02 file.  (Two PCX
         files since there are two pages in this fax image.)

         A special option, /BO, is also available with VIEW.EXE.  /BO
         tells VIEW that you wish to flip all the bytes in the fax data
         stream before processing it.  This should NEVER need to be used,
         as it is for my debugging purposes only.  (Basically, using the
         /BO parameter will let VIEW display/convert reverse bit order
         faxes.  Normally, BGFAX will save all faxes in direct bit order,
         no matter what bit order the modem actually receives in.)

         Another special option, /DB, forces VIEW to display the bad scan
         lines of a fax image.  Normally, if VIEW encounters a bad scan
         line, it will display it is a dotted line going all the way across
         the width of the fax image.  If /DB is active, VIEW will put up to
         1728 bits of the incorrectly decoded scan line on the page.

         DOPRINT.BAT
         ===========
         After you successfully receive a fax, BGFAX will exit with an
         errorlevel of 4 and append (or create) a DOPRINT.BAT file.

         CALL C:\BGFAX\EXEPRINT.BAT C:\BGFAX\FAX0085.FAX
         CALL C:\BGFAX\EXEPRINT.BAT C:\BGFAX\FAX0086.FAX

         You do not have to do anything with this at all, but it is
         provided for those of you who wish to print faxes as they are
         received.  It will call the EXEPRINT.BAT file and pass it the
         parameter with the path and name of the fax file that was just
         received.  If you are using Smith Micro Software's Quick Link II,
         for example, and are one of those people that leave your printer
         on 24 hours a day, your EXEPRINT.BAT file might contain this:

         @echo off
         printfax %bgfax%\%1 24pin.qlp

         Remeber to delete the DOPRINT.BAT file after you process it.

         -------------------------------------------------------------
         SEND FAX MODE
         -------------------------------------------------------------

         Currently, if you want to send a fax to another person, the fax
         file must already be in either ZFAX or Quick Link II fax image
         format.

              BGFAX /SEND FAX0001.FAX 893-9124

         See the BGFAX.CNF file for more info, such as maximum amount of
         busy signals and failures before exit, etc.

         At this time, only previously converted fax files can be sent.
         (i.e., ASCII files have to be translated to ZFAX .FAX format or
         QLII .QFX format.)

         BGFAX can exit with three possible errorlevels when sending...

              errorlevel 5  -> fax sent successfully
              errorlevel 1  -> fax send failure
              no errorlevel -> file not found, keypress abort, etc.

         If the number is BUSY, BGFAX will try a few more times (the number
         of times specified in the MB= entry in the BGFAX.CNF file) and
         will pause for SW= number of seconds between dials.  If a failure
         occurs during handshaking or during the actual sending of the fax,
         BGFAX will terminate with an failure errorlevel.

         If you are a programmer, and need to use BGFAX to send faxes, but
         need more information than success or failure, you need to use the
         /ER switch on the BGFAX /SEND command line.  BGFAX will make only
         ONE attempt to send the fax in /ER mode (regardless of BUSY, etc.)

              bgfax /send fax0001.fax 893-9124 /er

         The following "Extended Results" are available:

              errorlevel 14 -> a timeout occurred
              errorlevel 13 -> no +FCON ever occurred (NO CARRIER, etc.)
              errorlevel 12 -> a failure after connect (+FHNG, no XON, etc.)
              errorlevel 11 -> "NO DIALTONE"
              errorlevel 10 -> "BUSY"
              errorlevel 7  -> the number is BLACKLISTED by the modem
              errorlevel 5  -> fax sent succesfully
              errorlevel 1  -> generic fax send failure
              no errorlevel -> file not found, keypress abort, etc.

         MISCELLANEOUS /SEND OPTIONS
         ===========================

         Some Class 2 modems have bugs and cannot send to all fax machines
         reliably in Class 2 mode.  Because of this, the /C1 parameter is
         available.  It causes BGFAX to force the use of Class 1 when
         sending:

              bgfax /send c:\bgfax\fax0001.fax 893-9124 /c1

         Some fax machines and fax modems don't operate very well together
         at 14400 speeds.  You can force BGFAX to use a lower maximum speed
         by putting the BPS rate after the send command, e.g.:

              bgfax /send:9600 fax0001.fax 893-9124
              bgfax /send:7200 fax0001.fax 893-9124
              bgfax /send:12000 fax0001.fax 1-713-893-9124 /c1

         Some Class 1 fax modems, when sending, send the first few scan
         lines on each page garbled unless there is a pause before the
         actual page data is sent.  Using the /HW command will force a
         small delay, which should clear up the pages on the receiving
         end.  The Hayes modem seems to need this wait, while the Supra
         will loose the connection if the delay is initiated.

              bgfax /send fax0001.zfx 893-9124 /hw

         A special option, /SMD, is available for my testing purposes only.
         You should NEVER use this option.  Basically, between each page,
         it will tell the remote fax machine another "document" is coming
         next, rather than the normal response that another "page" is
         coming next.  Example:

              bgfax /send fax0001.fax 893-9124 /smd

         REMEMBER, /SMD is only for testing purposes.  DON'T USE /SMD!

         FAXOUT.LOG
         ==========

         A FAXOUT.LOG file is created when sending out faxes to indicate
         the success or failure.  Here is an example:

Date  Time  ET    Bytes   Rate  Filename     Phone Number         Pgs  Notes
-------------------------------------------------------------------------------
03-22 13:18 00:25    3882 14400 RESPOND.FAX  8939124                2  Finished
03-22 13:18 00:11    3884 NOFAX RESPOND.FAX  8939124                0  Busy
03-22 13:19 00:11    3884 NOFAX RESPOND.FAX  8939124                0  No Fcon
03-22 13:30 00:31    3208  7200 RESPOND.FAX  8939124                0  Bad Conn
03-22 13:31 00:28    3882  9600 RESPOND.FAX  8939124                2  Finished
03-23 14:42 00:26    3882 14400 RESPOND.FAX  8939124                1  Timeout
03-23 14:44 00:29    3882 NOFAX RESPOND.FAX  8939124                0  BlackLst
03-23 14:47 00:21    3882 NOFAX RESPOND.FAX  8939124                0  Max Busy
03-23 14:51 00:23    3882 14400 RESPOND.FAX  8939124                1  Gen Fail
03-23 14:54 00:05    3882 NOFAX RESPOND.FAX  8939124                0  No Dial

         -------------------------------------------------------------
         HANGUP STATUS CODES
         -------------------------------------------------------------

         When BGFAX reports "Problematic fax reception", it will indicate a
         fax hangup code, such as [+FHNG: 73].  This chart, taken from the
         Supra CLASS_2.TXT fax command set documentation (which, I believe
         was taken from the Rockwell Class 2 documentation), allows you to
         match up the +FHNG message with its true meaning.  For example,
         +FHNG: 73 would indicate "T.30 T2 timeout, expected page not
         received", which really does not say much, but it may give you
         some clue.  I don't know what most of these mean myself, so I
         don't know whether it will provide you any luck or not, but, many
         people asked that it be included, so here it is.

     /-----------------------------------------------------------------\
     | 2.0   Class 2 |  Cause Description                              |
     | --------------|-------------------------------------------------|
     | 00-0F     0-9 |  CALL PLACEMENT AND TERMINATION                 |
     |---------------|-------------------------------------------------|
     | 00          0 |  Normal and proper end of connection            |
     | 01          1 |  Ring Detect without successful handshake       |
     | 02          2 |  Call aborted, from +FK/+FKS or <CAN>           |
     | 03          3 |  No Loop Current                                |
     | 04        n/a |  Ringback detected, no answer (timeout)         |
     | 05        n/a |  Ringback detected, answer without CED          |
     |---------------|-------------------------------------------------|
     | 10-1F   10-19 |  TRANSMIT PHASE A & MISCELLANEOUS ERRORS        |
     |---------------|-------------------------------------------------|
     | 10         10 |  Unspecified Phase A error                      |
     | 11         11 |  No Answer (T.30 T1 timeout)                    |
     |---------------|-------------------------------------------------|
     | 20-3F   20-39 |  TRANSMIT PHASE B HANGUP CODES                  |
     |---------------|-------------------------------------------------|
     | 20         20 |  Unspecified Transmit Phase B error             |
     | 21         21 |  Remote cannot receive or send                  |
     | 22         22 |  COMREC error in transmit Phase B               |
     | 23         23 |  COMREC invalid command received                |
     | 24         24 |  RSPEC error                                    |
     | 25         25 |  DCS sent three times without response          |
     | 26         26 |  DIS/DTC received 3 times; DCS not recognized   |
     | 27         27 |  Failure to train at 2400 bps or +FMS/          |
     |               |                                  +FMINSP value  |
     | 28         28 |  RSPREC invalid response received               |
     |---------------|-------------------------------------------------|
     | 40-4F   40-49 |  TRANSMIT PHASE C HANGUP CODES                  |
     |---------------|-------------------------------------------------|
     | 40         40 |  Unspecified Transmit Phase C error             |
     | 41        n/a |  Unspecified Image format error                 |
     | 42        n/a |  Image conversion error                         |
     | 43         43 |  DTE to DCE data underflow                      |
     | 44        n/a |  Unrecognized Transparent data command          |
     | 45        n/a |  Image error, line length wrong                 |
     | 46        n/a |  Image error, page length wrong                 |
     | 47        n/a |  Image error, wrong compression code            |
     |---------------|-------------------------------------------------|
     | 50-6F   50-69 |  TRANSMIT PHASE D HANGUP CODES                  |
     |---------------|-------------------------------------------------|
     | 50         50 |  Unspecified Transmit Phase D error             |
     | 51         51 |  RSPREC error                                   |
     | 52         52 |  No response to MPS repeated 3 times            |
     | 53         53 |  Invalid response to MPS                        |
     | 54         54 |  No response to EOP repeated 3 times            |
     | 55         55 |  Invalid response to EOP                        |
     | 56         56 |  No response to EOM repeated 3 times            |
     | 57         57 |  Invalid response to EOM                        |
     | 58         58 |  Unable to continue after PIN or PIP            |
     |---------------|-------------------------------------------------|
     | 70-8F   70-89 |  RECEIVE PHASE B HANGUP CODES                   |
     |---------------|-------------------------------------------------|
     | 70         70 |  Unspecified Receive Phase B error              |
     | 71         71 |  RSPREC error   (before TCF??)                  |
     | 72         72 |  COMREC error   (after TCF??)                   |
     | 73         73 |  T.30 T2 timeout, expected page not received    |
     | 74         74 |  T.30 T1 timeout after EOM received             |
     |---------------|-------------------------------------------------|
     | 90-9F   90-99 |  RECEIVE PHASE C HANGUP CODES                   |
     |---------------|-------------------------------------------------|
     | 90         90 |  Unspecified Receive Phase C error              |
     | 91         91 |  Missing EOL after 5 seconds                    |
     | n/a        92 |  < Not assigned >           /--- Rockwell only  |
     | 92 -Note-> 94 |  Bad CRC or frame (ECM {or BFT} modes)          |
     | 93         93 |  DCE to DTE buffer overflow                     |
     |---------------|-------------------------------------------------|
     | A0-BF 100-119 |  RECEIVE PHASE D HANGUP CODES                   |
     |---------------|-------------------------------------------------|
     | A0        100 |  Unspecified Receive Phase D errors             |
     | A1        101 |  RSPREC invalid response received               |
     | A2        102 |  COMREC invalid response received               |
     | A3        103 |  Unable to continue after PIN or PIP            |
     |---------------|-------------------------------------------------|
     | C0-DF     n/a |  RESERVED FOR FUTURE STANDARDIZATION            |
     | E0-FF     n/a |  REVERVED FOR MANUFACTURER SPECIFIC USE         |
     | n/a   120-255 |  RESERVED CODES                                 |
     \-----------------------------------------------------------------/
 
         -------------------------------------------------------------
         ACKNOWLEDGEMENTS
         -------------------------------------------------------------

         I would like to thank the following people for their assistance
         during the beta test phase.

         Bill Huther
         Brian Wood
         Russell Kroll
         Ethan Brofman
         Ed Lucas
         ...and many people from the Internet and FidoNet.

         US Robotics and Hayes have also been very helpful in getting
         BGFAX to work with their modems.

         -------------------------------------------------------------
         SHAREWARE
         -------------------------------------------------------------

         THIS PROGRAM IS SHAREWARE.

         If you use this program for more than four weeks you are required
         to register it for its low cost of only $25 US DOLLARS.  If you
         cannot afford this we can work something out.

         Please make sure BGFAX works before registering.

         Registrations encourage frequent updates.

         If you are paying by check or money order, please print out the
         REGISTER.FRM file, fill it out, and mail it to my address.

         If you are paying by credit card (Visa, Mastercard, Discover or
         American Express) you can (1) mail the form to me, (2) fax the
         form to me, (3) netmail the form to me, or (4) call my BBS and
         open door #6 and instantly register.

         All people will have to call my BBS and open door #6 to pick up
         the BGFAX.KEY registration key file.

         I will mail (or air mail) registration letters out as well.

         -------------------------------------------------------------

         Regards,
         B.J. Guillot