ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
IRDC ù INFRA-RED Direct Control
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Version 1.03
October 1993

Copyright 1993 ù D.Huras ù All Rights Reserved

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄIRDC.DOC v1.03ÄÄÄÄÄÄ
CONTENTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 1. DESCRIPTION
 2. WARNING
 3. WARRANTY
 4. FEATURE OVERVIEW
 5. REQUIREMENTS
 6. INSTALLATION INSTRUCTIONS
 7. COMMAND LINE ARGUMENTS
 8. COMMUNICATION PORTS
 9. PROGRAM OVERVIEW
10. KEYBOARD USAGE
11. APPLICATIONS
12. ONE FOR ALL REMOTES
13. PROBLEM RESOLUTION
14. REGISTRATION INFORMATION
15. UPGRADE INFORMATION
16. OTHER HOME AUTOMATION SOFTWARE
17. RELEASE HISTORY

1. DESCRIPTION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
IRDC is a program that sends commands to a ONE FOR ALL (*1) Remote
Control that instruct the remote control to emit INFRA RED (I/R)
signals.  Essentially, IRDC emulates a person pressing buttons on
the remote control keypad.  Any button sequence that can be
physically entered on the remote control keypad can be emulated with
the IRDC program including setting the Device type.

IRDC will only operate with ONE FOR ALL remote controls that have an
external port; the ONE FOR ALL 6(*1) and ONE FOR ALL 12(*1) are
currently the only models with an external port.  A special serial
cable with a 3-pin male connector at one end (that plugs into the
ONE FOR ALL external port) and an RS232 9-pin female connector on
the other end (that plugs into a PC serial port) is used to allow
the software to communicate with the remote control.  (This cable
can be ordered from the author --- see REGISTRATION INFORMATION).
The external port is located under the battery cover and its
primary purpose is for upgrading the remote control (ie. loading
new I/R signals into the remote control).  The ONE FOR ALL remote
controls cannot "learn" new I/R signals; however, they can be "force
fed" new I/R signals through the external port.  This may be
necessary if you acquire new electronic equipment with I/R signals
that are not defined within your ONE FOR ALL remote control.

Unless your electronic equipment is located near your PC and you can
"aim" the ONE FOR ALL remote control appropriately, then the
benefits of IRDC may not be readily apparent.  To get the most out
of IRDC, you really need an I/R extender such as the X-10 Powermid
product.  This enables you to locate your PC and remote control
anywhere in your home or apartment and distribute I/R signals to
other locations.  See the 'APPLICATIONS' section of this document
for further information.

IRDC is a DOS program that uses a simple point & click user
interface.  (A Mouse though not required is highly recommended).
IRDC is designed to be robust software that is processor speed
independent.  This program is shareware and you are invited to
evaluate it for 30 days. If you continue to use the program after
the 30 day evaluation period you are asked to register it.  The
author retains all rights to the program.

ÄÄÄÄ
(*1) ONE FOR ALL, ONE FOR ALL 6, ONE FOR ALL 12, and The "Universal"
     Remote are trademarks of Universal Electronics Inc.

2. WARNING
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ONE FOR ALL Remote Controls are sensitive devices; using a ONE FOR
ALL Remote Control with a Special Serial Cable connected to a PC
Serial Port could alter the memory contents of the Remote Control
possibly rendering it inoperable if the following precautions are
not adhered to:

1) Ensure that the PC is powered-off.
2) Plug the Special Serial Cable into the PC Serial Port.
3) Plug the Special Serial Cable into the ONE-FOR-ALL Remote
   Control.
4) Ensure that there are no loose connections.
5) Power on the PC and run the software.
6) VERY IMPORTANT: DO NOT TOUCH ANY BUTTONS on the remote control
   when using the software.
7) Do not disconnect the Special Serial Cable until the PC is
   powered off.

The author assumes no liability for damages, direct or
consequential, which may result from the use of IRDC.

NOTES:
ÄÄÄÄÄÄ
ù If you follow these precautions you should not encounter any
  problems using your remote control with the software or manually.

ù If you physically press buttons on the keypad while the software
  is communicating with the remote control strange things can
  happen that could affect the operability of your remote control.
  If the memory contents of your remote control are altered then the
  only way to restore it to normal operation is to have it reloaded
  by Universal Electronics or a local Service Dealer.

3. WARRANTY
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
IRDC is supplied AS IS.  The author disclaims all warranties,
expressed or implied, including, without limitation, the warranties
of merchantability and of fitness for any purpose.  The author
assumes no liability for damages, direct or consequential, which may
result from the use of IRDC.

4. FEATURE OVERVIEW
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ù User-Friendly full screen point & click DOS character-based
  Interface; your PC screen becomes a large remote keypad.

ù All program functions can be controlled using a mouse; no keyboard
  intervention is required.

ù Supports Standard CommPorts 1 thru 4 and a User Defined CommPort
  which can support any IRQ between 1 & 15 (inclusive) and any
  Base I/O Address.

ù Optional comprehensive on-line Help sub-system.

ù All program parameters can be stored within an INI file thereby
  obviating the need for any command line arguments.

ù Extended Remote Codes can also be defined within the INI file
  and presented in a List Box along with your description.  (Eg. TV
  10  Surround ON).  You can simply double click on the list box
  entry instead of trying to remember the extended code and then
  clicking TV,A,1,0.  The entries in the list box are unsorted and
  added in the same order as they are encountered within the INI
  file.  This allows you to arrange the list in the order that you
  prefer.

ù The program WILL load without a ONE FOR ALL remote control
  connected.  It will still attempt to use the serial CommPort; in
  most cases (eg. if you have a modem attached to the serial port)
  the results will be innocuous.  However, be aware that any device
  connected to the CommPort configured for use with IRDC will
  receive serial transmissions.

5. REQUIREMENTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ù An IBM-Compatible PC with at least 1 serial port.

ù A ONE FOR ALL 6 (URC-4000-2) or ONE FOR ALL 12 (URC-5000-2) remote
  control.  IRDC does not currently support the 1st generation of
  these remote controls (URC-4000-1 & URC-5000-1) respectively.
  Support may be added in the future if user demand warrants it.
  (The 2nd generation remote controls have different keypad layouts,
  see the 'ONE FOR ALL REMOTES' section if you are unsure if your
  remote is a 1st or 2nd generation model).

ù A Special Serial Cable to connect the ONE FOR ALL remote to a PC
  Serial Port.  (Can be ordered from author --- see REGISTRATION
  INFORMATION).

ù A Colour adapter/display is recommended although the program
  should run with a monochrome display/adapter.  If you
  experience problems with the default colors, then try the /BW
  command line argument which will set everything to Black &
  White.

The program requires approximately 360K available conventional memory
to run.  The memory requirements will increase as you add Extended
Remote Code definitions to the IRDC.INI file.  (eg. 100 definitions
will require an additional 6.5K of memory --- approximately).

6. INSTALLATION INSTRUCTIONS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
There are no special installation instructions; simply copy the
program to a sub-directory of your choice and run it.  The program
will look for 2 files in the directory it is run from.  However,
the program will run with or without the following 2 files:

  1) IRDC.HLP
     IRDC retrieves the on-line help text from this file. If the
     file is not found then IRDC will disable the 'Help' command
     button and the Help feature will be unavailable.  The program
     will load slightly faster when the help sub-system is not
     loaded; if you decide that you no longer require the online
     help you can simply delete or rename the IRDC.HLP file.

  2) IRDC.INI
     IRDC will look for an IRDC.INI file in the current
     directory.  All program parameters can be defined within
     this file as well as Extended Remote Code definitions.  Any
     errors found within the IRDC.INI file will be reported and
     the program will be terminated.  IRDC will generate an
     IRDC.INI file (or overwrite an existing IRDC.INI file) when
     the 'Save' button on the Configuration panel is clicked.
     Note that Command Line Args will ALWAYS OVERRIDE
     conflicting parameters within the IRDC.INI file.  A sample
     IRDC.INI file, generated by IRDC, is shown below:

;
;IRDC.INI File Created: 10-02-1993 07:37:33
;
; All Lines prefixed with ; are ignored
; Program Options
; ---------------
; CommPort=1,2,3 OR 4  DEFAULT=1
; Model=6 or 12        DEFAULT=6
; BW=YES or NO         DEFAULT=NO (Colour)
; WARNING=YES or NO    DEFAULT=YES
;
Model=6
BW=NO
WARNING=YES
;
; User Defined CommPort
; ---------------------
; IRQ and Base_IO_Address apply to User Defined CommPort ONLY
;
; IRQ=1-15                 DEFAULT=4; IF Base_IO_Address is set
; Base_IO_Address=nnnn(n)  DEFAULT=1016; IF IRQ is set
;
; NOTE: The presence of either IRQ or Base_IO_Address in the
;       INI file will enable the 'User Defined CommPort'
;
IRQ=4
Base_IO_Address=1016
;
; Extended Remote Codes
; ---------------------
;
; The codes applicable to your I/R devices can be found in your
; your ONE FOR ALL manual.  These codes range from A10 - 78
;
CODE=TV,10,DISPLAY
CODE=TV,11,MTS
CODE=TV,12,PICTURE +
CODE=TV,13,PICTURE -
CODE=TV,14,SLEEP
CODE=TV,15,TV/VIDEO
CODE=TV,15,ANTENNA/AUX
CODE=TV,18,COLOUR UP
CODE=TV,19,COLOUR DOWN
CODE=TV,20,BRIGHT UP
CODE=TV,21,BRIGHT DOWN
CODE=TV,22,HUE UP
CODE=TV,23,HUE DOWN
CODE=TV,24,MATRIX/SURROUND
CODE=VCR,10,SLOW SRCH UP
CODE=VCR,11,SLOW SRCH DN
CODE=VCR,12,MENU
CODE=VCR,13,SELECT
CODE=VCR,14,ON SCREEN
CODE=VCR,15,CANCEL/SKIP
CODE=VCR,16,TIMER
;
; End of IRDC.INI (07:37:33)

7. COMMAND LINE ARGUMENTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
DEFAULTS:  If the program is run without any command line arguments
           it will default to COMMPORT 1,MODEL 6,COLOUR DISPLAY &
           WARNING=YES.  Note that CommPort, Model & Display can
           be toggled from within the program.

The following command line arguments can be entered in any order:

/Annnn(n) ù Base I/O Address applicable to User Defined CommPort
            (Must be specified as a decimal number)
            If /I argument is present, but /A is not; then Base
            I/O Address will default to 1016 (3F8 Hex).

/BW  ù Use Black & White colours
/BW- ù Use Colour (You would only use this argument to override
       an INI BW=YES)

/Cn  ù COMMPORT where n = 1,2,3 & 4

/In  ù IRQ applicable to User Defined CommPort where n = 1 - 15
       If /A argument is present, but /I is not; then IRQ
       will default to 4.

/Mn  ù MODEL where n = 6 or 12

/NW  ù Suppress the program reminder to read the WARNING within Help
       (This command line argument is not required if you have
       elected to forego the online help by renaming or deleting
       IRDC.HLP).
/NW- ù Display Warning (You would only use this argument to override
       an INI WARNING=NO)

/?   ù Display Command Line Arguments

NOTE: ù COMMAND LINE OPTIONS OVERRIDE IRDC.INI SETTINGS
      ù MULTIPLE OCCURRENCES OF THE SAME COMMAND LINE ARGUMENT
        ARE ACCEPTED; THE LAST INSTANCE WILL BE USED BY IRDC.

8. COMMUNICATION PORTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
IRDC supports "pseudo standard" CommPorts 1 thru 4 using the
following settings:

            ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
            ³          ³      ³ Base I/O Address ³
            ³ CommPort ³ IRQ  ÃÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄ´
            ³          ³      ³ Decimal ³  HEX.  ³
            ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
            ³    1     ³   4  ³  1016   ³  3F8   ³
            ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
            ³    2     ³   3  ³   760   ³  2F8   ³
            ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
            ³    3     ³   4  ³  1000   ³  3E8   ³
            ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
            ³    4     ³   3  ³   744   ³  2E8   ³
            ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÙ

If one of these CommPort settings matches your hardware
configuration simply use the /C command line argument with the
appropriate CommPort.  The CommPort= IRDC.INI directive can also be
used.   Note that if IRDC is run without the /I (IRQ) or /A (Base
I/O Address) Command Line arguments then the 'User Defined CommPort'
is "undefined" and cannot be selected from the Configuration panel.

If your hardware configuration differs from the table above, then
you can define your own CommPort by using the /I and /A command line
arguments (or IRQ= & Base_IO_Address= IRDC.INI file directives).
IRQ can be set to any value between 1 and 15 (inclusive).  Base I/O
Address can be set to any value greater than zero.  CAUTION: your
hardware may "lock up" if incorrect settings are used.  You should
supply both arguments (/A & /I), however, if you only supply one of
the arguments then the defaults applicable to CommPort 1 will apply
to the other argument.  (eg. if only the /I5 argument is supplied,
then the /A argument defaults to 1016).  If either the /I or /A
argument is supplied, then the 'User Defined Commport' on the
Configuration panel becomes enabled.

NOTES: 1) The Program will accept any combination of /C,/I,/A
          command line arguments and CommPort=,IRQ=,& Base_IO_Address=
          IRDC.INI settings.  The presence of any of the User Defined
          CommPort parameters will enable the 'User Defined CommPort'.
          However, the startup (or active) CommPort will always be
          the last CommPort setting.  For example, if IRQ=7 is defined
          in the INI file, but COMMPORT=3 is also defined later on
          in the file, then CommPort 3 becomes the startup CommPort.
          In the same scenario, if /A3220 is specified on the Command
          Line, then the startup CommPort becomes the User Defined
          CommPort where IRQ=7 and Base I/O Address=3220.  The
          CommPort is NOT opened until a remote keypad button is
          'clicked'.

       2) THE BASE I/O ADDRESS MUST BE SPECIFIED IN DECIMAL NOTATION.

          IBM PS/2 CommPort Parameters are shown below:
            ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
            ³   PS/2   ³      ³ Base I/O Address ³
            ³ CommPort ³ IRQ  ÃÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄ´
            ³          ³      ³ Decimal ³  HEX.  ³
            ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
            ³    1     ³   4  ³  1016   ³  3F8   ³
            ³    2     ³   3  ³   760   ³  2F8   ³
            ³    3     ³   3  ³ 12832   ³ 3220   ³
            ³    4     ³   3  ³ 12840   ³ 3228   ³
            ³    5     ³   3  ³ 16928   ³ 4220   ³
            ³    6     ³   3  ³ 16936   ³ 4228   ³
            ³    7     ³   3  ³ 21024   ³ 5220   ³
            ³    8     ³   3  ³ 21032   ³ 5228   ³
            ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÙ
          A User Defined CommPort must be used for
          PS/2 CommPorts 3-8.


9. PROGRAM OVERVIEW
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
When the program loads, it looks for an IRDC.INI file in the current
directory and then proceeds to parse it if one is found.  If any
errors are detected within the INI file the program will terminate
with an appropriate message, otherwise it will parse the command
line arguments (which override any conflicting INI directives).
Once again, if any errors are found it will terminate with an
appropriate message.  Finally, it will look for a IRDC.HLP file and
activate the online Help if the file is found.  The IRDC full screen
interface will then be presented with the remote keypad displayed on
the right and the various program controls displayed on the left.
The upper left button of the remote keypad is the "active" control
at this time.  The program DOES NOT open the CommPort until you
actually press one of the remote keypad buttons; this allows you to
confirm the active CommPort before actually using it.

The Status Window on the upper left side of the screen will display
all remote keypad button activity as it is executed.  In addition
it will display a message each time a CommPort is opened.  (eg. the
first time you press a remote keypad button there will be a very
brief delay as the CommPort must be opened first).  There is also
a small LED indicator in the middle of the screen which will flash
briefly whenever a remote keypad button is clicked/pressed.

When the configuration button is clicked, the Configuration panel is
overlaid on the left side of the screen.  The current settings for
the Model, CommPort, Display and the Warning Flag are indicated with
option buttons.  If you change the Model or Display settings the
screen will immediately reflect the new settings.  To make your
settings permanent, click on Save; all current settings (including
any Extended Remote Code definitions) will be written to the
IRDC.INI file.  If an IRDC.INI already exists, the program will
display an Overwrite Confirmation before overwriting the existing
IRDC.INI file.  To continue with these new settings for the current
session only, click on OK; to restore the prior settings, click on
Cancel (or press ESCAPE).

As stated earlier, a mouse is highly recommended; you can simply
click on the remote keypad buttons, the control buttons and the
Extended Remote Code List Box scroll bars to perform program
functions.  To execute an Extended Remote Code contained within the
Extended Remote Code list box, simply Double Click on it.

10. KEYBOARD USAGE
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Use the TAB/Shift-TAB keys to move among the various remote keypad
buttons and the control buttons (eg. Configure, Help & Exit).  The
Up/Down arrows can be used to move up and down the Extended Remote
Code List Boxes.  Use the Space Bar key to select the current List
Box item, check/uncheck a check box, or invoke a command button.
(The Enter key can also be used for all controls except the Extended
Remote Code list box; the space bar must be used.) The ESCAPE key
will exit the current function or the program if no other windows
are visible.

The cursor keys can be used to navigate within the keypad area; you
can jump to adjacent buttons by pressing the appropriate key.  The
program will jump over 1 blank row/button if an ajacent button is
not present.

The following quick access keys are applicable when
the Configuration Panel IS NOT displayed:

      Configure ù Alt-c
           Help ù Alt-h
           Exit ù Alt-x
   Remote Codes ù Alt-d

The following quick access keys are applicable when the Configuration
Panel IS displayed:

          Model ù Alt-m
       CommPort ù Alt-p
        Display ù Alt-d
        Warning ù Alt-w
             OK ù Alt-o
           Save ù Alt-s
         Cancel ù Alt-a

11. APPLICATIONS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
After experimenting a little with IRDC you may find yourself
thinking: "its a neat 'toy' but what practical uses does it have?"
This section attempts to describe the practical applications for
this type of software.

Generating I/R Signals & IRDQ.EXE
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
IRDC allows you to generate I/R signals simply by clicking the
buttons on the on-screen remote keypad.  It also allows you to build
a list box of those 'difficult to remember' Extended Remote Codes
which you can invoke with a double click.  It offers convenience
since you can leave it running in a window when working in a
multi-tasking or task-switching environment and simply switch to it
as required.  However, it does require 'human' intervention since
you have to physically click your mouse button in order to generate
I/R signals.  This is where IRDQ.EXE comes into play; IRDQ is a
command line driven version of IRDC that instructs ONE FOR ALL
remotes to emit I/R signals based on a button name passed on the
command line.  Alternatively, it will 'press' a series of buttons
that are contained within a file when the filename is passed to IRDQ
on the command line.  This means you can build "macros" by creating
files of the button names to be pressed.  In addition, it means the
entire library of ONE-FOR-ALL I/R codes is at your disposal because
you can dynamically set the device type at anytime.  For example,
you could build a button file containing the following button
names:

     ;
     ; IRDQ Button File - Turn on both TV's
     ; Note: lines prefixed with ";" are ignored
     ;
     ; Assign TV Code: 000 (Sony TV)
     TV
     A
     B
     C
     0
     0
     0
     ; The Wait button name does not exist,but instructs IRDQ
     ; to wait for 1/2 second to allow the ONE FOR ALL remote
     ; to 'catch up'
     Wait
     ; The SONY TV has an Extended Remote Code to turn the POWER ON
     ; use this code rather than the POWER button which is just
     ; a toggle
     A
     6
     8
     Wait
     ; Assign TV Code: 047 (GE TV)
     TV
     A
     B
     C
     0
     4
     7
     Wait
     ; The GE TV has an Extended Remote Code to turn the POWER ON
     ; use this code rather than the POWER button which is just
     ; a toggle
     A
     1
     8

The end result being you can build a virtually unlimited library
of I/R signal sequences and generate them simply by invoking a
program from the DOS command prompt.

I/R Signal Distribution
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
The range of the I/R signals that the remote control generates based
on instructions from the software is limited to the same room as
where your PC is located.  This limitation is severe enough that the
program would not be very useful at all unless you happened to
locate all of your I/R electronic equipment in the same room as your
PC.  This is obviously unrealistic, but fortunately there is a
relatively inexpensive solution that will enable you to distribute
I/R signals to virtually anywhere in your home or apartment.  An I/R
extender can be used to "read" I/R signals from one location,
translate them into radio waves and beam them to one or more other
locations where they'll be translated back into I/R signals and sent
to the targeted electronic equipment.  The entire process takes
milliseconds and is virtually instantaneous.  The X-10 Powermid is
an I/R Extender; it has 2 components, a unit that receives the I/R
signals and transmits them via radio waves, and a unit that picks up
the radio signals and transmits the I/R signals.  Both units are
small 3" x 3" x 3" pyramid-shaped devices enclosed within a black
plastic casing.  You can install multiple Receiver/I.R emitters that
are sourced by the same Transmitter; this allows you to distribute
I/R signals to multiple locations.  Recoton also markets an IR
Extender.  To use an I/R extender with IRDC/IRDQ, you'd simply aim
the ONE FOR ALL remote at the I/R Transceiver.

Scheduling I/R Signals
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
With IRDC/IRDQ, a ONE-FOR-ALL Remote & an I/R Extender you have the
capability to easily generate & distribute an I/R signal for just
about any electronic equipment that exists to virtually anywhere
within your home.  The capability to schedule I/R signal
transmissions at predetermined times would be a step closer towards
a completely automated I/R system.  Since IRDQ can be driven from
the DOS command prompt you could accomplish this through the use of
any DOS-based scheduler.  For example, a Scheduler is bundled with
Central Point's PC Tools.  You lodge the dates & times of the
programs you want to run and then load the resident portion of the
Scheduler into memory as a TSR from your AUTOEXEC.BAT.  The
Scheduler will kick in at the predetermined times and run the programs
you've defined.  If you happen to be working on your computer at a
scheduled program time, the scheduler will ask you if you want to
run the Scheduled program now or delay it; if you proceed to run it
the Scheduler will save the memory image of your current working
environment and restore it after it has run the scheduled program.
There are many other DOS schedulers around including several fine
shareware products.  Back'n Forth, a shareware Task-Switcher, has
many features including a built in scheduler.

Event-Driven I/R Signal Generation
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
A truly automated I/R system should support event-driven I/R signal
generation.  The transmission of I/R signals should not be limited
to scheduled times, but rather, should be driven by events such as
the reception of X-10 signals, changes in temperature, motion
detection, contact closure, etc.  Most PC-based home automation
systems which react to received events support 'shelling to DOS' to
execute programs based on the events you specify; so IRDQ could be
used with these programs to integrate I/R signal generation.  The
HC2000 program is an example of a home automation system that is
based on 2-way X-10 communications.

The HC2000 Home Automation Program
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
HC2000 is a software-based X-10 home automation system.  It requires
a dedicated PC but will run quite satisfactorily on a 4.77 MHz XT.
If you've upgraded your PC and have an older machine that is
collecting dust as a paperweight somewhere then HC2000 will allow
you to put it to good use as the 'brain' of your home automation
system.

HC2000 requires a TW523 device which is a two-way X-10 module that
sends and receives X-10 signals.  An Editor is supplied with HC2000
that allows you to build your home automation program.  You can
send X-10 signals at scheduled times, or when other X-10 commands
are received (allowing you to build remote 'macros'), or based on
the values of user variables that you define and manipulate.  In
addition to having the program respond to events by sending X-10
commands, you can also run DOS programs.  This means you can use
IRDQ.EXE to emit I/R signals based on the events that are trapped
by HC2000.  For example, you could define an X-10 command that would
invoke the button sequence to turn on the two TV's that was defined
earlier in this section; the following steps outline how you could
accomplish this:

1) Create the Button File: TURNTVS.ON

2) Start up the HC2000 editor and create a User Variable entitled
   'DOS IRDQ.EXE TURNTVS.ON'.

3) Add an X-10 remote command using the House/Unit Code that you
   want to define and add a 'LOG' statement using the User Variable
   you defined in step 2: eg:

     þ A1 ON {Turn on both TVs} ::=
       Log "DOS IRDQ.EXE TURNTVS.ON'

   (This command would respond to House Code A, Unit 1.)

4) Exit the HC2000 editor and run HCDOS; HCDOS checks all of the
   messages that HC2000 logs and when it encounters the IRDQ.EXE
   message it will execute IRDQ.EXE and pass it the TURNTVS.ON
   parameter.

IRDQ.EXE has been successfully tested with HC2000.

12. ONE FOR ALL REMOTES
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
IRDC supports ONE FOR ALL 6 and ONE FOR ALL 12 remote controls,
specifically, models URC-4000-2 and URC-5000-2 respectively.  It
does NOT currently support 1st generation models, URC-4000-1 &
URC-5000-1.  The differences between the "-1" and "-2" models are
summarized below:

   URC-4000-1 vs. URC-4000-2
   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   The URC-4000-1 does not have buttons labelled:
       AUX1, AUX2 or CD.

   URC-5000-1 vs. URC-5000-2
   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   The URC-5000-1 does not have buttons labelled:
       VCR, Sat, Aux, Amp, Tuner, F1, F2, F3, F4, Recall, Sleep,
       Display, A/B, Audio, Video, Sleep, or Pgm.

   The URC-5000-2 does not have buttons labelled:
       VCR1, VCR2, DO1, DO2, TV/VCR, Do, D, E, F, G, H.

13. PROBLEM RESOLUTION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The ONE FOR ALL remote control PC interface deploys a relatively
simple communications protocol and you should not experience any
problems provided that your special serial cable is in good
condition and there are no loose connections.  However, the timing
of the serial communications is very critical and there is not much
tolerance for even minor deviation.  Any resident software that
tampers with the system clock could throw the serial communications
out of sync.

If IRDC does not appear to be working at all, then read through the
following checklist to confirm your hardware/software setup.

1) Verify that your remote control is supported; currently only the
   URC-4000-2 and URC-5000-2 are supported.  (See the ONE FOR ALL
   section for details on identifying your remote control model.)

2) Ensure that you are using the correct CommPort; click on the
   Configuration button and verify that the active CommPort is
   correct.

3) Ensure that the special serial cable connections are firm and
   that the cable is not bent or stretched; The most likely cause is
   the 3-pin serial connector not being seated properly in the
   external port of the ONE FOR ALL remote.  In some cases, it may
   appear to be properly seated but in fact it is not.  It may be
   necessary to tape the connection to ensure that it is sound.

4) Ensure that memory resident software is not conflicting with
   IRDC by booting your PC without any Device Drivers or TSR's.
   (ie. use a stripped down CONFIG.SYS and AUTOEXEC.BAT).

If IRDC appears to be working but you run into a situation where the
LED on the remote control stays ON with an amber colour and will not
turn off, then communications between the remote control and the
software have been disrupted. The most likely cause for this is a
loose connection.  The remote control is in Serial Execution mode;
power OFF your PC, check cable connections, power ON your PC and
reload IRDC.  Click on a remote button and the LED should flicker
amber, then green, then turn off.  If your remote consistently
becomes stuck in Serial Execution mode, then it is probably the
result of a timing problem; please contact the author in this case,
adjustments can be made to the software to work around this.

If the ONE FOR REMOTE becomes "unresponsive" to IRDC, it could be
because commands were sent to it while it was executing a macro.
This only applies to a ONE FOR ALL 12 which will not act on commands
sent while it is executing a macro; you should wait for the macro
to complete before sending more commands.

If your problems persist, then please report your problem to the
author who will attempt to resolve any problems you encounter.

The open architecture of the PC compatible operating environment and
the near infinite combinations of hardware and software complicate
the compatibility of applications software.  While every effort has
been made to ensure that IRDC is compatible with as many hardware
and software combinations as possible, there may be operating
environments in which IRDC will not run properly.

Problems can be reported to:

   David Huras
   37 Ruddell Crescent
   Georgetown, Ont. L7G 5N4
   CANADA

   FAX: 905-873-6429
   CIS: 72767,472
   Internet: david.huras@canrem.com

14. REGISTRATION INFORMATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
IRDC is currently supplied as fully functioning software without
built-in delays or "nag" screens prompting you to register. However,
the program will timeout after 10 minutes.  This limitation does
not apply to the Registered version.

A significant amount of time and effort went into this program;
please register the program if you intend to use it beyond the 30
day evaluation period.  Registered Users will be shipped a printed
manual and a 3«" diskette (if you would prefer a 5¬" diskette please
advise) containing the Registered Version of the IRDC.

Registered Users will also receive IRDQ.EXE, a command line driven
version of IRDC.  With IRDQ you can press buttons on ONE FOR ALL
remote keypads simply by entering commands at the DOS prompt, for
example you would type IRDQ POWER to press the POWER button.
Alternatively you can pass a file name containing a list of button
names to IRDQ, eg.  IRDQ /F:BUTTON.FIL where BUTTON.FIL contains

  AUX
  WAIT
  POWER
  TV
  WAIT
  POWER
  VCR
  WAIT
  POWER
  "<<"

This "macro" would turn on your Receiver, TV & VCR and rewind the
tape in the VCR.  IRDQ is a compact program which was designed to be
interfaced with software based home automation systems like HC2000.
You could also "grow your own" home automation system by using IRDQ
with a DOS-based program scheduler like the one provided with
Central Point's PC Tools.  All IRDQ program options can be imbedded
within the DOS environment thereby eliminating the need for any
command line arguments other than button names or a filename
containing button names.  (See the APPLICATIONS section for further
information about IRDQ).

You can also order the Special Serial Cable directly from the
author; these cables can be difficult to find and I cannot
guarantee that I will always have stock.  Please feel free to
check on availability by contacting me via Email --- see PROBLEM
RESOLUTION section for Email addresses.  You may be able to find
these cables at a marginally lower cost from other suppliers; (I
have to acquire these cables at 'retail' prices and am charging a
price that merely allows me to break even).

                                         Shipping Destination
                                        USA*    CANADA*   OTHER*
                                       ------   ------    -----
IRDC Registration Fee (includes IRDQ): $25.00   $25.00   $25.00 US$
IRDC Shipping:                           0.00     0.00     2.00 US$

Special Serial Cable:                  $20.00   $20.00   $20.00 US$
Special Serial Cable Shipping:           2.50     2.00     4.00 US$

* USA Prices are quoted in U.S. Dollars.
  CANADIAN Prices are quoted in Canadian Dollars.
  OTHER Prices are quoted in U.S. Dollars.

Complete the REGISTRATION FORM contained in the REGISTER.FRM
file and send with your cheque*/money order to:

   David Huras
   37 Ruddell Crescent
   Georgetown, Ont. L7G 5N4
   CANADA

* Only cheques drawn on Canadian & US Banks will be accepted.
  Money Orders must accompany International Orders.

Alternatively, you may wish to register using CompuServe Shareware
Registration; you can register IRDC, IRDCw(WINDOWS) or BOTH using
CompuServe Shareware Registration.  The Registration Fee will be
charged to your CompuServe billing account and the latest version of
the software will be shipped within one business day. GO SWREG while
on CompuServe to use Shareware Registration.  (Special Serial Cables
must be ordered directly from the author).

Program Title                         Pgm Name  Pgm ID#    Charge
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ  ÍÍÍÍÍÍÍÍ  ÍÍÍÍÍÍÍ   ÍÍÍÍÍÍÍÍ
INFRA-RED Direct Control(DOS)         IRDC        1449     $25.00
(includes IRDQ-DOS)

INFRA-RED Direct Control for WINDOWS  IRDCw       2521     $25.00
(includes IRDQw)

INFRA-RED Control Bundle              IRCB        2522     $40.00
(includes IRDCw,IRDQw,IRDC & IRDQ)

Shareware Registration (SWREG) will prompt you through the
registration process; you can register programs by referring to them
by program name or ID #.  SWREG will display a description of the
program and prompt you to confirm the registration order; you have
the opportunity to abandon the registration process at any time.

15. UPGRADE INFORMATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
REGISTERED USERS of prior versions of IRDC can upgrade to the
current version at ANY TIME by simply sending a diskette containing
their registered version of the software and $2 for postage to the
author.

REGISTERED USERS of IRDCw(WINS) can upgrade to IRDC(DOS) for
a special price of $15.00.  (See REGISTER.FRM for Details)

REGISTERED USERS of IRDC(DOS) can upgrade to IRDCw(WINDOWS) for
a special price of $15.00.  (See REGISTER.FRM for Details)

16. OTHER HOME AUTOMATION SOFTWARE
Program   Description                                     Status
ÄÄÄÄÄÄÄ   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10DC     X10 Direct Control - CP290 Point & Click     Version 1.50
          Initial Release: February '93                December '93

X10EC     X10 Event Control - CP290 Point & Click      Version 1.02
          Interface Program to manage Event Data.      January '94
          Includes Sunrise/Sunset Time Offsets.
          Initial Release: December '93

IRDC/     INFRA-RED Direct Control/Command Line Ctrl   Version 1.03
IRDQ      A program which sends instructions to a      April '94
          ONE FOR ALL (6 or 12) remote control. The
          remote then emits I/R signals.

IRDCW/    INFRA-RED Direct Control for WINDOWS         Version 1.00
IRDQw     INFRA-RED Command Line Control for WINDOWS   April '94

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Please register this software if you use it regularly; by registering
you reinforce my commitment to ongoing development.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

17. RELEASE HISTORY ù IRDC Shareware/Registered Version
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 Date      Version     Changes
ÄÄÄÄÄÄ   ÄÄÄÄÄÄÄÄÄÄ   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

APR'94      1.03      ùAdded Save IRDC.INI prompt when Exit attempted
                       without saving a changed Configuration

MAR'94      1.02      ùRe-enabled ESCAPE key to exit Configuration
                       Panel

OCT'93      1.01      ùEnabled ESCAPE key to exit Program
                      ùCorrected typo in Help File Warning
                       (URC-5000-2 not supported should have
                       read URC-5000-1 not supported)

OCT'93      1.00      First Public Release
                      ùConfiguration Panel Re-organized
                       -SAVE Button Added
                       -Warning CheckBox Added
                      ù'F1' Key to invoke Help added
                      ùCursor Key navigation added to keypad area
                       (cursor keys will navigate to adjacent
                        buttons - will skip 1 row or button if
                        no adjacent button).
                      ùOFA-12 Button Definition Problems Corrected
                       (Mode Buttons, A,B,C, Power, CH+,CH-)
                      ùOFA-12 Extended Remote Code support added
                       for F1 - F4.
                      ùEuropean Date Format Support Added
SEP'93      1.00á     Beta Test

ÄÄÄÄÄÄ