***********************************************************

        VGAPRTSC.ASM   ver 1.3   February 1989

    Hardcopy Utility for VGA-(and EGA-) Graphics Modes

                   Robert Kaempf
                  <DB3D@DDATHD21>
              Institut fuer Kernphysik
           Technische Hochschule Darmstadt
             6100 Darmstadt, West Germany

***********************************************************

VGAPRTSC is similar to the MSDOS program GRAPHICS.COM.
The difference is: GRAPHICS supports low resolution
graphics modes (320x200,640x200), VGAPRTSC supports high
resolution graphics modes (640x480,640x350).
Text or low resolution graphics modes cause a call to the
old hardcopy routine. It is possible to install GRAPHICS
before VGAPRTSC. This will support any graphics modes.

Parameter:
/C= followed by 16 digits
The 16 digits correspond to the 16 screen colors.
An odd digit selects the color to be printed,
colors with even digits are not printed.

Example:
VGAPRTSC /C=0111111111111111   ( default )
   prints colors 1 to 15.
VGAPRTSC /C=0000222211113333
   prints highlighted colors ( 8 to 15 )

You may modify the colortable of an installed VGAPRTSC
version by typing: VGAPRTSC /C=... .
VGAPRTSC will not be installed twice !
---------------------------------------------
ADDITIONAL NOTE BY OH5IY:
I have modified the code to suit the Cannon BJ-10 bubble jet printer.
If you have a problem which can not be solved by chancing printer
setups, use pctoools to edit vgaprtsc.com file.
There is on the 73. byte a 06 hexcode after 1B 41, cgange the value of 06
to smaller if there is a gap between printing lines, larger if there
is compression in the printout. Notice that the printinglines run VERTICALLY
if you look the print sheet and the gaps or compression is also
vertically oriented on the paper.
(I hope this will help you. OH5IY @OH5RBG.FIN.EU)