Arnet AMODE for OS/2 (V1.1.1)

        Introduction

        AMODE is a 'work-alike' of the MODE command under OS/2 but with a
        number of added features and a few different rules of behavior.
        It came to the attention of the Arnet Technical Support Staff
        that the standard MODE command -- though useful for many things --
        was limited in the following ways:

        -- No communications device names besides COM1 - COM8 could be used.
        -- Baud rates above 9600 could not be assigned.
        -- Timeout, Handshake signals, etc. could not be set without having
           to re-specify the Baud rate, Parity and Data type parameters.
        -- If any of the set of Baud_rate:Parity:Databits:Stopbits was left
           off the command line, MODE would assign them to ITS defaults of
           1200,e,7,1, instead of the defaults of whatever those values are
           CURRENTLY set to.  Thus a user wanting only to change Baud rate
           would unknowingly also re-set the Data type and Parity of the
           device.

        AMODE addresses these issues while attempting to remain compliant
        with the familiar MODE command syntax.

        In general, AMODE attempts to forgive as much as possible in terms
        of both the order of the arguments and of each argument's
        requirements for other unrelated arguments.  Given the limited range
        of values that most of the parameters can assume, AMODE will assign
        a parameter based on its value instead of its position in the command
        line.  The syntax of the AMODE command is then

                AMODE device-name[:] [arguments]

        where the device name must be the name of a character-device that
        supports Generic IOCtl system calls.  The Colon is optional and is
        there only to be backward compatible with MODE.  The remainder of
        the arguments are parsed according the following rules.  The
        arguments may appear in any order and must be separated from
        each other with a space and/or comma.  Any parameters left unspecified
        on the command line will be left in their current settings.  In any
        case, AMODE will report the current settings of all parameters AFTER
        such changes as requested on the command line have been assigned.
        Thus with no arguments (i.e. no changes to current settings), AMODE
        simply reports the current settings.

Baud Rate Rules:
        Baud Rates parameters are recognized to be any 2 to 5 decimal
        digit argument to be mapped as follows.
        Accepted values....                     Assigned Baud rate
        -----------------------------------------------------------
        11  110                                           110
        15  150                                           150
        30  300                                           300
        60  600                                           600
        12  120  1200                                    1200
        24  240  2400                                    2400
        48  480  4800                                    4800
        96  960  9600                                    9600
        19  192  1920 19200                             19200
        38  384  3840 38400                             38400
        57  576  5760 57600                             57600
        07                                              76800
        01                                              115200
***Baud rates above 9600 NOT recommended for COM/XI on many channels
***Baud rates above 38400 NOT recommended for any of the cards except on a few
   channels at a time.

Data Bit Rules:
        Data Bit parameters are recognized to be any 1 digit
        consisting of 5,6,7, or 8.

Stop Bit Rules:
        Stop Bit parameters are recognized to be any argument with
        the value of 1, 2, or 1.5.

Parity Rules:
        The Parity parameter is recognized to be any single-letter
        argument with the value of   E, O, N, M, S  -- For (E)ven,
        (O)dd, (N)one, (M)ark, and (S)pace.   Upper or lower case letters
        are acceptable.


Handshake Signals and Timeout parameter Rules:
        These arguments follow the documentation for standard MODE command.
        The accepted signal names are listed below.  In all cases the
        name and assignment may be in any mix of upper an lower
        case characters.

        Full name                  Argument     State Assignments
        -----------------------------------------------------
        Read-timeout                    TO      ON  OFF
        Xon/Xoff handshake              XON     ON  OFF
        Input DSR sensitivity           IDSR    ON  OFF
        Output DSR sensitivity          ODSR    ON  OFF
        Output handshake on CTS         OCTS    ON  OFF
        DTR signal control              DTR     ON  OFF  HS
        RTS signal control              RTS     ON  OFF  HS  TOG

ALT_PIN processing:
        In some cases it is useful to have the driver report changes in
        DSR as if they were changes in CD (the modem Carrier Detect Signal).
        This is sometimes done to get around a limitation of the
        8-wire RJ45 connector -- a connector which leaves pin1 and pin10
        of the standard 10-wire RJ45 unterminated.  Since pin10 is defined to
        be Carrier Detect and so many communications programs depend on
        accurate reporting of the state of this CD signal use of 8-wire
        RJ45 connectors can prevent these programs from working.  A work-around
        is to slightly change the wiring scheme of the 8-wire RJ45 so that
        the CD wire is brought into the middle 8 wires which DO make contact.
        Of course this means that the signal that USED to be defined for that
        location must be moved out to pin10, where CD used to be.  In
        general the LEAST payed-attention-to signal is DSR (on Pin2) so if
        CD is wired to Pin2 and DSR is wired to Pin10 close to full modem
        control can be acheived on an 8-wire RJ45.  The final step in this
        trick is then to instruct the Device driver that for THIS channel
        pin2 is to be interpretted as CD instead of DSR.  AMODE permits
        this ALTERNATE PIN ASSIGNMENT PROCESSING mode to be established on
        channels by issueing the requisite custom command to the XALL driver.

        amode {devname} ALT=ON          ;; report PIN2 as CD
                or
        amode {devname} ALT=OFF         ;; report PIN2 as DSR (default)

        Those interested in implementing this custom call in software should
        look at the file XALL.DOC on the distribution diskette for information.

QUICKWRITE processing:
        Normally, each time an application program WRITEs to a device
        (i.e. makes a request to transmit data), the application is
        suspended until all of the data in the request has actually been
        transmitted.  With many small requests this can be wasteful.  An
        alternate method is to transfer all the data to the shared memory
        buffers on the ClusterPort/S card and leave it up to the intelligence
        on the card to transmit that data according to the relevant
        flowcontrol settings -- and permit the application program to
        proceed with execution.  This greatly increases overall system
        performance but can possibly confuse an application that is attempting
        to very closely track the throughput (bytes/sec transmission rate)
        or doing timeout of fine granularity.


        amode {devname} QW=ON           ;; enable QUICKWRITE processing
                or
        amode {devname} QW=OFF          ;; disable QUICKWRITE (default)

        Those interested in implementing this custom call in software should
        look at the file XALL.DOC on the distribution diskette for information.

Examples:

        amode cps12            [ interrogative; no settings changed ]

        amode com5 2            [ the '2' assumed to be stop bits..  ]

        amode com5:38 rts=ON    [ the '38' is parsed to the baud rate]
                                [ of 38.4K baud, and RTS is turned ON]

        amode com5 8            [ the '8' parsed as  data bits       ]

        amode comdev83 IDSR=OFF,TO=off e 7 12
                                [ IDSR is turned OFF, timeout on reads]
                                [ is set to off, Even-parity is set,  ]
                                [ 7 data bits is set, 1200 baud is set]

        amode com5 38 ALT=ON    [ set 38.4Kbaud, report PIN2 as CD      ]

        amode com5 e alt=off QW=on
                                [ set EVEN parity, report PIN2 as DSR , ]
                                [ enable QUICKWRITE processing        ]