A
                                   Comparison
                                       of
    
    
          ===========================================================
          MM   MM  IIIIIII    CCCC   RRRRRR     OOO             CCCC
          M M M M     I      C    C  R     R   O   O           C    C
          M  M  M     I     C        R     R  O     O         C
          M     M     I     C        RRRRRR   O     O  -----  C
          M     M     I     C        R   R    O     O         C
          M     M     I      C    C  R    R    O   O           C    C
          M     M  IIIIIII    CCCC   R     R    OOO             CCCC
          ===========================================================
          
                                     A N D
          
          ===========================================================
           SSSSS   MM   MM     A     L        L                 CCCC
          S     S  M M M M    A A    L        L                C    C
          S        M  M  M   A   A   L        L               C
           SSSSS   M     M  A     A  L        L        -----  C
                S  M     M  AAAAAAA  L        L               C
          S     S  M     M  A     A  L        L                C    C
           SSSSS   M     M  A     A  LLLLLLL  LLLLLLL           CCCC
          ===========================================================
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
                       Copyright 1990-1994 Dave Dunfield
                              All rights reserved

    MICRO-C .vs. SMALL-C                                             Page: 1


    1. INTRODUCTION
    
          The most common reaction of people hearing about DDS  MICRO-C  for
       the first time is something like "Humph... Another version of the old
       SMALL-C compiler". This couldn't be further from the truth.
    
                           MICRO-C IS NOT SMALL-C!!!
    
          MICRO-C is a completely  new  implementation  of  a  'C'  compiler
       suitable for use on very small systems. It offers several  advantages
       over SMALL-C:
    
        - It was designed from the  ground  up  to  be  easily  portable  to
          different processors & computer  platforms.  Code  generators  are
          available for 8080, 8051, 80x86, 8096,  6809,  68HC11  and  68HC16
          cpu's, and an entire section of the manual is devoted  to  porting
          the compiler.
    
          Although SMALL-C claims  to  be  easily  portable,  much  of  it's
          arcitecture is oriented toward the original 8080 processor. For an
          example of  how  this  affects  the  compiler,  compare  the  code
          generated by the 8086 version of SMALL-C to reference stack (auto)
          variables to that produced by MICRO-C.
    
        - It is a more complete implementation of the 'C' language, see  the
          features comparison later in this document.
    
        - It produces faster, more compact code. See the  benchmark  results
          later in this document.
    
        - MICRO-C employs  a  fully  tokenized  parser,  allowing  statement
          analysis to be performed  on  16  bit  "tokens"  instead  of  text
          strings as is  done  in  SMALL-C.  This  results  in  MUCH  faster
          compilation.
    
        - Although it is higher in functionality than SMALL-C,  the  MICRO-C
          compiler is much smaller than SMALL-C (Nearly half the size). This
          allows it to run on very small computer systems.
    
    2. DETAILED COMPARISON OF COMPILERS
    
          The following pages contain a detailed comparison of  the  SMALL-C
       version 2 compiler, and MICRO-C.

    MICRO-C .vs. SMALL-C                                             Page: 2


       2.1 'C' Implementation
            = Data Types ===========+ SMALL-C V1 + SMALL-C V2 + MICRO-C +
            int                     |    Yes     |    Yes     |   Yes   |
            char                    |    Yes     |    Yes     |   Yes   |
            unsigned int            |     No     |     No     |   Yes   |
            unsigned char           |     No     |     No     |   Yes   |
            pointers                |    Yes     |    Yes     |   Yes   |
            pointers to pointers    |     No     |     No     |   Yes   |
            structs & unions        |     No     |     No     |   Yes   |
            Single dimension arrays |    Yes     |    Yes     |   Yes   |
            Multi dimension arrays  |     No     |     No     |   Yes   |
            Arrays of pointers      |     No     |     No     |   Yes   |
            Arrays of structs       |     No     |     No     |   Yes   |
            Typecast                |     No     |     No     |   Yes   |
            sizeof                  |     No     |     No     |   Yes   |
            Static globals & locals |     No     |     No     |   Yes   |
            = Control Structures ===+ SMALL-C V1 + SMALL-C V2 + MICRO-C +
            if/else                 |    Yes     |    Yes     |   Yes   |
            while                   |    Yes     |    Yes     |   Yes   |
            do/while                |     No     |    Yes     |   Yes   |
            for                     |     No     |    Yes     |   Yes   |
            switch/case             |     No     |    Yes     |   Yes   |
            goto                    |     No     |    Yes     |   Yes   |
            Conditional Expressions |     No     |    Yes     |   Yes   |
            Inline assembler        |    Yes     |    Yes     |   Yes   |
            = Pre-Processor ========+ SMALL-C V1 + SMALL-C V2 + MICRO-C +
            #define (basic)         |    Yes     |    Yes     |   Yes   |
            #define (Parameterized) |     No     |     No     |   Yes   |
            #define (Multi-line)    |     No     |     No     |   Yes   |
            #undef                  |     No     |     No     |   Yes   |
            #include (single level) |    Yes     |    Yes     |   Yes   |
            #include (nested)       |     No     |    Yes     |   Yes   |
            #ifdef/#ifndef          |     No     |    Yes     |   Yes   |
            = Misc features ========+ SMALL-C V1 + SMALL-C V2 + MICRO-C +
            Optimization            |     No     |    Yes     |   Yes   |
            Multiple memory models  |     No     |     No     |   Yes   |
            Make/touch utility      |     No     |     No     |   Yes   |
            Source linker           |     No     |     No     |   Yes   |
            68HC08 code generator   |     No     |     No     |   Yes   |
            6809 code generator     |     No     |     No     |   Yes   |
            68HC11 code generator   |     No     |     No     |   Yes   |
            68HC16 code generator   |     No     |     No     |   Yes   |
            8080 code generator     |    Yes     |    Yes     |   Yes   |
            8051 code generator     |     No     |     No     |   Yes   |
            8086 code generator     |     No     |    Yes     |   Yes   |
            8096 code generator     |     No     |     No     |   Yes   |
            Complete standard lib   |     No     |    Yes     |   Yes   |
            Interrupt serial I/O    |     No     |     No     |   Yes   |
            Windowing library       |     No     |     No     |   Yes   |
            TSR support             |     No     |     No     |   Yes   |

    MICRO-C .vs. SMALL-C                                             Page: 3


       2.2 Generated code quality
    
             To test the actual performace  of  code  generated  by  MICRO-C
          against  code  generated  by  SMALL-C,  I  used  this  "Sieve   of
          Eratosthenes" prime number generator program, taken from the  BYTE
          benchmarks:
    
    
    
    
    
    /*
     * The classic "Sieve of Eratosthenes" prime number program.
     * from BYTE, January 1983.
     */
    #include <stdio.h>
    #include "timer.c"          /* The timer subroutines */
    
    #define SIZE  8190
    #define LOOP  100
    #define TRUE  1
    #define FALSE 0
    
    char flags [SIZE + 1];
    
    main()
    {
        int i, prime, k, count, iter;
    
        printf("BYTE Sieve Benchmark - %d iterations\n",LOOP);
    
    /* Start timer and execute loop */
        startimer(timestamp);
        for(iter = 1; iter <= LOOP; ++iter) {
            count = 0;                          /* prime counter */
            for(i = 0; i <= SIZE; ++i)          /* set all flags true */
                flags [i] = TRUE;
            for(i = 0; i <= SIZE; ++i) {
                if(flags [i]) {                 /* found a prime */
                    prime = i + i + 3;          /* twice index + 3 */
    /*              printf ("\n%d", prime);     */
                for(k = i + prime; k <= SIZE; k+= prime)
                    flags [k] = FALSE;          /* kill all multiple */
                ++count; } } }                  /* primes found */
        elapsed(timestamp);                     /* Calculate time taken */
    
    /* Report results */
        printf("%d primes.\n\n", count);        /* primes found on 100th pass */
        printf("Elapsed time: %02d:%02d:%02d.%02d\n",
            timestamp[1], timestamp[0], timestamp[3], timestamp[2]);
    }

    MICRO-C .vs. SMALL-C                                             Page: 4


       2.3 Speed of compilation
    
             To show the relative compilation times,  I  wrote  this  simple
          MICRO-C program, using the timing routines shown below, to execute
          the compilers & report the time taken:
    
    
    
    
    
    #include <stdio.h>
    #include "timer.c"          /* The timer subroutines */
    
    main()
    {
        startimer(timestamp);
        system("CC SIEVE");             /* Execute the SMALL-C compiler */
        elapsed(timestamp);
        printf("Elapsed time: %02d:%02d:%02d.%02d\n\n",
            timestamp[1], timestamp[0], timestamp[3], timestamp[2]);
    
        startimer(timestamp);
        system("MCC SIEVE.C SIEVE.ASM");/* Execute the MICRO-C compiler */
        elapsed(timestamp);
        printf("Elapsed time: %02d:%02d:%02d.%02d\n",
            timestamp[1], timestamp[0], timestamp[3], timestamp[2]);
    }
    
             NOTE: The results from the above program will include the  time
          taken to load the compilers. To minimize this, all tests were  run
          from a RAMdisk. This eliminates disk seek time, and  reduces  load
          time to the speed of a memory to memory copy.

    MICRO-C .vs. SMALL-C                                             Page: 5


       2.4 Timing the tests
    
             These subroutines were used to time  the  programs,  using  the
          MS-DOS internal clock which has a resolution of 1/100 of a second:
    
    
    
    
    
    char timestamp[4];          /* Stores initial timestamp */
    
    /*
     * Record system time for later calculation
     */
    startimer() asm
    {
            MOV     AH,2CH      ; Get time function
            INT     21H         ; Ask DOS
            MOV     SI,4[BP]    ; Get pointer to timestamp
            MOV     [SI],CX     ; Record hours & minites
            MOV     2[SI],DX    ; Record seconds & hundreds
    }
    
    /*
     * Calculate elapsed time since timestamp recorded
     */
    elapsed() asm
    {
            MOV     AH,2CH      ; Get time function
            INT     21H         ; Ask DOS
            MOV     SI,4[BP]    ; Pointer to timestamp
            SUB     DL,2[SI]    ; Convert 100ths
            JNC     ELAP1       ; No borrow
            ADD     DL,100      ; Re-adjust
            DEC     DH          ; Reduce seconds
    ELAP1:  MOV     2[SI],DL    ; Save elapsed hundreds
            SUB     DH,3[SI]    ; Convert seconds
            JNS     ELAP2       ; No borrow
            ADD     DH,60       ; Re-adjust
            DEC     CL          ; Reduce minites
    ELAP2:  MOV     3[SI],DH    ; Save elapsed seconds
            SUB     CL,[SI]     ; Convert minites
            JNS     ELAP3       ; No borrow
            ADD     CL,60       ; Re-adjust
            DEC     CH          ; Adjust hours
    ELAP3:  MOV     [SI],CL     ; Save elapsed minites
            SUB     CH,1[SI]    ; Convert hours
            MOV     1[SI],CH    ; Save elapsed hours
    }

    MICRO-C .vs. SMALL-C                                             Page: 6


       2.5 Test results
    
             After compiling the programs, I ran  the  various  tests  on  a
          standard 8-Mhz IBM PC/AT, with these results:
    
    E:\>dir
    
     Volume in drive E is VDISK  V3.3
     Directory of  E:\
    
    CC       EXE    40626   4-27-93  /* SMALL-C compiler */
    MCC      COM    24154   4-27-93  /* MICRO-C compiler */
    TIMER    C       1094   4-27-93  /* The timer subroutines */
    TIMECOMP C        527   4-27-93  /* The compiler timer */
    SIEVE    C       1149   4-27-93  /* The test program */
    SIEVE-S  EXE    16946   4-27-93  /* SMALL-C produced this */
    SIEVE-M  COM     1744   4-27-93  /* MICRO-C produced this */
    TIMECOMP COM     1908   4-27-93  /* Executable compiler timer */
            8 File(s)    430080 bytes free
    
    E:\>sieve-s     /* The SMALL-C version: 1 min, 28.98 secs */
    BYTE Sieve Benchmark - 100 iterations
    1899 primes.
    
    Elapsed time: 00:01:28.98
    
    E:\>sieve-m     /* The MICRO-C version: 0 min, 40.43 secs */
    BYTE Sieve Benchmark - 100 iterations
    1899 primes.
    
    Elapsed time: 00:00:40.43
    
    E:\>
    
    **NOTE: Before running TIMECOMP, I created a "generic" STDIO.H
            file which was suitable for both compilers.
    
    E:\>timecomp    /* Times to compile the program */
    Small-C Compiler, Version 2.1, (Rev. 75)
    Copyright 1982, 1983, 1985 J. E. Hendrix
    Elapsed time: 00:00:04.72       /* SMALL-C 4.72 secs */
    
    MICRO-C Compiler
    Copyright 1988-1993 Dave Dunfield
    All rights reserved.
    Elapsed time: 00:00:01.15       /* MICRO-C 1.15 secs */
    
    E:\>

    MICRO-C .vs. SMALL-C                                             Page: 7


    3. OTHER ADVANTAGES OF MICRO-C
    
          In addition to being a superiour and more portable  compiler,  The
       MICRO-C package also offers these advantages:
    
       3.1 Utilities
    
             MICRO-C Comes with the following utilities (all  with  complete
          MICRO-C source code):
    
        CC      - Command Coordinator, combines pre-processor, compiler,
                  optimizer, assembler and linker into a single command.
                  Command line parameters allow very flexible operation.
    
        MAKE    - Automates building of larger (multi module) programs.
    
        TOUCH   - Set timestamp of file to current or specified date.
                  (Used with MAKEs dependancy checking)
    
        SLINK   - Source LINKer, Allows pre-compiled (assembler) source to
                  be kept in a library and included as needed to resolve
                  external references. Useful when MICRO-C is used as cross
                  compiler for systems not supporting an object linker.
    
        SLIB    - Utility for updating and maintaining a source library.
    
        SINDEX  - Automatically indexes a source library for use by SLINK.
    
        SCONVERT- Converts assembly language source for use by SLINK.
    
        EXE2BIN - Converts MS-DOS EXE files to a binary image, useful for
                  users of later versions of DOS which no longer include
                  this utility.
    
        MCP     - The MICRO-C Pre-processor
    
        MCC     - The MICRO-C Compiler
    
        MCO     - The MICRO-C Optimizer

    MICRO-C .vs. SMALL-C                                             Page: 8


       3.2 Example Programs
    
    MICRO-C EXAMPLE PROGRAMS: (List revised 19-Apr-94)
    
    DOSUTIL: DOS utilities            CUTIL: 'C' utilities
    --------------------------------  -----------------------------------
    ANYFILE - Check for ANY file      CCREF   - cross referencing program
    BOOTMENU- BOOT controller         COMEXT  - Extract comments
    CALC    - TSR calculator          CVTCOM  - Convert '//' to '/* */'
    CAN     - Permanent args to .COM  OBSCURE - Make source un-readable
    CHAINSAW- Kill directory tree     PPC     - Pretty Printer for 'C'
    CHATTR  - Change file attribs     SHELL   - Cmd line/interactive shell
    CMOS    - Read/Write/Verify CMOS
    COMCHK  - Check COM file at load  MISC: Other misc. programs
    CSET    - TSR map of PC charset   -----------------------------------
    DIFF    - Show diffs in 2 files   ASM86   - 8086 assembler
    DUMP    - Hex/Oct/ASCII dump pgm  BASIC   - A BASIC interpreter
    EQUIP   - Show installed h/w      BIGNUM  - +-*/% very large numbers
    GREP    - Like unix "GREP"        BITARRAY- Example of array of bits
    HEM     - TSR trap unexpectd int  BJ      - Blackjack (21) game
    HEXED   - Hex file editor         BUZZ    - Jargon generator
    LZC     - TSR Control HP printer  BYTESWAP- Example of using UNION's
    MEMSAVE - Save mem image to file  CASTLE  - Large text adventure game
    MTERM   - TSR ANSI tty/XMODEM     DIS85   - 8085 Cross Disassembler
    OFF     - Screen saver            FIBO    - Compute fibonacci series
    PARK    - HD parking utility      FORTUNE - A "fortune cookie"
    PCD     - A "countdown" timer     HANOI   - Visual "towers of hanoi"
    RETAB   - Retabulate text files   HELLO   - Standard C demo program
    SCRUB   - Clean floppy drive      HFTEXT  - Text Huffman encoding
    SHOWEXE - Dump .EXE information   INVADER - Space invaders!
    SIZE    - Show #chars & #lines    KIDSMENU- mouse/kbd menu for kids
    STUFF   - Stuff keyboard buffer   KMEDIT  - Editor for kidsmenu
    TFB     - TSR File Browser        LONGCALC- "long" 32bit calculator
    TIMEIT  - Time DOS commands       MDCFS   - DOS compat. File System
    TR      - Like unix TR(anslate)   OBFUSC  - How NOT to write 'C'
    TYPE4   - TYPE/tabs at 4 spaces   PRIME   - Calculates prime numbers
    VALIDATE- ID files with 2 CRCs    PRIME1  - Another "" "" ""
                                      PTR2FUNC- Demo's ptrs to functions
    LAPTALK: Small/Powerful TTY pgm   RAIN    - Text 'falls' off screen
    -------------------------------   RDC     - File compression program
    LAPTALK - TTY with script lang.   RLTEXT  - Text run length encoding
    XMODEM  - Xmodem/1K/CRC etc.      ROBOFACE- Draws a "robot face"
                                      SELFDUP - Self-replicating pgm.
    MICROCAD: A VGA drawing program   SIMON   - Play "Simon-Says" game
    -------------------------------   TEXTNUM - Print numhers as words
    MICROCAD- Mouse/VGA drawing pgm   TTT3D   - 3 dimensional tic-tac-toe   
    MCPRINT - Print on LJET / EPSON   WINDEMO - Demo MICRO-C windowing
    MCDRAW  - Min. display routines
    FE      - Font Editor




                              MICRO-C .vs. SMALL-C

                               TABLE OF CONTENTS


                                                                         Page

     1. INTRODUCTION                                                        1


     2. DETAILED COMPARISON OF COMPILERS                                    1

        2.1 'C' Implementation                                              2
        2.2 Generated code quality                                          3
        2.3 Speed of compilation                                            4
        2.4 Timing the tests                                                5
        2.5 Test results                                                    6

     3. OTHER ADVANTAGES OF MICRO-C                                         7

        3.1 Utilities                                                       7
        3.2 Example Programs                                                8