T S X  --  L i t e


                                   Shareware

                   Multi-user/Multi-tasking Operating System


                           S&H Computer Systems, Inc.



      TSX-Lite is  a  full  32-bit,  multi-user,  multi-tasking  operating
      system  for  386  and  486  computer systems.  TSX-Lite supports two
      simultaneous users and  provides  multi-tasking  and  multi-sessions
      allowing  each user to control up to 10 interactive sessions as well
      as background batch jobs.

      TSX-Lite provides full support for modems and dial-in lines as  well
      as  providing  the TSXTERM terminal emulator program.  This makes it
      possible to call your computer and  remotely  execute  commands  and
      programs.

      TSX-Lite  uses  the  same  file structure as DOS, so you can install
      TSX-Lite  on  a  DOS  based   computer   without   reformatting   or
      partitioning  your disk.  And, you can run TSX-Lite part of the time
      and DOS at other times on the  same  computer.   TSX-Lite  does  not
      support disk compression such as Stacker or DoubleSpace.

      TSX-Lite  runs  most  DOS  16-bit  programs  and  also  provides  an
      advanced 32-bit program environment  with  integral  EMS,  XMS,  and
      DPMI  support.   This allows execution of modern 32-bit applications
      that need not be constrained  by  the  640kb  DOS  partition.   Full
      virtual  memory  support  is  provided  with demand paging, allowing
      execution of programs larger than the physical memory  installed  on
      the computer.

      TSX-Lite  is not a limited, 16-bit, multi-DOS add-on.  Rather, it is
      a  complete  32-bit  operating  system  that  runs  exclusively   in
      protected  mode  and  uses  the  full  potential  of  modern  32-bit
      processors.  TSX-Lite  has  the  power  of  DESQView,  PC  Anywhere,
      386MAX, Doorway, and Phar Lap combined.

      TSX-Lite  requires  a  386,  486, or Pentium computer system with at
      least 4Mb of memory and 10Mb  of  free  disk  space.   VGA  and  MDA
      display  adapters  are  supported  along  with  a  variety  of  disk
      adapters.

      TSX-Lite is a shareware version of  the  powerful  TSX-32  operating
      system  which  supports  over  100  simultaneous  users and provides
      TCP/IP networking, real-time control, and other features.

      As a shareware product, you are granted a no-cost, trial  period  of
      30 days during which you may evaluate TSX-Lite.






                               Table of Contents



      1. Introduction . . . . . . . . . . . . . . . . . . . . . . . . .  1
        1.1 What is TSX-Lite? . . . . . . . . . . . . . . . . . . . . .  2
          1.1.1 Execution Scheduling  . . . . . . . . . . . . . . . . .  3
          1.1.2 The TSX Kernel  . . . . . . . . . . . . . . . . . . . .  3
        1.2 Why Use TSX-Lite? . . . . . . . . . . . . . . . . . . . . .  4

      2. Getting Started  . . . . . . . . . . . . . . . . . . . . . . .  6
        2.1 Starting TSX  . . . . . . . . . . . . . . . . . . . . . . .  6
        2.2 Run Your Program  . . . . . . . . . . . . . . . . . . . . .  7
        2.3 Multi-tasking and the Session Manager . . . . . . . . . . .  7
        2.4 The TSGEN Program . . . . . . . . . . . . . . . . . . . . .  9
        2.5 Setting Up Multi-Tasking Applications . . . . . . . . . . . 10
          2.5.1 Setting up Wildcat for TSX-Lite . . . . . . . . . . . . 12
        2.6 Setting up COM Ports  . . . . . . . . . . . . . . . . . . . 13
          2.6.1 Hardware Connections  . . . . . . . . . . . . . . . . . 13
          2.6.2 Line Setup Options  . . . . . . . . . . . . . . . . . . 14
          2.6.3 Setting up Phone lines  . . . . . . . . . . . . . . . . 17
          2.6.4 Setting Up Password Protection  . . . . . . . . . . . . 18
          2.6.5 Monitoring Serial Lines . . . . . . . . . . . . . . . . 19
          2.6.6 Setting up COM3 and COM4  . . . . . . . . . . . . . . . 20
        2.7 Setting up Mouse Support  . . . . . . . . . . . . . . . . . 21
        2.8 Setting up CD ROM Support . . . . . . . . . . . . . . . . . 22
        2.9 Returning to DOS  . . . . . . . . . . . . . . . . . . . . . 22

      3. Terminal Operations  . . . . . . . . . . . . . . . . . . . . . 23
        3.1 Terminal Types  . . . . . . . . . . . . . . . . . . . . . . 23
        3.2 Terminal Input Editor . . . . . . . . . . . . . . . . . . . 24
        3.3 Control Characters  . . . . . . . . . . . . . . . . . . . . 24
        3.4 Screen Saver  . . . . . . . . . . . . . . . . . . . . . . . 26
        3.5 Communication Lines . . . . . . . . . . . . . . . . . . . . 26
        3.6 International Keyboard Support  . . . . . . . . . . . . . . 27

      4. Running DOS Programs . . . . . . . . . . . . . . . . . . . . . 29
        4.1 Installing and Tuning DOS Programs  . . . . . . . . . . . . 29
        4.2 Direct Write Programs . . . . . . . . . . . . . . . . . . . 30
        4.3 DOS Environment Variables . . . . . . . . . . . . . . . . . 31
        4.4 16-bit Program Device Names . . . . . . . . . . . . . . . . 31
        4.5 Support for COMMAND.COM and TSR Programs  . . . . . . . . . 32
        4.6 Controlling DOS Program Input Loops . . . . . . . . . . . . 32
        4.7 IDLETIME Attribute  . . . . . . . . . . . . . . . . . . . . 34
        4.8 Printer Flush Sysgen Parameters . . . . . . . . . . . . . . 35
        4.9 Virtual UART Support  . . . . . . . . . . . . . . . . . . . 35
          4.9.1 FOSSIL Driver . . . . . . . . . . . . . . . . . . . . . 36
        4.10 Expanded Memory Support (EMS)  . . . . . . . . . . . . . . 36
        4.11 Extended Memory Support (XMS)  . . . . . . . . . . . . . . 37
        4.12 DPMI Support . . . . . . . . . . . . . . . . . . . . . . . 38
        4.13 Phar Lap Native System Services  . . . . . . . . . . . . . 38


                                       i


      Contents                                                          ii



      5. The TSX Command Language . . . . . . . . . . . . . . . . . . . 39
        5.1 Command Qualifiers  . . . . . . . . . . . . . . . . . . . . 39
        5.2 Wildcard Specifications . . . . . . . . . . . . . . . . . . 40
        5.3 TSX Device Names  . . . . . . . . . . . . . . . . . . . . . 40
        5.4 Internal and External Commands  . . . . . . . . . . . . . . 41

      6. The System Menu  . . . . . . . . . . . . . . . . . . . . . . . 43

      7. Symbols and Logical Names  . . . . . . . . . . . . . . . . . . 44
        7.1 Defining Symbols with String Assignment Operators . . . . . 44
        7.2 Defining Symbols with Numeric Assignment Operators  . . . . 45
        7.3 ASSIGN Command and Logical Device Names . . . . . . . . . . 45

      8. Printing . . . . . . . . . . . . . . . . . . . . . . . . . . . 48
        8.1 Spooler and Queue Manager . . . . . . . . . . . . . . . . . 48
        8.2 Setting Up the Printer Queues . . . . . . . . . . . . . . . 49
        8.3 Printing from DOS Programs  . . . . . . . . . . . . . . . . 50
        8.4 Terminal Printers . . . . . . . . . . . . . . . . . . . . . 51
        8.5 Advanced Features . . . . . . . . . . . . . . . . . . . . . 52

      9. Command Procedures (Batch Files) . . . . . . . . . . . . . . . 53
        9.1 Introduction  . . . . . . . . . . . . . . . . . . . . . . . 53
        9.2 Invoking Command Procedures . . . . . . . . . . . . . . . . 53
        9.3 Background Batch Jobs . . . . . . . . . . . . . . . . . . . 54
        9.4 Branching: Labels and GOTO  . . . . . . . . . . . . . . . . 55
        9.5 Symbols and Operators . . . . . . . . . . . . . . . . . . . 56
        9.6 Conditionals: IF  . . . . . . . . . . . . . . . . . . . . . 56
        9.7 User Interaction: DISPLAY and INQUIRE . . . . . . . . . . . 56
        9.8 Seeing Commands . . . . . . . . . . . . . . . . . . . . . . 57
        9.9 Expression Operators  . . . . . . . . . . . . . . . . . . . 57
          9.9.1 Numeric Operators . . . . . . . . . . . . . . . . . . . 57
          9.9.2 String Operators  . . . . . . . . . . . . . . . . . . . 57
          9.9.3 Numeric Comparison  . . . . . . . . . . . . . . . . . . 57
          9.9.4 String Comparions . . . . . . . . . . . . . . . . . . . 57
          9.9.5 Logical Operators . . . . . . . . . . . . . . . . . . . 58
        9.10 Lexical Functions  . . . . . . . . . . . . . . . . . . . . 58

      10. Multiuser Computing . . . . . . . . . . . . . . . . . . . . . 63
        10.1 Workstations . . . . . . . . . . . . . . . . . . . . . . . 63
        10.2 Commands for the Multiuser Environment . . . . . . . . . . 64
          10.2.1 BATCH Command  . . . . . . . . . . . . . . . . . . . . 64
          10.2.2 SHOW Commands  . . . . . . . . . . . . . . . . . . . . 65
          10.2.3 STOP Command . . . . . . . . . . . . . . . . . . . . . 65
          10.2.4 SEND Command . . . . . . . . . . . . . . . . . . . . . 65
          10.2.5 PHONE Command  . . . . . . . . . . . . . . . . . . . . 66
          10.2.6 TUTOR Command  . . . . . . . . . . . . . . . . . . . . 66
        10.3 Virtual Memory . . . . . . . . . . . . . . . . . . . . . . 66
        10.4 Data Caching . . . . . . . . . . . . . . . . . . . . . . . 68
        10.5 Logon Access Control . . . . . . . . . . . . . . . . . . . 68
        10.6 Event Logs . . . . . . . . . . . . . . . . . . . . . . . . 69
        10.7 NetBIOS Support  . . . . . . . . . . . . . . . . . . . . . 69
        10.8 Mailboxes and Shared Memory Regions  . . . . . . . . . . . 70

      11. TSXTERM . . . . . . . . . . . . . . . . . . . . . . . . . . . 71


      Contents                                                         iii


        11.1 Installing TSXTERM . . . . . . . . . . . . . . . . . . . . 71
        11.2 Using TSXTERM  . . . . . . . . . . . . . . . . . . . . . . 71
        11.3 Control Screens  . . . . . . . . . . . . . . . . . . . . . 71
        11.4 Configuring TSXTERM  . . . . . . . . . . . . . . . . . . . 72
        11.5 Using Modem Connections  . . . . . . . . . . . . . . . . . 73
        11.6 Using Direct Connections . . . . . . . . . . . . . . . . . 73
        11.7 Printer Support  . . . . . . . . . . . . . . . . . . . . . 74
        11.8 Background File Transfer . . . . . . . . . . . . . . . . . 74
        11.9 Session Logging  . . . . . . . . . . . . . . . . . . . . . 74

      12. System Management . . . . . . . . . . . . . . . . . . . . . . 75
        12.1 Overview of System Startup . . . . . . . . . . . . . . . . 75
        12.2 Startup Command Files  . . . . . . . . . . . . . . . . . . 75
        12.3 System Customization . . . . . . . . . . . . . . . . . . . 76
          12.3.1 Line Startup Procedures  . . . . . . . . . . . . . . . 76
          12.3.2 User Authorization . . . . . . . . . . . . . . . . . . 77
          12.3.3 System Wide Settings . . . . . . . . . . . . . . . . . 77
        12.4 System Tuning  . . . . . . . . . . . . . . . . . . . . . . 78
          12.4.1 Introduction . . . . . . . . . . . . . . . . . . . . . 78
          12.4.2 CSHSIZE: Cache size  . . . . . . . . . . . . . . . . . 78
          12.4.3 VMAXJOBS: Job limit  . . . . . . . . . . . . . . . . . 78
          12.4.4 DOWINPRT: Window Print . . . . . . . . . . . . . . . . 79
          12.4.5 DOQUEUES: Queue Manager and Spooler  . . . . . . . . . 79
          12.4.6 MAXP0MEM: Maximum Memory Space . . . . . . . . . . . . 79
          12.4.7 PGFILSIZ: Page File Size . . . . . . . . . . . . . . . 79
          12.4.8 POOLSIZEN: System Pool Space . . . . . . . . . . . . . 79
          12.4.9 RAMDISKSIZ: Virtual Disk . . . . . . . . . . . . . . . 80

      13. Troubleshooting . . . . . . . . . . . . . . . . . . . . . . . 81
        13.1 RUNTSX Fails During TSX Start  . . . . . . . . . . . . . . 82
        13.2 Keyboard Is Dead . . . . . . . . . . . . . . . . . . . . . 82
        13.3 Serial Terminal Does Not Work  . . . . . . . . . . . . . . 82
        13.4 Screen is Corrupted after Session Switch . . . . . . . . . 83
        13.5 Mouse Does Not Work  . . . . . . . . . . . . . . . . . . . 83
        13.6 TSX Does Not Answer Incoming Calls . . . . . . . . . . . . 83
        13.7 Trash Characters During Logon and Screen Refresh . . . . . 83
        13.8 Lost Characters or Retries During File Transfers . . . . . 84
        13.9 Unable to Run TSR Programs . . . . . . . . . . . . . . . . 84
        13.10 Queue Manager and Spooler Are Gone  . . . . . . . . . . . 84
        13.11 Slow Performance -- Excessive Memory Paging . . . . . . . 85

      14. TSX Command Summary . . . . . . . . . . . . . . . . . . . . . 86
        14.1 ALLOCATE . . . . . . . . . . . . . . . . . . . . . . . . . 87
        14.2 ASSIGN . . . . . . . . . . . . . . . . . . . . . . . . . . 87
        14.3 ASSIGNMENT Expressions . . . . . . . . . . . . . . . . . . 87
        14.4 ASSIGNMENT for strings . . . . . . . . . . . . . . . . . . 88
        14.5 BACKUP . . . . . . . . . . . . . . . . . . . . . . . . . . 88
        14.6 BATCH  . . . . . . . . . . . . . . . . . . . . . . . . . . 92
        14.7 BOOT . . . . . . . . . . . . . . . . . . . . . . . . . . . 93
        14.8 BYE  . . . . . . . . . . . . . . . . . . . . . . . . . . . 93
        14.9 CALCULATE  . . . . . . . . . . . . . . . . . . . . . . . . 93
        14.10 CALENDAR  . . . . . . . . . . . . . . . . . . . . . . . . 94
        14.11 CALL  . . . . . . . . . . . . . . . . . . . . . . . . . . 94
        14.12 CHAIN . . . . . . . . . . . . . . . . . . . . . . . . . . 94
        14.13 CHDIR . . . . . . . . . . . . . . . . . . . . . . . . . . 95


      Contents                                                          iv


        14.14 CLS . . . . . . . . . . . . . . . . . . . . . . . . . . . 95
        14.15 COPY  . . . . . . . . . . . . . . . . . . . . . . . . . . 96
        14.16 COUNT . . . . . . . . . . . . . . . . . . . . . . . . . . 98
        14.17 DATE  . . . . . . . . . . . . . . . . . . . . . . . . . . 99
        14.18 DEALLOCATE  . . . . . . . . . . . . . . . . . . . . . . . 99
        14.19 DEASSIGN  . . . . . . . . . . . . . . . . . . . . . . . . 99
        14.20 DEFINE KEY  . . . . . . . . . . . . . . . . . . . . . .  100
        14.21 DELETE  . . . . . . . . . . . . . . . . . . . . . . . .  100
        14.22 DETACH  . . . . . . . . . . . . . . . . . . . . . . . .  101
        14.23 DIFFERENCES . . . . . . . . . . . . . . . . . . . . . .  103
        14.24 DIRECTORY . . . . . . . . . . . . . . . . . . . . . . .  105
        14.25 DISPLAY . . . . . . . . . . . . . . . . . . . . . . . .  107
        14.26 DOS . . . . . . . . . . . . . . . . . . . . . . . . . .  107
        14.27 DOWNLOAD  . . . . . . . . . . . . . . . . . . . . . . .  107
        14.28 DUMP  . . . . . . . . . . . . . . . . . . . . . . . . .  108
        14.29 EDIT  . . . . . . . . . . . . . . . . . . . . . . . . .  109
        14.30 EVALUATE  . . . . . . . . . . . . . . . . . . . . . . .  110
        14.31 EVENT . . . . . . . . . . . . . . . . . . . . . . . . .  110
        14.32 EXIT  . . . . . . . . . . . . . . . . . . . . . . . . .  110
        14.33 EXPAND  . . . . . . . . . . . . . . . . . . . . . . . .  111
        14.34 FILEWATCH . . . . . . . . . . . . . . . . . . . . . . .  113
        14.35 FMAN  . . . . . . . . . . . . . . . . . . . . . . . . .  114
        14.36 FORMAT  . . . . . . . . . . . . . . . . . . . . . . . .  117
        14.37 GOTO  . . . . . . . . . . . . . . . . . . . . . . . . .  117
        14.38 HANLOAD . . . . . . . . . . . . . . . . . . . . . . . .  117
        14.39 HELP  . . . . . . . . . . . . . . . . . . . . . . . . .  117
        14.40 HOST  . . . . . . . . . . . . . . . . . . . . . . . . .  118
        14.41 IF  . . . . . . . . . . . . . . . . . . . . . . . . . .  119
        14.42 INITIALIZE  . . . . . . . . . . . . . . . . . . . . . .  120
        14.43 INQUIRE . . . . . . . . . . . . . . . . . . . . . . . .  121
        14.44 JMAN  . . . . . . . . . . . . . . . . . . . . . . . . .  121
        14.45 KERMIT  . . . . . . . . . . . . . . . . . . . . . . . .  121
        14.46 KEYLOAD . . . . . . . . . . . . . . . . . . . . . . . .  122
        14.47 KILL  . . . . . . . . . . . . . . . . . . . . . . . . .  122
        14.48 LOGOFF  . . . . . . . . . . . . . . . . . . . . . . . .  122
        14.49 MACROS  . . . . . . . . . . . . . . . . . . . . . . . .  122
        14.50 MAIL  . . . . . . . . . . . . . . . . . . . . . . . . .  124
        14.51 MD  . . . . . . . . . . . . . . . . . . . . . . . . . .  124
        14.52 MESSAGE . . . . . . . . . . . . . . . . . . . . . . . .  125
        14.53 MKDIR . . . . . . . . . . . . . . . . . . . . . . . . .  125
        14.54 MN  . . . . . . . . . . . . . . . . . . . . . . . . . .  125
        14.55 OFF . . . . . . . . . . . . . . . . . . . . . . . . . .  125
        14.56 ON  . . . . . . . . . . . . . . . . . . . . . . . . . .  125
        14.57 PATH  . . . . . . . . . . . . . . . . . . . . . . . . .  126
        14.58 PAUSE . . . . . . . . . . . . . . . . . . . . . . . . .  127
        14.59 PHONE . . . . . . . . . . . . . . . . . . . . . . . . .  127
        14.60 PMAN  . . . . . . . . . . . . . . . . . . . . . . . . .  127
        14.61 PRINT . . . . . . . . . . . . . . . . . . . . . . . . .  128
        14.62 PROMPT  . . . . . . . . . . . . . . . . . . . . . . . .  130
        14.63 PROTECT . . . . . . . . . . . . . . . . . . . . . . . .  130
        14.64 QMAN  . . . . . . . . . . . . . . . . . . . . . . . . .  130
        14.65 R . . . . . . . . . . . . . . . . . . . . . . . . . . .  131
        14.66 RD  . . . . . . . . . . . . . . . . . . . . . . . . . .  131
        14.67 RECALL  . . . . . . . . . . . . . . . . . . . . . . . .  131
        14.68 RENAME  . . . . . . . . . . . . . . . . . . . . . . . .  132


      Contents                                                           v


        14.69 RESTORE . . . . . . . . . . . . . . . . . . . . . . . .  133
        14.70 RMDIR . . . . . . . . . . . . . . . . . . . . . . . . .  135
        14.71 RUN . . . . . . . . . . . . . . . . . . . . . . . . . .  135
        14.72 SEARCH  . . . . . . . . . . . . . . . . . . . . . . . .  136
        14.73 SEND  . . . . . . . . . . . . . . . . . . . . . . . . .  139
        14.74 SET CMDPROC . . . . . . . . . . . . . . . . . . . . . .  140
        14.75 SET DATE  . . . . . . . . . . . . . . . . . . . . . . .  141
        14.76 SET DEFAULT . . . . . . . . . . . . . . . . . . . . . .  141
        14.77 SET EDIT  . . . . . . . . . . . . . . . . . . . . . . .  141
        14.78 SET ENTRY . . . . . . . . . . . . . . . . . . . . . . .  142
        14.79 SET EVENT . . . . . . . . . . . . . . . . . . . . . . .  142
        14.80 SET HOST  . . . . . . . . . . . . . . . . . . . . . . .  142
        14.81 SET LOGOFF  . . . . . . . . . . . . . . . . . . . . . .  144
        14.82 SET LOG . . . . . . . . . . . . . . . . . . . . . . . .  144
        14.83 SET MESSAGE . . . . . . . . . . . . . . . . . . . . . .  145
        14.84 SET NEWSTATISTICS . . . . . . . . . . . . . . . . . . .  146
        14.85 SET PRINTWINDOW . . . . . . . . . . . . . . . . . . . .  146
        14.86 SET PROCESS . . . . . . . . . . . . . . . . . . . . . .  147
        14.87 SET . . . . . . . . . . . . . . . . . . . . . . . . . .  148
        14.88 SET SYSTEM  . . . . . . . . . . . . . . . . . . . . . .  148
        14.89 SET TERMINAL  . . . . . . . . . . . . . . . . . . . . .  149
        14.90 SET TIME  . . . . . . . . . . . . . . . . . . . . . . .  152
        14.91 SET VERIFY  . . . . . . . . . . . . . . . . . . . . . .  153
        14.92 SET VIDEO . . . . . . . . . . . . . . . . . . . . . . .  153
        14.93 SET WINDOW  . . . . . . . . . . . . . . . . . . . . . .  153
        14.94 SET WORKING_SET . . . . . . . . . . . . . . . . . . . .  154
        14.95 SHOW ALL  . . . . . . . . . . . . . . . . . . . . . . .  155
        14.96 SHOW ASSIGNS  . . . . . . . . . . . . . . . . . . . . .  155
        14.97 SHOW AUTHORS  . . . . . . . . . . . . . . . . . . . . .  155
        14.98 SHOW CACHE  . . . . . . . . . . . . . . . . . . . . . .  156
        14.99 SHOW COLORS . . . . . . . . . . . . . . . . . . . . . .  156
        14.100 SHOW DATE  . . . . . . . . . . . . . . . . . . . . . .  156
        14.101 SHOW DEVICES . . . . . . . . . . . . . . . . . . . . .  156
        14.102 SHOW ERRORS  . . . . . . . . . . . . . . . . . . . . .  156
        14.103 SHOW EVENTS  . . . . . . . . . . . . . . . . . . . . .  157
        14.104 SHOW FILES . . . . . . . . . . . . . . . . . . . . . .  157
        14.105 SHOW FSTATUS . . . . . . . . . . . . . . . . . . . . .  157
        14.106 SHOW JOBS  . . . . . . . . . . . . . . . . . . . . . .  158
        14.107 SHOW KEYS  . . . . . . . . . . . . . . . . . . . . . .  158
        14.108 SHOW MEMORY  . . . . . . . . . . . . . . . . . . . . .  158
        14.109 SHOW NAME  . . . . . . . . . . . . . . . . . . . . . .  158
        14.110 SHOW PAGING  . . . . . . . . . . . . . . . . . . . . .  158
        14.111 SHOW PRIVILEGES  . . . . . . . . . . . . . . . . . . .  158
        14.112 SHOW QUEUE . . . . . . . . . . . . . . . . . . . . . .  159
        14.113 SHOW SYMBOLS . . . . . . . . . . . . . . . . . . . . .  159
        14.114 SHOW SYSTEM  . . . . . . . . . . . . . . . . . . . . .  159
        14.115 SHOW TERMINALS . . . . . . . . . . . . . . . . . . . .  160
        14.116 SHOW TIME  . . . . . . . . . . . . . . . . . . . . . .  160
        14.117 SHOW UIC . . . . . . . . . . . . . . . . . . . . . . .  160
        14.118 SHOW USE . . . . . . . . . . . . . . . . . . . . . . .  160
        14.119 SHOW USERS . . . . . . . . . . . . . . . . . . . . . .  161
        14.120 SHOW VERSION . . . . . . . . . . . . . . . . . . . . .  161
        14.121 SHUTDOWN . . . . . . . . . . . . . . . . . . . . . . .  161
        14.122 SORT . . . . . . . . . . . . . . . . . . . . . . . . .  161
        14.123 SPY  . . . . . . . . . . . . . . . . . . . . . . . . .  162


      Contents                                                          vi


        14.124 STOP . . . . . . . . . . . . . . . . . . . . . . . . .  163
        14.125 SUBPROCESS . . . . . . . . . . . . . . . . . . . . . .  164
        14.126 SYSMON . . . . . . . . . . . . . . . . . . . . . . . .  165
        14.127 SYSTAT . . . . . . . . . . . . . . . . . . . . . . . .  165
        14.128 TIME . . . . . . . . . . . . . . . . . . . . . . . . .  165
        14.129 TMAN . . . . . . . . . . . . . . . . . . . . . . . . .  165
        14.130 TSAUTH . . . . . . . . . . . . . . . . . . . . . . . .  165
        14.131 TUTOR  . . . . . . . . . . . . . . . . . . . . . . . .  165
        14.132 TYPE . . . . . . . . . . . . . . . . . . . . . . . . .  166
        14.133 TSGEN  . . . . . . . . . . . . . . . . . . . . . . . .  167
        14.134 UNPROTECT  . . . . . . . . . . . . . . . . . . . . . .  167
        14.135 UPLOAD . . . . . . . . . . . . . . . . . . . . . . . .  168
        14.136 VERSION  . . . . . . . . . . . . . . . . . . . . . . .  168
        14.137 VIEW . . . . . . . . . . . . . . . . . . . . . . . . .  168
        14.138 WAIT . . . . . . . . . . . . . . . . . . . . . . . . .  169
        14.139 WHO  . . . . . . . . . . . . . . . . . . . . . . . . .  169
        14.140 WIN  . . . . . . . . . . . . . . . . . . . . . . . . .  169
        14.141 WSCMD  . . . . . . . . . . . . . . . . . . . . . . . .  170

      15. Use and Distribution of TSX-Lite  . . . . . . . . . . . . .  172
        15.1 Redistribution of TSX-Lite . . . . . . . . . . . . . . .  172
        15.2 Registering TSX-Lite . . . . . . . . . . . . . . . . . .  172
        15.3 Telephone Support  . . . . . . . . . . . . . . . . . . .  172
        15.4 Copyright notice . . . . . . . . . . . . . . . . . . . .  173
        15.5 Disclaimer . . . . . . . . . . . . . . . . . . . . . . .  173

      16. TSX-BBS . . . . . . . . . . . . . . . . . . . . . . . . . .  174
        16.1 A Multi-Line System  . . . . . . . . . . . . . . . . . .  174
        16.2 Super System Capacity  . . . . . . . . . . . . . . . . .  174
        16.3 Reliable, Non-stop Operation . . . . . . . . . . . . . .  175
        16.4 A Sysop's Dream  . . . . . . . . . . . . . . . . . . . .  175
        16.5 Door Program Support . . . . . . . . . . . . . . . . . .  176
        16.6 Flexibility is the Key . . . . . . . . . . . . . . . . .  176
        16.7 Use TPL to Extend Your System  . . . . . . . . . . . . .  177
        16.8 File Libraries . . . . . . . . . . . . . . . . . . . . .  178
        16.9 Newsgroups and Discussion Forums . . . . . . . . . . . .  179
        16.10 E-mail  . . . . . . . . . . . . . . . . . . . . . . . .  180
        16.11 Direct Internet Access  . . . . . . . . . . . . . . . .  180
        16.12 Incoming SLIP connections . . . . . . . . . . . . . . .  180
        16.13 On-line "Chat"  . . . . . . . . . . . . . . . . . . . .  181
        16.14 TSX-BBS System Security . . . . . . . . . . . . . . . .  181
        16.15 System Control  . . . . . . . . . . . . . . . . . . . .  181
        16.16 TSX-BBS Is a Complete System  . . . . . . . . . . . . .  182

      17. The Full TSX-32 System  . . . . . . . . . . . . . . . . . .  183
        17.1 Support for Large Systems  . . . . . . . . . . . . . . .  183
        17.2 Networking . . . . . . . . . . . . . . . . . . . . . . .  183
        17.3 Real-time Support  . . . . . . . . . . . . . . . . . . .  183
        17.4 Disk Shadowing . . . . . . . . . . . . . . . . . . . . .  183
        17.5 Tape Support . . . . . . . . . . . . . . . . . . . . . .  184
        17.6 MessageNet . . . . . . . . . . . . . . . . . . . . . . .  184
        17.7 Single-user Option . . . . . . . . . . . . . . . . . . .  184

      Index . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  185







                                   Chapter 1

                                  Introduction




      If  you  are  like  most  DOS  users  you probably suspect that your
      computer has a lot more power than you  are  currently  using.   You
      are  right.   But  to  tap  that  power  you  need  a  more powerful
      operating system than DOS; you need a system which was designed  for
      modern  386,  486,  and  Pentium  computers,  a  system  which fully
      utilizes the hardware potential such as  protected  execution  mode,
      virtual  memory,  and  32-bit  programs.   You  need  a  multi-user,
      multi-tasking system that allows more than one user  to  access  the
      computer  and allows you to execute multiple tasks at the same time.
      You need TSX.

      Although the primary purpose of TSX is not to emulate DOS, you  will
      find  that  most  DOS  commands  and  programs  work  with  TSX in a
      multi-user  environment.   And,  since  TSX  uses  the   same   file
      structure  as  DOS,  you  can install it on the same disk as DOS and
      run it part of the time and DOS at other times.   Files  created  by
      TSX  or  DOS  are  completely  compatible.   However,  TSX  does not
      support  software  disk  compression  schemes   like   Stacker   and
      DoubleSpace.

      This  manual  does  not  fully  document  TSX.   The  entire  TSX-32
      documentation set, including User's Manual, System Services,  System
      Management,  Networking,  etc.  is over 1,500 pages.  The philosophy
      of this manual is to introduce TSX-Lite and provide you with  enough
      information  to  use it productively.  See the REGISTER.DOC file for
      information about ordering TSX-32 manuals.

      In this document you will learn:

        . What TSX-Lite is;

        . Why it's better to run your software programs under TSX;

        . How to use features of your TSX-Lite system;

        . Benefits of registration and full TSX-32 systems.









                                       1


      Chapter 1. Introduction                                            2


      1.1 What is TSX-Lite?

      TSX is a multi-user, multi-tasking  operating  system.   This  means
      several  users can access the system at the same time, and each user
      can control several jobs.  TSX-Lite is  somewhat  like  DESQView  in
      that  you  can simultaneously run many programs or several copies of
      the same program such a bulletin board software.  But you will  find
      that TSX-Lite provides much more than just a multi-tasking system.

      We  use the terms job, task, and process interchangeably to describe
      one computing operation.  The term "session" describes  specifically
      a  job which is being controlled by a user sitting at a terminal (or
      the console) as opposed to a batch or detached job.

      With its dial-in support, TSX is little like a  multi-node  bulletin
      board  except  that with a full multi-user system like TSX each user
      can run any sets of commands and programs rather than being  limited
      to  a  specific  set of programs (or "doors") that are controlled by
      the bulletin board.  For example, one user can edit a document  with
      a  word  processor  while  another user runs a spreadsheet or uses a
      database program.

      A companion product to TSX is TSX-BBS -- a full multi-line  bulletin
      board  system.   See  Chapter  16  for  additional information about
      TSX-BBS.

      TSX-Lite can also be used as a "server" for multi-node BBS  systems.
      To  do this the BBS system would run on one computer and TSX-Lite on
      a different one.  The BBS computer would be linked to  the  TSX-Lite
      system  with one or more hardwired serial connections.  Users on the
      BBS who wanted to run programs  or  perform  other  functions  would
      cause  the  BBS  to connect their incoming line to one of the serial
      lines going to the TSX-Lite system.  The BBS  user  could  then  log
      onto  the  TSX-Lite  system  and  run "door" programs or any type of
      application.  This  is  somewhat  similar  to  using  the  "Doorway"
      product  but  TSX  allows  multiple  programs  to  run  on  the same
      machine.  See Section 4.9.1 on page 36  for  information  about  the
      FOSSIL driver that is built into TSX.

      With  a  full  TSX-32 system and the TSX-32 network applications kit
      it is even possible to use Telnet and FTP to access the Internet  or
      other systems through an arrangement of this type.

      Using  TSX-Lite  with  the TSXTERM terminal emulator program that is
      provided is a little like using PC Anywhere: you can call  in  using
      a  modem  and  execute commands and run programs.  And you will find
      that TSX's remote support is so good that you can  remotely  execute
      even complex programs like WordPerfect, FoxPro, and Lotus 1-2-3.

      TSX  coordinates  file  access  so  that multiple users can read and
      write the same or different files.  This makes  TSX  a  natural  and
      efficient  system for applications such as pharmacies, video stores,
      or other situations where multiple terminals are used  to  access  a
      common database.


      Chapter 1. Introduction                                            3


      A  multi-user  operating  system is a little like a computer network
      such as Novell or  Lantastic:  many  users  can  run  a  variety  of
      programs  at  the  same  time and they can access common data files.
      However, whereas a network requires each user  to  have  a  separate
      computer,  and  usually a dedicated file server, a multi-user system
      allows many users to run programs and access  common  files  on  the
      same  computer.   Each user will have an inexpensive serial terminal
      or a low-end computer with terminal emulation software, but all  the
      "computing" takes place on the central system.

      The  multi-user  approach  has  many  advantages.  First, it is less
      expensive since you do not have to buy a separate computer for  each
      user.   Second,  it  is  more  efficient since files can be accessed
      directly without  having  to  transfer  data  through  the  network.
      Third,  management  and  upkeep  of a single computer is much easier
      than a network.  Fourth, a multi-user system such  as  TSX  supports
      both hard-wired and dial-in users.

      The  full  TSX-32  system  is  actually  both  a  multi-user  and  a
      networking  operating  system.   The  basic  system  is   inherently
      multi-user  and  is  capable  of running dozens of users on a single
      computer.   The  networking  option  provides  TCP/IP   support   so
      multiple  TSX  systems can be linked together via Ethernet or serial
      connections.  With a network of TSX systems a user on  any  computer
      can  access  files  and  devices on any other computer; also, a user
      can log into another computer in the network  and  run  programs  or
      perform other operations on remote computers.

      1.1.1 Execution Scheduling

      The  multi-user,  multi-tasking  operation  is  achieved  through  a
      technique called  "time-sharing,"  in  which  the  operating  system
      allocates  the  CPU to the jobs as they have need for it, giving the
      illusion that each user has the  full  attention  of  the  computer.
      The   quality   of   the   execution  scheduling  algorithm  largely
      determines how  efficient  and  responsive  a  multi-user  operating
      system  is.   TSX  uses  a  patented "Adaptive Scheduling Algorithm"
      (trade mark) that does a very good  job  of  sharing  the  CPU  time
      among  the competing jobs and overlaps the I/O wait time for one job
      with  the  execution  of  others.    Until   recently,   multi-user,
      time-sharing  systems  such  as  TSX  were  available  only on large
      mainframe and mini-computer systems.

      1.1.2 The TSX Kernel

      The "brain" of the TSX operating system called the "kernel".  It  is
      located  in  the  file  TSX32.SYS  which  must be stored in the root
      directory.  When you type RUNTSX to start the TSX operating  system,
      the  kernel  is  loaded  into  memory  and  control of the system is
      transferred to it.  At this point, DOS and the BIOS  are  no  longer
      running.   All  functions that were previously controlled by DOS and
      the BIOS are now assumed by TSX.  But don't worry, DOS and the  BIOS
      are still there so you can reboot at any time and run DOS.


      Chapter 1. Introduction                                            4


      1.2 Why Use TSX-Lite?

      There are several reasons to choose TSX as your operating system:

        . TSX  is a multi-user system.  In addition to the primary user at
          the console, your TSX-Lite system allows a  second  user  to  be
          connected  through  the  COM1  or  COM2  port.   The full TSX-32
          system supports an unlimited  number  of  users.   Although  the
          practical  limit  is  set by the configuration of your computer,
          we have 386  and  486  systems  installed  supporting  over  100
          simultaneous  users.  TSX-Lite, the shareware version of TSX-32,
          supports a maximum of 2 users.

        . TSX provides multi-tasking and background batch jobs.   Using  a
          technique  called Process Windowing, each user can control up to
          10 tasks.   In  addition,  many  jobs  can  be  running  in  the
          background  as  batch  jobs (see Section 9.3).  This allows long
          running tasks to execute in the background  while  you  use  the
          computer  for  other  tasks.   You  can  also  execute  multiple
          "detached" jobs which can provide  server  functions  for  other
          jobs.  Detached jobs are not connected to any terminal.

        . TSX  supports  modems  and  dial-in  lines.  You can set up your
          TSX-Lite system so that you, or other users, can  call  in  from
          remote  locations  and run programs.  A terminal emulator called
          TSXTERM,  that  is  optimized  for  remote  access  to  TSX,  is
          provided  with  your  TSX-Lite  package.   See  Chapter  11  for
          additional  information  about  TSXTERM.   You  can   also   use
          programs  like  Procomm  to  call into TSX systems.  An optional
          TSX-Lite Security  Kit  is  available  with  programs  to  limit
          access  to  the system and control file access on a user-by-user
          basis.

        . TSX can run  arbitrarily  large  programs.   Using  a  technique
          called  virtual memory, the size of programs can actually exceed
          the amount of physical memory in the computer.

        . TSX runs a variety of programs.  The evolution of  the  computer
          industry   has  extended  programs  beyond  the  world  of  DOS.
          Programs requiring  DPMI  (a  technique  that  allows  DOS  type
          programs,  which  are  normally  16-bit, to run in 32-bit mode),
          Phar lap  (a  similar  technique),  as  well  as  native  32-bit
          software  can  all  be run simultaneously.  TSX has the combined
          power of 386MAX and Phar Lap.

        . TSX uses the "protected  mode"  of  386/486/Pentium  processors.
          This  protects  TSX  and  other programs from the misbehavior of
          one user's programs  and  greatly  reduces  the  occurrences  of
          system "hangs" or "crashes".

        . TSX  uses  the  same file structure as DOS.  This means that you
          can run TSX some of the time and DOS at other times on the  same
          disk  without having to reformat or partition it.  It also means
          that data can be exchanged easily between TSX based systems  and


      Chapter 1. Introduction                                            5


          DOS   systems.   TSX-Lite  does  not  support  disk  compression
          software such as Stacker or DOS version 6's DoubleSpace.

        . Data caching is an integral part  of  TSX.   This  cache  stores
          frequently  accessed data in memory and can greatly increase the
          speed of some I/O intensive programs.  On  large-memory  systems
          the  TSX  data  cache  can  be configured to store up to 12Mb of
          data.

        . TSX is a comprehensive system  that  includes  as  part  of  its
          basic  support  XMS,  EMS,  DPMI,  virtual memory, disk caching,
          multi-tasking, remote access, terminal  emulation,  and  NetBIOS
          (for  local  program-to-program  communication),  so  you do not
          have to buy and install additional products.

        . The TSX environment  includes  literally  hundreds  of  features
          designed  to  make  life  easier, not just for your software but
          for you.

        . There is an easy growth path from TSX-Lite to  the  full  TSX-32
          system  which  supports  dozens  of  users  and  provides TCP/IP
          networking and many other features.

        . S&H Computer Systems has an outstanding  support  team  that  is
          there  to  help  you.  Registered TSX-Lite users receive 90 days
          of support via mail, FAX, or CompuServe at no  additional  cost.
          Telephone  support  is  also available; see Section 15.3 on page
          172 for details.







                                   Chapter 2

                                Getting Started





      2.1 Starting TSX

      If you have not already done so, you should follow the  instructions
      in  the  INSTALL.DOC file to install TSX-Lite on your computer.  The
      installation process will create a  directory  named  \TSX32SYS\  on
      your  disk  and copy the TSX system files into it.  Furthermore, the
      file TSX32.SYS (literally the computer program  comprising  the  TSX
      operating system) has been placed in the root directory.

      The  program  RUNTSX  in  the \TSX32SYS\ directory is used to "boot"
      TSX from the DOS prompt.  This program  reads  the  TSX32.SYS  file,
      loads   it  into  memory,  places  your  386  or  486  processor  in
      "protected" (32-bit) mode, and jumps into TSX.  From this point  on,
      DOS (as well as the BIOS) are completely out of the picture.

      Should  you  reach  a  point  that you want your PC automatically to
      start TSX when it boots, you can use the STARTTSX program  which  is
      provided with the optional TSX-Lite Utilities Kit.

      Remember  that  when TSX is running, DOS is no longer in control (it
      is not even in memory).  While the TSX environment  is  designed  to
      make  DOS  users  feel  at home, it is not designed to be "just like
      DOS".  There are many  more  commands  available.   You  can  run  a
      greater  variety of programs than you can under DOS.  More memory is
      available, and you have multi-user and  multi-tasking  capabilities.
      However,  it  is  also  the  case  that  some commands work a little
      differently than they do under DOS.  It's also  true  that  not  all
      DOS  programs  will  run  under  TSX.   You  may  have  to  set up a
      technique for correctly  routing  printed  output  or  tame  certain
      programs   for  efficient  multi-user  operation.   See  Chapter  4,
      starting on page 29, for additional information installing,  tuning,
      and running DOS programs under TSX.

      When  you type RUNTSX to start TSX it will initiate a procedure that
      takes a few seconds to  load  TSX  into  memory  and  start  various
      "detached  jobs"  such as the print spooler and queue manager.  Once
      the initialization process finishes your console  should  display  a
      message  saying  that  TSX  is  available.  When you press Enter you
      will be "logged on" to the system.  An  optional  TSX-Lite  Security
      Kit  is  available  which includes a LOGON program to force users to
      enter a user name and password to gain access to  the  system.   See
      REGISTER.DOC for ordering and support information.


                                       6


      Chapter 2. Getting Started                                         7


      Decide  on  a  program  you  would like to run under TSX.  Since the
      chances are good that you will have to use the CD  command  to  move
      to  the  directory  where  the  program is, it's a good time to talk
      about how TSX handles disks and directories.

      Under TSX, you can issue familiar  commands  to  manage  directories
      like:

           C:
           CD \
           MD WP51
           CD \WP51
           CD ..

      Try  a  CD  command now to move to the directory where your favorite
      program resides.  If it's on a different disk, you can  combine  the
      device  and  directory  specifications  in a single CD command, such
      as:

           CD D:\WP51

      Another nice feature of the TSX CD  command  is  a  construct  which
      means "go back to where I was before":

           CD *


      2.2 Run Your Program

      Whatever  you  do  to  run  your  program  under  DOS,  do now.  TSX
      recognizes BAT files, EXE files, and COM files just like DOS.   Your
      program  should run just like it does under DOS.  If it does not let
      us make two suggestions at this point: (1) try another program,  and
      (2) see Chapter 13 that starts on page 81.


      2.3 Multi-tasking and the Session Manager

      Now  that  you  are executing your favorite application program, you
      may well be asking what the big deal about TSX is.  To  begin  with,
      let's  do  a  little  multi-tasking.  While your program is running,
      press the "Scroll Lock" key to invoke the TSX "Session Manager".   A
      menu  will  appear  in  the  upper  right  portion  of  your  screen
      displaying the  currently  active  sessions.   At  this  point  only
      session  number  0  will  be active.  Type the digit "1" (not on the
      keypad, but on the keyboard above the letter "Q") to  start  session
      1.   You will be greeted with a blank screen and a message that says
      something like "Subprocess 1, Job id=4".   What  you  have  done  is
      switched to a different Process Window.

      Process  windowing  is  the  TSX terminology for multi-tasking.  The
      term "process" (or "job", or "task") refers to a single  interactive
      session  controlled  from  a  terminal  which  is  running  a single
      program at any particular time.  There are also batch  and  detached
      processes,  which  are tasks that are not connected to a terminal at


      Chapter 2. Getting Started                                         8


      all.  Since TSX allows you to control more  than  one  process  from
      each  terminal,  each  process is associated with a single "window".
      Think of your monitor as being connected to a  single  window  at  a
      time,  looking  through  the window at the process you are currently
      controlling.

      Your primary window, number zero, is  still  running  your  program.
      In  window  1,  you  are  now  at  the  system  prompt.  To convince
      yourself that your original  program  is  still  running,  type  the
      following command:

           SHOW SYSTEM

      This  will display a list of jobs that are currently logged on.  You
      should see an entry for your current session (which will show  "(1)"
      after  the  terminal  name because this is your session 1), an entry
      for your original session, and entries for TSX system jobs  such  as
      the print spooler and queue manager.

      By   way  of  demonstrating  multi-tasking,  let's  talk  about  TSX
      commands for  a  minute,  taking  DIR  as  an  example.   Issue  the
      command:

           DIR

      You  will  see  a  listing  of  the  files  in  the directory with a
      familiar, but enhanced, format.  TSX has more commands than you  are
      used  to,  and the commands have many more features.  Take DIR as an
      example.  It's often nice to see  what  files  in  a  directory  are
      using up all the disk space.  Try the command:

           DIR/SORT=SIZE/REVERSE

      This  requests  a  listing  of files sorted by size in reverse order
      (listing the  biggest  ones  first).   So  just  what  commands  are
      available?  Try the command:

           HELP

      You  are  presented with a menu from which you can select DIRECTORY.
      This brings up a brief description of directory and tells  you  that
      you  can  press  the  F1  key  for a list of subtopics.  Try it: the
      pop-up menu shows a list of all the qualifiers (options)  legal  for
      the  directory  command.  Qualifiers are phrases used to qualify, or
      modify, the normal meaning of a command such as DIR.  You just  used
      two of them: /SORT and /REVERSE.

      Now  what  about the program you started in session 0?  Press Scroll
      Lock and the Session Manager will display  a  list  of  your  active
      sessions.   This  time  the  list will show that you have two active
      sessions: 0 and 1.  You could type a digit in the range 2 through  8
      to  start  another  session.   Type  "0" to select session 0 and the
      console  will  disconnect  from  session  1  and  reconnect  to  the
      original  session  that  is  running  the  application  you  started
      earlier.


      Chapter 2. Getting Started                                         9


      The  ability  to  flip  between  simultaneous  sessions  is   called
      multi-tasking.   You  can control up to 10 simultaneous tasks from a
      single terminal (the Session Manager runs as  session  number  9  so
      you  have  0  through  8 available for your own use).  Multi-tasking
      allows you to interrupt one task, work on another for a while,  then
      return  to  the first one right where you left off.  You can look up
      a fact, make a note to your self, or schedule an  appointment,  then
      resume  work  without  having  to  exit the software you were using.
      Multi-tasking also lets you  get  the  computing  going  on  a  long
      running  job, (say a query of a large database), then continue doing
      something else (such as word processing) while  the  computer  works
      on the first.

      In  addition  to  using  the  Session  Manager,  you can also switch
      between sessions by typing ALT-digit where 'digit'  is  the  session
      number  or  by typing Ctrl-W-digit (hold down Ctrl, press W, release
      Ctrl, press a digit to select the session).  However, these  methods
      do  not  work with some programs that take over keyboard interrupts.
      On serial terminals that do not have Scroll Lock or  ALT  keys,  you
      should type Ctrl-W-digit to select sessions.

      Now  that  you have gotten started with TSX-Lite you may want to try
      a few of the following commands to get a  feeling  for  the  system:
      "TSXSHELL"  (see  Chapter 6, starting on page 43), "HELP", "SYSMON",
      "FMAN", "SHOW SYSTEM", "SHOW USE", "SHOW TERMINALS", "SHOW  MEMORY",
      "SHOW  PAGING",  "SHOW  CACHE",  "SHOW FILES", "SHOW FSTATUS", "SHOW
      ERRORS".


      2.4 The TSGEN Program

      A program named TSGEN is used to  configure  TSX  for  a  particular
      hardware  configuration.   There  are two files that are manipulated
      by TSGEN: the TSX-Lite kernel, C:\TSX32.SYS, and  TSX32.GEN  in  the
      TSX  system  directory  (normally  TSX32SYS).  TSX32.GEN is an ASCII
      file that can be edited by any ASCII editor such  as  the  DOS  EDIT
      program.   TSGEN  has two modes of operation: batch and interactive.
      You start TSGEN in interactive mode by simply  typing  "TSGEN".   In
      this  mode the first screen will ask you for the name of your system
      generation parameter file.  Just press Enter  to  select  TSX32.GEN.
      Next  it  will  present  a menu with the following choices: (1) "Set
      Tuning Parameters"; (2) "Manage Equipment  List";  (3)  "Exit";  and
      (4)  "Reports".   You  can use the arrow keys to select one of these
      items and press Enter,  or  you  can  type  the  highlighted  letter
      within an item to select it.

      If  you  select "Set Tuning Parameters" you will be presented with a
      multi-screen menu listing each category of tuning  parameter  (there
      are  many).  The first entry "All parameters" can be selected to see
      an alphabetical list of all parameters.  TSGEN  has  extensive  help
      built  into  it  and  you can select a parameter and press F1 to get
      information about  what  the  parameter  does.   Be  cautious  about
      changing  parameters  that you do not fully understand.  See Section
      12.4 on page 78 for information about some  of  the  most  important
      tuning parameters.


      Chapter 2. Getting Started                                        10


      If  you  select "Manage Equipment List" you will be presented with a
      list of the devices installed in your computer  that  TSX  is  aware
      of.   Only  the device type and controller letter for each device is
      displayed.  The unit numbers for multi-unit  devices  are  shown  on
      menus  that  are selected by typing 'U'.  To modify parameters for a
      particular device unit (for  example  a  COM  port),  highlight  the
      desired  device  (TTA  is  the console, TTB is COM1 and TTC is COM2)
      and type 'U'.  A menu will appear showing each unit associated  with
      the  device  (most commonly there will be only one unit).  Highlight
      the desired unit and type 'U' again and you will be  presented  with
      the  first  page  of  a  multi-page  screen entry form that has each
      available parameter for the unit.  Move the cursor to any  item  and
      press F1 for help.

      Once  you  finish  making changes to tuning parameters and/or device
      unit information, type Esc repeatedly to exit from TSGEN.   When  it
      exits,  TSGEN  applies  the  changes  you  have made to the TSX-Lite
      kernel file (TSX32.SYS) and  updates  the  ASCII  system  generation
      commands  that are stored in TSX32.GEN.  The changes take effect the
      next time you reboot TSX.

      In the "batch" mode of operation, TSGEN reads the system  generation
      parameter   file  (normally  TSX32.GEN)  and  applies  the  commands
      specified into it to the kernel file (TSX32.SYS).   The  batch  mode
      would  be  used  if  you  edited  TSX32.GEN  using a separate editor
      rather than using TSGEN in interactive mode.  To run TSGEN in  batch
      mode  specify  the  name of the parameter file as the only argument.
      For  example,  the  following  command  applies  the   commands   in
      TSX32.GEN to the kernel:

           TSGEN TSX32

      There  are  three  versions  of  TSGEN  provided  with your TSX-Lite
      distribution: TSGEN.EXP, TSGEN.EXE, and MINIGEN.EXE.  The  TSGEN.EXP
      file  is  the  32-bit version of TSGEN that runs under TSX-Lite.  It
      is the full featured version of TSGEN and provides  both  batch  and
      interactive  modes.  The TSGEN.EXE and MINIGEN.EXE files can be used
      under DOS (when TSX is not running).  TSGEN.EXE provides  a  limited
      version  of  interactive  mode  with  only the ability to change the
      tuning  parameters  (you  cannot   manage   the   equipment   list).
      MINIGEN.EXE  operates  only  in  batch  mode.   It  can  be  used in
      situations where the DOS system does  not  have  enough  low  memory
      available  to  run  TSGEN.EXE.   It  is  best to use TSGEN.EXP while
      running  under  TSX-Lite  because  this  version  has  all  features
      available and can use as much memory space as necessary.


      2.5 Setting Up Multi-Tasking Applications

      As  you  have  just  learned,  TSX-Lite  allows you to have multiple
      programs running in separate sessions.  For  most  applications  you
      simply  can  type  Scroll  Lock  to  call up the session manager and
      switch between your sessions.  However, when a  16-bit  DOS  program
      is  executing  TSX  normally  suspends  the execution of the program
      when you switch away from it and select a  different  session.   The


      Chapter 2. Getting Started                                        11


      state  of  a  suspended  program  is  shown as "SPND" by the session
      manager and the SHOW JOBS command.  The reason that  these  programs
      are suspended is explained in Section 4.2.

      In  some  cases  it  is  important that programs continue to execute
      even when your terminal is not connected to their sessions.  A  good
      example  of this is a bulletin board system which is to run as a TSX
      session while you perform other operations  on  the  same  computer.
      Another  case  would  be  a  communications  program such as Procomm
      which you might wish to switch away from while it  is  performing  a
      large  file  transfer,  and  have  the  transfer  continue while you
      perform other  work.   Note:  the  TSX  HOST  command  described  in
      Section  14.40  on page 118 is much more efficent that communication
      programs like Procomm and  Telix.   TSX  fully  supports  concurrent
      execution  of multiple sessions but you must use the PMAN program to
      set certain attributes for the programs to cause this to happen.

      To enable concurrent execution of a program type PMAN to  start  the
      TSX  program  manager.   It  will  display  a  list of the currently
      "installed" programs (i.e., those for which special attributes  have
      already  been  set),  and  a  box  showing "Action Keys" that can be
      pressed to perform operations.  TSX-Lite comes configured with  some
      popular  DOS  programs  already  set  up in PMAN.  You should review
      this  list  of  programs  and  make  sure  the  disk  and  directory
      specifications   correspond   to   where   you  have  your  programs
      installed.

      Press "A" to add a new program entry.  You will  be  presented  with
      page  1  of  a 5 page information screen set.  Fortunately, you will
      need to only set a few of the values.  Press F1 at any time  to  get
      help about a particular PMAN item.

      Enter  the  full  program  specification  on  the  first line.  This
      should include the device name, directory, file name  and  extension
      (EXE  or  COM).   If there is a "starter" program that you initially
      run which loads some other program or overlay,  you  should  specify
      the  name  of  the starter program -- attributes are set up when TSX
      begins running a program and apply to any child program or overlay.

      After entering the program name, press Page Down to move to page  2.
      Press  down  arrow to move to the "HOLDPRIO" entry.  If you set this
      item to "Y" (yes) the program will execute at the same  priority  as
      the  session  that you are currently attached to.  This would be the
      appropriate setting for a program such as a bulletin board  that  is
      to  continue executing at full speed even when it is not the current
      session.  If you set the item to "N" (no) the program will  continue
      to  execute  when  it  is not running as the current session but its
      execution priority will be reduced to the  value  specified  by  the
      PRIVIR   sysgen   parameter.    This   would   be   appropriate  for
      "background"  tasks  such  as  compute  intensive  programs,  spread
      sheets,  etc.   You  can  use  TSGEN  to  change  the  PRIVIR sysgen
      parameter; its default value is 20 whereas the default  priority  of
      the  currently  active session is controlled by the PRIDEF parameter
      whose default value is 50.


      Chapter 2. Getting Started                                        12


      Now use down arrow to move to the item labeled "NODWRITE"  (be  sure
      you  select  the  "NODWRITE"  item  and not "DWRITE").  You must set
      NODWRITE to "Y" to enable continued execution when  the  program  is
      not  the current session.  This causes TSX to "virtualize" access to
      the video memory area so that the program is not directly  accessing
      the  hardware controller while it is running.  This option will work
      with programs that perform  character  type  displays  (most  spread
      sheets,  data  base  programs, etc.) but will NOT work with programs
      that do  graphic  displays  such  as  Windows,  games,  etc.   These
      graphical  programs  must have direct access to the video controller
      and must be suspended when they  are  not  running  in  the  current
      session.   If you prefer to have NODWRITE be the default setting for
      all programs, you can use TSGEN to set the  DEFDWRITE  parameter  to
      0.   You  can  then  use  PMAN  to  selectively  turn  on the DWRITE
      parameter for programs that are going to do graphical displays.

      A few more entries down is  an  item  labeled  "IDLETIME".   If  you
      provide  a  non-zero  value  this  is  the number of hundredths of a
      second of CPU time that a program may loop  without  performing  any
      other  operations  before TSX will consider it to be "idle" and give
      it a lower priority.  For example, if you specify a value  of  30000
      then  if  the  program  runs  for  300  seconds  (5 minutes) without
      performing any operations such as I/O or  communications,  TSX  will
      consider  it  to  be  "idle" and give it a lower execution priority.
      The priority will be increased and the timer reset  if  the  program
      performs any I/O operations (including accessing COM ports).

      If  you  have a program that is designed for multi-user operation in
      a network environment, you should go back to  page  1  and  set  the
      "DOSNET"  item to "Y".  This causes TSX to tell the program that all
      of its disks are remote network disks.  Some programs use this as  a
      signal to perform network record locking which TSX fully supports.

      After  you  set the appropriate options for the program press ESC to
      exit from the PMAN program  screens  back  to  the  initial  screen.
      Press  ESC  again  to  exit from PMAN.  Once you exit from PMAN, TSX
      will be aware of the attributes you have set  for  the  program  and
      they  will  take  effect  the  next time the program starts running.
      The attribute values are stored in a file called INSTALL.CMD in  the
      TSX  system  directory and are loaded automatically each time TSX is
      started.  You can use PMAN at any time  to  change  or  add  program
      attributes.   See  Section  4.6, starting on page 32, for additional
      information about installing and tuning DOS programs.

      2.5.1 Setting up Wildcat for TSX-Lite

      In order to run Wildcat  version  3x  under  TSX-Lite  follow  these
      steps:

      1.  Install  Wildcat  under  DOS  using  the  WINSTALL  and  WCMODEM
          programs  that  are  provided  with  Wildcat.   Using  MAKEWILD,
          select  the  "DOS Share" option for the Network type and set the
          COM UART FIFO trigger level to 14.


      Chapter 2. Getting Started                                        13


      2.  Start TSX-Lite and use the PMAN command to create an  entry  for
          WILDCAT.EXE.   Be  sure to provide the entire file specification
          including the device, directory  and  extension.   In  the  PMAN
          parameter  menus set the following items to 'Y' (yes): HOLDPRIO,
          NODWRITE, and TTWAIT.

      3.  To set up you serial port characteristics run TSGEN  and  select
          "Manage  equipment  list".   Highlight  the serial (TTx) line to
          which your modem is attached and press 'U' to  select  the  unit
          menu.   From the unit menu press the 'U' key again to modify the
          unit's settings.  In the qualifiers listing select  the  correct
          speed,  enable  the  phone  qualifier,  and  select  the correct
          handshaking required for your modem.  See Section 2.6.3 on  page
          17 for additional information about setting up phone lines.

      Because  of  the virtual UART emulation performed by TSX the maximum
      communications speed may be slower than it is under  DOS.   The  use
      of  actual  16550 type buffered controllers reduces the overhead and
      improves throughput.  See Section 4.9  on  page  35  for  additional
      information about UART emulation.


      2.6 Setting up COM Ports

      TSX-Lite  supports  access  to  the  system  from  both  the console
      terminal  and  serial  COM  ports.   TSX-Lite   is   restricted   to
      supporting  a  maximum  of two simultaneous users, but more than two
      COM ports  can  be  in  use  simultaneously  as  I/O  devices.   For
      example,  if you log onto the console and run Procomm which uses COM
      port 1 to access your modem,  another  user  could  log  on  through
      another  COM  port.   This is permissible because there are only two
      logged on users -- one at the console and one through  a  COM  port.
      Using  a  COM  port  as  an I/O device does not count as a logged on
      user so you could run a BBS  system  that  took  over  multiple  COM
      ports  as  I/O  devices  and  still  have  two  users  log  on.  The
      distinction is that a logged on user can type and  execute  TSX-Lite
      commands  whereas  I/O  device connections interact with application
      programs.  See Section 4.9 on page  35  for  additional  information
      about using the COM ports as I/O devices.

      Note:  it  is  highly  recommended that you obtain COM port adapters
      that use the 16550 buffering type  UART  chips.   The  16550  UART's
      provide  16  characters  of  buffering  in  the hardware and greatly
      reduce the risk of losing characters during file transfers.

      2.6.1 Hardware Connections

      You can connect to COM  ports  through  both  hard-wired  lines  and
      modems.   If  you  use  a  hard-wired line connection you must use a
      "null modem" device to reverse the transmit and receive  signals  in
      the  wire,  or  you  can  build your own cable with the transmit and
      receive data lines interchanged between the ends.  If you wire  your
      own cable you must connect the following pins on each end:


      Chapter 2. Getting Started                                        14


             -- 25 pin connector --     -- 9 pin connector --
               2  Transmit data           3  Transmit data
               3  Receive data            2  Receive data
               7  Signal ground           5  Signal ground

      If  you  use  a  modem you should connect it to the computer using a
      "straight through" connection that includes the lines for RTS,  CTS,
      DTR, DSR, Carrier detect, and Ring.

      2.6.2 Line Setup Options

      When  you  install  TSX-Lite  it checks for the presence of the COM1
      and COM2 serial ports.  If they  exist  it  defines  TSX  I/O  units
      named  TTB0 and TTC0.  TTB0 is the TSX name for COM1 and TTC0 is the
      TSX name for COM2.  Try using the  SHOW  TERMINALS  command  to  see
      that  these  device names exist.  See Section 5.3, beginning on page
      40, for additional information about TSX device names.

      These serial units may be used as I/O devices by  programs  such  as
      Procomm  without  any  further  changes.   However,  if  you want to
      accept incoming connections and calls  from  users  wishing  to  log
      onto  TSX-Lite  you  may  need  to use the TSGEN program to set some
      parameters for the lines (such as the PHONE attribute).

      By default, the serial lines are set up to  connect  to  hard-wired,
      ANSI  type  terminals  running at 9600 baud with XON (control-Q) and
      XOFF (control-S) flow control.  If you wish to connect  a  different
      type  of  terminal  (such  as  a VT-100 or PC-Term terminal), or you
      want to have a different baud rate, or  you  wish  to  have  dial-in
      modem  support, you need to use TSGEN to alter the line definitions.
      Note: terminal parameters can also be set  using  the  SET  TERMINAL
      command,  but you will have to repeat the commands (or put them in a
      start-up command file) if you want them to remain  in  effect  after
      TSX-Lite   is   restarted.   See  Section  14.89  on  page  149  for
      information about the SET TERMINAL  command.   See  Section  3.1  on
      page 23 for additional information about terminal types.

      To  permanently change a line parameter, start TSX-Lite and log onto
      the console terminal.  Then type "CD \TSX32SYS"  to  change  to  the
      system  directory  and  type  TSGEN  to  start  the  TSX-Lite system
      generation program.  Press Enter when TSGEN asks  for  the  name  of
      the  GEN  file  and  the  Main  Menu will be displayed.  Type 'M' to
      select Manage Equipment List.  Use the arrow keys to  highlight  the
      line  for  device  "TTB"  (COM1)  or  "TTC"  (COM2) and press 'U' to
      select the unit menu.  The unit  menu  should  show  a  single  unit
      numbered  0.   Type  'U'  again to set unit parameters.  You will be
      presented with the first of five screens of parameters that  can  be
      set  for  the  unit.   Use  the  arrow and Page Up/Down keys to move
      through the list.  You can select any item and press F1 to get  help
      information  for  that  item.  The following items are the ones that
      most frequently need to be changed:

      SPEED --  Press  Enter  and  a  list  of  available  baud  rates  is
          displayed.   Highlight  the  speed you desire and press Enter to
          select it.  If you are using a "smart" modem that  has  a  fixed


      Chapter 2. Getting Started                                        15


          rate  of communication to the computer, you should set that rate
          as the default speed.

      FIXEDSPEED -- Setting this option to 'Y'  causes  TSX  to  lock  the
          speed  of  the  line  to the speed set during system generation.
          If the option is set to 'N' then programs can  change  the  line
          speed.

      AUTOBAUD  --  If  you  are  using  a  hard-wired connection set this
          parameter to 'N'.  The SPEED parameter  will  control  the  baud
          rate.   If  a  modem  is connected to the line it is best to set
          the modem to communicate with the computer at a fixed  rate  and
          set  this  parameter  to  'N'.  However, if you have the type of
          modem that communicates with the computer at the  same  rate  as
          the  connection with the remote machine then you should set this
          parameter to 'Y'.

      HANDSHAKING -- Select  XONXON  if  XON  (control-Q,  DC1)  and  XOFF
          (control-S,  DC3) characters are used for software flow control.
          Select RTSCTS for the  popular  RTS/CTS  hardware  flow  control
          protocol.   If  you  are  using  a 14.4k or 28.8k modem you will
          almost certainly want to select RTSCTS handshaking.

      PARITY -- The standard setting for TSX is 8-bits, no parity.   Press
          Enter  and  you will be presented with a choice of even, odd, or
          no parity.

      PHONE -- Set this item to 'Y' if this line is connected to  a  modem
          and  you  wish  to support dial-in logons.  See Section 2.6.3 on
          page 17  for  additional  information  about  setting  up  phone
          lines.

      START  --  Set  this  item to 'Y' if you would like to have the line
          automatically log on each time TSX-Lite is started  rather  than
          waiting for Enter to be pressed.

      SYSPASSWORD  --  If you set this field to 'Y' users will be prompted
          with the string specified  by  the  SYSPASSPR  sysgen  parameter
          (default  is  '!')  and  they  must enter a password string that
          matches that specified by the SYSPASSWORD sysgen parameter.   An
          optional  TSX-Lite  Security  Kit  is available which includes a
          LOGON program to force users to enter a user name  and  password
          to  gain  access  to  the system.  See REGISTER.DOC for ordering
          information.  See  Section  2.6.4  on  page  18  for  additional
          information about setting up the system password.

      LOGON  --  If  this  unit is being used only as an I/O device (e.g.,
          serial mouse, modem for dial-out calls, etc.) set this field  to
          'N' to prevent users from logging onto the line.

      CMDFILE  --  You  may  specify  the device, directory, and name of a
          command file to be executed each time this line  logs  on.   The
          default start-up command file is \TSX32SYS\START.CMD.


      Chapter 2. Getting Started                                        16


      TERMTYPE  --  Press  Enter  and you will be presented with a list of
          terminal types.  Highlight the desired terminal type  and  press
          Enter  to  select it.  Here is a summary of some of the terminal
          types:

          ANSI -- Terminals or terminal emulator programs that handle  the
              basic  ANSI  control  sequences.  This is the best choice if
              the system is  being  accessed  using  a  terminal  emulator
              program  such  as  Procomm  or  Telix.   This is the default
              TSX-Lite terminal type.

          VT100 -- Digital Equipment Corporation  (DEC)  VT-100  terminal.
              Many   terminal  emulator  programs  provide  VT-100  as  an
              option.  If  you  select  this  terminal  type  and  "trash"
              characters  appear  on  the  screen  after  typing  the  CLS
              command or after a session window switch, you should  select
              ANSI terminal type.

          PCTERM  -- Serial PC-Term Terminals.  These are serial terminals
              that have IBM compatible keyboards and  transmit  make/break
              keyboard  codes like the console keyboard.  They can display
              25 lines and support the IBM display character set.

          TSXTERM -- Terminal Emulator.   The  TSXTERM  terminal  emulator
              program,  which  is  provided with TSX-Lite, can be run on a
              remote computer that is connected to  your  TSX-Lite  system
              via  either  a hardwired serial connection or a modem.  This
              is the best  type  of  TSX  workstation.   See  Chapter  11,
              starting  on  page  71,  for  additional  information  about
              TSXTERM.

          If you are configuring  a  line  for  dial-in  connections  from
          TSXTERM  stations,  it  is  best  to  set up the line as an ANSI
          terminal (use TSGEN  and  set  the  terminal  type  to  ANSI  or
          VT100).   Then  when  you  log into the TSX system using TSXTERM
          you will initially be in ANSI mode.  Once  the  logon  has  been
          established,  issue  the  following  TSX  command to switch into
          TSXTERM mode: "SET TERMINAL/TYPE=TSXTERM".   If  you  are  using
          the  LOGON  program  which is part of the TSX-Lite Security Kit,
          TSXTERM will shift into TSXTERM mode automatically  as  part  of
          the   logon  process.   If  you  are  setting  up  a  dedicated,
          hard-wired TSXTERM connection, choose  TSXTERM  as  the  default
          terminal  type.   See  Chapter 11, starting on page 71, for more
          information about installing and using TSXTERM.

      PRINTER -- Set this item to 'Y' if you have a printer  connected  to
          the auxiliary printer port that is available on some terminals.

      MRESET  --  You  may  specify a modem reset string to be sent to the
          line whenever a user logs off or a program releases  control  of
          the  line.   To  enter  control characters in the string specify
          the caret character ('^') in front of the letter.  For  example,
          "^M" means control-M which is carriage return.


      Chapter 2. Getting Started                                        17


      Press  ESC  to exit from the unit parameter screens after you change
      the desired settings.  Press ESC  three  more  times  to  exit  from
      TSGEN.   The  parameter settings are written to the TSX32.SYS kernel
      file and are recorded in the TSX32.GEN system  generation  parameter
      file.   You  must  reboot your computer and restart TSX-Lite to make
      them take effect.

      Once you have set up your COM lines you can use the  SHOW  TERMINALS
      command  to  display  summary  information  about all of your lines.
      For detailed information use the command "SHOW TTcuu" where  "TTcuu"
      is  a  terminal  device name such as TTA0 or TTB0.  The TMAN command
      can also be used to display terminal information.

      2.6.3 Setting up Phone lines

      The COM ports can be used for modems connected  to  phone  lines  as
      easily  as  they  can  be  used for terminals; to TSX, they are both
      simply time sharing lines.  We have been told that  this  equivalent
      treatment  of  phone  lines  and  hardwired  lines  makes  TSX modem
      support the best in the industry.  Specify the PHONE  attribute  for
      a  serial  unit  when you generate the TSX system (see Section 2.6.2
      on page 14) or issue a command like

           SET TTB0:/PERM/PHONE

      This tells TSX that a modem is connected  to  the  port.   TSX  will
      ignore  input  on  a  phone  line unless carrier is asserted.  Also,
      when a job logs off of a phone line TSX will drop DTR for  a  period
      of  time  to force the modem to hang up the phone.  See Section 2.6,
      starting on page 13, for additional  information  about  setting  up
      COM ports.

      For  proper  support,  a modem must be connected to TSX with a cable
      that has modem control signals such as  Carrier  Detect,  Ring,  and
      DTR  wired  through.   Also, the modem must be set up to only assert
      Carrier Detect when a connection is in effect, and it should be  set
      up so that it hangs up when DTR is dropped.

      Most  modern  modems  allow you to select a fixed communication rate
      between the modem and the computer so that the modem  converts  from
      the  actual baud rate used by the remote computer.  If possible, you
      should select this mode of operation for use with TSX.  However,  if
      you  have  a  modem that switches its baud rate to match that of the
      communications  connection,  then  you  should  set   the   AUTOBAUD
      parameter for the line to 'Y'.

      Most  modems come initially configured to not answer incoming calls.
      To enable Hayes compatible modems to answer incoming calls you  need
      to  set  the  modem "S0" register to a value other than 0 (the value
      you specify is the ring  number  to  answer  on  --  0  means  never
      answer).   To  set  this  "S0"  register  value  you  should  use  a
      communications program such as Procomm (or the TSX HOST command)  to
      talk  to  the modem.  You can then issue the following modem command
      to set S0 to 1:  "ATS0=1".   However,  this  type  of  setting  only
      remains  in  effect  until  the  modem  is powered off.  To make the


      Chapter 2. Getting Started                                        18


      setting permanent, issue the following  command:  "ATS0=1&W".   This
      stores the value in the non-volatile RAM memory in the modem.

      If  you  are  having  problems  getting  a  phone  line working, see
      Section 2.6.5 for debugging tips.

      2.6.4 Setting Up Password Protection

      If you set up a dial-in, phone line for access to  your  TSX  system
      you  must  immediately consider the issue of system security.  Since
      a dial-in user can potentially run any program, or access any  file,
      limiting  access to authorized users is vitally important.  TSX-Lite
      comes with a simple "system password"  facility  that  will  provide
      basic  access  protection.   A more sophisticated security system is
      available as part of the TSX-Lite Security Kit.

      The basic system password facility is a standard part  of  TSX-Lite.
      Using  it you can define a password of up to 31 characters in length
      that a user must enter to gain access to the system.  There are  two
      steps  to  setting  up  a system password: (1) defining the password
      itself, and (2) specifying  which  lines  are  to  require  password
      entry to access the system.

      To define the system password follow these steps:

      1.  Start   TSX-Lite,   switch  to  the  system  directory  (usually
          \TSX32SYS), and run the TSGEN program.

      2.  Press Enter or type in the name of your 'gen' file  in  response
          to the TSGEN prompt.

      3.  Select "Set Tuning Parameters".

      4.  Select "All parameters" (the first item on the list).

      5.  Type  'S'  to  position to the first parameter whose name begins
          with S.  Then use Page down and the arrow keys  to  position  to
          the SYSPASSWORD item and press Enter to select it.

      6.  Enter the string that you wish to use as your system password.

      7.  Press Esc 4 times to exit from TSGEN.

      By  default,  TSX prompts for the system password by displaying only
      an exclamation point.  This is done to avoid  revealing  information
      about  the  nature  of  the  system  before the user has entered the
      password.  If you would  like  to  have  a  more  friendly  greeting
      message,  use  TSGEN  to  set  the  value  of  the  SYSPASSPR sysgen
      parameter to whatever greeting string you choose; it may  be  up  to
      31 characters long.

      You  must also tell TSX which lines are to require entry of a system
      password for access.  Typically,  password  protection  is  set  for
      dial-in  lines but not the console or hard-wired terminal lines.  To
      require system password entry, follow the steps in Section 2.6.2  on


      Chapter 2. Getting Started                                        19


      page  14  and set the SYSPASSWORD parameter for each dial-up line to
      'Y'.  Remember to reboot TSX-Lite  after  making  these  changes  to
      have  them  take effect.  Also, be sure to test that the password is
      working correctly.

      The system password facility provides  basic  system  security.   If
      you  plan  to  have  multiple users accessing your system, or even a
      single user to whom you do not wish to give  unlimited  access,  you
      need  the  TSX-Lite  Security  Kit.  The Security Kit provides three
      utility programs: TSAUTH, LOGON, and FPROTECT.  TSAUTH is a  program
      you,  the  system  manager,  use to authorize users for access.  You
      assign a  user  name,  password,  account  number,  privileges,  and
      define  a  start-up  command  file to be executed when the user logs
      on.  You can set up many user names, each  with  a  unique  password
      and  set  of  privileges.   The  LOGON  program can be set to run on
      specific lines.  It prompts the user for a user name  and  password,
      checks  the  authorization  file, and, if the user is authorized for
      access, sets up the appropriate privileges and other attributes  for
      the  user.  The FPROTECT program is used in conjunction with FMAN to
      set up file access controls.  For each user you  can  control  which
      files  may  be  accessed.   Users  can  be  granted  write, read, or
      execute-only   access    to    files    on    a    device-by-device,
      directory-by-directory, or file-by-file basis.

      2.6.5 Monitoring Serial Lines

      If  you  have  problems getting a COM line working try the TSX "SPY"
      command.  The Spy facility is like a  "data  scope"  that  lets  you
      monitor  characters  sent to or received from a communications port.
      It will also display modem status line changes.   To  use  SPY,  log
      onto  the  console  terminal (or any other terminal than the one you
      wish  to  monitor)  and  then  issue  the  SPY  command   to   begin
      monitoring.   Type any character to terminate the SPY operation when
      you are finished.  For example, the following command line  monitors
      both  input  and  output  to  serial line TTB0 which is normally the
      COM1 port.

           SPY/INPUT/OUTPUT/HEX/BINARY/PHONE TTB0:

      If you don't see any characters coming in, check your modem and  the
      cable  from  the modem to the COM port (or the null modem cable from
      a hardwired serial terminal).  If you see  "trash"  characters  such
      as  "FF"  and  "00" coming in, check the baud rate setting specified
      when you generated the line (the current speed setting is  displayed
      when  you start SPY).  If the modem is not answering incoming calls,
      see Section 2.6.3 on page  17  for  information  about  setting  the
      modem  "S0"  register.   If  TSX  is not hanging up the phone when a
      user logs off you probably have not used  TSGEN  to  set  the  PHONE
      attribute  for the line or the modem is asserting the Carrier Detect
      signal even when carrier is not present.  Also, check to  make  sure
      that  the  modem is set up properly so that it will hang up when DTR
      is dropped.

      See Section 14.123 on page 162 for additional information about  the
      SPY command.


      Chapter 2. Getting Started                                        20


      Another  way  to  check  for  serial  line  errors  is to type "SHOW
      ERRORS" and see if there are any errors in  the  SERIAL  error  log.
      If so, type "EVENT SERIAL" to display the error records.

      2.6.6 Setting up COM3 and COM4

      The  installation of TSX-Lite will detect automatically the presence
      of the COM1 and  COM2  ports  and  define  them  as  valid  TSX  I/O
      devices.   If  you  have  COM3  and  COM4  ports  installed  in your
      computer you must use the TSGEN  program  to  inform  TSX  of  their
      presence.

      To  do this, start TSX and use the CD command to select the TSX32SYS
      directory as your current working area.  Then type  TSGEN  to  start
      the  TSX system generation program.  Press Enter to accept TSX32.GEN
      as the default system generation file.  From the main menu type  'M'
      to  select  Manage  Equipment  List.  From the Device List menu type
      'A' to add a device.  From the next  menu  use  the  arrow  keys  to
      select  the  "Serial  multiplexors" entry and press Enter.  The next
      menu shows the complete list of serial multiplexors  that  the  full
      TSX-32  system supports.  Since TSX-Lite is restricted to supporting
      only COM ports, you should use  the  arrow  keys  to  highlight  the
      "Dumb  serial  board"  entry.  Press Enter and you will be presented
      with a data entry screen titled "New  device  attributes."  You  can
      press F1 to get help for each field of the form.

      Press  Enter  while  positioned to the "CONTROLLER" field and a list
      of valid controller letters is displayed.  Select 'D'  for  COM3  or
      'E'  for  COM4  ('A'  is used for the console, 'B' for COM1, and 'C'
      for COM2).  Next, use the arrow keys to skip over  the  "TYPE"  file
      and  move  down to the "IO_ADDRESS" field.  The standard address for
      COM3 is 3E8 and the address for COM4  is  2E8.   Some  communication
      adapters   use   different  addresses  so  you  should  consult  the
      documentation that came with your board.   Next  move  down  to  the
      "INTERRUPT"  field.  The standard interrupt IRQ number for COM3 is 4
      and the standard for COM4 is 3; however, interrupt  4  is  also  the
      standard  for  COM1  and  3  is the standard for COM2.  TSX does not
      permit two devices to have the same interrupt numbers  so  you  must
      set  jumpers  or  DIP  switches  on  your  adapter  card  to  select
      different interrupt numbers for COM3 and COM4.  Interrupt values  5,
      7,  10  and  11  are  reasonable  choices  for additional COM ports.
      Consult the  documentation  for  your  adapter  card  for  what  the
      possible  interrupt  IRQ  values  are.   Once  you enter the correct
      interrupt number, press ESC to exit from the "New device  attributes
      field"  (you  do  not need to set values for the other fields on the
      screen).

      TSGEN will display the message "Type Y if you want  to  fill  in  an
      example  unit." Type 'N' for no.  You will now see an updated "TSGEN
      Device List" display.  Use the arrow keys and highlight  your  newly
      created  device  (TTD or TTE) and type 'U' to select the "Unit list"
      option.  You will see the "Unit list for device TTx"  screen.   Type
      'U'  again  to modify unit settings.  You will now be presented with
      a screen labeled "Device TTx unit 1".  From this  point  follow  the


      Chapter 2. Getting Started                                        21


      instructions  in  Section  2.6.2 for setting line parameters such as
      baud rate, etc.


      2.7 Setting up Mouse Support

      TSX supports the Microsoft serial mouse (or other  compatible  mice)
      attached to a COM port.  It does not support bus mouse controllers.

      To  use  the  mouse,  connect  it  to  a  COM port and use an ASSIGN
      command of the following form to  associate  the  MOUSEPORT  logical
      device name with the appropriate serial port:

           ASSIGN TTcuu: MOUSEPORT

      Where  "TTcuu" should be replaced by the appropriate TSX serial unit
      name such as TTB0 (COM1), TTC0 (COM2), TTD0 (COM3), or TTE0  (COM4).
      Note that the device name MUST end with a colon.

      If  you  wish  to  have the ASSIGN command executed each time TSX is
      started,  place  the  following   command   in   your   LSTARTUP.CMD
      system-wide startup command file:

           ASSIGN/SYSTEM TTcuu: MOUSEPORT

      In  addition  to  doing  the  ASSIGN  statement, you should also use
      TSGEN to specify the appropriate parameters for the serial COM  port
      to  which  the  mouse  is  connected.   Follow  the  instructions in
      Section  2.6.2  and  set  the  SPEED  to  1200  baud  for  Microsoft
      compatible  mice  or  2400  baud  for 2-button Logitec mice; set the
      LOGON parameter to 'N' (no) to prevent random input from  the  mouse
      from causing TSX to try to initiate a job.

      If  you  are  using  a  Logitech  brand  mouse,  you  must place the
      following  command  in   your   \TSX32SYS\LSTARTUP.CMD   system-wide
      start-up command file:

           MOUSETYPE:===LOGITECH

      If  this  command  is  not  present,  TSX-32 assumes you are using a
      Microsoft compatible mouse.

      See Section 14.140 on page 169 for information about setting up  the
      mouse for Microsoft Windows.

      If  you  have  problems  getting  the mouse to work, use the command
      "SHOW ERRORS" and see if there are any errors in  the  MOUERR  error
      log.   If so, type "EVENT MOUERR" to display the error records.  You
      can also use the SPY command to monitor input  from  the  mouse  COM
      port  to confirm that data is being received.  See Section 14.123 on
      page 162 for additional information about the SPY command.


      Chapter 2. Getting Started                                        22


      2.8 Setting up CD ROM Support

      TSX-Lite supports CD ROM drives connected to SCSI disk  controllers.
      Both  the  ISO  and  High Sierra CD ROM formats are supported.  When
      TSX is initially installed it senses automatically the  presence  of
      fixed  disk and diskette drives.  It does not detect the presence of
      CD ROM drives, so you must use TSGEN to declare their presence.

      If you have a CD ROM drive with a SCSI controller that you  want  to
      be  accessible  to TSX, perform the following steps.  Start TSX-Lite
      and type "CD \TSX32SYS" to  change  to  the  TSX  system  directory.
      Type  TSGEN  to  start the TSGEN system generation program and press
      Enter to select TSX32.GEN as your gen  file.   From  the  Main  Menu
      type  'M'  to  select  Manage Equipment List.  At this point look at
      the entries that already exist for disk drives -- all  of  the  disk
      names  will  begin  with  the letters "DH".  The third letter of the
      name specifies the logical controller; it is typically 'A', 'B',  or
      'C'.   Note  the  highest  controller letter currently in use.  Type
      'A' to add a new device.  Select "Disk drives" from the device  type
      list.   Select  "SCSI  CDROM"  from  the  next  menu and you will be
      presented with  a  data  entry  screen  for  the  device.   Enter  a
      controller  letter that is beyond the highest one that you noted was
      in use from the earlier device list.  Enter the  SCSI  ID  to  which
      the  drive  is  configured  and  enter "HAA" for the HOST_ADAP item.
      Press ESC to exit from the device  definition.   Next  you  will  be
      presented  with  a  screen  for  entering unit parameters.  You must
      enter a single letter for DOSDRIVE which  corresponds  to  the  disk
      letter  that you will use to refer to the device.  Typically letters
      'A' and 'B' are reserved for diskettes, 'C' is used  for  the  first
      hard  disk,  etc.   Choose  some  letter that does not conflict with
      with another disk.  Press ESC repeatedly until you exit from  TSGEN.
      You must reboot to have the drive definition take effect.


      2.9 Returning to DOS

      One  of the nice things about TSX-Lite is that you easily can switch
      between it and DOS.  The  preferred  way  to  stop  TSX-Lite  is  to
      execute  the  SHUTDOWN  command  procedure  that is in your TSX32SYS
      directory.  To  execute  it  simply  type  SHUTDOWN.   The  SHUTDOWN
      procedure  stops  all  jobs  and  performs an orderly shutdown; this
      normally takes about 30 seconds to complete.  When  it  finishes  it
      displays  the message "System ready for shutdown.  You may type BOOT
      to reboot." At this point you can type the BOOT  command  or  simply
      press  the  Reset  button  to reboot DOS.  If you don't want to wait
      for the SHUTDOWN procedure to  run,  simply  exit  from  application
      programs and type BOOT or press the Reset button.







                                   Chapter 3

                              Terminal Operations





      3.1 Terminal Types

      TSX-Lite   supports   several   types   of   terminals,  giving  you
      considerable flexibility  in  configuring  systems.   The  following
      list summarizes the different terminal types.

      Console  terminal -- The console terminal is the display device that
          is directly connected to your computer  through  a  MDA  or  VGA
          display  adapter.   TSX-Lite  supports  only  a  single  console
          station.  The full  TSX-32  system  supports  multiple  consoles
          connected through console multiplexer adapters.

      Serial  ANSI  Terminals  -- These terminals transmit and receive the
          ANSI standard characters and  control  sequences.   Examples  of
          ANSI  terminals  are  the  Digital Equipment Corporation VT-100,
          VT-200, and VT-300 series terminals.   These  terminals  usually
          do  not have an IBM compatible keyboard (they do not have all of
          the function keys) and they can usually only  display  24  lines
          of text.

          The  "ANSI" TSX terminal type is a subset of VT-100.  DEC VT-100
          terminals have attributes such as scrolling regions and  graphic
          character  sets  that  are not implemented by most ANSI terminal
          emulators.  You should use the ANSI terminal type  when  running
          with  ANSI  terminals  or  emulator programs that do not provide
          the full VT-100 control sequence emulation.

          TSX provides some keyboard mapping to make it  possible  to  run
          DOS  programs from these terminals.  To type DOS function key on
          a DEC VT type terminal  press  F20  followed  by  a  digit  (for
          example,  F20 followed by 2 generates the IBM code for F2).  For
          shifted, control, and ALT functions, type  F17  for  shift,  F18
          for  control,  or  F19  for  ALT,  followed  by  F20-digit.  For
          example, to generate ALT F3, press F19, F20, and then 3  on  the
          typewriter  portion  of  the  keyboard.   Press  the "Do" key to
          generate an ESC.

          If you run a program that has a 25 line display  only  24  lines
          will  be  displayed  at  a  time.   Type  control-V to shift the
          screen so that the additional line can be seen.




                                       23


      Chapter 3. Terminal Operations                                    24


      Serial PC-Term Terminals -- These are  serial  terminals  that  have
          IBM  compatible keyboards and transmit make/break keyboard codes
          like the console  keyboard.   They  can  display  25  lines  and
          support  the  IBM  display  character  set.  These terminals are
          much better  suited  for  running  DOS  applications  than  ANSI
          terminals.   Examples  of PC-Term terminals are Relisys and Wyse
          WY-150.  If you have one  of  these  terminals  you  should  use
          TSGEN and set the TERMTYPE for the line to PCTERM or RELISYS.

      TSXTERM  Terminal Emulator -- The TSXTERM terminal emulator program,
          which is  provided  with  TSX-Lite,  can  be  run  on  a  remote
          computer  that is connected to your TSX-Lite system via either a
          hardwired serial connection or a modem.  This is the  best  type
          of  TSX  workstation.   See Chapter 11, starting on page 71, for
          additional information about TSXTERM.


      3.2 Terminal Input Editor

      As you type TSX commands they are stored in a recall  list  so  that
      you  can  easily  recall  and reexecute commands.  This is useful if
      you make a typing error and want to recall, edit, and reexecute  the
      last  command.   You  can  also  recall  previous commands simply to
      avoid retyping them.

      There are two ways to recall commands, the  simplest  is  to  simply
      press  the  up-arrow  key  (or F3).  Each time you press up-arrow an
      earlier line in the recall list  is  displayed.   Once  the  desired
      line  has  been  recalled, press Enter to execute it.  You can press
      down-arrow to move in the  opposite  direction  through  the  recall
      list.   The second way to recall saved commands is to use the RECALL
      command which is described in Section 14.67 on page 131.   See  also
      the  description  of  the  SET EDIT command in Section 14.77 on page
      141.

      In addition to recalling previous lines, the Terminal  Input  Editor
      allows  you to edit lines.  To do this use the left- and right-arrow
      keys to position the cursor where the edit  is  to  take  place  and
      then  type  characters to be inserted or use the Backspace or Delete
      keys to remove characters.  The Home and  End  keys  will  move  the
      cursor  to  the  left  or  right  end  of  the  line.   You can type
      Control-A to switch between insert and overstrike edit modes.


      3.3 Control Characters

      Certain control characters have special meaning to  TSX.   They  are
      entered  by  holding down the "Ctrl" key while pressing the selected
      character.

      If you have a program that needs to receive one of these  characters
      for  its  own functions, you can use the PMAN program to install the
      application and specify that selected control characters are  to  be
      passed  directly  to  the  program  rather than being interpreted by
      TSX.


      Chapter 3. Terminal Operations                                    25


        . Control-\ -- Terminates  a  cross-connection  initiated  by  the
          HOST or SET HOST commands (see Sections 14.40 and 14.80).

        . Control-A  --  Switch  the  terminal input editor between insert
          and overstrike modes.

        . Control-B -- If you enabled the TSX print window facility,  this
          character  causes  the contents of the screen to be printed.  It
          has the same effect as pressing "Print Screen".  If you did  not
          enable  the print window facility when you installed TSX you can
          enable it by using TSGEN to set the DOWINPRNT  sysgen  parameter
          to   1.    See   Section   14.85  on  page  146  for  additional
          information.

        . Control-C -- Aborts the current program.  If the program is  not
          reading  characters  from  the terminal, you must type control-C
          twice to abort it.

        . Control-O -- Suppresses program output  to  the  terminal  until
          one  of  the following conditions occurs: (1) a second control-O
          is typed; (2) the program stops.

        . Control-Q -- Resumes output to the  terminal  after  output  was
          suspended by typing control-S.

        . Control-S -- Suspends terminal output until control-Q is typed.

        . Control-T  --  Displays  at  your terminal a line of information
          showing the status of your job.

        . Control-U -- Deletes all characters on the  current  input  line
          to the left of the cursor position.

        . Control-V  --  If  you  are  running  a  program that uses 25 to
          display information  on  a  serial  terminal  that  only  has  a
          24-line  display,  control-V  shifts  the  display up or down so
          that you can see the hidden line.

        . Control-W -- Type  control-W  followed  by  a  digit  to  switch
          between your TSX window sessions.

        . Control-X  --  Deletes  all  pending  terminal  input characters
          including characters you typed ahead which have not yet echoed.

        . Control-Z -- Indicates "end of file" to programs  reading  input
          from the terminal.

        . Backspace  (or  Delete)  -- Deletes the character to the left of
          the cursor.

        . Up-arrow -- Recalls previous command lines.

        . Down-arrow -- Moves downward through saved command lines.


      Chapter 3. Terminal Operations                                    26


        . Left/Right-arrow -- Moves the cursor within the current  command
          line for editing purposes.

        . Delete -- Deletes the character the cursor is positioned on.

        . Home -- Moves to the left end of the current command line.

        . End -- Moves to the right end of the current command line.

        . Print  Screen  --  If you enabled the TSX print window facility,
          this character causes the contents of the screen to be  printed.
          If  you  did  not  enable  the  print  window  facility when you
          installed TSX you can enable  it  by  using  TSGEN  to  set  the
          DOWINPRNT  sysgen parameter to 1.  See Section 14.85 on page 146
          for additional information.

        . Scroll Lock -- Call up the TSX Session Manager so that  you  can
          select  which  window  session you want to connect your terminal
          with.


      3.4 Screen Saver

      TSX features a "console  screen  saver"  feature  which  causes  the
      console  to  be  darkened  after a period of inactivity.  This helps
      lengthen the lifespan of the  console  display.   The  screen  saver
      only  affects  the  console display, not serial terminals.  When the
      screen saver blanks the console you can  press  any  key  (including
      Shift)  to  cause  the  display  to  be  reenabled.  By default, the
      console will be blacked out after 20 minutes  of  inactivity.   This
      time  period  can  be  modified  by using TSGEN to set the CONSSTIME
      parameter to the number of minutes before blanking occurs.  You  can
      set CONSSTIME to 0 to disable the screen saver.


      3.5 Communication Lines

      Your  serial  COM  ports can be used in two ways under TSX: (1) as a
      timesharing line through which you can log on and run  programs,  or
      (2)  as a "communication" line which is simply an I/O device used by
      a program to access some peripheral device such as a serial  printer
      or modem.

      TSX  allows  the  same  COM  port  to  be used part of the time as a
      communication line and at other times  as  a  timesharing  line.   A
      good  example  of  this is a line connected to a modem.  During part
      of the day remote users can call in and log on  through  this  line.
      At  other  times,  when no one is logged onto the line, the line can
      be used as a communication line when a program such  as  Procomm  is
      running  and  wants  to access the modem.  A port would also be used
      as a communication line when a bulletin board was running and  using
      the  line  to  accept  incoming  calls.   Note: the TSX HOST command
      described in Section 14.40 on page 118 is much  more  efficent  that
      communication programs like Procomm and Telix.


      Chapter 3. Terminal Operations                                    27


      When  a  user  is  logged  onto  a  timesharing  line, attempts by a
      program to allocate  the  line  as  a  communication  line  will  be
      rejected.   Conversely,  when  a  line  is in use as a communication
      line, TSX will not attempt to receive incoming calls or log  a  user
      on  because  control  of  the  line  has  been  relinquished  to the
      application program.  When the program exits the line  becomes  free
      and  TSX  will then log a user on when an incoming call arrives or a
      user presses Enter on a hardwired line.  If you wish  to  reserve  a
      line  as a communication line so that users may not log onto it, use
      TSGEN and set the LOGON parameter for the serial unit to  'N'  (no).
      See Section 2.6.2 for information about doing this.

      If  you  issue  a SHOW TERMINALS command the Status column will show
      "Logged on" if someone is  currently  logged  onto  the  line  as  a
      timesharing  line,  "I/O device" if a program is using the line as a
      communication line, or "Logged off" if the line is free.


      3.6 International Keyboard Support

      PC  keyboards  available  in  different  countries  have   different
      layouts  and  produce  different  characters than American keyboards
      do.  Under DOS, an alternate "keyboard driver" is  loaded  to  alter
      the  key  definitions.   In  TSX, alternate keyboard definitions are
      loaded from external control files called ".KEY files"  since  their
      extension is .KEY.

      The  .KEY  files  used  by  TSX  have the advantage that they can be
      edited with any text editor.  Hence, it is possible  to  create  new
      key  files  or  alter  the  definitions  of  keys  without obtaining
      additional drivers.

      For an alternate key file to take effect, it  must  be  loaded  with
      the KEYLOAD command, as in:

           KEYLOAD ITALY

      This  command  is normally placed in the site's LSTARTUP.CMD command
      procedure so that keyboard definitions are correct for  the  country
      each time the system boots.

      It  is  also  possible  for separate lines to have separate keyboard
      definitions, in the event that one computer is used by  people  with
      different  keyboards.  The use of the /LINE qualifier to the KEYLOAD
      command causes the loaded .KEY file  to  only  change  the  terminal
      from which the command was issued.

      Your  TSX  distribution  includes  the following .KEY files: US.KEY,
      GERMAN.KEY,  ITALY.KEY,  FRENCH.KEY,  and  SPANISH.KEY.   US.KEY  is
      provided  as an example; it is not necessary to use KEYLOAD for U.S.
      keyboards.

      You can use .KEY files to alter the definition of  any  key  in  any
      shift  state.   The  format of the file is documented in system file


      Chapter 3. Terminal Operations                                    28


      US.KEY, which also documents the keyboard  tables  which  TSX  comes
      preloaded with.







                                   Chapter 4

                              Running DOS Programs




      TSX  is  designed  to support modern 32-bit application programs and
      there are development tools available to write 32-bit  programs  for
      TSX  in  virtually all of the modern programming language.  However,
      at this point you may not have  any  32-bit  applications  and  just
      want   to   run  your  favorite  16-bit  DOS  applications.   Before
      proceeding, however, you should understand just a little  bit  about
      how DOS applications are supported in TSX.

      Under  TSX,  each  DOS  program  is run in "virtual 8086 mode." This
      means we fool the program into thinking  it  is  running  on  a  DOS
      computer  with  640Kb  of  memory  (plus  EMS  and  XMS).   TSX also
      supports programs that use the  DPMI  services  to  enter  protected
      mode.   In this mode, most 16-bit DOS programs run well under TSX --
      some even run faster under TSX than DOS.  However,  there  are  some
      "dirty"  DOS  programs  that  do  sneaky  tricks  under DOS (such as
      poking around in the operating system or directly messing  with  the
      hardware) that will run poorly, or not at all, under TSX.

      TSX  is  a true 32-bit, protected mode operating system.  "Protected
      mode" means  that  the  operating  system  and  its  components  are
      protected  from  harm by errant applications.  If a program tries to
      step outside of its bounds, the operating system will terminate  the
      program.   This  greatly  reduces  the chances of system "hangs" and
      "crashes" and prevents one application program from  disturbing  the
      execution of another.

      However,  protected  mode  prevents  the  execution of some programs
      such as SpinRite, Norton's Disk Doctor and SD,  CHKDSK,  DOS  16-bit
      device  drivers, and other programs that attempt to directly control
      the computer hardware.  This type of program will  have  to  be  run
      under DOS at a time that TSX is not in control.


      4.1 Installing and Tuning DOS Programs

      You  should use the same procedure for installing DOS programs under
      TSX as you would under DOS itself.  In fact, it is a  good  idea  to
      install  new  programs  under  DOS and verify their operation before
      using them with TSX.

      Once a program is up and running you may wish to use  the  TSX  PMAN
      command  to  specify  various  tuning  parameters for the program to
      optimize its execution under TSX.  The PMAN command  allows  you  to


                                       29


      Chapter 4. Running DOS Programs                                   30


      associate  attributes  with programs so that the attributes are used
      by TSX whenever the program is executed.   Attributes  that  may  be
      specified  for  a  program include the maximum memory space that the
      program may use, privileges to be granted to the  program  while  it
      is running, and many other options.

      A  program  whose  attributes  have  been  specified  using  PMAN is
      referred to as having been "installed" in TSX.  Many attributes  can
      be  set  with  PMAN, some of which can have a dramatic effect on the
      performance of programs running  under  TSX.   However,  it  is  not
      necessary  to "install" most programs with PMAN in order to use them
      with TSX; PMAN simply specifies parameters that tune  the  execution
      of  a  program  under TSX.  See Sections 2.5 and 4.6 for information
      about several important tuning parameters.

      When you use  PMAN  to  associate  attributes  with  a  program  the
      attribute  settings  take  effect  immediately  (you  do not need to
      reboot TSX).  In addition, PMAN updates a file  in  the  TSX  system
      directory  named  INSTALL.CMD  with information about the attributes
      for each program.  The INSTALL.CMD file  is  executed  automatically
      each  time  TSX  is  booted  so the attributes will remain in effect
      over system restarts.


      4.2 Direct Write Programs

      There are two basic methods used by programs to display  information
      on  the  screen.   Either  they perform system services to cause TSX
      (or DOS) to display the information or  they  directly  program  the
      video  memory  and  control  registers.   Many DOS programs directly
      access the video memory and registers -- this is especially true  of
      programs  that perform graphics.  TSX supports programs that use the
      display system services as well as those that  directly  access  the
      video  hardware.   Programs  that  do direct video access (bypassing
      the operating system) are called "direct write" programs.

      The TSX process windowing facility  operates  differently  depending
      on  whether  it  is  running a direct write program.  Because direct
      write programs control the display themselves -- behind the back  of
      the  operating  system -- TSX must suspend their execution when they
      are not in  the  session  currently  connected  to  the  screen  and
      keyboard.   Other  programs  that  do  not perform direct writes are
      allowed to  continue  executing  even  when  their  session  is  not
      connected  to  the  screen and keyboard.  If you have an application
      that does not do graphic display and which you would  like  to  have
      continue  executing  even  when  it is not connected to the console,
      you can start it by using the following command:

           RUN/NODWRITE program

      or you can use the TSX PMAN command to "install"  the  program  with
      the  NODWRITE  attribute  which  will  be invoked automatically each
      time the program is executed.  See Section  2.5,  starting  on  page
      10,  for  additional  information  about  setting  up  multi-tasking
      applications.


      Chapter 4. Running DOS Programs                                   31


      If you prefer to have  NODWRITE  be  the  default  setting  for  all
      programs,  you  can  use TSGEN to set the DEFDWRITE sysgen parameter
      to 0.  You can then use PMAN  to  selectively  turn  on  the  DWRITE
      parameter for programs that are going to do graphical displays.


      4.3 DOS Environment Variables

      When  you  begin  execution  of  a  16-bit  program,  TSX creates an
      "environment block" for the  program  containing  information  about
      all  symbols  defined  by use of the command "SET symbol".  The form
      of this command is

      SET[/SYSTEM] symbol=string

      For  example,  the  following  command  creates  a  DOS  environment
      variable named CL and assigns a string of options to it:

      SET CL = /Od /Zi

      If  you specify the /SYSTEM qualifier, the symbol is defined for all
      users and jobs; otherwise, it only applies  to  your  job.   If  you
      want  to  put  SET  commands  in  the  TSX LSTARTUP.CMD system-wide,
      start-up command file, be sure to use the /SYSTEM qualifier  or  the
      SET  commands  will apply only to the startup initialization job and
      not to other users and jobs.


      4.4 16-bit Program Device Names

      DOS treats the file names CON, PRN, AUX, and  NUL  specially  (note:
      these  are file names, not device names because there is no trailing
      colon).  If one of these file names is  specified,  the  channel  is
      opened  to a device rather than a disk file.  For compatibility, TSX
      also handles these file  names  specially  and  converts  them  into
      device names as shown below:

             CON --> TT:
             PRN --> LPT1:
             AUX --> AUX:
             NUL --> NL:

      You  may use an ASSIGN command to associate the logical device names
      LPT1 and AUX with the  actual  devices,  spooled  print  queues,  or
      files  of  your  choice.   If  a  16-bit  program attempts to open a
      channel to device or AUX: and no such logical device name  has  been
      defined, TSX directs the output to a disk file named STDAUX.LST.

      For  example,  the  following  command  assigns  the  name LPT1 to a
      spooled printer queue named LJPRINT:,

           ASSIGN  LJPRINT:  LPT1


      Chapter 4. Running DOS Programs                                   32


      4.5 Support for COMMAND.COM and TSR Programs

      TSX provides support for some  Terminate  and  Stay  Resident  (TSR)
      programs  such  as  Btrieve  and  Sidekick.   In  order to use a TSR
      program, you must run the  DOS  COMMAND.COM  command  processor  and
      then  use  it  to load the TSR program and execute programs that use
      the TSR program.  To do  this,  begin  by  running  the  COMMAND.COM
      program by issuing the TSX "DOS" command.

      Note  that  it is not necessary to issue the DOS command in order to
      run 16-bit programs with TSX.  Whenever  you  run  a  program  under
      TSX,  it  checks  to see if the program being started is a 16-bit or
      32-bit program and automatically shifts into the  correct  mode  for
      the  program.   You do not even have to be aware of whether a 16-bit
      or 32-bit program  is  executing.   When  a  16-bit  program  exits,
      control returns to the 32-bit TSX command processor.

      However,  there  are  two cases where it is useful to be able to run
      the DOS command processor: First, if you wish to run  a  16-bit  TSR
      program  such as Sidekick or Btrieve, it is necessary to establish a
      16-bit environment that will not be terminated when the TSR  program
      exits.   Second, you may wish to run COMMAND.COM so that you can use
      DOS commands or execute DOS BAT (batch) files that use commands  not
      supported by the TSX command processor.

      While  COMMAND.COM  is  running, you can issue DOS commands, execute
      BAT files, and run other 16-bit programs.  You may  not  run  32-bit
      programs  or  execute  TSX  specific commands such as FMAN until you
      exit from COMMAND.COM.  If you run a TSR program, the  program  will
      be   loaded  into  memory,  initialize  itself,  and  then  exit  to
      COMMAND.COM without freeing its memory  area.   Other  programs  can
      then  be  run  which  interact with the TSR program that is still in
      memory.

      Type the EXIT command to COMMAND.COM when  you  are  ready  to  exit
      from  it.   When  you  exit  from  COMMAND.COM  to  the  TSX command
      interpreter (and the native 32-bit environment), the 16-bit  program
      environment  is  released  and  memory space used by TSR programs is
      freed.  Thus, if you want to run other programs  that  use  the  TSR
      you   must   get   back  into  the  16-bit  environment  by  running
      COMMAND.COM again and reloading the TSR programs.

      If you  plan  to  make  heavy  use  of  TSR  programs  in  a  16-bit
      environment,  the  best  approach  is  to switch to a subprocess (by
      typing control-W-digit), issue the DOS command to  run  COMMAND.COM,
      load  TSR  programs,  and  then  switch  back to a subprocess in the
      32-bit environment when you want to run 32-bit programs rather  than
      stopping and restarting COMMAND.COM.


      4.6 Controlling DOS Program Input Loops

      TSX  provides  a  number  of  tuning parameters that can improve the
      performance  of  DOS  programs  --  especially  on  heavily   loaded
      systems.   However,  most  of  the  time the standard TSX scheduling


      Chapter 4. Running DOS Programs                                   33


      does a very good job and it is not necessary to  specially  tune  or
      install  programs.  Unless you are experiencing performance problems
      you may wish to skip the following sections  on  tuning,  especially
      on the first reading.

      Well  behaved  programs  suspend their execution while idle by using
      one of the system services that wait for terminal  input.   However,
      many  DOS  programs  have  an  idle  loop  that  checks  for pending
      terminal input without waiting, and then, if no  input  is  pending,
      loop  back  and check again.  This causes the program to burn up CPU
      time  while  it  is  waiting  for  terminal  input  and  places   an
      unnecessary burden on the system.

      You  can  detect  programs  that behave this way by using the SYSMON
      command  or  repeatedly  executing  the  SHOW  SYSTEM  command  from
      another  time-sharing  line  to  display information about a program
      that is in an  idle  state  waiting  for  terminal  input.   If  the
      "State"  of  the  job  is  continuously  shown as "CPU" and the "CPU
      time" value is increasing steadily, then the program is  in  a  loop
      while waiting for terminal input.

      TSX  provides  several program execution attributes that may be used
      to "tame" DOS programs that loop while waiting for  terminal  input.
      The  TTWAIT and TTCKIO attributes provide basic control over looping
      programs and may be associated  with  the  program  using  the  PMAN
      command.    Three   other   attributes,  MAXTTCHK,  MAXTTIOCHK,  and
      TTHANGTIME may be  used  with  the  PMAN  command  to  provide  more
      precise control.

      When  a  program  is  executed  with one or more of these attributes
      specified, TSX uses a counter to  tally  the  number  of  times  the
      program  checks  for terminal input without waiting.  The counter is
      reset when terminal input is received or when the  program  performs
      other  system  services  such  as  reading,  writing,  updating  the
      screen, etc.  If the TTWAIT attribute is specified and  the  program
      performs  more terminal input checks than the value specified by the
      MAXTTCHK  attribute  (or  the  MAXTTCHK  sysgen  parameter  if   the
      MAXTTCHK  attribute  is  not  specified),  without  doing  any other
      system services, the program is suspended for  the  length  of  time
      specified  by  the  TTHANGTIME  attribute  (or the TTHANGTIME sysgen
      parameter if the TTHANGTIME attribute was not specified),  and  then
      is  allowed  to  check  for  terminal  input until the counter again
      exceeds the MAXTTCHK attribute.

      The TTCKIO and  MAXTTIOCHK  attributes  have  a  similar  effect  to
      TTWAIT  and  MAXTTCHK,  but modify the number of times that terminal
      input checks may be  performed  after  a  disk  I/O  operation.   If
      TTCKIO  is  specified,  the program is allowed to perform the number
      of terminal input checks specified by the MAXTTIOCHK  attribute  (or
      the  value  of  the MAXTTIOCHK sysgen parameter if the MAXTTIOCHK is
      not specified) after each disk I/O operation.

      If you have a program which is continuously  in  the  CPU  execution
      state   while  waiting  for  terminal  input,  try  using  PMAN  and
      installing the program with the  TTWAIT  attribute  turned  on.   If


      Chapter 4. Running DOS Programs                                   34


      this  causes  its  execution  to  slow  down, try experimenting with
      different values for the MAXTTCHK attribute.

      As  an  example,  assume  that  you  are  trying  out  a   new   DOS
      application,  named  HEW, under TSX.  The program runs fine, just as
      it would under  DOS.   However,  other  users  complain  that  their
      processes  run  significantly  slower  while  HEW is executing.  You
      presume that HEW is needlessly looping for terminal input  while  it
      is  idling,  so  you use PMAN to install the program with the TTWAIT
      attribute to eliminate CPU waste.  Unfortunately,  this  causes  HEW
      to  run  too  slowly,  so you need to fine-tune its operation, using
      the MAXTTCHK attribute.

      Generally, by using this procedure you can greatly  reduce  the  CPU
      time  used  by  idling programs without having any adverse affect on
      response time.  However, a few programs have pathological  behaviors
      that  cause  problems.   WordPerfect  is  a good example.  Normally,
      WordPerfect checks  for  keyboard  input  a  few  times  after  each
      character   is   typed  and  the  MAXTTCHK  attribute  is  adequate.
      However, when performing some operations  such  as  a  mailing  list
      merge,  it  checks  for  keyboard  input many times while performing
      merging tasks and it does not  perform  any  other  system  services
      which  would  reset the terminal input check counter.  The result is
      that TSX "thinks" WordPerfect is in its idle loop  and  suspends  it
      periodically.  This significantly slows down the merge operation.

      To  handle this case, you may type control-W '+' (control-W followed
      by a plus sign) to cause  TSX  to  temporarily  allow  an  unlimited
      number  of  terminal  input  checks  without suspending the program.
      Type control-W '-' (control-W followed by a minus sign) to  reenable
      standard  terminal  input check suspension.  When you type control-W
      '+' a timer is started; if you do not type control-W '-' before  the
      amount  of  CPU  time  specified  by the NOWAITTIME sysgen parameter
      elapses, the terminal input check suspension is  reenabled  just  as
      if   you   had  typed  control-W  '-'.   Another  system  generation
      parameter, NOWAITCNT, causes the effects  of  control-W  '+'  to  be
      canceled  after  the  specified number of characters are typed.  The
      bell is rung at your terminal when control-W '+' is  canceled.   The
      NOWAITTIME  sysgen  parameter  is specified in units of 0.01 seconds
      and the default value is 30,000 (5 minutes).  The default  value  of
      NOWAITCNT is 100.


      4.7 IDLETIME Attribute

      If  you  are  unable  to  "tame"  a  program  by  use  of the TTWAIT
      attribute, there is one other method available.  If PMAN is used  to
      install  a program with a non-zero value for the IDLETIME parameter,
      then TSX starts a timer each  time  the  program  begins  computing.
      The  timer  is  reset  when  the program does terminal I/O, or other
      system services.  If  the  time  value  exceeds  the  value  of  the
      IDLETIME   parameter   specified  for  the  program,  the  program's
      execution state is reduced from the normal  CPU  state  to  a  lower
      priority  state called LOCP.  In this state the program continues to
      execute but because  it  is  at  a  reduced  priority  it  does  not


      Chapter 4. Running DOS Programs                                   35


      interfer  with  the  execution  of  normal  priority jobs, including
      those in the standard CPU compute-bound state.  The  idle  timer  is
      reset,  and  the  program  is  restored  to  normal priority, when a
      character is received or a system  service  is  executed.   If  this
      parameter  is  given  the value 0, the program is allowed to compute
      indefinitely without being classified as idle.

      In selecting a value for the IDLETIME  attribute,  it  is  important
      that  you  do  not  choose  a  value which is so low that legitimate
      computation performed by the program causes it to be placed  in  the
      LOCP  state.   Obviously,  this  is  dependent  on the nature of the
      program  and  will  require  some   experimentation   to   optimize.
      However,  a  reasonable  starting  point would be in the range of 10
      seconds, which corresponds to an IDLETIME parameter setting of  1000
      since it is specified in units of 0.01 seconds.

      It  is  suggested that you use the MAXTTCHK and MAXTTIOCHK to try to
      tame a program before resorting to using IDLETIME.


      4.8 Printer Flush Sysgen Parameters

      Some DOS programs open printer output, write  some  characters,  and
      leave  the printer open until they exit.  This causes the printer to
      be tied up  by  the  job,  blocking  output  by  other  users.   TSX
      provides   two   system  generation  parameters  to  alleviate  this
      situation: DOSLPTTIME  and  DOSLPTCLSTIME.   The  DOSLPTTIME  sysgen
      parameter  causes  output  to  be  flushed  to the printer after the
      specified number of seconds, but the printer is held for use by  the
      job.   The  DOSLPTCLSTIME sysgen parameter causes data to be flushed
      to the spooled printer and then releases  the  printer  for  use  by
      other  users.   The  printer  will  be  reclaimed by the job when it
      generates more output and it is not in  use  by  another  job.   The
      DOSLPTCLSTIME  parameter  specifies  that if the printer is idle for
      the number of seconds  (i.e.,  no  characters  are  written  by  the
      program)  it  is released.  The timer controlled by DOSLPTCLSTIME is
      reset each time the program writes to the printer.

      See Section 2.5, starting on page  10,  for  additional  information
      about installing and tuning DOS programs.


      4.9 Virtual UART Support

      In  order  to  support  a variety of serial adapter types, including
      "smart" serial adapters, TSX has to emulate  the  operation  of  the
      actual  hardware devices and make all adapter types look like simple
      UART COM ports for communication programs that  perform  direct  COM
      port  I/O.   This  emulation  forces TSX to intercept all IN and OUT
      instructions  performed  to  the  COM  port  control  registers  and
      convert  them into the appropriate commands depending on the type of
      serial adapter actually in  use.   This  emulation  allows  programs
      like  Procomm and BBS software to use any serial line on any type of
      adapter that is supported by TSX even though these programs  do  not
      understand  how to control the actual hardware.  TSX makes it "look"


      Chapter 4. Running DOS Programs                                   36


      like a 16550 UART type COM port.  This emulation works well but  may
      result  in  high-speed  communications  being slowed down because of
      the emulation overhead.  The  use  of  actual  16550  type  buffered
      controllers  reduces  the  overhead  and improves throughput.  Note:
      the TSX HOST command described in Section 14.40 on page 118 is  much
      more efficent that communication programs like Procomm and Telix.

      When  you  install  TSX-Lite  it checks for the presence of the COM1
      and COM2 serial ports.  If they  exist  it  defines  TSX  I/O  units
      named  TTB0 and TTC0.  TTB0 is the TSX name for COM1 and TTC0 is the
      TSX name for COM2.  Try using the  SHOW  TERMINALS  command  to  see
      that   these   device  names  exist.   TSX  also  does  an  implicit
      assignment of the logical device name "COM1" to  "TTB0"  and  "COM2"
      to  "TTC0".  When your program attempts to access a COM port the TSX
      virtual UART routine directs the request to  the  hardware  unit  to
      which  the  COM1,  COM2,  COM3,  or  COM4  logical  device  name  is
      assigned.  For example, if a program  attempts  to  access  COM1  it
      will  normally  be directed to TTB0, but the following command could
      be used to redirect it to TTC0:

           ASSIGN TTC0: COM1

      See Section 7.3 on page 45  for  additional  information  about  the
      ASSIGN command.

      4.9.1 FOSSIL Driver

      TSX  includes  an  integral FOSSIL driver that is a standard part of
      the system.  The TSX FOSSIL driver is similar  in  function  to  DOS
      drivers  such  as  X00  and  BNU; external DOS drivers such as these
      should not be used with TSX.  As described in Section  4.9  you  can
      use  an  ASSIGN  command  to  redirect virtual COM ports to selected
      devices.

      Normally the serial line speed for a FOSSIL line  is  controlled  by
      the  program  using the line.  However, if you wish to lock the line
      to the speed specified during system  generation  you  may  set  the
      FIXEDSPEED option for the unit to 'Y' (yes) by using TSGEN.


      4.10 Expanded Memory Support (EMS)

      TSX  supports  the  Expanded  Memory Specification (EMS) version 4.0
      developed by  Lotus/Intel/Microsoft.   Under  DOS,  expanded  memory
      support  is  provided  by  a  handler  such  as  EMM386.  Under TSX,
      expanded memory support is  an  integral  part  of  the  system  and
      EMM386 should not be loaded when TSX is started.

      By  default, 16-bit programs may access an amount of expanded memory
      space defined by the EMSDEFPGS sysgen parameter.   (Note:  each  TSX
      user  has  this  much expanded memory space available).  You can use
      the SET PROCESS command to control the  amount  of  expanded  memory
      space  you  want to make available to programs you run.  The form of
      this command to control expanded memory space is:


      Chapter 4. Running DOS Programs                                   37


           SET PROCESS/EMS=value

      Where value is the number of K-bytes to make available  in  expanded
      memory.   The  maximum value that may be specified is limited by the
      EMSMAXPGS sysgen parameter.  If the value is set  to  0  (zero)  EMS
      support is disabled for the process.


      4.11 Extended Memory Support (XMS)

      TSX  supports  the  Extended  Memory Specification (XMS) version 2.0
      developed by  Lotus/Intel/Microsoft.   Under  DOS,  extended  memory
      support  is  provided  by  a  handler such as HIMEM.SYS.  Under TSX,
      extended memory support is  an  integral  part  of  the  system  and
      HIMEM.SYS should not be loaded when TSX is started.

      TSX  is  a  "virtual  memory"  operating  system.   This  means that
      programs can potentially use more memory than  physically  installed
      in  your  computer.   In  other  words, you could run a program that
      needs 8 MB on a computer that only  has  4  MB  installed.   When  a
      program  uses  more  memory  than is available, TSX uses a technique
      called "demand paging" to keep in memory the most recently  accessed
      memory  pages.   The  other  pages  are  stored in a page file named
      PAGEFILE.TSX in the TSX system directory.   The  size  of  the  page
      file is controlled by the PGFILSIZ sysgen parameter.

      The  maximum  virtual  memory  space  available  to  each program is
      controlled  by  the  MAXP0MEM  sysgen  parameter.   This   parameter
      specifies  the  size in 1k units and the default value is 8192 which
      corresponds to 8 MB.  If you run  programs  that  need  more  memory
      space  than  this  you  can  increase the MAXP0MEM parameter up to a
      maximum of 32768 which corresponds to 32 MB.  The value of  MAXP0MEM
      limits  the  total  memory  space  available  to  each  program  and
      includes both the  640Kb  low  memory  area  and  any  EMS  and  XMS
      (extended)   memory  used  by  the  program.   The  disadvantage  of
      assigning a very large number to MAXP0MEM is that some programs  use
      all  available  memory space.  With TSX's virtual memory system they
      will be allocated more memory than they actually need and  this  can
      result in excessive memory paging and poor performance.

      If  you  want  to allow a potentially large virtual memory space but
      limit the space to a smaller value for  a  particular  program,  you
      can  use  the  PMAN  command  to  install a program and set a MAXMEM
      value that is smaller than the global limit.   You  can  also  limit
      your  virtual  memory  space by use of the SET PROCESS command.  The
      form of this command is

           SET PROCESS/MAXMEM=value

      Where "value" is the total number of K-bytes of memory space  to  be
      made  available  to  the  program  (including  the  640Kb low memory
      region).  The maximum value specified may not exceed  the  value  of
      the MAXP0MEM sysgen parameter.


      Chapter 4. Running DOS Programs                                   38


      4.12 DPMI Support

      TSX  supports  version  0.9  of  the  DOS  Protected  Mode Interface
      standard  including  the  Microsoft  DOS  extensions.   DPMI  is  an
      industry  standard  that allows programs to run in a DOS environment
      and use both 16-bit and protected 32-bit modes  of  operation.   TSX
      serves  as  a  DPMI  "host"  and provides the INT 31 services.  DPMI
      support is a standard part of TSX and DPMI extenders do not have  to
      be loaded to run DPMI programs under TSX.


      4.13 Phar Lap Native System Services

      In  addition  to  DOS, BIOS, and DPMI support, TSX also provides two
      32-bit Application Program Interfaces (API).  The first of these  is
      compatible  with the services provided by the Phar Lap DOS extender.
      These are basically the DOS INT 21 services extended to  use  32-bit
      register  values and addresses.  The Phar Lap EXP executable program
      image structure is used by TSX executable programs.  These  programs
      run  in  protected  mode  and  access a 32-bit "flat" memory address
      space.  32-bit compilers and linkers  designed  for  use  with  Phar
      Lap,  such  as  MetaWare  High C, and NDP Fortran, also run with TSX
      and produce 32-bit EXP files that run  directly  under  TSX  without
      requiring any extender products.

      The  "native"  API  for  TSX  provides  a 32-bit flat memory address
      space and over 200 system services designed for the  development  of
      advanced   32-bit   applications.   These  system  services  provide
      functions   such   as   "forking"   subtasks,   performing   no-wait
      asynchronous  I/O,  facility  locking, process control, and advanced
      memory management.  The full TSX-32  product  also  includes  system
      services for real-time program control.

      Both  the  Phar  Lap and native TSX system service sets are provided
      in TSX-Lite.  The  native  system  services  are  described  in  the
      TSX-32  System  Services  manual.   See REGISTER.DOC for information
      about  ordering  the  Programmers  Kit  if  you  are  interested  in
      developing programs that use the TSX native system services.







                                   Chapter 5

                            The TSX Command Language





      5.1 Command Qualifiers

      TSX  is  a command-driven operating system.  System commands are, in
      many cases, actual programs that perform services for you.  In  some
      cases  a  "front-end" has been provided to simplify the use of these
      programs.

      In many cases, the names of TSX system  commands  are  the  same  as
      their  counterparts in the DOS world.  However, TSX commands usually
      have a rich supply of command "qualifiers" which extend their  power
      far  beyond DOS.  Qualifiers are keywords you may add to the command
      to fine-tune what it does.  You may add as many  qualifiers  as  you
      wish  to  a  command,  simply  separating  them with the slash ('/')
      character.

      For example, you are probably familiar  with  the  DOS  DIR  command
      which  displays information about the files on a disk.  In TSX there
      are (at last count) 45 qualifiers to the DIR command.   Here  are  a
      few examples:

        . All files sorted in name order:

               DIR/SORT=NAME

        . All files in date order, most recent first, names only:

               DIR/SORT=DATE/REVERSE/BRIEF

        . All files created since yesterday:

               DIR/SINCE=YESTERDAY

          All files created before January 1, 1993:

               DIR/BEFORE=1-JAN-1993

        . All files except those with the extension ".BAK":

               DIR/EXCLUDE=*.BAK

        . All files whose names begin with 'A' and end with 'X':



                                       39


      Chapter 5. The TSX Command Language                               40


               DIR A*X.*


      5.2 Wildcard Specifications

      TSX  provides  a  more  powerful form of wildcard file specification
      than DOS.  In addition to being  able  to  use  a  "*"  (match  any)
      wildcard  character  at the end of a file name, you can also use "*"
      characters within file names.  For example, the specification  "A*C"
      would  match  any file that begins with the letter 'A' and ends with
      the letter 'C'.  The pattern "*X" would match  any  file  that  ends
      with the letter 'X'.

      TSX   also  allows  you  to  use  wildcard  matching  characters  in
      directory names.  In addition, TSX allows you  to  use  the  special
      directory  specification "\...\" which means "and all subdirectories
      below this level." For example, the command

           DIR C:\...\*.*

      would list all files,  in  all  directories  on  the  C  disk.   The
      command

           SEARCH C:\WORK\...\*.C "Cappannari"

      would  search  for  the  string  "Cappannari"  in all files with the
      extension ".C" in the WORK directory and  all  subdirectories  below
      WORK.   The "\...\" construct is especially handy in operations like
      DIR, DELETE, COPY, SEARCH, and BACKUP.


      5.3 TSX Device Names

      Former DOS users are sometimes  confused  when  they  discover  that
      peripheral  devices do not always have the same names under TSX that
      they have under DOS.  This is  necessary  because  TSX  can  support
      many more devices than DOS.

      A  TSX  device name has the form 'ddcuuu' where 'dd' is a two letter
      device type, 'c' is a letter that designates  a  device  controller,
      or  physical  unit  in  the case of disk drives, and 'uuu' indicates
      the individual unit, or partition in the  case  of  disks.   If  the
      controller  letter  is  omitted,  it  defaults  to  'A'  (the  first
      controller); if the unit number is omitted, it defaults  to  0  (the
      first unit).

      The following is a table showing the various TSX device type names:


      Chapter 5. The TSX Command Language                               41


           Name              Device type
           ----  ---------------------------------------
            DF   Floppy disk (diskette)
            DH   Hard (fixed) disk
            DV   Virtual (RAM) disk
            LP   Printer on parallel port
            MB   Mailbox
            NL   "Null" device. (Like DOS NUL).
            TT   Terminal lines (console or COM ports).

      For  compatibility  with DOS, TSX also recognizes single-letter disk
      names such as 'A' and 'B' for floppies,  and  'C',  'D',  etc.   for
      fixed  disks.  For example, the primary fixed disk (drive 'C') has a
      TSX name of 'DHA0' but can also be addressed as  'C'.   The  console
      terminal  is  named  'TTA0',  the  serial port connected to COM 1 is
      'TTB0' and COM port 2 is 'TTC0'.  Device names MUST be  followed  by
      a  colon  or  they  will  be considered to be file names rather than
      device names.  For example, "NL:" is the null device and "NL"  is  a
      file named "NL".

      Spooled  printer  "queues" have names similar to device names.  This
      is explained in Chapter 8.3.


      5.4 Internal and External Commands

      The command processor for TSX is a program named  TSKMON.EXP.   Like
      COMMAND.COM  under  DOS,  TSKMON  processes many commands internally
      (such as SHOW SYSTEM) while other  commands  are  actually  programs
      that  get  run (such as DIR).  When you type a command, TSKMON first
      checks to see if it is an internal command.  If it's not, it  checks
      for  command procedures or programs with the specified name, so that
      if you type ARGLE, TSKMON searches for ARGLE.EXE, ARGLE.BAT, and  so
      forth.   To  be  precise,  a set of directories (first your current,
      then the system directory, then any  directories  specified  by  the
      search   path)  is  searched  in  order.   In  each  directory,  the
      following files would be looked for:

           ARGLE.CMD
           ARGLE.EXP
           ARGLE.COM
           ARGLE.EXE
           ARGLE.BAT

      For more information on the search path, see HELP PATH.

      If you are unsure what  command  TSKMON  is  actually  finding,  you
      could use the following sequence:

           SET LOG/FILE=X.LOG
           SET PROCESS/CMDTRACE
           ARGLE
           (TSKMON finds ARGLE)
           SET LOG/CLOSE


      Chapter 5. The TSX Command Language                               42


      The  SET  LOG  commands create a log file containing all output sent
      to  your  terminal  (this  is  an  example  of  the  many  debugging
      facilities  built  into  TSX  to help you analyze program behavior).
      The SET PROCESS/CMDTRACE command  tells  TSKMON  to  report  on  its
      efforts to find ARGLE.BAT, ARGLE.COM, etc.







                                   Chapter 6

                                The System Menu




      TSX  comes with a menu shell which you can customize to create menus
      for yourself or  customers.   Your  TSX-Lite  system  comes  with  a
      couple  of  packaged  menus  as examples.  To access the main system
      menu, issue the command:

           TSXSHELL

      From the main menu, you can access several of  the  general  purpose
      full  screen utilities such as the help facility.  A full TSX system
      has an electronic mail option as well.

      A submenu for system management functions allows access to  programs
      which  customize your TSX installation.  We will describe the use of
      these programs in the chapter on system management.

      The TSXSHELL command invokes the  TSX  system  menu  driver  program
      called  SMD.   In  addition  to displaying TSX system menus, you can
      also use SMD to create your own menus.  The  file  SMD.DOC  contains
      instructions for creating custom menus.


























                                       43







                                   Chapter 7

                           Symbols and Logical Names




      Symbols  and  logical  names  are  both types of shorthand notation.
      Symbols are used to define your own commands.  They  are  also  used
      for  control  purposes within command files.  Logical names are used
      to give shorthand names to devices and files.


      7.1 Defining Symbols with String Assignment Operators

      Using symbols you  can  define  your  own  commands.   Suppose,  for
      example,  in  moving  between  directories,  you often find yourself
      moving "up, over, and down" as in:

           CD ..\HERE
           CD ..\THERE
           CD ..\HERE

      You get tired of typing "CD ..\" and wish there was a command  "OT",
      standing  for  "Over  To",  that  did  the  same  thing.  The symbol
      assignment:

           OT:==CD ..\^

      would set up such a pseudocommand for you.  The ":==" is the  symbol
      assignment  operator  and the "^" substitutes the next word from the
      command you type, so that typing "OT THERE" is equivalent to  typing
      "CD ..\THERE".

      In  a multi-user environment like TSX, the system manager may decide
      to  define  some  symbols  that  apply  to  all  users,   and   some
      individuals  may  choose  to  define  their  own  symbols  and  even
      override the system-wide symbols.  To define a symbol that is to  be
      available  for  all  users use the ":===" operator (note three equal
      signs) and place the symbol definition command in your  LSTARTUP.CMD
      system-wide,  start-up  command  file.   For  example, the following
      command, when placed in LSTARTUP.CMD, will  define  a  SDIR  command
      that will produce directory listings sorted by name:

           SDIR:===DIR/ORDER=NAME ^

      If  a  user  defines  his  or  her  own  SDIR symbol using the ":=="
      operator, that symbol definition overrides  the  system-wide  symbol
      for  that  user;  it does not affect the symbol definition for other
      users.  Symbols defined using ":==" are discarded when you  log  off


                                       44


      Chapter 7. Symbols and Logical Names                              45


      (or  the  system  is  rebooted)  so  if  you wish to define a set of
      symbols for yourself you should put them in a command file that  can
      be  executed each time you log on.  Note: when you generate a system
      you can specify a start-up file  for  each  time-sharing  line.   An
      optional  TSX-Lite  Security Kit is available which includes a LOGON
      program to force users to enter a user name  and  password  to  gain
      access to the system.  See REGISTER.DOC for ordering information.

      There  is  also a ":=" operator.  This defines a local symbol within
      a command procedure.  The symbol overrides  the  definition  of  any
      user  or  system-wide symbols with the same name for the duration of
      the command procedure and then is deleted.  If the ":=" operator  is
      used outside of a command procedure it is equivalent to ":==".


      7.2 Defining Symbols with Numeric Assignment Operators

      The  ":=",  ":==",  and  ":==="  operators  are called string string
      assignment operators because they equate  the  symbol  name  on  the
      left  of  the  equal  sign(s) to the string on the right.  There are
      three similar operators, "=", "==", and "===" that  perform  numeric
      assignments.   These  operators function in a very similar manner to
      the string assignment operators except that they require  a  numeric
      expression  to be to the right of the equal sign.  They evaluate the
      numeric expression and assign the resulting numeric  string  to  the
      symbol.  For example, the command:

           COUNT = 2+3

      Evaluates  the  expression  "2+3"  and assigns the string "5" to the
      symbol COUNT.  The following command procedure would execute a  loop
      5  times  displaying the value of the COUNT symbol each time through
      the loop:

           COUNT = 1
           TOP:
           DISPLAY COUNT IS 'COUNT
           COUNT = COUNT+1
           IF COUNT <= 5 THEN GOTO TOP

      The apostrophe character  before  "COUNT"  in  the  DISPLAY  command
      cause  the  value  of  the  COUNT  symbol to be substituted into the
      string being displayed.

      In an analogous fashion to  the  symbol  assignment  operators,  "="
      defines  a  local  symbol  for a command file, "==" defines a symbol
      for the current user only, and "===" defines a system-wide symbol.


      7.3 ASSIGN Command and Logical Device Names

      A different method can be used to  establish  a  shorthand  notation
      for  a  device,  directory,  and  file  specification.  This is done
      using the ASSIGN command to  define  a  logical  device  name.   For
      example, after executing the command:


      Chapter 7. Symbols and Logical Names                              46


           ASSIGN C:\XBDRV\C_DRV\BIN\ X

      You  have  defined  a logical device name "X" which is equivalent to
      "C:\XBDRV\C_DRV\BIN\".  You could issue commands like:

           DIR X:
           COPY DATA.DAT X:
           RUN X:APOS

      in which case TSX replaces "X:" by "C:\XBDRV\C_DRV\BIN\".   This  is
      much easier than typing:

           DIR C:\XBDRV\C_DRV\BIN\
           COPY DATA.DAT C:\XBDRV\C_DRV\BIN\
           RUN C:\XBDRV\C_DRV\BIN\APOS

      In  this example, X: is said to be a "logical name" which equates to
      a physical device  and  directory  specification.   There  are  many
      advantages  to  the  logical name facility, as we shall begin to see
      when we discuss printing.

      Frequently, single letter logical names like "X:" are  used  because
      some  DOS programs only accept a single character as a drive letter.
      However, TSX allows you to define logical names that are  up  to  16
      characters  long.   The logical name "SY:" is assigned by the system
      to point to the TSX system directory (typically, \TSX32SYS).

      If you wish to define logical names that apply  to  all  users,  you
      can  use  the  "/SYSTEM" qualifier with the ASSIGN command and place
      the commands  in  the  LSTARTUP.CMD  system-wide,  start-up  command
      file.    For   example,   the  following  command,  when  placed  in
      LSTARTUP.CMD, will define the logical device name  "TEMP:"  for  all
      users:

           ASSIGN/SYSTEM C:\WORK\ TEMP

      Note  that  TSX logical names can specify not only a particular disk
      but a directory and  even  a  particular  file  on  the  disk.   For
      example,  the following command associates the logical name WORKFILE
      with the a particular file:

           ASSIGN C:\WORK\TEMP1.DAT WORKFILE

      Having done this, the command

           COPY ABC.DEF WORKFILE:

      will cause the  contents  of  the  file  ABC.DEF  to  be  copied  to
      C:\WORK\TEMP1.DAT.

      You  can  also use logical device assignments to associate a logical
      device name with a device other than a disk file.  For example,  the
      following  command  assigns the logical name LPT1 to a spooled print
      queue named PRINT:


      Chapter 7. Symbols and Logical Names                              47


           ASSIGN PRINT: LPT1

      See Section 8.2 for information about setting up print queues.

      In full TSX-32 with networking you can use  the  ASSIGN  command  to
      create  logical drive letters that access files on remote computers.
      For example, the following command defines a logical  device  letter
      'N'  and  associates  it  with  a disk on a networked computer whose
      node name is ADMIN:

           ASSIGN ADMIN::C: N

      More detail on  symbols  is  available  under  HELP  ASSIGNMENT  and
      there's help under ASSIGN for logical names.







                                   Chapter 8

                                    Printing




      The  TSX  queue management and spooling system is much more powerful
      than anything you have encountered using DOS.   In  fact,  it  is  a
      world  class system designed to manage large installations with many
      users accessing many printers.  We could easily  devote  a  document
      the  size  of the one you are reading to explaining all the features
      of printing system!

      Fortunately there are two pieces of good news.  First,  it's  simple
      to  do simple things.  As with all aspects of TSX, you can get going
      right away and slowly build your  knowledge  as  you  tackle  harder
      tasks.   Second,  there  is  a  helpful, friendly program named QMAN
      that you can use to set up  print  queues  and  manage  print  jobs.
      QMAN  has  extensive  on-line  help (press F1 at any point while you
      are running it to get context sensitive help).


      8.1 Spooler and Queue Manager

      At the heart of the printing system are  two  programs:  the  "Queue
      Manager"  (QUEMAN.EXP)  and the "Spooler" (SPOOLER.EXP).  They share
      responsibility for  managing  data  that  you  wish  to  print.   To
      understand  how  these  programs work you need to understand the two
      basic methods for printing data with TSX.

      The first method is called "explicit printing".  To use this  method
      issue  a  PRINT  command  to  print  a  file  that  has already been
      created.  The request to print the  file  is  passed  to  the  queue
      manager   which  holds  it  until  the  specified  printer  finishes
      printing any other file.  The queue manager than  issues  a  command
      to  the  spooler  to cause the spooler to copy data from the file to
      the  printer.   The  spooler  is  a   "detached   job"   that   runs
      independently  of  the  queue  manager  and  the job that issued the
      PRINT request so the queue manager and the original job can  perform
      other  tasks  while  the  file  is being printed by the spooler (the
      spooler can drive more than one printer at once).

      The second method  is  called  "implicit  printing".   To  use  this
      method  you  simply  write  data destined for a printer to a logical
      device name associated with a print queue.  The data is diverted  to
      the  spooler  program which stores it in a temporary TSX system file
      until the printer becomes available.  It then  copies  the  data  to
      the  printer  at  the rate that the printer can accept it.  If there
      is adequate space in the temporary file, the program generating  the


                                       48


      Chapter 8. Printing                                               49


      data  to  be  printed  can execute very quickly (since it is writing
      its output to disk) and exit before the printing  is  finished.   If
      the  spooler  temporary  file  fills  up, the program generating the
      data is suspended until the printer can  accept  data  and  free  up
      space  in  the  temporary  file.   Implicit  printing  is convenient
      because programs can write to  printers  without  having  to  create
      print files that need to be cleaned up later.

      As  mentioned  earlier,  the  queue manager (QUEMAN.EXP) and spooler
      (SPOOLER.EXP) programs run as  detached  jobs  which  start  running
      each  time  TSX  is initiated.  Try using the SHOW SYSTEM command to
      see that the spooler and queue manager are running.

      The spooler  can  simultaneously  accept  printer  output  from  any
      number  of  programs  and  ensure that each report waits its turn to
      print.   Multiple  printers  are   supported,   including   parallel
      printers,  serial  printers,  printers attached to serial terminals,
      and TSXTERM printers (TSXTERM is our terminal  emulator  to  turn  a
      DOS  PC  into  a  TSX workstation -- see Chapter 11 starting on page
      71).  The spooler usually leaves program output  untouched,  but  it
      can  insert  form  feeds to eject paper, generate header and trailer
      pages, handle margins, and so on.

      In addition to managing  print  jobs,  the  queue  manager  is  also
      responsible   for   overseeing   background  batch  jobs.   This  is
      explained in Section 9.3 starting on page 54.

      The printing system uses print "queues" (lists  of  print  jobs)  to
      ensure  orderly  printing  and direct program output to a particular
      printer.  Queues have associated "forms" which control the  form  of
      output  and "stocks" which tell TSX what type of paper is mounted in
      the printer.


      8.2 Setting Up the Printer Queues

      If you have a parallel printer you are in  good  shape  because  TSX
      automatically  creates  a default queue named "PRINT" and associates
      it with the printer connected to your parallel port  number  1  (TSX
      device name LPA0:).

      If  you  have  a  serial  printer  you  can  use the QMAN program to
      quickly modify the PRINT queue to direct it to a  serial  port.   To
      do  this,  type  "QMAN"  to start the program.  QMAN starts out in a
      browse screen showing the available queues.   One  should  be  named
      PRINT,  with  associated  device  LPA0:.   You  can alter the device
      associated with the queue by typing "M" for Modify.   A  data  entry
      screen  is  presented  which allows you to modify various aspects of
      the queue.  The device name is listed first.   Position  the  cursor
      to  this  field  and  enter  device  name  TTB0:  if  the printer is
      connected to the first COM port or TTC0:  if  it  connected  to  the
      second  COM  port.  Press ESC to exit the data entry screen, and ESC
      again to exit QMAN.


      Chapter 8. Printing                                               50


      We should mention at this  point  that  context  sensitive  help  is
      available  in  all  data  entry fields of QMAN (as well as the other
      full screen utilities like TSGEN) by pressing the F1 key.

      If your system has no parallel port at all, but does have  a  serial
      printer,  no  PRINT  queue  will  exist.   Instead of typing "M" for
      modify, type "C" to create the queue; the same data entry screen  is
      used  for  both operations, except that one extra menu specifies the
      queue type (select "Base queue").

      Now that we have the queue named PRINT associated  with  the  device
      to  which  your  printer  is  attached,  we  will  print a test file
      (\AUTOEXEC.BAT is on everybody's machine so we'll  use  that).   The
      command to print the file is:

           PRINT \AUTOEXEC.BAT

      If  you  have  two  or  more printers you will need to set up queues
      with distinct names.  To create a new print  queue  start  QMAN  and
      type  'C'  for create.  Then select the "Base print queue" menu item
      which will cause a data entry screen to be displayed.  The only  two
      items  that  you  must fill in are the queue name (the first item on
      the screen) and the associated device name (the second  item).   For
      example,  to  create  a  queue  named  EPSON and associate it with a
      printer attached to TTC0:, you would  specify  EPSON  as  the  queue
      name  and  TTC0:  as the device name (don't forget to put a colon at
      the end of the device name).  TSX supports any  number  of  printers
      connected to a combination of parallel and serial ports.

      If  you  have  more  than  one print queue you must have some way to
      designate  which  queue  printed  output  is  to  be  directed   to.
      Suppose,  for  example, that your primary print queue named PRINT is
      connected to the parallel printer and a secondary queue named  EPSON
      is  connected  to  a  serial  port  printer.   By default, the PRINT
      command sends output to the PRINT queue.  If you want to direct  the
      output  to  a  different  queue, use the /QUEUE=name qualifier.  For
      example,  the  following  command  prints  a  file  on  the  printer
      associated with the EPSON queue:

           PRINT/QUEUE=EPSON \AUTOEXEC.BAT

      The  following  command  would  cause  output written by programs to
      device LPT2 to be directed to the EPSON queue:

           ASSIGN EPSON: LPT2

      See Chapter 7 for additional information about  the  ASSIGN  command
      and logical device names.


      8.3 Printing from DOS Programs

      Most  DOS  programs that provide printed output allow you to specify
      the DOS device to which the  output  is  to  be  directed.   Usually
      names  such  as  LPT1  and LPT2 are two of the choices.  By default,


      Chapter 8. Printing                                               51


      TSX associates the DOS device name LPT1 with the queue named  PRINT.
      So  if  you  can  select  LPT1 for printer output and define a PRINT
      queue, the program should be able to write  spooled  output  to  the
      printer without further intervention.

      Some  DOS programs allow you to specify an arbitrary device name for
      the printer.  In this case, the best  thing  to  do  is  to  specify
      "PRINT:"  (or  some  other  TSX queue name) as the print device.  If
      you do not have the choice of specifying an arbitrary  device  name,
      you  can use a TSX ASSIGN command to associate the logical name LPT1
      with any queue you  choose.   For  example,  the  following  command
      would  cause  output written to LPT1 to be directed to a queue named
      EPSON:

           ASSIGN EPSON: LPT1

      If you wish to place this command  in  your  LSTARTUP.CMD  file,  be
      sure   to  specify  "/SYSTEM"  after  ASSIGN.   See  Chapter  7  for
      additional information about the ASSIGN command and  logical  device
      names.


      8.4 Terminal Printers

      In   addition  to  supporting  printers  attached  directly  to  the
      computer through  serial  and  parallel  ports,  TSX  also  supports
      printers  attached  to the auxiliary printer ports of terminals used
      as workstations  to  TSX.   This  is  convenient  in  that  you  can
      configure  a  TSX  workstation, complete with a printer, and connect
      it to the TSX system using a single  serial  cable.   This  type  of
      arrangement  is  ideal  for  point-of-sale  terminals.   The TSXTERM
      program, that  turns  a  PC  into  TSX  workstation,  also  supports
      terminal  printers  (see Chapter 11 for additional information about
      TSXTERM).

      TSX provides  unequaled  support  for  attached  terminal  printers.
      Programs  can  directly  access  the  printer or use a spooled print
      queue.  Furthermore, TSX allows you  to  use  the  terminal  to  run
      programs  and  display  data  at  the  same  time  that the terminal
      printer is being used.  One user can  even  print  data  on  another
      user's terminal printer.

      To  tell  TSX  that you have a printer attached to the terminal, you
      can issue the command:

           SET TERM/PRINTER

      This command only remains in effect until you  log  off  or  TSX  is
      restarted.   If you want to permanently notify TSX that the terminal
      has an attached printer use TSGEN and set  the  "PRINTER"  attribute
      for the appropriate serial line to 1.

      When  you  notify  TSX  that a terminal has an attached printer, TSX
      creates a device whose  name  matches  the  name  of  the  terminal,
      except  that the the first two characters are TP instead of TT.  For


      Chapter 8. Printing                                               52


      example, if the terminal  attached  to  serial  port  TTB0:  has  an
      attached  printer, the device name of the printer is TPB0:.  You can
      then use the printer device name (TPB0:  in  this  example)  as  you
      would  use  any  other  device  name.   For  example,  the following
      command would cause output written to LPT1 to be directed to TPB0:

           ASSIGN TPB0: LPT1

      You can also create a spooled print queue  to  manage  output  to  a
      terminal  printer.   To  do  this follow the same steps described in
      Section 8.2 to create a queue and specify the terminal printer  name
      as the output device.


      8.5 Advanced Features

      The  TSX  printing  system  has  many  additional  features that are
      beyond the scope of  this  manual.   For  example,  you  can  define
      "forms"  that  have  attributes  such as margin sizes, page headers,
      and paper stock type.  The TSX spooling  system  automatically  will
      hold print requests until the specified paper stock is mounted.

      You  can  also  define  "logical"  print  queues that feed into base
      queues.  Using logical queues  you  can  set  up  the  TSX  printing
      system  so  that  there is a pool of printers and print jobs will be
      printed on the first printer that becomes available.







                                   Chapter 9

                        Command Procedures (Batch Files)





      9.1 Introduction

      Anybody who  has  configured  an  environment  for  a  PC  involving
      multiple  programs  and  databases  has  employed ".BAT" files.  TSX
      supports these DOS command  procedures,  and  additionally  supports
      advanced  native  command  procedures  which take the form of ".CMD"
      files.  This chapter reviews features which  make  the  TSX  command
      file processor flexible and programmable.

      Remember,   BAT  files  and  CMD  files  are  basically  text  files
      containing collections of commands, just like the commands you  type
      at  the  prompt.   You  can  test  out  commands interactively, then
      incorporate them into command procedures  once  you  understand  how
      they work.


      9.2 Invoking Command Procedures

      Invoking   a   command   procedure   from   the  prompt  is  usually
      accomplished simply by typing the name of the command procedure.

      There are a couple of ways  you  can  get  into  trouble  by  simply
      typing  a  name, then having TSKMON go out and find the command file
      or program you specified.  First,  suppose  you  have  command  file
      ARGLE.CMD,  which makes logical name assignments, copies files, then
      runs program ARGLE.EXE.  You can get that  command  procedure  going
      by  typing  ARGLE since TSKMON looks for ARGLE.CMD before ARGLE.EXE.
      But the command procedure can't simply have an ARGLE command  within
      it, to run ARGLE.EXE because it will end up invoking itself!

      The  way  around  this  problem  is  to  use  the RUN command, which
      explicitly tells TSX to run the program ARGLE.  The  entire  command
      procedure might read:

           COPY SY:IN.DAT DATA.NEW
           ASSIGN DATA.NEW IN:
           RUN ARGLE

      If  you  have  multiple program files named ARGLE, such as ARGLE.COM
      and ARGLE.EXE, you can specify the extension on the RUN command.




                                       53


      Chapter 9. Command Procedures (Batch Files)                       54


      Another sort of problem you can get into  with  simple  commands  is
      conflict  with  internal  commands.   Suppose  you  have  a  command
      procedure named SET.CMD:

           ASSIGN SET.LST OUTPUT:
           RUN SETRPT

      You can't invoke this procedure by typing SET, even if there are  no
      other  files  named  SET!  That's because SET is an internal command
      recognized by TSKMON.  Just typing SET will do the same thing  under
      TSX  as  it  does  under DOS: provide you with a list of environment
      variables.  Just as you can explicitly use the RUN  verb  to  run  a
      program,  you  can  use the "@" character to force TSKMON to realize
      you are invoking a command procedure:

           @SET

      Again, if you have SET.BAT  and  SET.CMD,  you  should  specify  the
      extension to avoid any possible confusion.

      Command  procedures  can  be  called from within command procedures.
      The  EXIT  command  is  used  to  return  to  the  calling   command
      procedure.

      Parameters  can  be  passed to command procedures by specifying them
      as separate words on the  command  line.   Parameters  are  assigned
      symbol  names  P1  through P8 (P0 is the name of the current command
      procedure itself).

      Command procedures can also get run in a  different  subprocess,  as
      if  you  had  switched to another window and executed them, with the
      SUBPROCESS command.  Finally, developers with full  TSX-32  licenses
      have  access  to  system services that can invoke command procedures
      from within programs.


      9.3 Background Batch Jobs

      One of the nice things about a multi-tasking operating  system  like
      TSX  is  that it can run more than one job at once.  This feature is
      especially useful when combined with batch  files  because  you  can
      execute  batch  files  as "background jobs".  A background batch job
      executes commands from a batch file that is  not  connected  to  any
      terminal.   The  listing  of  the  batch file that would normally be
      displayed at a terminal is instead written to a log  file  that  has
      the same name as the batch file but the extension ".LOG".

      The  BATCH command is used to initiate a batch job.  For example, if
      you had created a batch file  named  WORK.CMD  the  following  would
      start its execution as a background batch job:

           BATCH WORK

      If  you do not specify an extension with the file name for the BATCH
      command, TSX first looks for a file with the  extension  ".CMD"  and


      Chapter 9. Command Procedures (Batch Files)                       55


      if  no  such  file  exists  it  then tries to open the file with the
      extension ".BAT".

      When you issue a BATCH command  the  designated  batch  file  begins
      execution.   You  can  run  other programs or queue additional batch
      jobs while the batch job is running.  To  check  on  the  status  of
      executing  and  pending  batch  jobs  use  the BATCH command without
      specifying a file name.  For example, the  following  command  would
      display a list of all pending and executing batch jobs:

           BATCH

      By  default  TSX  does not notify you that a batch job has finished.
      However, you can request that  a  notification  message  printed  by
      using the "/NOTIFY" qualifier with the batch command.  For example,

           BATCH/NOTIFY WORK

      If  you  would  like  to have notification turned on by default, use
      QMAN to modify the BATCH queue (select  the  BATCH  queue  and  type
      'M') and specify 'Y' for the NOTIFY attribute of the queue.

      Screen  output  from  programs running as batch jobs is written to a
      file with the same name as  the  batch  command  file  but  with  an
      extension  of ".LOG".  You can specify a different name by using the
      "/LOGFILE=file" qualifier with the BATCH command.

      If you are submitting a long running batch job you may wish to  have
      it  execute  at  a  lower priority than interactive programs.  To do
      this, use the "/RUNPRIORITY=value" qualifier on the  BATCH  command.
      The  priority  value may be in the range 1 to 127 with higher values
      taking priority over  lower  values.   The  normal  interactive  job
      priority  is determined by the PRIDEF sysgen parameter whose default
      value is 50.  You can also use QMAN to  set  the  default  execution
      priority  for  jobs  submitted  to a batch queue.  To do this, start
      QMAN, select the batch queue, type "M" for Modify, and set  a  value
      for the RUNPRIORITY parameter.


      9.4 Branching: Labels and GOTO

      Like  BAT  files, CMD files support labels, but the preferred syntax
      is a  little  different.   In  TSX,  the  label  name  comes  first,
      followed  by  the colon (the way it is specified in most programming
      languages).  You transfer control to a label with the GOTO  command.
      Labels don't have to be the only thing on a line:

           TOP:ECHO WE ARE AT THE TOP
           RUN PROG1
           GOTO TOP


      Chapter 9. Command Procedures (Batch Files)                       56


      9.5 Symbols and Operators

      The  symbol  facility  described  previously  is used extensively in
      command procedures.  For example the INQUIRE command reads  keyboard
      input  and  creates  the  symbol  named.   You  can  use  the symbol
      substitution operator, apostrophe, to substitute a  symbol  for  its
      value in any command line.  For example:

           INQUIRE SYMA "Give me a word"
           DISPLAY SYMA is equal to 'SYMA'

      TSX  supports  numeric  symbols  as  well as string symbols.  The IF
      command has a complete set of operators to deal with both  types  of
      symbols.   You  can  also  use  numeric  operators in numeric symbol
      assignments:

           IF 'FILE' .EQS. "DATA.OUT" THEN PRINT 'FILE'
           COUNTER = 'COUNTER' + 1
           DISPLAY 'COUNTER'

      More information can be found under HELP IF and HELP Assignment.


      9.6 Conditionals: IF

      Commands can be conditionally executed by using the IF command.   An
      example:

           IF FILE .NES. "JUNK.DAT" THEN PRINT 'FILE'

      You  can combine the IF and GOTO constructs to conditionally execute
      entire sections of commands:

           IF LETTER .EQS. "A" THEN GOTO ADD
           IF LETTER .EQS. "E" THEN GOTO EXIT
           ECHO Invalid response, aborting.
           EXIT

           ADD:
             RUN ADD
             PRINT ADD.OUT
             EXIT
           EXIT:
             ECHO Goodbye
             EXIT


      9.7 User Interaction: DISPLAY and INQUIRE

      The DISPLAY command can be used to  display  strings  to  the  user.
      ECHO is a synonym for DISPLAY.

      INQUIRE  is  used  to get keyboard input from the user.  The command
      procedure shown above must have made use of INQUIRE  to  define  the
      symbol LETTER:


      Chapter 9. Command Procedures (Batch Files)                       57


           TOP:
           INQUIRE LETTER Enter E for EXIT, A for ADD:
           IF LETTER .EQS. "A" THEN GOTO ADD
           IF LETTER .EQS. "E" THEN GOTO EXIT
            .
            .
            .


      9.8 Seeing Commands

      The  VERIFY  setting  for your job controls whether you see commands
      as they are executed or not.  The commands

           SET VERIFY
           SET NOVERIFY

      control the current verify setting.  The DOS style ECHO ON and  ECHO
      OFF are also supported.


      9.9 Expression Operators

      A  number  of  operators  are  available  for  use  in  the  command
      language.  In comparisons and logical  operations  the  value  1  is
      returned for true and 0 for false.

      9.9.1 Numeric Operators

             +   Addition           -   Subtraction
             *   Multiplication     /   Division

      9.9.2 String Operators

             string1 // string2   Concatenate string2 to string1
             string[start:end]    Substring from position 'start' to 'end'

      9.9.3 Numeric Comparison

             .EQ.   Equal                   .NE.   Not equal
             .LT.   Less than               .GT.   Greater than
             .LE.   Less than or equal      .GE.   Greater than or equal

      9.9.4 String Comparions

      The following string comparisons are not case sensitive

             .EQS.   Equal                   .NES.   Not equal
             .LTS.   Less than               .GTS.   Greater than
             .LES.   Less than or equal      .GES.   Greater than or equal


      Chapter 9. Command Procedures (Batch Files)                       58


      9.9.5 Logical Operators

             .AND.  Logical AND
             .OR.   Logical OR
             .NOT.  Logical negation


      9.10 Lexical Functions

      Lexical  functions  may  be used in commands to perform a variety of
      functions involving strings and files.  All lexical  function  names
      start  with  a  dollar sign and have parenthesis enclosing arguments
      to the function.  The following is a simple example  that  uses  the
      $DATE  function  to  insert  the  current  date  into a string being
      printed.

           DISPLAY The date is $DATE()

      Full documentation of lexical functions is available by typing  HELP
      LEXICAL.  The following is a summary list of the lexical functions.

      $CHAR(value)  --  Generates a single ASCII character whose character
          code value is equal to the numeric argument.

      $CLOSE(channel) -- Close the specified I/O channel.   Use  $OPEN  or
          $CREATE to open a channel.

      channel  =  $CREATE(filespec)  --  Create  a new file.  The returned
          value of the function is an I/O channel number that may be  used
          with $WRITE and $CLOSE functions.

      $CWD() -- Return the current working directory specification.

      $DATE([format])  --  Return  the current date in the form "month dd,
          yyyy".  The optional "format" string can be used to  obtain  the
          date  in  other  styles.  The following operators may be used in
          the format string:

               Date operator           Information returned
               -------------  ------------------------------------------
                   %a         The abbreviated weekday name (Sun)
                   %A         The full weekday name (Sunday)
                   %b         The abbreviated month name (Dec)
                   %B         The full month name (December)
                   %c         The date and time (Dec 02 06:55:19 1979)
                   %d         The day of the month (02)
                   %j         The day of the year (335)
                   %m         The month of the year (12)
                   %w         The weekday number, from 0 for Sunday (0)
                   %x         The date (Dec 02 1979)
                   %y         The year of the century (79)
                   %Y         The year (1979)

          The $DATE function will also process any of  the  time  oriented
          format operators supported by the $TIME lexical function.


      Chapter 9. Command Procedures (Batch Files)                       59


      $ELEMENT(index,delimiter,stringlist)  --  Extract  the  string whose
          occurrence number  is  specified  by  'index'  from  the  string
          specified  by 'stringlist'.  The 'delimiter' parameter specifies
          the character that separates occurrences of the string.

      $EVAL(expression) -- Evaluate the expression and return its result.

      $EXISTS(filespec) -- Return 1 (true) if the specified  file  exists;
          return 0 (false) if the file does not exist.

      $FILMRG(file1[,file2])  --  Merge  together  two file specifications
          replacing any missing portions of 'file1' by  the  corresponding
          portion from 'file2'.

      $FILPRS(filespec,item)  --  Parse  (decompose)  a file specification
          into its component parts.  The values that may be specified  for
          'item'  are  NODE  (network  node  name),  DEVICE (device name),
          DIRECTORY  (directory  specification),  NAME  (file  name),  and
          EXTENSION (file extension).

      $HEX(value)   --   Convert   a   numeric  value  to  its  equivalent
          hexadecimal representation in the form "0Xnnnn".

      $ICHAR(string) -- Return a numeric value corresponding to the  ASCII
          character code of the first character in 'string'.

      $INSERT(string1,string2,position)    --    Insert   'string2'   into
          'string1' in  front  of  the  character  position  specified  by
          'position'.

      $ISALNUM(string)  -- Return 1 if all of the characters in the string
          are letters or numbers; otherwise return 0.

      $ISALPHA(string) -- Returns 1  if  all  of  the  characters  in  the
          string  are  letters (either upper or lower case).  Otherwise it
          returns 0.

      $ISCNTRL(string) -- Returns 1  if  all  of  the  characters  in  the
          string  have ASCII character code values in the range 0 to 31 or
          255.  Otherwise it returns 0.

      $ISDEF(string) -- 'string' should be a quoted string.  The  function
          returns  1  if  a symbol with this name is defined; otherwise it
          returns 0.

      $ISDIGIT(string) -- Returns 1  if  all  of  the  characters  in  the
          string are digits.  Otherwise it returns 0.

      $ISGRAPH(string)  --  Returns  1  if  all  of  the characters in the
          string are printable characters other than space.  Otherwise  it
          returns 0.

      $ISLOWER(string)  --  Returns  1  if  all  of  the characters in the
          string are lower case letters.  Otherwise it returns 0.


      Chapter 9. Command Procedures (Batch Files)                       60


      $ISPRINT(string) -- Returns 1  if  all  of  the  characters  in  the
          string  are  printable characters including the space character.
          Otherwise it returns 0.

      $ISPUNCT(string) -- Returns 1  if  all  of  the  characters  in  the
          string  are  printable  characters other than space, letters, or
          digits.  Otherwise it returns 0.

      $ISSPACE(string) -- Returns 1  if  all  of  the  characters  in  the
          string  are  either  space, form feed, newline, carriage return,
          tab, or vertical tab.  Otherwise it returns 0.

      $ISUPPER(string) -- Returns 1  if  all  of  the  characters  in  the
          string are upper case letters.  Otherwise it returns 0.

      $ISXDIGIT(string)  --  Returns  1  if  all  of the characters in the
          string are valid hexadecimal digits.  Otherwise it returns 0.

      $JOBINFO(item[,jobnumber]) -- The $JOBINFO lexical function  returns
          information  about  a  TSX-32 job.  Say HELP LEXICAL for further
          information.

      $LENGTH(expression)  --  Determines  the  number  of  characters  in
          'expression'.

      $LOCATE(substr,expression)  --  Locates the starting position of the
          first occurrence of the 'substr' substring within 'expression'.

      $LOGICAL(name)  --  Translate  a  logical   device   name   to   the
          corresponding  physical  device  and  directory  to which it has
          been assigned.

      $MESSAGE(status) -- Return the status message  that  corresponds  to
          the TSX error status code specified by 'status'.

      $MOD(value1,value2) -- Computes 'value1' modulo 'value2'.

      channel  =  $OPEN(filespec) -- Opens an existing file and returns an
          I/O channel number as the result.  The  channel  number  can  be
          used  with  $READ and $CLOSE functions.  The value 0 is returned
          if the file cannot be opened and the $CMDSTATUS  symbol  is  set
          to the error code.  Use $CREATE to make a new file.

      $PRIVILEGE(privname[,mode])  --  Returns  1  if  the  user  has  the
          specified  privilege;  otherwise  returns  0.   The   'privname'
          argument  indicates  which privilege item is to be tested (e.g.,
          "BYPASS", "OPERATOR",  "TERMINAL",  "UP1",  etc.   --  the  SHOW
          PRIVILEGE  command  will list the keywords); The 'mode' argument
          may be "AUTHORIZED", "CURRENT", or "SET" with  "SET"  being  the
          default.   The  'privilege' and 'mode' values should be enclosed
          in quote signs if literal values are used  (rather  than  symbol
          substitutions).

      record  =  $READ(channel)  --  Read  the next record from a file and
          return the record as the result of the function.


      Chapter 9. Command Procedures (Batch Files)                       61


      $REPEAT(string,count) -- Replicate 'string' 'count' times.

      $SEEK(channel,position)  --  Set  the  current  record  pointer   to
          'position' on a specified channel.

      $SEV(status)  --  Accepts  an  error status code as its argument and
          returns a value indicating  the  severity  of  the  error.   The
          following   values   are   returned:   0=success   (no   error);
          1=information message; 2=warning; 3=error; 4=severe error.

      $STRCMP(string1,string2) -- Performs a case sensitive comparison  of
          'string1'  with 'string2' based on the ASCII collating sequence.
          The result of the function is  -1  if  'string1'  is  less  than
          'string2',  0  if  'string1'  is  equal  to  'string2', and 1 if
          'string1' is greater than 'string2'.

      $STRIP(str1,str2) -- Remove from  'str1'  all  characters  that  are
          found in 'str2'.

      $STRLWR(expression)  --  Convert  all upper case characters to lower
          case.

      $STRUPR(expression) -- Convert all lower case  characters  to  upper
          case.

      $SYSINFO(item)  -- Returns information about the TSX-32 system.  The
          item  argument  is  a  string  that  selects   which   item   of
          information  is  to  be returned.  Type HELP LEXICAL for further
          information

      $TIME([format]) -- Return the current time in the  form  "hh:mm:ss".
          The  optional 'format' string can be used to produce the time in
          a different format.  The following operators can be used in  the
          format:

               Time operator                Information returned
               -------------     -----------------------------------------
                   %c            the date and time (Dec 02 06:55:19 1979)
                   %H            the hour of the 24 hour day (06)
                   %I            the hour of the 12 hour day (06)
                   %M            the minutes after the hour (55)
                   %S            the seconds after the minute (15)
                   %X            the time (06:55:15)
                   %t            the thousands of a second (357)

      $TRANSLATE(str1,str2,str3)  -- Each character in 'str1' is examined.
          If it matches any character in 'str2' the  character  in  'str3'
          which  is  at  the  same  position in the string as the matching
          character in 'str2' is placed back into the string.

      $TRIM(string) -- Removes trailing spaces from the string.

      $USER() -- Returns the user name of the current job.


      Chapter 9. Command Procedures (Batch Files)                       62


      $VALIDATE(str1,str2) --  Returns  the  index  number  of  the  first
          character  in  'str1'  that  is  not  in  'str2'.  If all of the
          characters in 'str1' are  found  in  'str2',  0  (zero)  is  the
          result of the function.

      stream  =  $WLDBGN(filespec)  --  Initiate a wildcard file scan with
          'filespec' as the wildcard pattern and return a "stream"  number
          than can be used with $WLDNXT and $WLDEND functions.

      $WLDEND(stream)  --  Terminate  a  wildcard  operation  and free the
          stream.

      name = $WLDNXT(stream) -- Get the next file name  that  matches  the
          pattern  specified  by  the  $WLDBGN  function  that started the
          stream.  Null is returned if there are no more matching names.

      $WRITE(channel,string) -- Write 'string' to the channel opened to  a
          file.







                                   Chapter 10

                              Multiuser Computing




      TSX  makes  it possible for several users to share the same computer
      at the same time.  And, each user can control up to 10 sessions  and
      execute  background  batch  jobs.   In  this  chapter  we  introduce
      various  aspects  of  TSX-Lite  that  relate  specifically  to   its
      multi-user and multi-tasking support.


      10.1 Workstations

      A  minimal TSX workstation consists of a keyboard and display device
      that allows an individual to use the computer.  A variety  of  types
      are supported.

      Both  MDA  (monochrome)  and  VGA  (mono  and  color)  adapters  and
      monitors can be used.  TSX also supports the Tseng  4000  super  VGA
      modes.   Hercules  graphics  for MDA and all 16 regular VGA graphics
      modes are supported.  CGA graphic adapters are not supported by  TSX
      although the CGA graphic modes may be used with VGA adapters.

      The  most  common  type of serial terminal used by TSX is the PCTERM
      terminal such as the Wyse 60.  If you have  a  PCTERM  terminal  you
      must  specify the terminal type to TSGEN (described later) before it
      will  work.   PCTERM  terminals  have  25  line  screens,  PC  style
      keyboards,  and  send  make and break codes (the same hardware codes
      sent to the  system  by  the  console  keyboard)  instead  of  ASCII
      characters.   They  connect  to  the  computer  through serial lines
      (i.e., COM ports).

      A more powerful  variation  of  the  PCTERM  terminal  supported  by
      TSX-Lite  is  made by RelAmerica.  Advanced escape sequences, color,
      and  built-in  support  for  TSX-32  make  these  units  well  worth
      considering.

      TSX  supports  ANSI  standard  terminals (i.e., TERMTYPE=ANSI).  The
      "ANSI" TSX  terminal  type  is  a  subset  of  VT-100.   DEC  VT-100
      terminals  have  attributes  such  as  scrolling regions and graphic
      character sets that  are  not  implemented  by  most  ANSI  terminal
      emulators.   You should use the ANSI terminal type when running with
      ANSI terminals or emulator programs that do  not  provide  the  full
      VT-100 control sequence emulation.





                                       63


      Chapter 10. Multiuser Computing                                   64


      DEC  ANSI  terminals such as the DEC VT100, 200, 300, and 400 series
      are also supported by  TSX.   See  HELP  SET  TERMINAL  for  a  full
      listing of the terminal types supported.

      The  TSX-Lite  product  also includes TSXTERM, our terminal emulator
      for PC's running DOS.  See Chapter 11,  starting  on  page  71,  for
      additional information about TSXTERM.

      The  full TSX-32 system also supports multi-console adapters.  These
      are the fastest, most DOS compatible types of workstations, and  the
      only   way   to   do   multi-user   graphics   with  a  single  CPU.
      Multi-console adapters allow multiple VGA monitors to  be  connected
      to  the  same computer running TSX-32.  Using multi-console adapters
      it is possible to have  many  users  efficiently  running  text  and
      graphic applications on the same TSX-32 system.

      TSX-32  also  allows  users to log in over ethernet from another TSX
      network node, Telnet connections, additional foreign terminals,  and
      the ability to write custom foreign terminal handlers.

      For  multi-user  access  to  TSX-Lite  you will need to use a serial
      terminal or a PC running TSXTERM.  Connecting the terminal  to  your
      COM  port  is mostly a matter of cabling.  See Section 2.6, starting
      on page 13, for information about connecting a  serial  terminal  to
      TSX-Lite.

      Pressing  Enter  (or  Return) should initiate a job on the terminal.
      The user at the terminal  and  the  user  at  the  console  are  now
      sharing  the computer system.  Both can simultaneously run programs,
      manage files, print output, and so  forth.   Welcome  to  multi-user
      computing!   The  patented  scheduling  algorithm  in  TSX  makes it
      practical to support dozens of terminals on  a  single  386  or  486
      computer  system.   Compared  to  LAN  networks,  this  can  be more
      economical by orders of magnitude, and you can  access  the  compute
      remotely over phone lines.


      10.2 Commands for the Multiuser Environment

      10.2.1 BATCH Command

      The  BATCH command starts execution of background batch jobs.  These
      jobs run without terminal interaction and  are  excellent  for  long
      running  programs.   The  form of the command used to initiate a new
      job is:

           BATCH file_name

      Where "file_name" is the name of the  command  or  BAT  file  to  be
      executed.   For  example,  the following command starts execution of
      "POVRUN.BAT" as a batch job:

           BATCH POVRUN.BAT


      Chapter 10. Multiuser Computing                                   65


      If you do not specify an extension with the file name for the  BATCH
      command,  TSX  first  looks for a file with the extension ".CMD" and
      if no such file exists it then tries  to  open  the  file  with  the
      extension ".BAT".

      Typing   "BATCH"  without  specifying  a  file  name  causes  status
      information about running and pending batch jobs  to  be  displayed.
      You  can  use  the  "/NOTIFY"  qualifier  to  cause  a message to be
      displayed at your terminal when the batch job completes.   The  QMAN
      program  can  also  be  used to display information about batch jobs
      and/or set parameters for batch jobs and queues.   See  Section  9.3
      on page 54 for additional information about batch jobs.

      Screen  output  from  programs running as batch jobs is written to a
      file with the same name as  the  batch  command  file  but  with  an
      extension  of ".LOG".  You can specify a different name by using the
      "/LOGFILE=file" qualifier.

      10.2.2 SHOW Commands

      TSX has a number of "SHOW" commands  to  display  information  about
      the  status  of  the  system.   The SHOW SYSTEM command displays the
      active jobs on the system.  Each task you control from the  console,
      and  each task the user at the COM port controls, is a separate job.
      Detached jobs such as the spooler and queue manager  are  also  jobs
      as  are  background  batch  jobs you submit.  Other commands you may
      want to try are JMAN, TMAN, SHOW USE, SHOW CACHE, SHOW  PAGING,  and
      SHOW MEMORY.

      10.2.3 STOP Command

      Normally  jobs initiate login by pressing Enter and log off with the
      LOGOFF (or OFF, or BYE) command.  However, you  can  "kill"  another
      job with a command exemplified by:

           STOP/ID=23

      The  actual  id value of the job is displayed by SHOW SYSTEM.  There
      are variants of the STOP command; see HELP STOP  for  details.   You
      can  also use the JMAN command to display a list of the current jobs
      and to stop jobs.

      10.2.4 SEND Command

      You can send a message to a user  on  another  line  with  the  SEND
      command.  An example:

           SEND/TERM=TTB0: "Hey, who are you using my modem?"

      Again, variants of the command are available; see HELP SEND.


      Chapter 10. Multiuser Computing                                   66


      10.2.5 PHONE Command

      If  you  wish  to  carry on an interactive conversation with another
      TSX user, you can call them by using the PHONE  command.   The  form
      of this command is:

           PHONE terminal_name

      where  you  should substitute an actual terminal device name such as
      TTB0 for terminal_name.  When you PHONE another user  a  message  is
      displayed  at  the  other user's terminal saying that they are being
      phoned.  The other user answers the phone call by typing "PHONE"  as
      a  command  without  specifying  a  terminal_name.   Either user can
      terminate the phone connection by pressing control-backslash.

      10.2.6 TUTOR Command

      Application developers and VARS who are contemplating using  TSX  as
      an  application  platform  will be pleased by the remote support and
      diagnosis capabilities of the TUTOR command.  TUTOR  allows  a  user
      to  "tutor" another terminal.  This synchronizes the two screens and
      keyboards so that you can see what  your  software  is  doing,  bail
      users  out  of tight spots, guide customers through the application,
      and so forth.  Any time  sharing  line  can  TUTOR  any  other  time
      sharing  line.   You  can  dial  into  a remote system and TUTOR the
      console from a modem  connected  to  a  TSXTERM  terminal,  tutor  a
      hardwired  VT100  from  a  hardwired  PCTERM terminal, and so forth.
      Multiple TUTOR connections  can  be  established  to  allow  you  to
      conduct  a  class  with  all  student  screens  synchronized  to the
      teacher.  To tutor another line, use the command

           TUTOR terminal_name

      where you should substitute an actual terminal device name  such  as
      TTB0  for  terminal_name.   Type  control-backslash to terminate the
      tutor session.


      10.3 Virtual Memory

      TSX is a full virtual memory, demand paging operating system.   This
      means  that  your  programs  can  access  large amounts of memory --
      potentially  more  than  the  physical  memory  installed  on   your
      computer.   This  feature is especially beneficial for modern 32-bit
      programs  which  can  be  many  megabytes  in  size  without   using
      overlays.

      Until   recently,   virtual   memory  operating  systems  were  only
      available on main-frame and super-mini computers such  as  the  VAX.
      Virtual  memory  is  especially  important  for  multi-user  systems
      because it allows many users to be running  large  programs  at  the
      same time.

      In  order  to  appreciate  how  virtual memory works it necessary to
      understand a few terms.  The "virtual  memory  space"  available  to


      Chapter 10. Multiuser Computing                                   67


      your  job  is  the area of memory that it may access.  Under DOS the
      directly  accessible  virtual  memory  space  is  limited  to  640Kb
      although  EMS  and  XMS  provide a means to access additional memory
      through the 640Kb area.  Under TSX,  32-bit  programs  can  directly
      access  a  virtual  memory  space of many megabytes.  This makes 386
      and 486 computers as powerful as VAX's for running large  scientific
      and commercial applications.

      The  SET  PROCESS/MAXMEM=size command is used to control the maximum
      amount of virtual memory space available to the job.

      When a program is running, all of its virtual memory  space  is  not
      necessarily  stored  in  physical  memory  (that is why it is called
      "virtual").  The hardware and  operating  system  work  together  to
      manage  the  virtual memory space and keep track of where the memory
      for a job is located.  Unlike the 8088 and 80286 computers, the  386
      and   486   processors   were  designed  to  handle  virtual  memory
      efficiently.

      The  CPU  organizes  memory  space  into  4,096  byte  units  called
      "pages".   The  set  of  pages  that  are  directly  accessible by a
      program at any instant of time is called the "working set"  for  the
      program.   Your virtual memory space may be larger than your working
      set.  Memory pages that are part of your virtual  memory  space  but
      not  in your working set may be located either in physical memory or
      in the system page file.  An attempt to access a memory  page  which
      is  not  in  your  working  set  causes a "page fault".  Despite its
      name, a page fault is not an error but rather  denotes  the  process
      that  TSX performs to add a memory page to your working set.  If the
      maximum allowed number of pages are in your working set when a  page
      fault  occurs,  the  oldest  entry  in the working set is removed to
      make room for the entry being added.  Page  faults  are  transparent
      to your application program -- they do not affect its operation.

      This  system of keeping only the most recently accessed pages in the
      working set works well because many programs contain  sections  that
      are  only  accessed  infrequently.   For  example, a word processing
      program may have an initialization portion  that  is  only  executed
      once  and  another  part  that is only used while actively printing.
      The pages that are not active are not part of the  working  set  and
      can be used by other programs.

      When  two or more users are running the same 32-bit program (such as
      the TSX command processor), only one copy of the  program  needs  to
      reside  in  memory.   TSX  "maps"  the virtual memory space for each
      user running that program to the common program image.   Only  local
      data cells used by the program need to be duplicated for each user.

      Normally,  TSX  performs automatic working set size adjustment based
      on the page fault rate.  If the number of  page  faults  per  second
      exceeds  the  value of the "WSDAUPRATE" sysgen parameter the working
      set  size  is  expanded  by  the  size  of  the  "WSDAUPAMT"  sysgen
      parameter.   If  the page fault rate is less than the "WSDADOWNRATE"
      sysgen parameter then the working set size is reduced by  the  value
      of   the  "WSDADOWNAMT"  sysgen  parameter.   You  can  disable  the


      Chapter 10. Multiuser Computing                                   68


      automatic  working  set  adjustment  process   by   specifying   the
      /NOADJUST  qualifier  with  the SET WORKING_SET command.  If this is
      done, the working set size is held at the maximum  value.   Use  the
      /ADJUST   qualifier   to   reenable   automatic   working  set  size
      adjustment.  This method TSX uses for managing  virtual  memory  and
      working  sets is state of the art and works well under varying loads
      with very little tuning.

      The SHOW MEMORY command displays  information  about  memory  space.
      The  SHOW  PAGING  command  displays page fault statistics.  You may
      type control-T at any time  to  display  your  current  working  set
      size.


      10.4 Data Caching

      TSX  performs  extensive data caching to optimize I/O to disk files.
      A "data cache" is an  area  of  system  memory  set  aside  to  hold
      recently  accessed  blocks  of  data  from  disk  files.  The system
      manager sets  the  size  of  the  data  cache  when  the  system  is
      generated  by use of the CSHSIZE sysgen parameter.  Each time a read
      operation is  performed  to  a  disk,  TSX  checks  to  see  if  the
      requested  data  is  stored  in the cache.  If so, the data is moved
      directly from the cache area and no I/O is performed.  If  the  data
      is  not  in the cache, the data is read from disk and stored in both
      the read buffer and the data cache.  When a write is done to a  disk
      file,  the  data  is updated in the data cache but is not written to
      disk until the file is closed,  a  system  service  is  executed  to
      flush  cache  data  to  disk,  or  a  sysgen-specified  time  period
      elapses.  When the data cache becomes full, the oldest  data  blocks
      in  the  cache are displaced to make room for more recently accessed
      data.

      The data caching system also attempts  to  "read  ahead"  data  from
      files   being  accessed  sequentially  so  that  the  data  will  be
      available in the cache by the time that the program requests it.

      In addition to data caching, TSX also has a separate cache  of  file
      directory  entries.  When you open a file TSX searches its directory
      cache and, if a file entry is found, the open is  completed  without
      having to perform any I/O operations.

      The   SHOW   CACHE   command   displays   statistics  about  caching
      operations.


      10.5 Logon Access Control

      TSX-Lite provides a "system password" feature that  you  can  enable
      for  dial-in lines.  When enabled, the caller is required to enter a
      password to gain access  to  the  system.   See  Section  2.6.2  for
      information about enabling the system password feature.

      An  optional  TSX-Lite  Security  Kit  is available to provide logon
      access control The Security Kit  includes  the  LOGON,  TSAUTH,  and


      Chapter 10. Multiuser Computing                                   69


      FPROTECT  programs.   The  TSAUTH program is used to manage the user
      authorization database.  The LOGON program is run from line  startup
      command  procedures  to  require  username  and passwords to log in.
      Accounts can be be customized by  granting  or  denying  privileges,
      resource  quotas, and given logon command procedures which lock them
      to an application.  The FPROTECT program allows the  system  manager
      to  limit access to disks, subdirectories, and individual files on a
      user-by-user  basis.   Users  can   be   given   read,   write,   or
      execute-only access to files.


      10.6 Event Logs

      An  "Event  Log"  is  an  ordered  set  of records describing events
      occuring within TSX or application programs.  Event  logs  are  most
      commonly  used  to  record  recently  occuring  events  so that if a
      problem occurs in the program generating the event log, a record  of
      recent  actions  is  available for examination.  However, event logs
      are not limited to diagnostic applications.

      An important use of event  logs  is  to  record  errors  or  unusual
      events  that  are  detected  by  TSX.   These  event logs are called
      "error logs".  You  can  check  to  see  if  any  errors  have  been
      detected  by  issuing  the SHOW ERRORS command.  If any of the error
      logs has some records, you may want to use the SHOW  EVENTS  command
      to examine the nature of the errors.

      The  SHOW  EVENTS  command is the primary command for displaying and
      controlling event logs.  When you  issue  this  command,  the  first
      screen  will  list  each event log file that is currently in use and
      show the number of records in it.  To  display  the  records  in  an
      event  log,  use  the  arrow  keys  to  highlight  the  event log of
      interest and then press Enter.  The display will  show  the  records
      in  the  event log and will be updated as new records are written to
      it.  Type Esc to return from the display screen to the main  screen;
      type  Esc  again  to  exit from SHOW EVENTS.  Type 'C' from the main
      screen to control which event logs are active.


      10.7 NetBIOS Support

      TSX supports the NetBIOS system services for establishing  sessions,
      sending  and  receiving  data  messages and datagrams.  This support
      allows cooperating programs running as separate jobs  under  TSX  to
      communicate  just  as  if  they were running on a network.  TSX also
      supports the NetBIOS services for file sharing and  record  locking.
      NetBIOS  support is a standard feature of TSX, so you do not have to
      install or  purchase  any  additional  software.   The  TSX  NetBIOS
      support  provides communication between cooperating programs running
      on the same TSX system.  It  does  not  support  networking  between
      separate   systems.    The  full  TSX-32  system  has  TCP/IP  based
      networking for communication between systems.

      Some DOS programs only do record locking for shared  data  files  if
      they  are  told  that the data files are on networked disks.  On the


      Chapter 10. Multiuser Computing                                   70


      other  hand,  some  DOS  programs  will  not  run  in  a   networked
      environment.   To  allow  the  use  of programs that need to be told
      they are in a networked environment, as well as those that will  not
      run  in a networked environment, an attribute may be associated with
      the program using the PMAN command to  control  which  programs  are
      told that they are running in a networked environment.

      If  PMAN  is used to install a program is with the DOSNET attribute,
      it will be told that all of its files are on networked devices.   If
      this  attribute  is  not  specified,  the  values  of the DOSNETFLAG
      sysgen parameter is checked.  If the value  is  1,  the  program  is
      told  that it is running in a networked environment; if the value is
      0, the program is told that it is not in  a  networked  environment.
      The default value for the DOSNETFLAG sysgen parameter is 0.

      If  your  software  can be installed for single user or network use,
      select the network option; this will  ensure  that  the  application
      allows two users to simultaneously access the same database.


      10.8 Mailboxes and Shared Memory Regions

      In  addition  to  the NetBIOS services, TSX also provides a facility
      called   "mailboxes"   for   exchanging   data   between   programs.
      Basically,  a mailbox is a logical device that functions as a "pipe"
      to store and transport data from one program to  another.   See  the
      TSX-32 User's Manual for additional information about mailboxes.

      Groups  of  32-bit  application programs can communicate efficiently
      by use of shared memory regions.  This concept allows  two  or  more
      programs  to  share the same area of memory so that data stored into
      it by one program is visible by all of the programs  in  the  group.
      This  is  especially  useful  for  real-time  applications.  See the
      TSX-32 System  Services  Manual  for  additional  information  about
      shared memory regions.







                                   Chapter 11

                                    TSXTERM




      If  you  have  another  computer available (even an old 8088 system)
      you can use it as a TSX workstation.  To do this you  will  need  to
      install  the  TSXTERM  terminal  emulator program on the workstation
      computer.   TSXTERM  is  provided   as   part   of   your   TSX-Lite
      distribution and is described in this chapter.

      TSXTERM  turns  any  PC  into one of the nicest workstations you can
      use with TSX.  The main reason for this is DOS  compatibility.   The
      TSXTERM  workstation  uses  a real DOS keyboard so the function keys
      and ALT, Shift, and Ctrl keys work just as they do  with  DOS.   The
      screen display also provides the full PC display character set.


      11.1 Installing TSXTERM

      To  install  TSXTERM,  create  a  directory  named  \TSXTERM  on the
      workstation computer and copy the TSXTERM.EXE file from  the  system
      directory  of  your  TSX-Lite  computer  (TSX32SYS)  to the \TSXTERM
      directory on the workstation computer.


      11.2 Using TSXTERM

      TSXTERM can  access  a  TSX-32  system  either  through  a  directly
      connected  serial  line  or  through a modem.  If you use a modem, a
      built in dialing directory  is  provided  to  automate  the  calling
      process  and, if the host system uses security, the logon process as
      well.

      Once you are connected, TSXTERM turns your PC into a DOS  compatible
      workstation  for accessing the TSX-32 system.  TSXTERM provides full
      color support, CGA graphics, enables use of  your  PC  printer,  and
      includes  file  transfers to and from the PC.  When you are finished
      using the TSX-32 system, you exit TSXTERM  and  return  to  the  DOS
      prompt to run other applications on your PC.


      11.3 Control Screens

      TSXTERM  is  controlled  by  single  letter  commands which are only
      recognized in conjunction with  a  set  of  shift  keys  called  the
      "wakeup  key  sequence".   Normally the wakeup key sequence consists
      of simultaneously pressing left control and  left  shift  while  you


                                       71


      Chapter 11. TSXTERM                                               72


      press  a  function  letter.  A summary of these commands is provided
      when you first start TSXTERM, and can be recalled  by  pressing  the
      wakeup keys and "H" for help.


      11.4 Configuring TSXTERM

      The  first  time  you  invoke  TSXTERM  it  will enter a setup menu.
      TSXTERM  is  configured  using  a  series  of  field  entry  screens
      selected  from  this  menu.  Your configuration, which is saved in a
      disk file named TSXTERM.INI, can be changed at any time by  pressing
      the wakeup keys, and S for setup.

      The  first time you use TSXTERM, you should enter the communications
      screen and specify the COM port and baud rate you wish to use.

      Next, enter the  "Customizations"  setup  screen.   It  contains  an
      importatnt  setting  which determines whether TSXTERM will initially
      operate in ASCII or TSXTERM mode.

      In "ASCII  MODE",  TSXTERM  emulates  an  ANSI  terminal,  but  this
      emulation  is  only  provided  to the extent necessary to log into a
      TSX system.  TSXTERM mode  is  the  normal  operating  mode  of  the
      program.   In  this  mode  the  program  emulates an advanced PCTERM
      terminal.

      Select ASCII mode unless you are  using  TSXTERM  with  a  hardwired
      connection  that will only be used for a TSXTERM connection.  In the
      case of a dedicated, hard-wired connection, select TSXTERM mode  and
      specify  TSXTERM  as  the  terminal type using TSGEN as described in
      Section 2.6.2 on page 14.

      When using TSXTERM in ASCII mode you can either manually type  modem
      commands  ("ATDT...",  etc.)  or  you  can  use  the TSXTERM dialing
      directory to connect to the host system running TSX.  Once you  have
      connected  and  logged  on  (entering  any password and user name if
      required), you should issue the following TSX command to shift  into
      TSXTERM mode:

           SET TERM/TYPE=TSXTERM

      If  you  purchase  the  optional  TSX-Lite  Security Kit and use the
      LOGON program with dial-in phone  lines,  then  you  should  specify
      your  user  name  and  password  in  the  TSXTERM dialing directory.
      TSXTERM will then connect to the host and  automatically  enter  the
      logon  information.   It  will also automatically shift into TSXTERM
      mode so that you do not need to enter the SET TERM command.

      You can also use the customization setup screen to change  the  keys
      which  wake  up  TSXTERM  to command mode.  The author, for example,
      prefers left ALT by itself.  Whatever keys  you  choose,  make  sure
      your  selection will not conflict with key combinations used by your
      applications.


      Chapter 11. TSXTERM                                               73


      The "Use dialing directory" field controls  whether  TSXTERM  starts
      out in the dialing directory screen or goes directly on-line.


      11.5 Using Modem Connections

      If  you  want to use TSXTERM to access the TSX system using a modem,
      you will probably want to select "Y" in the "start  in  phone  book"
      field  of  the  customization  field.   This causes TSXTERM to begin
      each session by presenting you with your phone directory.   You  can
      enter  the  dialing  directory  at  any  time by typing "D" with the
      wakeup keys.

      The first time you enter the dialing directory, you should type  "A"
      to  add  a  new  entry.   Fill  in  the name and phone number of the
      computer running TSX.  If the TSX system uses  logon  security,  you
      should  also  enter  the  username and password for the account into
      the dialing directory.  A field is  also  provided  for  the  system
      password  if  it  is  in  use  at the site.  You should also specify
      whether the dial-in line for the computer has been  permanently  set
      to TSXTERM terminal type.

      Other  fields  of the address book entry are optional.  The PORT and
      BAUD fields can be used to override  the  configuration  information
      if  multiple  COM  ports  on  the  PC  are connected to multiple TSX
      systems.  The  Internet  Address  field  is  used  to  access  fully
      licensed  TSX-32  systems over ethernet.  The note field is for your
      own informational notes.   The  tag  field  is  used  when  invoking
      TSXTERM  from  a .BAT file to ask it to immediately begin connecting
      to the specified entry.  For example, to connect to an  entry  whose
      tag is CUST23, you would use:

           TSXTERM C=CUST23

      Press  ESC  to  save  the  changes  and add the entry to the dialing
      directory.  You can edit the address  book  entry  at  any  time  by
      highlighting it and pressing "E".

      To  connect  to  a  computer,  highlight  the  entry  and  type "C".
      TSXTERM will dial the modem, wait for a connection, and then log  in
      using  any  username  and password you have specified in the address
      book.


      11.6 Using Direct Connections

      You can still use the dialing directory of TSXTERM for a hard  wired
      connection  if  you  want  TSXSTERM to enter a username and password
      for you.  If the logon program is not used, or if you want  to  type
      the  username  and  password  yourself, select "N" for the "start in
      phone book" setup field.  TSXTERM will pause when it  first  starts,
      then  immediately  enter  terminal  emulation  mode when you press a
      key.


      Chapter 11. TSXTERM                                               74


      11.7 Printer Support

      TSX supports printers attached to TSXTERM terminals in the same  way
      as  printers  attached  to  serial terminals.  See Section 8.4, page
      51, for a  description  of  terminal  printers.   To  configure  the
      TSXTERM  attached  printer, select the printer screen from the setup
      menu and specify  the  port  (parallel  or  serial)  to  which  your
      printer  is  connected.   If  the  printer  is serial, you must also
      specify the baud rate.


      11.8 Background File Transfer

      One  of  the  powerful  features  of  TSXTERM  is   the   integrated
      background  file  transfer.   This  means file transfers are done in
      the background while you  continue  to  use  the  host  TSX  system.
      Suppose,   for   example,  you  have  a  data  file  which  must  be
      manipulated by a program running under DOS  on  your  PC.   You  can
      download  the  data  in  background mode while you continue your TSX
      based work.  Just type "F" in conjunction with the  wakeup  keys  to
      activate the file transfer pop-up window, and issue a command like:

           GET DATA.NOW

      When  your data file has been transferred, exit TSXTERM and run your
      DOS application.  Rerun TSXTERM to upload your  modified  data  back
      to  the  "file server" TSX system using a SEND command from the file
      transfer window.

      The file transfers can be initiated by the TSX  system  as  well  as
      the  DOS  based PC using the WSCMD command; see Section 14.141, page
      170.  This allows file  transfers  to  be  integrated  into  command
      procedures  so  that  field  personnel of a service organization can
      (and do) upload daily reports without even knowing how.

      Command line options also allow TSXTERM to be  run  from  BAT  files
      under  DOS.   One, "C", calls the specified dialing directory entry.
      "S" and "R" are used to send and receive files.  Type TSXTERM ?   to
      see a full list.


      11.9 Session Logging

      You  can  create  a log file on your PC documenting your TSX session
      using the TSXTERM session logging  feature.   Type  the  letter  "L"
      with the wakeup keys to activate the logging pop-up window.







                                   Chapter 12

                               System Management




      One  of  the  things  that  distinguishes  TSX from other multi-user
      systems is ease of management.  Even systems with  dozens  of  users
      do  not  require  that  anybody  sacrifice  hours per week being the
      "system manager".   The  operating  system  mostly  manages  itself.
      However,  TSX provides a large number of options that you can use to
      customize and tune for best performance.


      12.1 Overview of System Startup

      Before we plunge into any  management  details  let's  get  a  broad
      picture  of what happens between the time that you type RUNTSX under
      DOS and log in your first interactive session under TSX.

      The primary purpose of the RUNTSX program is to read  the  TSX32.SYS
      file,  which  contains the executable code for the operating system,
      into  high  memory,  switch  your  processor  from  "real  mode"  to
      "protected mode", and jump into the TSX code.

      Next  it  begins  execution  of  the  "startup  job"  which performs
      various  startup  functions,  then  logs  off.   It  does  this   by
      executing the command procedure STARTUP.CMD.


      12.2 Startup Command Files

      The  first  thing  that  STARTUP.CMD does is to run a program called
      MAKELOAD which  uses  the  system  option  settings  to  generate  a
      secondary  command  procedure called TSXLOAD.CMD.  Executing TSXLOAD
      is the second  job  of  the  startup  procedure.   TSXLOAD  contains
      commands  to load terminal support handlers for TSXTERM, PCTERM, and
      Relisys terminals.  TSXLOAD  also  starts  detached  jobs  like  the
      spooler and queue manager for the printing system.

      The  next  step  is to execute the INSTALL.CMD command procedure, if
      it exists.  This command procedure, which is created for you by  the
      program  manager  utility  PMAN,  customizes  the  way  TSX  handles
      various software packages you have on your system.  Section 2.5  and
      Chapter  4 discuss many attributes that can be set when a program is
      installed using PMAN.

      Next  the  startup  job   executes   a   command   procedure   named
      LSTARTUP.CMD,  for  "local startup" functions.  This is the file you


                                       75


      Chapter 12. System Management                                     76


      can edit to place system wide logical names and symbols.  This  file
      is analogous to the DOS AUTOEXEC.BAT file.

      Finally   the   startup  job  executes  a  command  procedure  named
      PROTECT.CMD.   This  procedure  establishes  file   protection   and
      shadowing.  It is managed using the FMAN program.


      12.3 System Customization

      12.3.1 Line Startup Procedures

      Each  time  sharing  line  (the  console being one, the serial lines
      being others) has an associated startup command  procedure  that  is
      executed  each  time  the  line is initialized.  If you log off of a
      line (by use of the OFF command) the startup  command  procedure  is
      executed  when  you  press  Enter  to log on again.  By default, all
      lines execute the same command procedure  named  SY:START.CMD.   You
      are  welcome  to  edit  START.CMD.   You  can  also  change the line
      parameters to specify a different startup  command  for  each  line.
      See  Section 2.6.2 for information about setting a different startup
      command file.

      If you have purchased the TSX-Lite Security Kit,  you  may  want  to
      run  the  LOGON  program  to  force  users  to enter a user name and
      password to gain  access  to  the  system.   To  do  this  edit  the
      START.CMD file and insert the following command:

           R LOGON

      The  TSAUTH  program  that  is  part  of the Security Kit is used to
      manage the list of authorized users.   TSAUTH  also  allows  you  to
      specify  a  secondary  start-up  command  procedure that is executed
      when a user logs on; this command procedure is  based  on  the  user
      name.   For  example,  user  GEORGE  may  have the following command
      procedure:

           ECHO Hello George, just a moment
           RUN MAKEDISK
           ECHO Thanks George, bye.
           LOGOFF

      The only thing that George needs  the  computer  for  is  to  run  a
      program  that  makes  software  distribution  disks for his company.
      However, user SHANNON manages the office  and  wants  to  start  out
      running  the  office  management  menu.  Her login command procedure
      has:

           CD C:\OFFICE
           RUN OMENU

      Note that you can have different  startup  command  files  for  each
      line  so  you can have dial-in modem lines run LOGON but not require
      this for the console.


      Chapter 12. System Management                                     77


      12.3.2 User Authorization

      The program TSAUTH (which is part of the TSX-Lite Security  Kit)  is
      used  to  manage  the  authorized  users.  TSAUTH creates a database
      named SY:TSXUAF.TSX containing the list of usernames which  can  log
      into  the  system.   TSAUTH  can  be  run from the command prompt or
      accessed from the system management menu.

      TSAUTH is a self explanatory, user friendly program.  After you  run
      it,  start  out  by typing "C" to make a copy of the default record.
      This enters a data  entry  screen  which  is  used  to  specify  all
      attributes of the new user such as their name and password.

      Note  that  you  edit  the  default  record  to  match  your typical
      authorized user to make the authorization process more convenient.

      It is up to you, as the system manager, to create the login  command
      procedure  for  the  user.   You  may  want  to  create  a  separate
      directory for each user and place a CD command in their  login  file
      to  start them out in their home directory.  Since the login command
      procedure simply contains commands which are executed when they  log
      in,  they can customize their own environment (with symbols, logical
      names, running programs, and so on) by editing their  login  command
      file.

      You  also  use  TSAUTH  to limit use of system resources such as the
      maximum memory space that can be used.  There are an  extensive  set
      of  privileges  which specify what types of functions you will allow
      each user to perform.  If you do not use the login  mechanism,  each
      user has full privileges.

      12.3.3 System Wide Settings

      So  far  we  have discussed customizations based on individual users
      or individual lines.  System wide customizations are placed  in  the
      LSTARTUP.CMD  command  procedure.   Here  you  can  specify  a  PATH
      command to replace or augment the search path specified  under  DOS.
      When  defining  a  system-wide  path,  you should use a "SET/SYSTEM"
      command rather than a PATH command which defines a search  path  for
      the  current  job only.  The following is an example of a command to
      set up a system-wide search path:

           SET/SYSTEM PATH C:\TSX32SYS;C:\WATCOM

      You may also wish to place some ASSIGN commands in the  LSTARTUP.CMD
      file  to define some logical device names for the entire system.  Be
      sure  to  use  the  /SYSTEM  qualifier  to  make   the   assignments
      system-wide.  Here are some examples:

           ASSIGN/SYSTEM C:\INVOICES\CURRENT\ CURINV:
           ASSIGN/SYSTEM EPSON: LPT2:

      Either  of  these  commands can be overridden for a specific user by
      use of an  ASSIGN  command  without  the  /SYSTEM  qualifier.   User
      specific   ASSIGN  commands  can  be  placed  in  the  startup  file


      Chapter 12. System Management                                     78


      associated with the line or  the  user  name  (assuming  TSAUTH  and
      LOGON  are  used).   Debi  could  redirect  printer  output  to  the
      terminal printer attached to her terminal with:

           ASSIGN DEBI: LPT2:

      Similarly  you  can  establish  system  wide  symbols   to   provide
      shorthand notations for all your users:

           TOCUR :=== CD C:\INVOICES\CURRENT\
           INSPECT :=== E32/BORDER/READONLY

      The  three  equals  signs  denote  system-wide  symbols which can be
      overridden by personal symbols specified with two equals signs.


      12.4 System Tuning

      12.4.1 Introduction

      While there are hundreds of tuning parameters you can specify  using
      TSGEN,   most   of   them   are  only  used  in  highly  specialized
      circumstances.  Feel free to browse the tuning parameters  and  read
      help  screens  to get a feel for the ability of the operating system
      to adapt to different needs.  Fully  supported  customers  have  the
      benefit  of  S&H  Technical  Support  to  guide  them to the correct
      parameter if a program does not run correctly or the system  is  not
      running  at  peak  performance.  We will draw special attention to a
      few of the most critical tuning parameters here.   See  Section  2.4
      on page 9 for information about using the TSGEN program.

      12.4.2 CSHSIZE: Cache size

      Under  Data  Caching  Parameters,  CSHSIZE  controls  the  amount of
      memory that's allocated for a system cache.   If  you  only  have  4
      megabytes  of  memory  you should probably leave this at the default
      of 1000 512 byte blocks (half a megabyte).  In  fact,  if  the  SHOW
      MEMORY  command  says  there  is  less  than 800K available for user
      jobs, you may want to decrease  the  cache  size  to  free  up  more
      memory  for running programs.  But if you have more than 4 megabytes
      of memory you should use about 25%  of  your  memory  for  a  cache.
      Example:  on  an  8  meg system use 2 megs.  1 meg = 2000 blocks, so
      set CSHSIZE to 4000.  See Section  10.4,  page  68,  for  additional
      information about data caching.

      12.4.3 VMAXJOBS: Job limit

      Under  Job  Limit  Parameters, VMAXJOBS controls the total number of
      jobs allowed on your system.  Each process window and each  detached
      job  (Spooler, Queue Manager, Window Print, and batch jobs) count as
      a separate job.  The default value of 12 can  usually  be  decreased
      somewhat  for  a  single user system.  The benefit is that memory is
      freed up for other uses as VMAXJOBS is decreased.


      Chapter 12. System Management                                     79


      12.4.4 DOWINPRT: Window Print

      Under Optional System  Components,  DOWINPRT  controls  whether  the
      window  print  process  is detached when the system boots.  Set this
      to 1 if you want the Print Screen key to be active or 0  if  you  do
      not  use  this feature.  See Section 14.85, page 146, for additional
      information about screen printing.

      12.4.5 DOQUEUES: Queue Manager and Spooler

      Under Optional System Components, you can set DOQUEUES to 0  if  you
      do  not  use  batch  jobs,  print jobs, or require spooled output to
      printers.   Allowing  programs  direct  access  to  the  printer  is
      advisable  only on a single user system, and will cause your program
      to pause  until  printing  is  completed,  whereas  spooling  allows
      multiple  users  to  simultaneously use the same printer and accepts
      data, allowing the program to continue running, before the  data  is
      actually printer.

      12.4.6 MAXP0MEM: Maximum Memory Space

      The  maximum  virtual  memory  space  available  to  each program is
      controlled  by  the  MAXP0MEM  sysgen  parameter.   This   parameter
      specifies  the  size in 1k units and the default value is 8192 which
      corresponds to 8 MB.  If you run  programs  that  need  more  memory
      space  than  this  you  can  increase the MAXP0MEM parameter up to a
      maximum of 32768 which corresponds to 32 MB.  The value of  MAXP0MEM
      limits  the  total  memory  space  available  to  each  program  and
      includes both the  640Kb  low  memory  area  and  any  EMS  and  XMS
      (extended)   memory  used  by  the  program.   The  disadvantage  of
      assigning a very large number to MAXP0MEM is that some programs  use
      all  available  memory space.  With TSX's virtual memory system they
      will be allocated more memory than they actually need and  this  can
      result in excessive memory paging and poor performance.

      12.4.7 PGFILSIZ: Page File Size

      Under  System  Memory Parameters, PGFILSIZ controls the number of 4K
      pages which can be stored in the  system  page  file,  PAGEFILE.TSX.
      The  page  file  is  used  to implement virtual memory: memory pages
      which can not fit into the working set for  the  job  (the  physical
      memory  in  use) are written to the page file.  Increase this if you
      must run memory intensive programs that cause the page file to  fill
      up.   Decrease  this  if you only run modest programs and don't want
      disk space wasted by the page file.  The  SHOW  PAGE  command  (also
      available  from  the  system commands menus) displays various paging
      statistics, including how much of the page file has been used.

      12.4.8 POOLSIZEN: System Pool Space

      Under  Pool  Space  Parameters,  POOLSIZEN  determines  the  initial
      allocation  of system memory pool space.  The pool is memory used by
      TSX while it is running.  If TSX runs out  of  pool  space  it  will
      crash.   However,  if  your system runs for a long time and the SHOW
      MEMORY command shows plenty of pool space  left  (say,  over  70,000


      Chapter 12. System Management                                     80


      bytes)  you  may  want  to  decrease  POOLSIZEN  a little to free up
      memory for other purposes.

      12.4.9 RAMDISKSIZ: Virtual Disk

      TSX has a virtual disk driver built into the  system.   To  activate
      it  go  into  the  RAM Disk Parameters screen and assign the virtual
      disk a drive letter and specify the number of blocks  of  memory  to
      allocate for the disk.







                                   Chapter 13

                                Troubleshooting




      This   chapter  discusses  some  of  the  problems  that  you  might
      encounter  when  installing  or  using  TSX-Lite.   Hopefully,  your
      problems  will be few and you will be able to resolve them yourself.
      However, if you need additional assistance S&H Computer Systems  has
      an  outstanding  support team that is there to help you.  Registered
      TSX-Lite users  receive  90  days  of  support  via  mail,  FAX,  or
      CompuServe  at  no  additional  cost.   Telephone  support  is  also
      available; see Section 15.3 for details.

      Most problems that occur when using TSX-Lite  fall  in  one  of  the
      following categories:

        . Installation  problems caused by the presence of TSR programs in
          AUTOEXEC.BAT or device drivers (such  as  HIMEM.SYS)  loaded  by
          CONFIG.SYS  that  interfer with TSX getting started and entering
          protected mode.  These problems can be  avoided  by  creating  a
          "stripped   down"  CONFIG.SYS  and  AUTOEXEC.BAT  for  use  when
          starting TSX.

        . Hardware conflicts caused by aspects of the  computer  that  are
          used  by  TSX running in protected mode but not encountered when
          running a simpler system like DOS.  For example, computers  have
          an  inaccessible area of memory used to shadow the BIOS.  If you
          have problems getting TSX started and your  BIOS  give  you  the
          option, try disabling BIOS shadowing.

        . DOS  programs  that do "dirty" tricks such as accessing portions
          of the operating system or  BIOS  itself.   TSX  tries  hard  to
          support  all  DOS  programs, but there are some which are simply
          not  suitable  for  use  with   a   multi-user,   protected-mode
          operating system.

      If  your  system  is  not  performing  properly  use the SHOW ERRORS
      command to see if any errors have been  recorded.   If  any  of  the
      error  counts  are  non-zero, use the SHOW EVENTS command to examine
      the error logs.

      The  following  is  a  list  of  potential  problems  and  suggested
      solutions.






                                       81


      Chapter 13. Troubleshooting                                       82


      13.1 RUNTSX Fails During TSX Start

      The  RUNTSX  program may have trouble loading TSX into "high memory"
      if you have a HIMEM.SYS  type  driver  loaded.   Try  renaming  your
      CONFIG.SYS  and  AUTOEXEC.BAT  to  be  sure  you  are rebooting to a
      basic, naked DOS machine.  This should fix the problem.


      13.2 Keyboard Is Dead

      Your  system  seems  to  boot  TSX,  going  all  the   way   through
      initialization   to   a   message  announcing  that  the  system  is
      available.  However, you press the return key and  nothing  happens.
      It's as if your keyboard is dead, but it works under DOS.

      Reboot,  and  at  the  DOS  level,  use TSGEN and select "Set Tuning
      Parameters" from the main menu, then "Console Keyboard  Parameters".
      Set  the value of parameters KBDELAY1 through KBDELAY4 all to a very
      high value, such as 10,000.  Then bring the system back to TSX  with
      the  RUNTSX  program.   This  should  bring  your  keyboard to life.
      Chances are that only KBDELAY4 needs to be  set,  and  that  smaller
      values   will  work.   These  delays  only  occur  when  programming
      keyboard LEDs so don't be too concerned at the high values.


      13.3 Serial Terminal Does Not Work

      As explained  earlier,  TSX-Lite  can  be  accessed  both  from  the
      console  display  and  keyboard  and  from  serial terminals (and/or
      modems) connected to COM ports.  If you connect  a  serial  terminal
      to a COM port and it does not operate, check the following things.

        . Is  the cabling good.  Do you need a "null modem" which reverses
          signal lines 2 and 3?

        . Does the baud rate of the terminal  match  that  for  which  the
          line  is  genned?   The  default TSX baud rate is 9600.  You can
          use a SET ttcuu:/SPEED=xxx/PERM command to change the line  baud
          rate without regenning.

        . Has  the  line  been  genned for the correct terminal type?  The
          default is ANSI.  A TERMTYPE of PCTERM must be  set  for  PCTERM
          type terminals.

        . If  you  are  using  TSXTERM  on a hard-wired line make sure the
          line is genned with TERMTYPE of TSXTERM.  Also  make  sure  that
          TSXTERM is not operating in ASCII mode.

      If  none  of  these  checks  reveal  problems, try using the TSX SPY
      command to check for characters being received from the  line.   The
      following  is  an  example  of  a command to spy on characters being
      received from line TTB0:

           SPY/INPUT/HEX/BINARY/PHONE TTB0:


      Chapter 13. Troubleshooting                                       83


      See Section 2.6 for further information about setting up  COM  ports
      and  Section  2.6.5 for more information about using SPY to diagnose
      serial line problems.


      13.4 Screen is Corrupted after Session Switch

      If you switch between a graphics  application  and  another  session
      and  find  that the graphics screen is not correct when you reselect
      it, then the most likely cause of the problem is that  a  super  VGA
      mode  is  being  used that is not supported by TSX-Lite.  Currently,
      the only super VGA modes supported by TSX-Lite are those offered  by
      the  Tseng  4000  and  Paradise  512 video adapters.  Other adapters
      that offer super VGA modes may  be  used  with  TSX-Lite  only  when
      running  in  the  standard VGA modes.  If you are using Windows with
      TSX-Lite you should select standard VGA as the adapter type.


      13.5 Mouse Does Not Work

      TSX supports the Microsoft serial mouse (or other  compatible  mice)
      attached to a COM port.  It does not support bus mouse controllers.

      To  use  the  mouse,  connect  it  to  a  COM port and use an ASSIGN
      command of the following form to  associate  the  MOUSEPORT  logical
      device name with the appropriate serial port:

           ASSIGN TTcuu: MOUSEPORT

      Where  "TTcuu" should be replaced by the appropriate TSX serial unit
      name such as TTB0 (COM1), TTC0 (COM2), TTD0 (COM3), or TTE0  (COM4).
      Note  that  the  device name MUST end with a colon.  See Section 2.7
      for additional information about setting up the mouse.  See  Section
      14.140  for  information  about  setting  up  the mouse for use with
      Windows under TSX.


      13.6 TSX Does Not Answer Incoming Calls

      If you have a modem connected to a TSX serial line  and  it  is  not
      answering  incoming  calls  check  three  things:  (1)  is  the line
      generated as a "Phone" line; (2) are you using a  cable  with  modem
      control  signals  (DTR  and  carrier  detect);  and (3) is the modem
      configured to answer the phone --  the  "S0"  modem  setup  register
      must  be  set to a non-zero value.  See Section 2.6.3 on page 17 for
      additional information about setting up phone lines.


      13.7 Trash Characters During Logon and Screen Refresh

      If some "trash" characters (large  stars  or  other  things)  appear
      when  you  log  onto  TSX  from  a  serial terminal or when you do a
      session window switch, you probably need to set your  terminal  type
      to  ANSI.  The VT100 terminal type is appropriate for terminals that
      support DEC VT-100 control sequences.  When VT100 terminal  type  is


      Chapter 13. Troubleshooting                                       84


      selected,  TSX  sends  certain  control  codes  during logon, window
      refresh,  and  window  clear   operations   that   cause   spurrious
      characters  to  appear if the terminal cannot handle the full VT-100
      control set.  See Section 2.6.2 on page  14  for  information  about
      setting terminal types.


      13.8 Lost Characters or Retries During File Transfers

      If  you  are using a communications program to send or receive files
      using a protocol like  Z-modem  and  find  that  many  communication
      errors  or  retries  are  occuring,  the first thing that you should
      check is that you have specified the correct type  of  flow  control
      handshaking  for  the  COM  port.  The default TSX flow control uses
      XOFF  (control-S)  to  stop  transmission  and  XON  (control-Q)  to
      restart  it.   Most  high-speed  modems  use the RTS/CTS signals for
      flow control rather than XON/XOFF.  If your modem is  using  RTS/CTS
      flow  control  you  should follow the procedure described in Section
      2.6.2 on page 14 and set the HANDSHAKING parameter to RTSCTS.

      If  you  have  the  handshaking  set   correctly   and   are   still
      experiencing  character  losses,  you  should check the type of UART
      communication controllers installed in  your  computer.   There  are
      two  common  types: 16450 UART's and 16550 UART's.  The 16550 UART's
      are highly recommended  for  use  with  multi-tasking  systems  like
      TSX-Lite  because  they contain a 16 character buffer that can store
      characters while TSX is performing other functions.


      13.9 Unable to Run TSR Programs

      If you try to run a TSR program as a TSX command  you  will  receive
      the  error  mssage:  "You  must  use  the  DOS  command  to  run TSR
      programs".  This means that in order to run this  program  you  must
      first  use  the  TSX  "DOS"  command to invoke COMMAND.COM, and then
      start the TSR program from within  COMMAND.COM.   You  can  use  the
      EXIT   command   to   exit  from  COMMAND.COM  to  the  TSX  command
      interpreter.  See Section 4.5 on page 32 for additional  information
      about running TSR programs.


      13.10 Queue Manager and Spooler Are Gone

      First  make  sure  that the GEN parameter DOQUEUES is set to 1.  You
      can type STARTQUE yourself from the TSX command  prompt  to  restart
      the queue manager and spooler.

      Sometimes  an  error  in  the  queue  manager or spooler program, or
      corruption of the queue manager database, causes the  queue  manager
      and  spooler  to abnormally terminate.  You may be able to determine
      some  information   by   typing   the   files   SY:SPOOLER.LOG   and
      SY:QUEMAN.LOG.   For  example,  perhaps the system killed these jobs
      because the system page file was filling up (increase GEN  parameter
      PGFILSIZ).


      Chapter 13. Troubleshooting                                       85


      If  there  is  no  obvious solution, try deleting files SY:SPOOL.SYS
      and  SY:QUEMAN.SYS.   SPOOLER.SYS  is  only  used  to  hold  program
      printer   output   which   is  being  implicitly  spooled.   However
      QUEMAN.SYS contains information about all the queues and  forms  you
      have  set  up  using  QMAN or SET QUEUE and SET FORM commands.  Note
      that QMAN automatically maintains a file named  QINIT.CMD  with  the
      SET  QUEUE or SET FORM commands needed to rebuild your queues if you
      ever loose them.  If you use commands, not QMAN,  to  alter  queues,
      you must maintain QINIT.CMD yourself.

      After  deleting these two system files restart the spooler and queue
      manager by typing STARTQUE.  Wait a minute, then type  QINIT.   This
      should solve the problem.


      13.11 Slow Performance -- Excessive Memory Paging

      TSX  is a virtual memory operating system and allows programs to use
      more memory than is physically installed in your computer.   When  a
      program  uses  more  memory than installed, TSX reads and writes the
      extra memory pages to a "page file" on disk.  If  you  run  programs
      that  use  much more memory than actually installed in your computer
      your performance may be poor because  TSX  is  being  forced  to  do
      excessive   paging   operations.    The  MAXP0MEM  sysgen  parameter
      specifies the maximum number of k-bytes of virtual memory that  each
      program  may  use.   You  can  reduce this parameter or use PMAN and
      install a program with the MAXMEM parameter set to a smaller  value.
      Note,  some  programs  use  all  available memory even if they don't
      actually need that much memory so limiting their memory  space  will
      benefit  system  performance  without restricting program operation.
      You can use the SYSMON program to monitor memory paging.







                                   Chapter 14

                              TSX Command Summary




      This chapter is a quick reference to  TSX  commands.   Much  of  the
      information here is also available from the on-line HELP facility.

      A  detailed  guide  to  the  use  of  these commands is found in the
      TSX-32  User's  Manual  which  may  be  purchased  separately   (see
      REGISTER.DOC for ordering information).

      In this summary, the following conventions are used:

        . Items in square brackets are optional.

        . Items in lower case should be replaced by an appropriate value.

        . Dates  and  times  used with qualifiers such as /SINCE, /BEFORE,
          and /AFTER, must be  in  the  format  dd-mmm-yyyy:hh:mm:ss.   If
          left  out,  the  date  defaults to the current date and the time
          defaults to midnight.  If both date and time are left  out,  the
          command  assumes  midnight  of  the  current  day.   Here  is an
          example qualifier: /SINCE=5-MAY-1993.

        . Qualifiers preceded by [NO] are  negatable.   So,  for  example,
          you  may  toggle  process  monitoring  for  your  job  with  SET
          PROCESS/MONITOR and SET PROCESS/NOMONITOR.

        . Qualifiers followed by the word "Default"  in  parentheses  need
          not  be  specified  except  to  toggle a setting previously made
          with the  negated  form  of  that  qualifier.   If  a  negatable
          qualifier   is   specified   as   "default",   then  the  normal
          (non-negated) form of that qualifier is the default.

        . Qualifiers which include "=(files)" will accept a list of  files
          enclosed in parentheses and separated by commas.













                                       86


      Chapter 14. TSX Command Summary                                   87


      14.1 ALLOCATE

      The  ALLOCATE  command  allocates  a device for exclusive use by the
      job.

      Syntax:

           ALLOCATE device

      Example:

           ALLOCATE TTB0:

      The ALLOCATE command allocates one or  more  devices  for  exclusive
      use  by  your  job.  Other users will be denied access to the device
      until you use the DEALLOCATE command to release the  device  or  you
      log off.

      When  you  allocate  a  device, your primary process and all of your
      subprocesses may access the device.  You must have  ALLOC  privilege
      to use this command.



      14.2 ASSIGN

      The  ASSIGN  command defines a logical device name and associates it
      with a particular device and/or disk file.

      Syntax:

           ASSIGN[/qualifiers] actual_device logical_device

      Qualifiers:

         /SYSTEM specifies  that  the  assignment  is  to  be  made  on  a
                 system-wide  basis  and  apply  to  all  users.   If this
                 qualifier is not specified, the ASSIGN  applies  only  to
                 your job.

      See  Chapter  7,  starting  on  page  44, for additional information
      about the ASSIGN command.



      14.3 ASSIGNMENT Expressions

      The following operators  are  used  to  define  symbols  as  numeric
      expressions:  "=",  "==", and "===".  They define symbols and equate
      them to the values of expressions.


      Chapter 14. TSX Command Summary                                   88


      Syntax:

           symbol_name = expression     (Process local symbol table)
           symbol_name == expression    (Process global symbol table)
           symbol_name === expression   (System symbol table)

      Examples:

           COUNT = 1
           COUNT = COUNT + 1
           SUBSTR == FULLSTR[1:3]
           DOSLIST = ANSWER .EQS. "YES"

      When a numeric assignment statement is executed  the  expression  on
      the  right  side  of  the equal sign(s) is evaluated and its numeric
      value is assigned to the symbol name.  See Chapter  7,  starting  on
      page 44, for additional information about defining symbols.



      14.4 ASSIGNMENT for strings

      The  following  operators  are  used  to  define symbols as strings:
      ":=", ":==", and ":===".

      They define symbols and equate them to replacement strings.

      Syntax:

           symbol_name := replacement_string     (Process local symbol)
           symbol_name :== replacement_string    (Process global symbol)
           symbol_name :=== replacement_string   (System symbol)

      Examples:

           TTPR*INT := COPY ^ TTA1:
           SDIR*ECTORY :== DIRECTORY/ORDER=NAME
           INFILE := DHA0:JUNE.DAT
           TTPRINT :== COPY ^ TTA2:

      See Chapter 7, starting  on  page  44,  for  additional  information
      about defining symbols.



      14.5 BACKUP

      The  BACKUP  command makes extra ("backup") copies of files.  BACKUP
      copies one or more input  files  into  a  single  output  "container
      file"  called  a  "backup save set".  BACKUP is usually used to copy
      groups of files from a hard disk to  floppy  disks  or  tape.   This
      ensures  that  if files are lost on the hard disk (due to failure of
      the hard drive or human error) they can be restored from the  backup
      copy.   The  RESTORE  command, described in Section 14.69, page 133,
      is used to restore files saved with BACKUP.


      Chapter 14. TSX Command Summary                                   89


      Syntax:

           BACKUP[/qualifiers] infile outfile

      Qualifiers:

         /AFTER[=date-time] selects files created since a given  date  and
                 time.

         /ARCHIVE  Specifies  that  only  files  with  the  "archive"  (or
                 "updated") attribute set should be backed up.

         /BEFORE[=date-time] Selects files created  before  a  given  date
                 and time.

         /BELL  Specifies  that  BACKUP should ring the bell during volume
                 change operations.

         /COMPRESS Specifies that BACKUP should compress data  from  files
                 as  it  is  writing to the output device.  This typically
                 reduces the size of the output save set  by  30%  to  50%
                 but  increases  the  CPU  time  used  by the backup.  The
                 RESTORE program automatically recognizes compressed  save
                 sets and decompresses them during the restoration.

         /CONFIRM  Specifies  that  you  want to confirm whether each file
                 should be backed  up.   For  each  file  selected  to  be
                 backed  up  you  will be prompted for confirmation.  Type
                 'Y' to backup the file, 'N' to skip the file and  proceed
                 with the next one, or '?' to list other choices.

         /EXCLUDE=(files)    specifies    that   any   file   matching   a
                 specification in the "files" list is  not  to  be  backed
                 up.   Wildcard  file  specifications are permitted in the
                 exclusion list.  If more than one file  specification  is
                 provided,  enclose  the specifications in parentheses and
                 separate them with commas.

         /GROUP=count Specifies the number of save  set  records  in  each
                 redundancy  group.   Each  redundancy  group  includes an
                 extra record which can be used by RESTORE to  reconstruct
                 one  unreadable  record  in the group.  The default group
                 count is 10.

         /IGNORE Specifies that you want to backup the file even if  other
                 processes   currently  have  the  file  open  with  write
                 access.

         /INITIALIZE May be used  when  the  BACKUP  output  device  is  a
                 floppy  disk,  magnetic  tape  or  other  removable  file
                 structured device.  /INITIALIZE specifies that all  files
                 should   be   deleted  from  each  output  volume  before
                 creating a backup save set.


      Chapter 14. TSX Command Summary                                   90


         /NEW selects only files created today.

         /NOCRC Specifies that you do not want CRC  (cyclical  redundancy)
                 checksums calculated and recorded in the save set.

         /NOLOG  Specifies  that  BACKUP should not report which files are
                 being backed up.  By default BACKUP  logs  this  activity
                 to the terminal.

         /RECORD  Specifies  that  the  "updated"  attribute flag for each
                 file backed up should be cleared (turned off).  This  can
                 be  used  to  keep  track of which files have been backed
                 up.  This qualifier  can  be  used  in  conjunction  with
                 /ARCHIVE  to  perform  incremental backups -- saving only
                 files created or modified since the last backup.

         /SINCE=date-time Is equivalent to the /AFTER qualifier.

      The BACKUP command copies all selected input files to  to  a  backup
      save set.  For example,

           BACKUP  *.C  B:CODE

      creates  a  single backup save set (which is itself a valid file) on
      floppy disk B: named CODE.BSS containing all files from the  current
      directory  with  the  extension  ".C".  In addition to the data from
      the input files, the save set file also contains  information  about
      the  names  of  the  input  files and the device and directory where
      each input file was located.  The files in the backup save  set  can
      only  be restored using the RESTORE command (see Section 14.69, page
      133).

      Most variations of the  BACKUP  command  select  different  sets  of
      files  to  be  backed up.  File selection is done by combining lists
      of file specifications  (with  wildcard  characters  and  file  name
      factoring) with selection and exclusion qualifiers.

      The  /ARCHIVE qualifier causes BACKUP to select only files that were
      created or modified since the last backup.   The  /RECORD  qualifier
      causes  BACKUP  to  mark  the  directory entries of files indicating
      that they have been backed up.

      The output save set file can reside on a single volume  but  backing
      up  to  floppy disks often requires multiple volumes.  Save sets are
      stored with redundant information so that if some of it can  not  be
      read the lost data can be reconstructed.

      You  can  use  the  RESTORE/VERIFY command to read a backup save set
      and compare the contents of its files with those on disk  to  verify
      that the save set was written correctly and can be read.

      The  BACKUP  command  must  include  at least one file specification
      indicating which files are to be backed  up.   All  files  with  the
      extension ".C" could be backed up with the command,


      Chapter 14. TSX Command Summary                                   91


           BACKUP *.C B:CODE

      Multiple  input  file  specifications should be separated by commas.
      For example, to  backup  up  BIG.DAT  as  well  as  all  files  with
      extension ".C", use the command:

           BACKUP *.C,BIG.DAT B:ALL

      To  back  up  all files in the \DAN directory and all subdirectories
      under DAN, use the "..." wildcard directory  operator  (see  Section
      5.2, page 40) with a command such as:

           BACKUP \DAN\...\*.* B:DAN

      The  following  command  backs  up all files in all directories (and
      subdirectories) on the C: disk:

           BACKUP C:\...\*.* C:FULLBACK

      The /EXCLUDE qualifier can be used to  exclude  certain  files  from
      the  backup  operation.  For example, the following command backs up
      all files in the DAN and ALEX  directories  except  files  with  the
      extension BAK and TMP,

           BACKUP/EXCLUDE=(*.BAK,*.TMP) \DAN\...\*.*,\ALEX\...\*.* A:SAV

      Another  technique  to manage the volume of files backed up is known
      as "incremental backup".  This backs up only the  files  which  have
      been  created  or  updated  since  the last backup was done.  For an
      incremental backup, files are  selected  which  have  the  "updated"
      attribute  flag  set.   This attribute is set when a file is created
      or modified indicating that it has been updated since  it  was  last
      backed  up.   The  /ARCHIVE  qualifier  causes BACKUP to select only
      files with this updated attribute set.  For example,  the  following
      command  backs  up  all  files on C: that have the updated attribute
      set:

           BACKUP/ARCHIVE C:\...\*.* B:FULL

      The /RECORD qualifier is a companion to /ARCHIVE.   Whereas  ARCHIVE
      causes  BACKUP  to select only files with the updated attribute set,
      /RECORD causes BACKUP to reset the updated attribute flag  for  each
      file  that  is  backed up.  To perform periodic incremental backups,
      you should specify both the /ARCHIVE and /RECORD  qualifiers.   This
      selects  files  created or updated since the last incremental backup
      and causes the updated attribute to be cleared once the  backup  has
      been done.  The following command illustrates this:

           BACKUP/ARCHIVE/RECORD C:\...\*.* A:INC0511

      When   using   the   incremental   backup   technique,   you  should
      occasionally perform a full (or "baseline")  backup  of  all  files.
      When  performing this baseline backup you would normally specify the
      /RECORD qualifier but would not use  the  /ARCHIVE  qualifier  since
      you want to select all files.


      Chapter 14. TSX Command Summary                                   92


      When  copying  to  floppy  disk  more  than one output volume may be
      needed to store all the  files.   When  a  removable  output  device
      fills  up,  BACKUP  closes  the output save set and asks the user to
      mount another volume.  You can load another  floppy  disk  and  type
      "OK"  to continue the backup operation or you can type "QUIT" if you
      do not want to go on.  You can also type "INITIALIZE"  if  you  want
      to  continue but need to delete all files from the new volume first.
      The same file name  is  used  for  each  volume  of  the  save  set.
      Volumes  must  be provided to the RESTORE facility in the same order
      that the BACKUP facility wrote them.

      Often a set of floppy disks used for backup  may  contain  old  save
      sets  or  other  unwanted  data.   The  /INITIALIZE qualifier causes
      BACKUP to delete all the files on the output volume  before  opening
      a  new save set file.  Be sure that the output disk does not contain
      data you need before running BACKUP with /INITIALIZE.   BACKUP  will
      not  allow  you  to  specify the /INITIALIZE qualifier if the output
      disk is a fixed disk.  /INITIALIZE also will not delete  files  with
      the  protected  attribute  set (the UNPROTECT command will clear the
      protected attribute).



      14.6 BATCH

      BATCH Submits a command file to be executed as  a  background  batch
      job.

      Syntax:

           BATCH[/qualifiers] filespec [/qualifiers]

      Qualifiers:

         /AFTER[=date-time] Run job at specified date-time.

         /[NO]ASSIGNS  (Default)  The  batch job "inherits" logical device
                 names and symbol names currently in effect.

         /[NO]HOLD Specifies that the  batch  job  is  to  be  held  until
                 later.

         /[NO]IDENTIFY  (Default)  Display  the  job id and queue name for
                 job.

         /LOGFILE[=filename] Write output to filename.  (Default: Name  of
                 command file)

         /NAME[=nametext]   Specify   the  job  name.   Default:  Name  of
                 invoking command file.

         /[NO]NOTIFY Print a  message  on  terminal  when  the  batch  job
                 completes.


      Chapter 14. TSX Command Summary                                   93


         /PARAMETERS=params   Specify  parameters  to  be  passed  to  the
                 command file.

         /PRIORITY=n Specify the queue priority for the batch job.

         /QUEUE=quename Specify the queue to  submit  job  to.   (Default:
                 BATCH:)

         /[NO]RESTART  Restart  the  job if a system shutdown occurs while
                 job is running.

         /RUNPRIORITY=n Run the batch job at this priority.   The  default
                 priority  for  both  interactive  and  batch  jobs is 50.
                 Specify a priority lower than 50 if you wish to have  the
                 background  batch  job  execute  at a lower priority than
                 interactive users.  You can use QMAN to set  the  default
                 execution priority for a queue.

      See  Section  9.3  on  page  54 for additional information about the
      BATCH command.



      14.7 BOOT

      BOOT Stops TSX and reboots DOS.  It is recommended that you  execute
      the  SHUTDOWN  procedure first which does an orderly shutdown of all
      jobs.



      14.8 BYE

      BYE is a synonym  to  the  LOGOFF  command.   See  LOGOFF  for  more
      detail.



      14.9 CALCULATE

      CALCULATE Evaluates a numeric expression and displays the result.

      Syntax:

           CALCULATE expression

      Examples:

           CALC 22/7
           CALC (121+822)/4.71
           CALC SQRT(43)

      In  addition to the arithmetic operators, CALCULATE also accepts the
      following library functions: ACOS, ASIN, ATAN, COS, EXP,  ABS,  LOG,


      Chapter 14. TSX Command Summary                                   94


      LOG10,  SIN,  SQRT,  TAN, DEG, RAD.  Arguments to trig functions are
      in units of degrees.



      14.10 CALENDAR

      CALENDAR Displays a calendar for a selected month.  If  you  do  not
      specify a month, a calendar for the current month is displayed.

      Syntax:

           CALENDAR [month [year]]

      Examples:

           CALENDAR
           CALENDAR JAN
           CALENDAR DEC 92



      14.11 CALL

      The  CALL  statement  is  used  in  a  DOS-style  BAT file to invoke
      another BAT file.

      Syntax:

           CALL[/qualifiers] file [arguments]

      Qualifiers:

         /[NO]ECHO List each line of the file as it is executed.

      The CALL command can be used to invoke  a  command  procedure  or  a
      .BAT  file.   It  is identical to using the '@' sign but is provided
      for compatibility with DOS.

      The optional qualifiers are  /ECHO,  which  forces  echoing  of  the
      lines   in   the   called  command  procedure,  and  /NOECHO,  which
      suppresses echoing.  By default the called  command  procedure  will
      inherit the echo characteristics of the caller.



      14.12 CHAIN

      CHAIN  chains  from  one  command  file to another.  When the second
      command file exits control does not return to the  invoking  command
      file.

      Syntax:


      Chapter 14. TSX Command Summary                                   95


           CHAIN[/qualifiers] filespec [arguments]

      Qualifiers:

         /ABORT  Close  all  currently  nested  command  procedures before
                 running.

      The CHAIN command allows command files to  "chain"  together.   This
      is  a  useful tool for large applications which may not wish to have
      one central command file driving them.  There  are  many  advantages
      to  having command files be the topmost layer of large applications.
      For one, it provides instant  access  to  all  the  normal  keyboard
      monitor  commands  for  doing  utility work such as copying, backup,
      allocation of devices, etc.  The technique of chaining  also  allows
      developers  to  keep  command  file driven applications from getting
      nested too deeply by allowing one command procedure to pass  control
      to another while terminating itself and closing its file.

      If  no  qualifiers  are  specified,  the  CHAIN  command  closes the
      currently  executing  command  file  and  begins  execution  of  the
      command  file specified as the first parameter to the CHAIN command.
      Any open command files above the  one  invoking  the  CHAIN  command
      remain  open  so  the  new command file begins executing at the same
      nesting level as the one being exited.  If the /ABORT  qualifier  is
      specified,  all  open  command  files for the job are closed and the
      command file being entered is started as the topmost command file.



      14.13 CHDIR

      CHDIR Changes the current default  working  disk  and/or  directory.
      It is equivalent to the SET DEFAULT and the CD command.

      Syntax:

           CHDIR dirspec
           CD dirspec
           SET DEFAULT dirspec

      Examples:

           CD \TSX32SYS
           CHDIR ..\TEST
           SET DEFAULT E:\BIN



      14.14 CLS

      CLS clears and resets the terminal screen.


      Chapter 14. TSX Command Summary                                   96


      14.15 COPY

      COPY copies one or more files.

      Syntax:

           COPY[/qualifiers] inputnames outputname

      Qualifiers:

         /ALLOCATE=size Preallocate this many bytes for the output file.

         /BEFORE[=date-time]  Copy  only files created before a given date
                 and time.

         /BLOCKSIZE=size Specify the number of bytes in  each  data  block
                 written by COPY.

         /[NO]CONCATENATE  Concatenate  files  together  to  form a single
                 output file.

         /[NO]CONFIRM Request confirmation before copying each file.

         /[NO]CONTIGUOUS  Store  data   blocks   for   the   output   file
                 contiguously on disk.

         /[NO]CREDIR Create output directory if it doesn't exist.

         /DATE Copy files created on the given date.

         /[NO]DELETE Delete input file(s) after copying.

         /EXCLUDE=(files) Exclude listed files from copy.

         /[NO]LOG Display log information.

         /[NO]MBXALLOC=bytes Allocate this many bytes for mailbox device.

         /[NO]MBXPERM Create permanent mailbox.

         /[NO]MD Same as /[NO]CREDIR

         /[NO]MKDIR Same as /[NO]CREDIR.

         /[NO]MULTI_VOLUME Prompt for additional output volumes.

         /NEWFILE Only copy files created today.

         /[NO]PREDELETE  Delete  output  file  before  copy  if it already
                 exists.

         /PROTECT Set protection on output file.

         /QUERY Same /[NO]CONFIRM.


      Chapter 14. TSX Command Summary                                   97


         /[NO]REPLACE (Default) Overwrite old files with new copies.

         /SETDATE Set date/time of output file to current date/time.

         /SINCE[=date-time] Copy files created since date-time.

         /UPDATE Prevents overwriting existing files which are newer  than
                 the file about to be copied over it.

      The  COPY command makes a copy of one or more files.  It can be used
      to move files between devices or directories.   Unless  the  /DELETE
      qualifier is specified, the input file is not altered.

      Subdirectory  files  are  not  copied.   However,  you  can  use the
      /CREDIR qualifier to cause COPY to create subdirectories for  output
      files.

      Wildcard  characters  may  be  used  in  file  specifications.   The
      asterisk ('*') character matches zero or more  characters,  and  the
      question  mark  ('?') character matches exactly one character.  Both
      may be used in input file names, but only the asterisk may  be  used
      in the output file name.  For example, the command

           COPY MANUAL.TXT,AUTO.TXT  *.OLD

      results  in MANUAL.TXT being copied to MANUAL.OLD and AUTO.TXT being
      copied to AUTO.OLD.

      To copy all files with the  extension  ".C"  created  yesterday  and
      today to the same name with the extension ".NEW", type

           COPY/SINCE=YESTERDAY  *.C  *.NEW

      See   Section  5.2,  page  40,  for  more  information  on  wildcard
      characters and their usage.

      If a part of a file specification is missing from  the  output  file
      name,  the  missing  part  is treated as if it were the '*' wildcard
      character, and the corresponding part is used from  the  input  file
      name.

      If  "\...\"  is  specified  as  the output directory, then the input
      directory for each file  is  used  as  the  output  directory.   For
      example,  the  following command copies all files in all directories
      on device DHA1: to device DFA0: and preserves the directory tree:

           COPY/CREDIR  DHA1:\...\*.*  DFA0:\...\*.*

      Note the use of the /CREDIR qualifier which causes  COPY  to  create
      any non-existing directories on the output disk.

      It  is also possible to use an output directory specification of the
      form \directory...\ to copy a directory tree under  a  directory  on
      the  output  device.   For example, the following command copies all
      files in all directories on device A: to device C: and constructs  a


      Chapter 14. TSX Command Summary                                   98


      directory  tree  on  the output disk that matches the directory tree
      on the input disk except it is rooted under the directory \PASCAL\,

           COPY/CREDIR  B:\...\*.*  C:\PASCAL...\*.*

      A  technique  called  "factoring"  may  be  used  to  simplify   the
      specification  of a list of files that have a common portion for the
      input file specification.  To use  factoring,  enclose  the  varying
      parts  of the file specification in parentheses separated by commas.
      For example, the command

           COPY PAYROLL.(CBL,OBJ,EXP) OLDPAY.*

      is equivalent to the command

           COPY PAYROLL.CBL,PAYROLL.OBJ,PAYROLL.EXP OLDPAY.*

      or to the commands

           COPY PAYROLL.CBL OLDPAY.CBL
           COPY PAYROLL.OBJ OLDPAY.OBJ
           COPY PAYROLL.EXP OLDPAY.EXP

      See the description of the FMAN command on page 114 for  information
      about a screen-oriented file management program.



      14.16 COUNT

      COUNT counts the records in files.

      Syntax:

           COUNT[/qualifiers] filespec

      Qualifiers:

         /BEFORE[=date-time]  Select files created before a given date and
                 time.

         /DATE[=date] Selects files created on the given date.

         /EXCLUDE=(files) Exclude specified files.

         /NEW Only count files created today.

         /OUTPUT=file Redirects count output to a file.

         /SINCE[=date-time] Select only files  created  since  given  date
                 and time.


      Chapter 14. TSX Command Summary                                   99


      14.17 DATE

      DATE  is  a  synonym  for SET DATE.  It can also be used to show the
      current date.



      14.18 DEALLOCATE

      DEALLOCATE releases exclusive use of a device  previously  allocated
      by use of the ALLOCATE command.

      Syntax:

           DEALLOCATE device[,device...]



      14.19 DEASSIGN

      DEASSIGN   Removes   (deletes)   symbol   and  logical  device  name
      assignments.

      Syntax:

           DEASSIGN[/qualifiers] name

      Qualifiers:

         /ALL Deleate all symbols in the specified table.

         /GLOBAL Specified symbol is in the process global table.

         /LOCAL Specified symbol is in the process local table.

         /SYMBOL Specified symbol is a symbol, not a logical device name.

         /SYSTEM Specified symbol is in the system table.

      The DEASSIGN command removes a symbol name from a symbol  table,  or
      a  logical  device  name  from  an  assign  table.   If  the /SYMBOL
      qualifier is specified, the name is treated as a  symbol  name.   If
      /SYMBOL  is  not  specified, the name is treated as a logical device
      name.

      The qualifiers /LOCAL, /GLOBAL,  and  /SYSTEM  specify  whether  the
      name  is  in the process local, process global, or system table.  No
      more than one of these qualifiers may be  specified  on  a  command.
      If  none  of these qualifiers is specified, the process global table
      is searched for a logical device name and the  process  local  table
      is searched for a symbol name.

      If  the  /ALL  qualifier  is  specified, all entries in the selected
      symbol or assign table  are  deleted.   In  this  case,  the  "name"
      parameter is ignored.


      Chapter 14. TSX Command Summary                                  100


      SYSPRV  privilege  is  required  to  remove an entry from the system
      table.



      14.20 DEFINE KEY

      The  DEFINE  KEY  command  defines  a  replacement  string  that  is
      substituted  for  a specified key when the key is pressed.  See also
      the description of the MACROS command on page 122,  for  information
      about   defining  keyboard  macros  for  the  console  keyboard  and
      make/break type terminals.

      Syntax:

           DEFINE KEY[/qualifiers] key_name replacement_string

      Examples:

           DEFINE KEY/NOECHO F11 CLS
           DEFINE KEY/NOECHO F12 DIR/SINCE=YESTERDAY

      Qualifiers:

         /[NO]ECHO  Display  replacement  string  when  replacement  takes
                 place.

         /GOLD "Gold" key must be pressed before the defined key.

         /[NO]LETTER key_name is a character, not a function key.

         /[NO]TERMINATE Insert carriage-return after replacement.



      14.21 DELETE

      DELETE deletes one or more files from the disk.

      Syntax:

           DELETE[/qualifiers] filespec

      Qualifiers:

         /ALLOCATION  Display  allocated  size  of file rather than actual
                 size.

         /BEFORE[=date-time] Selects filescreated before a given date  and
                 time.

         /[NO]CONFIRM Request confirmation before deleting each file.

         /DATE[=date] Delete files created on the given date.


      Chapter 14. TSX Command Summary                                  101


         /ERASE Actually erase contents of file from the disk.

         /EXCLUDE=(files) Do not delete files specified in list.

         /[NO]LOG Display file information as each file is deleted.

         /NEWFILE Delete only files created today.

         /[NO]QUERY Same as /[NO]CONFIRM.

         /SINCE[=date-time]  Delete files created since specified date and
                 time.



      14.22 DETACH

      DETACH initiates execution of a detached job.

      Syntax:

           DETACH[/qualifiers] filespec arguments
           DETACH[/qualifiers] command

      Qualifiers:

         /[NO]COMMAND Detach command is a system command,  not  a  command
                 file.

         /[NO]IDENTIFY  Print  detached  job  ID  on  terminal.   Default:
                 IDENTIFY

         /[NO]INHERIT (Default) Inherit attributes from the parent job.

         /LOGFILE=filename Write log information to specified file.

         /NAME=job_name Specify the job name.

         /[NO]NOTIFY (Default) Notify when job is completed.

         /PRIORITY=value Run job at specified priority.

      The DETACH command starts a detached  job  to  execute  a  specified
      command   file   or   system   command.    The   detached  job  runs
      asynchronously from your job and your job does not have to wait  for
      the  detached  job to finish.  You can use the STOP command to abort
      a detached job you started.

      Detached jobs are very similar to batch jobs  described  in  Section
      9.3,  page  54.   The  main  difference is that detached jobs always
      start immediately whereas  there  can  be  a  queue  of  batch  jobs
      waiting  to  begin  execution.   In fact, the queue manager uses the
      detached job facility to execute batch jobs.


      Chapter 14. TSX Command Summary                                  102


      The type of parameter specified to the  DETACH  command  depends  on
      whether  the /COMMAND qualifier is specified.  If you do not specify
      the /COMMAND qualifier, then the parameter to the DETACH command  is
      the  name  of  a command file to be executed as a detached job.  You
      may optionally specify parameters for  the  command  file  following
      the  command file name.  For example, the following command executes
      the command file named BACKALL passing it one parameter MARCH:

           DETACH BACKALL MARCH

      Within the BACKALL  command  file,  the  MARCH  parameter  could  be
      accessed using either the 'P1' or ^1 notations.

      If  the  /COMMAND  qualifier is specified, then the parameter to the
      DETACH command is a single system command rather than the name of  a
      command  file.   The  effect is the same as if you created a command
      file consisting of only the single command and executed  that  as  a
      detached  job.   The  advantage  is that you do not have to create a
      command file to execute a single command as a detached job.

      For example,  the  following  command  executes  a  "DIRECTORY  *.C"
      command as a detached job and creates a log file named DIRLOG:

           DETACH/COMMAND/LOGFILE=DIRLOG DIRECTORY *.C

      If   the   command   being  executed  as  a  detached  job  contains
      redirection operators ('>' and '<'), then  enclose  the  command  in
      quotation  marks  to prevent the command processor from applying the
      redirection to the DETACH command itself.

      All program input for the detached job comes from the  command  file
      or  the  single command line if /COMMAND was specified.  When all of
      the commands in the  command  file  are  exhausted,  and  a  program
      running  in  the  detached  job tries to read from the terminal, the
      detached job is logged off.

      All output directed to the terminal by programs in the detached  job
      is  discarded.   You  can  use  the  /LOGFILE=filename  qualifier to
      specify a log file into which output directed  to  the  terminal  by
      the detached job will be written.

      You  can place a SEND/PARENT command in a detached (or batch) job to
      send a message to the initiating ("parent") job.

      If you do not specify the /NOINHERIT qualifier, the following  items
      of  information  are  "inherited"  by  the  detached  job  from  the
      initiating job:

        . Process global logical device assignment names.

        . Process global symbol names.

        . The current default working directory.


      Chapter 14. TSX Command Summary                                  103


        . The directory search path.

        . The maximum authorized execution priority.

        . The maximum authorized privileges.

        . The command prompt string.

        . The user and group numbers (UIC).

      You must have DETACH privilege to use detached jobs.



      14.23 DIFFERENCES

      DIFFERENCES compares two files and reports the  differences  between
      them.

      Syntax:

           DIFFERENCES[/qualifiers] primary_file secondary_file

      Qualifiers:

         /BINARY Same as /FAST.

         /CONTINUE In fast mode, report all differences between files.

         /[NO]EXACT (Default) Consider upper and lower case as different.

         /FAST Do a fast byte by byte comparison of the two files.

         /IGNORE=type  Ignore  differences  in certain characters.  If you
                 specify /IGNORE=DECIMAL then differences between  decimal
                 digits  (0-9)  are  ignored.   If you specify /IGNORE=HEX
                 then differences between hexadecimal digits are  ignored.
                 Hexadecimal  digits  are  the digits 0 to 9 and the upper
                 case letters A to F.

         /MAXDIF=sect Allow  this  many  difference  sections.   (Default:
                 100)

         /MAXSECTION=n   Allow   n   records   in  a  difference  section.
                 (Default: 50)

         /NUMBER Display record numbers.

         /OUTPUT[=file] Redirects output to file.

         /RECLEN=length Specify  the  maximum  record  length.   (Default:
                 1024)

      DIFFERENCES  features  two  different  modes of operation.  The most
      common of these is a record oriented mode intended  for  text  files


      Chapter 14. TSX Command Summary                                  104


      which  produces  an  output report displaying each area in which the
      two files differ.  A second, faster mode, suited for  comparing  two
      binary  files,  simply compares the files character by character and
      determines whether they  are  the  same  or  different.   This  mode
      reports  the  byte  position  from  the beginning of the file of any
      mismatch.  By default DIFFERENCES operates in  ASCII  mode;  if  you
      want  the  fast,  binary  mode,  specify either the /FAST or /BINARY
      qualifiers.

      When operating in fast mode, DIFFERENCES  reads  large  portions  of
      each  file  and  compares  them  character  by  character.   When  a
      mismatch between the two files is  discovered,  DIFFERENCES  reports
      the  position  of  the mismatch and stops.  The position reported is
      the byte position relative to the start of the file.

      If you need to know all the bytes which differ  between  two  files,
      specify the /CONTINUE qualifier on the command line.

      In  the normal mode of operation, DIFFERENCES reads records from the
      primary file and tries to locate each one  in  the  secondary  file.
      As  it  locates  matching  records,  DIFFERENCES  updates  a current
      record position in the each file.

      When a  section  in  which  the  two  files  differ  is  encountered
      DIFFERENCES  reports  the  section.   Each  such report includes the
      following.

        . The name of the primary input file.

        . Records from the primary file, beginning with  any  last  record
          found  in  the  secondary file, followed by any records from the
          primary file which could not be located in the  secondary  file,
          ending  with  any  record  which  again  could  be  found in the
          secondary file.

        . The name of the secondary input file.

        . Records from the secondary file, beginning with any last  record
          which  matched  a  primary  file record, followed by any records
          which do not match primary file records, ending with any  record
          which did match a primary file record.

      When  DIFFERENCES  can not locate the current primary file record in
      the secondary file it will not search all the way to the end of  the
      secondary   file   looking  for  it.   The  /MAXSECTION=n  qualifier
      controls how far forward DIFFERENCES will look.  If DIFFERENCES  can
      not  locate  a  primary  file record at all, the record is listed in
      the differences section and the comparison continues with  the  next
      record from the primary file.

      The   /MAXSECTION  qualifier  also  controls  how  many  consecutive
      primary file records are allowed  not  to  match  records  from  the
      secondary  file.   If  this  limit is exceeded DIFFERENCES gives up,
      assuming the differences between the two files are too extensive  to
      describe.


      Chapter 14. TSX Command Summary                                  105


      Usually  DIFFERENCES  directs output to the terminal.  Output can be
      redirected to a file by specifying  the  /OUTPUT=file  qualifier  or
      using a redirection operator on the command line.

      DIFFERENCES  sets  the  $STATUS  symbol to the number of differences
      encountered.  This allows command  procedures  to  take  conditional
      action when two files differ.



      14.24 DIRECTORY

      DIRECTORY displays information about a file or a list of files.

      Syntax:

           DIRECTORY[/qualifiers] filespec

      Qualifiers:

         /[NO]ACROSS Display sorted files across the screen.

         /BEFORE[=date-time]  Display  files  created  before a given date
                 and time.

         /[NO]BLOCKS List file sizes in units of 512 byte  blocks  [or  in
                 bytes].

         /[NO]BRIEF List only directory headers and file names.

         /COLUMNS=n Use this many columns for display.

         /[NO]CREATION_DATE=n   Use   this  many  columns  for  file  date
                 display.

         /DATE[=date] Select files created on the specified date.

         /[NO]DESCENDING Display files in descending order.

         /DIRECTORY List only subdirectories.

         /[NO]DOWN Sort items in columns on the screen.

         /EXCLUDE=(files) Exclude specified files.

         /[NO]FAST Same as /BRIEF.

         /[NO]FORMAT[=parts]  Produce  output  suitable  for  input  to  a
                 program.  If used, parts must be one of the following:


      Chapter 14. TSX Command Summary                                  106


                 NONODE       Omit node specification, if any.
                 NODEVICE     Omit device specification
                 NODIRECTORY  Omit directory specification
                 NONAME       Omit file name
                 NOEXTENSION  Omit file extension
                 NOTYPE       Omit file extension

         /FREE Report only free space on disk.

         /[NO]GRAND Report only grand total size of specified files.

         /[NO]HEADER (Default) Include header line in listing.

         /LOWCASE List file names in lower case.

         /[NO]NAME[=n] Use this many columns for file name.  Default: 12

         /NEWFILES List only files created today.

         /[NO]NUMBNU[=n]  Assign  sequential numbers to files; n specifies
                 number of columns to be use for numbers.

         /ORDER[=sort_key]  Sort  file  list  on  the  specified   key(s).
                 Sort_key must be one of the following:

                 ALLOCATED       Space file takes on disk.
                 CREATED         Creation date.
                 CREATION_DATE   Creation date.
                 DIRECTORY       File directory.
                 EXTENSION       File name extension.
                 NAME            Primary file name.
                 SIZE_ALLOCATED  Space file takes on disk.
                 SIZE_USED       File space actually used.
                 TYPE            File name extension.
                 USED            File space actually used.

         /OUTPUT[=file]  Send  output  to  the  specified  file.  Default:
                 DIRECT.LST

         /PAUSE Pause after each screen of output.

         /REVERSE Same as /DESCENDING.

         /SINCE[=date-time] Select files created since a  given  date  and
                 time.

         /[NO]SIZE[=sizespec]  Include  file  sizes  in listing.  If used,
                 sizespec must be one of the following:

                 ALL             Show both size allocated and used.
                 ALLOCATED       Show space file takes on disk.
                 USED            Show actual size of file.

         /SORT[=sort_key] Same as /ORDER.


      Chapter 14. TSX Command Summary                                  107


         /[NO]TOTAL Same as /[NO]GRAND

         /[NO]TRAILER (Default) Include trailer lines in listing.

         /WIDTH=n Use this width for output.

      You can use the "\...\" wildcard notation to obtain a  directory  of
      all  files  in  a  directory tree.  See Section 5.2, on page 40, for
      additional information about wildcards.

      See the description of the FMAN command on page 114 for  information
      about a screen-oriented file management program.



      14.25 DISPLAY

      DISPLAY displays a text string on your terminal.



      14.26 DOS

      DOS  Invokes  the  DOS command processor (COMMAND.COM).  See Section
      4.5 on page 32 for additional information about this command.

      Syntax:

           DOS[/qualifiers] [dos_command]

      Qualifiers are the same as for the RUN command.



      14.27 DOWNLOAD

      The DOWNLOAD command causes TSX to initiate  a  file  transfer  from
      the  TSX  host  computer  to  your local PC using ZMODEM, YMODEM, or
      XMODEM protocol.  You must be running a  communications  program  on
      your  local  PC that can handle one of these protocols.  In order to
      use this facility the ZMODEM sysgen parameter must be set to 1.

      Syntax:

               DOWNLOAD[/qualifiers] file1[,file2,...]

      You must specify at least one file name and you may provide  a  list
      of  names separated by commas.  You may use wildcard characters such
      as '*' and '?' in the file list if you are using ZMODEM  or  YMODEM.
      Only a single file may be specified if you are using XMODEM.


      Chapter 14. TSX Command Summary                                  108


      Qualifiers:

         /AFTER[=date-time]  Selects  files created since a given date and
                 time.  If  /AFTER  is  specified  without  an  associated
                 date-time value, the implied date is today.

         /BELL   Requests   that  the  bell  be  rung  when  the  transfer
                 completes.

         /BEFORE[=date-time] Selects files created  before  a  given  date
                 and time.

         /CRC  Specifies  that  CRC  checks are to be performed for XMODEM
                 transfers rather than using checksums.   CRC  checks  are
                 always used for YMODEM and ZMODEM transfers.

         /EXCLUDE=(files)]    Specifies   that   any   file   matching   a
                 specification  in  the  files   list   is   not   to   be
                 transferred.    Wild   card   file   specifications   are
                 permitted in the exclusion list.  If more than  one  file
                 specification  is provided, enclose the specifications in
                 parentheses and separate them with commas.

         /NEW Select files created today.

         /SINCE[=date-time]  Select  files  created  since  the  specified
                 date.

         /XMODEM  Specifies  that  XMODEM  protocol  is to be used for the
                 transfer.

         /YMODEM Specifies that YMODEM protocol is  to  be  used  for  the
                 transfer.

         /ZMODEM  Specifies  that  ZMODEM  protocol  is to be used for the
                 transfer.  This is the default protocol.



      14.28 DUMP

      DUMP provides various formatted displays of the contents of a file.

      Syntax:

           DUMP[/qualifiers] filespec

      Qualifiers:

         /[NO]ASCII(Default)  Display   ASCII   representation   of   each
                 character.

         /BLOCK  (Default)  Dump  is  block  oriented  instead  of  record
                 oriented.


      Chapter 14. TSX Command Summary                                  109


         /COLUMNS=columns Display this many columns in the output.

         /CONTINUOUS Display offset from start of file  instead  of  start
                 of block.

         /COUNT=count Dump this many blocks or records.

         /DRADIX=radix Use this radix (2,8,10, or 16).  Default: 16

         /END=value Stop dump at this block or record.

         /FORMAT=name Use this format: DEFAULT or COLUMN.

         /[NO]HEADER  (Default) Display header lines introducing each line
                 or block.

         /LOGICAL Read logical blocks instead of virtual blocks (for  disk
                 partition).

         /LONGWORD   (Default)   Display   32-bit  longwords  as  separate
                 entities.

         /MAXREC=value Specify the longest record in the  file.   Default:
                 2048.

         /NRADIX=radix  Use this radix for offset numbers (2,8,10, or 16).
                 Default: 16.

         /[NO]NUMBER (Default) Display labels for byte numbers.

         /OUTPUT=file Write output to the specified file.

         /PHYSICAL Read physical blocks instead  of  virtual  blocks  (for
                 disk partitions).

         /NRADIX=radix Use this radix for data and offset labels.

         /RECORD Display individual records instead of blocks.

         /START=value Begin display at this block or record.

         /WIDTH=width  Specify  how  wide  the output should be.  Default:
                 80.

         /WORD Display  16-bit  words  as  separate  entities  instead  of
                 longwords.



      14.29 EDIT

      EDIT  Invokes the EDIT-32 (E32) editor program.  EDIT-32 is designed
      to facilitate the migration of users familiar with the EVE  and  KED
      editors  on  DEC computer systems.  See REGISTER.DOC for information
      about ordering an EDIT-32 Reference Manual.


      Chapter 14. TSX Command Summary                                  110


      14.30 EVALUATE

      EVALUATE evaluates an  expression  and  print  the  result  at  your
      terminal.   Symbols  may  be  used  in the expression.  See also the
      description  of  the  CALCULATE  command  for  a   general   numeric
      expression calculator.

      Examples:

           EVALUATE 12*15*3
           EVALUATE NUMFILES + 3

      The  EVALUATE  command  is  a  convenient  way to evaluate a command
      expression and display the result at your  terminal.   The  EVALUATE
      command  is  especially  convenient  for  experimenting with lexical
      functions (see Section 9.10).



      14.31 EVENT

      EVENT Displays records in  an  event  log  file.   The  SHOW  EVENTS
      command does this in a screen-oriented fashion.

      Syntax:

           EVENT[/qualifiers] eventlog

      Qualifiers:

         /DATE Display date record was written in output.

         /DELETE Delete the specified event log file.

         /OUTPUT=file Send output to specified file.

         /[NO]SCREEN (Default) Display output on screen.

         /TIME Display time record was written in output.



      14.32 EXIT

      EXIT  terminates  command  file  and returns to higher level command
      file or the keyboard monitor.  This command will also exit  the  DOS
      command interpreter (entered using the DOS command).

      Syntax:

           EXIT[/qualifiers]


      Chapter 14. TSX Command Summary                                  111


      Qualifiers:

         /ABORT  Abort  higher  level  command files and return to command
                 prompt.

         /STATUS=value Return the specified exit status code.



      14.33 EXPAND

      The EXPAND command is used to generate a command file consisting  of
      a  set  of  commands  merged with a set of file specifications.  You
      could, for example,  use  EXPAND  to  generate  a  command  file  to
      compile  all  source files in a certain directory.  The set of files
      may be specified with wildcard file specifications much the same  as
      for the DIRECTORY command.

      Syntax:

           EXPAND[/qualifiers] filespec "command"

         filespec  is  a filename or a comma separated list of file names.
                 Each file name may include wildcards.  See  Section  5.2,
                 page  40,  for  more information about wildcards.  Fields
                 not specified on a file name are taken from the  previous
                 file  name  in  the  command  if  one has been specified.
                 Otherwise directory and device fields are taken from  the
                 current default directory.

                 You   may   also   specify   a  file  name  of  the  form
                 "@filespec".    In   this   case,   the   set   of   file
                 specifications   to   be  merged  with  the  commands  is
                 provided in the file specified by filespec.

         command specifies the command(s) to be  executed  once  for  each
                 file  selected.   The commands you specify should include
                 substitution  constructs,  explained  below,  which  tell
                 EXPAND  where  the  name  of  the selected file should be
                 inserted  in  the  command.   The  command  specification
                 should be enclosed in quote marks.

      Qualifiers:

         /ARCHIVE Select files with the archive attribute set.

         /BEFORE[=date-time]  Select files created before a given date and
                 time.

         /DATE[=date] Select files created on the given date.

         /DIR=dir-command Execute this  command  for  each  new  directory
                 encountered.


      Chapter 14. TSX Command Summary                                  112


         /EXCLUDE=(files) Don't process specified files.

         /HEADER="text"  Insert  specified text at start of output command
                 file.

         /NEW Only include files created today.

         /OUTPUT[=file] Specify the  name  of  the  output  command  file.
                 Default: ALL.CMD

         /RECORD Clear archive bit on processed files.

         /SINCE[=date-time]  Selects  files created since a given date and
                 time.

         /TRAILER="text" Insert specified text at end  of  output  command
                 file.

         /UNIX  Specifies  only  line  feeds  between  records  of  output
                 command file.

      The "command" parameter to the EXPAND command specifies  the  format
      of  the  commands  which  are written to the output command file for
      each selected file.  Substitution constructs of the  form  "|letter"
      (vertical  bar  followed  by one or more letters) inside the command
      are used to instruct EXPAND where to place the name of each file  in
      the  command.   As  a  simple example, consider the following EXPAND
      command:

           EXPAND *.C "CC |A"

      This  EXPAND  command  generates  a  command  file   named   ALL.CMD
      containing  commands  to  perform the "CC" command on each file with
      an extension of  ".C".   The  "|A"  construct  instructs  EXPAND  to
      insert  the  entire  filename into the command at the position where
      "|A"  occurs.   The  resulting  ALL.CMD  file  might   contain   the
      following commands:

           CC INIT.C
           CC MAIN.C
           CC EXIT.C

      Note  that  all  the  text besides substitution constructs is copied
      verbatim from  your  command  specification  to  each  line  of  the
      generated command procedure.

      The  following  substitution  operators  may  be used in the command
      string:


      Chapter 14. TSX Command Summary                                  113


            |A   Entire filename.
            |N   Device name.
            |D   Directory name.
            |F   File name.
            |E   Extension (with leading period).
            |V   A VAX/VMS style directory.
            |-D  File name with no device or directory.
            |-E  File name with no extension.
            |/   Begin a new line.
            ||   Literal '|' (vertical bar) character.



      14.34 FILEWATCH

      The FILEWATCH command causes TSX to create  an  event  log  file  to
      record all accesses to a specified file or group of files.

      Syntax:

           FILEWATCH[/qualifiers] filespec

      Qualifiers:

         /[NO]READ (default) Monitor file reads.

         /[NO]WRITE (default) Monitor file writes.

         /NONE Disable monitoring of the file.

      The  FILEWATCH  command  causes TSX to monitor accesses to all files
      that  match  the  "filespec"  specification.   This  is  useful  for
      security  purposes or any other time that you want to determine who,
      if anyone, is accessing or altering a  particular  file  or  set  of
      files.   The  file  accesses  that  are monitored are: open, create,
      delete, and rename.

      When you issue a FILEWATCH command, TSX creates an  event  log  file
      named  FWATCH  (if  it does not already exist).  Use the SHOW EVENTS
      command described on page 157 to monitor events in the FWATCH  event
      log  file.   See  Section 10.6 on page 69 for additional information
      about event logs.

      If no qualifiers are specified, both read and  write  type  accesses
      are  monitored.   Use the /NOREAD and /NOWRITE qualifiers to disable
      either type of monitoring.  The /NONE qualifier disables  monitoring
      of the specified file.

      The  "filespec"  parameter  to the command is the file specification
      that is to be monitored.  This specification  may  include  wildcard
      characters  in  the  file  name,  extension, and directory.  You may
      also use the "..." wildcard operator in  the  directory  portion  to
      monitor  all  file  accesses  in  or below a certain directory.  The
      device name portion of the specification may  not  include  wildcard
      characters.   For  example, the following command monitors all write


      Chapter 14. TSX Command Summary                                  114


      type accesses  to  all  files  in  the  C:\PHIL  directory  and  all
      directories below it:

           FILEWATCH/NOREAD C:\PHIL\...\*.*

      SYSPRV privilege is required to use the FILEWATCH command.



      14.35 FMAN

      FMAN  The  full  screen file management utility.  Use FMAN to manage
      files and directories, and control file access.

      Syntax:

           FMAN [directory]

      In response to the FMAN command, TSX displays a list  of  the  files
      in  the current directory or the directory that was specified on the
      command  line.   For  each  file,  the  name,  extension,  size  and
      date/time  of  last  modification  are  displayed.   The  letter 'P'
      appears in the right most column if the file  is  protected  against
      deletion.     Use    the    Up-arrow/Down-arrow    keys    or    the
      Page-up/Page-down keys to move through the  list  of  files.   Press
      ESC (or "Do" on a DEC VT series terminal) to exit from FMAN.

      A  menu of action keys appears to the right of the file list; choose
      an action by typing the appropriate key.  Each  of  the  actions  is
      described below:

         Enter  =  Mark/Unmark -- If you are performing the same action on
                 a group of files, it is sometimes easier  to  "mark"  the
                 set  of  files  and  then  apply the action to the entire
                 set.  When you  press  Enter  the  currently  highlighted
                 file  is  marked  and an indicator appears to the left of
                 its name.  If you  reselect  the  file  and  press  Enter
                 again, the mark will be removed.

         A  =  Attributes  --  Pressing  "A" causes a menu to appear which
                 allows you to protect or unprotect  a  file,  or  set  of
                 files,  against  deletion.   If you have BYPASS privilege
                 you will also be given menu  choices  for  modifying  the
                 access controls for a file.

         C  =  Copy  --  A  box appears requesting the destination for the
                 copy.  If you are copying a  set  of  files,  you  should
                 specify  a  wildcard  for  the  destination file names so
                 that the original file names will be used for  the  newly
                 created files.

         D  =  Delete  -- A confirmation box appears asking you if you are
                 sure you want to delete the selected file(s).


      Chapter 14. TSX Command Summary                                  115


         E = Edit -- The EDIT--32 editor is invoked to edit  the  selected
                 file.   The  FMAN  display resumes when you exit from the
                 editor.

         F = Find file -- A box appears asking for a search  string.   You
                 may  type  an entire file specification or only the first
                 letter or two of a file  name.   The  list  of  files  is
                 searched  and  the  first  file  name  that  matches  the
                 letters you type is selected.

         G = Go into directory -- You may type this to begin browsing  the
                 subdirectory  whose file name is currently selected.  The
                 right  arrow  key  may  also  be  used  to  perform  this
                 operation.

         H  =  Higher  directory  -- This causes FMAN to leave the current
                 directory and display files in the  directory  above  the
                 current  directory  (i.e., closer to the root).  The left
                 arrow key will  also  perform  this  operation.   If  you
                 continue  to type 'H' (or left arrow) you will eventually
                 be presented with a list of the disks  installed  in  the
                 computer.

         K  =  Make  directory  --  This action allows you to create a new
                 subdirectory.  A box appears asking for the name  of  the
                 directory to create.

         L  =  Mark  all  --  Marks  all  files  in the current directory.
                 Equivalent to moving down the  list  and  pressing  Enter
                 for each file.

         M  = Move file -- Copies the selected files to a destination that
                 you specify and then deletes the files from  the  current
                 directory.

         N  =  New directory -- You will be prompted for the name of a new
                 directory whose files will be displayed.

         R = Rename file -- You will be prompted for the new name for  the
                 selected file(s).

         S  =  Sort list -- This action causes FMAN to reorder the list of
                 file names.  A menu will appear allowing  you  to  select
                 the  item  to  sort  on  (name,  extension, date/time, or
                 size)  and  another  menu  will  allow  you   to   select
                 ascending or descending order.

         U = Unmark all -- All marked files are unmarked.

         V  = View file -- The VIEW command displays a file on the screen.
                 You can use the Page-up  and  Page-down  keys  to  scroll
                 upward  and  downward  through  the  file.   The Home key
                 moves to the top of the file and the  End  key  moves  to
                 the  end  of  the  file.   You  can  also use the up- and
                 down-arrow keys to scroll up or down one line at a  time.


      Chapter 14. TSX Command Summary                                  116


                 Press  ESC  to  exit  from the VIEW command.  The display
                 will begin in either ASCII or hexadecimal mode  depending
                 on  the  nature  of  the data in the file.  While viewing
                 the file you can type 'A'  to  switch  to  ASCII  display
                 mode or 'H' to switch to hexadecimal mode.

         X = Exit -- Exit from FMAN.  Equivalent to typing ESC.

      FMAN  is  also  used  to control which files and/or directories each
      TSX user may access.  The access control is  based  on  a  user  and
      group  ID code that is assigned by the system manager and associated
      with the user name entered to the LOGON program.  (TSAUTH and  LOGON
      are part of the TSX-Lite Security Kit.)

      If  you  have BYPASS privilege, the right most column of the primary
      file display list will be labeled "PA" The  letter  'A'  appears  in
      this  column  if  there  are  file access control entries associated
      with the file.  To modify the access control  entries  for  a  file,
      type  'A'  to  select  the  Attributes  menu item, and then type 'A'
      again to select the Access control entry from the attributes menu.

      To set access controls for an entire disk, type 'H' (or left  arrow)
      until  you  reach  the  menu with the disk drive names.  Then select
      the appropriate drive entry  and  type  'A'  to  invoke  the  access
      control list display for the disk.

      The  access  control list screen displays all access control entries
      that are in effect for the selected file or  directory.   To  add  a
      new  entry type 'A', to delete an entry type 'D', to modify an entry
      type 'Enter'.

      The first field in the access control entry box is the name  of  the
      user  whose  access  to  the  file or directory is to be controlled.
      You may type one of three things: (1) a valid user name that  exists
      in  the  TSX  account  authorization file, (2) a group/member number
      written in square brackets (e.g., "[121,47]"),  or  (3)  a  question
      mark,  in which case you will be presented with a list of authorized
      users when you exit by pressing ESC.  If you  specify  a  group  and
      member  number,  you  may  specify  an  asterisk ('*') as a wildcard
      character to match any group number, member number,  or  both.   For
      example  [233,*]  would  match any member number but applies only to
      users in group 233.  Similarly, [*,*] applies to all users.

      The next three items  control  the  type  of  access  the  specified
      user(s)  will  have  to  the  file.   If  you  specify 'Y' for write
      access, the user will have full access and may write  to  the  file,
      delete  the  file,  rename  the  file, and execute the file.  If you
      specify 'Y' for read access, the user may read the  file,  copy  it,
      and  execute it but may not delete or otherwise modify the file.  If
      you specify 'Y' for execute access, the user may  execute  the  file
      but may not read, copy, or modify the file.

      Press ESC to exit from the access control entry box.


      Chapter 14. TSX Command Summary                                  117


      14.36 FORMAT

      FORMAT Formats diskettes.

      Syntax:

           FORMAT drive: [/qualifiers]

      Qualifiers:

         /4 indicates that this is a 360K diskette in a 1220K drive.

         /7 indicates that this is a 720K diskette in a 1440K drive.

         /8 formats 8 sectors per track.

         /N:n Formats n sectors per track.

         /O  formats  a  diskette which is compatible with versions 1.x of
                 DOS.

         /T:n Formats a diskette with n tracks.  (Maximum 80)

         /V prompts for a volume label for the disk.

         /[NO]QUERY (Default) prompts for  a  diskette  before  and  after
                 format.



      14.37 GOTO

      GOTO Transfers control to a label in a command file.

      Syntax:

           GOTO label



      14.38 HANLOAD

      HANLOAD  Used  by  the  system  manager  to  install loadable device
      drivers.  Normally HANLOAD commands are generated  automatically  by
      the   MAKELOAD  program  and  placed  in  the  system  startup  file
      TSXLOAD.CMD.  Only certain foreign  terminal  support  handlers  are
      supported by TSX-Lite.



      14.39 HELP

      HELP Displays information about system commands and options.


      Chapter 14. TSX Command Summary                                  118


      Syntax:

           HELP [topic]



      14.40 HOST

      Syntax:

           HOST ttname

      The  HOST  command  cross-connects  your  time-sharing  line  with a
      specified communication line.  The HOST command can also be used  to
      do  X,  Y, and Zmodem file transfers.  The HOST command is much more
      efficient than running a  communications  program  like  Procomm  or
      Telix under TSX.

      Syntax:

           HOST com_port [phone_number]

      Examples:

           HOST TTB0
           HOST TTC0 320-1820

      The  "com_port"  argument  is  the name of the communication line to
      which you wish to connect.  This should be the name of a TSX  serial
      device  such as TTB0 (com 1), TTC0 (com 2), etc.  The "phone_number"
      argument is optional.  If specified, the modem command  "ATDT"  will
      be  prepended  to the front of it and the string will be sent to the
      communication line when HOST first starts running.

      "Cross-connecting"  a  communication  line  with  your  time-sharing
      terminal  means  that  each  character  typed  at  your  terminal is
      transmitted on the communication line, and each  character  received
      on  the  communication  line is displayed at your terminal.  Because
      the  system  buffers  characters  between  your  terminal  and   the
      communication  line,  your  terminal  may  operate  at  a  baud rate
      different from that of the cross connected communication line.

      The HOST command is  somewhat  less  efficient  than  the  SET  HOST
      command  described  in Section 14.80 on page 142 but it has two main
      advantages:

      1.  You can use  the  HOST  command  to  perform  file  uploads  and
          downloads using X, Y, and Zmodem transfers.

      2.  The  HOST command processes ANSI control sequences when run from
          the console or PC-term terminals whereas the  SET  HOST  command
          does not.

      Once  the  cross-connection  is  established,  nearly all characters
      typed at your terminal are transmitted  on  the  communication  line


      Chapter 14. TSX Command Summary                                  119


      rather   than  being  interpreted  by  the  system.   This  includes
      characters such as rubout, control-C, control-U, control-W, etc.

      The one character  that  is  interpreted  by  the  system  during  a
      cross-connection  is  the  control-backslash  character.   When this
      character is typed, it is not transmitted on the communication  line
      but  causes  HOST  to  display  a  one  line  menu  with options for
      Uploading a file, Downloading a  file,  or  Exiting.   Type  `U'  to
      begin  an upload, 'D' to begin a download, or 'X' to exit from HOST.
      If you type any other character the cross connection will resume.

      The normal sequence of operations  to  cross-connect  your  terminal
      with a communication line is as follows:

      1.  Use  the ALLOCATE command to allocate the communication line for
          your exclusive use.  This also allows your to perform  temporary
          parameter  settings on the line which will be cancelled when you
          deallocate the line.

      2.  Use the SET TERMINAL command to  set  line  parameters  such  as
          baud rate for the communication line.

      3.  Use  the  HOST  command  to cross-connect your time-sharing line
          with the communication line.

      4.  Type  control-backslash   followed   by   'X'   to   break   the
          cross-connection  and  reconnect  your terminal with the command
          interpreter.

      5.  After  the  cross-connection  is  broken,  use  the   DEALLOCATE
          command  to  release  the communication line.  If the parameters
          set by the SET TERMINAL command were  temporary,  they  will  be
          restored to their permanent values.



      14.41 IF

      The  IF  command  evaluates  a  logical expression and conditionally
      executes a command if the value of the expression is true.  The  DOS
      forms of the IF command are also supported.

      Syntax:

           IF expression THEN command

      DOS Style Syntax:

           IF ERRORLEVEL value command
           IF EXIST filespec command
           IF string1==string2 command


      Chapter 14. TSX Command Summary                                  120


      Examples:

           IF X .EQ. Y THEN GOTO END
           IF ERRORLEVEL 1 THEN EXIT
           IF EXIST FILE.TXT THEN GOTO READFILE

      The  expression  is  evaluated; it may contain operators and lexical
      functions.  If its value contains any characters  other  than  0  or
      space  it is considered to be true and the command following THEN is
      executed.   If  the  value  of  expression  is  zero  or  null,  the
      controlled command is not executed.

      For example, the statement:

           IF SYM1 .EQS. "this is a string" THEN DISPLAY Strings matched

      compares  the string "this is a string" with the value of the symbol
      SYM1.  Note  that  it  was  not  necessary  to  use  the  apostrophe
      substitution operator to get the value of SYM1.

      Examples:

           S1:= string1
           S2:= string2
           IF S1 .EQS. S2 THEN DISPLAY S1 is equal to S2

      This  test  compares  the  values of the symbols S1 and S2.  In this
      case the strings are not  equal,  so  the  DISPLAY  command  is  not
      executed.

           I = 1;
           IF I .LT. 10 THEN @DOMORE

      In  this  example the expression is true, so the DOMORE command file
      is executed.

      The expression can be quite complex and involve  lexical  functions.
      For example, the statement:

           IF (COUNT.LE.10).OR.$LENGTH(ANSWER).LT.3 THEN EXIT

      executes  the  EXIT  statement if the value of COUNT is less than or
      equal to ten or the length of the string associated with the  ANSWER
      symbol  is less than 3.  See Section 9.10 for additional information
      about lexical functions.



      14.42 INITIALIZE

      INITIALIZE Initializes removable disks  and  tapes.   This  has  the
      effect of deleting all files on the device.


      Chapter 14. TSX Command Summary                                  121


      Syntax:

           INITIALIZE drive



      14.43 INQUIRE

      INQUIRE  Reads  a  string  from  the  terminal  and  assigns it to a
      symbol.

      Syntax:

           INQUIRE symbol [prompt]

      Examples:

           INQUIRE YESNO Do you wish to continue?

      The INQUIRE command gets a string from the terminal and  assigns  it
      to  a  local  symbol.   The  input comes from the terminal even if a
      command file is in operation.  Since the  input  always  comes  from
      the  terminal,  this command is useful for prompting for values from
      within a command file.   The  value  which  is  collected  from  the
      terminal is the entire input line, including any spaces.



      14.44 JMAN

      JMAN  is  a full screen job management utility.  Use JMAN to display
      information about currently executing jobs and  perform  common  job
      related  system management functions.  These include displaying open
      files for a job and killing a job.

      Syntax:

           JMAN

      In response to the JMAN command, TSX displays a  list  of  the  jobs
      currently executing on the system.

      A  menu  of action keys appears to the right of the job list; choose
      an action by typing the appropriate key.



      14.45 KERMIT

      KERMIT  Invokes  the  Kermit  file  transfer  program.   Kermit   is
      provided  as  part  of  the  optional  TSX-Lite  Utilities  Kit (see
      REGISTER.DOC).


      Chapter 14. TSX Command Summary                                  122


      14.46 KEYLOAD

      The KEYLOAD commands loads the character mapping tables  needed  for
      international keyboard support.

      Syntax:

           KEYLOAD[/LINE] file.KEY

      Where  'file.KEY'  is  a  keyboard mapping file such as ITALY.KEY or
      GERMAN.KEY.  If  the  /LINE  qualifier  is  specified  the  keyboard
      mapping  applied only to the line executing the command.  Otherwise,
      it applies to all lines on the system.

      See Section 3.6 on page 27 for more information about this command.



      14.47 KILL

      KILL is a synonym for STOP.  See the description  of  STOP  on  page
      163 for information.



      14.48 LOGOFF

      LOGOFF  Logs  off  the  current  job.  You can use OFF or BYE if you
      prefer.

      Syntax:

           LOGOFF
           OFF

      Qualifiers:

         /NOACCOUNTING Disables reporting of  the  accounting  information
                 to your terminal.



      14.49 MACROS

      MACROS  Invokes  macro  definition  program to edit or load keyboard
      macros.

      Syntax:

           MACROS[/qualifiers] [filespec]

      Examples:

           MACROS
           MACROS/LOAD TED.MAC


      Chapter 14. TSX Command Summary                                  123


      Qualifiers:

         /LOAD Load macro definitions from specified file.

         /SYSTEM Make macros available for all lines on the system.

      The MACROS facility associates  a  sequence  of  keystrokes  with  a
      single  keystroke.   Macros can only be used with workstations which
      send make/break codes into the system.  This  includes  the  console
      keyboard,  PC-term  terminals,  and  TSXTERM terminals.  You may not
      used macros from ASCII terminals such as the VT300.

      Macros are most commonly used  to  provide  a  shorthand  method  of
      entering  common  commands.  For example, you may want to define the
      F10 key to generate the command:

           DIR/SINCE=YESTERDAY

      Macro  definitions  may  be  stored  in  a  file   and   loaded   in
      automatically  when  the  system boots (for system wide definitions)
      or when you log in (for line specific definitions).

      The MACROS command makes available macros from the  specified  file,
      as  well  as any revisions you make in edit mode.  These definitions
      are active for your time-sharing line, even after you  log  off  and
      back  on.   Use  the /SYSTEM qualifier to specify that macros are to
      become available for  all  lines  on  the  system.   Use  the  /LOAD
      qualifier  to  load  macros  from  the  specified  file  without any
      interactive editing.

      Suppose you require a shorthand method of entering the command

           PRINT/QUEUE=LASER1/STOCK=LETTERHEAD LEADS.TMP

      and decide that the key sequence ALT-P is  a  natural  mnemonic  for
      this command.  You can issue the command

           MACROS

      to  operate  the key definition facility in edit mode to specify the
      definition.  The facility provides  you  with  instructions  on  the
      screen.    Commands   are   entered  with  two  keystroke  sequences
      beginning with the ESCAPE key.  Any other key you press  allows  you
      to  associate  a macro definition for that key.  Hence you hold down
      the ALT key and press P.

      The macro definition facility informs you that you are  now  editing
      the  definition  of  "LALT-P"  or "RALT-P", depending on whether you
      pressed the left or right ALT  key.   The  facility  allows  you  to
      establish  separate  definitions  for every key in each of six shift
      states: unshifted, shifted, left ALT, right ALT, left  CONTROL,  and
      right CONTROL.

      The  MACROS  program  will  show you the current definition, if any,
      when you redefine  a  key.   Note  that  MACROS  is  only  aware  of


      Chapter 14. TSX Command Summary                                  124


      keyboard  macros  defined  in the file you are editing, or which you
      have specified in the current session.   MACROS  can  not  determine
      whether  a  key  has  been  defined  in  a  different  file  or in a
      different session.

      If the macro is being used with a  16-bit  DOS  program  that  takes
      over  keyboard interrupts, such as WordPerfect, the macro definition
      may not exceed 16 characters in length.

      After  you  finish  entering  the  macro  definition  press   ESCAPE
      followed  by  'E'  to exit the macro definition facility.  The macro
      you established will remain active for your  line,  even  after  you
      log  off.   Only  rebooting  the  system  or using the MACRO command
      again will erase or alter the definition of ALT-P.

      Let us now suppose that you wish to store  this  definition  in  the
      file  CINDY.KEY  so you do not have to respecify the definition each
      time the system is booted.  Use the command

           MACROS CINDY.KEY

      to create (or edit an existing) file named CINDY.KEY.  Re-enter  the
      definition of ALT-P and exit normally using ESCAPE followed by 'E'.

      To  force  the  macros in file CINDY.KEY to be loaded for your line,
      you can place the command

           MACROS/LOAD CINDY.KEY

      in your line specific startup command procedure.

      If you wish to establish  system-wide  macro  definitions,  place  a
      command  of  the  following  form  in  your  SY:LSTARTUP.CMD  system
      start-up command file:

           MACROS/LOAD/SYSTEM filename



      14.50 MAIL

      MAIL Starts the MessageNet electronic mail program.   MessageNet  is
      provided   with   the   optional   TSX-Lite   Utilities   Kit   (see
      REGISTER.DOC).



      14.51 MD

      MD is a synonym for MKDIR.  See MKDIR for information.


      Chapter 14. TSX Command Summary                                  125


      14.52 MESSAGE

      MESSAGE Displays the  error  message  text  for  the  specified  TSX
      status code.  MSG is an equivalent.

      Syntax:

           MESSAGE message_code

      Examples:

           MESSAGE 30010041
              ?TSX-E-INSUFMEM, Insufficient memory for allocation
           MESSAGE 301E0009
              ?RTL-E-FCH2BIG, Fortran character string too long



      14.53 MKDIR

      MKDIR  Creates  subdirectory  files.   It  is  equivalent  to the MD
      command.

      Syntax:

           MKDIR dirspec
           MD dirspec



      14.54 MN

      MN is a synonym for MAIL.



      14.55 OFF

      OFF is a synonym for LOGOFF.  See LOGOFF for information.



      14.56 ON

      ON is used to declare a statement that  is  to  be  executed  if  an
      error  occurs.   You can specify different statements to be executed
      based on the error severity level.

      Syntax:

           ON INFORMATION THEN statement
           ON WARNING THEN statement
           ON ERROR THEN statement
           ON NONE


      Chapter 14. TSX Command Summary                                  126


      Specify one of the keywords INFORMATION, WARNING, ERROR, or NONE  to
      indicate  what  error  severity  level  is  to trigger the statement
      specified by "statement".  If an error of the specified severity  or
      greater  occurs  in  the  command  file,  the  stored  statement  is
      executed.  If you specify ON NONE  then  no  statement  is  executed
      when a subsequent error occurs.

      As an example, consider the following statements:

           ON ERROR THEN GOTO ABORT
           COPY LAB1.DAT A:LAB1.DAT
           COPY LAB2.DAT A:LAB2.DAT
           COPY LAB3.DAT A:LAB3.DAT
           EXIT
           ABORT:
           DISPLAY "Copy error occurred"
           EXIT/ABORT

      The  first  statement  in  this  example  specifies that if an error
      occurs on  subsequent  statements  in  the  command  file  then  the
      statement  "GOTO  ABORT"  is to be executed, transferring control to
      the ABORT label.

      If you simply want to cause a command file to terminate if an  error
      occurs, specify the statement:

           ON ERROR THEN EXIT

      Or,  if  you  wish  to  abort  all  nested  command  files,  use the
      statement:

           ON ERROR THEN EXIT/ABORT

      Only a single ON statement can be in  effect  for  a  command  file.
      Thus  is  you  specify  ON ERROR...  and later specify ON WARNING...
      the second ON statement will supersede the first.

      Each level of command file nesting may have its  own  ON  statement.
      Outer  level ON statements apply to nested command files unless they
      have local ON  statements.   When  a  command  file  exits,  the  ON
      statement appropriate to the next higher level takes effect.



      14.57 PATH

      PATH defines or displays search path.

      Syntax:

           PATH [pathspec]

      If  you  want to define a path for all users, place a command of the
      following  form  in  your  SY:LSTARTUP.CMD   system-wide,   start-up
      command file:


      Chapter 14. TSX Command Summary                                  127


           SET/SYSTEM PATH=pathspec



      14.58 PAUSE

      PAUSE pauses command file execution until Return key is pressed.

      Syntax:

           PAUSE [message]

      Examples:

           PAUSE Mount second output disk
           PAUSE Press Return when ready...



      14.59 PHONE

      PHONE   connects   to   another   terminal   to  carry  on  a  2-way
      conversation.  See the description of the SEND command  on  page  65
      for information about sending a message to another user.

      Syntax:

           PHONE [user_name]
           PHONE [terminal_name]

      See  Section  10.2.5 on page 66 for additional information about the
      PHONE command.



      14.60 PMAN

      The PMAN command allows you to associate  attributes  with  programs
      so  that  the  attributes  are  used  by TSX whenever the program is
      executed.  A program whose  attributes  have  been  specified  using
      PMAN  is  referred  to  as  having  been  "installed"  in TSX.  Many
      attributes can be set with PMAN, some of which can have  a  dramatic
      effect  on  the performance of programs running under TSX.  However,
      it is not necessary to "install" most programs with  PMAN  in  order
      to  use  them  with  TSX; PMAN simply specifies parameters that tune
      the execution of a program under TSX.

      When you use  PMAN  to  associate  attributes  with  a  program  the
      attribute  settings  take  effect  immediately  (you  do not need to
      reboot TSX).  In addition, PMAN updates a file  in  the  TSX  system
      directory  named  INSTALL.CMD  with information about the attributes
      for each program.  The INSTALL.CMD file  is  executed  automatically
      each  time  TSX  is  booted  so the attributes will remain in effect
      over system restarts.


      Chapter 14. TSX Command Summary                                  128


      See Chapter 4 for additional information about using PMAN.



      14.61 PRINT

      PRINT Submits a request to the spooler to print one or  more  files.
      You  can  use  the PRINT command or the QMAN program to check on the
      status of jobs in the print queue.

      Syntax:

           PRINT[/qualifiers] filespec

      Qualifiers:

         /AFTER[=date-time] Print files created after this date/time.

         /BEFORE[=date-time] Print files created before this date/time.

         /[NO]BINARY Print in "binary" mode.

         /[NO]CONFIRM Request confirmation before each file is printed.

         /COPIES=n Print each file in print job this number of times.

         /DATE[=date] Print files created on this date.

         /[NO]DELETE Delete file after printing.

         /[NO]DOUBLESPACE Print files doublespaced.

         /ENDPAGE=n Stop printing at this page.

         /EXCLUDE=(files) Don't print specified files.

         /[NO]FEED Issue form feeds between pages.

         /FLAG[=(JOB[=n],FILE[=n],NOJOB,NOFILE)] Specify printing of  flag
                 pages.

         /FORM=formname Use the specified form.

         /[NO]HEADER Put header lines on each page of print job.

         /[NO]HOLD  Hold  job  until  released  with  SET  ENTRY id/NOHOLD
                 command.

         /[NO]IDENTIFY Display queue name and id number on print job.

         /LENGTH=n Start a new page after this many lines (default: 66).

         /[NO]LOG Display the name of each file printed.


      Chapter 14. TSX Command Summary                                  129


         /MARGIN=(LEFT=lmar, RIGHT=rmar,  TOP=tmar,  BOTTOM=bmar)  Specify
                 margins.

         /NAME=nametext Specify the job name.

         /NOTE="notetext" Print notetext on job and file flag pages.

         /[NO]NOTIFY   Display  a  message  on  terminal  when  print  job
                 completes.

         /[NO]PASSALL Equivalent to /BINARY.

         /PRIORITY=n Run print job at this priority.

         /QUEUE=queuename Submit job to the specified print queue.

         /QUIET Do not display the job name, entry number,  and  the  name
                 of the queue.

         /[NO]RESET=   ([NO]FILE=file,FORMATTED],[NO]JOB=file[,FORMATTED])
                 Use the specified reset files.

         /[NO]RESTART Restart printing after a system reboot.

         /[NO]SETUP=   ([NO]FILE=file[,FORMATTED],[NO]JOB=file[,FORMATTED]
                 Use the specified setup files.

         /SINCE[=date-time]    Print   files   created   since   specified
                 date/time.

         /[NO]SPACE Same as [NO]DOUBLESPACE.

         /STARTPAGE=n Start printing at this page.

         /STOCK=stockname Use this paper stock for job.

         /[NO]TRAILER[=(JOB[=n],FILE[=n],NOJOB,NOFILE)   Specify   trailer
                 pages.

         /[NO]TRUNCATE Truncate lines that extend beyond right margin.

         /WIDTH=n Page is this many characters wide, including margins.

         /[NO]WRAP Wrap line that extend beyond right margin.

      If  you  type  PRINT  without  specifying a file name, a list of all
      pending print jobs will be displayed.  You can  also  use  the  QMAN
      program  to  check  on  the  status  of  print jobs.  See Chapter 8,
      starting on page 48, for additional information  about  the  use  of
      spooled printers.


      Chapter 14. TSX Command Summary                                  130


      14.62 PROMPT

      PROMPT  Changes  the  prompt string that is displayed by the command
      processor.

      Syntax:

           PROMPT [string]



      14.63 PROTECT

      PROTECT sets the file protection attribute on one or more files.

      Syntax:

           PROTECT[/qualifiers] filespec

      Qualifiers:

         /BEFORE[=date-time] Select only files  created  before  specified
                 date/time.

         /[NO]CONFIRM Request confirmation before acting on each file.

         /DATE[=date] Select files created on specified date.

         /EXCLUDE=(files) Exclude specified files.

         /[NO]LOG Display each file name on terminal.

         /NEW Select only files created today.

         /[NO]QUERY Same as /[NO]CONFIRM.

         /SINCE[=date-time]   Select   files   created   since   specified
                 date/time.

      Examples:

           PROTECT MAINTEST.C
           PROTECT TEST1.DAT,TEST2.DAT,TEST3.DAT
           PROTECT *.C



      14.64 QMAN

      The QMAN command invokes a screen  oriented  queue  manager  program
      for  creating and modifying print and batch queues.  It is also used
      to define and modify print forms and to delete or  modify  print  or
      batch jobs.


      Chapter 14. TSX Command Summary                                  131


      Syntax:

           QMAN

      The  initial  screen  shows  a list of all currently existing queues
      (both print and batch).  Along the right side of  the  screen  is  a
      menu  of action keys that can be pressed to perform functions on the
      queues.  Use the arrow keys to select  a  queue  and  then  type  an
      action  key to perform the desired function.  Extensive on-line help
      is available for QMAN; type F1 at any point for help  regarding  the
      current situation.  Press ESC to exit from QMAN.

      See  Chapter  8,  starting  on  page  48, for additional information
      about the use of QMAN.



      14.65 R

      The R command runs a  program  which  is  located  in  the  SY  area
      (\TSX32SYS).

      Syntax:

           R[/qualifiers] program

      Qualifiers  are the same as those used for the RUN command (see page
      135).



      14.66 RD

      RD is a synonym for RMDIR.  See RMDIR for information.



      14.67 RECALL

      The RECALL command displays the set of saved commands and recalls  a
      specific  saved  command  either  by specifying an index number or a
      string that matches the beginning of the command.

      Syntax:

           RECALL[/qualifiers] [selector]

      Qualifiers:

         /REVERSE Display commands from oldest to newest.

      If you use  the  RECALL  command  without  specifying  a  "selector"
      parameter,  a  numbered  list  of  all  saved commands is displayed.
      Normally, the most recently saved command  is  displayed  first  and
      the  oldest  command  is  displayed  last.  You can use the /REVERSE


      Chapter 14. TSX Command Summary                                  132


      qualifier to reverse the order of display.  An example of  a  RECALL
      command list is shown below:

             1: RUN TEST
             2: LINK TEST
             3: COMPILE TEST
             4: EDIT TEST

      The  number  displayed to the left of each command is an index which
      can be used to recall a saved command.  For example,  the  following
      command  recalls the third saved command (the "COMPILE TEST" command
      in this example):

           RECALL 3

      You can also use a character string to specify  the  command  to  be
      recalled.   The characters in your selector string are compared with
      the beginning characters of each saved command in the  order  newest
      to  oldest.   The first command that matches the specified string is
      recalled.  For example, the following command recalls  the  "COMPILE
      TEST" command:

           RECALL COMP

      See also Sections 3.2 and 14.77.



      14.68 RENAME

      RENAME  renames one or more files.  You can also use this command to
      rename directories.

      Syntax:

           RENAME[/qualifiers] old_name new_name

      Qualifiers:

         /BEFORE[=date-time] Select files created  before  specified  date
                 and time.

         /[NO]CONFIRM Request confirmation before renaming each file.

         /DATE[=date] Select files created on the specified date.

         /EXCLUDE=(files) Exclude specified files.

         /[NO]LOG Display file names after each file is renamed.

         /NEWFILE Select only files created today.

         /[NO]QUERY Same as /[NO]CONFIRM


      Chapter 14. TSX Command Summary                                  133


         /[NO]REPLACE (Default) Overwrite existing files.

         /SINCE[=date-time]   Select   files   created   since   specified
                 date/time.



      14.69 RESTORE

      RESTORE restores files from a  backup  save  set  created  with  the
      BACKUP command.

      Syntax:

           RESTORE[/qualifiers] save-set [out-spec]

      Qualifiers:

         /AFTER[=date-time]  Select files created since specified date and
                 time.

         /BEFORE[=date-time] Select files created  before  specified  date
                 and time.

         /BELL Ring the bell during volume change operations.

         /[NO]CRC Perform CRC checksum calculations.

         /[NO]CONFIRM Confirm whether each file should be restored.

         /DIRECTORY List the contents of the input save set.

         /EXCLUDE=(files) Exclude the specified files.

         /INCLUDE=(files) Include only the specified files.

         /LIST Same as /DIRECTORY

         /LOCAL Place files on the local network node.

         /[NO]LOG (Default) Display name of each file restored.

         /REPLACE Overwrite existing files with the same name.

         /SINCE[=date-time] Same as /AFTER.

         /[NO]WARN Print a warning message if a file cannot be restored.

      The  simplest  RESTORE  command  specifies  that  all files from the
      input save set should be copied to their  original  location  (i.e.,
      the  device  and  directory  where they were when BACKUP created the
      save set).  An example of such a command is:

           RESTORE B:SAVE1


      Chapter 14. TSX Command Summary                                  134


      All files in save set B:SAVE1.BSS are  restored  to  their  original
      location.   Variants  of  the RESTORE command select which files are
      restored from the input save set and also specify what  devices  and
      directories they are written to.

      The  contents  of  a  save  set  can be listed without restoring any
      files by using the /LIST qualifier, as in the command:

           RESTORE/LIST A:FULL.BSS

      You can select only certain files from the save  set  by  using  the
      /INCLUDE qualifier.  For example, the command:

           RESTORE/INCLUDE=*.C  A:FULL

      restores only files having the extension ".C".

      Directory  specifications  can  be used in the /INCLUDE qualifier as
      well.  The command

           RESTORE/INCLUDE=\TRAUMA\*.*  A:FULL.BSS

      restores all files from the \TRAUMA\ directory and

           RESTORE/INCLUDE=\TRAUMA\...\*.*  A:FULL.BSS

      selects the subdirectories of \TRAUMA\ as well.   If  you  know  you
      want  some,  but not all files matching a /INCLUDE criteria, you can
      use the /CONFIRM qualifier.  When you use this you are  asked  on  a
      file by file basis whether you really want the file restored.

      In  addition  to selecting files, you can use the /EXCLUDE qualifier
      to specify files that are not to be restored.   This  qualifier  can
      be used by itself or in combination with /INCLUDE.  For example,

           RESTORE/INCLUDE=*.C/EXCLUDE=\TSX32\KERNEL\*.C  A:FULL

      restores  all  files  with  an  extension of ".C" except those which
      reside in directory \TSX32\KERNEL.

      To specify that output files  should  be  restored  to  a  different
      device  or  directory  than  where  they  originally  resided  it is
      necessary to provide an output  file  specification.   Suppose,  for
      example,  that save set FULL.BSS contained a backup of device C: but
      you want to restore the files to device D:.  The  following  command
      command does this.

           RESTORE A:FULL.BSS D:

      The  elements present in the output specification (in this case only
      the device name) are used first in constructing  the  name  of  each
      output  file.   Then  any  missing parts are taken from the original
      filename.  Thus, the  files  will  be  restored  to  their  original
      directories but on device D: rather than C:.


      Chapter 14. TSX Command Summary                                  135


      The  following  command restores only the files with an extension of
      ".DAT" to a single specific output directory named \TEMP,

           RESTORE/INCLUDE=*.DAT  A:FULL.BSS  DHA0:\TEMP\*.*

      The RESTORE facility will create directories as necessary  to  write
      output  files  so  that  is  not necessary that the target directory
      even exist when the RESTORE command is  issued.   If  directory  and
      subdirectory  files  are  restored,  all nonexisting portions of the
      directory tree will be created.

      The RESTORE facility can recover files even when some of  the  input
      save  set  is missing or damaged.  If a single save set block cannot
      be read due to faulty media, RESTORE will reconstruct the lost  data
      using the redundancy blocks written by the BACKUP facility.

      If  you  lose  some volumes of a multi-volume save set you can still
      recover the files which reside on the remaining volumes.   In  fact,
      if  you  know in what order files were backed up and you have a save
      set spanning several  volumes,  you  may  want  to  skip  the  first
      volumes  and  begin  the  restore  operation with volumes containing
      files you want.



      14.70 RMDIR

      RMDIR deletes subdirectory files.  It is equivalent to RD.

      Syntax:

           RMDIR dirspec
           RD dirspec



      14.71 RUN

      RUN begins the execution  of  a  program.   This  is  equivalent  to
      typing  the  name  of the program; however, by using the RUN command
      you can specify the qualifier shown below to apply to the  program's
      execution.

      Syntax:

           RUN[/qualifiers] program

      Qualifiers:

         /BYPASN Don't perform logical device name assignments.

         /DOSNET  Tell DOS programs that all of its files are on networked
                 devices.


      Chapter 14. TSX Command Summary                                  136


         /[NO]DWRITE Allow program to directly access video memory.

         /[NO]GRAPHICS Same as /[NO]DWRITE.

         /HOLDPRIORITY  Don't  reduce  priority  when  user  switches   to
                 subprocess.

         /IOMAP Map virtual memory from 640Kb to 1MB to physical memory.

         /IOPRIV  Allow the privileged machine instructions: CLI, STI, IN,
                 OUT, INS, and OUT (this is the default).

         /KBINT Allow program to take over the keyboard interrupt vector.

         /LOCK Log off when program completes.

         /NOCFIN Do not take input to program from command file.

         /NONINT Run in "non-interactive".

         /NORUNDIS Suspend program when user switches to a subprocess.

         /NOSHARE Don't share the executable program with other users.

         /[NO]TTWAIT Suspend program  after  default  number  of  terminal
                 input loops.

         /NOVARY3BA Always set video port 3BA to 0x80.

         /OPT3BA  Optimize  programs  doing  IN operations from video port
                 3BA.

         /SCCA Disallow Control-C abort of program.

         /TTCKIO Allow more terminal input loops after an I/O operation.



      14.72 SEARCH

      SEARCH searches files for strings of text.

      Syntax:

           SEARCH[/qualifiers] filespec string

      Qualifiers:

         /BEFORE[=date-time]  Selects  files  created   before   specified
                 date/time.

         /BLOCK Read file in blocks of 512 bytes instead of records.

         /[NO]BRIEF (Default) Display file name on same line as string.


      Chapter 14. TSX Command Summary                                  137


         /DATE[=date] Selects files created on the specified date.

         /EXACT Do a case-sensitive search.

         /EXCLUDE=(files) Exclude specified files.

         /[NO]HEADER (Default) List file names in the output.

         /LENGTH=length Specify maximum length of input records.

         /LF Records are delimited with line-feeds alone.

         /[NO]LOG Display the name of each file before it is searched.

         /NAMES Display file names containing matches only.

         /NEW Search only files created today.

         /OUTPUT=file Redirects search output to specified file.

         /REGULAR  Search  strings  are  regular  expressions, not literal
                 text strings.

         /REX Same as /REGULAR.

         /SINCE[=date-time] Select files created since specified date  and
                 time.

      The  SEARCH  command  locates occurrences of a specified text string
      in a set of files.  For example, the  following  command  looks  for
      the text string "ALPHA" in a file named PARTICLE.C:

           SEARCH PARTICLE.C ALPHA

      Wildcards  are  frequently  used  in the file specifications for the
      SEARCH command.  For example, the  following  command  searches  for
      all  occurrences of the string ALPHA in all files with the extension
      ".C" in the current directory:

           SEARCH *.C ALPHA

      The "..." wildcard construct can be useful with the SEARCH  command.
      The  following  command  searches  for  the string BETA in all files
      with the extension ".C" in the \PILOT directory and all  directories
      below it:

           SEARCH \PILOT\...\*.C BETA

      See  Section 5.2, page 40, for additional information about wildcard
      constructs.

      It is often desirable to use SEARCH  to  identify  a  set  of  files
      which   need   some  further  processing  (such  as  editing).   The
      following command creates a file X.X containing  the  names  of  all
      files with an extension of ".C" containing the string "SPFUN":


      Chapter 14. TSX Command Summary                                  138


           SEARCH *.C SPFUN/OUT=X.X/NAMES

      If  the  search  string  contains  spaces  or  characters other than
      letters  and  digits,  enclose  the  string  in  quote  marks.   For
      example, the following command searches for the string "NEW YORK":

           SEARCH *.DAT "NEW YORK"

      The  SEARCH  command  allows  you  to  specify  more than one search
      string.  When this is done, any occurrence of  any  of  the  strings
      will  be found.  For example, the following command searches for the
      strings CALIFORNIA, TEXAS, and NEW YORK:

           SEARCH *.LST CALIFORNIA,TEXAS,"NEW YORK"

      Output can be redirected using the  /OUTPUT=file  qualifier.   Names
      of  files  can  be suppressed using the /NOHEADER qualifier.  Use of
      the /NAMES qualifier specifies that output should  consist  only  of
      file  names  instead  of  data  from  the file.  Finally, the /BRIEF
      qualifier specifies that each line of output should contain  both  a
      filename and the target record.

      SEARCH  normally reads in individual records of a file and looks for
      search strings within a record.  This is appropriate for text  files
      which  use  carriage-return line-feed sequences to mark the end of a
      record.  Since Unix systems delimit records with line-feeds (but  no
      carriage  returns),  the  /LF  option  can  be  used to specify this
      alternate record delimiter.  If the input file does not  consist  of
      records  at  all,  the  /BLOCK qualifier can be used to specify that
      the input file be searched in single 512  byte  blocks.   Note  that
      search  strings  which  begin in one block but end in the next block
      will not be matched.  The /BLOCK qualifier  can  not  be  used  with
      /BRIEF mode.

      A  "regular  expression"  describes  a  pattern of text instead of a
      literal  text  string.   The  syntax  used  to  describe  a  regular
      expression   search   pattern   consists  of  letters,  digits,  and
      operators  such  as  '*',  '+',  '$',  and   '%'.    Using   regular
      expressions  you  can search for complex patterns.  For example, the
      following SEARCH command locates the phrase "NEW YORK" allowing  the
      words  "NEW"  and  "YORK" to be separated by spaces on the same line
      or split across two lines.

           SEARCH/REGULAR *.TXT "NEW#+YORK"

      The following SEARCH command locates all  occurrences  of  the  word
      "void"  as the first word on a line allowing spaces and tabs only to
      occur between the start of the line and the word:

           SEARCH/REGULAR *.C "$%W*void"

      Because of the operator characters that are usually used in  regular
      expressions,  you  will need to enclose regular expressions in quote
      marks.  The SEARCH command strips  off  the  enclosing  quote  marks
      before  interpreting the search pattern.  In some cases you may need


      Chapter 14. TSX Command Summary                                  139


      to specify quote signs as part of  the  regular  expression  itself.
      To  do  this,  enclose the entire pattern in quote marks (") and use
      the apostrophe character (') to quote the desired string within  the
      pattern.   For  example, the following command searches for a string
      consisting of two dollar signs, followed  by  one  or  more  digits,
      followed by a colon:

           SEARCH/REGULAR *.ASM "'$$'%D+':'"

      Refer  to  the EDIT-32 User's Guide for additional information about
      using regular expressions.   The  table  below  lists  each  regular
      expression operator.

           Expression               Meaning                   Example
           ----------    ---------------------------------    -------
               c         any non-operator character c           a
              \c         character c literally                  \$
              's'        string s literally                   '$2.50'
               .         any character but line-delimiter       a.b
               $         line delimiter (end of line)          $begin
               #         space or line-delimiter              New#York
              [s]        any character in s                     [abc]
              (p)        subpattern p                          a(b|c)d
              ~p         anything but p                          ~%D
              p*         zero or more occurrences of p           a*
              p+         one or more occurrences of p            a+
              p?         zero or one occurrence of p             a?
            p{m,n}       m to n occurrences of p               a{1,3}
             p1p2        p1 followed by p2                    [ab][cd]
             p1&p2       item must be p1 and p2                %D&~0
             p1|p2       item may be p1 or p2                 a(b|c|d)
              %A         upper- or lower-case letter
              %C         control character
              %D         decimal digit (0..9)
              %H         hexadecimal digit (0..9 or A..F)
              %L         lower-case letter
              %N         letter or digit
              %P         printing character
              %Q         quote mark (")
              %U         upper-case letter
              %W         "white space" -- space or tab
              %X         any char including line-delimiter
              %(         open paren with matching close paren
              %[         open bracket with matching close bracket
              %{         open brace with matching close brace



      14.73 SEND

      SEND   sends   a  message  to  another  user's  terminal.   See  the
      description of the PHONE command on page 66  for  information  about
      conversing with another user.


      Chapter 14. TSX Command Summary                                  140


      Syntax:

           SEND[/qualifiers] message

      Examples:

           SEND/NAME=PHIL/FORCE  I think the computer is on fire.
           SEND/TERM=COMPUTER_ROOM Please mount backup disk

      Qualifiers:

         /ALL Send to all jobs (except the sender).

         /FORCE Override /GAG setting on other terminals.

         /ID=job_id Send to specified job id number.

         /NAME=user_name Send to specified user.

         /NOBELL Don't ring bell on receiving terminals.

         /PARENT Send to parent of current process.

      See  Section  10.2.4 on page 65 for additional information about the
      SEND command.



      14.74 SET CMDPROC

      The SET CMDPROC command allows you to specify the name of a  program
      to  act  as  the  command  processor for your job.  You can also use
      this command to specify a program to be run when some other  program
      exits.

      Syntax:

           SET CMDPROC /FILE=name[/qualifiers]

      Qualifiers:

         /FILE=name (Required) Specify name of command processor program.

         /TEMP Use new command processor only once then use TSKMON.

      The   SET   CMDPROC   command   allows   you  to  provide  the  file
      specification of a program to be used as the command  processor  for
      your  job.   The command processor is the program that is run by TSX
      when a program exits to the system.   The  initial  default  command
      processor  for  each  job  is  SY:TSKMON.EXP  which  can process the
      keyboard commands described in the TSX-32 User's Manual.

      If the /TEMP qualifier is not specified with  this  command,  a  new
      default  command processor is established for your job.  Each time a
      program exits, either normally  or  do  to  an  abort,  the  current


      Chapter 14. TSX Command Summary                                  141


      default  command processor is executed.  Be careful about using this
      command because unless your program  correctly  processes  commands,
      or  resets TSKMON as the default command processor, you will have no
      way to regain  control.   Note  that  typing  control-C  aborts  the
      current  program and causes the current default command processor to
      be run.

      The /TEMP qualifier may be  used  to  declare  a  temporary  command
      processor  that  will  be  executed  only once when the next program
      exit occurs.  After that, the current default command processor  for
      your  job  will  be  used.  The /TEMP qualifier is useful in that it
      allows you to specify a program to do cleanup  processing  for  some
      other program.



      14.75 SET DATE

      SET  DATE  sets the system date.  Date format is dd-mmm-yyyy.  It is
      equivalent to DATE.

      Syntax:

           SET DATE date
           DATE date



      14.76 SET DEFAULT

      SET DEFAULT is equivalent to CHDIR.  See CHDIR for information.



      14.77 SET EDIT

      SET EDIT controls the terminal input (command line) editor.

      Syntax:

           SET EDIT/qualifiers

      Qualifiers:

         /INSERT Start editor in insert mode.

         /OVERSTRIKE Start editor in overstrike mode.

         /KEYPAD Turn on numeric keypad editing keys.

         /NOKEYPAD (Default) Use keypad as in DOS.

         /[NO]KEYSUBSTITUTIONS (Default) Do DEFINE KEY substitutions.


      Chapter 14. TSX Command Summary                                  142


         /MAXUKD=n Allow n key definitions.

         /MAXUKDLENGTH=n Allow key replacement string  of  maximum  length
                 n.

         /OFF Turn off the terminal input editor.

         /ON (Default) Turn on the terminal input editor.

         /SAVESIZE=n Recall a maximum of n command lines.

      See also Sections 3.2 and 14.67.



      14.78 SET ENTRY

      SET  ENTRY  is  used to control batch or print jobs.  Using the QMAN
      program is the preferred way to do this.  See  Chapter  8,  starting
      on  page  48,  for  additional information about the use of QMAN and
      spooled printers.



      14.79 SET EVENT

      SET EVENT starts or stops writing to  event  log  files.   The  SHOW
      EVENTS command is the preferred way to do this (see page 157).

      Syntax:

           SET EVENT/qualifiers

      Qualifiers:

         /[NO]FILE Create log of file operations.

         /[NO]FLOCK Create log of file lock operations.

         /[NO]SECURITY Create log of security operations.



      14.80 SET HOST

      SET  HOST  cross-connects your terminal with a communication port or
      network node.  Once connected, characters  typed  at  your  terminal
      are  sent to the designated line and characters received from it are
      displayed on your  terminal.   Type  control-backslash  followed  by
      Enter to break the connection.

      Syntax:

           SET HOST ttname


      Chapter 14. TSX Command Summary                                  143


      The  SET  HOST  command cross-connects your time-sharing line with a
      specified communication line.   "Cross-connecting"  a  communication
      line  with  your  time-sharing  terminal  means  that each character
      typed at your terminal is transmitted  on  the  communication  line,
      and  each  character received on the communication line is displayed
      at your terminal.  Because the  system  buffers  characters  between
      your  terminal and the communication line, your terminal may operate
      at  a  baud  rate  different  from  that  of  the  cross   connected
      communication line.

      Note:  The  SET  HOST  command  does  not  do  ANSI  escape sequence
      processing when run from the console so it does not work well  as  a
      communications  program  when  dialing  into  a  bulletin  board.  A
      better choice for this type  of  application  is  the  HOST  command
      described  in  Section  14.40  on  page  118.   The  HOST command is
      somewhat less efficient than  SET  HOST  but  performs  ANSI  escape
      sequence  processing and allows you to perform X, Y, and Zmodem file
      transfers.

      Once the cross-connection  is  established,  nearly  all  characters
      typed  at  your  terminal  are transmitted on the communication line
      rather  than  being  interpreted  by  the  system.   This   includes
      characters such as rubout, control-C, control-U, control-W, etc.

      The  one  character  that  is  interpreted  by  the  system during a
      cross-connection is defined by the "CCXCTL"  sysgen  parameter.   By
      default,  it  is  the  control-backslash character (hex 0x1C).  When
      this character is typed, it is not transmitted on the  communication
      line  but causes the system to interpret the next typed character as
      a cross-connection function character.  Type  carriage-return  after
      control-backslash  to  break the cross-connection and return control
      to the  program  that  initiated  the  cross-connection.   Type  two
      consecutive   control-backslash   characters  to  cause  one  to  be
      transmitted through the communication line.  Other  cross-connection
      function characters are listed in the following table:

           Character                      Meaning
           ---------       --------------------------------------
               B           Transmit a break
               C           Break connection and drop DTR
               D           Raise DTR
               H           Drop DTR (hangup)
               R           Reset XON/XOFF status
               X           Break connection without dropping DTR
             Enter         Break connection and drop DTR

      The  normal  sequence  of  operations to cross-connect your terminal
      with a communication line is as follows:

      1.  Use the ALLOCATE command to allocate the communication line  for
          your  exclusive use.  This also allows your to perform temporary
          parameter settings on the line which will be cancelled when  you
          deallocate the line.


      Chapter 14. TSX Command Summary                                  144


      2.  Use  the  SET  TERMINAL  command  to set line parameters such as
          baud rate for the communication line.

      3.  Use the SET HOST  command  to  cross-connect  your  time-sharing
          line with the communication line.

      4.  Type  control-backslash followed by carriage-return to break the
          cross-connection and reconnect your terminal  with  the  command
          interpreter.

      5.  After   the  cross-connection  is  broken,  use  the  DEALLOCATE
          command to release the communication line.   If  the  parameters
          set  by  the  SET  TERMINAL command were temporary, they will be
          restored to their permanent values.



      14.81 SET LOGOFF

      SET LOGOFF specifies options related to job logoff processing.

      Syntax:

           SET LOGOFF/qualifiers

      Qualifiers:

         /ACCOUNTING  Specifies  that  a  logoff  message  and  accounting
                 information  is  to  be  printed  when  the job logs off.
                 This is the default case.

         /FILE=filespec Specify the name of a command file to be  executed
                 when the job logs off.

         /NOACCOUNTING  Specifies  that  the logoff message and accounting
                 information that is normally printed when a job logs  off
                 is to be suppressed.

         /SILENT Equivalent to /NOACCOUNTING



      14.82 SET LOG

      SET  LOG controls logging of terminal I/O.  When terminal logging is
      turned on, all  output  sent  to  the  terminal  by  use  of  system
      services  (not  direct  video  memory  writes)  is  written  to  the
      specified log file.

      Syntax:

           SET LOG/qualifiers


      Chapter 14. TSX Command Summary                                  145


      Qualifiers:

         /ALL (Default) Log both terminal input and output.

         /CLOSE Close log file and terminate logging..

         /FILE=filespec Write output to specified file.

         /[NO]LOGIN (Default) Log terminal or command file input.

         /[NO]LOGOUT (Default) Log terminal output.

         /OFF Same as /CLOSE

         /[NO]SUSPEND Suspend logging until a SET  LOG/RESUME  command  is
                 issued.

         /RESET  Discard  data  in  the current log file, but do not close
                 the file.

         /RESUME Resume logging after a SET LOG/SUSPEND command.

      The SET LOG command controls terminal logging.   To  begin  terminal
      logging,  use  the  /FILE=filespec  qualifier.   If  a  log  file is
      already open, the current log file is closed before the new  one  is
      opened.   The default extension for the log file name is ".LOG".  To
      close the current log file without opening a new log file,  use  the
      /CLOSE  qualifier.   The  log  file is automatically closed when you
      log off.

      Normally, both terminal input and  output  are  copied  to  the  log
      file.   However,  you  can use the /NOLOGIN and /NOLOGOUT qualifiers
      to prevent either terminal input or output from being logged.



      14.83 SET MESSAGE

      SET MESSAGE controls the format of TSX status and error messages.

      Syntax:

           SET MESSAGE/qualifiers

      Qualifiers:

         /ALL Print all parts of message.

         /[NO]FACILITY Print the facility name.

         /FULL Same as /ALL.

         /[NO]IDENTIFICATION Print identifying mnemonic name.


      Chapter 14. TSX Command Summary                                  146


         /[NO]SEVERITY Print error severity indicator letter.

         /[NO]TEXT Print text of message.



      14.84 SET NEWSTATISTICS

      SET NEWSTATISTICS resets  system  statistics  information  which  is
      reported  by  commands  such  as  SHOW USE, SHOW CACHE, SHOW PAGING,
      etc.

      Syntax:

           SET NEWSTATISTICS



      14.85 SET PRINTWINDOW

      The SET PRINTWINDOW command is used  to  specify  the  name  of  the
      printer  and  other parameters related to the print window facility.
      The print window facility  allows  you  to  print  a  copy  of  your
      current  screen  image  by  pressing  the  "Print Screen" key on the
      console or PC-term terminals.  On terminals that do not have  "Print
      Screen"  keys,  you  can  print  the screen by pressing control-B or
      another control character specified by the "PWCH" system  generation
      parameter.

      Syntax:

           SET PRINTWINDOW/qualifiers

      Qualifiers:

         /[NO]BEGINFF Print form feed at beginning of print.

         /[NO]BELL Ring terminal bell when screen image is stored.

         /DEVICE=name Print to this device.

         /ENDFF Print a form feed at end of print.

         /OFF Turn off print window facility for your job.

         /ON (Default) turn on the print window facility for your job.

      The  SET  PRINTWINDOW command is used to specify the device to which
      print  window  output  is  to  be  written,  and  to  specify  other
      parameters  related  to the print window facility.  For example, the
      command

           SET PRINTWINDOW/DEVICE=PRINT:


      Chapter 14. TSX Command Summary                                  147


      directs print window output to  the  standard  spooled  print  queue
      named  "PRINT:".   If  you specify a device without a file name, the
      system generates a  file  name  of  the  form  "WINnnnnn.LST"  where
      "nnnnn" is the id number of your job.

      You  must  set  the  system  generation  parameter DOWINPRNT to 1 in
      order to enable the TSX window printing facility.  This is  normally
      done when you select an option during the TSX-Lite installation.

      When  you  type  Print  Screen (or some other character specified by
      the "PWCH" sysgen parameter), the system signals the WINPRT  program
      (running  as  a  detached  job)  which  takes  a  "snapshot" of your
      current screen image.  If you specify the  /BELL  qualifier  on  the
      SET  PRINTWINDOW  command, WINPRT will ring your terminal bell after
      it has taken the shapshot.  WINPRT  then  queues  the  snapshot  for
      printing  and  prints  if  after  all  other previously queued print
      window requests have been serviced.



      14.86 SET PROCESS

      SET PROCESS alters job characteristics.

      Syntax:

           SET PROCESS/qualifiers

      Qualifiers:

         /AUTHORIZED Command applies to authorized privileges.

         /[NO]BELL (Default)Enable terminal bell.

         /[NO]CMDTRACE Trace search for an executable file.

         /[NO]DBSS Turn on system service trace facility.

         /[NO]DBV86 Turn on  system  service  trace  facility  for  16-bit
                 programs.

         /[NO]DPMI Turn on or off DPMI support.

         /EMS=value   Enable  specified  amount  of  EMS  memory  for  DOS
                 programs.

         /IDENTIFICATION=id Specify which job  this  SET  PROCESS  command
                 applies to.

         /MAXMEMORY=value  Specify max number of k-bytes of virtual memory
                 for job.

         /MAXPRIORITY=value Specify maximum job priority.


      Chapter 14. TSX Command Summary                                  148


         /MAXTTCHK=n Allow DOS programs to  check  for  terminal  input  n
                 times before suspending.

         /MAXTTIOCHK=n  Allow  DOS  programs to check for terminal n times
                 after an I/O operation before suspending.

         /[NO]MONITOR Allow others to monitor this job with SPY  or  TUTOR
                 commands.

         /NAME=string Set process name.

         /PRIORITY=value Specify execution priority.

         /PRIVILEGES=privlist Specify a list of privileges.

         /RESUME Resume the execution of a suspended job.

         /[NO]SCCA Suppress control-C aborts

         /SMANAGER=n   Specify   the  invocation  level  for  the  session
                 manager.

         /SUSPEND Suspend the execution of a job.

         /[NO]TTFWBELL Ring terminal when suspending  a  DOS  program  for
                 too many terminal input checks.

         /TTHANGTIME=n  Specify 1/100's of a second to suspend DOS program
                 after excessive terminal input checks.

         /USERNAME=name Set the user name for the process.



      14.87 SET

      SET symbol defines a symbol to be placed in  the  environment  block
      for DOS programs.

      Syntax:

           SET[/qualifiers] symbol=string

      Qualifiers:

         /SYMBOL  SET  command  is  a  symbol  definition,  not  a TSX SET
                 command.



      14.88 SET SYSTEM

      SET SYSTEM alters system-wide parameters.


      Chapter 14. TSX Command Summary                                  149


      Syntax:

           SET SYSTEM/qualifiers

      Qualifiers:

         /[NO]ACCOUNTING Enables accounting log file.

         /[NO]CACHEWRITETHROUGH Same as /[NO]IOFLUSH.

         /[NO]IOFLUSH Write data directly to disk, not to the cache.

         /[NO]LOGON Enables new jobs to log onto the system

         /QUAN1=value Execution time slice for interactive state.

         /QUAN1A=value  Execution  time  slice  for  high  priority   wait
                 reactivation.

         /QUAN1B=value  Execution time slice switching between interactive
                 jobs.

         /QUAN1C=value Execution time at highest interactive state.

         /QUAN2=value Execution time slice for cpu-bound jobs.



      14.89 SET TERMINAL

      SET TERMINAL sets attributes and options for a terminal line.

      Syntax:

           SET TERMINAL/qualifiers
           SET ttname/qualifiers

      Qualifiers:  (cl  indicates   communication   line,   ts   indicates
      time-sharing line)

         /7BIT (cl,ts) Same as /NOEIGHTBIT.

         /8BIT (cl,ts) Same as /EIGHTBIT.

         /ADDLF (cl) Add a line feed to each carriage return.

         /ANYXON  (ts)  Any  character  will resume output after Ctrl-S is
                 pressed.

         /[NO]AUTOBAUD (ts) Allow automatic baud selection during login.

         /BACKGROUND=color (ts) Specify the default background color.

         /[NO]BACKRUB (ts) Convert backspace characters to rubout.


      Chapter 14. TSX Command Summary                                  150


         /[NO]BININ (cl) Pass  all  characters  directly  to  the  reading
                 program.

         /[NO]BINOUT  (cl)  8-bit  characters  are  to be sent to the line
                 without modification.

         /[NO]BINUART (cl, default)  Pass  all  characters  when  line  is
                 being used as a virtual UART COM port.

         /BITS=n(cl,ts)  Specify data bits to be used by the hardware line
                 controller.

         /[NO]BOARDHS (cl,ts,default) Allow  serial  hardware  to  perform
                 flow control.

         /[NO]CR   (cl,   default)   Okay   to   transmit  carriage-return
                 characters.

         /[NO]CTL (cl,default) Okay to transmit control characters to  the
                 communication line.

         /[NO]DEAD (cl,ts) Do not use this line.

         /DEVICE_TYPE=name (ts) Same as /TERMTYPE.

         /[NO]DTR  Raises  the  Data  Terminal  Ready  (DTR) signal on the
                 specified line.

         /[NO]ECHO  (ts,sp,default)  Echo  received  characters   to   the
                 terminal.

         /[NO]EIGHTBIT (cl,ts) Pass all 8 bits of each character.

         /ENDFF=n  (cl)  Write  n  form-feed  characters  to the end of an
                 output file when I/O channel is closed.

         /FOREGROUND=color (ts) Set foreground color.

         /[NO]FORM (cl,ts) Okay to send form-feed characters.

         /[NO]FORM0 (cl) Send a form-feed character  to  the  line  before
                 the first write.

         /[NO]GAG (ts,sp) Don't display messages from other jobs.

         /HANDSHAKING=type (ts,cl) Use specified handshaking method:


      Chapter 14. TSX Command Summary                                  151


                  XONXON
                  XONCTS
                  XONDSR
                  RTSXON
                  RTSCTS
                  RTSDSR
                  DTRXON
                  DTRCTS
                  DTRDSR

         /IXLATE=(received=converted,received=converted,...) (ts,cl)
                 Define a translation table for received characters.

         /[NO]LC (ts,sp,default) Okay to send lower-case characters.

         /LENGTH=n (cl) Specify the number of lines per page.

         /[NO]LFIN  (cl,ts,default)  Pass  line  feed  characters  to  the
                 program.

         /[NO]LFOUT (cl,default) Pass transmitted line-feed characters  to
                 the

         /[NO]LOGON (cl,ts,default) Allow logon.

         /OXLATE=(sent=converted,sent=converted,...)(ts,cl)    Define    a
                 translation table for transmitted characters.

         /[NO]PAGE (cl,ts,default) Control-S and  control-Q  perform  flow
                 control functions.

         /[NO]PARITY=type  (cl,ts) Use specified parity control:EVEN, ODD,
                 or NONE.

         /[NO]PCDIM (ts)  Make  dim  characters  the  default  on  PC-Term
                 terminals.

         /PERMANENT (cl,ts) Make changes permanent.

         /[NO]PHONE (ts) Perform modem control.

         /[NO]PRINTER   (ts,cl)  There  is  a  printer  attached  to  this
                 terminal.

         /RESET (ts,cl) Reset line to original condition.

         /[NO]RTS (ts,cl) Raises the Request To Send (RTS) signal.

         /[NO]SCOPE (ts) Terminal is a CRT.

         /[NO]SEVENBIT (cl,ts,default) same as /NOEIGHTBIT.

         /SKIP=n (cl) Send form-feed when n lines remain on the page.


      Chapter 14. TSX Command Summary                                  152


         /SPEED=value (cl,ts) Set speed to  one  of  the  following:  100,
                 150, 300, 600, 1200, 2400, 4800, 9600, or 19200.

         /[NO]START (ts) Start a job on the line.

         /[NO]SYSPASSWORD  (ts)  Require  system  password before starting
                 job.

         /[NO]TAB (cl,ts) Okay to send tab characters.

         /TERMTYPE=name (ts) Specify the type of terminal.  Name  must  be
                 one of:

                  ANSI
                  PCTERM
                  TSXTERM
                  VT100
                  VT220
                  VT320
                  VT420
                  RELISYS

         /[NO]TPFFCLOSE  (ts) Send a form feed to terminal printer on file
                 close.

         /[NO]TPFFOPEN (ts) Send a form feed to terminal printer  on  file
                 open.

         /TPCPS=n  (ts)  Send data to terminal printer at n characters per
                 second.

         /[NO]UPCASE (cl) Convert lower case characters to upper case.

         /VUARTBUF=size Specify  size  of  output  buffer  used  to  store
                 characters  when the line is being used as a virtual UART
                 such as with a communications program.  The default  size
                 is   32   characters.    Increasing   this   may  improve
                 efficiency but could cause problems for timing  sensitive
                 programs that are doing flow control.

         /WIDTH=n (cl) Specify the maximum line width.

         /NOXLATE Turns off any character translation for the line.

         /XON (cl,ts) Resets line in hold (XOFF) condition.

      See also the description of the TMAN command on page 165.



      14.90 SET TIME

      SET  TIME  sets  the  system  time.   It  is  equivalent to the TIME
      command.


      Chapter 14. TSX Command Summary                                  153


      Syntax:

           SET TIME time
           TIME time

      Examples:

           SET TIME 10:30
           TIME 15:24:05



      14.91 SET VERIFY

      SET VERIFY controls echo of command files to terminal.

      Syntax:

           SET [NO]VERIFY



      14.92 SET VIDEO

      SET VIDEO changes the default video mode of the console and  TSXTERM
      terminals.

      Syntax:

           SET VIDEO/qualifiers

      Qualifiers:

         /MODE=value  Specify  the  new  mode.  Valid values: VGA: 0,1,2,3
                 and 7; EGA: 0,1,2 and 3; MDA: 7 only.



      14.93 SET WINDOW

      SET WINDOW controls process windowing.

      Syntax:

           SET WINDOW/qualifiers

      Qualifiers:

         /DARK Display light characters on dark background.

         /LIGHT Display dark characters on light background.

         /LINES=n Specify the number of lines on the screen.


      Chapter 14. TSX Command Summary                                  154


         /NARROW Display 80 columns.

         /NOSCROLL Disallow scrolling while window is in background.

         /SCROLL=n Allow n lines to scroll while window is in background.

         /WIDE Display 132 columns.



      14.94 SET WORKING_SET

      SET WORKING_SET sets physical memory  space  available  for  current
      job.

      Syntax:

           SET WORKING_SET/qualifiers

      Qualifiers:

         /[NO]ADJUST   (Default)   Enables   automatic  working  set  size
                 adjustment

         /EXTENT=value Same as /MAXIMUM.

         /MAXIMUM=value Specify maximum K-bytes of memory for the job.

         /MINIMUM=value Specify minimum K-bytes of memory for the job.

      The "working set" for your process is the set of memory pages  which
      is  currently resident in physical memory and directly accessible by
      your programs.  (A "page" of memory consists of 4,096 bytes).   Your
      virtual  memory  space  may be larger than your working set.  Memory
      pages that are part of your virtual memory space  but  not  in  your
      working  set  may  be  located  either  in physical memory or in the
      system page file.  An attempt to access a memory page which  is  not
      in  your  working  set  causes  a "page fault".  Despite its name, a
      page fault is not an error but rather denotes the process  that  TSX
      performs  to  add a memory page to your working set.  If the maximum
      allowed number of pages are in your working set when  a  page  fault
      occurs,  the oldest entry in the working set is removed to make room
      for the entry being added.

      Normally, TSX performs automatic working set size  adjustment  based
      on  the  page  fault  rate.  If the number of page faults per second
      exceeds the value of the "WSDAUPRATE" sysgen parameter  the  working
      set  size  is  expanded  by  the  size  of  the  "WSDAUPAMT"  sysgen
      parameter.  If the page fault rate is less than  the  "WSDADOWNRATE"
      sysgen  parameter  then the working set size is reduced by the value
      of  the  "WSDADOWNAMT"  sysgen  parameter.   You  can  disable   the
      automatic   working   set   adjustment  process  by  specifying  the
      /NOADJUST qualifier with the SET WORKING_SET command.   If  this  is
      done,  the  working  set size is held at the maximum value.  Use the


      Chapter 14. TSX Command Summary                                  155


      /ADJUST  qualifier  to   reenable   automatic   working   set   size
      adjustment.

      The  /MAXIMUM  and  /MINIMUM  qualifiers  allow  you  to specify the
      maximum and minimum number of K-bytes of space that may be  used  by
      the  working  set.   If  automatic  working  set  size adjustment is
      enabled, the working set size will vary within  these  limits  based
      on the page fault rate.

      The  SET  PROCESS/MAXMEM=size command is used to control the maximum
      amount of virtual memory space  available  to  the  job.   The  SHOW
      MEMORY  command  displays  information about memory space.  The SHOW
      PAGING  command  displays  page  fault  statistics.   You  may  type
      control-T at any time to display your current working set size.



      14.95 SHOW ALL

      SHOW ALL displays a variety of system information.

      Syntax:

           SHOW ALL



      14.96 SHOW ASSIGNS

      SHOW   ASSIGNS   displays  information  about  logical  device  name
      assignments.

      Syntax:

           SHOW ASSIGNS[/qualifiers] [logical_name]

      Qualifiers:

         /GLOBAL Display only assignments in  the  process  global  assign
                 table.

         /LOCAL  Display  only  assignments  in  the  process local assign
                 table.

         /SYSTEM Display only assignments  in  the  system  global  assign
                 table.



      14.97 SHOW AUTHORS

      SHOW  AUTHORS displays the names of the three developers of TSX-Lite
      and TSX-32.  The names appear in random order.


      Chapter 14. TSX Command Summary                                  156


      14.98 SHOW CACHE

      SHOW CACHE displays statistics about data caching.

      Syntax:

           SHOW CACHE



      14.99 SHOW COLORS

      SHOW COLORS displays a table of available colors.

      Syntax:

           SHOW COLORS



      14.100 SHOW DATE

      SHOW DATE displays the current date.  Equivalents: DATE

      Syntax:

           SHOW DATE



      14.101 SHOW DEVICES

      SHOW DEVICES displays information about  devices  installed  on  the
      system.

      Syntax:

           SHOW DEVICES



      14.102 SHOW ERRORS

      SHOW ERRORS displays error statistics

      Syntax:

           SHOW ERRORS

      See  Section  10.6 on page 69 for additional information about event
      and error logs.


      Chapter 14. TSX Command Summary                                  157


      14.103 SHOW EVENTS

      The SHOW EVENTS command is used to display information in event  log
      files.  It is also used to enable and disable event logs.

      Syntax:

           SHOW EVENTS

      The  first  screen  displayed  by the SHOW EVENTS command lists each
      active event log and shows the number of records in  the  event  log
      file.   To  display  the records in an event log file, use the arrow
      keys to select an event log entry and then press Enter.   Press  'R'
      to reset an event log and delete all files in it.

      Press  'C'  to  display  a  second  screen which lists all available
      event log files.  From this screen you can highlight  an  event  log
      entry  and  press  'E' to enable the event log or 'D' to disable the
      event log.

      Press ESC to exit.

      See Section 10.6 on page 69 for additional information  about  event
      logs.



      14.104 SHOW FILES

      SHOW FILES displays information about open files.

      Syntax:

           SHOW FILES[/qualifiers] [filename]

      If  a  file  name is specified, information is printed for that file
      only.  If no file name is specified, information  is  printed  about
      all  currently  open files.  This information shows which users have
      the file open and indicates whether they have it open  for  read  or
      write access.

      Qualifiers:

         /ID=jobid Show files only for specified job id.

         /LOCKED Only show files which are locked.



      14.105 SHOW FSTATUS

      SHOW FSTATUS displays information about file usage.


      Chapter 14. TSX Command Summary                                  158


      Syntax:

           SHOW FSTATUS



      14.106 SHOW JOBS

      SHOW  JOBS is equivalent to SHOW SYSTEM, described on page 159.  See
      also the description of the JMAN command on page 121.



      14.107 SHOW KEYS

      SHOW KEYS displays a list of your user-defined keys.

      Syntax:

           SHOW KEYS



      14.108 SHOW MEMORY

      SHOW MEMORY displays information about available memory space.

      Syntax:

           SHOW MEMORY



      14.109 SHOW NAME

      SHOW NAME displays the user name and  other  information  about  the
      current job.  This is equivalent to the SHOW UIC command.



      14.110 SHOW PAGING

      SHOW PAGING displays statistics about memory paging operations.

      Syntax:

           SHOW PAGING



      14.111 SHOW PRIVILEGES

      SHOW PRIVILEGES displays your current and authorized privileges.


      Chapter 14. TSX Command Summary                                  159


      Syntax:

           SHOW PRIVILEGES



      14.112 SHOW QUEUE

      SHOW  QUEUE  displays  information  about  jobs  in  print  or batch
      queues.

      Syntax:

           SHOW QUEUE[/qualifiers] [queuename]

      Qualifiers:

         /BATCH Show information about batch jobs only.

         /FILES Show information on each file in print queues.

         /FULL Show all information about queues.

         /OWNER[=username]  Show  information   on   jobs   submitted   by
                 specified user.

         /PRINT Show information about print jobs only.



      14.113 SHOW SYMBOLS

      SHOW SYMBOLS displays information about symbol names.

      Syntax:

           SHOW SYMBOLS[/qualifiers] [symbol_name]

      Qualifiers:

         /ALL (Default) Show symbols from all symbol tables.

         /GLOBAL Show symbols from global symbol table only.

         /LOCAL Show symbols from local symbol table only.

         /SYSTEM Show symbols from system symbol table only



      14.114 SHOW SYSTEM

      SHOW  SYSTEM  displays  information about each process.  Equivalent:
      SHOW JOBS, SYSTAT, WHO.   See  also  the  description  of  the  JMAN
      command on page 121.


      Chapter 14. TSX Command Summary                                  160


      Syntax:

           SHOW SYSTEM[/qualifiers]
           SHOW JOBS[/qualifiers]
           SYSTAT[/qualifiers]

      Qualifiers:

         /BATCH Show only batch jobs.

         /DETACHED Show only detached jobs.

         /INTERACTIVE Show only interactive jobs.



      14.115 SHOW TERMINALS

      SHOW  TERMINALS  displays summary or detail information about serial
      lines.

      Syntax:

           SHOW TERMINALS -- Display summary information for all lines.

           SHOW ttcuu: -- Display details for line ttcuu.

      See also the description of the TMAN command on page 165.



      14.116 SHOW TIME

      SHOW TIME displays the current time of day.  Equivalent: TIME

      Syntax:

           SHOW TIME
           TIME



      14.117 SHOW UIC

      SHOW  UIC  is  equivalent  to  SHOW  NAME.   See   SHOW   NAME   for
      information.



      14.118 SHOW USE

      SHOW  USE  displays statistics about the utilization of the computer
      system.


      Chapter 14. TSX Command Summary                                  161


      Syntax:

           SHOW USE



      14.119 SHOW USERS

      SHOW USERS displays information about each logged on user.

      Syntax:

           SHOW USERS



      14.120 SHOW VERSION

      SHOW VERSION displays the current TSX version number.   Equivalents:
      VERSION

      Syntax:

           SHOW VERSION



      14.121 SHUTDOWN

      The  SHUTDOWN  command  procedure  does  an  orderly shutdown of all
      jobs.  Once it finishes you can type BOOT or press the reset  button
      to reset your computer.



      14.122 SORT

      The  SORT  command sorts one or more input files and produces either
      a new sorted output file or writes the sorted records back into  the
      original  input  file.  Multiple keys may be specified and a logical
      expression may be used to select which records are  to  be  included
      in  the  sort.   TSX  SORT  is  very  fast and is capable of sorting
      enormous files (hundreds of megabytes).

      The  TSX  SORT  program  is  provided  with  the  optional  TSX-Lite
      Utilities Kit (see REGISTER.DOC).

      Syntax:

           SORT[/qualifiers] input_file1,input_file2,... [output_file]

      Qualifiers:

         /ITYPE=type  Specify  the  type  of the input file.  Type must be
                 one of:


      Chapter 14. TSX Command Summary                                  162


          CRLF -- Variable length terminated by CR/LF (default).

          FIXED -- Fixed length records.

         /KEY=(key1,key2,...) Specify one or more  sort  key  fields  (see
                 below).

         /MEMORY=size  Specify  the maximum number of K-bytes of memory to
                 be used.

         /NOBLANK Discard blank records.

         /OTYPE=type Specify type of records in the output file.

         /QUIET Don't display statistics.

         /RECLEN=length  Specify  the  record  length  for  fixed   length
                 records.

         /SELECT=expression   Include   only  records  satisfying  logical
                 expression.

         /SKIP=value Skip this many records  at  the  beginning  of  input
                 file.

         /STATISTICS Print detailed statistics.

         /UNIQUE Discard duplicate records.

         /WORKFILE=file Use specified work file.

      Each  key  specification  has the form "tas.l" where 't' is the type
      of the key (see  below),  'a'  is  'A'  for  ascending  or  'D'  for
      descending,  's'  is  the  starting  column number of the field (the
      first column of the record is 1), and 'l' is the length of  the  key
      field.   If  0  is  specified for the length, the field extends from
      the starting column to the end of the record.

      The first letter of the key specification denotes the  type  of  the
      key field.  The table below lists each of the available key types.

            A  ASCII collating sequence
            C  ASCII sequence ignoring case differences
            D  DBL signed value
            N  Numeric value string
            S  Signed binary
            U  Unsigned binary



      14.123 SPY

      SPY  monitors  data  on  a serial line.  See also the description of
      the TUTOR command (page 66).  Press any key  to  terminate  the  spy
      operation.


      Chapter 14. TSX Command Summary                                  163


      Syntax:

           SPY[/qualifiers] terminal_name

      Qualifiers:

         /ALLHEX Show all characters in hexadecimal format.

         /BINARY Display flow control characters.

         /CRLF  Add  a  carriage-return  line-feed  sequence to the end of
                 output records.

         /DISPLAY=file  Display  characters  using  an  EDIT-32   "display
                 file".

         /FILE=name Write output to specified file.

         /FREQUENCY=n   Specify   sampling  frequency  of  n/100  seconds.
                 (default: 20).

         /HEX Show non-printing characters in hexadecimal format.

         /INBUF=size Allocate size bytes of memory  for  an  input  buffer
                 (default: 512).

         /INPUT Show input data.

         /MARK Print labels for incoming and output data.

         /MODEM Display changes in modem control signals.

         /OUTBUF=size  Allocate  size bytes of memory for an output buffer
                 (default: 512).

         /OUTPUT (Default) Show output data.

         /SCREEN Enable enhanced screen mode.

         /NOSCREEN Do not display data on terminal.

         /WIDTH=cols Specify the width of terminal output.

      See Section 2.6.5 on page 19 for additional  information  about  the
      SPY command.



      14.124 STOP

      STOP stops (logs off) a specified process.

      Syntax:


      Chapter 14. TSX Command Summary                                  164


           STOP/qualifiers

      Qualifiers:

         /ID=job_id Stop the specified job.

         /PROGRAM=name Stop all processes running specified program.

         /USER=name Stop all processes for specified user.

         /WINDOW=n  Stop  the  process  running  in  the specified virtual
                 process window.



      14.125 SUBPROCESS

      The  SUBPROCESS  keyboard  command  allows  you  to  switch  between
      subprocesses  in  the  same  way  that  the control-W-digit sequence
      does.  However, the SUBPROCESS command can be placed  in  a  command
      file, whereas control-W cannot.

      Syntax:

           SUBPROCESS[/qualifiers] process_number

      Qualifiers:

         /CMDFILE=file  Specify  a  command  file  to run in the specified
                 subprocess.

         /COMMAND Specify that /CMDFILE qualifier is a system command.

         /NOINHERIT Don't inherit information from primary process..

         /NOSWITCH Create specified subprocess, but do not switch to it.

      The SUBPROCESS command allows you to select a  subprocess  similarly
      to  typing  control-W-digit.   The  command  accepts one argument, a
      digit 0 to 9 which indicates the desired subprocess to switch to.

      Here is an example  command  which  will  create  subprocess  1  and
      switch terminal control to it:

           SUBPROCESS 1

      As  a result of this command, the new sub-process will start just as
      if ctrl-W-1 were typed to select session 1.

      The following  command  initiates  subprocess  1  and  executes  the
      command  file  SY:RAMSTART.CMD  but does not switch terminal control
      to the subprocess.  Later, if you type Ctrl-W-1, you may  switch  to
      the running program initiated by SY:RAMSTART.CMD,


      Chapter 14. TSX Command Summary                                  165


           SUBPROCESS/NOSWITCH/CMDFILE=SY:RAMSTART.CMD 1



      14.126 SYSMON

      SYSMON displays dynamic information about system activities.

      Syntax:

           SYSMON



      14.127 SYSTAT

      SYSTAT -- See SHOW SYSTEM (page 159).



      14.128 TIME

      TIME See SHOW TIME



      14.129 TMAN

      TMAN  is  a  full  screen  terminal management utility.  Use TMAN to
      display information about your terminal  lines  and  perform  common
      system management functions.

      Syntax:

           TMAN

      In  response  to  the  TMAN  command,  TSX  displays  a  list of the
      terminal lines.  A menu of action keys appears to the right  of  the
      terminal list; choose an action by typing the appropriate key.



      14.130 TSAUTH

      TSAUTH  invokes  the  TSX  user  authorization utility.  The account
      authorization facilities are supplied  with  the  optional  TSX-Lite
      Security Kit (see REGISTER.DOC).



      14.131 TUTOR

      TUTOR  allows  one  user to "tutor" another's line so that each user
      sees  the  same  output  and  either  user  can  type  input.   Type


      Chapter 14. TSX Command Summary                                  166


      control-backslash   followed   by   Enter   to   release  the  tutor
      connection.

      Syntax:

           TUTOR terminal

      See Section 10.2.6 on page 66 for additional information  about  the
      TUTOR command.



      14.132 TYPE

      TYPE prints one or more files at your terminal.

      Syntax:

           TYPE[/qualifiers] filespec

      Qualifiers:

         /BEFORE[=date-time]  Select  files  created before specified date
                 and time.

         /[NO]CONFIRM Request confirmation before typing each file.

         /DATE[=date] Select files created on the given date.

         /[NO]DELETE Delete file after typing it.

         /END=n Stop output after specified line number.

         /EXCLUDE=(files) Exclude specified files from being typed.

         /[NO]HEADER Write a header  line  for  each  file  typed  at  the
                 terminal.

         /[NO]LOG Type file name before typing file.

         /MAXIMUM=n  Specify  the maximum number of lines to be typed from
                 a file.

         /NEWFILE Type only files created today.

         /[NO]PAGE Divide output into pages.

         /[NO]QUERY Same as /[NO]CONFIRM.

         /SINCE[=date-time] Select files created since specified date  and
                 time.

         /START=n Start typing at line n.


      Chapter 14. TSX Command Summary                                  167


      14.133 TSGEN

      TSGEN  allows  you  to  examine  or  modify system customization and
      tuning parameters.

      Syntax:

           TSGEN [genfile] [kernel]

      Examples:

           TSGEN
           TSGEN TSX32
           TSGEN TSX32.GEN C:\TSX32.SYS

      See Sections 2.4 and 12.4 for  additional  information  about  using
      TSGEN.



      14.134 UNPROTECT

      UNPROTECT  turns  off  file  protection  for  one  or more specified
      files.

      Syntax:

           UNPROTECT[/qualifiers] filespec

      Qualifiers:

         /BEFORE[=date-time] Select files created  before  specified  date
                 and time.

         /[NO]CONFIRM Request confirmation before acting on each file.

         /DATE[=date] Select files created on the specified date.

         /EXCLUDE=(files) Do not select specified files.

         /[NO]LOG Type the file name before acting on each file.

         /NEW Act only on files created today.

         /[NO]QUERY Same as /[NO]CONFIRM.

         /SINCE[=date-time]  Select files created since specified date and
                 time.


      Chapter 14. TSX Command Summary                                  168


      14.135 UPLOAD

      The UPLOAD command causes TSX to initiate a file transfer from  your
      local  PC  to  the host TSX computer using ZMODEM, YMODEM, or XMODEM
      protocol.  You must be running  a  communications  program  on  your
      local  PC  that  can handle one of these protocols.  In order to use
      this facility the ZMODEM sysgen parameter must be set to 1.

      Syntax:

               UPLOAD[/qualifiers] [file]

      If you are using XMODEM you must specify a file name.   If  you  are
      using  ZMODEM  or YMODEM the name is provided by your local computer
      when you start the upload.  If you specify a name it  will  override
      the  name  sent from the local PC allowing you to create a file with
      a different name on the host computer than on  the  local  PC.   You
      may specify device and directory names with the file specification.

      Qualifiers:

         /BELL   Requests   that  the  bell  be  rung  when  the  transfer
                 completes.

         /CRC Specifies that CRC checks are to  be  performed  for  XMODEM
                 transfers  rather  than  using checksums.  CRC checks are
                 always used for YMODEM and ZMODEM transfers.

         /XMODEM Specifies that XMODEM protocol is  to  be  used  for  the
                 transfer.

         /YMODEM  Specifies  that  YMODEM  protocol  is to be used for the
                 transfer.

         /ZMODEM Specifies that ZMODEM protocol is  to  be  used  for  the
                 transfer.  This is the default protocol.



      14.136 VERSION

      VERSION -- See SHOW VERSION



      14.137 VIEW

      The VIEW command displays the contents of a file on your screen.

      Syntax:

           VIEW filename

      The  VIEW  command  displays  a file on the screen.  You can use the
      Page-up and Page-down keys to scroll  upward  and  downward  through


      Chapter 14. TSX Command Summary                                  169


      the  file.   The  Home  key moves to the top of the file and the End
      key moves to the end of the file.  You can  also  use  the  up-  and
      down-arrow  keys to scroll up or down one line at a time.  Press ESC
      to exit from the VIEW command.

      The  display  will  begin  in  either  ASCII  or  hexadecimal   mode
      depending  on the nature of the data in the file.  While viewing the
      file you can type 'A' to switch to ASCII  display  mode  or  'H'  to
      switch to hexadecimal mode.



      14.138 WAIT

      WAIT pauses command file execution for a specified length of time.

      Syntax:

           WAIT time

      Examples:

           WAIT 1.5
           WAIT 1:05
           WAIT 2:30:00

      The  WAIT  time  value  is  in  units  of  seconds, but you can also
      specify a value using the format "hh:mm:ss.ddd".



      14.139 WHO

      WHO -- See SHOW SYSTEM and JMAN.



      14.140 WIN

      The WIN command starts the execution of Microsoft Windows as a  task
      under  TSX.   Windows must run in standard (not enhanced) mode under
      TSX.

      Syntax:

           WIN

      Once Windows is in operation you  can  run  programs  such  as  Page
      Maker  in the Windows environment under TSX.  You may only issue the
      WIN command while running from the console.

      Before issuing the WIN command you should assign the logical  device
      name  COM1 to the serial port to which your mouse is connected.  For
      example, if the mouse is connected to the actual COM1  port  on  the


      Chapter 14. TSX Command Summary                                  170


      computer,  which  has  the TSX device name TTB0:, then the following
      ASSIGN statement would be used:

           ASSIGN TTB0: COM1

      Any serial port may be used for the mouse connection as long as  the
      appropriate  ASSIGN  command  is  issued.   If  you wish to place an
      ASSIGN command in the SY:LSTARTUP.CMD system-wide  start-up  command
      file,  you  must use the /SYSTEM qualifier to make the assignment on
      a system-wide basis.  The following line is an example of this:

           ASSIGN/SYSTEM TTB0: COM1

      Once the assignment of COM1 has been verified,  TSX  looks  for  the
      Windows   files   in  each  directory  that  is  part  of  the  PATH
      specification.  Therefore, your PATH specification must include  the
      directory with the Windows files (typically C:\WINDOWS).

      TSX  currently  supports  only the Paradise 512 and Tseng 4000 video
      controllers in super VGA modes, so if you have some  other  type  of
      card you will have to use it in standard VGA mode.

      Windows  should  be  configured  to access disk files using standard
      DOS I/O operations rather than  attempting  any  type  of  enhanced,
      direct I/O.



      14.141 WSCMD

      WSCMD  Used  to perform a file transfer operation between TSX system
      and a workstation running TSXTERM.  See Chapter  11  for  additional
      information about TSXTERM.

      Syntax:

           WSCMD TOWS file1 file2
           WSCMD TOHOST file1 file2
           WSCMD CD \directory
           WSCMD BYE

      Qualifiers:

         /NOWAIT Start transfer but do not wait for it to complete.

      The  TOWS command transfers a file from the TSX host computer to the
      workstation running TSXTERM.  FROMHOST and DOWNLOAD  are  synonymous
      keywords for TOWS.

      The  TOHOST command transfers a file from the TSXTERM workstation to
      the host computer.  FROMWS and UPLOAD are  synonymous  keywords  for
      TOHOST.

      The CD command changes the default directory on the workstation.


      Chapter 14. TSX Command Summary                                  171


      The  BYE command causes TSXTERM to wait 5 seconds, then exit to DOS.
      Note that a command procedure can log out during the pause.

      For example, the following commands change the default directory  on
      the  workstation  to  \WORK  and then transfer a file named TROY.DAT
      from current directory on the host TSX computer to the workstation:

           WSCMD CD \WORK
           WSCMD TOWS TROY.DAT

      If you wish to assign a different name to the output than the  input
      file,  specify  the  new  file  name  as the second parameter to the
      command.  You may also provide a full file specification,  including
      device  letter  and  directory  names.   For  example, the following
      command  transfers  a  file  named  CRUSHER.DAT  from  the  \MEDICAL
      directory  on  the  'A'  disk  of  the  workstation  to a file named
      ILLNESS.DAT on the host computer:

           WSCMD TOHOST A:\MEDICAL\CRUSHER.DAT ILLNESS.DAT

      The /NOWAIT qualifier can be  specified  to  cause  the  command  to
      start  a  transfer but not wait for it to complete.  A WSCMD without
      any arguments can be used to wait for a previously  started  command
      to  finish.  For example, the following commands initiate a transfer
      of the file FARM1.DAT from the host to the  workstation,  and  then,
      while  the  transfer  is taking place, perform a sort, then wait for
      the transfer to complete:

           WSCMD/NOWAIT TOWS FARM1.DAT
           SORT BIGFILE.DAT
           WSCMD







                                   Chapter 15

                        Use and Distribution of TSX-Lite





      15.1 Redistribution of TSX-Lite

      TSX-Lite is a shareware product.  You are welcome to make copies  of
      the  TSX-Lite  distribution and pass them on to friends or post this
      program on  bulletin  boards  or  distribute  it  via  disk  catalog
      services  provided  the  entire TSX-Lite distribution is included in
      its original, unmodified form and no files are  added,  deleted,  or
      modified.   A  distribution  fee  may be charged for the cost of the
      diskette, shipping and  handling.   However,  TSX-Lite  may  not  be
      sold,  or  incorporated in another product that is sold, without the
      permission of S&H Computer Systems, Inc.  Vendors are encouraged  to
      contact S&H to get the most recent version of TSX-Lite.


      15.2 Registering TSX-Lite

      Shareware  is  a  type  of  software  distribution  that gives you a
      chance to try a software product before you decide if  you  want  to
      pay   for   it.   A  shareware  product,  such  as  TSX-Lite,  is  a
      copyrighted program; it is NOT public  domain  or  "freeware".   Its
      use  is  governed  by  the  terms of the shareware license and it is
      protected  by  the  copyright  laws  of  the   United   States   and
      international agreements.

      As  a  shareware product, you are granted a no-cost, trial period of
      30 days during  which  you  may  evaluate  TSX-Lite.   If  you  find
      TSX-Lite   to  be  useful,  educational,  and/or  entertaining,  and
      continue to use it beyond the 30 day trial period, you are  required
      to  register  your  use  by  sending  the  registration  form in the
      REGISTER.DOC file along with the appropriate registration fee.


      15.3 Telephone Support

      Both registered and unregistered users of TSX-Lite  are  welcome  to
      call  for  technical  assistance.  The fee for this service is $1.50
      per minute which may be charged to a Visa, MasterCard,  or  American
      Express  credit  card.   There  is  a $10.00 minimum charge for each
      call.  The S&H support number is 615-327-3670.





                                      172


      Chapter 15. Use and Distribution of TSX-Lite                     173


      15.4 Copyright notice

      The TSX-Lite and TSX-32 systems and documentation are copyright  (c)
      1990-1994  by  S&H Computer Systems Inc.  These products may only be
      used in accordance with the terms of the written license.

      TSX-Lite,  TSX-32,  TSX-Plus,  TSX,  MessageNet,  TSXTERM,  Edit-32,
      TSX-Net,  and  Adaptive  Scheduling  Algorithm are trademarks of S&H
      Computer Systems, Inc.

      Note that TSX-Lite is a shareware product and may be distributed  as
      described  in  Section  15.1;  however,  TSX-32  is  NOT a shareware
      product and it may only be distributed by licensed distributors.


      15.5 Disclaimer

      TSX-Lite is provided "as is" without warranty of  any  kind,  either
      expressed  or  implied.  TSX may contain "bugs" which interfere with
      its operation and not all programs will run correctly with it.   S&H
      Computer  Systems  assumes no responsibility for the use of TSX-Lite
      and will not be responsible for any damage resulting from its use.







                                   Chapter 16

                                    TSX-BBS




      TSX-BBS is a full multi-line bulletin board system (BBS)  that  runs
      in  conjunction  with  TSX  and  TSX-Lite.   Like  TSX,  TSX-BBS  is
      available as a  commercial  product  and  as  a  shareware  program.
      Since  TSX-BBS  is  a  separate product from TSX and TSX-Lite, it is
      distributed independently (although you need TSX-32 or  TSX-Lite  to
      run  TSX-BBS).   The  TSX-BBS  shareware  distribution  has the name
      TSXBBSxx.ZIP where 'xx' is  the  version  number.   You  can  always
      download  the  latest  copy of the shareware version of TSX-BBS from
      the S&H Support BBS: 615-320-1820.

      The following is  a  summary  of  some  of  the  major  features  of
      TSX-BBS:


      16.1 A Multi-Line System

      Designed  from  the ground up as a multi-line operating environment,
      TSX-BBS can support up to 256  lines  on  a  single  computer.   The
      reason  TSX-BBS  can do this is that it was designed specifically to
      run with TSX and to use the features of the operating system in  the
      most efficient manner possible.

      So,  instead  of  a  room  full  of computers, you can have a single
      system running  TSX-BBS  connected  through  an  intelligent  serial
      multiplexer   to   many   modem   lines.    For   medium   to  large
      installations,  this  could  save  thousands  (or   even   tens   of
      thousands)  of  dollars  in  hardware  expenses,  not to mention the
      complexity of maintaining a large networked system.

      An advantage of a multi-line TSX-BBS system is that  it  provides  a
      smooth  growth  path.   Many  systems run well for one or two lines,
      but when you grow  you  will  hit  a  barrier  that  necessitates  a
      radical  change.   With  TSX-BBS,  you  can  start  out with a small
      system and grow smoothly to an enormous system.


      16.2 Super System Capacity

      Suppose your dreams are so big that you think  you  will  outgrow  a
      single  computer  no  matter  how efficient the software is.  Relax,
      TSX-BBS will take care of you.  For extremely large  configurations,
      TSX  systems  can be networked together so that you can grow without
      bounds.  With its TCP/IP networking option, you  can  link  multiple


                                      174


      Chapter 16. TSX-BBS                                              175


      TSX  systems  together.   Any program on any computer in the network
      can transparently access any file.  Because TSX  networking  uses  a
      peer-to-peer  model,  you  do  not  have to dedicate a computer as a
      "file server".  All computers in the network  can  store  files  and
      run the TSX-BBS system.


      16.3 Reliable, Non-stop Operation

      If  you  are  running a single-line hobby board it may be acceptable
      to  take  the  system  down   periodically   for   maintenance   and
      improvements.   But, if you are serious about running a professional
      quality board, you  need  a  BBS  system  that  will  run  reliably,
      non-stop, 24-hours a day.  TSX-BBS is such a system.

      All  of  the  BBS maintenance functions such as adding and modifying
      user authorizations, reviewing and posting new uploads, and  backing
      up  files  can be done without stopping the BBS or interrupting your
      users.  You can do new program development using the  TPL  language,
      C,  Pascal, or the language of your choice, while the BBS is in full
      operation.   You  can  develop  and  test   menu   changes   without
      interrupting  your  users.   And,  the sysop (or properly authorized
      users) can do development and maintenance from  dial-in  connections
      as well as from the local console.

      Routine  operations  such  as  new user registrations are completely
      automatic.  Internet Usenet newsgroups,  Fido  echoes,  and  netmail
      processing  is  automatic with messages being posted in real-time as
      they arrive.   TSX-BBS  can  even  be  configured  to  automatically
      create  new  Fido  and Usenet newsgroups without sysop intervention.
      You can literally take a vacation without most of your  users  being
      aware that your board is unattended.


      16.4 A Sysop's Dream

      With  other  multi-line  BBS  systems,  the computer is dedicated to
      running the BBS software and the sysop must use auxiliary  computers
      for  tasks  such  as  viewing  uploaded  GIF  files,  running "door"
      programs, and processing incoming satellite feeds.

      TSX-BBS is the only multi-line BBS system that lets  the  sysop  run
      DOS  programs,  view GIF's, do file maintenance, and run games while
      the BBS is live on the same PC.  The same computer that  is  running
      TSX-BBS  can  process incoming satellite data including Usenet feeds
      and add it to your board in  real-time.   Since  most  DOS  programs
      such  as WordPerfect, dBase, Foxpro, CSHOW, Procomm, and Windows 3.1
      run under TSX with the BBS in operation, you can run  your  business
      on the same computer and at the same time that you run your BBS.

      Using  the  HOST  program  that  is  provided  with TSX, or your own
      favorite communications program, you  can  call  other  systems  and
      upload  and  download  files  while  your BBS is running on the same
      computer.


      Chapter 16. TSX-BBS                                              176


      16.5 Door Program Support

      "Door" programs are applications  designed  to  run  in  cooperation
      with  a  BBS  to  provide  extended services such as games.  Because
      traditional multi-line BBS systems dedicate the computer to  running
      the   BBS   software,  they  are  unable  to  execute  popular  door
      applications.   TSX-BBS,  on  the  other  hand,  can  execute   door
      programs  on  the  same  computer with the BBS.  And, many users can
      run doors at the same time.  TSX-BBS takes care of  the  details  of
      creating   a  DOOR.SYS  "drop"  file  with  user  information.   TSX
      includes an internal, optimized "FOSSIL"  communication  driver  for
      efficient operation of door programs.


      16.6 Flexibility is the Key

      Successful  computer  bulletin  boards  evolve  over  time.  As your
      system grows and you acquire new users and add more lines, you  will
      develop  new  ideas  for  improvements  and  new  features.   It  is
      important  that  you  select  a  BBS  package  that  allows  you  to
      customize  your  system  and doesn't box you in with fixed menus and
      no way of adding extensions.

      TSX-BBS comes with a complete set of menus and support  programs  so
      it  is  easy  to get up and running the same day you receive it, but
      it doesn't hold  you  back  when  you  are  ready  to  do  your  own
      development  and  customization.   Virtually every menu, phrase, and
      color can be changed.   Some  sysops  like  very  flamboyant  menus,
      others  prefer  more reserved ones; have it your way.  With a little
      creative effort you can configure TSX-BBS  to  present  exactly  the
      image  you  desire.   And,  you will find that this customization is
      surprisingly easy; we give you the tools and materials, you can  put
      them together in many different ways.

      TSX-BBS  comes  with  an  advanced  menu compiler that allows you to
      modify any of the standard menus and create new menus  of  your  own
      design.   You can change the menu tree structure, change the wording
      of menu options,  translate  them  to  foreign  languages,  add  and
      remove menu items, and integrate text from ANSI and RIP editors.

      TSX-BBS  menus  are  organized  into three sections: initialization,
      display, and action.  The initialization  section  is  optional,  if
      present  it  allows  you to specify actions that are to be performed
      each time the menu is entered.  You can use this  section  to  write
      information  to  log files, start programs, and perform other tasks.
      Conditional expressions  allow  you  to  perform  different  actions
      based on the user and many other conditions.

      The  display  section  contains  the menu image that is presented to
      the user.  You can put the text in the menu source file or  you  can
      display  an  external  file  that may have been created with an ANSI
      editor.   TSX-BBS  allows  you  to  place  commands  of   the   form
      "@command@"  within  the  menu  text  to  select  colors,  do cursor
      positioning, and check conditions.  You can also use these  commands
      to  cause  TSX-BBS  to  insert parameters such as the caller's name,


      Chapter 16. TSX-BBS                                              177


      the time, the date, the remaining time  available,  and  many  other
      values.   This makes it easy to create personalized menus and status
      displays.

      The action section of a  menu  specifies  what  actions  are  to  be
      performed  when  a  user  types  a  letter  or  command.  All of the
      inherent BBS functions are available as "building  blocks"  for  you
      to  use, such as browsing file libraries, entering chat, reading new
      mail, etc.  (there are over 65 actions).  In addition,  actions  can
      call  other  menus or execute external programs that you write.  The
      following is an example of a menu action section:

             $item key=C action=menu(chat)
             $item key=F action=menu(file)
             $item key=V action=vote
             $item key=W action=who
             $item key=G action=logoff

      You can design menus that present options  to  some  users  and  not
      others  based  on  privilege flags.  Entirely different menus can be
      selected based on capabilities such as ANSI,  color  and  RIP.   You
      can  even  have menu options that appear only on certain days of the
      week or during certain hours of the day.

      For the finest level of customization you  can  change  the  phrases
      and  colors presented by each "building block" menu action.  This is
      especially useful for creating bulletin boards to  serve  users  who
      prefer a language other than English.

      Don't  let your users down.  You can enhance and upgrade your system
      while it is running continuously, 24-hours a day.   You  can  create
      your  own  test  menus  while  your  users  continue to run with the
      production menus.  When you are ready, you can add the new menus  to
      the   production   system  without  taking  the  BBS  down  or  even
      interrupting on-line users.   You  can  even  configure  TSX-BBS  to
      present  experimental  menus  and  features on selected lines or for
      selected users only.


      16.7 Use TPL to Extend Your System

      The optional TSX Programming Language (TPL) is the  ideal  tool  for
      writing  extensions to TSX-BBS.  You can also use TPL for developing
      your own application programs.  Using TPL, you can  develop  plug-in
      enhancements  to  your  BBS  that are a seamless part of the system.
      If you are so inclined, you can use TPL to  develop  extensions  and
      commercial  applications  that  can  be marketed in source or object
      language form to other TSX-BBS sites.

      TPL is a powerful programming language with a  C-like  syntax.   TPL
      includes  integer,  real,  and  string variables and constants.  The
      string variables are especially powerful because they  have  dynamic
      size  so  you  never  have  to  reserve  a fixed size area to hold a
      value.  You can also write string functions that accept  and  return
      strings of varying sizes.


      Chapter 16. TSX-BBS                                              178


      The  TPL  language  includes  over  300  built-in library functions.
      Many of these functions perform BBS operations such as adding  files
      to  the  BBS  file libraries or getting information about registered
      BBS users.  It is easy to write TPL programs to add new files  using
      the  FILE_ID.DIZ  descriptions  so  that  you  do  not  have to type
      multi-line  descriptions.   You  can  also  write  TPL  programs  to
      produce  reports  such  as  a list of the most frequently downloaded
      files, or a list of users whose  accounts  will  expire  during  the
      next month.

      A  communication  "script"  facility  is  integrated  into  the  TPL
      language.  You can write  TPL  programs  that  dial  other  bulletin
      boards,  check  for  new files, download files, and add them to your
      BBS file library; this can be done while your BBS  is  in  operation
      and  without  intervention  on your part.  Because the communication
      script facility is an integral part of the TPL language, all of  the
      other  language  features  are  available  such  as  dynamic  string
      variables, functions, file I/O, and X/Y/Z-modem transfers.  You  can
      schedule  scripts (and other TPL programs) to run at specified times
      of the day.


      16.8 File Libraries

      A good file library facility is important for most  bulletin  boards
      and  is the primary reason for existence for many.  TSX-BBS provides
      a world class file library.  You can  set  up  any  number  of  file
      areas  and  organize  them  in hierarchical categories (CD-ROMs, IBM
      files, Macintosh, etc.).  File descriptions can be up  to  16  lines
      long  and  TSX-BBS  stores  extended  information  about  each  file
      including the date and time when it was uploaded, the  name  of  the
      person  who uploaded the file, the number of times that the file was
      downloaded, and the date of the last download.  Users  can  download
      files  one  at  a time or they can tag files while browsing and then
      download them as a group.  Daily download byte and time  limits  can
      be set for each user.

      TSX-BBS  includes a powerful file search facility.  Users can search
      file names and descriptions for single words  or  for  words  joined
      with  the  logical  operators  'AND' and 'OR'.  For example, a valid
      search expression is "GAMES AND WINDOWS", or "HIV OR AIDS".  A  date
      search  allows users to find files uploaded since the last time they
      checked or since a specified date and time.   The  search  can  span
      all file areas or can be restricted to specified areas.

      A  "privilege  expression"  is  used  to control access to each file
      area (see  Section  16.14).   For  each  file  area,  users  can  be
      restricted to the following types of access:

      1.  No access whatsoever (they do not even know the area exists)

      2.  List the file names and descriptions

      3.  Download files from the area


      Chapter 16. TSX-BBS                                              179


      4.  Upload to the area

      The  sysop  can set up a private upload area for all user uploads so
      that the files can be examined before being publicly posted.

      It is easy to set up private file  areas  for  groups  of  users  or
      companies that may want to use your board as a support center.


      16.9 Newsgroups and Discussion Forums

      TSX-BBS  includes  a  powerful  message storage and retrieval system
      that is ideal for Usenet newsgroups, Fido echoes and other types  of
      discussion  forums.   The  message  system can efficiently store and
      recall messages from thousands of message areas making it ideal  for
      major  Usenet  storage  sites.   The  maximum number of messages and
      message areas is limited only  by  available  disk  space.   Message
      text  compression  is  performed  automatically to reduce disk space
      requirements.

      Messages are organized in a hierarchical (tree-structured)  fashion.
      The  top  level can have categories such as Usenet and Fido.  Within
      the Usenet group there might be  subcategories  such  as  "alt"  and
      "comp".     Within    usenet.alt    you    would   find   additional
      subsub-categories, etc.  Users can explore the areas  by  moving  up
      and  down  through  the  hierarchical levels or by browsing the full
      set of forums as  an  alphabetical  list.   By  using  sophisticated
      indexing   techniques,   TSX-BBS   is   able  to  provide  virtually
      instantaneous access to any message area.  Users can locate  message
      areas  by doing searches for words in the area name.  Users also can
      search for messages containing specified words  and  expressions  in
      the body of the message.

      Within  an  area, messages are sorted by their creation date (rather
      than the date they were received by the  board).   Messages  on  the
      same  topic  are  grouped into "threads" making it easy to follow an
      exchange of messages.  TSX-BBS keeps track of the last message  read
      in  each  area  so that users can easily read new messages in forums
      with many messages.  Reading messages in one area  does  not  affect
      the last-message-read pointer for other areas.

      A  "privilege expression" (see Section 16.14) can be associated with
      each area to control which users can access the  area.   This  makes
      it  easy  to  set  up  adult discussion forums and to create private
      forums for groups that are using the board  as  a  message  exchange
      system.   Forum access restrictions are especially useful for Usenet
      which has a number of newsgroups which are not suitable for  general
      distribution.

      A   QWK   facility  is  built  into  TSX-BBS  to  provide  efficient
      downloading of messages for off-line readers.

      A touch of a key invokes the TSX-BBS full-screen message  editor  to
      compose  a  new  message  or  a  reply.   When  writing a reply, the
      original message is shown in a  split  screen  window  and  original


      Chapter 16. TSX-BBS                                              180


      text  can  be  quickly  cut  and  pasted  into the reply.  Users can
      delete messages that they wrote but only the  sysop  (or  designated
      message managers) can delete messages posted by other users.

      There  are  "tosser" programs available to process incoming Fido and
      Usenet messages.  At the option of  the  sysop,  new  message  areas
      (categories)  can  be  created  automatically  by  the  tosser  when
      messages arrive for areas that did not previously exist.  The  sysop
      can  block  all  automatic  area  creation or can enable it only for
      subcategories of selected areas.


      16.10 E-mail

      TSX-BBS includes a powerful electronic  mail  (e-mail)  system  that
      allows  users  to  send  messages to each other.  They can also send
      and receive SMTP (Simple Mail Transfer  Protocol)  messages  through
      the Internet and they can send and receive Fido netmail messages.


      16.11 Direct Internet Access

      In  addition  to Internet mail and Usenet newsgroups, TSX-BBS offers
      direct, interactive access to the Internet  using  FTP  and  Telnet.
      The  File  Transfer  Protocol  (FTP)  program  allows  you to browse
      through files on other computers connected to  the  Internet.   Once
      you  have  found  a  file  of  interest, FTP transfers the file to a
      "personal file workspace" directory on the TSX-BBS system.  You  can
      then  use  X/Y/Z-Modem  to  download  the file from the TSX-BBS work
      area to the local computer.

      Telnet is a terminal emulator program that you can use to  log  onto
      another  computer  connected to Internet.  With Telnet you can be an
      interactive user on computers around the world.

      If you authorize it, users can also  access  your  BBS  through  the
      Internet  by  using  Telnet.   They  run  Telnet  on  their personal
      computers and specify your BBS address as the  host  address.   They
      then  log  on  just  like  dial-in users and have full access to the
      BBS.

      FTP and Telnet run as "native" programs on the  same  computer  that
      is  running  TSX-BBS.  There is no need to buy a separate, dedicated
      Internet server computer.  You can  provide  your  users  with  full
      Internet access and do it all with a single computer system.


      16.12 Incoming SLIP connections

      If  you  have  an  Internet  connection,  you  can  resell  Internet
      connections to your users.  Your users can call your  BBS,  log  on,
      and  then  shift  their  connection  from ASCII to SLIP (Serial Line
      Interconnect Protocol).  They are then  connected  to  the  Internet
      through  your BBS and they can run programs such as FTP, Telnet, and
      Mosaic on their local computers to access  sites  on  the  Internet.


      Chapter 16. TSX-BBS                                              181


      You  can  limit  which  users are authorized for SLIP access and the
      BBS daily time limits apply to SLIP connections.


      16.13 On-line "Chat"

      A popular multi-line BBS feature is real-time conferencing,  "Chat".
      Chat  allows  users to set up round-table conferences where they can
      carry on multi-party discussions in real-time.  TSX-BBS chat  allows
      the  sysop  to  create permanent discussion topics; users can create
      temporary chat areas that are deleted automatically  when  the  last
      user  leaves  the  area.  The chat system features split screen mode
      which allows users to view the ongoing conversation while  composing
      their own contributions.


      16.14 TSX-BBS System Security

      TSX-BBS  allows the sysop to set many privilege and limit values for
      each user.  Controls such as daily time limit, download file  limit,
      and  use  of  individual  system functions such as the file library,
      E-mail, chat, QWK, etc.  may be set for each  individual  user.   To
      simplify  management, the sysop may also define user "classes" which
      describe sets of  limits  and  privileges.   A  class  can  then  be
      assigned   to  a  user,  changing  each  of  the  users  limits  and
      privileges to those of the class.

      The TSX-BBS user privilege system is simple but extremely  powerful.
      Each  user  is  assigned  a  "security  level" that ranges from 0 to
      65535.  In addition, there  are  80  sysop-defined  privilege  flags
      that  may  be turned on or off.  The meaning for each privilege flag
      may be assigned by the sysop.  The privilege flags can  be  used  in
      privilege  expressions  along  with  the  security  level  and other
      conditional tests such as the date, time,  day  of  the  week,  etc.
      TSX-BBS  privilege  expressions  can  include multiple logical items
      with 'AND' and 'OR' logical operators and parentheses for  grouping.
      For  example,  the following privilege expression is true for a user
      who has a security  level  equal  to  or  greater  than  50  or  has
      privilege   flag  1  enabled:  "(PRIVLEV>=50||P1)".   The  following
      privilege expression is true only on Saturday: "(DAYOFWEEK==7)".

      In addition to the security level and  privilege  flags,  the  sysop
      can  also assign a "group" number to users.  This can be used to set
      up private file and message areas accessible only to members of  the
      group.   This is extremely useful for commercial BBS operations that
      provide support areas for various companies or organizations.


      16.15 System Control

      TSX-BBS comes with a "SYSOP"  program  that  provides  comprehensive
      control  over  your  system.   With  the "dashboard" display you can
      monitor which lines are in use, what users  are  on-line,  and  what
      activities  are  taking  place.   The  sysop  can also "spy" on user
      sessions.  Real-time statistics  displayed  include  the  number  of


      Chapter 16. TSX-BBS                                              182


      logons,  new  user  authorizations,  files  uploaded and downloaded,
      messages sent and received,  door  programs  executed,  and  overall
      system loading.

      The  sysop can examine and modify user authorization entries, change
      privileges  and  examine  usage  statistics  while  the  system   is
      running.   Statistics  kept  for  each  user include the date of the
      user's  first  and  last  logons,  the  total  connect  time,  bytes
      uploaded  and  downloaded,  and  information about the current day's
      usage.  Log  files  can  be  enabled  to  record  even  more  detail
      including the date and time of each file upload and download.

      The  sysop  can  examine and edit file descriptions and monitor file
      download counts.  A cut-and-paste clipboard makes it  easy  to  move
      files  from one file area to another.  All of this can be done while
      the system is in full operation.

      The SYSOP program can be run  from  the  console  and  from  dial-in
      lines by properly authorized users.


      16.16 TSX-BBS Is a Complete System

      When  you  buy  TSX-BBS  you get a complete, integrated system.  The
      basic system includes the  file  librarian,  mail,  forums,  voting,
      QWK,  and  classified  ads,  all  without  having to buy third-party
      add-ons.  Optional components are Chat,  Fido  and  Usenet  support,
      the TPL programming language, networking, FTP, Telnet, and NFS.







                                   Chapter 17

                             The Full TSX-32 System




      If  you  like  TSX-Lite  but need to support more than two users, or
      need networking, real-time, or 32-bit development tools, it is  time
      to  step  up to a full TSX-32 system.  The following list summarizes
      features that either come with, or  are  available  as  options  for
      TSX-32.


      17.1 Support for Large Systems

      Whereas  TSX-Lite  is  limited  to  supporting  two  users, the full
      TSX-32 system is available with or without limits on the  number  of
      interactive  users.   Most  TSX  installations  run  8,  16,  or  32
      terminal  lines,  with  some  systems  supporting  over  100  users.
      TSX-32  supports "smart" serial cards and multi-console devices from
      several vendors.


      17.2 Networking

      TSX-32 networking is a full  featured,  TCP/IP  based,  peer-to-peer
      network.    Programs  can  transparently  access  files  across  the
      network including full file  sharing  and  record  locking.   Remote
      login  allows  you  to  work  on other network nodes as easily as if
      your workstation were directly connected to  them.   Other  features
      include  remote program execution, printer sharing, and an interface
      to Internet and systems such as VAX/VMS, Unix, and  Novell,  through
      FTP, Telnet, and NFS.


      17.3 Real-time Support

      S&H  is  famous  for  combining  critical  real-time facilities with
      timesharing services on the same computer.   TSX-32  is  the  choice
      for   factory   automation,  instrumentation,  and  other  real-time
      applications.


      17.4 Disk Shadowing

      The  disk  shadowing  option  for  TSX-32  causes  changes  made  to
      selected  files  on  one  disk  to  be "shadowed" (or "mirrored") to
      another  disk  on  either  the  same  machine  or  another   machine
      connected  through  the  network.   This  makes  it  easy  to set up


                                      183


      Chapter 17. The Full TSX-32 System                               184


      fault-tolerant systems that can quickly recover without losing  data
      even if one disk or computer goes down.


      17.5 Tape Support

      SCSI  tape  support  allows  the  TSX BACKUP and RESTORE programs to
      manage large data loads with ease.


      17.6 MessageNet

      MessageNet is  the  electronic  mail  system  for  TSX.   The  basic
      MessageNet  system, which is provided when you register TSX-Lite and
      is a standard part of TSX-32, allows users to send  electronic  mail
      to  each other.  It features address books, mailing lists, and "file
      folders"  for  storing  mail.   The  optional  Advanced   MessageNet
      product  extends  MessageNet  to  allow  messages to be sent between
      computers running TSX.  These transfers can take place on  a  demand
      basis  or at scheduled times to take advantage of lower phone rates.
      Advanced MessageNet also provides a bridge to global e-mail  systems
      such as EasyLink and MCI Mail.


      17.7 Single-user Option

      For  those  situations  where  TSX-32 may be used in a networking or
      real-time environment, a low-cost, single-user version of TSX-32  is
      available.    This  version  supports  real-time,  networking,  disk
      shadowing, and all of the features of the full  product  but  limits
      access  to  one  user  at a time.  This is especially attractive for
      factory automation and instrumentation applications.

      S&H Computer Systems wants to  be  your  operating  system  business
      partner.   We  regularly enhance our product to suit customer needs,
      assist customers in using the TSX environment as an  application  or
      development   platform,   and   employ  a  vast  array  of  built-in
      diagnostic tools to help solve problems.  You have now had  a  taste
      of  our  product.   What  we  can't  convey  with this demonstration
      version is that the staff at  S&H  is  helpful,  knowledgeable,  and
      available.  Please call us and experience the S&H difference today!

                           S&H Computer Systems, Inc.
                            1027 17th Avenue, South
                         Nashville, TN 37212-2299  USA

                              Phone: 615-327-3670
                              Fax:   615-321-5929
                              CompuServe: 71333,27
                       Internet: 71333.27@compuserve.com

      Note:  The  latest  version  of  TSX-Lite  and TSX-BBS can always be
      obtained from the S&H Support BBS.


      Index                                                            185


      16550 UART adapters, 13, 84         Console screen saver, 26
      Adaptive scheduling, 3              CONSSTIME sysgen parameter,
      ALLOCATE command, 87                         26
      ALT-digit session selection,        Control characters, 24
               9                          COPY command, 96
      ANSI terminals, 16, 23, 63          Copyright notice, 173
      Answer enable, 17                   COUNT command, 98
      ASSIGN command, 87                  CSHSIZE sysgen parameter, 78
         system wide symbols, 77          Ctrl-W-digit, 9
      ASSIGNMENT command, 87              Data cache, 5
      Authors of TSX-Lite                    showing statistics, 156
         Dan Cappannari, 155                 size of, 78
         John Mott, 155                   Data caching, 68
         Phil Sherrod, 155                Datascope, 19
      Autobaud setting, 15, 17            Date
      AUX device name, 31                 DATE command, 99
      Background batch jobs, 54              displaying, 156
      BACKUP command, 88                     format of, 86
      BATCH command, 54, 64, 92              setting, 141
      Batch files, 53                     DEALLOCATE command, 99
      Baud rate setting, 14               DEASSIGN command, 99
      BBS, 174                            DEC terminals, 16, 23, 63
      BBS server, 2                       DEFDWRITE parameter, 31
      BBS software                        DEFINE KEY command, 100
         setting up, 10                   DELETE command, 100
      BIOS, 3                             DESQView, 2
      BNU FOSSIL driver, 36               DETACH command, 101
      BOOT command, 22, 93, 161           Device names, 40
      Bulletin board server, 2            DIFFERENCES command, 103
      Bulletin board software             Direct write programs, 30
         setting up, 10                   DIRECTORY command, 105
      BYE command, 93                     Directory searching, 40
      CALCULATE command, 93               Disclaimer, 173
      CALENDAR command, 94                Discussion forums, 179
      CALL command, 94                    Disk shadowing, 183
      Cappannari, Dan, 155                DISPLAY command, 56, 107
      CD command, 95                      Doorway program, 2
      CD ROM support, 22                  DOQUEUES sysgen parameter, 79
      CGA controllers, 63                 DOS command, 32, 107
      CHAIN command, 94                   DOSLPTTIME sysgen parameter,
      Chat, 181                                    35
         see PHONE command, 66            DOSNET option, 12
      CHDIR command, 95                   DOSNETFLAG sysgen parameter,
      CHKDSK, 29                                   69
      CLS command, 95                     DOWINPRT sysgen parameter, 79
      Colors                              DOWNLOAD command, 107
         setting, 149                     DPMI, 38
         showing possible, 156            DUMP command, 108
      COM port setup, 13                  E-mail, 184
      COM3 setup, 20                      E32, 109
      Command files, 53                   EasyLink interface, 184
      COMMAND.COM running, 32, 107        EDIT command, 109
      Commands, 86                        EDIT-32, 109
      Communication lines, 26             EMM386, 36
      CON device name, 31                 EMS, 36


      Index                                                            186


      EMS enabling, 147                   Keyboard
      Environment variables, 31           Keyboard mapping, 27
      Error logs, 69                         problems, 82
      Ethernet, 3, 64                     KEYLOAD command, 27, 122
      EVALUATE command, 110               KILL command, 122
      EVENT command, 110                  Lantastic, 3
      Event logs, 69, 157                 Lexical functions, 58
      Execution priority                  Log files, 54
         setting, 147                     Logging of terminal I/O, 144
      EXIT command, 110                   Logical operators, 58
      EXP executable programs, 38         Logitech mouse, 21
      EXPAND command, 111                 LOGOFF command, 122
      Expanded memory, 36                 LOGON program, 19, 76
      Explicit printing, 48               Lost characters, 84
      Extended memory, 37                 LSTARTUP.CMD file, 75, 77
      Factoring commands, 98              MACROS command, 122
      Fido, 179                           MAIL command, 124
      File access control, 19, 116        Mailboxes, 70
      File protection, 116                MAKELOAD program, 75
      FILEWATCH command, 113              MAXP0MEM parameter, 37, 79,
      FIXEDSPEED line option, 15,                  85
               36                         MCI Mail interface, 184
      Flow control, 15, 84                MD command, 124
      FMAN command, 114                   Memory
      Foreign keyboards, 27               Memory page, 67
      FORMAT command, 117                 Memory space limit, 37, 79,
      FOSSIL driver, 36                            85
      FPROTECT program, 19                   displaying size, 158
      French keyboards, 27                   paging statistics, 158
      FTP, 2, 180, 183                       setting virtual size, 147
      German keyboards, 27                MESSAGE command, 125
      GOTO command, 55, 117               MessageNet, 124, 184
      Handshaking setting, 15, 84         MetaWare High C, 38
      HANLOAD command, 117                Microsoft Windows, 169
      HELP command, 117                   MINIGEN, 10
      High C, 38                          Mirroring disks, 183
      High Sierra CD ROM format, 22       MKDIR command, 125
      HIMEM.SYS, 37                       MN command, 125
      HOLDPRIO option, 11                 Modem connection, 13, 15, 17
      HOST command, 118                      answer enable, 17
      IDLETIME attribute, 34                 S0 register, 17
      IDLETIME parameter, 12              Modem reset string, 16
      IF command, 56, 119                 Mott, John, 155
      Implicit printing, 48               Mouse support, 21
      Incremental backup, 91              MOUSEPORT logical name, 21,
      INITIALIZE command, 120                      83
      INQUIRE command, 56, 121            MOUSETYPE symbol, 21
      INSTALL.CMD file, 30, 75, 127       Multi-console adapters, 64
      International keyboards, 27         Multi-user, 4
      Internet access, 2, 180, 183        Names of devices, 40
      Introduction, 1                     Native system services, 38
      Italian keyboards, 27               NDP Fortran, 38
      JMAN command, 121                   NetBIOS support, 69
      KERMIT command, 121                 Networking, 180, 183
      Kernel file, 3                      Newsgroups, 179


      Index                                                            187


      NFS, 183                            QUEMAN.LOG file, 84
      NODWRITE option, 12                 QUEMAN.SYS file, 85
      Novell, 3                           Queue manager, 48
      Novell connection, 183                 problems, 84
      NUL device name, 31                 R command, 131
      Null modem, 13                      RAMDISKSIZ sysgen parameter,
      Numeric comparison, 57                       80
      Numeric operators, 57               RD command, 131
      Numeric symbols, 45                 Real-time support, 183
      OFF command, 125                    Rebooting, 22, 93, 161
      ON command, 125                     RECALL command, 131
      Operators, 57                       Registering TSX-Lite, 172
         logical, 58                      Relisys terminals, 24, 63
         numeric, 57                      RENAME command, 132
         numeric comparison, 57           RESTORE command, 133
         string, 57                       Ring answer enable, 17
         string comparison, 57            RMDIR command, 135
      Page fault, 67                      RS232 signals, 13
      Page Maker, 169                     RTS/CTS flow control, 15
      Page of memory, 67                  RUN command, 135
      PAGEFILE.TSX file                   RUNPRIORITY parameter, 55
         controlling size, 79             RUNTSX program
      Paradise 512 video, 170                problems, 81
      Parity setting, 15                  S0 modem register, 17
      Password for lines, 15, 18          Scheduling algorithm, 3
      PATH command, 126                   Screen corruption, 83
      PAUSE command, 127                  Screen print, 79
      PC Anywhere, 2                      Screen saver, 26
      PC-Term terminals, 16, 24           Scroll lock key, 7
      PGFILSIZ sysgen parameter, 79       SCSI support, 184
      Phar Lap, 38                        SEARCH command, 136
      PHONE command, 66, 127              Security Kit, 19
      Phone connection, 15                SEND command, 65, 139
      Phone lines, 17                     Session Manager, 7
      PMAN command, 11, 29, 127           SET CMDPROC command, 140
      POOLSIZEN sysgen parameter,         SET DATE command, 99, 141
               79                         SET DEFAULT command, 141
      PRIDEF sysgen parameter, 11,        SET EDIT command, 141
               55                         SET ENTRY command, 142
      PRINT command, 128                  SET EVENT command, 142
      Printing, 48                        SET HOST command, 142
      Priority of batch jobs, 55          SET LOG command, 144
      Priority of subprocesses, 11        SET LOGOFF command, 144
      Privileges                          SET MESSAGE command, 145
         displaying, 158                  SET NEWSTATISTICS command,
      PRIVIR sysgen parameter, 11                  146
      PRN device name, 31                 SET NOVERIFY command, 57
      Process windowing, 7                SET PRINTWINDOW command, 146
      Procomm, 118                        SET PROCESS command, 147
      PROMPT command, 130                 SET symbol command, 148
      PROTECT command, 130                SET SYSTEM command, 148
      PROTECT.CMD file, 76                SET TERMINAL command, 149
      Protected mode, 29                  SET TIME command, 152
      QINIT.CMD file, 85                  SET VERIFY command, 57, 153
      QMAN command, 130                   SET VIDEO command, 153


      Index                                                            188


      SET WINDOW command, 153                      18
      SET WORKING_SET command, 154        SYSPASSWORD sysgen parameter,
      Shadowing disks, 183                         15, 18
      Shared memory regions, 70           SYSTAT command, 165
      Sherrod, Phil, 155                  System commands, 86
      SHOW ALL command, 155               System management, 75
      SHOW ASSIGNS command, 155           System password, 15, 18
      SHOW AUTHORS command, 155           System statistics
      SHOW CACHE command, 156                resetting, 146
      SHOW COLORS command, 156            System wide logical symbols,
      SHOW DATE command, 156                       77
      SHOW DEVICES command, 156           Tape support, 184
      SHOW ERRORS command, 69, 156        TCP/IP networking, 180, 183
      SHOW EVENTS command, 157            Telephone support, 172
      SHOW FILES command, 157             Telix, 118
      SHOW FSTATUS command, 157           Telnet, 2, 64, 180, 183
      SHOW JOBS command, 158              Terminal printers, 51
      SHOW KEYS command, 158              Terminal type setting, 16
      SHOW MEMORY command, 158            Terminal types, 23
      SHOW NAME command, 158              Terminate and Stay Resident,
      SHOW PAGING command, 158                     32
      SHOW PRIVILEGES command, 158        Time
      SHOW QUEUE command, 159             TIME command, 165
      SHOW SYMBOLS command, 159           Time-sharing, 3
      SHOW SYSTEM command, 159               format of, 86
      SHUTDOWN procedure, 22, 93,            setting, 152
               161                        TMAN command, 165
      SLIP connections, 180               Trademark notice, 173
      SMD.DOC file, 43                    Troubleshooting, 81
      SORT command, 161                   TSAUTH program, 19, 77, 165
      Spanish keyboards, 27               Tseng 4000 video card, 170
      Speed setting, 14                   Tseng VGA controllers, 63, 83
      Spitfire                            TSGEN, 9, 167
         installing, 10                   TSR programs, 32, 84
      SPOOL.SYS file, 85                  TSX-32, 183
      Spooler, 48                         TSX-BBS, 174
      Spooler problems, 84                TSX32.SYS file, 3
      SPOOLER.LOG file, 84                TSXLOAD.CMD file, 75
      SPY command, 19, 162                TSXTERM, 71
      START.CMD, 76                       TSXUAF.TSX file, 77
      STARTQUE.CMD file, 84               Tuning the system, 78
      STARTUP.CMD file, 75                TUTOR command, 66, 165
      Statistics                          TYPE command, 166
         resetting, 146                   UART adapters, 13
      STOP command, 65, 163               UART emulation, 35
      String comparisons, 57              UNPROTECT command, 167
      String operators, 57                UPLOAD command, 168
      String symbols, 44, 88              Usenet, 179
      SUBPROCESS command, 164             VERSION command, 168
      Symbols, 56                         VGA controllers, 63, 83
         defining, 87                     VIEW command, 168
         removing, 99                     Virtual disk, 80
         string, 88                       Virtual memory, 37, 66, 79,
      SYSMON command, 165                          85
      SYSPASSPR sysgen parameter,         Virtual UART support, 35


      Index                                                            189


      VMAXJOBS sysgen parameter, 78
      VT100 terminals, 16, 23
      VTxxx terminals, 63
      WAIT command, 169
      Warranty, 173
      WHO command, 169
      Wildcard specifications, 40
      Wildcat
         installing, 12
      WIN command, 169
      Windows under TSX, 169
      WINPRT program, 147
      Working set, 67
      Working set size, 154
         controlling size, 154
      WSCMD command, 170
      Wyse terminals, 24
      X00 FOSSIL driver, 36
      XMODEM, 118
         download, 107
         upload, 168
      XMS, 37
      XON/XOFF flow control, 15
      YMODEM, 118
         download, 107
         upload, 168
      ZMODEM, 118
         download, 107
         upload, 168