PrintGL 1.52 HP-GL, HP-GL/2, and ADI Commands

                      (c) Copyright Ravitz Software Inc. 1990,1994


         Ravitz Software Inc.                              BBS/FAX 606-268-0577
         P.O. Box 25068
         Lexington, KY  40524-5068
         USA                                  Compuserve Cary Ravitz [70431,32]


         ------------------------------ Contents ------------------------------

         Introduction ....................................................... 2
         HP-GL Commands                                                       2
         HP-GL Character Sets .............................................. 10
         HP-GL/2 Commands                                                    12
         ADI Commands ...................................................... 15


                                                                            p-2
         Introduction ---------------------------------------------------------

           This   document  is   a   description   of   the  subset   of  HP-GL
           (Hewlett-Packard  Graphics  Language), HP-GL/2,  and  ADI  (Autodesk
           Device  Interface) that is supported by  PrintGL.  If you  are using
           PrintGL to work with commercial  graphics software,  then  you  will
           probably not need this manual.  If you are writing graphics software
           you  will  find  here  the information  needed  to  make your output
           compatible with PrintGL.

         HP-GL Commands -------------------------------------------------------

           PrintGL's HP-GL specification is taken from the  programming manuals
           for the HP 7475A, ColorPro (7440/17440), and 7550A.  The 7550 manual
           is  the  best reference for HP-GL - HP  manual 07550-90001.  PrintGL
           supports  the 7475, and 7440/17440 command sets except for character
           set 8 (Katakana), digitize commands, output commands, the error mask
           command, and some device control  commands.  Supported commands  are
           listed below.  Commands that are not applicable to printing, such as
           pen velocity, are  considered supported  but are completely ignored.
           Commands that are not supported are flagged and then ignored.

           In addition, PG,  AF, ES, LO, the enhanced IW command, character set
           5, and proportional spaced fonts, from the 7550, are supported.  And
           forty pens are allowed instead of eight.

           In reading a plotfile, PrintGL ignores carriage returns, line feeds,
           and nulls  except where  they may be valid characters (LB,  SM,  DT,
           esc.), and ASCII EOF (026) is interpreted as an end of file mark.

           AA x_center , y_center , arc_angle [, chord_angle]

             Arc absolute - AA moves  the pen through  an arc,  starting at the
             current position, with the pen in the current up/down state.

           AF

             Advance full page -  AF  starts  a new plot.  PrintGL starts every
             page with the pen up at 0,0.

           AP

             Automatic pen pickup - IGNORED

           AR x_center_delta , y_center_delta , arc_angle [, chord_angle]

             Arc  relative  - AR moves the pen through an arc, starting at  the
             current position, with the pen in the current up/down state.

           AS

             Acceleration select - IGNORED                                     


                                                                            p-3
           CA character_set

             Designate alternate character set - See HP-GL Character Sets for a
             list of character sets.

           CI radius [, chord_angle]

             Circle - CI draws a circle centered at the  current position.  The
             current up/down state and position are unchanged by a CI command.

           CP [spaces , lines]

             Character plot  - CP moves the pen by character spaces (+ is along
             the text)  and lines  (+ is up), using  the current up/down state.
             Using no parameters is the same as a carriage return/line feed.

           CS character_set

             Designate standard character set - See HP-GL Character Sets for  a
             list of character sets.

           CV

             Curved line generator - IGNORED

           DF

             Default values -  This  sets  default  values  for  the  following
             commands: CA, CS,  DR, DT, ES, FT, IW, LO, LT, PA, PT, SC, SM, SL,
             SR, SS, TL.

           DI [run , rise]

             Absolute  character direction - DI sets the baseline direction for
             labels. The default is 1,0.

           DR [run , rise]

             Relative character direction - DR sets the  baseline direction for
             labels. Run and rise are a percentage of P2X-P1X and P2Y-P1Y.  The
             default is 1,0.

           DTt

             Define label terminator - The label terminator ends an LB command.
             The default is ASCII 003.

           EA x_opposite_corner , y_opposite_corner

             Edge  rectangle  absolute  - EA draws a rectangle  defined by  the
             current position and the parameters.  The pen position and up/down
             state are unchanged.

           EC

             Enable cutter - IGNORED                                           


                                                                            p-4
           EP

             Edge polygon - EP draws the current polygon edge.  Any pen up/down
             used in creating the polygon is respected in drawing the edge.

           ER x_opposite_corner_delta , y_opposite_corner_delta

             Edge  rectangle relative  -  ER  draws  a rectangle  with  corners
             defined by  the current position  and the command parameters.  The
             current pen position and up/down state are unchanged.

           ES [ space [, line]]

             Extra space  - ES adds to the  space between characters and lines.
             The  units  are in  character  cells  (1.5*width,  2*height).  The
             allowed range is -1 to 1. -.3333 causes characters to touch.

           EW radius , start_angle , sweep_angle [, chord_angle]

             Edge  wedge - EW draws a wedge centered  at the  current position.
             The current pen position and up/down state are unchanged.

           FP

             Fill polygon - FP fills the current polygon.  Pen up/down commands
             used in creating the polygon are ignored.

             There is a limit of 2000 fill line segments per polygon.

           FS

             Force select - IGNORED

           FT [type [, spacing [, angle]]]

             Fill type - These are the fill types.  Type 2 is identical to type
             1 for PrintGL.

               1  solid lines spaced at half the pen thickness (see PT command)
               2  unidirectional solid lines spaced at half the pen thickness
               3  lines at the specified spacing
               4  cross hatched lines at the specified spacing
               5  type ignored

             A spacing  parameter  of 0 sets  the  spacing  to 1%  of the P1-P2
             diagonal. Spacing is in x axis units (this is only relevant if the
             axes have different scaling).  PrintGL supports any  integer angle
             for fill. Cross hatched lines are at angle + 90.

           IN

             Initialize                                                        


                                                                            p-5
           IP [p1x , p1y [, p2x , p2y]]

             Sets scaling points P1 and P2 - IP sets the scaling points (P1 and
             P2) in plotter units.  P1  and P2 are used by several commands  to
             help with size independent plots.

           IW [x_lower_left , y_lower_left , x_upper_right , y_upper_right]

             Input window - IW sets a clipping window in plotter units. With no
             parameters, the clipping window is turned off.

             If  PrintGL's  /YE switch is  set and user  scaling  is on then IW
             parameters are in user units.  In this case the window is rescaled
             with an IP command, but any SC command locks the current window.

           LB..text..terminator

             Label - Labels use the current character set, based on CA, CS, SA,
             and SS commands. See HP-GL Character Sets for font specifics.

           LO [ position_number ]

             Label origin -  LO  sets  the  label  origins,  shown  below.  For
             positions 4..9  and  14..19  the  label buffer is  limited  to 150
             characters. The default is 1.

             13                     16                      19
                3......  .......  ...6...  .......  ......9
                .     .  .     .  .     .  .     .  .     .
             12 2     .  .     .  .  5  .  .     .  .     8 18
                .     .  .     .  .     .  .     .  .     .
                1......  .......  ...4...  .......  ......7
             11                     14                      17

           LT [pattern_number [, pattern_length]]

             Line  type  - PrintGL's line type patterns are close  to, but  not
             identical  to HP's.  Pattern  length is a  percentage of the P1-P2
             diagonal with a default of 4%  and a minimum of 4 dots for types 1
             and 2 and 16 dots for other types.  Negative (adaptive) line types
             from the HP 7550 are supported.

             no parameter  solid            1  .               .
                                            2  ________        ________
             0             dots at          3  ____________    ____________
                           endpoints        4  ____________  . ____________  .
                           only             5  __________  __  __________  __
                                            6  ______  __  __  ______  __  __
                                            7  __________  . . __________  . .
                                            8  ______  . __  . ______  . __  .

           PA [x , y] [, x , y] ...

             Plot absolute - PA sets absolute mode and optionally moves the pen
             in the current up/down state.                                     


                                                                            p-6
           PD [x , y] [, x , y] ...

             Pen down - PD sets the pen  down and optionally moves it with  the
             current absolute/relative mode.

           PG [i]

             New page - PG starts a new plot. The parameter is ignored. PrintGL
             starts every page with the pen up at 0,0.

           PM i

             Polygon mode - PM  0 starts polygon mode.  The current position is
             the first point in the polygon.

             PM 1 starts  a new  subpolygon.  The  position after the next  pen
             movement is the first point in the subpolygon.  The first pen move
             of a subpolygon is done with the pen up, regardless of the current
             up/down status.

             PM 2 ends polygon mode.

             PM  1 and PM 2 close  the current subpolygon with  the current pen
             up/down state. If used without first starting polygon mode (PM 0),
             PrintGL adds an implied PM 0 before processing the PM 1 or PM 2.

             The following  commands are accepted in polygon  mode: PM, PA, PR,
             PU, PD,  AA,  AR,  CI  (circles  are  automatically  prefixed  and
             suffixed by PM 1), and IN.

             The polygon buffer is limited to 1000 data points.

           PR [x_delta , y_delta] [, x_delta , y_delta] ...

             Plot relative - PR sets relative mode and optionally moves the pen
             in the current up/down state.

           PS

             Paper size - IGNORED

             PrintGL ignores PS. The paper size must be set with the /L option.

           PT [thickness]

             Pen  thickness - PT specifies twice the line spacing used in solid
             fills and may be from 0 to 5.0 mm.  It is reset to .3 mm with each
             SP command.

           PU [x,y] [,x,y] ...

             Pen  up  - PU  raises  the pen and optionally  moves  it with  the
             current absolute/relative mode.                                   


                                                                            p-7
           RA x_opposite_corner , y_opposite_corner

             Shade  rectangle  absolute  -  RA  fills  a rectangle with corners
             defined  by the current position and the  command parameters.  The
             current  pen  position  and  up/down  state  are  unchanged.   The
             rectangle edge is not drawn.

           RO [angle]

             Rotate coordinate  system - RO or RO0  sets up a normal coordinate
             system.  RO90, the only other allowed value, sets up a system that
             is rotated 90 degrees.  The type of rotation depends on  the paper
             size.  This command  does  not change the scaling points, so an IP
             command is useful after an RO.

             The HP 7475 specifies two different meanings for RO90 depending on
             the  paper  size (A/A4 or B/A3).  PrintGL  decides  which  type of
             rotation to do based on the sum of  the  print  window  width  and
             height.  If this sum  is  greater than 24 inches  then large paper
             rotation is used. Otherwise, small paper rotation is used.

             Small paper rotation:              Large paper rotation:

             RO 0             RO 90             RO 0             RO 90

               y --------    0,0 -------- y     0,0 -------- y    y --------
                |        |      |        |         |        |      |        |
                |        |      |        |         |        |      |        |
             0,0 -------- x    x --------          |        |      |        |
                                                   |        |      |        |
                                                   |        |      |        |
                                                   |        |      |        |
                                                  x --------    0,0 -------- x

           RR x_opposite_corner_delta , y_opposite_corner_delta

             Shade  rectangle  relative -  RR fills  a rectangle  with  corners
             defined by  the current position and the  command parameters.  The
             current  pen  position  and  up/down  state  are  unchanged.   The
             rectangle edge is not drawn.

           SA

             Select alternate  character  set  -  SA  specifies  the  alternate
             character set as current.  The alternate character set  is  chosen
             with CA.

           SC [xmin , xmax , ymin , ymax]  or  SC xmin,xrto,ymin,yrto,2

             Scaling - SC sets user units. The units are defined by user values
             for  P1 (xmin,ymin)  and P2 (xmax,ymax)  or P1 and  the  ratio  of
             plotter to user units.  Using no parameters turns scaling off, and
             subsequent drawing is done in plotter units (1/1016 inch).        


                                                                            p-8
           SI [width , height]

             Character size absolute - SI sets the capital letter box width and
             height in centimeters.  Letter  spacing  is 1.5 *  width  and line
             spacing  is 2 * height.  Using no parameters with B or A3 paper is
             the same as  SI.285,.375  and  any  other  paper is  the  same  as
             SI.187,.269.

           SL [tan_angle]

             Character slant - SL sets  the character  slant.  The parameter is
             interpreted as the tangent  of  the angle from vertical.  Using no
             parameter sets the slant to 0 degrees.

           SM[c]

             Symbol mode  -  SM sets symbol mode, which centers the symbol mode
             character  at  any plotted point.  Any character from ASCII 033 to
             127 except ";" sets symbol mode.  Any other character turns symbol
             mode off.

           SP pen_number

             Select pen - SP selects a pen.  Using 0 or no parameter stores the
             pen  without selecting a new pen.  This is usually done at the end
             of a plot. PrintGL ignores any drawing with pen 0.

           SR [width , height]

             Character size relative - SR sets the capital letter box width and
             height as a percentage of  P2X-P1X and P2Y-P1Y.  Letter spacing is
             1.5 * width and line spacing is 2 * height. Using no parameters is
             the same as SR.75,1.5.

           SS

             Select  standard  character  set  -  SS   specifies  the  standard
             character  set as  current.  The standard character set  is chosen
             with CS.

           TL [positive_length [, negative length]]

             Tick length -  TL  sets the  tick lengths used by XT and  YT.  The
             parameters are lengths above  and  below the current position as a
             percentage of P2Y-P1Y for x-axis ticks and a percentage of P2X-P1X
             for y-axis ticks.

           UC [[pen_control ,] x_delta , y_delta] ...

             User character - UC specifies a  user defined character.  The  pen
             control number is 99 for pen down or -99 for pen up. Pen movements
             are relative, with x_delta in units of 1/4 the character width and
             y_delta in units of 1/8 the character height.

           VA

             Adaptive velocity - IGNORED                                       


                                                                            p-9
           VN

             Normal velocity - IGNORED

           VS

             Pen velocity - IGNORED

           WG radius , start_angle , sweep_angle [, chord_angle]

             Shade  wedge - WG fills a  wedge centered at the current position.
             The current  pen  position and up/down  state are  unchanged.  The
             wedge edge is not drawn.

           XT

             X-axis tick - XT draws a  vertical line, with  length specified by
             the  TL  command, at the current  position.  The  pen position and
             up/down state are unchanged.

           YT

             Y-axis tick - YT draws a horizontal line, with length specified by
             the TL  command, at  the  current position.  The  pen position and
             up/down state are unchanged.

           esc.(
           esc.Y

             Plotter on  - Esc.( and esc.Y turn the plotter  on.  This is  only
             relevant with the /YY option.

           esc.)
           esc.Z

             Plotter off - Esc.)  and esc.Z turn the plotter off. They are only
             effective with the /YY option. The plotter on and off commands let
             you  include comments or data to pass through to another device in
             the plotfile.  These are flagged as unsupported commands if /YD is
             set, as an indication that you should set /YY.

           esc.@, esc.H, esc.I, esc.M, esc.N, esc.R

             RS-232 device control commands - IGNORED                          


                                                                           p-10
         HP-GL Character Sets -------------------------------------------------

           PrintGL  supports all of the character sets that  are included  with
           the HP 7475 and 7440/17440 except Katakana, and adds character set 5
           and  the  proportional  spaced  fonts   from  the  7550.   PrintGL's
           characters are similar to but not identical to HP's.

              0  ANSI ASCII
              1  9825 character set
              2  French/German
              3  Scandinavian
              4  Spanish/Latin American
              5  Special Symbols (7550 extension)
              6  JIS ASCII
              7  Roman Extensions
              8  Katakana - NOT SUPPORTED
              9  ISO IRV
             30  ISO Swedish
             31  ISO Swedish For Names
             32  ISO Norway Version 1
             33  ISO German
             34  ISO French
             35  ISO United Kingdom
             36  ISO Italian
             37  ISO Spanish
             38  ISO Portuguese
             39  ISO Norway Version 2

           The character sets specify a font for codes 033..127. Codes 000..032
           and 128..255 are independent of the character set and are all no ops
           except these.

             003  default label terminator
             008  backspace
             009  half backspace
             010  line feed
             011  reverse line feed
             013  carriage return
             014  select alternate character set
             015  select standard character set
             032  space

           Each of  the  character sets  is available as a proportional font by
           adding 10 to the set number.  The proportional  fonts  are kerned to
           improve  appearance (the character spacing is adjusted to compensate
           for  character shape).  Use the LO  command to simplify working with
           proportional fonts. To improve the appearance of large text, use the
           ES command to reduce the character spacing.

           Codes 65 to 81 in character set 5 are symbols designed to be used in
           symbol mode (SM command) or as one character labels.  When used in a
           label (LB command) these characters  are centered at the current pen
           position and leave the pen position unchanged.                      


                                                                           p-11
           The  HP-GL  characters cannot  be printed  with  the  standard ASCII
           character  set.  The file HPGL.CHR is an HP-GL file that can be used
           to print a  replacement  for this page, showing  the character sets.
           Use  the command PRINTGL  HPGL.CHR  /M1  /AO0,0  with  a  /F  option
           specific to your printer to do this.                                


                                                                           p-12
         HP-GL/2 Commands -----------------------------------------------------

           PrintGL's HP-GL/2 commands include a subset of HP-GL/2 that lets you
           take  advantage  of  HP-GL/2's  pen  control  and  data compression.
           PrintGL's HP-GL/2 interpreter reads all of the HP-GL commands above,
           except  as noted below.  PrintGL acts like  an  HP-GL/2 plotter, not
           printer,  so  form feeds are done with the PG command  not the  form
           feed character.

           The  LA command  is not supported  - all  lines are drawn with round
           ends and round joints. And all clipping is done to the line center.

           When the  output format is  HP-GL  all of the  HP-GL/2 extended  pen
           control commands are  ignored.  The PT command  is needed to  ensure
           solid fills look good.

           AC [x , y]

             Anchor corner - AC  specifies the origin of  stroked fills.  It is
             handled even with HP-GL/2 off.

           BP

             Begin plot - BP is interpreted as PG;IN;.  It is handled even with
             HP-GL/2 off.

           CO "comment"

             Comment - This is handled even with HP-GL/2 off.

           CR [black_ref_red , green , blue , white_ref_red , green , blue]

             Color range - Sets the color ranges used by the PC command.

           FT [type [, spacing or shading [, angle]]]

             Fill type - When reading HP-GL/2, PrintGL accepts type 10 (shading
             percentage is the additional parameter) and 11 (raster fill number
             is the additional parameter).  Type 11 fills are converted to type
             10 with the shade level taken from the RF command.

             For solid  and  shaded fill types, to guarantee  good results, you
             must use the PW command to set the pen width  and  this width must
             magnify to no  more than 24 dots in the final image.  If either of
             these rules is broken, the fill may be striped rather than solid.

           IR [p1x , p1y [, p2x , p2y]]

             Set  scaling points relative - This is handled even if  HP-GL/2 is
             turned off.

           LT [pattern_number [, pattern_length, [mode]]]

             Line type -  HP-GL/2 allows  the  additional parameter  to  select
             relative (default) or  absolute pattern lengths.  This  is handled
             even with HP-GL/2 off.                                            


                                                                           p-13
           NP [number]

             Number  of  pens  -  Sets  the number of pens.  This is ignored by
             PrintGL, which can handle up to 256 pens.

           PC [pen [, red , green , blue]]

             Pen color - Sets the pen color.

           PE

             Polyline encoded  - This  starts PE mode.  It is handled even with
             HP-GL/2 off.

           PT [thickness]

             Pen  thickness  -  The  command is  not  part  of  HP-GL/2 and  is
             generally ignored.  If the  output format is HP-GL  or if  you are
             using /Y1 (HP-GL/2 without pen  control) then PT is interpreted as
             it is in HP-GL.

           PW [width [, pen]]

             Pen width - Sets the  pen width.  After magnification, the maximum
             width is 24 dots. PW is ignored if the output format is HP-GL.

           QL

             Quality level - IGNORED for HP-GL or HP-GL/2

           RF [index [,width, height, pen [.. pen]]

             Raster fill - RF is not fully implemented.  Instead it is read and
             the  pattern is  converted to  a shade level.  Pen numbers and the
             specific  pattern are ignored.  The shade level  is saved for  use
             with fill type 11.

           RO [angle]

             Rotate coordinate system  -  When  reading HP-GL/2,  this  command
             accepts 0, 90, 180, and 270 and always rotates counter-clockwise.

           SV [type [, option1 [, option2]]]

             Screened vectors - Sets the shade level used  to draw lines.  Only
             modes 0 and 1 are supported.

           TR [mode]

             Transparency mode - Sets opaque or translucent mode.

           UL [index [,gap1, .., gapn]]

             User  line type - UL is not fully implemented.  Instead it is read
             and the pattern is converted  to one  of PrintGL's eight  standard
             line types. The gaps must be less that 256.                       


                                                                           p-14
           WU [type]

             Width units - Sets the units used by the PW command.

           esc% .. A

             Enter PCL or RTL mode -  This command is treated  like esc.).  All
             commands are ignored until the next esc% .. B.

           esc% .. B

             Enter  HP-GL/2 mode - This command  is treated like esc.(.  It  is
             required before any commands are interpreted.

                                                                           p-15
         ADI Commands ---------------------------------------------------------

           With the /YA option PrintGL can read Autodesk ADI 4.0 vector plotter
           binary commands intermixed in the HP-GL. 1016 dpi coordinates or the
           current HP-GL user coordinates are assumed. The table shows each ADI
           command  and  the  equivalent  HP-GL  command   (as  interpreted  by
           PrintGL).  In  the ADI code column, the  code  number  and  "b"s are
           bytes,  and  "x" and  "y"  are words.  Eight line  types (other than
           solid) are supported.

             ADI command     ADI code     equivalent HP-GL

             begin plot      1 b          ignored
             end plot        2            PG;
             move            3 x y        PUx,y;
             draw            4 x y        PDx,y;
             pen             5 b          SPb;
             speed           6 b          ignored
             line type       7 b          if b=0 then LT; else LTb,2;
             raise pen       8            ignored
             abort           9            ignored