ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                       ANTIVIRAL TOOLKIT PRO 2.1                   for DOS

                                by Eugene Kaspersky

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ







                            USER'S GUIDE









ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ





 (c)Kami corp., Russia, 1992-1994.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ






Microsoft, MS-DOS and Windows are registered trademarks of Microsoft
Corporation. Borland, Turbo C, Borland C++ and Turbo Vision are registered
trademarks of Borland International. Other brand and product names are
trademarks or registered trademarks of their respective holders.









AVP is a powerful integrated antiviral package. This package can be used as
conventional and/or professional (Pro) antiviral system. It consists of
four programs:

 Antiviral scanner/disinfector  AVP.EXE
 Antiviral scanner/disinfector with database editor  AVPRO.EXE
 Antiviral resident monitor  AVPTSR.EXE
 Antiviral utilities  AVPUTIL.COM

The main features of AVP antiviral are:

 - a great number (more than 4500) of viruses and virus families that
   are detected and disinfected by AVP scanner;

 - Code Analyzer (heuristic scanner) detects new viruses or modified
   variants of old ones;

 - Unpacking and Extracting Engine allow to scan packed and archive files
   in on-the-fly mode;

 - Database Editor allows to add detection and disinfection information
   about new viruses which are unknown to current version of AVP scanner;

 - professional utilities and antiviral monitor are included.





 Table of Contents
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 1.     Installation and Getting Started with AVP
 1.1.   System Requirements
 1.2.   Using AVP to Detect, and Disinfect Viruses
 1.3.   SET file and Updating Procedure
 1.4.   Language Support File
 1.5.   It Seems that I have an Infection. What Should I Do?

 2.     Antiviral Scanner/Remover  AVP
 2.1.   Description and Features
 2.1.1. Main Features of the Pro Version
 2.1.2. Main Database Features
 2.2.   Command Line Options and Errorlevels
 2.3.   Interface and Menu Commands
 2.3.1. Scan Commands  (Alt-S)
 2.3.2. View Commands (Alt-V)
 2.3.3. Edit Commands (ALt-E)   (Pro Version)
 2.3.4. Tools Commands (Alt-T)
 2.4.   Code Analyzer
 2.5.   Unpacking Engine
 2.6.   Extracting Engine
 2.7.   Help System
 2.8.   Messages

 3.     Antiviral Database      (Pro version)
 3.1.   FILE Record
 3.2.   JMP Record
 3.3.   MEMORY Record
 3.4.   SECTOR Record
 3.5.   Link of Special Procedures






 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 1.  Installation and Getting Started with AVP
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ







The installation procedure is quite simple. You should copy all files from
the distributive floppy disk(s) to a newly created subdirectory of your
hard drive (for example "C:\AVP") or use AVP from the floppy disk. If you
already have a previous version of AVP you should overwrite it with the
latest version. After copying this package to your hard disk it is ready to
use.

This product is a professional antiviral toolkit. It contains four main
executable files:

 - antiviral scanner/disinfector AVP.EXE
 - antiviral scanner/disinfector/database editor AVPRO.EXE
 - antiviral monitor AVPTSR.EXE
 - antiviral utilities AVPUTIL.COM

If you are a NOVICE USER it is better to use antiviral scanner AVP.EXE only.
By running AVP.EXE you can scan your disk(s) for a virus presence, and
disinfect a virus if one is found. The AVP.EXE is an integrated environment
scanner. The control for AVP.EXE is based on standard pop-up menus and
dialog boxes. By pressing the F1 hot key or by using the Help menu you will
get all the information you need.

If you are a SECURITY EXPERT you can use the professional features of this
package the database editor, antiviral monitor, and utilities which are
used for detecting, and analysis of new unknown viruses.


 1.1.   System Requirements
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  Hardware:

Any PC-compatible computer with memory >= 640K. PC386+ with 1M or more of
memory is recommended.

  Software:

 DOS version - 3.30 or above.
 Minimum free conventional memory - 580K.
 Minimum free file handles - 16.

It is recommended to install XMS driver to avoid memory problems.

To reach these conditions it is necessary to include in CONFIG.SYS file
the lines:

 DEVICE=HIMEM.SYS
 DOS=HIGH
 FILES=32



 1.2.   Using AVP to Detect, and Disinfect Viruses
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

When using AVP.EXE it loads the antiviral database(s) at first, and then
scans the system memory for a memory resident virus presence. Next the Test
Dialog Box appears on the screen. Press the ENTER key to virus scan all
your hard disks for viruses or point to the path of the files you want to
virus scan for example (C:\TEST\).

If you want to change the virus scanning options you should press the Alt-S
hot key to call the Setup Dialog Box.

To change the virus scanning path you should press the F9 hot key or
select the Scan|Test menu. To cure infected files you should press Ctrl-F9
hot key or select the Scan|Cure menu.

To exit AVP.EXE press the standard Alt-X hot key or select Scan|Exit menu.


 1.3. SET file and Updating Procedure
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The SET file (AVP.SET) contains a list of file names for the antivirus
databases that are used for scanning, and disinfection of computer viruses.
The SET file contains text strings (in ASCII format) that can be modified or
changed with any text editor.

Each line contains only one file name. They are the names of the antivirus
database files used to scan, and disinfect computer viruses. To add a new
database file to the list it is necessary to insert a new line into the SET
file, and type the new file name there. To exclude a database file or files
from the list you should either delete the line, or place the charcter
";" at the beginning of the line.

For example:

 Database file      Comment <- Do not include this line in
                    the SET file or any comments below.
 -------------      --------------------------------------

 KERNEL.AVB         Kernel database
 ;DISINF.AVB        Disinfection database, now excluded from the set
 V_941104.AVB       Main anti-virus database
 TROJAN.AVB         Trojan programs database
 UNPACK.AVB         Unpacking engine
 EXTRACT.AVB        Extracting engine
 CA.AVB             Code Analyzer

AVP should not be executed without the file KERNEL.AVB because no viruses
will be detected. This file name must be in the first line of the SET file.

To update your AVP package it is necessary to copy the update files into the
AVP directory, and add the new database names to the SET file.

For example:

Database file       Comment
-------------       -------------------------------------------------------

 KERNEL.AVB         Kernel database
 V_941104.AVB       Main antivirus database
 UP941113.AVB       Update database
 UP941120.AVB       Update database that was just added


 1.4. Language Support File
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

All messages from the AVP scanner (including Pro version) are collected in a
Language Support File (AVP.LNG). This file must be present in AVP directory.
The AVP scanner will not run if it cannot find the LNG file in the AVP
directory.

The default LNG file contains messages in English. To force AVP to use
another language you should overwrite the default AVP.LNG (English) file
with the language you want to use. To obtain a LNG file with the language
you want to use contact the AVP dealer in your country.


 1.5.  It Seems that I have an Infection. What Should I Do?
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The first step is executing AVP.EXE to virus scan all the programs files
(executable/batch/SYS/overlay), and sectors of your disks including
floppies disks. If the infected files/sectors are found, run the Cure
process.

If the infections are not found you should press the "Alarm!" button in
Setup dialog box, and virus scan all your disks again. If AVP.EXE displays
any warning messages you should call the system programmer, security
expert, or contact us via E-Mail to send one of these infected files to us
for analysis.

For more information see the topic "Computer viruses detection, and removal
methods" of the AVP.EXE Help system.






 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 2.  Antiviral Scanner/Remover  AVP
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ







The AVP.EXE antiviral scanner tests, and disinfects files, and system disk
sectors that are infected by known viruses, and checks them for
suspicious code. You can read the descriptions of the known viruses in
the Help system topics.


 2.1.   Description and Features
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The AVP.EXE antiviral scanner checks for a virus presence in:

 - system memory
 - files including packed and archive
 - hard disk sectors containing the Master Boot Record
 - disk sectors containing the Boot sector
 - File Allocation Table

The main features of AVP.EXE are:

- removing of viruses from files, and system sectors. We recommend to
restore the infected files from the backup copies but if it's impossible
the AVP.EXE antiviral restores the infected objects to their original form
(if it is possible) or in a form closest to the original one.

- possibility to scan inside of packed and archive files.

- the AVP.EXE scanner checks files, and system sectors for new unknown
viruses the are not included in antiviral database. This feature is
available with the Code Analyzer routine. According to several test results
this routine detects about 80% of unknown viruses.

- two different modes of file scanning: the default mode, and the
redundant one. The default mode is enough in most of cases. By using the
default mode the antiviral scanner analyses the file header, and the file
entry point(s). The redundant search mode causes complete scanning of
entire file instead of scanning the file's entry point(s) only. This is
necessary in case of a infection by a specific virus or in case of a
incorrect infection.

- the test, and disinfection of the system memory. It's recommended to boot
from the virus-clean system floppy before scanning the files, and sectors
for viruses. It is necessary for a guaranteed absence of viruses in the
memory because the memory resident virus can prevent the file
recovery, and even reinfection of the files after scanning. There are memory
resident viruses which wait for a antiviral program execution, and when
this antiviral scanning is started these viruses damage disk sectors (see
the virus "Caz".

- the files, and system sectors can be tested for the changes in their
bodies by using control sum (CRC) algorithm. If used the next antiviral
scanning using AVP.EXE finds the differences between the old, and new
control sums then AVP.EXE displays a corresponding message.

- the AVP.EXE antiviral scanner checks whether it's own file has been
modified, and if it detects changes AVP.EXE reports about it.

- the powerful Help-system that contains the complete information about the
viruses, and the methods about the removing the viruses. It's possible to
view demo-effects while reading the virus descriptions if the virus
manifests itself by a visible sign.

- the support of the XMS memory, mouse, screen format 43/50 lines for
EGA/VGA adapters. The antiviral scanner allows you to change, and save
these settings.


 2.1.1. Main Features of the Pro Version
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The antiviral scanner/remover of the Pro version contains the antiviral
database editor. By using this editor it's possible to create new antiviral
database(s), and insert records with detection, and disinfection
information for new viruses. By using these records the computer expert can
direct the antiviral scanner to detect, and remove new unknown viruses.

The antiviral database contains four types of records:

JMP: calculation of the Entry Point into the file or sector body

FILE: information about detection, and disinfection of file viruses

SECTOR: information about detection, and disinfection of boot viruses

MEMORY: information about detection, and disinfection of the memory
component of TSR viruses

The database fields are appending in the semi-automatical mode: it's enough
to point where to search for the virus, how to remove it, and to point to
the infected file or the file containing the infected sector. The
information about this virus will be inserted into the new database record.



 2.1.2. Main Database Features
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The main database features are:

- using the control sums instead of the virus masks. The checksums of the
parts of the virus code are placed into the records instead of the parts of
code for comparing. This feature will decrease the size of the database,
and increase scanning speed;

- several standard methods of the virus detection, and disinfection.  More
than 10 standard methods of the virus disinfection make the procedure of
including the new records quite easy;

- dynamical linker of the special subroutines. This feature is used with
detection, and disinfection of viruses that use encryption or nonstandard
methods of infection. In these cases it's enough to write one's own C or
Assembler program that decrypts/disinfects the virus, compile this program
into OBJ-file, and insert this OBJ-file into the database record. These
special subroutines will be linked with main EXE-module, and would be
called during processing of the database records;

- calls to external functions. These special subroutines of the database
can access external names (constants, functions, arrays and structures).
The external names are divided into standard (they are defined into the
main EXE-module), and special (they are defined by user in one of the
database records). The viruses from one virus family that use the same
decryption algorithm can be decrypted by a special subroutine that is
called with different arguments from several records. In this case it is
necessary to write only a decryption subroutine, compile it, append it into
the one of the database records, and then to call that routine from other
database records.



 2.2.   Command Line Options and Errorlevels
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
When called from the DOS prompt AVP.EXE and AVPRO.EXE support the following
format:

 AVP [OPTIONS ...] [file or disk NAME]

 Options
 ÄÄÄÄÄÄÄ

"/T" switch directs the antiviral scanner to scan files, and sectors for the
presence of viruses. In this mode, searching for viruses, and virus-like
blocks in files, and disk boot sectors is carried out. This switch is "ON"
default.

"/-" switch directs the antiviral scanner to disinfect files, and boot sectors
infected by viruses. The antiviral scanner recovers files, and sectors in
their original form (if possible), or in a form closest to the original one.
The infected boot sector, and MBR are overwritten by MS-DOS 6.0 system sectors
if it is impossible to restore them to their original form.

"/W[A][=filename]" directs tells the antiviral scanner to save all messages
displayed in the scan windows into a report file. The "Filename" parameter
is the name of the report file, the default name is AVP.MSG. "/WA" switch
directs the antiviral scanner to append the report to the existing one,
otherwise the report file will be overwritten.

"/C" switch directs the antiviral scanner to detect modification in objects
by using CRC table if this table has been created beforehand.

"/D" switch directs the antiviral scanner to run in daily mode. In this mode
AVP.EXE will process the antiviral scanning on the first execution only
(in this day). It will not scan for viruses if it is executed again. This
option is recommended for using the antiviral scanner from the AUTOEXEC.BAT
file only. Note: The antiviral scanner will test it's host file (AVP.EXE or
AVPRO.EXE) on every execution.

"/M" switch directs the antiviral scanner to skip memory testing.

"/P" switch directs the antiviral scanner to skip testing of the local disks
Master Boot Records.

"/B" switch directs the antiviral scanner to skip testing of the Boot Sectors
of local logical drives.

"/F" switch directs the antiviral scanner to test the File Allocation Table
of local logical drives.

"/O" switch directs the antiviral scanner to skip disinfection of the
read-only files.

"/S" switch turns off the beep signal.

"/TMP=path" switch points to the directory for temporary or swap files.
The environment variable TEMP (or TMP) is used by default. If neither the
"/TMP" switch or environment variable are defined, the program's
home directory is used for temporary, and swap files.

"/X" switch directs the antiviral scanner not use XMS memory. If you
experience conflicts with some memory managers you should disable the using
of XMS memory.

"/Y" switch directs the antiviral scanner to skip the dialog messages.
This option is recommended for using the antiviral scanner in batch mode.

"/Q" switch directs antiviral scanner to exit to the DOS prompt after
virus scanning, otherwise the main antiviral menu will be invoked.
This option is recommended for using the antiviral scanner in
batch mode.

"/?" switch directs the antiviral scanner to display the command-line help,
and return to the DOS prompt.

"NAME" parameter is the list of disk letters and/or file names which
should be virus scanned. It is possible to use the wildcard symbols "?", and
"*" in filenames, and wildcards instead of disk letters. When only the name
of a disk has been specified, for example "A:", then the files with default
extensions of the specified disks will be virus scanned. Other settings are
loaded from AVP.INI file.

 Examples:

 C:\COMMAND.COM - to virus scan C:\COMMAND.COM file
 C:\*.COM       - to virus scan all COM-files of C: drive
 C:*.*          - to virus scan all files of C: drive
 C: D: E:*.COM  - to virus scan all files with default extensions of C: and D:
                  drives, then scan all COM-files of E: drive
 *:             - to virus scan all files with default extensions of
                  all logical hard disks (C:, D:, ...)


Example of using AVP.EXE amd AVPRO.EXE from DOS command line:

 AVP.EXE /T /W C:*.* D:\MY_PROG\*.EXE D:*.COM /Y /Q

This set of parameters directs AVP.EXE to virus scan all files of drive C:,
then virus scan all *.EXE files of drive D: in directory D:\MY_PROG, and
there after all *.COM files of drive D:. The report will be saved into the
AVP.MSG (default) file. When the virus scanning is finished AVP.EXE will return
to the DOS prompt.


 Errorlevels
 ÄÄÄÄÄÄÄÄÄÄÄ
The results of virus scanning are available in return codes (DOS
Errorlevel) for use in batch files:

 0 - No viruses were found.
 1 - Scan is not complete.
 3 - Suspicious objects were found.
 4 - Known viruses were detected.
 5 - All detected viruses were cured.
 7 - File AVP.EXE is corrupted.
10 - Internal error in AVP.EXE program.



 2.3.   Interface and Menu Commands
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

This program has a standard Turbo-Vision user interface. Press the F10 hot
key to activate the menu system. Use the right-left up-down, and enter keys
to select an item. Then the submenus are displayed. Use the up-down, and
enter keys to select an item:

    Scan  (Alt-S)
    View  (Alt-V)
    Edit  (ALt-E)  (Pro version)
    Tools (Alt-T)


 2.3.1. Scan Commands  (Alt-S)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

With the Scan menu (Alt-S) you can test and/or disinfect files, and disk
sectors.


 Scan³Test (F9)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

With the Test command (F9) you can virus scan pointed objects for a virus
presence. Several messages will appear in the information windows.

The Start Dialog Box appears before the test/cure procedure:

 ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍ Test ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º                                         º
 º   Path _c:________________________      º
 º                                         º
 º                                         º
 º        OK   Ü   Setup  Ü   Cancel Ü     º
 º      ßßßßßßßß   ßßßßßßßß   ßßßßßßßß     º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

The "Path" field contains the list of disk letters and/or file names which
should be virus scanned.  It is possible to use the wildcard symbols '?'
and '*' in filenames and wildcard '*' instead of disk letter. When only the
name of a disk has been specified, for example 'A:', then the files with
default extensions of the specified disk will be virus scanned. Other
settings are loaded from AVP.INI file.

 Examples:

 C:\COMMAND.COM - to virus scan C:\COMMAND.COM file
 C:\*.COM       - to virus scan all COM-files of C: drive
 C:*.*          - to virus scan all files of C: drive
 C: D: E:*.COM  - to virus scan all files with default extensions of C: and D:
                  drives, then scan all COM-files of E: drive
 *:             - to virus scan all files with default extensions of
                  all logical hard disks (C:, D:, ...)


 Scan³Cure (Ctrl-F9)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

With the Cure command (Ctrl-F9) you can virus scan pointed objects for a
virus presence, and cure it. Several messages will appear in the
information windows.

The Request Dialog appears if the virus is detected while curing.

 ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍ Cure Request ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º                                                º
 º  File:   E:\VIRUS\v.com                        º
 º                                                º
 º  Virus:  Yankee                                º
 º                                                º
 º      Cure    Ü     Delete   Ü      Skip    Ü   º
 º    ßßßßßßßßßßß    ßßßßßßßßßßß    ßßßßßßßßßßß   º
 º    Cure All  Ü    Delete AllÜ     Cancel   Ü   º
 º    ßßßßßßßßßßß    ßßßßßßßßßßß    ßßßßßßßßßßß   º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

The commands are:

 Cure        - to cure this file
 Cure All    - to cure all the files without request
 Delete      - to delete the infected file
 Delete All  - to delete all the infected files
 Skip        - to skip curing this file
 Cancel      - to cancel virus scanning


 Scan³RAMCure
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

With the RAMCure command you can cure the memory parts of the viruses.
This operation can be performed automatically at the start of the program.
See "Scan³Setup" also.


 Scan³Cure & make CRC
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

With the Cure & make CRC command you can virus scan, remove viruses, and
create the CRC table at the same time. The CRC check is in use if the Use
the CRC option in the Setup menu. It checks for modifications of the
file/sector, and will accelerate the virus scanning about 2 times.



 Scan³Setup
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Setup command brings Setup Dialog, and you change the different options
if it is necessary.

 ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Scan Setup ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º                                                                      º
 º   Path: _*:________________________          Options                 º
 º                                               [X] Load for cure      º
 º   Mask:                   Sector options      [ ] Beep               º
 º    ( ) Programs            [X] MBR            [X] Show tree          º
 º    (*) All files           [X] Boot           [X] Split messages     º
 º    ( ) User defined:       [X] FAT            [X] Auto test dialog   º
 º           *.exe *.com                                                º
 º   Mode                    File options            Set options for:   º
 º    [X] Warnings            [ ] Subdirectories                        º
 º    [X] Code analyzer       [X] Remote disks            Speed     Ü   º
 º    [X] Deep scan           [X] Packed files        ßßßßßßßßßßßßßßß   º
 º    [ ] Redundant scan      [X] Archive files        Reliability  Ü   º
 º    [ ] Use CRC             [X] Cure readonly       ßßßßßßßßßßßßßßß   º
 º                                                       Alarm!     Ü   º
 º   Objects                 Memory options           ßßßßßßßßßßßßßßß   º
 º    [X] Sectors             [X] Interrupts                            º
 º    [X] Files               [X] Buffers                               º
 º    [X] Memory                                                        º
 º                                 OK   Ü       Save  Ü      Cancel Ü   º
 º                               ßßßßßßßß      ßßßßßßßß      ßßßßßßßß   º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

 Path
 ÄÄÄÄ
In this field you should type one or more path strings to be used for
the virus scan procedure. See Start Dialog.

 Mask
 ÄÄÄÄ
The files that have these extensions will be virus scanned by default (when
the file extensions are not pointed to directly in the "Path" field).

The standard setting is "Programs" which will direct virus scanning of the
files with extensions:  *.BAT, *.COM, *.EXE, *.OV?, *.SYS.

The selection of "All files" directs the virus scanning of all files marked
in "Path" field. This is necessary in case of an infection by viruses that
infect files on their opening and/or closing.

When the "User defined" block is choosen only the files defined in
corresponding field will be virus scanned.

 Mode
 ÄÄÄÄ
This box contains the options of main virus scanning modes. See also Scan
Messages.

"Warnings" directs activation of additional check procedures. This will
display a warning message if a file/sector contains the modified or
corrupted body of the known virus or a suspicious set of instructions is
found in memory while memory scanning.

"Code analyzer" directs activation of Code Analyzer engine.

The "Deep scan" switch turns on the "quality" of virus scanning if their is
suspicion of a infection by a self encrypted virus. When virus scanning
self encrypted files (viruses) the antiviral scanner decrypts the encrypted
code, and searches for a virus mask by using the result of the decryption.
If the "Deep scan" switch is turned on, the virus scanner completely
decrypts the encrypted code before virus scanning. If that switch is turned
off, the virus scanner processes a "brief" decryption procedure before
virus scanning.

"Redundant scan" directs complete virus scanning of entire file instead of
virus scanning only the file's entry point(s). This feature is strongly
recommended in case of a infection by viruses such as "3nop" which writes
itself into the middle of the file. In other cases this mode is not
recommended because it will make the virus scanning procedure several times
slower.

"Use CRC" directs using the CRC table to detect modification of virus
scanned objects. This table has to be created before using it by command
Cure & make CRC.

 Objects
 ÄÄÄÄÄÄÄ
This box contains the list of objects to scan.

"Sectors" directs virus scanning of system sectors depending on which
"Sector options" are choosen.

"Files" directs virus scanning of disk files including System, Hidden, and
Read Only files depending on the selection of the "File options".

"Memory" directs virus scanning of system memory including the High Memory
Area (if it is necessary) depending on "Memory options" choosen.

 Sector options
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
This box contains the list of system sectors to virus scan.

"MBR" directs virus scanning of all Master Boot Records (first disk
physical sector) of all available local Hard Drives for known viruses, and
suspicious code. These sectors are virus scanned if the "Path" string
contains any hard drive letter.

"Boot" directs virus scanning of the Boot sectors of selected local logical
drives for known viruses, and suspicious code. The boot sector is tested
before the first disk file virus scanning.

"FAT" directs the virus scanning engine to check the File Allocation Tables
for suspicious situations such as "pseudo-bad" sectors. See also Scan
Messages.

 File options
 ÄÄÄÄÄÄÄÄÄÄÄÄ
This box contains the list of file virus scanning options. See also Scan
Messages.

"Subdirectories" directs the virus scanning engine to process the
subdirectory tree from the directory pointed to in the "Path" field.  If
the disk name is entered in "Path" field ("C:") the scanning engine will
check the files, and directories from root directory.

"Remote disks" directs the virus scanning engine to virus scan remote
(network) drives if the "Path" field contains the string "*:" (all disks).

"Packed files" activates the Unpack Engine.

"Archive files" activates the Extract Engine.

"Cure readonly" directs disinfection of the Read Only files.

 Memory options
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
This box contains two memory virus scanning options. See also Scan
Messages.

"Interrupts" directs tracing, and checking disk and DOS interrupts. This
routine can conflict with some antiviral memory resident utilities, and
generate false alarms. In this case either disable the "Interrupts" option,
or remove the antiviral utility from memory. Warning: some memory resident
viruses cannot be detected if the "Interrupts" option is disabled.

"Buffers" directs checking the number of system buffers, and comparing this
value with the number of string BUFFERS=xxx in CONFIG.SYS file. This routine
displays a warning message if these values are different. Warning: some
utilities such as QEMM change the format of the buffers list. The buffer
checking routine does not work correctly in this case.

 Options
 ÄÄÄÄÄÄÄ
This box contains miscellaneous options.

"Load for cure" directs the loading of the entire antiviral database into
memory. If this option is disabled the main virus scanning engine will load
only the data needed to detect viruses, and not load the data needed to
disinfect them. In this case the antiviral scanner occupies less system,
and XMS memory.

"Beep" directs the virus scanning engine to beep if the virus is found.

"Show tree" directs the virus scanning engine to display a tree of scanned
directories.

"Split messages" directs the virus scanning engine to split the messages in
two different windows: "Scan window" and "Checkup window". The Scan window
will contain information about infected objects (files, sectors and memory)
as well as warnings, and some other messages. The Checkup window will contain
a list of clean objects. If this option is disabled all messages will be
shown in the "Scan window".

"Auto test dialog" directs the virus scanner to display Start Dialog Box
directly after execution from DOS prompt.

 Set option for
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
We understand very well that there are too many different options for the
NOVICE USER. To make the NOVICE USER's life more comfortable we have
decided to include a few buttons which globally change the setup for
different situations.

"Speed" sets the corresponding options to make the virus scanning process
fast.

"Reliability" sets the options to virus scan with confidence.
This option is default.

"Alarm!" should be used in case of an unknown virus which infects your
computer, and cannot be found with other settings. Warning: if you have a
large hard drive with thousands of files, and a lot of archives,
virus scanning  with "Alarm!" can take several hours.

 Save button
 ÄÄÄÄÄÄÄÄÄÄÄ
By using this button you can save the setup settings into the configuration
file AVP.INI.



 Scan³Save Report
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Save Report command brings Report Dialog. You can save the virus
scanning information in the text file or print it.

 ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Report ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º                                                º
 º  To  ( ) Printer          [X] Statistics       º
 º      (*) File             [X] Scan info        º
 º      C:\AVP\AVP.msg       [ ] Check up info    º
 º                                                º
 º        OK   Ü     Save Setup Ü     Cancel Ü    º
 º      ßßßßßßßß     ßßßßßßßßßßßß     ßßßßßßßß    º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

Switch 'To' is used for direct report to printer or file.

Options and buttons:

 Statistics    - include statistic information
 Scan info     - include virus scan information
 Check up info - include information about clean objects
 Save Setup    - save the setup settings into the configuration file AVP.INI


 Scan³Dos Shell
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

With the DOS Shell command you can leave the program temporarily to perform
a DOS command or run another program. To return to this program, type EXIT
at the DOS prompt.



 Scan³Exit       (Alt-X)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Exit command (Alt-X) terminates the program AVP.EXE.

The program terminates automatically after scanning if command line
includes the /Q option.

Errorlevels:

 0 - Viruses are absent.
 1 - Scan is not complete.
 3 - Suspicious objects are founded.
 4 - Viruses are detected.
 5 - All detected viruses are cured.
 7 - File AVP.EXE is corrupted.
 10- Internal error AVP.EXE.



 2.3.2. View Commands (Alt-V)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The View menu (Alt-V) contains commands to close, move, and perform other
window-management instructions. Most of the windows in this program support
all standard window elements including scroll bars, close box, and zoom
icons.


 View³Scan Window     (F7)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the Scan Window (F7) to view the output of the main virus scan
information, and any related messages. This window is opened automatically
if any messages are directed into it.


 View³Check Up Window     (Alt-F7)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the Check Up Window (Alt-F7) to view the output of files that have
been virus scanned, and listed as "ok."  This window is automatically
opened if any message are directed into it.


 View³Statistics
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the Statistics window to view statistical information about the
virus scanning process.


 View³Clear Messages
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the Clear Messages (F8) to clear all messages in both the Scan, and
the Check Up windows.


 View³25/50 Lines  (Alt-F9)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the (ALT-F9) to change the video mode from 25/50 lines.


 View³Zoom     (F5)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the Zoom (F5) to re-size the active window to the maximum size. If
the window is already zoomed you can choose this command to restore it to
its previous size.

You can also double-click anywhere on the window's title bar (except where
an icon appears) to zoom or un-zoom the window.


 View³Next      (F6)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the Next (F6) to cycle forwards through the windows of the
desktop.


 View³Close      (Alt-F3)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the Close (Alt-F3) to close the active window. You can also
click the Close box in the upper right corner to close the window.


 View³Resize      (Ctrl-F5)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the Resize (Ctrl-F5) to re-size, and move the active window. Use
Up,Dn,Left,Right keys to move, and Shift-(Up,Dn,Left,Right) to re-size the
window. Press ENTER when done.



 2.3.3. Edit Commands (ALt-E)   (Pro Version)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Menu Edit (Alt-E) is used for editing the antiviral databases.


 Edit³Open Base (F3)     (Pro version)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Open Base command (F3) displays the Open Base dialog box. With this
dialog box you can select the base to edit with the Base Editor.

Keys:

 Up,Dn,PgUp,PgDn - moving through the records
 Ins             - new record
 Del             - delete record
 Ctrl-Ins        - get record into clipboard
 Ctrl-Del        - cut record into clipboard
 Shift-Ins       - paste record from clipboard

Select record and press ENTER. Form Dialog appears, then you can modify
different fields in record. Use TAB to move through fields.


 Edit³Close Base         (Pro version)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Close Base command is used for saving, and the closing the database.


 Edit³Save Base (F2)     (Pro version)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Save Base command (F2) is used for the saving of the database.


 Edit³Save All (Ctrl-F2) (Pro version)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Save All command (Ctrl-F2) is used for saving all the opened bases.


 Edit³Cut  (Shift-Del)   (Pro version)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Cut command (Shift-Del) is used to cut the record into the clipboard.
You can use the Paste command to paste the record from the clipboard.


 Edit³Copy (Ctrl-Ins)    (Pro version)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Copy command (Ctrl-Ins) is used for copying the record into the
clipboard. You can use the Paste command to paste the record from the
clipboard.


 Edit³Paste (Shift-Ins)  (Pro version)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Paste command (Shift-Ins) is used to paste the record from the
clipboard. You can use the Copy command to copy the record into the
clipboard, and Cut command to cut the record into the clipboard.


 Edit³Active Bases (F4)  (Pro version)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Active Bases command (F4) displays the dialog box used to control the
list of the antiviral bases which are active during scanning.


 2.3.4. Tools Commands (Alt-T)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Tools menu (Alt-T) contains the commands to backup, and restore the
disk system areas.


 Tools³Backup system area
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the Backup system area command to make a backup copy of the system
area of the computer's CMOS information, the MBR of the first hard drive,
and the Boot sector of the Active partition.

This copy is stored in the file AVP.SBK of the A: drive (rescue disk).

To restore the system area in case of an infection by an unknown virus
choose the Restore system area command.


 Tools³Restore system area
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Choose the Restore system area command to restore the system area of the
computer's CMOS information, the MBR of the first hard drive, and the Boot
sector of the Active partition from the backup copy in case of infection by
unknown virus.

The reserve copy must be previously stored by the Backup system area
command. This procedure creates the file AVP.SBK on A: drive (rescue disk).



 2.4.   Code Analyzer
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The Code Analyzer (heuristic scanner) scans the code of algorithm branches
of the files, and disk boot sectors for virus-like instructions. This
routine displays several warning messages, if there are instructions such
as, file opening, and/or writing, interrupt hooking, and so on. The
messages of Code Analyzer are in the format

 : virus Type XXXX suspicion ([encrypted],tail)

where

"XXXX" is one of the strings:

Com - this file looks like it's infected by a unknown COM virus;

Exe - this file looks like it's infected by a unknown EXE virus;

ComExe - this file looks like it's infected by a virus which infects the
files of both COM and EXE formats;

ComTSR, ExeTSR, ComExeTSR - this file looks like it's infected by a memory
resident COM, or EXE, or COM and EXE virus;

Boot - this file looks like a file image of boot virus, or like a
boot-virus dropper;

Trojan  - this file looks like a trojan program.

"encrypted" indicates that a suspicious file, and/or sector contains a
decryption routine.

"tail" is the distance in bytes between file length, and the file (program)
entry point.

Of course, this engine theoretically can generate false alarms in some
cases, as well as, any heuristic algorithm, but we have tested this one on
a very large number of files, and it didn't have any one really false
alarm. If you experience false alarms on your computer please send us
samples of these files for us to analyze, or send us the names of the
files, and the corresponding packages to help us create a known false alarm
list.

Second, the Code Analyzer checks a lot of algorithm branches (including
several sub-branches) of code when virus scanning files. As the result, the
virus scanner works about two times slower with the Code Analyzer active.
This routine detects about 80% of our collection of viruses without the
main antiviral database, so we suppose that about 80% of new viruses will
be detected.

Third, the current version of the Code Analyzer does not remove viruses
from files, and it marks possible infections as "suspicious". For removing
new viruses call a technical expert or send us a sample by E-mail for
analysis. We will send back a small antiviral base to cure this virus as
soon it is possible (usually within two days).


 2.5.   Unpacking Engine
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The utilities which compress the body of a executable file are quite
popular. They save a compressed file on a disk with self-uncompressing
code. On execution this code uncompresses (in memory) the body of host
program, and returns control to it.

The executable file infected by a virus can be compressed by different
versions of compression utilities. Ordinary antiviral scanners pass this
file as not being infected because this file does not contain a virus mask
- that mask is compressed, as well as, the body of host file. For complete
scanning it is necessary to uncompress the file before scanning. The
Unpacking Engine module of AVP 2.0 does this for different versions of the
most popular compression utilities such as DIET, PKLITE, LZEXE and EXEPACK.

When virus scanning the Unpacking Engine creates a temporary file, and
writes into it the uncompressed body of the host file. Then the Unpacking
Engine passes this temporary file to the virus scanning engine. If this
file is not infected, the virus scanning engine will delete the temporary
file after the virus scanning. If this file is infected by known virus,
it's possible (in the Cure mode of Scan menu) to remove the virus from the
temporary file (disinfect the file), and replace the original compressed
file with an uncompressed, and disinfected result.

The Unpacking Engine module does the same operations as above for some
versions of the immunization routines used by CPAV, and F-XLOCK immunizers.
This is necessary because the infected, and then immunized file has another
entry point, and it makes the virus detection procedure more difficult. By
using the Unpacking Engine it's possible to scan these types of files for
possible virus infections.

This module also detects some versions of executable file encryptors, such
as CryptCOM. These utilities encrypt executable files, and make it
impossible to detect a virus within them without decryption of the file
first.

The Unpacking Engine module will be updated for new versions of compression
utilities, immunizers, and encryptors in case of need.



 2.6.   Extracting Engine
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The problem "viruses in archives" is one of the most difficult antiviral
problems. The infected file can sleep several years in some old archive,
and quickly spread upon extracting. If you use Pkware's PKZIP (.ZIP) or ARJ
Software's (.ARJ) you can detect viruses within these archives, and protect
yourself from this situation.

When scanning compressed archives the Extracting Engine extracts the files
from the archive by masking them into a temporary file, and then passing it
to the virus scanning engine. This temporary file will be deleted after
virus scanning.

Note: AVP does not disinfect the viruses in archives, but only detects
infected files. AVP cannot scan archives locked with a password.

Of course, if the infected file was encrypted by the CryptCOM utility, then
compressed with DIET or PKLITE, and then stored in ZIP or ARJ file, AVP
will detect it as infected.



 2.7.   Help System
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Context sensitive Help System is available any time, except scanning, by
pressing the F1 key. The Alt-F1 combination brings previous help screen,
the Alt-P and Alt-N combinations bring previous/next topics.

Some of the viruses call the sound or video effects. These effects are
extracted from the virus bodies and included into the effect demonstration
database. It is necessary to press the Alt-D key in the Help windows for
call the demonstration, if this demonstration presents. To exit from
demonstration it is necessary to press the ESC key.

Some of viruses or the families of viruses call several effects. In this
case it is necessary to press the SPACE key to see or hear next
demonstration. Press the SPACE key also for accelerate the moving some of
the demonstration, for example, for demonstration of the falling letters by
"Cascade" viruses.

Attention! Some of the viruses cause not dangerous changes of the system
parameters while executing effects, for example, the timer value, the value
of some ports, etc. This can cause the incorrect executing of the next
effects or conflict with execution of background programs in multitasking
mode. Some of the viruses use direct writing to video memory and can crash
the system managers such as QEMM.

PLEASE leave multitasking environment (MS-Windows, OS/2) and disable system
managers (QEMM) before viewing of demo effects.

The demonstration of some video effects can be executed correct under
certain conditions, for example, on VGA or HERCULES monitor only. The
executing of this demonstration on the wrong type of adapter can cause the
hang-up of the computer. Recommended VGA adapter for executing the video
demonstrations.



 2.8.  Messages
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 Scan Messages
 ÄÄÄÄÄÄÄÄÄÄÄÄÄ

 : ok
No virus is found in this file/sector. This file/sector will not cause a
"warning" or "suspicious" message.

 : virus NAME detected
Virus NAME has been detected in this file/sector. To remove this virus you
should run the scan procedure in CURE mode.

 : virus NAME cured
Virus NAME has been removed from this file/sector or the TSR part of a
memory resident virus has been disinfected in the system memory.

It is not necessary to reboot the computer after CURE with AVP.EXE if
the virus was detected in system memory, but we recommend to reboot
computer anyway, and execute the virus scanner again in this situation.

 : virus NAME deleted
Infected file was deleted.

 : virus NAME cure failed
This file/sector is infected incorrectly by a virus, and the cure procedure
may destroy this file/sector. This message appears if the file/sector is
placed on a write protect disk also. You should replace these files with the
original ones (from a backup) or reinstall the DOS in case of a infected
sector.

 : virus NAME cure skipped
The cure procedure of the file/sector is skipped by user.

 : virus NAME cure cancelled
The cure procedure of the file/sector is cancelled by user.

 : virus NAME warning (tail)
The virus scanner displays this message if file/sector contains a modified or
corrupted body of a known virus or a suspicious set of instructions has
been found in memory. Tail is the distance in bytes between file length,
and file (program) entry point.

 : virus TYPE suspicious (encrypted,tail)
These messages are displayed by the Code Analyzer engine if a virus-like
set of instructions has been found in a file/sector.

 : EXE file but COM extension
 : COM file but EXE extension
The internal file format, and the file name extension are different.

 : pseudobad cluster NUMBER
The normal disk cluster is marked as bad on File Allocation Table.
This situation may be a warning of new boot virus infection.

 : I/O error
This message appears in cases of write protected disk / share violation /
unpacking errors / disinfection of a read-only file if the switch 'Cure read
only' is disabled in the Setup.

 : trace warning at xxxx:xxxx
Interrupt 13h or/and 21h handler(s) contains "virus-like" instructions.
This message may be a first signal of virus infection. In some cases this
message is displayed when the some uninfected programs are present in the
memory, for example the popular utility RELEASE.

If the 'trace warning' displays you should find out the program that caused
this message. It is necessary to analyze the memory map at the address
where the message pointed. Next is to comment out by using the REM
instruction different commands in the AUTOEXEC.BAT, and CONFIG.SYS files
while the message appears.

Attention! Some of the resident viruses stop the tracing. They reset or
hang-up the computer while tracing. It is necessary to be careful because
if the computer hangs up while tracing it can indicate that the memory
resident virus is present in the system memory.

 : Buffers warning: Config.sys:N1, really:N2
This is a message displayed during analysis of the number of system
buffers. You should be careful if the number of system buffers, and the
number of buffers of CONFIG.SYS file are different because the virus can
infect the DOS system areas.

 : packed file. Method XXXX
This message appears on processing of packed or immunized file.

 : archive file. Format XXXX
This message appears on processing of archive file.

 : unknown format
This message appears on processing of files packed or compressed with
unknown format or stored in archive with password.


 Scan Dialog Messages
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 : This virus is not curable, and the infected file must be deleted
 : This sector is not curable, and must be overwritten with a standard one
These messages indicate that a file or sector is infected by a
not-disinfectable virus. You should delete all these files, and replace them
with backup copies or re-install the system on infected disk.

 : Delete all infected files?! Are you sure?
 : Delete all infected sectors and files?! Are you sure?
These messages are displayed when pressing the "Delete all" button in Cure
Request Dialog.

 : Could not open file
Error opening the file while scanning.

 : No memory to init tables. Redundant scan is not available
No free memory to allocate tables.

 : Can't use CRC from floppy drive
CRC tables are placed on floppy drive.

 : Wrong Path
Wrong path string for scanning.

 : Error with swap file
No free space for swap data or no free system handles for file. Check disk
free space or increase FILES= value in CONFIG.SYS file.


 Installation Messages
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 : File AVP.EXE is infected by virus
This message indicates that AVP.EXE executable file is infected.

 : File AVP.EXE is corrupted. Continue of execution can caused a lost of
   data. Continue?
This message warns about modification or corruption of the AVP.EXE file.

 : File NAME not exist
The database file not found.

 : No database in set
No SET file found.

 : The set of virus bases is out of date. You should update your antiviral
   software at least once in three months.
The databases are out of date.

 : Not enough free file handles. Insert line FILES=32 in CONFIG.SYS file.
No free file handles to create swap files.

 : Your system clock is not set to a correct date
The current system date value is wrong.


 Backup and Restore Messages
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 : Insert rescue disk in A:
 : Backup file corrupted. Restore not complete
 : I/O Error. Restore not complete
 : I/O error. Backup not complete


 Database Messages
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 : LINK name: need linked proc
 : Different pages in record
 : Large Offset in record
 : Error file format
 : This base is locked for edit
 : Error version number
 : Corrupted data in record
 : Record too large
 : Unknown record in base
 : Data is already being edited. Close form before deleting
 : Are you sure you want to delete this item?
 : Reload bases?
 : Cannot create file. Data not saved
 : Error opening file
 : Database has been modified. Save?
 : Form data has been modified. Save?
 : Unresolved external
 : Can't link FIXUPP 8X. All functions must be declared as "far"
 : Unknown FIXUPP type
 : Can't link Groups
 : Unknown OBJ record type
 : Large record
 : Effective part of OBJ module must be < 64K


 Other Messages
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 : Error with INI File
 : Out of Memory
 : Low memory to load help system
 : Reload bases for cure?
 : There are no XMS memory detected. To avoid memory problems
   we recommend to install XMS driver
 : Can't open temporary file







 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 3.  Antiviral Database      (Pro version)
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ





The Antiviral Database (DB) is the file which contains the records of the
different types of infections. The main types of records are: MEMORY,
SECTOR, JMP, FILE.

The MEMORY record contains the information for searching, and disinfecting
memory resident viruses. The virus scanner checks the system memory for
memory resident viruses according to the list of MEMORY records, and if a
virus is detected, the scanner deactivates it in memory, and displays a
corresponding message.

The SECTOR record contains information for the searching, and disinfecting
boot viruses. The virus scanner checks, and disinfects boot sectors
according to the list of SECTOR records, and displays a messages if the
virus is found.

The FILE record contains information for the searching, and disinfecting of
file viruses. The virus scanner checks, and disinfects files according to
the list of SECTOR records, and displays a messages if a virus is found.

Records of type JMP are used for the calculation of the file (virus) entry
point. In EXE files the JMP record calculates the start address of the
module. In SYS files the JMP record calculates the STRATEGY & INTERRUPT
subroutines addresses, and in COM files, and boot sectors it analyzes the
code at the beginning of the file/sector.

The record contains fields, and the main types of fields are:

 Name
 Type (internal format of the file, MBR or BOOT sector)
 Area1: Page, offset and length of code to calculate the first checksum
 Area2: Page, offset and length of code to calculate the second checksum
 Pointers to special routines (decryption and disinfection routines)
 Method of disinfection

All digits in all fields of the database records are hexadecimal. JMP, and
MEMORY records contain the limited set of fields listed above.


 Field "Name"
 ÄÄÄÄÄÄÄÄÄÄÄÄ
Each record (excluding JMP ones, in which the Name field is comment only)
begin with the Name field. This field contains the string that is displayed
if the virus scanner detects a corresponding virus. An example of names are:

 Atomic
 Intruder.1331
 Jeru.Sunday.b

You are allowed to use any ASCII digits or characters in the Name excluding
spaces, and special characters: delimiter "." and "the same name"
identifier "#".

The Delimiter "." is used to separate the virus name with subnames, and
copy the part of previous name to current one. If the name begins from
point delimiter, it means that name of current record begins from first
subname of previous record. If the name begins from two point delimiters,
it means that the name begins from first, and second subnames of previous
record.

If the Identifier "#" is at the beginning of the record it forces the virus
scanner to use the name of the previous record. If the string begins with
the "#" identifier the rest of that string is not used. You can fill it
with comments if you like.

Examples:

 Record Name:      Output:
 --------------------------------
 Cascade.1701.a    Cascade.1701.a
 #                 Cascade.1701.a
 ..b               Cascade.1701.b
 .1704.a           Cascade.1704.a
 ..b               Cascade.1704.b
 #Cascade_Virus    Cascade.1704.b
 #Cascade_Memory   Cascade.1704.b


 Field "Type"
 ÄÄÄÄÄÄÄÄÄÄÄÄ
The TYPE field identifies the format of file, and where the virus scanner
searches for that virus (FILE record) or the type of system sector where
the virus scanner searches for a boot virus (SECTOR record).

The allowed types are COM, EXE, SYS, and NEW EXE in the FILE records, BOOT,
and MBR in the SECTOR records.

If the record is marked as COM, and EXE, the scanner will not check
SYS-files for that record, if the record is marked as SYS only, the scanner
will scan SYS-files only for that record.


 Pages
 ÄÄÄÄÄ
When virus scanning the virus scanner puts the code of file or sector into
its internal pages (blocks of memory). There are several available pages:

 HEADER  - 400h bytes, file header code
 PAGE_A  - 400h bytes, entry point code
 PAGE_B  - 400h bytes, "second jump" code
 PAGE_C  - 1000h bytes, for using in special routines
 FILE    - virtual page, is used to reach the data
           that is out of other pages.

When virus scanning the system sectors or DOS executables the HEADER
contains the body of sector it scanned (200h bytes) or 400h bytes of code
from the file beginning. The PAGE_A contains 400h bytes (or rest of the
sector) from the entry point. It there is another JMP command in PAGE_A,
the 400h bytes of code where the "second jump" points, is placed in PAGE_B.

When virus scanning multi-entries files (such as SYS and NEW EXE files) the
virus scanner checks each entry many times, until the number of entries is
found. When scanning the code of entry, it is placed in PAGE_A, and code of
"second jump" is placed in PAGE_B.

If there are NEW EXE files two parts of file are virus scanned the DOS
component, and NEW component. When virus scanning of NEW component the code
of the NEW EXE Header it is copied into the page HEADER, and the other
pages are filled as written above.

      COM file          EXE/SYS file      NEW EXE file
      ÚÄÄÄÄÄÄÄ¿         ÚÄÄÄÄÄÄÄ¿         ÚÄÄÄÄÄÄÄ¿
    ÚÄ³Page   ³  EXE/SYS³Page   ³   EXE   ³       ³
 JMP³ ³HEADER ³   header³HEADER ³   header³       ³
    ³ ³-------³         ³-------³         ³-------³
    ³ ³       ³         ³       ³   NE    ³Page   ³
    ³ ³       ³         ³       ³   header³HEADER ³
    À>³-------³    Entry³-------³         ³-------³
    ÚÄ³PAGE_A ³       ÚÄ³PAGE_A ³         ³       ³
 JMP³ ³       ³    JMP³ ³       ³    Entry³-------³
    ³ ³-------³       ³ ³-------³       ÚÄ³PAGE_A ³
    ³ ³       ³       ³ ³       ³       ³ ³       ³
    À>³-------³       À>³-------³       ³ ³-------³
      ³PAGE_B ³         ³PAGE_B ³       À>³PAGE_B ³
      ³       ³         ³       ³         ³       ³
      ³-------³         ³-------³         ³-------³
      ÀÄÄÄÄÄÄÄÙ         ÀÄÄÄÄÄÄÄÙ         ³       ³
					  ÀÄÄÄÄÄÄÄÙ

The Algorithm for filling of the pages is HEADER, PAGE_A and PAGE_B, and is
defined in the JMP records.

PAGE_C is used by the special (decryption or cure) subroutines and used as
a read/write buffer, and area for decrypted virus code.

 ÚÄÄÄÄÄÄ¿    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿    ÚÄÄÄÄÄÄ¿
 ³PAGE_A³ÄÄÄ>³decryption routine³ÄÄÄ>³PAGE_C³
 ÀÄÄÄÄÄÄÙ    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ    ÀÄÄÄÄÄÄÙ

 file
 ÚÄÄÄÄÄÄÄ¿<ÄÄÄÄ¿
 ³       ³     ³ writing
 ³-------³  ÚÄÄÄÄÄÄ¿
 ³       ³  ³PAGE_C³
 ³       ³  ÀÄÄÄÄÄÄÙ
   . . .       ^
 ³-------³     ³ reading
 ³       ³ÄÄÄÄÄÙ
 ÀÄÄÄÄÄÄÄÙ

The page FILE is a virtual one. It is not a block of memory. Elements of
the page FILE have signed offsets. The null address of page FILE equals the
file entry point address. This page is used during file disinfection to
reach the file code which is out of other pages.

 file
 ÚÄÄÄÄÄÄÄ¿
 ³HEADER ³
 ³-------³
 ³       ³
 ³       ³FILE-0400h
 ³       ³
 ³-------³FILE+0000
 ³PAGE_A ³
 ³-------³FILE+0400h
 ³       ³
 ³       ³FILE+0800h
   . . .
 ³-------³
 ³PAGE_B ³
 ³-------³
 ³       ³
 ÀÄÄÄÄÄÄÄÙ


 Check Sums
 ÄÄÄÄÄÄÄÄÄÄ
To detect a virus the virus scanner uses check sums (control sums) instead
of the conventional signatures. All check sums are double word in length
(32 bits). The algorithm of check sum calculation is one of the standard
CRC algorithms.

The virus scanner calculates check sums for each scanned object, and
compares it with list of check sums that are stored in the database
records.

There are two check sums that are used in the SECTOR, and FILE records:
rough (on code of small length), and final (on code of long length). The
MEMORY record contains only the checksum.

In FILE and SECTOR records it is recommended to use length, and offset of
the code for the first checksum in these limits:

 - the length of code is less or equal to 10h;
 - the offset of the start of code is equal to zero.

In this case the internal cache is used. If it is impossible to select the
code in these limits, you should use another one.

If the length of first check sum is over or equal to 8 and the calculated
(on scanning) sum is equal to that check sum, the virus scanner displays
the warning message:

 virus NAME warning (tail length)

where NAME is string from Name field of corresponding database record.


 Record Processing
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
When virus scanning files or sectors the virus scanner opens the file
(locates the sector), calculates entry point, fills the pages HEADER,
PAGE_A, PAGE_B, and then calculates the first checksum. If that checksum is
equal to first checksum of record a second checksum is calculated. If there
is special decode routine, it is executed before calculation of second
checksum.

If the second checksum is equal to checksum stored in the record, the virus
scanner displays a corresponding message. If it is executed for the cure
process, it processed the disinfection fields. If there is a special
disinfection routine, it is executed before processing of these fields.

When virus scanning the system memory the virus scanner calculates the
checksums of the areas of the system memory at addresses from a limited
list (Memory Record). If that checksum is equal to the checksum of the
record, it disinfects that area of the system memory according to other
record fields.

When calculating the entry point the virus scanner calculates checksums in
the page HEADER, and compares them to the checksums from JMP records. If
sums are equal to the record's ones, it processes corresponding method of
entry point address calculation.


 Creating a New Record
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ-
To attach the information about a new virus into the database it is
necessary to:

 - open a new record (INSERT key),
 - select the type of the record (FILE, SECTOR, JMP, MEMORY, ...)
 - type the name of virus,
 - select the type of objects to check (for FILE and SECTOR records),
 - fill the checksum areas (select pages, offsets and lengths),
 - fill the disinfection fields (or set method of disinfection to FAIL),
 - link the special routines (if it is necessary),
 - calculate the checksum by using the SUM command that automatically
   calculates sums by pointing to an infected file, or type the virus mask
   manually.

If you describe a virus that does not have the code which is useful for
calculating the sums (polymorphic virus), it is necessary to set the length
of the first control sum to zero, and link the object code of the decryptor
by the LINK command of the form. In this case you should calculate the
second control sum in PAGE_C.

See samples of database records in SAMPLES.ZIP file.




 3.1. FILE Record
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 Fields
 ÄÄÄÄÄÄ
 Type           type of the record (COM or/and EXE or/and SYS or/and WIN)
 Name           virus name
 Page_1         page for the control sum 1
 Offset_1       offset for the control sum 1
 Len_1          length for the control sum 1
 Sum_1          control sum 1

 Page_2         page for the control sum 2
 Offset_2       offset for the control sum 2
 Len_2          length for the control sum 2
 Sum_2          control sum 2

 Cure_Method    remove method
 Cure_Page      page for the cure method
 Cure_Data_1    cure data
 Cure_Data_2    cure data
 Cure_Data_3    cure data
 Cure_Data_4    cure data
 Cure_Cut       number of the bytes to cut file

 Commands
 ÄÄÄÄÄÄÄÄ
 Link       attach the object code to the record
 Sum        calculate the control sums


 The Record Processing Algorithm
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The file is dispatched by the JMP records (the calculation of the EP,
EP_Next values, filling the HEADER, PAGE_A, PAGE_B pages) before calling
the virus check loop.

The check loop processes all the file records. For each file record the
first control sum is calculated (in page pointed by Page_1 field from
Offset_1 on Len_1 bytes). This sum is compared with the value from the
field Sum_1. If these values are equal then the second control sum is
calculated (in page pointed by field Page_2 from Offset_2 on Len_2 bytes).
The decode procedure is called before the calculation of second control sum
if that procedure presents in linked module.

If the second control sum is equal to the Sum_2 field then the virus
scanner removes the viruses according to the method pointed in the field
Cure_Method. The Fields Cure_Page, Cure_Data_1, Cure_Data_2, Cure_Data_3,
Cure_Data_4, Cure_Cut are used for removing the virus. The field Cure_Page
is used to point to the page from which the data for cure is getting with
the offsets Cure_Data_x. If Cure_Page=FILE then the data for cure is
getting from the tested file with the offsets EP+Cure_Data_x. The
Cure_Data_x fields is signed.

The standard method is applied after the special cure procedure, if this
procedure is presented in linked module and returned R_PRECURE.


 Cure Methods
 ÄÄÄÄÄÄÄÄÄÄÄÄ

 MOVE and LEHIGH
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
These methods repair the bytes of file beginning. They are used against the
viruses that append themselves to the file end, and alter the file
beginning.

 Repairing:

Cure_Data_2 bytes are copied to file beginning with offset Cure_Data_3 from
the page pointed to in the Cure_Page with offset Cure_Data_1. If the file
name is COMMAND.COM, then fill file with 0 from the Entry_Point minus
Cure_Cut offset to the end of the file, otherwise it sets the file length
to the Entry_Point minus Cure_Cut offset. The Cure_Data_4 field is not
used.


 JERUSALEM
 ÄÄÄÄÄÄÄÄÄ
It is used against the viruses which write themselves into the file
beginning, and shift the file body.

 Repairing:

The file is moved to the beginning on Cure_Data_1 bytes. The file length is
decreased by Cure_Data_1 + Cure_Cut bytes. The Cure_Page, Cure_Data_2,
Cure_Data_3, Cure_Data_4 fields are not used.


 START
 ÄÄÄÄÄ
It is used against viruses which write themselves into the file beginning,
and move the original beginning to the end of the file.

 Repairing:

The file length is decreased by the Cure_Cut bytes, then the part of the
code is moved from the file end to the file beginning. If the file length
is less than Cure_Data_1*2, then it moves the File_Length minus Cure_Data_1
bytes (File_Length after decreasing by Cure_Cut bytes), otherwise is moves
Cure_Data_1 bytes, and the file length is decreased by Cure_Data_1 bytes.
The Cure_Page, Cure_Data_2, Cure_Data_3, Cure_Data_4 fields are not using.


 EXE_CISS, EXE_CISS_10, EXE_CIS, EXE_CIS_10, EXE_CI, EXE_CI_10
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
EXE-file header repair methods.

 EXE_CISS - repair the values of all header register fields (CS,IP,SS,SP)
 EXE_CIS  - repair the values of CS, IP and SS header register fields
 EXE_CI   - repair the values of CS and IP header register fields

EXE_CISS_10, EXE_CIS_10, EXE_CI_10 methods are the same as listed above
with one exception: the CS and SS header register fields are decreased by
10h before restoring.

The values of the header register fields for all the Pages except FILE are:

 CS: word ptr Cure_Page[ Cure_Data_1 ]
 IP: word ptr Cure_Page[ Cure_Data_2 ]
 SS: word ptr Cure_Page[ Cure_Data_3 ]
 SP: word ptr Cure_Page[ Cure_Data_4 ]

Cure_Data_x are unsigned.

The values for the header register fields if Cure_Page=FILE are:

 CS: word ptr File[ EP+Cure_Data_1 ]
 IP: word ptr File[ EP+Cure_Data_2 ]
 SS: word ptr File[ EP+Cure_Data_3 ]
 SP: word ptr File[ EP+Cure_Data_4 ]

Cure_Data_x are signed.

The file length is decreased by EP minus Cure_Cut bytes. The EXE-module
size fields of EXE-header are corrected too.


 SYS_SI and SYS_I
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
SYS-file header repair methods.

 SYS_SI  - repair the value of the Strategy and Interrupt header fields
 SYS_I   - repair the value of the Interrupt header field

The values for the header fields are:

 Strategy   - word ptr Cure_Page[ Cure_Data_1 ]
 Interrupt  - word ptr Cure_Page[ Cure_Data_2 ]


 DELETE
 ÄÄÄÄÄÄ
It deletes the infected file.


 FAIL
 ÄÄÄÄ
This method displays the message "virus NAME cure failed". It is used as a
temporary name for viruses which are "disinfectable", but the current
version of the virus scanner does not disinfect them correctly.


 SPECIAL
 ÄÄÄÄÄÄÄ
For a complex virus that uses encryption or the courage algorithm the
standard methods are not allowed. In this situation you should write a
special procedure to cure the virus, then compile it and, attach the object
code to the record by Link command.


 Example
 ÄÄÄÄÄÄÄ
The COM-file is infecting by the virus "Tiny".

On infection this virus appends to file 4 bytes at the beginning of the
file, then it appends 140 bytes of the virus body, then it modifies the
first four bytes of the file (jmp to the virus body):

 4D             DEC  PB
 E9 xx xx       JMP  NEAR Loc_Virus

It is necessary to register a new JMP record because the code of the virus
jump is not standard:

JMP record:

 Name           Tiny
 Len_1          02
 Sum_1          xxxxxxxx  <<< sum is calculated with Sum command
 Offset_2       00
 Len_2          00
 Sum_2          00
 Jmp_Method     OFFSET
 Jmp_Data       02

Then you should register a new FILE record:

 Type           COM
 Name           Tiny
 Page_1         PAGE_A
 Offset_1       00
 Len_1          08
 Sum_1          xxxxxxxx  <<< sum is calculated with Sum command
 Page_2         PAGE_A
 Offset_2       00
 Len_2          40
 Sum_2          xxxxxxxx  <<< sum is calculated with Sum command
 Cure_Method    MOVE
 Cure_Page      FILE
 Cure_Data_1   -04
 Cure_Data_2    04
 Cure_Data_3    00
 Cure_Data_4    00
 Cure_Cut      -04



 3.2. JMP Record
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 Fields
 ÄÄÄÄÄÄ
 Name           name of the record (information field)
 Len_1          length for the control sum 1
 Sum_1          control sum 1
 Offset_2       offset for the control sum 2
 Len_2          length for the control sum 2
 Sum_2          control sum 2

 Jmp_Method     method of jump
 Jmp_Data       data for jump method


 Commands
 ÄÄÄÄÄÄÄÄ
 Link   attach the object code to the record
 Sum    calculate the control sums


 The Record Processing Algorithm
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The file is dispatched by the JMP records (the calculation of the EP,
EP_Next values, filling the HEADER, PAGE_A, PAGE_B pages) before calling
the virus check loop.

After the file opening the 400h bytes from the file beginning are read into
the pages Header and Page_A. The contents of the other pages are set to
zero.  Next the virus scanner will run the JMP loop for detecting the file
entry point (EP). The first control sum on Len_1 bytes of the page Header
is calculated for each JMP record. This value is compared to the value of
the field Sum_1. If these values are equal then the second control sum in
the page Header from Offset_2 on Len_2 bytes is calculated. If the second
control sum is equal to the value of the Sum_2 field then the value of EP
is calculated according to the method which is pointed by the field
Jmp_Method with data from the field Jmp_Data. The 400h bytes of the code
from the file at the offset EP are read into the page Page_A.

This procedure repeats one time for filling EP_Next and Page_B by using the
page Page_A instead of the page Header.

This procedure is called on calculation of jumps in boot sectors also.


 EP Calculation Methods
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 OFFSET
 ÄÄÄÄÄÄ
It used to dispatch the commands like:

 xxxx:0100  E9 xx xx     JMP  NEAR Loc_Virus
 .... ....

 xxxx:0100  E8 xx xx     CALL NEAR Loc_Virus
 .... ....

or the instruction combinations like:

 xxxx:0100  90           NOP
 xxxx:0101  E9 xx xx     JMP  NEAR Loc_Virus
 .... ....

The EP value is calculated as address of command, where control is passed
to by instruction JMP NEAR or CALL NEAR.

 EP = word ptr Header[Jmp_Data] + Jmp_Data + 2.


 ADDRESS
 ÄÄÄÄÄÄÄ
It used to dispatch the commands of the COM-files like:

 xxxx:0100  68 xx xx     PUSH OFFSET Vir_Loc
 xxxx:0103  C3           RET
 .... ....

 xxxx:0100  B8 xx xx     MOV  AX, OFFSET Vir_Loc
 xxxx:0103  FF D0        CALL AX
 .... ....

The EP value is calculated as the address of command, where control passed
to by the RET/JMP/CALL instruction.

 EP = word ptr Header[Jmp_Data] - 0100h.


 DATA
 ÄÄÄÄ
It used to dispatch commands of the COM-files like:

 xxxx:0100  FF 26 04 01  JMP  WORD PTR [0104]
 xxxx:0104  xx xx        DW   Vir_Offset
 .... ....

 EP = word ptr File [Jmp_Data] - 0x100.


 FAIL
 ÄÄÄÄ
This method displays the message "virus NAME cure failed" and is used as a
temporary name for viruses under analysis.


 SPECIAL
 ÄÄÄÄÄÄÄ
For complex commands the standard methods are not allowed. In that
situation you should write a special procedure to calculate EP, then
compile it, and attach the object code to the record by the Link command.
The dispatch of the EXE-file header, and the short jumps instruction use
SPECIAL methods.

Note: Most jump codes are calculated by the current set of JMP records
which are included in main antiviral database. Please check the virus scanner
for jump calculation before adding a new one.


 Example
 ÄÄÄÄÄÄÄ

The code of the infected file beginning:

 0000 90          NOP
 0001 90          NOP
 0002 E9 xx xx    JMP   Virus

The files filling:

 Name            nop_nop_jmp
 Len_1           0003
 Sum_1           xxxxxxxx  <<< sum is calculated with Sum command
 Offset_2        0000
 Len_2           0003
 Sum_2           xxxxxxxx  <<< sum is calculated with Sum command
 Jmp_Method      OFFSET
 Jmp_Data        0003



 3.3. MEMORY Record
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 Fields
 ÄÄÄÄÄÄ
 Name           virus name
 Method         search method
 Segment        value of the segment Segm (method ADDRESS)
 Offset_1       offset value for search
 Control_Byte   control byte
 Len_1          length for the control sum 1
 Sum_1          control sum 1

 Offset_2       offset of the replace code
 Len_2          length of the replace data ( <5 )
 Replace_Bytes  bytes for replacing


 Commands
 ÄÄÄÄÄÄÄÄ
 Link   attach the object code to the record
 Sum    calculate the control sums


 Record Processing Algorithm
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The virus scanner scans the set of the addresses Segm:Offs according to the
Method field. For each of the addresses it compares the byte of the system
memory at the address Segm:Offs + Offset_1 with the value of the
Contol_Byte field. If these value are equal then it calculates the control
sum at the address Segm:Offs + Offset_1 on the Len_1 bytes. If the control
sum is equal to the Sum field the scanner displays a corresponding message,
and replaces the Len_2 bytes from Segm:Offs+Offset_2 by the sequence of the
bytes from the Replace_Bytes field.


 Search Methods
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 ADDRESS
 ÄÄÄÄÄÄÄ
To search at one fixed address. Segm, and Offs are pointed by the field.
The value of Offs is equal to the zero.


 CUT
 ÄÄÄ
To search in memory that is 'cut' from DOS (as a lot of boot viruses do).
The Segm value is changed from the end of the Z block of DOS memory blocks
until A000h by increasing by the one. The value of Offs is equal to the
zero.


 MCB
 ÄÄÄ
To search in the DOS memory blocks. The Segm value is changed in the
segment addresses of all the MCB blocks. The value of Offs is equal to the
zero. Attention! The Segm value is equals to the address of memory block
body not to the address of the memory CONTROL block (MCB).


 TRACE
 ÄÄÄÄÄ
To trace the interrupts 21h, and 13h. The values of Segm:Offs are changed
in the list of the address with all the over-segment jumps.


 SCAN
 ÄÄÄÄ
The virus scanning of the memory. The Segm value is changed from 0000h
until the segment address of scanner by increasing by one. The value of
Offs is equal to the zero.


 FULL_SCAN
 ÄÄÄÄÄÄÄÄÄ
The virus scanning of the entire memory. The Segm value is changed from
0000h until A000h by increasing by one. The value of Offs is equal to the
zero.


 SPECIAL
 ÄÄÄÄÄÄÄ
The special search, and removing procedure is called if this method is
pointed. You should write a special procedure, compile it, and attach the
object code to the record by the Link command if you point this method.


 Example
 ÄÄÄÄÄÄÄ

The code in infected system memory:

 1234:0123 80 FC 3D    CMP   AH,3Dh
 1234:0126 74 xx       JE    Infect_File
 1234:0128 E9 xx xx    JMP   Continue
 1234:012B . . . .     . . . . .

 The first deactivation method:  TRACE
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The fields filling:

 Method          TRACE
 Segment         0000
 Offset_1        0000
 Control_Byte    80
 Len_1           8
 Sum             xxxxxxxx  <<< sum is calculated by the Sum command
 Offset_2        3
 Len_2           2
 Replace_Bytes   90 90

The code in the memory after curing:

 1234:0123 80 FC 3D     CMP   AH,3Dh
 1234:0126 90           NOP
 1234:0127 90           NOP
 1234:0128 E9 xx xx     JMP   Continue
 1234:012B . . . .      . . . . .


 The second deactivation method:  MCB
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The fields filling:

 Method          MCB
 Segment         0000
 Offset_1        0123
 Control_Byte    80
 Len_1           8
 Sum             xxxxxxxx  <<< sum is calculated by the Sum command
 Offset_2        0126
 Len_2           2
 Replace_Bytes   90 90



 3.4. SECTOR Record
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 Fields
 ÄÄÄÄÄÄ
 Type           type of the record (BOOT and/or MBR)
 Name           virus name
 Offset_1       offset for the control sum 1
 Len_1          length for the control sum 1
 Sum_1          control sum 1

 Page_2         page for the control sum 2
 Offset_2       offset for the control sum 2
 Len_2          length for the control sum 2
 Sum_2          control sum 2

 Cure_Method    remove method
 Cure_Page      page for the cure method

 Cure_Addr_A    cure data
 Cure_Addr_B    cure data
 Cure_Offset    cure data

 Commands
 ÄÄÄÄÄÄÄÄ
 Link   attach the object code to the record
 Sum    calculate the control sums


 Record Processing Algorithm
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
When virus scanning the system sector is read into the page Header (200h
bytes). Next the virus scanner will run the JMP loop for detecting the
entry point (EP) as well as the calculation of file entry point. The bytes
from entry point until the end of sector are moved to Page_A. The contents
of other pages are set to zero before running the detection loop. The first
control sum is calculated in the page Header from Offset_1 on Len_1 bytes.
If the first control sum is equal to the Sum_1 value then the second
control sum is calculated in page which is pointed to by the Page_2 field
from Offset_2 on Len_2 bytes. The decode procedure is called before
calculating the second control sum, if this procedure is presented linked
module. If the second control sum is equal to the Sum_2 field then the
virus scanner removes the virus according to method which is pointed to in
the field Cure_Method. The Cure_Addr_A, Cure_Addr_B, Cure_Offset fields are
used for removing the virus.

The standard method is applied after the special cure procedure, if this
procedure is presented linked module and returned R_PRECURE.

The address of the sector (Boot or MBR) can be pointed to by two methods: the
physical address (head,track&sector - two arguments) or the logical
address (the number of the sector of the logical disk - one argument).
These methods use different interrupts.

 Addressing      Sector address                 Interrupt
 ÄÄÄÄÄÄÄÄÄÄ      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ                 ÄÄÄÄÄÄÄÄÄ
 logical        logical sector - CX             INT 25h/26h
 physical       track and sector - CX           INT 13h
                head  - DH


 Cure Methods
 ÄÄÄÄÄÄÄÄÄÄÄÄ

 ADDRESS
 ÄÄÄÄÄÄÄ
If absolute addressing is used. The original MBR or Boot sector are moved
from the disk sector at the absolute address Cure_Addr_A/Cure_Addr_B
(track&sector/head or CX/DH in the INT 13h format). The fields Cure_Page,
and Cure_Offset are not used.


 ABSOLUTE
 ÄÄÄÄÄÄÄÄ
If absolute addressing is used. The original MBR or Boot sector are moved
from the disk sector at the absolute address CX/DH in the INT 13h format,
where CX and DH values are got from the page Cure_Page:

 CX = word ptr Cure_Page [Cure_Addr_A] + Cure_Offset
 DH = byte ptr Cure_Page [Cure_Addr_B]


 LOGICAL
 ÄÄÄÄÄÄÄ
It is the same as the ABSOLUTE method except for the addressing. The
logical addressing is used:

 CX = word ptr Cure_Page [Cure_Addr_A] + Cure_Offset

The Cure_Addr_B field is not used.


 DELETE
 ÄÄÄÄÄÄ
The standard MBR or Boot sector of MS-DOS 6.0 is placed into the disk
sector.

Note: this method can be dangerous if the disk has been formatted with non
standard utilities.


 FAIL
 ÄÄÄÄ
This method displays the message "virus NAME cure failed". It is used as a
temporary name for viruses which are "disinfectable", but the current
version of scanner does not disinfect them correctly.


 SPECIAL
 ÄÄÄÄÄÄÄ
For complex viruses that use an encryption or a stealth algorithm the
standard methods are not allowed. In this situation you should write a
special procedure to cure the virus, then compile it, and attach the object
code into the record by the Link command.


 Example:
 ÄÄÄÄÄÄÄÄ

The Boot sector has been infected by the "Stoned" virus. That virus saves
the original Boot sector in the absolute sector at the address 3/1
(sector/head).

Fields filling:

 Type          BOOT
 Name          Stoned
 Offset_1      00
 Len_1         08
 Sum_1         xxxxxxxx   <<< sum is calculated with Sum command
 Program_Flag  NO

 Page_2        HEADER
 Offset_2      15
 Len_2         80
 Sum_2         xxxxxxxx   <<< sum is calculated with Sum command

 Cure_Method   ADDRESS
 Cure_Page     FILE

 Cure_Addr_A   03
 Cure_Addr_B   01
 Cure_Offset   00



 3.5. Link of Special Procedures
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

These special procedures are used to expand the capability of the antiviral
database. They attach to the records in the antiviral database, and are
used for the detection, and removal of difficult viruses that use
nonstandard infection methods or self-encryption algorithms. The special
procedures may be written on C, assembler, and other languages that support
the C standard of subroutines calls. Borland C compilers are recommended.

You can attach these special procedures to the records of the antiviral
database after compiling them to the object modules. The attached code
would be read from the database, and linked with the main anti-virus
executable during the loading of the database. When virus scanning the main
program would use these procedures, as well as, its own internal
subroutines.  We recommend the SMALL model for compiling the source modules
if there is no static data, and the HUGE model if the static data is
present. The using of TINY model is impossible.

For example, the compiling FILENAME.C to FILENAME.OBJ can be performed
with Borland C by the command:

 bcc -mh -c -K filename.c


 Standard Names of Special Procedures
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
One or two procedures with standard names (like 'main' in C) must be
present in the linked module. There are three standard names:

 decode() {procedure body} // decryption procedure
 cure()   {procedure body} // removing procedure
 jmp()    {procedure body} // procedure for entry point calculation

The names "decode" and "cure" can be used together or separately in FILE,
and SECTOR records. In TSR records it can be used in the "cure" procedure
only. In JMP records it can be used in the "jmp" procedure only.


 Using of External Procedures, and Data
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The special procedures use external procedures, and data. Before access to
these names it is necessary to describe those names as external. The names
which are defined in the main program can be accessed from any special
procedure. These names are defined in SAMPLES\DLINK.H file. See this file
for more info.

The access to the external names that were defined in other linked modules
are available if the record with the definition is placed BEFORE the record
with the call to the external name.

Correct example:

 Record Cascade.1701: define Decode_Cascade(...) {...}
                      call   Decode_Cascade(...)

 Record Cascade.1704: call   Decode_Cascade(...)


Incorrect example:

 Record Cascade.1701: call   Decode_Cascade(...)

 Record Cascade.1704: define Decode_Cascade(...) {...}
                      call   Decode_Cascade(...)