550RESET.DOC  formatted Wed  10-19-1994  15:11:27

          This program clears the 16550A's FIFO to prevent system hangs
          when "Super I/O" cards with SMC665 or SMC666 chips are used
          with communications programs that enable the 16550A UART. Just
          run this program before you run your favorite communications
          program and you should *not* experience further system hangs.
          NOTE:  If you have an external device connect it and turn it
          on BEFORE you run this program.

          The specific problem is that if you output a 0x7 to the FIFO
          control register of these chips while there is data in the
          FIFO the chip will go into a state where the Receive Ready
          flag (bit 0 in the LSR) remains high NO MATTER HOW MANY TIMES
          YOU READ THE RECEIVER BUFFER REGISTER.  If your communication
          program is unfortunate enough to enable interrupts while the
          UART is in this condition your system will lockup, and require
          a hardware reset or power cycle to restore operation.
          Needless to say this is inconvenient!

          I discovered this problem when I upgraded my "SUPER I/O card"
          to a "SIDE jr L" vlb card.  While the features are great I
          immediately ran into problem with EVERY program I have that
          uses serial I/O.  I found that I could only execute Windows
          programs that used serial I/O once, the whole system locked up
          the second time I ran the program.  This occurred with several
          different Windows programs.  Searching the Microsoft Knowledge
          base yielded the answer... an updated SERIAL.386 driver
          (search for WG1001 for the new driver).  Unfortunately the new
          Windows driver did nothing for DOS programs I use regularly
          such as Qmodem and Telix, that is why I wrote this program.
          The Microsoft writeup provided enough information on the
          problem for this program to be written.

                    Comments are welcome:

                     Skip Hansen WB6YMH.
                    internet: wb6ymh@amsat.org
                     BBS: (310) 541-2503
                    Packet: WB6YMH@WB6YMH.#SOCAL.CA.USA

          If you find this program of value I am pleased, send no cash!