TeleShare  DOS  REMOTE ACCESS       Page 1




     UPDATED: December, 1994

                   _______
              ____|__     |               (R)
           --|       |    |-------------------
             |   ____|__  |  Association of
             |  |       |_|  Shareware
             |__|   o   |    Professionals
           -----|   |   |---------------------
                |___|___|    Member




     TeleShare SETUP the TsSETUP.EXE program


     The TeleShare/SETUP program is called TsSETUP.EXE.  To execute
     the  program  just  change  to  the  sub-directory  where  you
     deposited the TeleShare programs and enter 'TsSETUP'.  You can
     type it in all lower or all uppercase;  it  appears  in  mixed
     case here to emphasize the SETUP portion of the name.

     You  will  see  a  simple menu screen with some catagories, as
     follows:

     General Defaults   Security   Remote   Transfer   Modem Sharing

     The center of the screen displays various settings as you move
     from  catagory  to  catagory  using  the  arrow  keys   and/or
     PGUP/PGDN.   Use  the  sideways  arrow keys or PGUP or PGDN to
     change catagories.  Use the up/down arrow keys  to  move  from
     field to  field  within  each catagory.  Every selection has a
     matching context sensitive help area  at  the  bottom  of  the
     screen.

     Save your  changes  using  the  ESCape  key.  You will need to
     verify saving by pressing 'Y' when asked if you wish to  'SAVE
     TO DISK?'.

     All settings are written to a binary configuration file called
     TSCONFIG.CFG.   This  file  is  used  by  both HOST and REMOTE
     programs.

     The TsSETUP program is identical for  both  HOST  and  REMOTE.
     Some settings only apply to one or the other but most apply to






              TeleShare  DOS  REMOTE ACCESS       Page 2


     both.

     If  the TSCONFIG.CFG file ever becomes corrupted or you simply
     want  to  reset  to  the  defaults  then   just   delete   the
     TSCONFIG.CFG file  and  run TsSETUP.EXE.  You will be asked if
     you want to create a new TSCONFIG.CFG file.  Answer 'Y'es  and
     a new one will be created with the default settings.

     If  you  run  TsSETUP  while  either the TSH.exe or TSR.exe is
     running then you will also be asked on exit  if  you  want  to
     'Update the  TSR running on this PC?'.  This will send some of
     the new defaults directly to the program so you don't need  to
     load/unload.

     NOTE:    The   only   settings  which  will  not  take  effect
     immediately if you elect to update  the  running  program  are
     those that deal with the COM port ( baud rate, etc ) and those
     that deal  with  security  ( password, etc. ).  These settings
     cannot be changed on the fly.  You  have  to  UNLOAD  the  TSR
     currently running with 'TSH U' or 'TSR U' and then reload with
     'TSHOST'  or  'TSREM'  batch  files  to  be sure all parameter
     changes are now in effect.

     This option was  intended  to  make  it  easy  to  turn  'send
     attributes?' ON/OFF  without  unloading  the  TSR.    Critical
     settings can only be updated by re-loading the TSR.

     A list of ALL settings in TsSETUP follows along with  a  brief
     description of each.


     TsSETUP.EXE CATEGORY 1 - GENERAL DEFAULTS

     - Software interrupt(Decimal):

     Enter the  DECIMAL  value  of  the  software interrupt.  Valid
     entries are interrupts 60 <thru> 67.  The  default  should  be
     fine on  most  PC's.    Change it only if you have a good idea
     what you are doing.

     - Communications port # (1,2):

     Enter the number of the COMMUNICATIONS PORT to use.   Enter  1
     for COM1 or 2 for COM2.

     - Baud   rate........(2400-115200):     Enter  the  baud  rate
     (2400-115200).







              TeleShare  DOS  REMOTE ACCESS       Page 3


     - Send video attributes?.....:

     Press <Y>es to include attributes in update msgs.  Press  <N>o
     to exchange  only  TEXT characters.  TEXT ONLY provides faster
     screen updates.  You may enter any realistic baud rate.

     TeleShare will not transmit GRAPHICS screens!

     - Use alternate video buffer?:

     Press <Y>es to use a non-standard video buffer  address  Press
     <N>o to use normal DOS video buffer address(es)

     NOTE:   If  active  then the HOST will SEND from the specified
     alternate buffer.  Normally do not try to  use  this  feature,
     unless you develop a need and know what you are doing.

     This  could  allow  the  program  to  be  used as a poor man's
     network with certain task switching programs or DOS kernels if
     you find out where the screens are stored in memory.


     - Address of alternate buffer:

     Enter the decimal value of the video buffer  segment  address.
     This  would be something other than B000 or B800 which are the
     standard PC video buffer addresses for Monochrome  and  colour
     respectively.  Remember to enter the decimal value.


     TsSETUP.EXE CATEGORY 2 - SECURITY OPTIONS

     If  you  use  the security option then set it ON for both HOST
     and REMOTE, or you will 'lock yourself out'.    You  won't  be
     able  to  get  in  if  it's  set on one and not the other end.
     Also, the password is case sensitive:    any  capital  letters
     must  be  entered the same way every time you use the password
     on both the host and the remote.


     Use security?  :

     Press <Y>es to use SECURITY or <N>o for NONE.

     Password:

     Enter the system access password.







              TeleShare  DOS  REMOTE ACCESS       Page 4


     The password exchange takes place  each  time  you  press  the
     remote  access  hotkey  sequence to request a session with the
     HOST.

     This prevents anyone from 'sneaking on' due to LOST CARRIER as
     you can with some other remote access programs.



     TsSETUP.EXE CATEGORY 3 - REMOTE OPTIONS

     - Polling pause :

     Enter the number of timer ticks to  wait  before  polling  the
     HOST program  for a session update.  A timer tick is 1/18 of 1
     second, so 18 ticks equals 1 second.  The minimum is 3 ticks.

     The REMOTE program uses a scheme to request video updates from
     the HOST computer being accessed.  The value specified here is
     the number of timer ticks to wait between attempts to poll  or
     ask for an update.

     Never  set  the  polling pause to anything faster than about 3
     timer ticks or the HOST may become so busy sending you  screen
     updates that it won't be able to process the last command in a
     timely way.

     This  poll  pause  is  intended  to  allow slower systems some
     breathing room.   A  fast  HOST  PC  can  handle  short  pause
     values.  As can PC's using a direct serial connection.

     A  value  of  9 timer ticks should provide good performance on
     all types of PC's.

     You may also adjust this value to whatever you need to  access
     systems where interrupt activity is higher than normal.


     - Popup key ALT-

     Press  the  key  to  use  with  ALT  to  enter the REMOTE HOST
     session.  Your choices are  limited  to  the  capital  letters
     A-Z.   This  allows you to customize the hotkey to you choice,
     and to avoid hotkey conflicts with other software.


     - Exitkey ALT-







              TeleShare  DOS  REMOTE ACCESS       Page 5


     Press the key to use with ALT  to  return  to  the  LOCAL  DOS
     session.   Your  choices  are  limited  to capital letters A-Z
     only.  Customize the hotkey to fit what you want and need.


     - Mode indicator:

     The MODE indicator is the small highlighted block  which  will
     appear  in  the  upper right corner of the monitor to indicate
     LOCAL or REMOTE mode.  Press <Y>es  to  show  it  or  <N>o  to
     exclude it.


     TsSETUP CATEGORY 4 - TRANSFER OPTIONS


     - Transfer display box ROW:

     Enter  the  ROW  (1-9)  to  use for the top left corner of the
     transfer display window.


     - Wait for filename RCVD OK:

     When sending files the filename is sent to the receiver before
     transfer starts.  Enter the number  of  seconds  to  wait  for
     acknowledgement of the filename.


     - Retry filename on SEND:

     When sending files the filename is sent to the receiver before
     transfer starts.    Enter  the  number of times to re-send the
     filename before giving up.


     - Wait for filename on RECV:

     When receiving files the filename must arrive before  transfer
     can begin.    Enter  the  number  of  seconds  to wait for the
     filename before giving up.  The minimum is 10 seconds.


     - Wait for SOH between files:

     When receiving files with the XMODEM protocol we must  receive
     the SOH  character  before  a  transfer  can begin.  Enter the
     number of seconds to wait before giving up.  The minimum is  1






              TeleShare  DOS  REMOTE ACCESS       Page 6


     second.


     - Fixed loop timeout on XCHNG:

     Transfer routines  use  fixed counters for timeouts.  Increase
     this value if you get transfer errors.  the minimum  is  1000,
     and the maximum is 500000.  A 386PC should be at least 20000.


     - Log all sends to XMSEND.LOG:

     Press  'Y'  to log all send transactions to a special LOG file
     called XMSEND.LOG.


     - Log all RECVS to XMRECV.LOG:

     Press 'Y' to log all RECEIVE transactions  to  a  special  LOG
     file called XMRECV.LOG.

     Use  the  Log  file  options when you need to keep a record of
     your activities.  Example  uses  are  support,  security,  and
     financial monitoring for each session.


     - Default PATH for log files.:

     Enter the  default  pathname to use for log files.  This tells
     the system where to put the log files, and where you  will  be
     able to find them later.

     Please  read the TELE.DOC file for more information, including
     contact and support information.


     Support and the ASP


     For technical support, either call (604) 433-5189, or write to
     Suite 606 - 6455 Willingdon Avenue, Burnaby, British Columbia,
     Canada, V5H 4E4.  Both registered and soon  to  be  registered
     users  currently  get  the  same support without any arbitrary
     time limit.  You may also try leaving a Compuserve message  at
     75020, 2664.     Your  message  has  better  chance  of  avoid
     Compuserve 'scroll off' if you send it to:

     INTERNET:vic_williams@mindlink.bc.ca






              TeleShare  DOS  REMOTE ACCESS       Page 7


     ASP Introduction:

     Please  also  carefully  read  the  accompanying  SHR_WARE.DOC
     document.

     "This  program  is  produced by a member of the Association of
     Shareware Professionals (ASP). ASP wants to make sure that the
     shareware principle works  for  you.  If  you  are  unable  to
     resolve  a  shareware-related  problem  with  an ASP member by
     contacting the member directly, ASP may be able to  help.  The
     ASP  Ombudsman  can help you resolve a dispute or problem with
     an ASP member, but does  not  provide  technical  support  for
     members'  products.  Please  write to the ASP Ombudsman at 545
     Grover Road, Muskegon, MI 49442 or send a  CompuServe  message
     via CompuServe Mail to ASP Ombudsman 70007,3536."


     This  document and associated TeleShare documents and software
     are Copyright (C)1992-4 P. C. Softsmith All Rights Reserved.

     THE DOCUMENTATION AND ASSOCIATED SOFTWARE ARE DISTRIBUTED  AND
     SOLD  WITH NO WARRANTIES, EITHER EXPRESS OR IMPLIED, REGARDING
     ITS MERCHANTABILITY OR FITNESS  FOR  ANY  PARTICULAR  PURPOSE.
     THE  INFORMATION  IN  THIS  DOCUMENTATION IS SUBJECT TO CHANGE
     WITHOUT NOTICE AND DOES NOT REPRESENT  A  COMMITTMENT  ON  THE
     PART OF THE VENDOR.

     OTHER  PRODUCT  AND  BRAND  NAMES  MENTIONED ARE TRADEMARKS OR
     REGISTERED TRADEMARKS OF THEIR RESPECTIVE HOLDERS,  or  so  we
     presume.