ÜÜÜÜÜ                        ÜÜÜÜÜ
  ÞÛÛÛÛÛÛÛÛÝ   ÜÜÜÜÜ           ÞÛÛÛÛÛÛÛÛÝ
 ÞÛÛÛÛ ÞÛÛÛÛÞÛÛÛÛÛÛÛÛÝ ÜÜÜÜÜÜÜÞÛÛÛÛ  ÛÛÛÛ ÜÜÜÜÜ
 ÞÛÛÛÝ ÞÛÛÛÞÛÛÛÛ  ÛÛÛÛÞÛÛÛÛÛÛÛÞÛÛÛÝ      ÛÛÛÛÛÛÛÝ
ÞÛÛÛÛÛÛÛÛÛÛÞÛÛÛÝ      ÛÛÛÛ    ÞÛÛÛÛ     ÛÛÛ   ÛÛÛ   ÜÜÜÜÜÜ      ÜÜÜÜÜ
ÞÛÛÛÝ ÞÛÛÛÞÛÛÛÛÛ     ÛÛÛÛÛÛÛÞÛÛÛÛÛ     ÛÛÛ     ÛÛÛÞÛÛÛÛÛÛÛÛÛ ÞÛÛÛÛÛÛÛÛÛ
ÛÛÛÛ ÞÛÛÛÛÞÛÛÛÝ  ÛÛÛÞÛÛÛ     ÞÛÛÛÝ  ÛÛÛÞÛÛÝ   ÛÛÛÞÛÛÛ ÛÛÛ ÞÛÝÛÛÛ ÛÛÛ ÞÛÝ
ÛÛÛÝ ÞÛÛÛÝ ÛÛÛÛÛÛÛÛÛÞÛÛÛÛÛÛÝ  ÛÛÛÛÛÛÛÛ  ÛÛÛÛÛÛÛÛ ÞÛÛ ÞÛÛ ÛÛÛÞÛÛÝÞÛÛ ÞÛÛ
 ßß   ßßß   ßßßßß    ßßßßßß    ßßßßß      ßßßß   ßß      ßß  ßß      ßßß



AceComm (tm)

Macro Language




Copyright 1991-1994 by MGP Software, all rights reserved.

All rights reserved.  No part of this publication may be reproduced, stored in
a retrieval system, or transmitted by any means, electronic, mechanical,
photocopying, recording, or otherwise, without express written permission from
MGP Software.  The software described in this publication is furnished under a
license agreement and may be used or copied only in accordance with the terms
of that agreement.

This publication and its associated software are sold without warranties,
either expressed or implied, regarding their merchantability or fitness for any
particular application or purpose.  The information in this publication is
subject to change without notice and does not represent a commitment on the
part of MGP Software.  In no event shall MGP Software be liable for any loss of
profit or any other commercial damage, including but not limited to special,
incidental, consequential, or other damages resulting from the use of or the
inability to use this product, even if MGP Software has been notified of the
possibility of such damages.


First Printing, July 1994

AceComm version 1.90











All brand and product names mentioned in this publication are trademarks or
registered trademarks of their respective holders.





AceComm Software Support



You can get more help by contacting the
author Michael Phelps at the following

- VOICE 602-846-4563 6 days 12-7pm MST

- BBS   602-846-2940 24 hours

- COMPUSERVE User ID 75120,3306

- FIDONET ADDRESS 1:114/35

- FIDONET COMM echo

- FIDONET ACECOMM echo
I distribute the "ACECOMM" echo to
USA NODES, until it makes BACKBONE.

- Write to: MGP Software (AceComm)                 *New Address*
            BOX 301 C  Route 3                      Yes we are moving
            Detroit Lakes, MN 56501 USA             later this year.









                T a b l e   o f   C o n t e n t s


Chapter 1  AceComm Macro Language..............................1
Chapter 2  Macros list.........................................3
              Local User Input (LUI) Functions.................4
              Character I/O Functions..........................9
              Flags...........................................20
              File Functions..................................21
              Data Transfer functions.........................24
              Dialing/Fon.Record..............................27
              Misc Functions..................................30
Chapter 3  MACRO Parameter Symbols............................33
              PRM-data Representatives........................34
              Replaceable Macro Functions.....................40
Chapter 4  Scripts............................................41
              AutoScriptGen (Tm)..............................42
              Labels, Gotos, Data Area........................47
              Mini Host Script Example........................49
Chapter 5  LICENSE............................................56
Chapter 6  Contacting the author..............................59



Chapter 1  AceComm Macro Language




Almost all of AceComm's internal functions are represented with a macro
programming language.  The AceComm keyboard is completely re-programmable using
the macro language.  In fact, the AceComm keyboard is macro driven.

Many of AceComm's menus are also macro driven, and can be re-programmed.
Some of the menus are user definable, where the title and menu items can be
defined by the user.


Reference to characters such as carriage return, space, escape, etc.  are made
in this document.  Reference to a character is made in the following manner.
<CR> <SP> where <CR> refers to a carriage return, and <SP> refers to a space
character.  Macros are bounded by the same <> brackets as character reference.
Character references are not macros.  A complete macro listing follows this
chapter.



What is a Macro?
----------------

o Macros are directives bounded inside of angle brackets < >

o Macros must have a SPACE character in front of the '<' left bracket when
    stacking.

 <ChgDir>[DIR_MAIL] <RunProg>OFFLINE <ChgDir>[DIR_START]
                   |                 |
                   |_________________|
                   |
                   Leading space

o Macros may be any combination of CaSe

 <RunProg> jmodem
 <runprog> jmodem


o The Macro Processor supports "Macro Stacking".  Macro Stacking means multiple
  Macros per line

 <SendStr>u z ACE0601.ARJ^M <SendZmo>files\ace0601.arj

 <SendStr>u z ACE0601.ARJ^M <RunProg>DSZ sz -m files\ace0601.arj

 <SetDTR> ON <SendStr>ATDT846-2940^M <WaitStr>CONNECT <SendStr>^[^[


o MACRO DATA PARAMETERS are bounded inside of square brackets [ ]

o MACRO DATA PARAMETERS need not have a <SP> character in front of them

o MACRO DATA PARAMETERS must be upper CASE

 <SendStr>[USER_NAME]^MY^M[FON_PWD]
          |          |    |
          |          |    Data Param (Fon.Record password field)
          |          |


       Page 1              AceComm (tm) v 1.90



          |          ^M translates into a <CR> (carriage return)
          |
          Data Param (IEMSI user name field)

 <SendStr>[USER_NAME]^M~[PASSWORD]^M
 |        |          | |  |
 |        |          | |  IEMSI password field
 |        |          | |
 |        |          | One second delay (~ = second delay)
 MACRO    |          |
          |          Control character representation for <CR>
          |
          MACRO DATA PARAMETER (IEMSI data)


o MACRO FUNCTION PARAMETERS are prefixed with a % character

 <SendZmo> %PF
  |        |
  |        MACRO FUNCTION PARAMETER (prompt for filename)
  |
  Internal Zmodem sending unit

 <RunProg>dsz port %P speed %B sz %PF %WK <SendStr>^M
                      |        |     |   |
                      |        |     |   |
                      |        |     |   MACRO FUNCTION PARAM
                      |        |     |   (wait for key press)
                      |        |     |
                      |        |     MACRO FUNCTION PARAM
                      |        |     (prompt for filename)
                      |        |
                      |        MACRO FUNCTION PARAM
                      |        (insert ascii baud)
                      |
                      MACRO FUNCTION PARAM
                      (insert ascii port)



Please submit all macro suggestions to:
a)  MSG to Michael Phelps on the AceComm Support BBS
b)  MSG to Michael Phelps on Compuserve UID 75120,3306



















       Page 2              Chapter 1  AceComm Macro Language


Chapter 2  Macros list
































































       Page 3              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Local User Input (LUI) Functions
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



LUI MACROS require local user input, and so are not suited to un-attended
scripts.  LUI MACROS contain a '_' underscore as the last character inside the
brackets.

<AutoAMenu_>

   Bring up a quick "Point Mail" / "Auto Answer" service menu. This for those
   using the scheduler and automated host modes.


<AutoScrGen_>

   Toggle AutoScrGen(tm) mode

   Toggle AutoScript Generation mode On/Off.  When "On" an extended status line
   will appear at the bottom of the TERMINAL screen.  At the far left of the
   extended status line will be the phrase "AutoScriptGen"


<ScrollBack_>

   Menu Area
   Enter Back Buffer Screen Area

   The "Scroll Back Buffer" contains the last n lines of display that scrolled
   off the TERMINAL screen.  <ScrollBack_> has a status line of it's own.  The
   status line contains such information as current line position into the
   buffer, total lines buffered, and some of the navigational keys are
   displayed.


<CaptureFile_>

   Toggle Capture File
   Prompts for filename

   Capture will also prompt for append or overwrite.  Capture does absolutely
   NO filtering of any kind.  All data is recorded to file "as it comes in the
   port".  The AceComm package comes with separate utilities which can strip
   video control codes from files.

   See also <OpenCapture> filename
            <CloseCapture>


<DOSShell_>

   Enter Shell to Command Processor/ Operating System

   In most cases "Drop to DOS", if your DOS compatible operating system places
   it's name in the environment where AceComm can find it.  "Shell" is not hard
   wired to COMMAND.COM but the COMMAND PROCESSOR as found in the environmental
   data area.



       Page 4              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Local User Input (LUI) Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   Notes: When SWAP is "ON", the serial port is effectively disabled during the
          shell.  When SWAP is "OFF" the serial port remains active and any
          incoming data is handled properly, unless the receive buffer wraps
          around.


<FileReq_>
   Menu driven EMSI file request function.


<PhoneList_>

   Menu Area
   Enter .FON List / Dialer

   Dial/.FON directory area.  While AceComm allows manual dialing from inside
   the TERMINAL area, it most convenient to dial from a record contained in one
   of the .FON files available for use from the DIAL area.


<FileList_>

   Menu Area
   Enter File Lister

   Files lister inside AceComm provides a basic directory list function capable
   of changing directories and drives.  File-marking, deletion, selection for
   appropriate file-utility, etc.  LISTFILES may be created.  UPLDS.LST is a
   file created by the Tag feature inside the File Lister Area.  files tagged
   will be listed inside UPLDS.LST as CR LF terminated strings.  When selecting
   any of AceComm's internal batch capable sending protocols, AceComm will
   check for the existent of the file UPLDS.LST and allow sending from the
   LISTFILE if desired.


<MdmHangUp_>

   Prompts Yes/no before,
   Sends PRM-data MDM_HANGUP string to modem.  Waits 1/2 second, then drops DTR
   for 1 second.

See also    <MdmHangUp> (no Yes/no prompt, good in scripts)


<PrmData_>

   Menu Area
   Enter PRM-data Menu Area (Configuration Area)

   Notes: When AutoSave is "ON", all data changed is automatically saved when
          exiting the PRM-data area.


<RProtocols_>

   Menu Area


       Page 5              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Local User Input (LUI) Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   Enter Receiver Protocols Area menu


<RunScript_>

   List .SCR directory, Allow selection, Run selected .SCR file

   Lists the PRM-data .SCR directory Allows selection of a .SCR file for
   immediate execution.

   Notes: AceComm allows .SCR file as an argument when started which
          immediately executes the script.


<ScrnDump_>

   Menu Area
   Take Screen Snapshot

   Create a "SnapShot" of the current screen minus any status lines active.
   Prompts for a filename.  Filenames always will have the .SNA extension.
   AceComm can detect and will strip away filename extensions provided by the
   user when they do not match that of the function.  This command is available
   from most ALT POP UP REFERENCE areas.


<ScrnTag_>

   Menu Area
   Enter Screen Tagger Screen Area

   Tagger will allow tagging to the first SPACE_CHAR or press RIGHT-ARROW
   Tagger tags the entire line of text.  Tagger has it's own status line, and a
   block cursor will appear inside of the Tagger mode.  Tagged items will be
   assigned to the next available SHIFT-Fn key.

   Tagger pops up the SHIFT-Fn key window and displays each tagged item, as
   they are tagged.  Tagger is most handy for grabbing filenames for download
   off a BBS screen.  SHIFT-Fn key fires the tagged item back when ready.  This
   command is available from most ALT POP UP REFERENCE areas.


<SProtocols_>

   Menu Area
   Enter Sender Protocols Area


<KeyRef_>

   Bring up Pop up Reference The key press assigned this macro is always
   displayed on the right side of the status line.


<TopBar>



       Page 6              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Local User Input (LUI) Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   Activate the menu bar at top of screen

   The key press assigned this macro is always displayed on the right side of
   the status line.
   "Top Bar" menu can also be brought up inside the terminal area by double
   clicking the left mouse button.

The following macros can be used to call individual menus otherwise choices
from the TopBar single line menu


<FileMenu>

   The TopBar File menu


<HelpMenu>

   The TopBar Help menu

   The key press assigned this macro is always displayed on the right side of
   the status line.


<Users>

   The TopBar Users menu

   This is a menu that lists and allows menu selection for the User menus.
   (User1 - User5)


<PhoneMenu>

   Calls the <FonListDialer_> macro


<SetupMenu>

   Calls the <PrmDataMenus_> macro


<XfrMenu>

   The TopBar Transfer menu

<User>n

The following individual User menus can be brought up by themselves.
Otherwise they are selectable from inside the <Users> menu.
The macro takes a parameter 1 - 5

<User>1

   This macro brings up User menu # 1.
...


       Page 7              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Local User Input (LUI) Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


<User>5

   This macro brings up User menu # 5.






















































       Page 8              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³ Many macros are3 way toggles. Where no parameter toggles.   ³
  ³                                                             ³
  ³       <AutoAnswer>ON     ; Enable                           ³
  ³       <AutoAnswer>OFF    ; Disable                          ³
  ³       <AutoAnswer>       ; Toggle                           ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


--------------------
I/O Function Toggles
--------------------

<AutoAnswer>

   <AutoAnswer>ON     ; Enable
   <AutoAnswer>OFF    ; Disable
   <AutoAnswer>       ; Toggle

   PRM-data MDM_HOST_INIT is sent to the modem when hostmode flag is toggle
   "ON".  PRM-data MDM_INIT is sent to the modem when hostmode flag is toggled
   "OFF".  AceComm begins responding to the RI bit SET, and will send the
   MDM_ANSWER string to the modem when RI BIT becomes asserted.  Upon
   Answer/Connect, AceComm attempts to match the modem response to strings
   defined in the Auto Answer Setup menu.  The appropriate macro stack will
   then be run.  AceComm stores the actual connect speed for use with the %C
   macro parameter.  %B represents the port rate, %C represents the connect
   speed as reported by the modem.

   If you are using <AutoAnswer> alone, without any host script or host
   software, then be sure and also use <HostEcho>ON.  If you want to act as a
   host with characters being bounced back to the caller.

   Notes: Auto Answer is also terminated whenever the user dials out from the
          FON LIST MENU AREA.  If automated auto answer is being used by way of
          the scheduler, then auto answer mode will be re-entered as soon as
          AceComm detects carrier drop.

   See also   Auto Answer Setup menu


<DoorWayMode>

   <DoorWayMode>ON     ; Enable
   <DoorWayMode>OFF    ; Disable
   <DoorWayMode>       ; Toggle

   Toggle doorway mode.  Traps the key press on entry, whatever key press you
   assign <DoorWayMode> to, is the only way back out.  Doorway sends all key
   presses to the modem in their RAW 'un-cooked' form.  Non extended key
   presses are send LOW BYTE ONLY.  Extended key presses are sent LOW BYTE,
   HIGH BYTE.

   Notes: Pressing CONTROL BREAK will always end AceComm.  CONTROL BREAK is a


       Page 9              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         back door to the <EndAceComm> macro.  When you exit the program by
         pressing CONTROL BREAK, all data is saved as usual, and program
         cleanup is as it would be using the <EndAceComm> macro.


<HostEcho>

   <HostEcho>ON     ; Enable
   <HostEcho>OFF    ; Disable
   <HostEcho>       ; Toggle

   Toggle Host echo mode.  This macro emulates HostMode's ECHO capability.  It
   does not answer the phone. Use <AutoAnswer>On to have AceComm answer.

   Host echo means that characters typed locally will be displayed both local
   and sent to the modem.

   Host echo will also translate <CR> into <CR><LF> pairs and <BS> into
   <BS><SP><BS>.


<LocalEcho>

   <LocalEcho>ON     ; Enable
   <LocalEcho>OFF    ; Disable
   <LocalEcho>       ; Toggle

   Toggle local character echo.  Local key-presses will be echoed to the
   screen.  (same effect as sending "ATE1^M" to the modem)
   If you use <LocalEcho> be sure your modem is set up with echo off.
   To turn the modem echo off   ATE0


-------------------------------------
I/O Flags Toggles internal to AceComm
-------------------------------------

<BitStrip>

   <BitStrip> on
   <BitStrip> off
   <BitStrip>

   AceComm going to strip high bit from ascii characters (above 127d)


<CTS>

   <CTS> on
   <CTS> off
   <CTS>

   AceComm uses CTS/RTS hardware handshaking.


<XON>


       Page 10              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


   <XON> on
   <XON> off
   <XON>

   AceComm uses XON/XOFF software handshaking

----------
I/O Modem
----------


<GetDCD>

   Returns 0 or 1 current carrier detect signal
:DIAL
   ...
   <GetDCD>
   <if>1 <goto>CONNECT
         <goto>DIAL
   ...
:CONNECT


<MdmHangUp>

   Sends PRM-data MDM_HANGUP string to modem.  Waits 1/2 second, then drops DTR
   for 1 second.


<MdmStill>

   <MdmStill>n

   Wait for n seconds where nothing arrives from the modem.

   <SendStr>d^M ACE185.ZIP^M
   <RecvZmo>
   <MdmStill>5 <SendStr>G^M Y^M <Delay>2 <MdmHangUp>


<SetDTR>

   <SetDTR> on
   <SetDTR> off

   Assert or Reset UART Bit for data terminal ready


<SetLCtrl>STRING

   <SetLCtrl>8N1
   <SetLCtrl>7E1
   <SetLCtrl>7N1




       Page 11              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

<SetBaud>STRING

   <SetBaud>300
   <SetBaud>1200
   <SetBaud>2400
   <SetBaud>4800
   <SetBaud>9600
   <SetBaud>19200
   <SetBaud>38400
   <SetBaud>57600
   <SetBaud>115200


-----------------------
I/O Mostly Scripts Uses
-----------------------

The sample MINIHOST.SCR included with the AceComm package demonstrates most of
the macros in this manual. Remember that macros ending in _> require local
keyboard input, so are not suited to un-attended scripts.
          Example:
                  <MdmHangUp_>  will prompt the user (Yes/no)
             where
                  <MdmHangUp>  hangs up with no (Yes/no) prompt




<CheckMdm>STRING

   This macro checks to see if STRING has come in from the modem.
   The macro does not wait, but sets the result for a following <if>
   to 1 or 0.
   Result to <if> is 1 or 0

--- Example ---
;
; Clear screen,  Send ansi video request,  Display banner
;
   <Timer0>3                        ; Init Timer0 and set 3 second timeout
   <RawCapture>On                   ; Allow all caller's input in wait buffer
                                    ; ESC[6n  is video request (detect ansi)
   <SendStr>^L^[[6n^MMini Host Script for AceComm v1.85^M
;
; Loop here for 3 second maximum waiting for answer to Ansi detect sequence
;
:@@DetectAnsi
   <CheckMdm> [ <if>1 <goto>@@AnsiDetected     ; Remote will answer with
   <Timer0> <if>1 <goto>@@DetectAnsi           ; ESC[n;nR  if ANSI capable
   <RawCapture>Off
   <HostEcho>ON                                ; HostEcho translates CR
                                               ; into CR,LF pair
   <DispStr>^MAnsi video request un-answered^M ; Ansi video request
   <goto>@@Welcome
:@@AnsiDetected
   <RawCapture>Off


       Page 12              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   <HostEcho>ON                     ; HostEcho translated CR into CR,LF pair
   <SendStr> ^MAnsi video detected!^M

--- End Example ---


<DirList> PATH\*.*

   List a directory, can be used from host mode.

   <DirList>[DIR_DNLDS]\*.*
   <DirList>C:\files\*.ZIP

<DispStr>TEXT


   <DispStr>^M[BWhi][Blu]Hello to you![AttrOff]^M^J


<DispText> LABEL_NAME

   Display text defined in a data area of a script file LABEL_NAME is
   descriptive text following {-TEXT_START-} Text is displayed at current
   cursor position Text display is local

--- Example ---

:@@Top
   <ClrWin>
   <DispText>Intro
   <DispText>Ask_Continue
:GetKey
   <GetKey>60
      <if>Y <goto>Dial
      <if>N <goto>End
      <goto>GetKey
:Dial
   <INITFONREC>ACECOMM Support BBS      ; Initialize a FON RECORD
   <FON_NUM>1-602-846-2940            ;
   <FON_BAUD>19200                    ;
   <FON_TERM>Av/An                    ;
   <FON_REDIAL>                       ; Go into re dial mode
   <DispText>Connect
   <WAITSTR> your name:
   <GetDCD>                           ; <WaitStr> may have timed
   <if>1 <goto>Connect                ; out
   <goto>@@Top
:Connect
   <SENDSTR>Michael Phelps^M
   <SENDSTR>Y^M
   <SENDSTR>password^M
   <WAITSTR>Select:
   <SENDSTR>ff
:End
   <ENDS>



       Page 13              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

{-DATA_AREA-}
{-TEXT_START-}Intro
-- Generic Log On Script --
{-TEXT_END-}
{-TEXT_START-}Ask_Continue
Continue (Y/n) {-TEXT_END-}

{-TEXT_START-}Connect
-- Connect --
{-TEXT_END-}

--- End Example ---


<EndS>

   Marks the exit point for the script processor.


<FindUser>

   Searches a file names USERLIST.LST for user names.
   Result to <if> is 1 or 0

   Sample USERLIST.LST file contents:

Michael Phelps,password,9
Guest Pass,guest,1

The user name must be First Last,password,level
Level is not currently supported, but must be there. The commas are important.


--- Example ---
   <DispStr> ^MEnter your first and last name:
   <GetStr>26 <FindUser> <if>1 <goto>@@GetPwd
   <DispStr> ^MEnter your first and last name:
   <GetStr>26 <FindUser> <if>1 <goto>@@GetPwd
   <DispStr> ^MEnter your first and last name:
   <GetStr>26 <FindUser> <if>1 <goto>@@GetPwd
:@@1
   <DispStr>^L^MYour name has not been registered in the user file, you may
   <DispStr>^Moptionaly leave a short not for the SysOp, pleas include your
   <DispStr>^Mfirst and last name along with a password.
   <DispStr>^M^MWould you like to leave a note? (Y)es/(N)o
   <GetKey>
   <if>Y <goto>@@LogOffComment
   <if>N <goto>@@OFF
   <Goto>@@1
--- End Example ---


<GetKey>n

   <GetKey>60
   The macro excepts a parameter. Seconds to wait for a key press. The


       Page 14              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   parameter range if 1 second - (60 * 7) seconds

   :@@Top
         <DispText>Main_Menu
   :@@GetKey
        <GetKey>10
                  <If>L <goto>@@List
                  <If>M <Goto>@@Main
                  <If>^M <Goto>@@Top
        <GetDCD> <If>0 <goto>@@UseDroppedCarrier
        <Goto>@@GetKey

   When a key press is checked with the <if> macro, it is first made upper
   case. Control characters can be trapped by representing it as ^[character].

   To see if the user pressed the ENTER key   <if>^M
                                    ESC key   <if>^[

   <if> will also check for extended key presses that might be made locally.
   This needs <LocalKeys>ON.
   <If>ALT+J <Goto>@@JumpToDOS
   <If>CTRL+J <Goto>@@JumpToDOS
   <If>F11 <Goto>@@JumpToDOS
   <If>SF11 <Goto>@@JumpToDOS
   <If>CF11 <Goto>@@JumpToDOS
   <If>AF11 <Goto>@@JumpToDOS


<GetMsg>

   This macro will create a message.  It needs host echo on.  The macro inputs
   for From:, To:, Subject: fields.  When called after <FindUser> the From:
   field is initialized with the user's name.  The macro write a message header
   to the beginning of the message file.  The message text is taken from the
   screen after the user saves the message with CONTROL Z.  Message filenames
   are created as 1.MSG, 2.MSG, 3.MSG etc.  The macro is designed for a small
   number of messages.  It will create the first filename that does not exist.

   See <ReadMsg>  and  <YourMsg> macros.


<GetStr>n

   <GetStr>36
   Parameter n is the maximum characters to allow entered. Range is 1 - 128.
   The macro is used for the <FindUser>, <UserPwd>, and %FN.
   %FN maximum length is 80 characters.
   %FN always represents the string entered with <GetStr>.

       <DispStr> ^M^JEnter your first and last name:
       <GetStr>26 <FindUser> <if>1 <goto>@@GetPwd
       <DispStr>^M^J^G%FN not found in user list!
       <Goto>@@DumpCaller
   :@@GetPwd




       Page 15              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

<GoTo>

   Can be used alone or after an <If> macro.
   Parameter to <GoTo> is a label. Labels begin with a :.
   Labels need to be unique character strings.

   <GoTo>@@Done

   <GetDCD> <if>1 <Goto>@@Carrier
                  <Goto>@@OffLine

   <CheckMdm>password: <if>1 <Goto>@@SendPwd


<If>
   Can only be used after macros that produce a result.


      <GetDCD>   <if>1 <Goto>@@DCD
      <CheckMdm> <If>0 <Goto>@@WaitStr
      <Timer0>   <If>1 <Goto>@@WaitStr
      <Timer1>   <If>0 <Goto>@@Timeout
      <FindUser> <If>0 <Goto>@@DumpCaller
      <UserPwd>  <If>0 <Goto>@@LetCallerLeaveMsg
      <GetKey>   <If>^M <Goto>@@UserEnter

<LocalKeys>

<LocalKeys> on
<LocalKeys> off
<LocalKeys>

   3 way macro
   Enable/disable local LUI key press during script (host mode)


<NCWaitStr> STRING

   Non CaSe sensitive version of <WaitStr>

   Waits for a string (sequence of characters) to come in the
   from the modem.  Can Timeout. If <WaitStr> times out, it falls through.

   Timeout seconds is set with <WaitTime>n

          <WaitStr> name:
                   |
                   leading <SP> character is part of search


<ReadMsg>

   This macro displays the messages found. A key press is prompted between
   each message.


<SendStr> STRING


       Page 16              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


   Sends a string to the modem.

       <SendStr>^M

       Send a single CR_CHAR


       <SendStr> Michael Phelps^M

       Notes: the leading space character is part of STRING


      <SendStr>[USER_NAME]^M~Y^M~[FON_PWD]

       Send IEMSI data user name field, a <CR> char, 1 second pause, Y, <CR>
       char, 1 second pause, current Fon.Record.Password.


      <SendStr>[USER_NAME]^M^M[PASSWORD]^M

       Send IEMSI data user name field, 2 <CR> chars, IEMSI data password
       field.


<Timer0>
<Timer1>

   Two separate timers
   A parameter to the <Timer0> macro sets the timeout time in seconds
   Result to <if> is 1 or 0

   <Timer0>30  Sets a timeout of 30 seconds for Timer 0

   <Timer0>    Sets the result for an <if> to 1 or 0.   0 if the timer has
               expired,
   <Timer1> works the same way.


<UserPwd>

   This macro can only be called immediately after the <FindUser> macro.
   This macro will verify the password. Success or failure is determined with
   the immediate call to <if> macro. (see below)
   Result to <if> is 1 or 0

--- Example ---
   <DispStr> ^MEnter password:
   <GetStr>26 <UserPwd> <if>1 <goto>@@MainMenu
   <DispStr> ^MEnter password:
   <GetStr>26 <UserPwd> <if>1 <goto>@@MainMenu
   <DispStr> ^MEnter password:
   <GetStr>26 <UserPwd> <if>0 <goto>@@OFF
                              <goto>@@MainMenu
--- End Example ---



       Page 17              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


<Var0>
<Var1>

   Variables that can store a result.

--- Example ---
;
; Clear screen,  Send ansi video request,  Display banner
;
   <Var0>0                          ; See if we can set this to 1 with
                                    ; our ansi video detection scheme.
   <Timer0>3                        ; Init Timer0 and set 3 second timeout
   <RawCapture>On                   ; Allow all caller's input in wait buffer
                                    ; ESC[6n  is video request (detect ansi)
   <SendStr>^L^[[6n^MMini Host Script for AceComm v1.85^M
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
;
; Loop here for 3 second maximum waiting for answer to Ansi detect sequence
;
:@@DetectAnsi
   <CheckMdm> [ <if>1 <goto>@@AnsiDetected     ; Remote will answer with
   <Timer0> <if>1 <goto>@@DetectAnsi           ; ESC[n;nR  if ANSI capable
   <RawCapture>Off
   <HostEcho>ON                                ; HostEcho translates CR
                                               ; into CR,LF pair
   <DispStr>^M^JAnsi video request un-answered ; Ansi video request
   <goto>@@Welcome
:@@AnsiDetected
   <Var0>1
   <RawCapture>Off
   <HostEcho>ON                     ; HostEcho translated CR into CR,LF pair
   <SendStr> ^M^JAnsi video detected!

:@@Welcome
   ;
   ; %C is the connect speed
   ;
   <Var0> <if>1 <DispStr>^M^J[Whi]Connected at [Blink][Bold][Red]%C[AttrOff]
   <Var0> <if>0 <DispStr>^M^JConnected at  %C

--- End Example ---


<WaitStr> STRING

   Waits for a CASE sensitive string (sequence of characters) to come in the
   from the modem.  Can Timeout. If <WaitStr> times out, it falls through.

   Timeout seconds is set with <WaitTime>n

          <WaitStr> name:
                   |
                   leading <SP> character is part of search




       Page 18              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Character I/O Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

<WaitTime> n

   Where n is in seconds Set the timeout value for <WaitStr> (default is 40
   seconds)

      <Timer0>10
      <WaitTime>15
      <WaitStr>name?
      <Timer0> <if>0 <goto>@@Timeout
      <SendStr>[USER_NAME]^M
   :@@TimeOut


<YourMsg>

   This macro is the same as <ReadMsg>, except that the To: field in the
   message header must match the caller's name.
   You can use this macro to display personal messages to the callers.
   Messages must be created with <GetMsg>.







































       Page 19              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Flags
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



------------------------
Internal Protocols Flags
------------------------

<AutoD> on/off

   Enable/disable auto engage sequence scanning for protocols

   Does not affect auto log on


<Resume> on/off

   Enable/disable file resume (internal zmodem receive)


<Rename> on/off

   Enable/disable file rename (internal zmodem receive)


-------------
General Flags
-------------

<SwapSpawn> on/off

   3 way toggle
   Enable/disable swap to EMS/XMS/DISK for <RunProg> macro


<SwapShell> on/off

   3 way toggle
   Enable/disable swap to EMS/XMS/DISK for <CommandShell_> macro


<DTRExit> on/off

   3 way toggle
   DTR state for <EndAceComm> macro


<Scheds> on/off

   <Scheds>ON     ; Enable
   <Scheds>OFF    ; Disable
   <Scheds>       ; Toggle

   3 way toggle
   This macro will simply turn the schedules on or off.





       Page 20              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   File Functions
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ




<ChgDir> FILENAME

   Make FILENAME current directory
   This macro can change drives

   <ChgDir>C:\WORK\TXT <ToPrn>melissa.01 <ChgDir>[DIR_START]

   <ChgDir>[FIR_DNLDS] <RunProg>DSZ port %P speed %B rz -mr <ChgDir>[DIR_START]

   Notes: [DIR_START] is the directory Acecomm is started in.
          [DIR_DNLDS] is the directory pointed to inside PRM-data
          "Directories" menu for "Downloads".


<CloseCapture>

   Close the current open capture file, or just returns if none is open.

   Capture files are stamped with date/time when closed.

   Capture files are automatically closed on detection of a loss in carrier.

   Capture files are automatically closed when the <OpenCapture> macro is
   called, so that any previous open capture file is sure to be closed before
   opening the new one.


<FileDel> FILENAME

   If the file exists, it will be deleted without prompt.  Use full path name
   if not in current directory.



<LogFile> text

   Adds "text" to ACE.LOG


<OpenCapture> FILENAME

   Calling this function opens a capture file in the directory path defined
   inside PRM-data Area "Directories" menu, .CAP files.

   Existing capture files of same FILENAME are appended to.  DOS eof character
   may end up just ahead of the time stamp.

   This function will first close any previously opened capture file, properly
   saving it to disk.

   Capture files are stamped with date/time when opened.

   Capture files can record either in "Raw" or "Text" mode. "Raw" mode being


       Page 21              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   File Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   where no video control characters are filtered. "Text" being everything
   that the current video emulation does not pick out.

   See also <RawCapture> macro


<RawCapture>on/off

   <RawCapture>on
   <RawCapture>off
   <RawCapture>

   3 way toggle
   <rawCapture>ON <OpenCapture>xmas.ans

   Captured data will be stored with or without video control characters.  The
   current video emulation must mach that of the host.

   AN/AV covers both Ansi and Avatar video at the same time ans is the AceComm
   default video type.


<RunScript> FILENAME

   Open and run FILENAME

   Notes: Just FILENAME no PATH.  PATH found in PRM-data for SCR directory is
          used.
          Note the difference between <RunScript> and <RunScript_>, where
          the later does filename prompting.


<RunProg> FILENAME

   Spawn an executable file.

   Can search the DOS PATH.

   Can determine files's extension (.COM, .EXE).

   All system ISRS are restored before the spawn takes place.  The serial port
   is un-hooked.  The state of DCD, and LINE CONTROL are left in tact.

   After the spawn the system ISRs AceComm uses are taken back, the serial port
   is re-assumed.

   SWAP FLAG "ON" and XMS,EMS, or DISK swapping takes place.  SWAP FLAG "OFF"
   and AceComm is left in memory, with exception to first restoring the serial
   port and interrupts.


<SetFonFile> FILENAME

   Tacks FILENAME onto the PATH defined in PRM DATA for .FON files.  AceComm
   keeps track of the current(last accessed) .FON file.  FILENAME becomes the
   current .FON file.  <SetFonFile> 1_114.fon <DialRecord> 1


       Page 22              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   File Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



<ToPrn> FILENAME

   Send FILENAME to the printer.

   Notes: This macro opens the filename PRN using DOS file handle function, and
          writes the file.  Any character translation DOS may do will depend
          upon the IOCTL functions of DOS.  (eof etc.)

















































       Page 23              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Data Transfer functions
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ




Internal receiver protocols will receive to the sub directory for Downloads as
setup inside the PRM-data "Directories" menu.


<SendAscii> FILENAME

   Outputs from a file to the modem.  Sends the complete file.  Does *NO*
   CONTROL CHARACTER TRANSLATION.  Data sent to the modem is paced for buffer
   FULL, and all handshaking is valid.

   ESC-key press aborts the function.


<SendZmo@> @FILENAME

   Where @FILENAME is a LISTFILE
   The @ denotes a LISTFILE
   Filenames contained in the listfile should be full drive path filenames,
   if not all contained in the current working directory.

   Call internal zmodem sending unit with 1k data frame size.
   ESC-key press aborts the function.


<SendZmo> FILENAME

   Call internal zmodem sending unit with 1k data frame size.
   ESC-key press aborts the function.


<SendYmo> FILENAME

   Call internal ymodem sending unit with 128 byte data frame size.
   ESC-key press aborts the function.


<SendYmo1k> FILENAME

   Call internal ymodem sending unit with 1k data frame size.
   ESC-key press aborts the function.


<SendYmoG> FILENAME

   Call internal ymodemG sending unit with 1k data frame size.
   ESC-key press aborts the function.


<SendXmo> FILENAME

   Call internal xmodem sending unit with 128 byte data frame size.
   ESC-key press aborts the function.



       Page 24              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Data Transfer functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


<SendXmo1k> FILENAME

   Call internal xmodem sending unit with 1k data frame size.
   ESC-key press aborts the function.


<RecvAscii> FILENAME

   Ascii receiver will close the file when End Of File "eof" character is
   seen.  Eof character is set from inside "Protocol Options" menu.  The
   default eof character is the DOS standard 26d.
   ESC-key press aborts the function.


<RecvZmo>

   Call internal zmodem recv unit.  AceComm's internal zmodem receiver is
   capable of up to 8k data frame size.  The receive unit will continue in
   batch mode until the sender stops sending files, or the user terminates the
   transfer.  Files are placed into the directory pointed to in the PRM-data
   area for Downloads.
   ESC-key press aborts the function.


<RecvYmo>

   Call internal ymodem.  The receive unit will continue in batch mode until
   the sender stops sending files, or the user terminates the transfer.  Files
   are placed into the directory pointed to in the PRM-data area for Downloads.
   ESC-key press aborts the function.


<RecvYmo1K>

   Call internal ymodem1K.  The receive unit will continue in batch mode until
   the sender stops sending files, or the user terminates the transfer.  Files
   are placed into the directory pointed to in the PRM-data area for Downloads.
   ESC-key press aborts the function.


<RecvYmoG>

   Call internal ymodemG.  The receive unit will continue in batch mode until
   the sender stops sending files, or the user terminates the transfer.  Files
   are placed into the directory pointed to in the PRM-data area for Downloads.
   ESC-key press aborts the function.


<RecvXmo> FILENAME

   Call internal xmodem.  Files are placed into the directory pointed to in the
   PRM-data area for Downloads.
   ESC-key press aborts the function.




       Page 25              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Data Transfer functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

<RecvXmo1K> FILENAME

   Call internal xmodem1k.  Files are placed into the directory pointed to in
   the PRM-data area for Downloads.
   ESC-key press aborts the function.


<SendEMSI_CLI>

   Send an EMSI_CLI HDR sequence to modem

   BBS mailer front ends that use EMSI handshake protocol will, if EMSI is
   implemented properly, interpret an "EMSI_CLI" HDR sequence, as "this is a
   human caller" and drop to the BBS without any delay.  Note: At this writing
   Front Door, and Binkley recognize EMSI_CLI HDR.  DBridge does not.  See
   default AutoD trigger assignments (ACE.CTL)


<SendEMSI_ICI>

   IEMSI support macro
   Send an EMSI_ICI data packet to modem

   EMSI_ICI is a response made by the caller (CLIENT) to a BBS system (HOST)
   which supports Interactive EMSI handshake protocol.  IEMSI data is contained
   inside the PRM-data area.  This data can be used for automating log on when
   call a BBS that supports IEMSI.  See default AutoD trigger assignments
   (ACE.CTL)




Notes: Xmodem/Ymodem Receive units are capable of adopting to frame size.
       128 / 1024 data frames are determined by the sender and can be sent in
       any combination.

       The Internal Zmodem in AceComm is capable of up to 8k data frames.  For
       compatibility, AceComm only uses larger than 1k data frames with it's
       sending unit in mailer modes.  AceComm's zmodem receive unit can handle
       up to 8k data frames at any time.
       The internal zmodem can make filename management decisions based on the
       status of option flags for "resume" and "rename".
















       Page 26              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Dialing/Fon.Record
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ




<DialNum> PHONE_NUMBER

   Builds a dial string.  Uses PRM-data MDM_DIAL_PREFIX and PHONE_NUMBER Sends
   the dial string to the modem.  One time.  No re dials as this will typically
   take place from terminal area.


<DialRecord> n

   Retrieves the n record found in current .FON file

   Re dials number until CONNECT or USER ABORT

       <SetFonFile> 1_114.FON <DialRecord> 1



-----------------------------------------
For creating a Fon.Record inside a script
-----------------------------------------

<InitFonRec> RECORD NAME

   This MACRO must be called first.  The MACRO initializes a FON RECORD with
   AceComm defaults.  RECORD NAME is copied into the system name for this
   record.

      <InitFonRec> Compuserve


<Fon_Num> PHONE_NUMBER

   Set the phone number field.  Any dial statements in ACE.CFG will be applied
   to this number when AceComm builds the dial string.

      <Fon_Num>468-0285


<Fon_Baud>BAUD

   If using a locked port, AceComm will ignore this value when getting ready to
   dial.

      <Fon_Baud>19200


<Fon_LineCtrl> DATA_PARITY_STOPBIT

   Valid parameters are as follows
         8n1
         7e1
         7n1



       Page 27              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Dialing/Fon.Record (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      <Fon_LineCtrl>8n1


<Fon_Flags> FLAG, FLAG

   Possible Control Flags

   "Script" when set,

   AceComm will attempt to load and run the filename defined next to "AutoLogOn
   Script".  If a script file is not found, AceComm ignores the error and
   continues normal operation.

   Notes: .SCR files are looked for in the directory defined inside PRM-data
           Area "Directories"


   "Macro"  when  set,

   AceComm will enable the defined Auto Log on Sequence Triggers and
   corresponding MACRO stacks.


   "DTag"  when  set,

   AceComm will tag un-successful dial attempts (busy, etc.) to the Que
   Dialer.  An "*" character appears to the left of a Fon.Record's display
   line, when it is either Q tagged or, D tagged.  When this flag is not set,
   the only other way to Q tag a record is by manually selecting the menu
   option "<SPACEBAR>-Que" from the fon list display.


   "Capture" when  set,

   When this flag is selected, a capture file is opened upon
   Dial/Connect.  Any previously open capture file is first
   closed.


   "Raw"  when set,

   Data to capture file is as it comes in from the modem


   "Text"  when set,

   Data to capture file is filtered of video control codes
   as applicable to the current Video type


   "IEMSI"  when  set,

   Allow Interactive EMSI log on

  "AutoL"



       Page 28              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Dialing/Fon.Record (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

  Allow auto log on methods (script/macro)


<Fon_Term> VIDEO_TYPE

      - Valid parameters are as follows

        TTY
        Ansi
        Avatar
        Av/An
        VT102

      <Fon_Term>Av/An


<Fon_CapFile> FILENAME


<Fon_Redial>

   Presents the FON record to the AceComm re dial function.

<Redials>n

   Where n is the number of redials before giving up.  This macro works only
   when dialing from a script using the <FON_ReDial> macro.  <ReDials> does
   not affect normal interactive use, and is not the same as the menu option
   found inside the "Point Mail" "Options" menu.





























       Page 29              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Misc Functions
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ




<Alarm> SECONDS

   Sound alarm for SECONDS


<BbsEndAceComm>

   This macro will Exit AceComm with an error level based on the current baud
   setting.  Baud is taken from the UART, and if the port is locked, will vary
   from the connect speed.

   Error level is decimal of the first 2 ascii decimal digits of the current
   UART baud setting.

   DTR state is left as is.

   Error levels returned are:
                             57 - 57600
                             38 - 38400
                             19 - 19200
                             96 -  9600
                             48 -  4800
                             24 -  2400
                             12 -  1200
                             30 -   300
   Sample use:
:Start
   echo off
   ace
   if error level 96 goto error96
   if error level 57 goto error57
   if error level 48 goto error48
   if error level 38 goto error38
   if error level 24 goto error24
   if error level 19 goto error19
   goto start
:error57
   BBS.EXE 57600
   goto Start
:error38
   BBS.EXE 38400
   goto Start
:error19
   BBS.EXE 19200
   goto Start
:error96
   BBS.EXE 9600
   goto Start
:error48
   BBS.EXE 4800
   goto Start
:error24
   BBS.EXE 2400


       Page 30              Chapter 2  Macros list



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Misc Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   goto Start
:error12
   BBS.EXE 1200
   goto Start
:End


<ClrWin>

   Clear screen. Clears screen above status line


<Delay> SECONDS

   Create program function delay.

   <SendStr>Go IBMCOM^M <OpenCapture>ibmcom <Delay>7 <SendStr>Read New^M
   <Delay> allows I/O, you could trip your <CheckMdm> with this one.


<EndAceComm> ERROR LEVEL

   <EndAceComm> 0
   AceComm session end with error level

   Exit AceComm back to the operating system.  End AceComm session.  A QUICK
   snap, no prompt "Are you sure?".  If your on line, your still on line when
   you come back unless "drop DTR on exit is SET"

   See Drop DTR on EXIT flag inside Terminal Area Options

   Notes: Pressing CONTROL BREAK will always end AceComm.  CONTROL BREAK is a
         back door to the <EndAceComm> macro.  When you exit the program by
         pressing CONTROL BREAK, all data is saved as usual, and program
         cleanup is as it would be using the <EndAceComm> macro.


<PollHost>1-5

   This macros take Host data and builds a FLO file.  The macro then creates a
   Fon.Record with the BOSS info and goes into mailer mode.  If the connect is
   un-successful or aborted, the FLO file still exits in the MAIL OUT
   directory.  Any schedule that allows mail will see the FLO file and cause
   the system to be polled again.
   Long distance calls need the "LD," schedule flag,


<RingBell> SECONDS

   A value of 0 does not ring bell, a value of 1 plays a victory tune, values
   from 2 - 30 ring the internal bell for the number of seconds.  This is the
   same bell sound heard in the Dial/Connect window.


<Wait_To_HHMM> hh:mm



       Page 31              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Misc Functions (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   Wait until hour:minute 24 hour format leading zeros not needed

           <Wait_To_HHMM>4:10    is valid

--- Example ---
    <Wait_To_HHMM>15:45                ; wait till 3:45 pm
    <INITFONREC>A.C.E. Software Support; call Init FON function
    <FON_NUM>1-602-846-2940            ; set phone number
    <FON_BAUD>2400
    <FON_TERM>Av/An                    ; video type for script
    <FON_REDIAL>                       ; call redial function
    <WAITSTR>it a few moments.
    <SENDSTR>^M
    <WAITSTR>s your name:
    <SENDSTR>Michael Phelps^M
    <WAITSTR>ael Phelps [Y,n]?
    <SENDSTR>^M
    <WAITSTR>Password:
    <SENDSTR>melissa_jean^M
    <WAITSTR>Select:
    <SENDSTR>f^M
    <SENDSTR>d^Mz^Mace170.arj^M
    <RecvZmo>
    <WAITSTR>Select:
    <SENDSTR>gyn^M
    <ENDS>
--- End Example ---































       Page 32              Chapter 2  Macros list


Chapter 3  MACRO Parameter Symbols
































































       Page 33              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   PRM-data Representatives
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



o MACRO parameters are UPPER case only

[MODA]
   Replaced with mmdd (month day)  0704 (July 4)
   Good for frequently used filesnames. Assigning a Fon.Record capture filename
   to something like CIS[MODA]  would result in a unique filename for each
   differant day you log onto Compuserve.

   Another example:  <OpenCapture>CIS[MODA]

-----------
Fon.Records
-----------

[FON_PWD]

   Replaced with the current Fon.Record "password"


[FON_ALIAS]

   Replaced with the current Fon.Record "alias"


[FON_ID]

   Replaced with the current Fon.Record "ID"


[FON_CAP]

   Replaced with the current Fon.Record CAPTURE "filename"


[FON_SCR]

   Replaced with the current Fon.Record SCRIPT "filename"




--------------
PRM-data IEMSI
--------------

[USER_NAME]

   Replaced with the current PRM-data/IEMSI "User Name"

      <SendStr> [USER_NAME]


[ALIAS]



       Page 34              Chapter 3  MACRO Parameter Symbols



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   PRM-data Representatives (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   Replaced with the current PRM-data/IEMSI "alias"


[LOCATION]

   Replaced with the current PRM-data/IEMSI "location"


[DATA_PNUM]

   Replaced with the current PRM-data/IEMSI "data #"


[VOICE_PNUM]

   Replaced with the current PRM-data/IEMSI "voice #"


[PASSWORD]

   Replaced with the current PRM-data/IEMSI "password"


The following are data from PRM-data DIRECTORY section




--------------------
PRM-data Directories
--------------------

[DIR_START]

   Replaced with the current PRM-data/DIR "start up"
   This is the directory AceComm is started in.


[DIR_FON]

   Replaced with the current PRM-data/DIR ".FON"


[DIR_CAP]

   Replaced with the current PRM-data/DIR ".CAP"


[DIR_SCR]

   Replaced with the current PRM-data/DIR ".SCR"


[DIR_KTS]

   Replaced with the current PRM-data/DIR ".KTS"


       Page 35              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   PRM-data Representatives (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



[DIR_DNLDS]

   Replaced with the current PRM-data/DIR "dnlds"
   <ChgDir> [DIR_DNLDS] <RunProgram>DSZ rz -mr <ChgDir> [DIR_START]


[DIR_NODELIST]

   Replaced with the current PRM-data/DIR "nodelist"


[DIR_MAILIN]

   Replaced with the current PRM-data/DIR "mail_in"


[DIR_MAILOUT]

   Replaced with the current PRM-data/DIR "mail_out"



--------------
PRM-data Modem
--------------

[MDM_INIT]

   Replaced with the current PRM-data/MDM "init"
   <SendStr>[HANGUP]^M~[MDM_INIT]^M


[DIAL_PREFIX]

   Replaced with the current PRM-data/MDM "dial prefix"


[DIAL_SUFFIX]

   Replaced with the current PRM-data/MDM "dial suffix"


[ANSWER]

   Replaced with the current PRM-data/MDM "answer"


[HANGUP]

   Replaced with the current PRM-data/MDM "hangup"


[OFFHOOK]



       Page 36              Chapter 3  MACRO Parameter Symbols



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   PRM-data Representatives (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   Replaced with the current PRM-data/MDM "off hook"


[ABORT]

   Replaced with the current PRM-data/MDM "abort"


[RESET]

   Replaced with the current PRM-data/MDM "reset"


[ECHO]

   Replaced with the current PRM-data/MDM "echo"


[HOST_INIT]

   Replaced with the current PRM-data/MDM "host init"


[CMD_LINE_TERMINATOR]

   Replaced   with   the   current   PRM-data/MDM  "command  line
   terminator"


------------------------
Ansi Video Control Modes
------------------------

[AttrOff]

   All attributes Off, reset to gray


[Bold]

   Bold color attribute


[Faint]

   Faint color attribute


[Italic]

   Italics text on


[Blink]

   Blinking attribute on


       Page 37              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   PRM-data Representatives (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



[RBlink]

   Rapid blinking attribute on


[Rev]

   Reverse video attribute on


[Con]

   Concealed attribute

-------------------------
Ansi Video Control Colors
-------------------------

The following foreground colors become intense with [Bold], and normal with
[Faint].

Replaceable macro          Foreground Color
-----------------          ----------------

[Bla]                      Black
[Red]                      Red
[Gre]                      Green
[Yel]                      Yellow
[Blu]                      Blue
[Mag]                      Magenta
[Cya]                      Cyan
[Whi]                      White


Replaceable macro          Background Color
-----------------          ----------------

[BBla]                     Black
[BRed]                     Red
[BGre]                     Green
[BYel]                     Yellow
[BBlu]                     Blue
[BMag]                     Magenta
[BCya]                     Cyan
[BWhi]                     White


-------------------------
Ansi Video Cursor Control
-------------------------


Replaceable macro          Background Color
-----------------          ----------------



       Page 38              Chapter 3  MACRO Parameter Symbols



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   PRM-data Representatives (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

[CUp]                      Cursor Up 1
[CDn]                      Cursor Down 1
[CFw]                      Cursor Right 1
[CBw]                      Cursor Left 1
[Cls]                      Clear Screen
[Cle]                      Clear to End Of Line

--------------
Host Mode Data
--------------

[USR_NAM]

   Caller name as found in the USERLIST.LST file.

[CURTIME]

   Replaced with the current time in 12 hour format.

[DCDTIME]

   Replaced with the online time.

[EMINUTE]

   Replaced with ascii decimal minutes untill next event
































       Page 39              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Replaceable Macro Functions
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ




o  Replaceable MACRO Functions are UPPER case only

%B
   Insert ascii baud, %B is replaced with current baud setting in ascii
   format.  Current baud setting is UART line speed, if the port is locked,
   this will differ from the modem connect speed.

%C
   Insert ascii connect speed, same as above, but CONNECT speed in stead of
   port rate.

%P
   Insert ascii port, %P is replaced with current port number is ascii format.
   Port number is 1 based (com1 =1, com2 =2)

%FN   (Valid when used from <FileLister_>)

   Use from File Lister Area, %FN is replaced with currently "highlighted"
   filename.

%PF
   Prompt for filename, %PF is replaced with what you type into the prompt box.

%WK

   Wait for Key press, stops MACRO execution and waits for a key press.





























       Page 40              Chapter 3  MACRO Parameter Symbols


Chapter 4  Scripts
































































       Page 41              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   AutoScriptGen (Tm)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ




AceComm generates script files automatically when running in "AutoScriptGen"
mode.  The macro <AutoScrGen_> puts AceComm into "Script Learn".  AceComm's
default keyboard file, assigns ALT A to toggle <AutoScrGen_> on.


"AutoScriptGen" first prompts for a filename to use for the script file.  The
extension .SCR will automatically be appended.

ÉÍInput WindowÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
ºÍEnter filename, <ENTER> alone when done, ESC-abortÍÍÍÍÍÍÍÍÍÍÍÍ
º>=> D:\ACE\CSERVE°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

Having a filename, AutoScriptGen creates the file and waits for activity.  We
want to call out.  Lets bring up the FON directory and select Compuserve.

ÉÍ Telephone_directory fon\ACE.FON, 9 RecordsÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
ºÍ      System Name              Phone Number     Line Control V
º 1    AceComm Support BBS      1-602-846-2940     19200,8N1   A
º>2    CIS (local phoenix 9600) 468-0285           19200,7E1   A
º 3    CIS (phones)             1-800-346-3247     2400,7E1    A
º 4    Comp USA #2              1-214-620-7993     19200,8N1   A
º 5    Supra Modem BBS          1-503-967-2444     19200,8N1   A
º 6  - Comput Connections (PCB) 1-202-547-2008     19200,8N1   A
º 7  - Comp USE (Dallas TX)     1-214-620-2255     19200,8N1   A
º  Dial  Edit  <SPACEBAR>-Que  Circling_dial_queue  Fon_files  S
ÈÍ Add_record  Remove_record  UnMark_All  Import  Paint  Quit  H

AutoScripGen will write Fon.Record information to the script file in the form
of macro commands.

The macro to start "Script Learn" is <AutoScrGen>.  AceComm's default setup
uses ALT A to toggle <AutoScrGen> on.  The following short scrip is exactly as
was recorded by the "Script Learn" function.

<INITFONREC>CIS (local phoenix 9600)
<FON_NUM>468-0285
<FON_LINECTRL>7E1
<FON_BAUD>19200
<FON_TERM>Av/An
<FON_FLAGS>Macro,DTag,Cap,Text,IEMSI,
<ReDials>100
<FON_REDIAL>
<LocalKeys>On
<OPENCAPTURE>cserve.CAP
<SendStr>^M
<WaitStr>Host Name:
<SendStr>cis^M
<WaitStr>User ID:
<SendStr>75120,3306^M
<WaitStr>Password:
<SendStr>your/pwd^M
<WaitStr>r HELp!


       Page 42              Chapter 4  Scripts



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   AutoScriptGen (Tm) (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

<SendStr>rea^M
<WaitStr>e(s) # (or ALL)?!
<SendStr>all^M
<WaitStr>CR> for more !
<SendStr>^M
<WaitStr>CR> for more !
<SendStr>^M
<WaitStr>CR> for more !
<SendStr>^M
<WaitStr>e, REPly or NEXt!
<SendStr>^M
<WaitStr>CR> for more !
<SendStr>^M
<WaitStr>CR> for more !
<SendStr>^M
<WaitStr>e, REPly or NEXt!
<SendStr>^M
<WaitStr> ADDress or HELp!
<SendStr>^M
<WaitStr>ssages? (Y or N)!
<SendStr>n^M
<WaitStr>Enter choice !
<SendStr>go IbmPro^M
<CLOSECAPTURE>
<OPENCAPTURE>ibmpro.CAP
<WaitStr>CR> !
<SendStr>Read New^M
<WaitStr>CR> !
<SendStr>^M
<CLOSECAPTURE>
<WaitStr>Enter choice !
<SendStr>off^M
<WaitStr>Host Name:
<SendStr>off^M
<ENDS>



To begin "Script Learn", I pressed ALT A for <AutoScrGen>.  This macro will
turn on "Script Learn" and prompt you for a filename.  Type in the filename for
the new script.  Next, I pressed ALT D for <PhoneList>, and selected the local
9600 CIS record for dialing.

This segment was written to the script when entering the dialer.

<INITFONREC>CIS (local phoenix 9600)
<FON_NUM>468-0285
<FON_LINECTRL>7E1
<FON_BAUD>19200
<FON_TERM>Av/An
<FON_FLAGS>Macro,DTag,Cap,Text,IEMSI,
<ReDials>100
<FON_REDIAL>
<LocalKeys>On
<OPENCAPTURE>cserve.CAP



       Page 43              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   AutoScriptGen (Tm) (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

The dialer sees we are in "Script Learn" and writes the macros required to
initialize a Fon.Record.  Notice the "Flags" include opening a capture file
upon Dial/Connect.  The "Cap," flag was recorded here, and is responsible for
the "<OpenCapture>cserve.CAP" to be recorded into the script.  Because the
<OpenCapture> macro has been recorded, we want to edit out the "Cap," flag.  If
we leave it in, the capture file will be opened twice, it not be a problem,
except for duplicate time stamps.  It is nice to have a capture file open while
recording in "Script Learn", a capture file provides a good reference later on
when editing the script.

What follows is a script that captures a forum (IBMPRO) to a capture file, and
also checks for "Compuserve Mail" along the way.  I have CIS configured to
announce my mail, and so some decision making is required for the scripts to
operate all the time.  The fastest way for me to read a forum is to capture it
to file 2 or 3 times a week.  I can reply off line.  Since personal mail
announcements are capable of tripping up a script, like the one generated
above, some more complex macros are put to work.


;    We can place comments into our scripts.  ";" is used as a comment
;    character.  Text following ";" is a comment.
   <DispStr>[AttrOff] <ClrWin>
   <DispStr>[BWhi][Blu] <DispText>Intro <DispStr>[AttrOff]
   <DispStr>^M^JQ)uit
   <DispStr>^M^JAny key continues, or wait 10 seconds^M
   <GetKey>10    <if>Q <Goto>@@EndScript


<INITFONREC>CIS (local phoenix 9600)
<FON_NUM>468-0285
<FON_LINECTRL>7E1
<FON_BAUD>19200
<FON_TERM>Av/An
<FON_FLAGS>Macro,DTag,Text,IEMSI,   ; I deleted "Cap," from the flags

<ReDials>100                        ; This macro gives control over how many
                                    ; times to re-dial before giving up.
<FON_REDIAL>
<LocalKeys>On
<OPENCAPTURE>cserve.CAP



; Note: when stacking macros, a space character MUST precede the macro.
<SendStr>^M
<WaitTime>15                        ; 15 seconds to timeout (<WaitStr> only)
<WaitStr>Host Name: <SendStr>cis^M
<WaitStr>User ID: <SendStr>75120,3306^M
<WaitStr>Password: <SendStr>your/pwd^M

;   The following checks for personal messages, "Compuserve Mail".
;   waiting for me. I won't have messages waiting every time I log on to
;   Compuserve. We need a way for the script to make decisions. If there are
;   messages, we can stop and read them, recording them into the already open
;   capture file, if no messages, we want to continue to capture the forum, and
;   log off.


       Page 44              Chapter 4  Scripts



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   AutoScriptGen (Tm) (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


   <Timer0>30                       ; Set a timer to 30 seconds
:@@CheckMail                        ; Label we loop to while checking
   <CheckMdm>CompuServe Mail <if>1 <goto>@@PersonalMail
   <CheckMdm>messages pending <if>1 <goto>@@PersonalMail
   <CheckMdm>SCAn, REAd, <if>1 <goto>@@PersonalMail
   <CheckMdm>Enter choice ! <if>1 <goto>@@CompuserveTop

   <Timer0> <if>1 <Goto>@@CheckMail ; <if>1 while not timed out
;
;  Fall through to the forum on timeout
;
   <SendStr>^M
   <Goto>@@IBMPRO
;
;  Here if we got a hit with <CheckMdm>. <CheckMdm> is not case sensitive.
;
:@@PersonalMail
   <WaitTime>10                     ; New, faster timeout for <WaitStr>
   <OPENCAPTURE>cismail.CAP         ; <WaitStr> falls through on timeout
   <SendStr>Read^M
   <WaitStr># (or ALL)?! <SendStr>all^M

   <Timer0>300          ; 5 minutes till timeout, up this if you are popular
:@@ReadMail
   <CheckMdm>CR> for more ! <if>1 <SendStr>^M
   <CheckMdm>REPly or NEXt! <if>1 <SendStr>Next^M
   <CheckMdm>SCAn, REAd, <if>1 <SendStr>^M
   <CheckMdm>CR> for more ! <if>1 <SendStr>^M
   <CheckMdm>Delete these messages? (Y or N)! <if>1 <goto>@@AfterMail
   <Timer0> <if>1 <goto>@@ReadMail
;
;  Fall through to here on timeout
;
:@@AfterMail
   <SendStr>N^M
   <Timer0>60                       ; Here we use 2 timers in 2 loops
:@@CompuserveTop
:@@ResetTimer1
   <Timer1>10
:@@TenSecondLoop
   <CheckMdm>Enter choice ! <if>1 <goto>@@IBMPRO
   <CheckMdm>Last page ! <if>1 <SendStr>^M
   <Timer1> <if>1 <goto>@@TenSecondLoop
   <SendStr>^M
   <Timer0> <if>1 <goto>@@ResetTimer1

:@@LogOff
   <SendStr>off^M <Delay>5 <SendStr>off^M <Delay>2 <MdmHangup>

:@@IBMPRO
   <CLOSECAPTURE>
   <SendStr>go IbmPro^M <OPENCAPTURE>ibmpro.CAP
   <Delay>7
   <SendStr>Read New^M
   <MdmStill>10


       Page 45              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   AutoScriptGen (Tm) (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


   <CheckMdm>CR> ! <if>1 <SendStr>^M
   <CLOSECAPTURE>
                           ; If you want more forums
                           ; you can un-comment the following line
                          <Goto>@@IBMCOM

   <WaitTime>15
   <WaitStr>Enter choice ! <SendStr>off^M
   <WaitStr>Host Name: <SendStr>off^M
   <MdmHangup>
   <Goto>@@EndScript

:@@IBMCOM
   <SendStr>go IBMCOM^M <OPENCAPTURE>ibmCOM.CAP
   <Delay>7
   <SendStr>Read New^M
   <MdmStill>10

   <CheckMdm>CR> ! <if>1 <SendStr>^M

   <CLOSECAPTURE>
   <WaitTime>15

   <WaitStr>Enter choice ! <SendStr>off^M
   <WaitStr>Host Name: <SendStr>off^M
   <MdmHangup>

:@@EndScript

<ENDS>

{-DATA_AREA-}
{-TEXT_START-}Intro
ÚÄÄÄÄÄÄ Compuserve Forums ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³                                                                            ³
³  This script calls Compuserve, and captures forums to their respectively   ³
³  named capture files. The script demonstrates some basic decision making   ³
³  using <CheckMdm> and <Timer0> macros. The script is capable of capturing  ³
³  personal mail, if any, and continue on to get the forums.                 ³
³  The script will pause for 10 seconds after it has logged onto Compuserve. ³
³  This pause is where we detect for any "Compuserve Mail" that may be       ³
³  waiting for us.                                                           ³
³                                                                            ³
³   You will need to edit the script where the login process sends your      ³
³   CIS ID  and  CIS password.                                               ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
{-TEXT_END-}










       Page 46              Chapter 4  Scripts



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Labels, Gotos, Data Area
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ




         :Label
            Labels begin with ':' character
            Labels are used as arguments to the <goto> macro

         <goto> label
            "Label"  can be defined any where in the script file, either
            before or after a <goto> macro.

         <if> condition
            AceComm supports a set of conditional macros. Conditional
            macros return either 1 or 0.

         {-DATA_AREA-}
            Defines a data area

         {-TEXT_START-}
          see examples
         {-TEXT_END-}


            {-Data_ Area-} will be covered extensively next month with
            many complex scripts as well as complete documentation.

            The following script introduces some un-documented script
            language features.


            Follows is a basic script which includes a data area.

         ------------snip here -------------
         <ClearWindow>
         <DispText>Intro
         <DispText>Ask_Continue
         :GetKey
         <GetKey>
            <if>Y
            <goto>Dial
            <if>N
            <goto>End
            <goto>GetKey
         :Dial
         <INITFONREC>ACECOMM Support BBS      ; Initialize a FON RECORD
         <FON_NUM>1-602-846-2940            ;
         <FON_BAUD>19200                    ;
         <FON_TERM>Av/An                    ;
         <FON_REDIAL>                       ; Go into re dial mode
         <DispText>Connect
         <WAITSTR> your name:
         <GetDCD>                           ; <WaitStr> may have timed
            <if>1                           ; out
            <goto>Connect
            <goto>Dial
         :Connect


       Page 47              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Labels, Gotos, Data Area (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

         <SENDSTR>Michael Phelps^M
         <SENDSTR>Y^M
         <SENDSTR>password^M
         <WAITSTR>Select:
         <SENDSTR>ff
         :End
         <ENDS>


         {-DATA_AREA-}
         {-TEXT_START-}Intro
         -- Generic Log On Script --
         {-TEXT_END-}
         {-TEXT_START-}Ask_Continue
         Continue (Y/n) {-TEXT_END-}

         {-TEXT_START-}Connect
         -- Connect --
         {-TEXT_END-}
         ------------snip here -------------



------------snip here -------------
    <Wait_To_HHMM>15:45                ; wait till 3:45 pm
    <INITFONREC>A.C.E. Software Support; call Init FON function
    <FON_NUM>1-602-846-2940            ; set phone number
    <FON_BAUD>2400
    <FON_TERM>Av/An                    ; video type for script
    <FON_REDIAL>                       ; call redial function
    <WAITSTR>it a few moments.
    <SENDSTR>^M
    <WAITSTR>s your name:
    <SENDSTR>Michael Phelps^M
    <WAITSTR>ael Phelps [Y,n]?
    <SENDSTR>^M
    <WAITSTR>Password:
    <SENDSTR>melissa_jean^M
    <WAITSTR>Select:
    <SENDSTR>f^M
    <SENDSTR>d^Mz^Mace170.arj^M
    <RecvZmo>
    <WAITSTR>Select:
    <SENDSTR>gyn^M
    <ENDS>
    <ENDS>
------------snip here -------------











       Page 48              Chapter 4  Scripts



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Mini Host Script Example
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ



;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
;;
;;          --  Mini Host Mode Script for AceComm v1.86  --
;;
;;  Note:  Labels are CaSe sensitive
;;         :@@Start    will not be found if accessed as <goto>@@start
;;                                                          => S <=
;;         Labels begin with ':' character, and start at the beginning
;;         of a line
;;         Each label must be a unique character string
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
;
;         Back up here after caller
;
;;;;;;;;;;
:@@Start
;;;;;;;;;;

<HostEcho>OFF <SendStr>ATE0^M       ; We do not want the modem to echo
                                    ; as AceComm handles this when we turn
                                    ; <Host_Echo>ON
<AutoAnswer>On

   <LocalKeys>Off
   <SetDTR>Off <Delay>1 <SetDTR>On  ; This will hang up most modems
   <SetLCtrl>8n1                    ; new macro for 1.86
   <Delay>2                         ; This will help wait for modem response
                                    ; strings to clear

   <ClrWin>
   <DispText>TellAutoAnswer         ; Display text defined in Data Area
                                    ; %P (port), %B (connect speed)
   <DispStr>Port %P Setup for %B^M^JWaiting for caller^M^J
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
;
; Top of wait for caller loop
;
;;;;;;;;;;
:@@Wait
;;;;;;;;;;
   <DispStr>^M[CURTIME]^M

   <GetDCD> <if>1 <goto>@@DCDLogIn  ; Here is where we detect a caller
   <GetKey>5 <if>L <goto>@@LogIn   ; Allow local keyboard login
            <if>C <DOSShell_>
            <if>ALT+J <DOSShell_>
            <if>R <RunProg>list.com
            <if>E <goto>@@END       ; Provide a clean exit
   <goto>@@Wait                     ; 'Wait' is a case sensitive label...
;
; Here if carrier detected
;
:@@DCDLogIn
;


       Page 49              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Mini Host Script Example (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

; Clear screen,  Send ansi video request,  Display banner
;
   <Var0>0                          ; See if we can set this to 1 with
                                    ; our ansi video detection scheme.
   <Timer0>3                        ; Init Timer0 and set 3 second timeout
   <RawCapture>On                   ; Allow all caller's input in wait buffer
                                    ; ESC[6n  is video request (detect ansi)
   <SendStr>^L^[[6n^MMini Host Script for AceComm v1.86^M
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
;
; Loop here for 3 second maximum waiting for answer to Ansi detect sequence
;
:@@DetectAnsi
   <CheckMdm> [ <if>1 <goto>@@AnsiDetected     ; Remote will answer with
   <Timer0> <if>1 <goto>@@DetectAnsi           ; ESC[n;nR  if ANSI capable
   <RawCapture>Off
   <HostEcho>ON                                ; HostEcho translates CR
                                               ; into CR,LF pair
   <DispStr>^M^JAnsi video request un-answered ; Ansi video request
   <goto>@@Welcome
:@@AnsiDetected
   <Var0>1
   <RawCapture>Off
   <HostEcho>ON                     ; HostEcho translated CR into CR,LF pair
   <SendStr> ^M^JAnsi video detected!

:@@Welcome
   <Var0> <if>1 <DispStr>^M^J[Whi]Connected at [Blink][Bold][Red]%C[AttrOff]
   <Var0> <if>0 <DispStr>^M^JConnected at  %C

;
; Caller names are pre registered into an ascii comment file "USERLIST.LST"
; Sample Line:  Michael Phelps,acecomm,9
; where "acecomm" is the password
;
;;;;;;;;;;;
:@@LogIn
;;;;;;;;;;;
   <Var0> <if>1 <DispStr>[Whi]
   <DispStr> ^M^JEnter your first and last name:
   <GetStr>26 <FindUser> <if>1 <goto>@@GetPwd
   <DispStr>^M^J%FN not found!

   <DispStr> ^M^JEnter your first and last name:
   <GetStr>26 <FindUser> <if>1 <goto>@@GetPwd
   <DispStr>^M^J%FN not found!

   <DispStr> ^M^JEnter your first and last name:
   <GetStr>26 <FindUser> <if>1 <goto>@@GetPwd

   <DispStr>^L^M^JYour name has not been registered in the user file, you may
   <DispStr>^M^Joptionaly leave a short not for the SysOp, pleas include your
   <DispStr>^M^Jfirst and last name along with a password.
   <DispStr>^M^J^M^JWould you like to leave a note? (Y)es/(N)o
:@@1
   <GetKey>60


       Page 50              Chapter 4  Scripts



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Mini Host Script Example (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   <if>Y <goto>@@LogOffComment
   <if>N <goto>@@OFF
   <Goto>@@1
:@@GetPwd
   <DispStr> ^M^JEnter password:
   <GetStr>26 <UserPwd> <if>1 <goto>@@MainMenu
   <DispStr> ^M^JEnter password:
   <GetStr>26 <UserPwd> <if>1 <goto>@@MainMenu
   <DispStr> ^M^JEnter password:
   <GetStr>26 <UserPwd> <if>0 <goto>@@OFF
                              <goto>@@MainMenu
:@@LogOffComment
   <HostEcho>ON                     ; This needs be on for message, even local
   <GetMsg> <Goto>@@OFF
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
;
; Top of main menu loop
;
:@@MainMenu
   <DispStr>^L
   <Var0> <if>1 <DispStr>[Bblu][Whi][Bold][Cle]
   <DispStr>                 --  AceComm Mini Host Script for AceComm v1.86 --
   <Var0> <if>1 <DispStr>[AttrOff]
   <DispStr>^M^J^M^J

   <Var0> <if>1 <DispText>AnsiMainMenu
   <Var0> <if>0 <DispText>MainMenu

:@@MainMenuKey
   <GetKey>60                       ; <GetKey> times out every n seconds
   <if>1 <goto>@@BBS                ; so if the caller drops carrier, we
   <if>C <goto>@@Comment            ; can fall through to the carrier check
   <if>Y <goto>@@YourMail           ; below. Default timeout is 60 if param.
   <if>R <goto>@@ReadMail
   <if>F <goto>@@Files
   <if>G <goto>@@OFF
   <if>^M <goto>@@MainMenu          ; ^M for <CR>

   ; Note: any invalid key press while off line,
   ;       results in '<goto>'@@Start
   <GetDCD> <if>0 <goto>@@NoDCD     ; Detect if caller hung up
   <goto>@@MainMenuKey              ; Wait for a key press we can process

:@@BBS
   <ChgDir>BBS <RunProg>BBS %P %C <ChgDir>[DIR_START]
   <goto>@@MainMenu
:@@Comment
   <HostEcho>ON                     ; This needs be on for message, even local
   <GetMsg> <Goto>@@MainMenu
:@@YourMail
   <HostEcho>ON                     ; This needs be on for message, even local
   <YourMsg> <Goto>@@MainMenu
:@@ReadMail
   <HostEcho>ON                     ; This needs be on for message, even local
   <ReadMsg> <Goto>@@MainMenu
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;


       Page 51              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Mini Host Script Example (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

; Files Menu
;
:@@Files
   <DispStr>^M^L^M
   <Var0> <if>1 <DispStr>[BWhi][Blu]
   <DispStr>^M^J  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
   <DispStr>^M^J  ³ (Z)modem  AceComm version 1.86 ³
   <DispStr>^M^J  ³ (D)ownload file                ³
   <DispStr>^M^J  ³ (U)load file                   ³
   <DispStr>^M^J  ³ (L)ist file titles             ³
   <DispStr>^M^J  ³ (R)aw directory list           ³
   <DispStr>^M^J  ³ (M)ain menu                    ³
   <DispStr>^M^J  ³ (G)ood bye                     ³
   <DispStr>^M^J  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
   <Var0> <if>1 <DispStr>[AttrOff]
   <DispStr>^M^J^M^JSelect:

:@@FilesKey
   <GetKey>60
   <if>Z <goto>@@DownloadAceComm
   <if>D <goto>@@DownloadFile
   <if>U <goto>@@UploadFile
   <if>L <goto>@@ListFiles
   <if>R <goto>@@RawDir
   <if>M <goto>@@MainMenu
   <if>G <goto>@@OFF
   <if>^M <goto>@@Files
   <GetDCD> <if>0 <goto>@@NoDCD     ; Detect if caller hung up
   <goto>@@FilesKey

:@@DownloadAceComm
   <SendZmo@>@ACECOMM.LST
   <goto>@@Files
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
; Provide Download Options
;
:@@DownloadFile
   <ChgDir>[DIR_DNLDS]              ; So files displayed with
                                    ; <DirList>[DIR_DNLDS]\*.* can be found
   <DispStr> ^M^JEnter filename: <GetStr>15 <DispStr>^M
:@@ChooseDnProtocol
   <DispStr>^M^JZ)modem
   <DispStr>^M^JY)modem  / Ymodem G
   <DispStr>^M^JX)modem
   <GetKey>60
   <if>Z <goto>@@ZmodemSend
   <if>Y <goto>@@YmodemSend
   <if>X <goto>@@XmodemSend
   <if>^M <goto>@@RetFiles

   <GetDCD> <if>0 <goto>@@NoDCD     ; Detect if caller hung up
   <goto>@@ChooseDnProtocol

:@@ZmodemSend
   <SendZmo>%FN
   <ChgDir>[DIR_START] <goto>@@Files


       Page 52              Chapter 4  Scripts



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Mini Host Script Example (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

:@@YmodemSend
   <SendYmo1K>%FN
:@@RetFiles
   <ChgDir>[DIR_START] <goto>@@Files
:@@XmodemSend
   <SendXmo>%FN
   <ChgDir>[DIR_START] <goto>@@Files
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
; Provide Upload Options
;
:@@UploadFile
:@@ChooseUpProtocol
   <DispStr>^M^JZ)modem
   <DispStr>^M^JG)Ymodem G
   <DispStr>^M^JY)modem
   <DispStr>^M^JX)modem
   <GetKey>60
   <if>Z <goto>@@ZmodemRecv
   <if>G <goto>@@YmodemGRecv
   <if>Y <goto>@@YmodemRecv
   <if>X <goto>@@XmodemRecv
   <if>^M <goto>@@Files             ; <CR> alone aborts

   <GetDCD> <if>0 <goto>@@NoDCD     ; Detect if caller hung up
   <goto>@@ChooseUpProtocol

:@@ZmodemRecv
   <DispStr>^M^JBegin Zmodem Upload^M
   <RecvZmo>
   <goto>@@Files
:@@YmodemGRecv
   <DispStr>^M^JBegin Ymodem G Upload^M
   <RecvYmoG>                             ; Note: the sending Ymodem sends
   <goto>@@Files                          ; filename in the first data block
:@@YmodemRecv
   <DispStr>^M^JBegin Ymodem Upload^M
   <RecvYmo1k>
   <goto>@@Files
:@@XmodemRecv
   <DispStr> ^M^JEnter filename: <GetStr>15 <DispStr>^M
   <RecvXmo>%FN
   <goto>@@Files
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
; Display ready made files list to caller
;
:@@ListFiles
   <SendAscii>files.lst
   <DispStr>^M^JPress CR
   <GetKey>60
   <goto>@@Files
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
; Display directory to caller
;
:@@RawDir
   <DispStr>^M^J
   <DirList>[DIR_DNLDS]\*.*


       Page 53              AceComm (tm) v 1.90



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Mini Host Script Example (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

   <DispStr>^M^JPress CR
   <GetKey>60
   <goto>@@Files
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
;
; Here when caller selects G)o option
;
:@@NoDCD
   <DispStr>^M^JCarrier not detected, Restarting script!
   <DispStr>^M^JLocal mode, you can navigate the script by making correct
   <DispStr>^M^Jkey press for the menu options.
:@@OFF
   <DispStr>^M^L^MGood bye [USR_NAM]!
   <DispStr>^M^JYour on line time [DCDTIME]^M^J

   <MdmHangUp>
   AutoAnswer>OFF                   ; Need this to recycle properly

   <Delay>2                         ; This will help wait for modem response
                                    ; strings to clear
   <goto>@@Start
;
; Here when local keyboard E)nd option is selected
;
:@@END
   <AutoAnswer>OFF
   <ClrWin>
<EndS>
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;
{-DATA_AREA-}
{-TEXT_START-}TellAutoAnswer

              [37;44m --  AceComm Mini Host Script for AceComm v1.86 --  [0m

   AceComm was first release on May 15 of 1993.  Since then the
   script/macro language has evolved slowly.  This is a very simple script
   allowing pre registered log in.  The macro language will continue to
   evolve making possible a more elaborate host script.  For a powerful
   Host mode, take a look at the AutoAnswer setup area.  People are using
   AceComm as a front-end, and calling their favorite BBS software from the
   AutoAnswer macros.  Sample setups for external BBS software are included
   in the manual.
                                            [34;47mÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ [0m
                                            [34;47m³ L)ocal log in    ³ [0m
                                            [34;47m³ C)ommand Shell   ³ [0m
                                            [34;47m³ R)un LIST.COM    ³ [0m
                                            [34;47m³ E)nd script      ³ [0m
                                            [34;47mÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ [0m
{-TEXT_END-}

{-TEXT_START-}AnsiMainMenu

                    [34;47mÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ [0m
                    [34;47m³ 1) Through to BBS   ³ [0m
                    [34;47m³ 2) Download (*.REP) ³ [0m
                    [34;47m³ 3) Uplopad (*.QWK)  ³ [0m
                    [34;47m³ C)omment to SysOp   ³ [0m


       Page 54              Chapter 4  Scripts



ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
   Mini Host Script Example (continued)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

                    [34;47m³ Y)our mail          ³ [0m
                    [34;47m³ R)ead all messages  ³ [0m
                    [34;47m³ F)iles              ³ [0m
                    [34;47m³ G)o (hang up)       ³ [0m
                    [34;47mÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ [0m
 Enter Choice: {-TEXT_END-}
{-TEXT_START-}MainMenu

                   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                   ³ 1) Through to BBS   ³
                   ³ 2) Download (*.REP) ³
                   ³ 3) Uplopad (*.QWK)  ³
                   ³ C)omment to SysOp   ³
                   ³ Y)our mail          ³
                   ³ R)ead all messages  ³
                   ³ F)iles              ³
                   ³ G)o (hang up)       ³
                   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
 Enter Choice: {-TEXT_END-}







































       Page 55              AceComm (tm) v 1.90


Chapter 5  LICENSE



AceComm is not a Public Domain program and is not free.  AceComm is copyright
(C) 1990-1993 by MGP Programming Services.

Non-registered users of this program are granted a limited 30 day license to
evaluate the programs suitability for their requirements.  Any usage of AceComm
beyond the evaluation time period requires registration of each copy of the
program used.  Use of non- registered copies of AceComm beyond the original
evaluation period is prohibited.

AceComm may NOT be modified in any respect, for any reason, including but not
limited to, de-compiling, disassembling, or reverse engineering of the
program.  The opening title screen, help screens, and all other proprietary
program output must never be altered, removed, bypassed or modified by any
means.

You are free to distribute the PUBLICLY AVAILABLE evaluation version of AceComm
to others subject to the above restrictions and also the following:

   A.   No fee is charged for its use.

   B.  No re numeration may be accepted for AceComm.  This does not apply to
        computer access charges the system operators (Sysops) of or
        organizations owning bulletin board systems, on line services, etc...
        may charge subscribers.

   C.  AceComm must be copied in unaltered form, complete with files containing
        license information, the FULL documentation and all accompanying
        files.  The self-extracting archive distributed by MGP Programming
        Services must not be altered in ANY respect.

   D.  All shareware houses/distribution firms must make explicitly clear that
        the diskette purchase containing any shareware program has NOT
        registered the software with the author MGP Programming Services
        Software/Michael G Phelps.



























       Page 56              Chapter 5  LICENSE




System Operators may make AceComm available for download only if the above
conditions are met.  The archive (Acennnn.EXE) distributed by AceComm or an
equivalent archive may be made available only in complete form.  Refer to
FILELIST.DOC to verify complete package contents.  If the contents appear
altered or not complete, you may obtain the latest release of AceComm directly
from MGP Programming Services by sending a formatted diskette labeled with the
word "AceComm".  Please include $5 for handling.

The latest version of AceComm is also available on Compuserve.

Commercial distributors of "Public Domain", "Shareware", and/or User Supported
software may distribute AceComm subject to the above conditions only after
obtaining WRITTEN permission from MGP Programming Services.  This condition
statement supersedes all previous agreements.

Please refer to the section entitled registration/ordering section for
additional information on registration, corporate site-licensing and related
topics.











































       Page 57              AceComm (tm) v 1.90




The above license statement does not apply to the REGISTERED version of
AceComm.  The registered software of MGP Programming Services is protected
under United States Copyright and Trademark Laws.  It must be treated just like
a book with certain exceptions as follows:

   A.  MGP Programming Services authorizes the making of archival copies of the
       registered software for the sole purpose of backing-up your software and
       protecting your investment from possible loss.

   B.  The medium on which the registered software is recorded is transferred
       to the customer, but not the title to the software.

   C.  The customer may resell or distribute unmodified copies of the
       registered software provided the customer has purchased from MGP
       Programming Services one copy of the registered software for each one
       sold or distributed.  The provisions of this software license shall also
       be applicable to third parties receiving copies of the registered
       software from the customer.

   D.  By saying, "just like a book", MGP Programming Services means that the
       registered software may be used by any number of people and may be
       freely moved from one computer location to another so long as there is
       ABSOLUTELY NO POSSIBILITY of it being used at one location while being
       used at another.  Just like a book that cannot be read by two different
       people in two different locations at the same time.




































       Page 58              Chapter 5  LICENSE


Chapter 6  Contacting the author




You can get more help by contacting the
author Michael Phelps at the following

AceComm Software Support
------------------------
- VOICE 602-846-4563 6 days 12-7pm MST

- BBS   602-846-2940 24 hours

- COMPUSERVE User ID 75120,3306

- FIDONET ADDRESS 1:114/35

- FIDONET COMM echo

- FIDONET ACECOMM echo
I distribute the "ACECOMM" echo to
USA NODES, until it makes BACKBONE.

- Write to: MGP Software (AceComm)          * New address takes affect with
            BOX 301 C  Route 3                AceComm 1.85 release. Phone
            Detroit Lakes, MN 56501 USA       lines will remain the same until
                                              we actualy move later this year.