SimpTerm - V1.00 
 
                           Simple Terminal Emulator  
 
 
 
 
                    Copyright 1995, B&B Electronics Mfg Co  
                                  PO Box 1040  
                                 707 Dayton Rd 
                               Ottawa, IL 61350  
                                release: 3/9/95  
 



                               



2
1.0  General Information 
     1.1   Disclaimer of Warranty 
     1.2   License 
     1.3   Introduction 
 
2.0  Screen Layout 
     2.1   Main Menu 
     2.2   Terminal Screen(s) 
     2.3   Setup Window 
     2.4   Handshake Line 
 
3.0  Users Guide 
     3.1   Port Menu 
           3.11   Port | Open 
           3.12   Port | Close 
           3.13   Port | Setup 
           3.14   Port | Change 
           3.15   Port | Copy Settings 
           3.16   Port | Summary 
           3.17   Port | Exit 
 
     3.2   Control Menu 
 
          3.21  Control | RTS 
          3.22  Control | DTR 
          3.23  Control | Break 
          3.24  Control | Last 
          3.25  Control | FIFO 
          3.26  Control | Clear RX_Buffer 
          3.27  Control | Clear TX_Buffer 
 
     3.3   Options Menu 
 
          3.31  Options | Test Mode 
          3.32  Options | Set Trigger 
          3.33  Options | Monitor Mode 
          3.34  Options | Define String 
          3.35  Options | Log to File 
          3.36  Options | Transmit File 
 
     3.4  Display Menu 
 
          3.41  Display | Clear 
          3.42  Display | Split 
          3.43  Display | Settings 
          3.44  Display | Character 
          3.45  Display | Show/Hide 
          3.46  Display | 43/50 Lines 
 
     3.5  Config Menu 
 
          3.51  Config | Load 
          3.52  Config | Save 
          3.53  Config | Save As 
          3.54  Config | About 


3
1.0   General Information 
---------------------------------------------------------------------------- 
 
     1.1  Disclaimer of Warranty 
          THIS SOFTWARE AND MANUAL ARE SUPPLIED "AS IS".  B&B ELECTRONICS 
          HEREBY DISCLAIMS ALL WARRANTIES RELATING TO THIS SOFTWARE AND ITS 
          DOCUMENTATION FILE, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED 
          TO DAMAGE TO HARDWARE, SOFTWARE AND/OR DATA FROM USE OF THIS 
          PRODUCT.  IN NO EVENT WILL B&B ELECTRONICS BE LIABLE TO YOU OR 
          ANY OTHER PARTY FOR ANY DAMAGES.  YOUR USE OF THIS SOFTWARE 
          INDICATES THAT YOU HAVE READ AND AGREE TO THESE AND OTHER TERMS 
          INCLUDED IN THIS DOCUMENTATION FILE. 
 
     1.2  License 
          SimpTerm is neither free software nor is it in the public domain. 
          The software and its documentation, this file, are property of 
          B&B Electronics and may not be sold without written permission. 
 
          SimpTerm is distributed as shareware.  This means that you are 
          granted a limited license to use it for a period of 30 days.  If 
          you find it useful and decide to continue using it after the 
          trial period, registration is required. 
 
          Registered users will be granted a just-like-a-book license which 
          means a registered version of the software can be used by more 
          than one person and can be moved from one computer to another so 
          long as there is NO POSSIBILITY of it being used by two different 
          persons on two different computers at the same time, just like a 
          book can not be read by two different persons in two different 
          places at the same time. 
 
          If you register for a license you are eligible for assistance 
          from our tech-support team and will be granted one free upgrade 
          of SimpTerm.  You can register SimpTerm by phone, fax, E-Mail, or 
          by mail.  The information is listed below: 
                  PH: 815-434-0846     FAX: 815-434-7094 
                  sales@bb-elec.com    P.O. BOX 1040 - OTTAWA, IL 61350 
 
     1.3  Introduction 
          SimpTerm is a shareware software package that assists users in 
          solving serial communication problems.  Some of the features 
          included in SimpTerm are the following: 
            * Up to four ports can be opened at a time 
            * Any hardware supported baud rate 
            * RS-232/RS-485 support 
            * Handshaking control 
            * Loop back tests 
            * Triggers 
            * Monitor Mode which monitors communications between a DTE/DCE 
              (requires hardware). 
 

4
2.0   Screen Layout 
---------------------------------------------------------------------------- 
 
     2.1  Main Menu 
          The Main Menu is located on the top line of the screen.  It allows 
          you to access all the features of SimpTerm.  It is accessed by 
          pressing ALT+"highlight char".  Then the right/left arrow keys are 
          used to move to the next/previous menu while the down/up keys are 
          used to move to the next/previous menu items.  Some of the menu 
          items have a key or key sequence to the right of the option, this 
          is a hot key that can be used at any time to access that menu 
          function. 
 
    2.2   Terminal Screen 
          This is the area where all the characters that are transmitted 
          and received are displayed.  On color monitors the transmit 
          characters are displayed in yellow and the receive in cyan.  On a 
          black and white monitor the transmit characters are displayed in 
          white and the receive in gray.  If an Overrun Error, Parity Error, 
          Framing Error, or Break Interrupt is detected the character will 
          be blinking (see the Handshake Line section).  When a port is 
          in split mode (see Display|Split), a horizontal line will be 
          splitting the terminal screen in which the transmit characters 
          (DTE side) will be displayed in the upper half, and the receive 
          characters (DCE side) will be displayed in the lower half. 
 
          A 45 line ring buffer is maintained for each of the ports opened. 
 
    2.3   Setup Window 
          This window is located on the right side of the Terminal Screen 
          when the Settings option is selected (see Display|Settings).  This 
          is used for a constant reminder of the ports settings. 
 
    2.4   Handshake Line 
          The Handshake Line is located on the bottom of each of the opened 
          ports and is split up into four sections. 
 
          The first is the "DTE:" section.  This section displays the state of 
          the handshakes: DTR - Data Terminal Ready, RTS - Request to send, 
          and BRK - Break. 
 
          The second section is the "DCE:" section.  This 
          section displays the state of:  DSR - Data Set Ready, CTS - Clear 
          to Send, DCD - Data Carrier Detect, and RI - Ring Indicator. 
 
          The third is the state of the error flags.  This displays the 
          state of BRK - Break, OE - Overrun Error, PE - Parity error, and 
          FE - Framing Error.  If one or more of these errors occur on a 
          receive character, the state will be set until the next receive or 
          transmit character is displayed. 
 
          The fourth is the current size of the Transmit "TXB:" and Receive 
          "RXB:" buffers. 
 
          For all of these flags, when the state is found to be "high", the 
          representation characters will be displayed with a gray background 
          with a black foreground, otherwise they will be displayed with a 
          black background and a gray foreground. 



5 
3.0  Users Guide 

     3.1  Port Menu 
 
          3.11  Port | Open 
                Allows the user to open a serial communications port.  An 
                "Address, IRQ, Transmit Buffer Size, and Receive Buffer Size," 
                is required to install a port.  The address is the location of 
                the port, and the IRQ is the interrupt request line the port 
                will be operating under.  Some of the more common address: 
                03F8h, 02F8h, 03E8h, and 02E8h are the usual address for 
                COM1-COM4 respectively, although any address through 3FFh may 
                be specified.  All IRQ's (2-15) are also supported. 
 
                The transmit and receive buffers are used as a temporary 
                holding areas for characters that are waiting to be transmitted 
                and characters that are received before they can be placed on 
                the screen.  The larger the receive buffer the less chance 
                there is to lose characters.  The minimum size of the each of 
                the transmit and receive buffers is 2 characters.  The 
                maximum size has to be less than the following: 
                      (2*Receive Buffer) + (Transmit Buffer)) < 65535. 
 
                When a port is opened, it transmits a NULL to determine if 
                the IRQ is set correctly. 
 
          3.12  Port | Close 
                Allows the user to close an existing port.  Any ports that 
                are left open are automatically resized to fill the screen. 
 
          3.13  Port | Setup 
                This dialog box allows you to set up the communication 
                parameters for the port. 
 
          3.14  Port | Change 
                This allows you to change a ports address, irq, receive 
                buffer size, or transmit buffer size without losing any of 
                the ports triggers, handshake settings, etc. 
 
          3.15  Port | Copy Settings 
                Copys the baud rate, parity, data bits, stop bits, triggers, 
                and all the display settings from one port to another. 
 
          3.16  Port | Summary 
                Shows a summary of the active port.  The address, irq, 
                transmit buffer size, receive buffer size, type of uart, and 
                FIFO trigger level if the UART is a 16550AFN.  The type of 
                UART's that are supported are: 8250 or 8250B, 8250A or 16450, 
                16550, or 16550AFN. 
 
          3.17  Port | Exit 
                Exits SimpTerm.  If a configuration file is open and changes 
                have been made since it has been open, you will be prompted 
                to save the changes before exiting.  If no configuration is 
                open it will just exit. 


6
     3.2  Control Menu 
 
          3.21  Control | RTS 
                Toggles the state of Request to Send. 
 
          3.22  Control | DTR 
                Toggles the state of Data Terminal Ready. 
 
          3.23  Control | Break 
                Toggles the state of the Break condition.  This condition is 
                caused by holding the transmit data line high. 
 
          3.24  Control | Last 
                Toggles continuous transmit.  The character that is repeated 
                could either be the last character that was typed 
                (transmitted) or a string that was defined and transmitted. 
 
          3.25  Control | FIFO 
                If the UART is a 16550AFN then the FIFO trigger level can be 
                set here.  It is a good idea to only change this when the 
                receive buffer is empty, otherwise characters could be lost. 
 
          3.26  Control | Clear RX_Buffer 
                If there are characters in the Receive Buffer they are 
                cleared.  Also this option is used to clear the receive 
                overflow flag which, when set is displayed on the handshake 
                line as "OF". 
 
          3.27  Control | Clear TX_Buffer 
                If there are characters in the Transmit buffer they are 
                cleared. 
 
 
     3.3  Options Menu 
 
          3.31  Options | Test Mode 
                Allows you to test a serial port or external device by either 
                looping back on itself pins 2 and 3 (transmit and receive) or 
                by connecting one port to another by configuring one as a DCE 
                device.  If two ports are being used in test mode, then the 
                active port transmits characters while the second port 
                receives. 


7

          3.32  Options | Set Trigger 
                A trigger is defined as a string that is looked for while a 
                port is receiving characters.  If this string is detected, a 
                second defined string is then transmitted out the port as a 
                reply to the trigger. 
 
                In the Set Trigger dialog box you can enable/disable each 
                of the triggers separately by the check box preceding each of 
                the triggers.  Also, there is a "Enable Port ? Triggers" 
                check box on the bottom of the dialog box that allows you to 
                enable/disable all of the triggers for that port.  This check 
                box does not enable triggers that are disabled by the 
                individual check boxs.  The "Make Global" check box allows 
                all the ports that have there "Enable Port ? Triggers" 
                enabled to use that ports triggers.  This allows the user to 
                set up one set of triggers for all ports open.  The "Trigger" 
                edit boxes contains the strings that a port is going to look 
                for before transmitting its reply.  This string is case 
                sensitive.  The "Reply" check boxes is the string that is 
                automatically transmitted when the "Trigger" is received. 
                Hexadecimal values can be specified in either the "Trigger" 
                or "Reply" edit boxes by placing the value between "<>".  For 
                example to "Reply" a Null you would include: <0> in the 
                "Reply" string. 
 
          3.33  Options | Monitor Mode 
                Allows you to monitor communications between a DTE and DCE. 
                This feature requires an external piece of hardware as well 
                as two ports being open at a time.  This piece of hardware 
                can be purchased from B&B Electronics (model 232MMA) for 
                $34.95, or can be constructed by yourself.  The cable 
                requires the pinouts in diagram  A.1. 



8
     3.5  Config Menu 
 
          3.51  Config | Load 
                Loads a configuration file. 
 
          3.52  Config | Save 
                Saves a configuration file.  If a configuration is not 
                currently open, a dialog box will come up for you to specify 
                a name for the file.  The default directory is the directory 
                where SimpTerm is located.  If a configuration file is 
                currently open it saves the current settings to the file. 
 
          3.53  Config | Save As 
                Saves the current configuration file to a user supplied name. 
                The default directory is the directory SimpTerm is located in. 
 
          3.54  Config | About 
                Displays copyright notice and version number. 


11
                          SimpTerm Mail Registration 
                                    v 1.00
 
 
To:  B&B Electronics Mfg Co 
     PO Box 1040 
     Ottawa IL, 61350  
 
            Name:  _______________________________________________________  

           Title:  _______________________________________________________  

         Company:  _______________________________________________________  

         Address:  _______________________________________________________  
 
                   _______________________________________________________  
 
City, state, Zip:  _______________________________________________________  
 
    Phone number:  ____________________________  
 
 
I wish to become a registered user of SimpTerm version 1.00.  
 
I request ___ copies of SimpTerm 1.00, a printed SimpTerm manual for each.  
 
 
 
(To Illinois State residents:  As a licensed business in the state of Illinois  
we are required to charge 6.25 percent sales tax on sales made within the  
state.  Please include the tax when you calculate the amount of your payment  
for the next item.)  
 
I enclose a check or money order for $______.____ for ____ copies (including  
sales tax if applicable).