Panasonic / MKE device driver information: 
Copyright (c) Matsushita Kotobuki Electronics Industries 1989-1995 


*****************************************************
       	Matsushita Kotobuki Elec.  AT-BUS
        Proprietary Interface CD-ROM drive series
        CR-521/522/523  &  CR-562/563
*****************************************************


Files on this Disc:

README.DOC	This text file for DOS and OS/2

		[ Required files for DOS installation]

INSTALL.EXE	Executable file for Installation for DOS
CDMKE.SYS	Device driver file (Version 4.11) for DOS and Windows 3.1
INSTALL.DAT	Setup file for customized executable file


		[Required files for OS/2 installation]

INSTOS2.EXE	Executable file for Installation for OS/2
INSTOS2.DAT	Setup file for customized executable file
MKECR56x.ADD 	Device driver for OS/2 (Version 2.11) 
MKECR56x.DDP  	Setup file for device driver for OS/2




*****************************************************
	Installation procedure for DOS and OS/2
	Date: 3/3/1995
	Written by : MKE/Panasonic.
*****************************************************


*****************************************************
(A) DOS Installation procedure:
    ( also supported for Windows 3.1)
*****************************************************
1. Supported  CD-ROM drive:
	<Proprietary CD-ROM>
	CR-562/563 (double speed, tray loading type)

2. Installer file name:
	INSTALL.EXE (Version 1.00, common file for installation)
	INSTALL.DAT (installation's data file for proprietary CD-ROM)

3. Description for execution:
	If you are setting up CR-56X (proprietary CD-ROM), please type following from the DOS prompt:

		A: or B: INSTALL [return]






********************************************************
(B) OS/2 2.1; 2.11 and OS/2 Warp installation procedure:
********************************************************

1. Supported CD-ROM drive:
	<Proprietary CD-ROM>
	CR-562/563 (double speed, tray loading type)


2. Installer file name:
	INSTOS2.EXE (Version 2.00, common file for installation)
	INSTOS2.DAT (installation's data file for proprietary CD-ROM)

3. Description for execution:
	If you are setting up CR-56X (proprietary CD-ROM), please type following:
		A: or B: INSTOS2 [return]





*****************************************************
(c) DOS device driver support:
*****************************************************

1. Supported CD-ROM drive series:
	CR-562/563 	(double speed, tray loading type)
	CR-521/522/523 	(single speed , Caddy type)

2. Device Driver name:
	CDMKE.SYS (Version 4.11)

3. Driver description: The device driver must be installed in the Config.sys 		       file.
	
	Example: DEVICE=CDMKE.SYS /D:MSCD001 /SBP:220 or /P:300
       	
	[/D:xxxxxxx]	---> Device name option
	[/SBP:nnn]	---> I/F board address option(Sound Blaster)
	*[/P:nnn]	---> I/F board address option(Other)
		
	a)	If Sound Blaster I/F board is used;
		Config.sys must be as follows:

		DEVICE=CDMKE.SYS /D:MSCD001 /SBP:nnn
		
		where nnn=220, 240, 260 or 280 port address.   
		(Default is 220)

		for  Sound Blaster Pro(8 bit) port address nnn=220 or 240
		for  Sound Blaster 16(16 bit)  nnn=220, 240, 260 or 280

	
	b)	If MKE original I/F board or other board is used;
		Config.sys must be as follows:

		DEVICE=CDMKE.SYS /D:MSCD001 /P:nnn
		
		where nnn=I/O base port address of interface board. 
		      nnn=300,310,320,340,350,360,370,380,390,
			  3A0,3B0,3C0,3D0,3E0,3F0.
		For Panasonic original I/F board, the default address is 		300.

	*[/Q]		---> Non stop option
		Non stop(no message <A>bort, <R>etry) in initializing 		driver.
		example: DEVICE=CDMKE.SYS /D:MSCD001 /Q

	* : You can omit this option.



*******************************************************
(D) OS/2 2.1, 2.11 and OS/2 Warp device driver support:
*******************************************************

1. Supported CD-ROM drives
	CR-562/563
	CR-521/522/523

2. Driver name:
	MKECR56X.ADD (Version 2.11)

3. Driver description:
	*[/P:nnn]	---> I/F board address option(Other)
		
	a)	if Sound Blaster board is used;
		Config.sys must be as follows:
		
		BASEDEV=MKECR56X.ADD /P:nnn
		
		nnn=220, 240, 260 or 280(Default is address auto-scan)
		Sound Blaster Pro(8 bit) 220 or 240
		Sound Blaster 16(16 bit) 220, 240, 260 or 280
	
	b) 	if MKE original I/F board or other board is used;
	 	Config.sys must be as follows:

		BASEDEV=MKECR56X.ADD /P:260       for I/O address 260

		nnn=300, 310, 320 or 330(Default is address auto-scan)

	* : You can omit this option.











  Trademarks and Copyrights:
    	OS/2 is a trademark of International Business Machines Corporation.
	Sound Blaster is a trademark of Creative Labs, Inc.
	Windows 3.1 is a trademark of Microsoft Corporation.