AFC.DOC

			      AIR-FLOW-CALC
			     Copyright (c) 1994 
			      by J. W. Slusser
			    Snyder Creek Software  

			    For your balancing act
		       --------------------------------

				 Disclaimer
			      ----------------

   The author makes no claims or warranties regarding the usefulness 
   or functionality of this program. It is provided "AS IS". You, the 
   user, accept full responsibility and liability for any problems or 
   damages associated with its operation.



				Shareware Plug
			    -----------------------
   A lot of time and effort has gone into this program. If you find it 
   useful please register it. The registration fee for this program is 
   $15.00. Send cash, check or money order drawn on "US" funds to:

			       James W. Slusser
				 RR2 Box 128
			     West Union, Il. 62477

   Make sure your address is included on the check or M.O.. Registration 
   means you will be eligible for one (1) free upgrade.



 About AIR-FLOW-CALC:
	The program was developed to aid engineers and technicians in
 tracking the performance of fan systems.
	A fan's performance is subject to certain physical laws which are
 commonly referred to as fan laws.  Performance of a fan at varying speeds
 can be predicted through the use of these three basic fan laws.

	1. The volume of air delivered by a fan varies in direct proportion
	   to its speed.
	2. Static pressure varies as the square of the fan speed.
	3. Power required to run the fan varies as the cube fan speed.

	These laws are the basis of this program and the formulas used are
 indicated in the program.


	An IMPORTANT NOTE about adjusting fan speeds:
	
	Before making any adjustments to the fan always check the 
 manufacturers recommended safe fan speeds and also the motor manufacturers
 safe operating amps.

	
	
	For this program to be useful to you some involvement in measuring
 air flow would be required.  Knowing how to use a monometer and a pitot tube
 to measure velocity pressures in air streams would be helpful.

	The air flow calculations are based on standard air density of .075
 lbs. per cu. foot.  Future versions will allow the user to enter air
 temperatures and barometric pressures and calulate actual air densities.

 THE MAIN MENU
	
	Selection #1: 
	
	Allows you to enter your field collected data, duct type and size, 
number of traverse points, and velocity pressure (VP), in inches of water 
column, for each point.  It then does the calculations for you to establish:
			
			a. The square root of each VP measured.
			b. Multiplies the square root of the VP by 4005 to
			   establish the velocity at each point (standard air
			   density).
			c. Calculates the average of all velocities.
			d. Calculates duct area in square feet.
			e. Multiplies the area times the average velocity to
			   establish the cubic feet of air per minute (CFM)
			   produced in any given duct.
			f. Allows you to save the final results to a file for
			   future reference.  

	
	Selection #2: 
	
	Allows you to use the information you have in hand to calculate fan 
speeds needed to produce the required CFM's.  Once the data has been entered 
and a required speed has been calculated you will be able to enter the next 
stage of the program, selection #3.
	
	
	Selection #3:
	
	Allows you to size the fan pulley or motor sheave to produce the 
desired CFM.  When entering this area from inside the program, from selection 
#2 area, the required speed is presented for you.  When you enter this area 
from the main menu you must enter the required speed.  At any rate you have 
two choices you can calculate the fan pulley or the motor sheave size, your 
choice.
	
	
	Selection #4:
	
	Allows you to read existing files.  It searches the current directory 
and lists all the files that are available for reading.  It then prompts you 
for a filename.  When you enter a valid file name it displays the file for 
reading.
	
	
	Selection #5: 
	
	Allows you to print existing files.  Again this is like the read file 
selection, it lists all available files in the AFC directory.
	It will print any text file you ask for, including this one.
	
	
	Selection #6: 
	
	Does just what it says, Quits.        
	
	AIR-FLOW-CALC was written and compiled with Borland's 'Turbo C++ 3.0.' 
Copyright (c) 1992 by Borland International.
	AFC.Exe was then compressed using PKLITE Professional Version 1.00
Copyright (c) 1990 PKWARE, Inc. 
	      
	      
	      Your comments and suggestions are welcome anytime!

			       James W. Slusser
				 RR2 Box 128
			     West Union, Il. 62477
			     
			      Snyder Creek BBS
			       (217) 826-8975
			   1200 - 14,400 bps 8-N-1
				     or 
			    jslusser@prairienet.org