The following programs are provided.

BPQCODE.EXE

    The TSR version of the packet switch. It provides a NET/ROM compatible
    packet switch, and an interface to application-level software (such as
    a BBS).


SWITCH.EXE

    This is a foreground version of BPQCODE. It is intended to run only as
    a packet switch, and not to support an application system (eg BBS). A
    simple terminal program (equivalent to PAC4) is built in, as is the
    SYSOP handler from the Data Engine version of the switch. The diffences  
    from BPQCODE are listed below:

	BPQCFG.TXT

	This can be the same as for the normal version. The code will assume
	NODE=1 and BBS=0, whatever is entered. 


	Terminal support.

	See PAC4 below for details. Ctrl/Y shuts down the whole switch.

	IPGATE.

	SWITCH.EXE includes IPGATE. See IPGATE.DOC for details.

	SYSOP Commands.

	The SYSOP feature is similar to SYSOPH, but the password protection
	works rather differently. To enter SYSOP mode, enter PASSWORD. If 
	you are using the console, the switch will respond Ok, and enter 
	SYSOP mode. If you are accessing the system remotely, it will respond 
	with 5 random numbers. You must reenter PASSWORD, this time followed 
	by the corresponding characters from the password string contained 
	in the file PASSWORD.BPQ. If these are correct the switch responds 
	OK, otherwise it ignores the message.

	So, if the password string is ABCDEFGHIJKLM the following is a
	typical sequence:

		PASSWORD
		BPQ:G8BPQ} 04 02 05 06 03
		PASSWORD DBEFC
		BPQ:GBBPQ} Ok

	Note that the password is converted to upper case before testing, so 
	PASSWORD.BPQ should contain upper case letters or digits. It should
	not contain spaces or other special characters.

	There are a number of extra SYSOP commands. These were added primarily
	for the Data Engine version, where experimenting with parameters is 
	rather more difficult, but I've left them in this version as well.
	
		Command		Corresponding BPQCFG parameter

		OBSINIT			OBSINIT
		OBSMIN			OBSMIN
		NODESINT		NODESINTERVAL
		L3TTL			L3TIMETOLIVE 
		L4RETRIES		L4RETRIES
		L4TIMEOUT		L4TIMEOUT
		T3			T3
		IDLETIME		IDLETIME
		LINKEDFLAG		ENABLE_LINKED
		IDINTERVAL		IDINTERVAL
		MINQUAL			MINQUAL
		FULLCTEXT		FULL_CTEXT
		HIDENODES		HIDENODES
		L4DELAY			L4DELAY
		L4WINDOW		L4WINDOW
		BTINTERVAL		BTINTERVAL

	There is also one commend which isnt in the DE version - SAVENODES.


IPGATE.EXE

    An IP router to run above the switch (Normally in a DesqView window). See
    IPGATE.DOC for further information.


ODIDRV.EXE

    An EXTERNAL hardware driver to link switches via Ethernet (using Novell's
    ODI interface). See DRIVERS.DOC for further information.


BPQCFG.EXE

    This program converts the configuration file BPQCFG.TXT to a binary file
    (BPQCFG.BIN) for use by the switch software. It must be run after any
    change to BPQCFG.TXT.



BPQNODES.COM


    This program dump the ROUTES and NODES tables to a file (BPQNODES). This
    file is then used to initialise the above tables when the switch is 
    reloaded. It should be run before reloading the switch, and if possible
    at regular intervals, so that if the system crashes, it comes back with
    a reasonably up-to-date view of the network. Many BBS systems allow you
    to run a program as part of the forwarding cycle, or at specified times.


    It is possible to edit the BPQNODES file. This provides a way of defining
    Route Qualities, etc. without changing BPQCFG.TXT, or using SYSOPH.

    The file format is: ( {} indicates optional entries - don't include the{})

    ROUTE ADD CALL P QUAL {!} {VIA DIGI1 {DIGI2}}

    where P is the port, QUAL the Quality, and the optional ! indicates a
    locked route. Up to 2 DIGIS may be specified. 

    NODE ADD ALIAS:CALL CALL-1 P QUAL {!} {CALL-2 P QUAL {!} } {CALL-3 ....}

    where CALL-1, CALL-2, CALL-3 are up to 3 alternate routs, which must be
    defined (by ROUTES config entries or ROUTE ADD) before being used.

    Although locked nodes are allowed, I strongly recommend that they are used
    only in exceptional circumstances (eg when using a digi'ed route). Note
    also that a locked route to a node will be removed if the system finds 3 
    higher quality routes to it.


    Lines beginning with ; are treated as comments, and fields should be
    separated by one (and only one) space.




BPQDUMP.COM


    BPQDUMP.COM  is a simple program to dump my code to a file to aid
    diagnosis of fault conditions. It creates a file in the current directory
    called BPQDUMP (about 98k).

    If run without a parameter, it dumps immediately.

    If a param is specified, it will loop until the free buffer count drops
    below 20 ( the point when the code starts to shut down), then dumps and
    exits. Note this mode must only be run in a desqview window.


    eg

    BPQDUMP		- dumps now

    BPQDUMP X	- dumps when buffers < 21



PAC2.COM


    PAC2 is a small, simple terminal program, primarily for use with my switch,
    but it also works with a normal TNC + COMBIOS. It has one paramter (port
    number), so enter PAC2 N, where N is the (virtual) COMBIOS port you want
    to access. The program provides a buffered input line, which allows use of
    the editing keys ins, del, cul, cur, etc, It allows logging to disk (CTRL/L
    toggles this function on and off), and maintains a simple 'Response Time
    Monitor' function - useful for seeing how badly the network is performing!
 
    To exit from PAC2, enter CTRL/Y


PAC4.EXE


    PAC4 is a simple terminal program, which uses the BPQ Host Mode to talk
    to the switch. The program provides a buffered input line, which allows
    use of the editing keys ins, del, cul, cur, etc. It allows logging to disk
    (CTRL/L toggles this function on and off), and maintains a simple 'Response
    Time Monitor' function. A scroll-back buffer is also provided - use PageUp
    and PageDown to scroll.


    The program has one required paramter (port number), and a second optional
    one (M for mono mode). So possible command lines are:

	PAC4 63			; to use stream 63

	PAC4 1 M		; to use stream 1, if you have a mono monitor.

    Connection is made to the switch when a message is input. The ESC key 
    disconnects you from the switch.

    Monitoring is toggled on/off using F1. F2 toggles MCOM mode (monitoring of
    control frames as well as info frames). F3 allows you to set MMASK. Press
    F3, then key up to 4 hex digits, terminated with a newline. Each bit of
    MMASK enables the monitoring of the corresponding radio port. Bit 0 
    enables port 1, bit 15 port 16. Any combination of bits may be set. The 
    current monitor settings are displayed on the status line.


    To exit from PAC4, enter CTRL/Y


SYSOPH.COM



    This program allows the manipulation of certain parameters within the
    switch. The program may be run as a normal DOS program, either in a
    Desqview window or standalone, or it may run as a TSR. The TSR mode would
    normally be used if you were running a BBS system that doesnt need 
    DesqView (eg AA4RE). In TSR mode, commands cannot be entered locally, and 
    the SAVENODES command is disabled. It either mode, it may be accessed over
    the network. 

    The system has now been modifed to use BPQHOST mode rather than a virtual
    TNC2 port. Program SYSOP.COM is withdrawn.


    Installation.

    1. Add a suitible application name as the third APPLICATIONS Param, ie

       APPLICATIONS=BBS,,*SYSOP

       I suggest you use a name starting with a '*', as this will 'hide' the
       command from the Valid Commands display.

    2® Creatå á file¬ PASSWORD.BPQ, containing a string of up to 80 characters.
 
    3. Run program SYSOPH, with a single parameter of the stream to be used,
       either on its own, or in a DesqView window. If a second parameter of
       'RESIDENT' is specified, the program will become a TSR routine.



    Commands may now be entered directly on the PC, (unless in TSR mode) or
    remotely by connecting to the Node, and entering the APPL name (eg *SYSOP). 
    When accessed remotely, a password prompt is sent, containing 5 random
    numbers in the range 1 to the length of the PASSWORD.BPQ string. The first
    command entered must be the corresponding five letters from the password
    string, or the user will be disconnected.

    Available Commands.

    The following commands are supported:

    BYE - Disconnect remote user (even if entered from console)

    TXDELAY
    MAXFRAME
    FRACK
    RESPTIME
    PACLEN
    RETRIES
    QUALITY
    PERSIST
    TXTAIL
    XMITOFF
    DIGIFLAG
    DIGIPORT
    USERS
    VALIDCALL
    L3ONLY
    BBSALIAS
    SOFTDCD
    
       The above display or update the parameter for a specified port,
    
       eg   PACLEN 1 100
            PERSIST 2 50
    
       If the third parameter is omitted, the current value is displayed.
    
       Setting XMITOFF will supress all TX activity on a port (including CWID,
       beacons, etc). I put it in so I could monitor the satellites without
       causing QRM, but it could be used as a way of shutting down a port in
       an emergency.
    
       Setting BBSALIAS will cause connects to the port call or port alias to
       go to the BBS rather than the node.

   It is not currently possible to update VALIDCALLS, but you can display
   the current setting.


   *** Warning ***  

     At the moment the FRACK value is in 1/3sec units, and the TXDELAY is in
     50ms units for HDLC cards, and 10ms units for KISS TNCs. I'll be sorting
     this out when I get the time to rationalize the timer code, but in the 
     meantime, I suggest you make a note of the current values before you
     start fiddling. 

     Also KISS users should note that the params are only sent to the TNC every
     5 mins or so, so the updated values may not take effect for a while.


   ROUTES

       To display ROUTES table, enter ROUTES

       To display entry for a particular neighbour, enter ROUTES Call Port,

       eg   ROUTES G8BPQ-2 2

       To update an entry, enter ROUTES Call Port Params

       eg   ROUTES G8BPQ-2 2 100	- Set quality to 100
            ROUTES G8BPQ-2 2 !         - Toggle 'Locked Route' flag

       To clear the stats counters on a route, enter:

            ROUTES G8BPQ-2 2 Z


    SAVENODES (Not available in TSR mode).

       Writes the ROUTES and NODES tables to the BPQNODES file.

       The SAVENODES function may also be invoked directly from the DOS command
       line - this function replaces BPQNODES.COM

           ie.  SYSOP SAVENODES



John Wiseman, G8BPQ
31.8.92