STPCB Version 3.05B, 7/10/95

    This document is a Beta draft!

    ---[ Introduction ]--------------------------------------------------

    STPCB is a PCBoard PPE program which acts as a "front-end" or "shell"
    for USRSTAT2.EXE.   This allows your callers to use USRSTATS and view
    the BBS modem's diagnostic reports while they are online, no matter
    what type of modem *they* are using.  It allows capturing the reports
    into the message base, and allows the caller to initiate a modem
    retrain from the BBS end of the connection.

    * Again, the _caller_ can be using ANY brand or model of modem. *

    That is one of the most important aspects of STPCB.   Many modems have
    little or no online diagnostics, leaving the owner completely in the
    dark when trying to diagnose problems or test performance.   STPCB
    provides a way for _callers_ to take advantage of the tremendous
    diagnostic abilities of _your_ USR modem.

    To use this PPE program, you must be running PCBoard version 15.1 or
    later, and USRobotics Courier or Sportster modems.   STPCB provides the
    most detailed information when used with V.34 and VFC models, but it
    will also work with many of the earlier 14400, 16800, and 21600 models.
    If your BBS uses a mixture of USR and other brand modems, STPCB can be
    configured to run only on the USR-equipped nodes.

    If for some reason you cannot use STPCB on your system, there is an
    alternative called STGEN.  (ST Generic.)   This is a more traditional
    "Door" type of program which works with many different BBS packages.
    it is similar to STPCB in operation, but does not have the
    message-capture ability built into it, and it is installed through the
    old "shell to a batch file" system interface.

    STPCB is compatible with single and multi-node PCBoard setups.  It has
    been extensively tested on a single-node system running under DesqView
    and Lantastic, and on a large multi-node system running Netware.

    STPCB is a featured attraction on the USRobotics Customer Support BBS,
    and has been running successfully there for over a year without a
    single trouble report.   STPCB is currently in use on hundreds of
    PCBoard BBS systems world-wide.

    ---[ Important Information ]------------------------------------------

    Before installing STPCB, make sure you understand what "Online Command
    Mode" is and how it works.   (See Appendix A for detailed info.) STPCB
    can be configured to use either Escape Character or DTR switching.
    You must select the method that best suits your system and your
    preferences.   If you are in doubt, use Escape Character switching.

    ---[ STPCB File Locations ]------------------------------------------

    Create a directory or subdirectory to hold STPCB and its related files.
    You may select any name or location for this directory, provided that
    STPCB will have read and write access there.   STPCB creates temporary
    files during execution.

            Example: If you have PCBoard installed to C:\PCB, you
            might want to use a subdirectory called STPCB, like this:

            MKDIR C:\PCB\STPCB

    Copy all of the STPCB files into the new directory.

    ---[ Modifying CMD.LST ]----------------------------------------------

    Using PCBSETUP, modify the CMD.LST files for the Main Board and/or any
    conferences that you wish to be able to call the program from.  Edit
    the CMD.LST file, entering the command name you wish to use to call the
    program, and full path and filename of USRSTATS.PPE.

    Example:

    ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
    º                      CMD.LST Editor                                 º
    º                                                                     º
    º                  Charges Per     PPE/MNU File Specification -or-    º
    º   Command  Sec  Minute    Use    Keystroke Substitution             º
    º ÍÍÍÍÍÍÍÍÍÍ ÍÍÍ ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ  ±
    º 1) USRSTATS    0      0        0 C:\PCB\STPCB\STPCB.PPE             ±
    º                                                                     ±
    º                                                                     ±
    º                                                                     ±
    º   ESC=Exit AltI=Insert AltD=Delete AltR=Repeat Alt5=25/50 F2=Edit   º
    ÈÍ 20:31:55 Í 07-02-95 ÍÍÍ F1 Í help ÍÍ caps: OFF  num: ON  ins: OFF Í¼


    ---[ Modify modem init string ]---------------------------------------

    In most cases, installation of STPCB does not require re-programming
    your modem's stored settings.   The required changes in modem setup can
    be done entirely in the modem init strings found in PCBSETUP.

    BE SURE YOU UNDERSTAND THE ADVANTAGES AND DISADVANTAGES OF EACH COMMAND
    MODE SWITCHING METHOD BEFORE YOU GO ANY FARTHER.  THIS INFORMATION CAN
    BE FOUND IN APPENDIX A.

    IT IS YOUR RESPONSIBILITY TO VERIFY THAT THE SELECTED METHOD WILL NOT
    HAVE ANY ADVERSE REACTION WITH OTHER SOFTWARE OR HARDWARE IN YOUR
    SYSTEM.

    The normal init string for PCBoard is "ATZ" which simply resets the
    modem.  The standard modem setting of &D2 allows PCBoard to hang up by
    simply dropping the DTR lead on the serial port.  The standard modem
    setting of S2=255 disables the Escape Sequence detection.

    STPCB requires that these settings be modified to match the Online
    Command Mode switching method defined in STPCB.CFG.  For DTR switching,
    the modem must be running with the &D1 setting.  For Escape Character
    switching, the S2 register must be set to the ASCII value of the
    desired Escape Character.

    ---[ Modem init string for Escape Character switching ]---------------

    Using PCBSETUP, modify the modem initialization string as shown below.

    Modem initialization string: ATHZ^M~~~~ATS2=1

    The S2 value of 1 is only an example.  This number must match the
    number defined in the STPCB.CFG file.  The factory default S2=43 can be
    used, but really isn't a good choice.

    PCboard v15.2 has two entries for the modem init string, so the
    commands may be split up, like this:

    Modem initialization string 1: ATHZ
    Modem initialization string 2: ATS2=1

    Again, S2=1 is only an example.  Make sure this number matches the one
    defined in STPCB.CFG.

    Helpful Hint:  When using Escape Character switching, Courier modems
    must have DIP switch #9 in the ???  or DOWN position.   Sportster
    modems do not have an equivalent DIP switch, they require S14=1 to
    imitate this function.  If you forget to do this, the modem will drop
    the connection every time you run STPCB.

    ---[ Modem init string for DTR switching ]----------------------------

    Using PCBSETUP, modify the modem initialization string as shown below.

    Modem initialization string: ATHZ^M~~~~AT&D1

    Be sure that STPCB.CFG is correctly set for DTR switching mode.

    PCboard v15.2 has two entries for the modem init string, so the
    commands may be split up, like this:

    Modem initialization string 1: ATHZ
    Modem initialization string 2: AT&D1

    Be sure that STPCB.CFG is correctly set for DTR switching mode.

    Because PCBoard expects to be able to drop a connection by toggling
    DTR, there are several operational problems that can result from using
    DTR switching.  When the modem is running with &D1, it can't be forced
    to drop the connection simply by dropping DTR, it must also be sent an
    ATH or ATZ command.

    We can work around the minor issues involved with PCBoard, however,
    you may have a front-end mailer or a door installed that also expects
    to be able to drop connections in a manner that conflicts with the
    STPCB modem setup.  THOROUGHLY TEST YOUR SYSTEM FOR ANY PROBLEMS THAT
    MIGHT RESULT FROM USING DTR SWITCHING.

    ---[ Optional add-on for DTR switching ]------------------------------

    THE FOLLOWING SECTION IS AN OPTIONAL PART OF THE DTR SWITCHING METHOD.

    To improve the way PCBoard hangs up when using DTR switching, we need
    to replace 3 entries in the PCBTEXT file so that instead of just
    displaying the "goodbye" message to the caller, it also hangs the modem
    up properly.  This is done with a tiny PPE program to replace the
    default PCBoard text strings.

    Use the MKPCBTXT utility to modify the following records in PCBTEXT.

    ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
    ³ Record No.:   55   Record Length:  56   Justification:  Left  ³
    ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
    ³Keyboard Time Expired!                                         ³
    ³!c:\pcb\stpcb\rec55.ppe                                        ³
    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

    ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
    ³ Record No.:  166   Record Length:  75   Justification:  Left  ³
    ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
    ³Thanks for calling, @FIRST@!                                   ³
    ³!c:\pcb\stpcb\rec166.ppe                                       ³
    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

    ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
    ³ Record No.:  435   Record Length:  70   Justification:  Left  ³
    ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
    ³Hanging up now.  Thank you for the upload(s).                  ³
    ³!c:\pcb\stpcb\rec435.ppe                                       ³
    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

    The REC55.PPE, REC166.PPE, and REC435.PPE files are included in the
    STPCB package.  You may modify them as you wish, and of course the file
    and path names in the example above should reflect whatever your system
    requirements are.

    There may be other entries in PCBTEXT that would benefit from this
    sort of modification.  PPL source code is included to allow patching of
    any additional fields that you need.

    ---[ STPCB configuration file ]-------------------------------------

    STPCB uses a configuration file to control its optional features.
    This file MUST be located in the same directory as the PPE file, and it
    MUST be named STPCB.CFG.  A *sample* file named STPCB.DEF is supplied
    in the distribution archive, or the program will create another one for
    you if no config file is found.

    *********************************************************************
    * All documentation for the fields in the config file, and the      *
    * STPCB options, are contained as comments within the sample config *
    * file itself.                                                      *
    *********************************************************************

    ** Copy the STPCB.DEF file to STPCB.CFG. **

    Then edit STPCB.CFG, setting the options as desired for your system.
    Be sure to read all the comments in the file, they form a large portion
    of the STPCB documentation!  Save the STPCB.DEF file for future
    reference.

    ---[ User interface ]-----------------------------------------------

    The last installation step is to edit your system's menu files so
    that your users will be able to find the new feature.

    You might also consider installing REPORT.DOC as a bulletin for users
    to read or download.   When callers have questions about the data in
    the report, you can refer them to this bulletin for the technical info.

    That's it, installation is complete.   Now, when your callers enter the
    new command you have defined, the BBS will chug and puff for a few
    seconds and then display a nicely formatted screen of modem status
    info.

    Please note that it doesn't work in local mode, there has to be a real
    live modem connection.

    ---[ STPCB/USRSTATS Support ]-----------------------------------------

    The home of STPCB and USRSTATS is:

    The Majestik Moose BBS,  708-843-2871

    Only calls at 9600 BPS and faster are accepted.  MNP/V42 is required.

    The latest version of this program is always available as a free
    download in the Main Board area.  First time callers can get immediate
    free access to these files by bypassing the registration prompt.
    You will be allowed 30 minutes per call and complete access to the
    "Free Downloads" area of the BBS.

    If you need help with STPCB or USRSTATS, you may leave a message for
    the SYSOP.  I'll help you if I can, but I make no promises.  After all,
    the software is free.  Do NOT call and ask questions that are already
    answered in the documentation.  You will receive only a very brief
    answer under those circumstances.

    STPCB and USRSTATS are available through ftp.usr.com on the Internet.
    Use anonymous login, and your Internet ID as the password.

    STPCB and USRSTATS are available (and running) on the USRobotics
    Customer Support BBS at 708-982-5092.

    At the present time, there is no registration required for this
    software.  If you really want to pay me a few bucks for the many hours
    of effort that went into this, I'll be glad to take it from you.  Call
    The Majestik Moose and leave a (C)omment.

    ---[ Disclaimer ]----------------------------------------------------

    Use this software at your own risk.  It works fine for me.  All product
    and feature names are trademarks of their respective owners.  This
    software is NOT a product of USRobotics, Inc.

    Joseph C. Frankiewicz
    The Majestik Moose BBS
    708-843-2871

    ---[ Appendix A - Modem Escape Sequences ]---------------------------

    An "Escape Sequence" is a mechanism or method for forcing the modem
    into "Command Mode" while it is already connected and on-line.
    "Command Mode" is normally associated with the OFF-LINE condition,
    where the modem will accept and act upon "AT" commands entered from the
    terminal.  However, it is also possible to put the modem into this mode
    DURING a call, WITHOUT disconnecting the call first.  This ability is
    required for making use of certain diagnostic commands which only
    return valid data when used in this on-line command mode.

    USRobotics modems offer 2 methods of getting into on-line command mode.
    Each has its own advantages and disadvantages, depending on the point
    of view.

    The first method is the &D1 setting.   When the modem is set to &D1, a
    momentary "toggling" of the DTR signal (pin 20), from ON to OFF and
    back ON again, will suspend the data connection and place the modem
    into command mode.  USRSTATS documents refer to this as "DTR
    switching".

    The second method is the infamous "Escape Character with Guard Time."
    A designated ASCII character is defined as the "Escape Character", and
    when the modem receives three of these characters in a row, with a
    defined period of inactivity both before and after, it suspends the
    data connection and places the modem in command mode.  The character
    used for the escape is defined in the S2 register, and the default
    value is 43, the "+" character.  (This is where the often-seen "+++"
    comes from.)  The inactivity or "Guard" time is defined in the S12
    register, with a default of 1 second.  USRSTATS documents refer to this
    as "Escape Character switching".

    When using DTR switching, the remote user does not see the "+++"
    characters on the screen when the BBS modem is placed into command
    mode.  This provides a professional seamless interface.  Also, the BBS
    modem is not susceptible to entering command mode if the _caller_ is
    also using Escape Character switching with an identical Escape
    Character definition.

    The disadvantage of DTR switching is that software cannot drop
    connections by simply toggling the DTR pin, it must _also_ send an ATH
    or ATZ command.  It is possible to work around this in PCBoard, however
    you may be using other software in your system that cannot be altered
    this way.

    Using Escape Character switching, your software retains the ability to
    drop connections by toggling the DTR pin, as normal.  The disadvantages
    are that the remote user will see the "+++" sequence on screen when
    STPCB runs, and there is a possibility that the remote user may ALSO
    be trying to use Escape Character switching with the same Escape
    Character that the BBS is using.   This results in the BBS modem going
    into command mode when the intended target was the remote modem.  Since
    the BBS modem can no longer pass any data to the user, and the BBS
    software is unaware of what happened, the user has no alternative but
    to drop the connection and call back.  For this reason, avoid using the
    standard S2 register value of 43.  (The "+" character.)   A value of 1
    (S2=1) usually works well.

    [End of File]