APT2APR   Version 1.91
Copyright (C) GraphiCode Inc 1992,1993,1994  All Rights Reserved.
This program may be distributed as shareware.  No user fee or registration 
is required.

This converter will convert from a Mentor Graphics .APT aperture file to a 
GraphiCode .APR aperture file.  The converter can be used to convert single 
files or groups of files.  Five different formats from Mentor are currently
supported - see the examples at the end of this file.  Version 1.3 adds the
ability to convert APT files written in mm (if metric is not specified, inch 
units are assumed).

    usage: APT2APR [-Metric] <aperture file> [<outfile>]

    Example:
          To convert the aperture file "ALIST1.APT" for use with GraphiCode 
          products, type:
                APT2APR ALIST1

          This creates the GraphiCode aperture wheel file "ALIST1.APR".


          To convert "ALIST1.APT" to "NEWALIST.APR" type:
                APT2APR ALIST1 NEWALIST

          To convert several aperture files type:
                APT2APR *.APT

          For .APT files with values in mm, use the -M option:
                APT2APR -M ALIST1 NEWALIST

Any comments about this converter may be directed to THE SYSOP of the 
GraphiCode BBS (206)771-6980.


Example of Type 1:

 Aperture Position    D_Code  Shape        Type         Power    Height(Y)/Diameter  Width(X)     Used Last Run 
       1                 10   circle        trace                  0.005000           0.000000            yes 
       2                 11   circle        trace                  0.010000           0.000000            yes 
       3                 12   circle        trace                  0.012500           0.000000            yes 
       4                 13   circle        flash                  0.075000           0.000000            yes 

Example of Type 2:

# DEFine APerture Position  Shape       Type   Height(Y)/Diameter  Width(X) 
DEFine APerture    1    Circle          Trace          0.015000      0.000000 
DEFine APerture    2    Circle          Trace          0.050000      0.000000 
DEFine APerture    3    Circle          Trace          0.400000      0.000000 


Example of Type 3:

Pos.  D_Code    Shape       Type    Power   Width(X)/Dia         Height(Y)
1     10      circle        trace                                0.0050   
2     11      circle        trace                                0.0300   
3     12      donut         flash           0.1250 O.D.          0.0470 I.D.
4     13      circle        trace                                0.0150   


Example of Type 4:

 Aperture Position    D_Code  Shape        Type         Power    Width(X)     Height(Y)/Diameter       Used Last Run 
       1                 10   circle        trace                0.0                0.01                  yes 
       2                 11   circle        trace                0.0                0.06                  yes 
       3                 12   circle        trace                0.0                0.03                  yes 
       4                 13   circle        trace                0.0                0.025                 yes 
       5                 14   circle        trace                0.0                0.05                  yes 
       6                 15   circle        trace                0.0                0.08                  yes 
       7                 16   circle        flash                0.0                0.1                   yes 
       8                 17   rectangle     flash                0.1                0.1                   yes 



Example of Type 5:

# Aperture nr. D_Code Shape      Type   Power  Diam./Width(X)  Height(Y)
      1         14    circle     flash            0.0157        0.0000
      2         17    circle     flash            0.0276        0.0000
      3         18    circle     flash            0.0472        0.0000
      4         19    circle     flash            0.0591        0.0000
      5         20    circle     flash            0.0748        0.0000
      6         21    circle     flash            0.0985        0.0000
      7         23    circle     flash            0.1969        0.0000
      8         24    circle     flash            0.0020        0.0000

Example of Type 6:

 APERTURE POSITION  D_CODE  SHAPE        TYPE       SPECIAL    DIAMETER/HEIGHT(Y)  WIDTH(X) 
 
       1              10   CIRCLE        TRACE                  0.007           
       2              11   CIRCLE        FLASH                  0.032           
       3              12   CIRCLE        FLASH                  0.058           
       4              13   RECTANGULAR   FLASH                  0.058              0.058
       5              14   CIRCLE        FLASH                  0.042           
       6              15   RECTANGULAR   FLASH                  0.042              0.042
       7              16   RECTANGULAR   FLASH                  0.032              0.032
       8              17   CIRCLE        FLASH                  0.033           


Example of Type 7:

---------------------------------------------------------------------
		     MENTOR APERTURE WHEEL

D-CODE  DESCRIPTION
---------------------------------------------------------------------
10      5  MIL ROUND
11      6  MIL ROUND
12      7.75 MIL ROUND
13      10 MIL ROUND
14      12 MIL ROUND
15      15 MIL ROUND
16      17 MIL ROUND


Example of Type 8:

// Wednesday August 4, 1993; 16:56:49
//
$$define_aperture(  1 , @Circle      , @Trace,    0.002000 ,     0.000000 ,  10 );
$$define_aperture(  2 , @Circle      , @Flash,    0.005000 ,     0.000000 ,  11 );
$$define_aperture(  3 , @Circle      , @Flash,    0.008000 ,     0.000000 ,  12 );
$$define_aperture(  4 , @Rectangle   , @Flash,    0.012000 ,     0.070000 ,  13 );